# DESIGN PARAMETERS

This section summarizes the design parameters of the NuMI.

# Extraction and Primary beam  (see Debbie’s spec page for parameter revisions in progress)

# Proton Beam from Main Injector

| Proton beam energy | 120 GeV |
| --- | --- |
| Spill cycle time | 1.87 sec |
| Bunch length | 3-8 nsec |
| Batch length | 84 bunches |
| Bunch spacing | 18.8 nsec (53 MHz) |
| Emittance | 40( mm-mr expected 500 mm-mr max |
| Momentum spread | 2 x 10-4 (p/p 2 expected 23 x 10-3 (p/p 2 max |
| NuMI spill (pbar operation) | 5 batches x 84 + 4x3 = 432 bunches = 8.14 (sec |
| NuMI spill (no pbar operation) | 6 batches x 84 + 5x3 = 519 bunches = 9.78 (sec |
| Maximum intensity | 4 x 1013 ppp (protons/spill) |
| Total beam power | 404 kW at maximum intensity |

# Extraction Method and Parameters

| Extraction | Single turn |
| --- | --- |
| Method | 3 traveling wave kicker magnets |
| Position stability (transport) | ( 1 mm max |
| Beam size @ target | 1 mm H x 1 mm V (() |
| Position stability @ target | ( 250 ( |
| Angular stability @ target | ( 60 (-radian max |
| Max DC beam loss (MI region) | 10-4 at maximum intensity |
| Max DC beam loss (Carrier pipe) | 10-6 at maximum intensity |
| Max DC beam loss (Pre-target) | 10-4 at maximum intensity |
| Max beam loss - accident | 5 spills at maximum intensity |

# Instrumentation

| Dynamic range | 100 (= 4x1013/4x1011 protons/spill) |
| --- | --- |

| Profile monitors | Multi-wire SEM |
| --- | --- |
| Number of wires/plane | 48 of 0.003” gold plated tungsten wires |
| Transport region | 3 H + 3 V 1 mm wire spacing, motor-driven |
| Pre-Target | 2 H + 2 V 0.5 mm wire spacing,motor-driven |
| Position reproducibility | < 50 ( |
| Intensity range | 2.5x1011 ppp to 4x1013 ppp |
| Channel signal/noise | 100x over intensity range |
| Material in beam | <10-4 loss |

| Profile monitors | Ti Foil SEM (developed at UTA) |
| --- | --- |
| Thickness of Foils Spacing Width of Foils | 5 microns 1mm (0.5mm for 2 pre-target monitors) 0.25mm |
| MI Access region | 6 (H+V) |
| NuMI Access region | 6 (H+V) of which 2(H+V) are just upstream of target |
| Position reproducibility | < 50 (m (target) <100m (others) |
| Foil Alignment precision with respect to external fiducial | 0.005” (125m) |
| Intensity range | 2.5x1011 ppp to 4x1013 ppp |
| Channel signal/noise | 100x over intensity range |
| Vacuum Flange Size | 4” |
| Ion Pump Port on Vacuum Can | Yes |
| Readout | Once per pulse |
| Mounting Angle of vacuum can with respect to horizontal | 45o |

| Calibration Targets |  |
| --- | --- |
| Material in Beam | 10m Ti foil |
| MI Access region | 1 |
| NuMI Access region | 1 |
| Alignment tolerance | Modest |
| Position Reproducibility | Modest |
| Readout | None |
| Mounting Angle of vacuum can with respect to horizontal | 45o |
| Ion Pump Port on Vac. Can | Yes |
| Stands Required | Identical to Profile Monitors |

| Beam position monitors | Cylindrical plate BPM |
| --- | --- |
| Transport region | 6 H + 6 V |
| Position resolution | 0.2 mm rms within ( 20 mm for 3x1010 to 9.5x1010 protons/bunch |
| Intensity resolution | ( 3% |
| Sampling | One sample per batch |
| Calibration | Electronics charge injection inter-spill |
| Pre-target | 2 H + 2 V |
| Position resolution | 0.05 mm rms within ( 6 mm for 3x1010 to 9.5x1010 protons/bunch |
| Intensity resolution | ( 3% |
| Sampling | One sample per batch |
| Calibration | Electronics charge injection inter-spill |
| Position stability @ target | ( 250 ( |

| Beam position monitors | Cylindrical plate BPM |
| --- | --- |
| Transport region | 12 H + 10 V |
| Position resolution | 0.2 mm rms within ( 20 mm for 3x1010 to 9.5x1010 protons/bunch |
| Intensity resolution | ( 3% |
| Sampling | One sample per batch (80 bunches) |
| Calibration | Electronics charge injection inter-spill |
| Targeting | 2 H + 2 V |
| Position resolution | 0.05 mm rms within ( 6 mm for 3x1010 to 9.5x1010 protons/bunch |
| Intensity resolution | ( 3% |
| Sampling | One sample per batch (84 bunches) |
| Required readback time | 0.5 sec |
| Calibration BPM Electronics | Electronics charge injection inter-spill Needed for 28 BPM’s |
| Crate Locations | 13 Channels in MI60 Service Bldg (MI60N) 11 Channels in MI65 Service Bldg Electronics Room 4 Channels of Electronics for MI Quads (MI60N) |
| Position stability @ target | ( 250 ( |

|  | Transport BPM | Target BPM |
| --- | --- | --- |
| # Channels | 20 for NuMI + 4 for MI | 4 |
| System Type | Single Pass | Single Pass |
| Beam Bunch Freq | 53 MHz | 53 MHz |
| # Bunches | 84 x (1 to 6) | 84 x (1 to 6) |
| Dynamic Range (particles/bunch) | 5e9 – 10e10 | 5e9 – 10e10 |
| Processing BW | Single batch | Single batch |
| Position Accuracy (mm) RMS (may be too optimistic) | 0.2 @ 1e10 0.3 @ 4.5e9 (over +/- 20 mm) | @ 1e10 0.15 @ 4.5e9 (over +/- 6 mm) |
| Plate Diameter (mm) | 100 | 50 |
| Stability (mm) | ** | ** |
| Resolution (mm) | ** | ** |
| Processing Technology | Digital Receiver | Digital Receiver |
| Signal Cables | 3/8 in. Heliax | 3/8 in. Heliax |

| Toroid intensity monitor |  |
| --- | --- |
| Intensity resolution | 3% absolute for > 1x1013ppp 30% for > 3x1011ppp |
| Stability | < 3% at > 1x1013ppp |

| Toroid intensity monitor | 2 needed, 1 in MI access, one in NuMI access |
| --- | --- |
| Intensity resolution | 3% absolute for > 1x1013ppp |
| Stability | < 3% at > 1x1013ppp |
| Monitoring | None required |
| Readout | Once per pulse |
| Differential Signal | Not required in hardware |

| Beam loss monitors | 35 Sealed gas ionization chambers |
| --- | --- |
| Accuracy | ( 30% at 2x108ppp |
| Dynamic range | 2x108 to 4x1013ppp |
| Monitoring | High voltage status |
| Function | Sensitive to small localized losses |

| Beam loss monitors | 45 Sealed gas ionization chambers (+7 spares in beamline, + 8 spares upstairs) |
| --- | --- |
| Total Electronics Channels | Channels to read out 52 units |
| Accuracy | ( 30% at 2x108ppp |
| Dynamic range | 2x108 to 4x1012ppp |
| Monitoring | High voltage status |
| Function | Sensitive to small localized losses |
| Readout | Once per pulse |

| Total Loss Monitors | 4 coax hose ionization, Ar-CO2 purged |
| --- | --- |
| Carrier pipe region | 1 of 430' long, 2 of 215' long |
| Pre-target region | 1 spanning the entire region |
| Accuracy | ( 30% at 2x108ppp |
| Dynamic range | 2x108 to 4x1013ppp |
| Monitoring | Radioactive source current inter-spill |
| Function | Sensitive to large losses |

| Total Loss Monitors | 4 coax hose ionization, Ar-CO2 purged |
| --- | --- |
| MI Access region | 1 of 194' long, 1 of 220' long |
| NuMI Access region | 1 of 194’ long, 1 of 155’ long |
| Accuracy | ( 30% at 2x109ppp |
| Dynamic range | 2x109 to 4x1013ppp |
| Monitoring | Radioactive source current inter-spill High Voltage Status Gas Flow |
| Function | Sensitive to large losses |
| Readout | Once per pulse |

| Backup profile monitors | Multiwire SEM (developed at FNAL) |
| --- | --- |
| Thickness of wires Wire Spacing | 0.001” diameter W wire 1mm |
| MI Access region | 6 (H+V) |
| Position reproducibility | <100m |
| Foil Alignment precision with respect to external fiducial | 0.005” (125m) |
| Intensity range | 2.5x1011 ppp to 4x1013 ppp |
| Channel signal/noise | 100x over intensity range |
| Vacuum Flange Size | 4” |
| Ion Pump Port on Vacuum Can | Yes |
| Readout | Once per pulse |
| Mounting Angle of vacuum can with respect to horizontal | 45o |

# Neutrino Beam Devices

Low Energy Beam                  Peak at 3 GeV

Baffle/Target Module

| Module motion control |  |
| --- | --- |
| Baffle |  |
| composition | Graphite |
| aperture | 5.4 mm H x 12 mm V |
| length | 2 m |
| motion control | ~10 cm H (manual drive) |
| cooling | Air or RAW under consideration |
| Target |  |
| composition | Graphite segments (Poco ZXF-5Q) |
| length | 47 of 20 mm long segments, 0.3mm spacing |
| density | 1.686 ( 0.025 gm/cm3 |
| width | 6.4 mm |
| height | 18 mm |
| cooling | RAW cooling tubes top/bottom of fin |
| distance from horn 1 | 35 cm to Monte Carlo upstream end |
| motion control | ~1 m Z insertion into Horn 1 (manual drive) |

Neutrino Horn 1 Module

| Horn shape | Double Parabolic |
| --- | --- |
| Construction | Nickel plated aluminum inner conductor Anodized aluminum outer conductor |
| Minimum aperture field-free neck | 9 mm radius |
| Inner conductor thickness | 2 mm (min) – 4.5 mm (max at neck) |
| Outer conductor | 11.75 inch I.D. 13.75 inch O.D. |
| Horn Length | 300 cm focus region, 132 inches overall |
| Current | 200 kA |
| Motion control | (1 cm H x (1 cm V each end (motor drive) |
| Horn cooling | RAW spray, 30 gal/min |

Neutrino Horn 2 Module

| Horn shape | Double Parabolic |
| --- | --- |
| Construction | Nickel plated aluminum inner conductor Anodized aluminum outer conductor |
| Minimum aperture field-free neck | 3.9 cm radius |
| Inner conductor thickness | 3 mm (min) - 5 mm (max) |
| Outer conductor | 29.134 inch I.D. 31.134 inch O.D. |
| Horn Length | 300 cm focus region, 143 inches overall |
| Current | 200 kA |
| Motion control | None |
| Distance from Horn 1 | 10 m (upstream end H1 to upstream end H2) |
| Horn cooling | RAW spray, 30 gal/min |

# Power Supply Systems

Kicker Power Supply :         Single pulse forming network, drives 2 magnets in parallel

Conventional Power Supplies Regulation requirements

| Lam60 | 200 ppm |
| --- | --- |
| V100 | 400 ppm |
| HV101 | 65 ppm |
| V104 | 200 ppm |
| V105 | 60 ppm |
| V109 | 200 ppm |
| V110 | 55 ppm |
| Trims | 0.1% |
| Quadrupoles | 400 ppm |

Horn Power Supply, current, voltage, Flat top regulation, Pulse width

The design criteria for the horn power supply and stripline are the current, current regulation, and pulse width. Horn 1 and horn 2 are connected in series with the power supply. The voltage is given at the output of the power supply. It is determined by the resistance and inductance of the strip line and horns. When we switched to single turn extraction, the power supply design was modified to give a pulse width of 2.6 msec. The section of stripline to the high energy horn 2 position was later eliminated, shortening the pulse length to 1.7 msec. The "flat-top" regulation is the allowed pulse to pulse variation.

Horn Power Supply :  Series connection to Horn 1 and Horn 2

| Peak current | 240k A |
| --- | --- |
| Operating current | 200k A average ( 2.5% |
| Current monitoring | 0.4% |
| Operating voltage | 800 V |
| Repeatability | ( 1% pulse to pulse |
| Pulse width | ~half-sine 1.7 ms @ base |
| Pulse period | 1.9 sec |

Horn Stripline

| Construction | 30 cm x 10 cm Aluminum strips, 1 cm spacing |
| --- | --- |
| Resistance | 10 ((/m |
| Inductance | 16 nH/m |

# Hadron Decay Pipe

| Size | 1.98 m inner dia x 677.1 m long |
| --- | --- |
| Vacuum | <1 Torr |
| Upstream vacuum window | 4.76 mm thick steel |
| Downstream vacuum window | 6.35 mm thick steel |

# Hadron Absorber

| Primary beam size at Absorber (target out) | 5.4 cm H x 7.9 cm V (1 () |
| --- | --- |
| Primary beam size at Absorber (target in) | 29 cm (rms) |
| Beam power - normal | 64 kW (82% primary protons, 18% secondaries) |
| Beam power - accident | 404 kW |
| Accident condition | 1 hour (1900 pulses) mis-targeted primary proton |
| Absorber core | 8 aluminum modules + 10 steel CCSS layers |
| Aluminum modules | 1.29 m H x 1.29 m V x 30 cm Z RAW cooled |
| Steel CCSS layers | 1.29 m H x 1.29 m V x 23 cm Z |
| Max temperature - normal | 60 oC in aluminum modules 3 and 4 270 oC in steel module 1 |
| Max temperature - accident | 160 oC in aluminum modules 3 and 4 800 oC in steel module 1 |

# Neutrino Beam Monitoring

The NuMI beam monitoring system consists of 1 plane of Hadron Monitors (DHM) downstream of the decay pipe and upstream of the Hadron Absorber, 3 planes of Muon monitors located in the Hadron Absorber enclosure (Muon Alcove 0) , Muon Alcove 1 and Muon Alcove 2. The peak charged particle fluxes per spill in the various monitoring locations, assuming 4x1013 protons per spill.

| Station | Maximum Flux/spill |
| --- | --- |
| DHM | 2.5x109/cm2 |
| Alcove 0 | 3.2 x107/cm2 |
| Alcove 1 | 1.7x107/cm2 |
| Alcove 2 | 0.22x107/cm2 |

The following table gives the fluxes per spill, and the associated radiation doses per year, expected in the monitoring locations, as a function of particle type.  Doses calculated by translating fluxes to Sieverts and then to rads, taking into account spectral information

| Station | Particle | Flux (/cm2/spill) | Dose/year(Rads) |
| --- | --- | --- | --- |
| DHM | protons | 1.3x109 | 13Grad |
| DHM | other charged hadrons | 2.0x109 | 0.3Grad |
| DHM | neutrons | 3.5x109 | 0.2Grad |
| Alcove 0 | neutrons | 10.0x107 | 10Mrad |
| Alcove 0 | muons | 1.30x107 | 5Mrad |
| Alcove 1 | muons | 0.40x107 | 1.8Mrad |
| Alcove 1 | neutrons | 0.04x107 | 0.1Mrad |
| Alcove 2 | muons | 0.14x107 | 0.6Mrad |
| Alcove 2 | neutrons | 0.04x107 | 0.04Mrad |

# Alignment Systems

Alignment tolerances for Low Energy beam

| Beam position at target | ( 0.45 mm |
| --- | --- |
| Beam angle at target | ( 0.7 mrad |
| Target position - each end | ( 0.5 mm |
| Horn 1 position - each end | ( 0.5 mm |
| Horn 2 position - each end | ( 0.5 mm |
| Decay pipe position | ( 20 mm |
| Downstream Hadron monitor | ( 25 mm |
| Muon Monitors | ( 25 mm |
| Near Detector | ( 25 mm |
| Far Detector | ( 12 mm |

# Water, Vacuum & Gas Systems

CUB = Central Utility Building

CW = Chilled Water

LCW = Low Conductivity Water

PW = Pond Water

RAW = Radioactive Water

SB = Service Building

Power dissipation

| Beam transport magnets | 628 kW |
| --- | --- |
| MI-62 LCW system | 700/1200 (kW nominal/max) to MI Pond G |
| MINOS LCW system | 108/200 (kW nominal/max) to MINOS SB CW |
| Absorber RAW | 60/200 (kW nominal/max) to MINOS SB PW |
| Decay pipe RAW | 150/200 (kW nominal/max) to CUB CW (1/2) and MINOS SB CW (1/2) |
| Target RAW | 10/25 (kW nominal/max) to MI62 LCW |
| Horn 1 RAW | 40/200 (kW nominal/max) to CUB CW |
| Horn 2 RAW | 10/50 (kW nominal/max) to CUB CW |

Vacuum

| Main Injector extraction region | 10-8 Torr |
| --- | --- |
| Primary beam transport vacuum | 10-6 Torr |
| Carrier pipe |  |
| Diameter | 12” |
| Vacuum maximum | 10-5 Torr |
| Vacuum expected | 7 x 10-7 Torr maximum |
| Hadron Decay Pipe vacuum | 0.1 to 1 Torr |

Carrier Pipe size, vacuum

The 430' long carrier pipe diameter was determined by an informal cost/benefit analysis. The pipe size is much larger than all magnet apertures, however the consequence of a significant beam loss in the carrier pipe region is severe. The maximum vacuum level is determined by the ground water requirement during normal operation due to interactions with the residual gas. The expected vacuum level is achieved in the middle of the carrier pipe by 3 large ion pumps located at each end of the carrier pipe.

# Installation & Integration

| Controls | Power supplies, instrumentation, vacuum, water, beam position & intensity, beam permit, beam loss budget monitor |
| --- | --- |
| Beam permit System | Power suppy current & voltage nominal Multi-wire fully inserted/extracted Loss monitors nominal Vacuum valves open Previous Main Injector spill transport nominal BPM positions nominal Target Budal monitor nominal |

# Commissioning

| Beam intensity | 5 x 1012 ppp |
| --- | --- |
| Near detector fiducial mass | 0.015 kt (40 planes tgt region, 75 cm radius) |
| Near Detector exposure | 2 x 10-6 kt-yr/day |