| Process Checklist for Requirements Phase |
| --- |
| Overview | The Complex Electronics requirements are derived from system and sub-system requirements. The requirements process includes: Deriving CE requirements from higher level system requirements Performing a feasibility assessment Performing a risk analysis |
| Entrance Criteria | The following criteria should be met prior to beginning the requirements phase for complex electronics: The system requirements are complete and baselined, or at least sufficiently complete to allow derivation of requirements for sub-systems and the complex electronics. Sub-system requirements for the sub-system(s) the complex electronics reside in are sufficiently complete and baselined. As with the system requirements, the level of fidelity must be sufficient to allow derivation of the complex electronics requirements to commence. The Configuration Management process is defined and in operation. The Complex Electronics Assurance Plan is created and operational. The assurance engineers responsible for the complex electronics have been identified. The proposed technology set (e.g., FPGA, ASIC, SoC, chip family) is identified at a high level. |
| Responsible Personnel | Design Engineer - Derive complex electronics requirements. Quality Assurance – Perform the process and product assurance activities listed below. System Safety – Evaluate requirements for safety impacts and inclusion of safety features. Systems Engineer – Ensure proper derivation of requirements. |
| Not all steps listed below have to be completed sequentially. When a step is finished, the completion date is added to the table below, along with initials of the assurance representative. |

| ID | Process Step | Completion Date | QA |
| --- | --- | --- | --- |
| 1 | Entrance Criteria are met. |  |  |
| 2 | Review the complex electronics requirements document prepared by the CE designer (engineer). Assess the requirements derivation and ensure all higher-level requirements are properly flowed down to the complex electronics. |  |  |
| 3 | Review the feasibility assessment. |  |  |
| QA Analyses for this phase |  |  |
| 4a | Risk analysis |  |  |
| 4b | Reverse Engineering of Requirements |  |  |
| 4c | Requirements Evaluation |  |  |
| 4d | Requirements Review (participate in) |  |  |
| 4e | Interface Analysis to verify correct interfaces |  |  |
| 4f | Traceability Analysis |  |  |
| 4g | Simulation or Modeling of the complex electronics |  |  |
| 4h | Formal Methods – Requirements specification |  |  |
| 4i | Decision Tables/Trees |  |  |
| 4j | Fault Tree Analysis |  |  |
| 4k | Failure Modes and Effects Analysis |  |  |
| Review the following documents (or information included within higher-level documents) that are created at this phase. Approve where authorized. |  |  |
| 5 | - Complex Electronics Requirements |  |  |
| 6 | - Interface Control Document |  |  |
| 7 | - Testing Plan for the complex electronics |  |  |
| Review any updates to these plans. Ensure that new information is incorporated in the plans. |  |  |
| 8 | - Complex Electronics Development Plan |  |  |
| 9 | - Verification and Validation Plan |  |  |
| 10 | - Configuration Management. |  |  |
| 11 | - Problem Reporting and Corrective Action process |  |  |
| 12 | - Safety Plan |  |  |
| 13 | - Risk Management Plan |  |  |
| 14 | Update the Complex Electronics Assurance Plan to reflect any changes in the assurance process. Re-evaluate the classification of the complex electronics and adjust tasks as appropriate. |  |  |
| 15 | Exit Criteria are met. |  |  |

| Exit Criteria | At the end of the requirements phase, the following criteria should be met: Requirements for complex electronics are baselined and under configuration control. |
| --- | --- |

| Documentation Status |
| --- |
| Document ID | Document Name | Revision | Date |
|  | Complex Electronics Requirements |  |  |
|  | Interface Control Document |  |  |
|  | Complex Electronics Testing Plan |  |  |
|  | Complex Electronics Development Plan |  |  |
|  | Complex Electronics Assurance Plan |  |  |
|  | Verification and Validation Plan |  |  |
|  | Configuration Management Plan |  |  |
|  | Safety Plan |  |  |
|  | Risk Management Plan |  |  |
|  | Problem Reporting/Resolution Process |  |  |