# IEEE P1451.3 Proposal

| Proposal Title: | Pre-trigger acquisition |
| --- | --- |
| Proposal Number: | 2002-23 |
| Revision Number: |  |
| Date: | 10/12/02 |
| Name: | Lee Eccles |
| Company: | Boeing Commercial Airplanes |
| Phone Number: | (206) 655-2824 |
| Fax Number: | (206) 655-7724 |
| Email Address: | Lee.h.eccles@boeing.com |
| Proposal Status: | Initial Draft Revised Draft Ready for Vote |
| Impacts: | __ __ |
| Action: | _X Approved __ Approved with changes __ Rejected __ Returned for revision |

Background:

Catlin-11

4.6 – Standard does not allow for pre-trigger acquisition of data.

This proposal assumes that proposal2002-19 has been accepted.

The proposal below should be considered a starting point for discussion.

Proposal:

#### 5.6.1.2	Free-running without pre-trigger

In the free-running sampling mode, a sensor is measuring some physical parameter autonomously and continuously when in the operating state. The data being acquired and converted is discarded until a trigger is received. Once a trigger has been received, the next sample converted is stored in the TBIM as the first word in the data set. Consecutive samples are stored in the TBIM until the entire data set is completed. At this point, the TransducerChannel returns to discarding samples until the next trigger is received. The sampling operation of a TransducerChannel when in the halted state is at the discretion of the manufacturer.

An actuator operating in the free-running sampling mode shall apply the data set received before the trigger in accordance with its End-of-data-set Operating mode.

#### 5.6.1.3	Free-running with pre-trigger

The following two sub-clauses describe the operation of a sensor when operating in the free-running mode with or without buffers enabled.

An actuator may not be operated in the free-running with pre-trigger mode.

#### 5.6.1.3.1	Free-running with pre-trigger without buffers enabled

In the free-running sampling mode, a sensor is measuring some physical parameter autonomously and continuously when in the operating state. The data being acquired and converted is stored until a trigger is received or the pre-trigger count (see 6.1.1.4) is reached. After the number of samples that have been stored reaches the pre-trigger count, the next sample acquired shall cause the oldest sample to be discarded and the new sample stored. After a trigger has been received, the next sample converted is stored in the TBIM as the next word in the data set. Consecutive samples are stored in the TBIM until the entire data set is completed. The data set shall be complete when the number of samples equal to the data set size minus the pre-trigger count has been acquired after the trigger is received. At this point the TransducerChannel returns to discarding samples until the next trigger is received or the data set is read. After the data set is read the TransducerChannel shall start storing samples again while waiting for another trigger. In this mode the data set may only be read once. Subsequent reads before the next trigger will return zero octets. The sampling operation of a TransducerChannel when in the halted state is at the discretion of the manufacturer.

#### 5.6.1.3.1	Free-running with pre-trigger and buffers enabled

In the free-running sampling mode, a sensor is measuring some physical parameter autonomously and continuously when in the operating state. The data being acquired and converted is stored until a trigger is received or the pre-trigger count (see 6.1.1.4) is reached. After the number of samples that have been stored reaches the pre-trigger count, the next sample acquired shall cause the oldest sample to be discarded and the new sample stored. Once a trigger has been received, the next sample converted is stored in the TBIM as the next word in the data set. Consecutive samples are stored in the TBIM until the entire data set is completed. The data set shall be complete when the number of samples equal to the data set size minus the pre-trigger count has been acquired after the trigger is received. The TransducerChannel shall switch to the next empty buffer and start acquiring data samples for the next data set. If no empty buffers are available it shall discard any samples acquired until a buffer becomes available. A buffer shall be considered available after it has been read. The sampling operation of a TransducerChannel when in the halted state is at the discretion of the manufacturer.

### 6.1.1	Initialization commands

No text changes

Table 1—Initialization commands

| Function | Command | Address | Required/ Optional |
| --- | --- | --- | --- |
|  |  | TBIM | TransducerChannel | Global | Group |  |
|  |  |  | Normal | Proxy |  |  |  |
| 0 | Reserved | — | — | — | — | — | — |
| 1 | Sleep | Yes | Yes | Yes | Yes | Yes | Optional |
| 2 | Wake-up | Yes | Yes | Yes | Yes | Yes | Optional |
| 3 | Set TransducerChannel data repetition count | Yes | Yes | No | Yes | Yes | Optional |
| 4 | Set TransducerChannel pre-trigger count | Yes | Yes | No | Yes | Yes | Optional |
| 5 | Calibrate TransducerChannel | Yes | Yes | Yes | Yes | Yes | Optional |
| 6 | Zero TransducerChannel | Yes | Yes | Yes | Yes | Yes | Optional |
| 7 | Logical CommunicationsChannel assignment | No | Yes | Yes | No | No | Required |
| 8 | Enable corrections | Yes | Yes | Yes | No | No | see 0 |
| 9 | Disable corrections | Yes | Yes | Yes | No | No | see 0 |
| 10 | Enable transducer | Yes | Yes | Yes | Yes | Yes | Required |
| 11 | AddressGroup definition | Yes | Yes | Yes | No | No | Required |
| 12 – 127 | Reserved | — | — | — | — | — | — |
| 128 – 255 | Open for manufacturers | — | — | — | — | — | — |

#### 6.1.1.1	Sleep

No text changes

#### 6.1.1.2	Wake-up

No text changes

#### 6.1.1.3	Set TransducerChannel data repetition count

No text changes

#### 6.1.1.4	Set TransducerChannel pre-trigger count

This command is used by Transducerchannels that are capable of being operated in the free-running with pre-trigger mode to change the number of data samples in a data set that can be acquired and stored before the receipt of a trigger. This number may be any number between zero the number found in the Maximum data repetitions field of the TransducerChannel TEDS. The only argument to this command is a sixteen-bit integer. If the value of the argument exceeds the Maximum data repetitions, the pre-trigger count shall be set to the Maximum data repetitions and the TBIM invalid command bit shall be set in the status register.

If an acknowledgment is required for this command, the reply shall contain the thirty-two-bit status word for the TBIM in the data field (see 5.10).

#### 6.1.1.5	Calibrate TransducerChannel

No text changes

#### 6.1.1.6	Zero TransducerChannel

No text changes

#### 6.1.1.7	Logical CommunicationsChannel assignment

No text changes

#### 6.1.1.8	Enable corrections

No text changes

#### 6.1.1.9	Disable corrections

No text changes

#### 6.1.1.10	Enable TransducerChannel

No text changes

#### 6.1.1.11	AddressGroup definition

No text changes

### 6.1.7	Set operating mode commands

No text changes

Table 21—Operating mode command functions

| Function | Operational mode | Choices | Value | Related TEDS Field |
| --- | --- | --- | --- | --- |
| 0 | Reserved | — | — | — |
| 1 | Sampling mode | Trigger-initiated | 1 | Table 45 |
|  |  | Free-running without pre-trigger | 2 |  |
|  |  | Free-running with pre-trigger | 3 |  |
| 2 | Buffered mode | Unbuffered | 1 | Table 46 |
|  |  | Buffered | 2 |  |
| 3 | End-of-data-set operation | Hold | 1 | Table 47 |
|  |  | Recirculate | 2 |  |
| 4 | Streaming mode | Off | 1 | Table 48 |
|  |  | On | 2 |  |
| 5 | Edge-to-report mode | Rising | 1 | Table 49 |
|  |  | Falling | 2 |  |
|  |  | both | 3 |  |
| 6 | Actuator-halt | Hold | 1 | Table 50 |
|  |  | Finish data set | 2 |  |
|  |  | Ramp | 3 |  |
| 7 - 127 | Reserved | — | — | — |
| 128 - 255 | open to manufacturers | — | — | — |

## 7.4	TransducerChannel TEDS

No text changes

### 7.4.1	Access

No text changes

### Data block

No text changes

Table 38—Structure of the TransducerChannel TEDS data block

| Field | Description | Type | # octets |
| --- | --- | --- | --- |
| — | TEDS length | U32L | 4 |
| 1 | TEDS identifier | U8E | 1 |
| — | TransducerChannel related information | — | — |
| 2 | Calibration key | U8E | 1 |
| 3 | TransducerChannel type key | U8E | 1 |
| 4 | Physical units | UNITS | 10 |
| 5 | Lower range limit | F32 | 4 |
| 6 | Upper range limit | F32 | 4 |
| 7 | Worst-case uncertainty | F32 | 4 |
| 8 | Self-test key | U8E | 1 |
| — | Data converter related information | — | — |
| 9 | Data model | U8E | 1 |
| 10 | Data model length | U8C | 1 |
| 11 | Model significant bits | U16C | 2 |
| 12 | Maximum data repetitions | U16C | 2 |
| 13 | Series origin | F32 | 4 |
| 14 | Series increment | F32 | 4 |
| 15 | Series units | UNITS | 10 |
| 16 | Maximum pre-trigger samples | U16C | 2 |
| — | Timing related information | — | — |
| 17 | TransducerChannel update time (tu) | F32 | 4 |
| 18 | TransducerChannel write setup time (tws) | F32 | 4 |
| 19 | TransducerChannel read setup time (trs) | F32 | 4 |
| 20 | TransducerChannel sampling period (tsp) | F32 | 4 |
| 21 | TransducerChannel warm-up time | F32 | 4 |
| 22 | TransducerChannel read delay time (tch) | F32 | 4 |
| 23 | TransducerChannel self-test time requirement | F32 | 4 |
| — | Time of the sample information | — | — |
| 24 | Source for the time of sample | U8E | 1 |
| 25 | Incoming propagation delay through the data transport logic with sync | F32 | 4 |
| 26 | Incoming propagation delay through the data transport logic without sync | F32 | 4 |
| 27 | Outgoing propagation delay through the data transport logic | F32 | 4 |
| 28 | Trigger-to-sample delay uncertainty with sync | F32 | 4 |
| 29 | Trigger-to-sample delay uncertainty without sync | F32 | 4 |
| — | Attributes | — | — |
| 30 | Sampling attribute | U8E | 1 |
| 31 | Buffered attribute | U8E | 1 |
| 32 | End-of-data-set operation attribute | U8E | 1 |
| 33 | Streaming attribute | U8E | 1 |
| 34 | Edge-to-report attribute | U8E | 1 |
| 35 | Actuator-halt attribute | U8E | 1 |
| — | Sensitivity | — | — |
| 36 | Sensitivity direction | F32 | 4 |
| 37 | Direction angles | Two F32 | 8 |
| — | Options | — | — |
| 38 | Event sensor options | U8E | 1 |
| — | Checksum | U16C | 2 |

#### 7.4.2.1	TEDS identifier

No text changes

#### 7.4.2.2	Calibration key

No text changes

#### 7.4.2.3	TransducerChannel type key

No text changes

#### 7.4.2.4	Physical units

No text changes

#### 7.4.2.5	Lower range limit

No text changes

#### 7.4.2.6	Upper range limit

No text changes

#### 7.4.2.7	Worst-case uncertainty

No text changes

#### 7.4.2.8	Self-test key

No text changes

#### 7.4.2.9	Data model

No text changes

#### 7.4.2.10	Data model length

No text changes

#### 7.4.2.11	Model significant bits

No text changes

#### 7.4.2.12	Maximum data repetitions

No text changes

#### 7.4.2.13	Maximum pre-trigger samples

Data type: unsigned octet integer used for counting (U16C, 2 octets)

This field contains the number, L, of repetitions of the TransducerChannel value that may be sampled and stored prior to a trigger when operating in the free-running with pre-trigger mode. Each repetition represents an additional measurement value produced by the TransducerChannel, which shall be spaced apart from the initial value along some axis (for example time) by an amount defined by the TransducerChannel TEDS fields Series increment (7.4.2.14) and Series units (7.4.2.15) respectively. When L is zero, the sensor may not be operated in the free-running pre-trigger mode.

In operation, the number of TransducerChannel values that may be acquired and stored prior to a trigger may be set to any value lower than the contents of this field by issuing the Set TransducerChannel pre-trigger count command as defined in 6.1.1.4.

When reading or writing data with data repetition count greater than zero, the order of transmittal shall be with the zeroth (oldest) data sample transmitted first, the first repetition transmitted second, etc.

#### 7.4.2.14	Series origin

No text changes

#### 7.4.2.15	Series increment

No text changes

#### 7.4.2.16	Series units

No text changes

#### 7.4.2.17	TransducerChannel update time

No text changes

#### 7.4.2.18	TransducerChannel write setup time

No text changes

#### 7.4.2.19	TransducerChannel read setup time

No text changes

#### 7.4.2.20	TransducerChannel sampling period

No text changes

#### 7.4.2.21	TransducerChannel warm-up time

No text changes

#### 7.4.2.22	TransducerChannel read delay time

No text changes

#### 7.4.2.23	TransducerChannel self-test time requirement

No text changes

#### 7.4.2.24	Source for the time of sample

No text changes

#### 7.4.2.25	Incoming propagation delay through the data transport logic

No text changes

#### 7.4.2.26	Incoming propagation delay through the data transport logic without sync

No text changes

#### 7.4.2.27	Outgoing propagation delay through the data transport logic

Text not changed

#### 7.4.2.28	Trigger-to-sample delay uncertainty with sync

Text not changed

#### 7.4.2.29	Trigger-to-sample delay uncertainty without sync

Text not changed

#### 7.4.2.30	Sampling attribute

Data type: unsigned 8-bit integer used for enumeration (U8E, 1 octet)

This attribute is used to describe which Sampling modes (see 5.6.1) are support by this TransducerChannel. Table 45 lists the allowable values for this attribute.

Table 45—Sampling attribute

| Value | Description |
| --- | --- |
| 0 | Reserved |
| 1 | This TransducerChannel is only capable of being operated in the trigger-initiated sampling mode as described in 5.6.1.1 |
| 2 | This TransducerChannel is only capable of being operated in the free-running sampling mode without pre-triggering as described in 5.6.1.2 |
| 3 | This TransducerChannel is only capable of being operated in the free-running sampling mode with pre-triggering as described in 5.6.1.3 |
| 4 | This TransducerChannel may be operated with either the trigger-initiated sampling mode or the free-running sampling mode without pre-triggering. The trigger-initiated sampling mode is the default. |
| 5 | This TransducerChannel may be operated with either the trigger-initiated sampling mode or the free-running sampling mode with pre-triggering. The trigger-initiated sampling mode is the default. |
| 6 | This TransducerChannel may be operated with either the trigger-initiated sampling mode or either of the free-running sampling modes. The trigger-initiated sampling mode is the default. |
| 7 | This TransducerChannel may be operated with either the trigger-initiated sampling mode or either of the free-running sampling modes. The free-running sampling mode without pre-triggering is the default. |
| 8 | This TransducerChannel may be operated with either the trigger-initiated sampling mode or either of the free-running sampling modes. The free-running sampling mode with pre-triggering is the default. |
| 5 - 255 | Reserved |

#### 7.4.2.31	Buffered attribute

No text changes

#### 7.4.2.32	End-of-data-set operation attribute

No text changes

#### 7.4.2.33	Streaming attribute

No text changes

#### 7.4.2.34	Edge-to-report attribute

No text changes

#### 7.4.2.35	Actuator-halt attribute

No text changes

#### 7.4.2.36	Sensitivity direction

No text changes

#### 7.4.2.37	Direction angles

No text changes

#### 7.4.2.38	Event sensor options

No text changes