Ford is recalling 8,585 MY 2001-2002 Explorer sport vehicles equipped with high back seats.   The upper bolt on the driver's side high back seat, that attaches the seat recliner mechanism to the seat back frame, could fracture.  If the bolt fractures, the seat back may recline until it makes contact with an object behind the seat, such as the second row seat cushion.  The driver could potentially lose contact with the steering wheel or foot pedals during such an event, increasing the risk of a crash.  Dealers will replace the driver seat upper bolt with a metal spacer and bolt.  In addition, seats with tubular back frames will have the fully threaded lower recliner bolt replaced with a partially threaded bolt.  The recall is expected to begin on April 10, 2006.  This is a supplement to a previous recall campaign (03V-281).  06V-114