LARP: Magnet-Connection Interface Definitions for TQC01

Authors: N. Andreev, J. Blowers, R. Bossert, S. Feher, F. Lewis, M. Whitson (FNAL)

Review History:

| Revision DRAFT: | Date: |
| --- | --- |
| Revision A: | Date: |
| Revision B: | Date: |
| Revision C: | Date: |
| Revision D: | Date: |
| Revision E: | Date: |
| Last Reviewed: | Date: |
| Approved for Trial: | Date: |
| Final Approval: | Date: |

------------------------------ TABLE OF CONTENTS ----------------------------

1.0	PURPOSE OF Document:	3

2.0	General Specifications	3

3.0	MECHANICAL INTERFACES	3

4.0	ELECTRICAL INTERFACES	5

5.0	DIAGNOSTIC DEVICE CALIBRATIONS	9

6.0	KNOWN ISSUES	10

# PURPOSE OF Document:

The purpose of this document is to communicate the all interfaces for magnet TQC01.

# General Specifications

TQC01 is the first “Technological Quadrupole” using the collared coil design (same design as the LHC IR quadrupoles, i.e. collar and stainless steel shell; low axial preload). The purpose is to compare the two prevalent designs for Nb3Sn magnets (the other design is referred to as TQS and uses an aluminum shell over an iron yoke; high axial preload).

Table 1 is a summary of the TQC parameters.

| Item | Value |
| --- | --- |
| Length | 46.750 inches |
| Mass | 2260 lbs |
| Outer Diameter | 16 11/16 inches |
| Aperture | 90mm |
| Type | Cos2θ |
| Strand | MJR |
| Maximum current |  |
| Nominal Field Gradient | 200 T/m |
| Peak Field Gradient | 215-265 T/m |
| Peak Coil Field | 11-13 T |
| Total resistance (room temp.) | 0.71915 Ω |
| L (1KHz) | 2.0944 mH |
| Q (1KHz) | 2.34 |
| L (20 Hz) | 3.3247 mH |
| Q (20 Hz) | 0.57 |
| 1 KV Hipot (coil to ground) | 0.05 μA |
| 1 KV Hipot (heaters to ground) | 0.05 μA |
| 1 KV Hipot (heaters to coil) | 0.02 μA |

Table 1 – TQC parameters

# MECHANICAL INTERFACES

Overall the mechanical interfaces are defined by the physical magnet dimensions and the support points for testing preparation and installation into the test dewar. The overall dimensions of TQC01 are reported in figure 1a below. The support structure for TQC01 is different from the “standard” scheme which will be followed for all subsequent magnets. The standard supports will consist of threaded holes on the top plate according to drawing XXX. TQC01 uses holes down the length of the magnet to insert threaded rod and connect a support plate underneath the magnet assembly, per figure 1b below.

Figure 1a – Dimensions of TQC01 (source: Marty Whitson)

Figure 1b – Sketch of TQC01 lead end

# ELECTRICAL INTERFACES

Electrical connections consist of voltage taps, protection heaters, spot heaters, low-voltage connections (for strain gauges and temperature sensors), and magnet power. Figures 2a through 2c contain the hypertronics connector layouts. Figure 3a is the intra-coil wiring diagram (coil connections and voltage tap placements), and table 2 shows the voltage tap distances on each coil. The spreadsheet which contains the wiring connections for TQC01 is maintained in a separate document (LARP-doc-347):

https://larpdocs.fnal.gov/LARP-private/DocDB/ShowDocument?docid=347.

Figure 2a - Voltage Tap Connector Layout (solder-cup view of female)

Figure 2b - Heater Connector Layout.  Magnet side uses male (pins). Modules are numbered according to the Hypertronics convention.

Figure 2c – Low-Voltage Connector Layout

Figure 3a – Intra-coil Wiring Diagram for TQC01 (source: Rodger Bossert)

Tap Distances (-) Lead Saddle to Taps

|  | Q4 INNER |  |  |  | Q4 OUTER |  |
| --- | --- | --- | --- | --- | --- | --- |
| ( - ) Q4-I | COIL 12 |  |  | Q4-O/Q2-I | COIL 12 |  |
| V TAP | DISTANCE |  |  | V TAP | DISTANCE |  |
| NAME | IN mm | Notes |  | NAME | IN mm | Notes |
| VTLN | (-)307.0 | run along (-) power lead |  | VT12B6 | 29808.5 |  |
| VTMN | (-)307.0 |  |  | VT12B5 | 30364.8 |  |
| VT012A1 | (-)2.0 |  |  | VT12B4 | 30503.1 |  |
| VT12A2 | 127 |  |  | VT12B3 | 31056.3 |  |
| VT12A3 | 20227.4 |  |  | VT12BSH2 | 52399.2 |  |
| VT12A4 | 20787.2 |  |  | VT12BSH1 | 52459.2 |  |
| VT12A5 | 22312.8 |  |  | VT12B2 | 53388.2 |  |
| VT12A6 | 28186.3 |  |  | VT12B1 | 53517.2 |  |
| VT12A7 | 28350.7 |  |  | VTQ24N | 53664.2 |  |
| VT12A8 | 28895 |  |  | VTQ24P | 53664.2 |  |
| VT12A9 | 29087.3 |  |  | VTQ24 | 53664.2 |  |
| VT12A10 | 29474.1 |  |  |  |  |  |
|  | Q2 INNER |  |  |  | Q2 OUTER |  |
| Q2-I/Q2-0 | COIL 10 |  |  | Q2-O/Q1-O | COIL 10 |  |
| V TAP | DISTANCE |  |  | V TAP | DISTANCE |  |
| NAME | IN mm | Notes |  | NAME | IN mm | Notes |
| VT10A1 | 53952.2 |  |  | VT10B6 | 83761.9 |  |
| VT10A2 | 54081.2 |  |  | VT10B5 | 84318.2 |  |
| VT10A3 | 74181.6 |  |  | VT10B4 | 84456.5 |  |
| VT10A4 | 74741.4 |  |  | VT10B3 | 85009.7 |  |
| VT10A5 | 76266.2 |  |  | VT10B2 | 107341.6 |  |
| VT10A6 | 82140.5 |  |  | VT10B1 | 107470.6 |  |
| VT10A7 | 82304.9 |  |  | VTMCN | 107782.2 |  |
| VT10A8 | 82848.4 |  |  | VTMCP | 107782.2 |  |
| VT10A9 | 83040.8 |  |  | VTMHN | 107782.2 |  |
| VT10A10 | 83427.5 |  |  | VTMHP | 107782.2 |  |
|  | Q1 OUTER |  |  |  | Q1 INNER |  |
| Q1-O/Q1-I | COIL 13 |  |  | Q1-I/Q3-0 | COIL 13 |  |
| V TAP | DISTANCE |  |  | V TAP | DISTANCE |  |
| NAME | IN mm | Notes |  | NAME | IN mm | Notes |
| VT13B1 | 107929.2 |  |  | VT13A10 | 131964.3 |  |
| VT13B2 | 108058.2 |  |  | VT13A9 | 132351.1 |  |
| VT13BSH1 | 108979.2 |  |  | VT13A8 | 132543.5 |  |
| VT13BSH2 | 109039.2 |  |  | VT13A7 | 133087.0 |  |
| VT13B3 | 130382.1 |  |  | VT13A6 | 133251.4 |  |
| VT13B4 | 130935.3 |  |  | VT13A5 | 139125.7 |  |
| VT13B5 | 131073.6 |  |  | VT13A4 | 140650.5 |  |
| VT13B6 | 131629.9 |  |  | VT13A3 | 141210.3 |  |
|  |  |  |  | VT13A2 | 161310.7 |  |
|  |  |  |  | VT13A1 | 161439.7 |  |
|  |  |  |  | VTQ13 | 161727.7 |  |
|  |  |  |  | VTQ13N1 | 161727.7 |  |
|  |  |  |  | VTQ13P1 | 161727.7 |  |
|  | Q3 OUTER |  |  |  | Q3 INNER |  |
| Q3-0/Q3-I | COIL 09 |  |  | Q3-I (+) | COIL 09 |  |
| V TAP | DISTANCE |  |  | V TAP | DISTANCE |  |
| NAME | IN mm | Notes |  | NAME | IN mm | Notes |
| VT09B1 | 161874.7 |  |  | VT09A10 | 185917.8 |  |
| VT09B2 | 162003.7 |  |  | VT09A9 | 186304.6 |  |
| VT09B3 | 184335.6 |  |  | VT09A8 | 186497.0 |  |
| VT09B4 | 184888.8 |  |  | VT09A7 | 187040.5 |  |
| VT09B5 | 185027.1 |  |  | VT09A6 | 187204.9 |  |
| VT09B6 | 185583.4 |  |  | VT09A5 | 193079.2 |  |
|  |  |  |  | VT09A4 | 194604.0 |  |
|  |  |  |  | VT09A3 | 195163.8 |  |
|  |  |  |  | VT09A2 | 215264.2 |  |
|  |  |  |  | VT09A1 | 215393.2 |  |
|  |  |  |  | VTMP | 215544.2 |  |
|  |  |  |  | VTLP | 215695.2 | run along (+) power lead |

Table 2 – Voltage tap distances (source: Marty Whitson)

# DIAGNOSTIC DEVICE CALIBRATIONS

Calibration data for all the diagnostic devices are maintained in separate spreadsheets. For simplicity all the files are contained in one document in the document database (LARP-doc-349). The following information is accessible from:

https://larpdocs.fnal.gov/LARP-private/DocDB/ShowDocument?docid=349.

- Bullet Gages summary file - contains all data for the bullet gages (source: Marty Whitson)

- Strain Gage summary file - contains the following (source: Marty Whitson):

  - Layer 1 Pole Strain Gages

  - Skin Strain Gages

  - Block Strain Gages (77K)

  - Block Strain Gages (300K)

- RTD calibration data (source: Al Rusy)

# KNOWN ISSUES

Below is a running list of the known issues with TQC01:

- The following low-voltage diagnostic connections (wire label/module-pin) are not part of this magnet:

  - SGCSTI9+ / SG07-12

  - SGCSTI9- / SG07-13

  - SGCSTV9+ / SG07-14

  - SGCSTV9- / SG07-15

  - SGCSTI10+ / SG07-16

  - SGCSTI10- / SG07-17

  - SGCSTV10+ / SG07-11

  - SGCSTV10- / SG07-10

- The following voltage taps (wire label/module-pin) are open:

  - SGSKAZI20+ / SG12-16

  - SGSKAZI20- / SG12-17

  - SGSKAZV20+ / SG12-11

  - SGSKAZV20- / SG12-10

  - VT10A8 / VT03-M2-3

  - VT10B5 / VT03-M4-1

  - VT12BSH2 / VT04-M4-2

# Text boxes

17

16

15

17

16

15

14

13

12

11

7

6

5

4

3

2

46.750”

19.560”

16.750” straight section

1

2

1

Assembled Hypertronics Low-voltage Connector (36-pin grouping)

Solder-cup Side of Magnet-Half (female)

Coil

3.560”

3.125”

RE End Plate

LE End Plate

39.200”

14

13

12

11

7

6

5

4

3

2

1

Support rods slide through the four rectangular holes and are attached to the support plate underneath.

Instrumentation wire bundles come through each round hole, as well as out from the end of each block closest to the bore.

Power leads come out of quadrant 2.

These lines show approximate locations of strain gage wiring placement (same on opposite side of magnet).