Survey Plans

Submittal Form

## Approvals

## _______________________________________________         ____________

George Ison									Date

Ship Operations Contract Project Officer, Ship

Safety Officer

## _______________________________________________         ____________

Glenn Warren								Date

Environmental Monitoring and Indicators Team Leader

## _______________________________________________         ____________

Paul Horvatin								Date

Monitoring Indicators and Reporting Branch Chief

# IFYLE-2005

# May Survey Cruise

Dates  		May 11th, 2005 – May 16th, 2005

Vessel:		Lake Guardian

#### Ports

Embark:		Monroe, Michigan:   10:00 EDT May 11th  (Turning Basin)

(The Estimated ETA for Lake Guardian in Monroe MI is 7:00 EDT May 11th.  )

Disembarkment: 	Monroe, Michigan:   16:00 EDT May 16th

Ports of Call:	 None

## Cruise Participants

PI’s (indicate project PI if PI will not be on board)                                                        status        cabin	    Citizen

| (M) Dr. Greg Boyer SUNY-ESF, Syracuse NY glboyer@esf.edu | PI |  | US |
| --- | --- | --- | --- |
| (M) Steven Ragonese | Tech |  | US |
| (F) Karen Howard | student |  | US |
| (F) Juliette Smith | student |  | US |
| (F) Raija Suomela | student |  | US |
| (F) Tracy Meilander (acting coPI for Robert Heath) | student |  | US |
| (M) Dr. Robert Leshkevich George.leshkevich@noaa.gov | PI |  | US |
| (M) Bradley Robinson | student |  | US |
| (M) Chuck Hatt | student |  | US |
| (F) Beth Oswald (for Tom Johengen) | student |  | US |
| (M) Dr. David Raikow David.Raikow@noaa.gov | coPI |  | US |
| (F) Margaret Lansing margaret.lansing@noaa.gov | Admin |  | US |

Other pertinent contacts and collaborators who will not be on board in May:

| (M) Dr. Tom Johengen Thomas.Johengen@noaa.gov | coPI |  | US |
| --- | --- | --- | --- |
| (M) Dr Hunter Carrick hjc11@psu.edu | PI |  | US |
| (F) Jessica Moon | student |  | US |
| (M) Dr. Peter Lavrentyev peter3@uakron.edu | PI |  | US |
| (M) Ken Moats | student |  | US |
| (M) Dr. Stuart Ludsin stuart.ludsin@noaa.gov | Admin |  | US |

Purpose of Cruise:

To carry out a survey of both harmful algae and dissolved oxygen in Lake Erie as part of the NOAA International Field Year on Lake Erie.  A full basin survey will be undertaken.  The overall goals of the IFYLE 2005 sampling program are to (1) examine the causes and consequences of low-oxygen events, (2) evaluate how lake physics and food webs affect fish production and (3)  examine the distribution and timing of harmful algal blooms in Lake Erie.  All three objectives are interconnected through Lake Erie’s food webs with the ultimate application of this research being to develop forecasts of anoxia, harmful algal blooms and fish production that can aid in the decision making process.

Individual Tasks and Projects listed by PI:

## Boyer:

Collect samples for molecular and cyanobacterial toxin analysis.  This includes collecting a 25L water sample from 1 m depth using a high speed submersible pump.   This pump can be hand deployed.  Samples are returned to the lab and filtered through glass fiber filters for later toxin, DNA, and pigment analysis.   A vertical net tow will be taken using a hand-held phytoplankton net (Wisconsin type).  These samples occur at every station.

A second project will collect mud samples using a large box corer to determine the sedimentation of toxins and toxic organisms to the bottom sediments.  This sampling will occur at limited stations in the western and eastern basins of Lake Erie

## Leshkevich and Johengen:

Make optical measurements with Satlantic profiling  radiometer and surface reference.   Once on station, deploy  floating surface reference into water and let float away from ship.  Then deploy profiling radiometer using articulated  arm .  Once  in the water,  lower radiometer using cable positioned around the movable  winch or capstan positioned in stern  (I  used this method last year on the EPA  Lake Erie cruise in August  - Capitan  should remember the routine)  Any shadows from  articulated arm, etc. should be cast back toward the ship to avoid shadowing the  instruments.  Make three (3) replicate casts per station.    Water needs to be taken  at or near time of optical measurements  and processed  for chlorophyll,  dissolved organic carbon and suspended matter.    Sampling should take about 30 min and must occur between 10:00 and 15:00 when the satellite is passing overhead.  No measurements will be taken if it is raining.

## Raikov:

I will collect zooplankton and water (i.e. phytoplankton). A 150um net will be towed to collect zooplankton from the the entire water column.   This sample will then be stored in a bottle with 95% Ethanol. One liter of water sampled from the epliminion, metalimnion, and hypolimnion will be composited in a carboy. This water sample will then be returned to the lab and filtered. I'm still deciding on the methods, but since you want this today... The composited water will be filtered through a 64um mesh. The particulates will be discarded. The water will then be filtered onto a 47mm filter of type to be determined using Tom Johengen's Filter apparatus. The filter will then be frozen. The water will be discarded. I may make changes to the procedures for processing, but in terms of ship operation I need to make a zoop tow and take water samples.

## Heath and Meilander:

I will be investigating how labile dissolved organic carbon (LDOC) influences phosphorus dynamics and community structure in bacterioplankton at sites of differing trophic state and oxygen concentration.  From 12-16 stations, I will need 10L of epilimnetic water (from rosette).  From one central basin site and one eastern basin site, discrete water samples will be analyzed from epilimnion, metalimnion, and hypolimnion.  Water for bacterial number and biomass will be preserved with formalin.  Samples for analysis of algal and bacterial particulate phosphorus and TSP will be filtered shipboard and frozen.  Whole water will be filtered for DNA extraction and frozen.  Initial oxygen concentrations for LDOC bioassay and bacterial respiration will be determined via Winkler titration.  Phosphate uptake and bacterial production will be determined radiometrically with 33-P and 3H-leucine.  Also, from 1-2 sites, I will need 12L of water for nutrient amendment experiments, 10L of water for swap experiments, and 4L for testing of microbial shunt hypothesis (this is all in addition to the standard 10L).

## Johengen:

Water samples from each station and depth will be processed for TP, TDP, SRP, NO3, NH4, SiO2.  We plan on sampling at 2 depths in the western basin and three depths in the central and eastern basin.  Water depths in all basins will be 2m from surface and 2m from bottom.  In the central and eastern basin the third depth will be taken at the base of the thermocline, which will be determined by the CTD cast and Niskin bottles being fired on the upcast.  When a thermocline is not present the third depth can be omitted or taken at mid-water column depth.  For the remote sensing water analyses, samples will be collected at stations occupied only during the daylight hours of 9am -3pm EST, and only if not full clouds (see Leshkevich and Johengen above).  Only a single 2 m depth water sample will be analyzed per station.  The water sample will be processed for CHL (bulk-GFF method), TSM and DOC according to the protocols below.  CHL will be analyzed onboard, the other analytes are frozen and returned to the lab for analysis.

# SURVEY Plan

## Chemical background information:

## Core:

Acetone, 4 gal for chlorophyll analysis

90% acetone solution will be collected in 1 gallon plastic containers and removed by PI-Boyer for disposal at SUNY-ESF.

## Boyer:

glutaraldyde in tubes for phytoplankton preservation (10 ml)

Lugols iodine solution for phytoplankton preservation (10ml).

## Heath and Meilander::

33-P   as potassium phosphate (1 mCi)

3H- Leucine (1mCi)

Liquid radioactive waste will be stored in plastic containers and returned to Kent for disposal (after several decay cycles).  Solid waste will be collected in a special plastic bag and returned to Kent for disposal according to our radiation safety protocols, also.

% trichloroacetic acid,

formalin

sodium thiosulfate,

MnSO4,

conc sulfuric acid

alkali-iodide-azide,

NH4Cl,

NaHPO4

Nutrient amendments - glucose, glutamate

## Leshkevich and Johengen:

None

## Raikov:

Colloidal Silica

95% ethanol (maybe)

#### CORE MEASUREMENTS FOR SURVEYS

| Variable | Responsible Group | Technique |
| --- | --- | --- |
| Depth profiles for temp, O2, transmissometry, fluorometry | Guardian support staff | EBT, Seabird fluorometer |
| Secchi depths | Guardian support staff | Secchi Disk |
| Size fractionated chlorophyll: (+2m; bottom –2m; mid depth in central and eastern basins only) | Boyer group (May cruise) | 0.2, 2.0, 20 um filters in parallel, extraction and fluorometric measure (Welschmeyer) |
| Bulk Surface Chlorophyll (1m) | Boyer group | Fluorometric (Welschmeyer) |
| Surface phycocyanin (1m) | Boyer group | Fluorometric (Welschmeyer) |
| Nutrients (TN, TDP, SRP, SiO2, NO3, NH3) | Johengen |  |
| Cyanobacterial toxins | Boyer group | Submersible pump |
| Phytoplankton taxonomy / diversity | Guardian support staff (??) | Wisconsin hand net |

## Equipment to be brought and used on Deck:

## (equipment marked with an * will be provided by the individual PI)

- *Submersible pump (Boyer)  (110 volt power required)

- Rosette sampler (multiple)

- Go Flow bottles (Heath, Johengen)

- EBT, DO, Cond, pH, Transmissometer

- *Satlantic profiling radiometer (Leshkevich)

- *Profiling radiometer (Leshkevich)

- Large Box corer (Boyer)

- 150 µ zooplankton net (Raikov)

- *63 µ hand phytoplankton net (Wisconsin type) – (Boyer)

- Plankton Centrifuge (Raikow)

## Mooring Requirements:

No mooring experiments are currently planned for this cruise.

## Diving Operations:

No diving operations are currently planned for this cruise.

## Special Operating Requirements:

The ship will sample on a 24 hr schedule.  Selected experiments (Satlantic) can only be done during daylight hours when the satellite is overhead (10:00 – 15:00).  The are no special requirements for sea or wind conditions.  Nothing is planned to be towed between stations.   It is not necessary that the Lake Guardian be anchored at the station.  Our preference is that you drift on to the station and do not use the props to hold the ship in positon as it stirs up the bottom mud.  It is necessary the ship record the initial and final latitude and longitude for each station.

# Lab Space Requests (if known):

Boyer:   	Chemistry Lab near sink

Johengen:	Chemistry Lab

Meilander:  	Primary Productivity Lab

# Sample Sites and Location

| # | Station name | latitude | Longitude | Depth | Date | ETA | Station Time (hr) | Tasks | Transit time (hr)* |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | Monroe | 41.90000 | -83.35833 |  | 11-May | 10:00 |  | Depart Monroe |  |
| 1 | 881 | 41.96861 | -83.20833 | 5 |  | 12:49 | 2 | CTD/rosette 1m pump Satlantic Zooplankton | 0.83 |
| 2 | e60 | 41.89167 | -83.19670 | 9.5 |  | 15:24 | 2 | CTD/rosette 1m pump Box Core | 0.47 |
| 3 | 973 | 41.79250 | -83.33306 | 6 |  | 17:09 | 0.75 | CTD/rosette 1m pump | 0.88 |
| 4 | 882 Maumee R | 41.73444 | -83.38417 | 6 |  | 18:39 | 1 | CTD/rosette2e 1m pump Zooplankton | 0.43 |
| 5 | e59 | 41.72667 | -83.15000 | 10 |  | 21:05 | 1.25 | CTD/rosette 1m pump Box Core | 1.12 |
| 6 | 580 | 41.84806 | -83.10667 |  |  | 22:56 | 1 | CTD/rosette2e 1m pump Box Core | 0.76 |
| 7 | e61 | 41.94667 | -83.04500 | 10 | 12-May | 0:11 | 0.5 | CTD/rosette 1m pump | 0.66 |
| 8 | e91M | 41.84083 | -82.91670 | 10.5 |  | 2:07 | 1 | CTD/rosette 1m pump Box Core | 0.88 |
| 9 | e92 | 41.95000 | -82.68670 | 11 |  | 4:29 | 1 | CTD/rosette 1m pump Box Core | 1.28 |
| 10 | 968 | 41.74139 | -82.73333 |  |  | 6:21 | 0.5 | CTD/rosette 1m pump | 1.27 |
| 11 | e58 | 41.68500 | -82.93330 | 11.5 |  | 8:57 | 1.5 | CTD/rosette2e 1m pump Zooplankton Box Core | 1.02 |
| 12 | 969 | 41.60806 | -82.92444 | 8 |  | 10:31 | 1 | CTD/rosette 1m pump Satlantic | 0.46 |
| 13 | 496 | 41.56778 | -82.72139 | 10 |  | 13:50 | 2.25 | CTD/rosette2e 1m pump satlantic Zooplankton Box Core | 1.00 |
| 14 | 965 Central Basin | 41.50139 | -82.50028 | 13 |  | 16:07 | 1 | CTD/rosette2e 1m pump Box Core | 1.13 |
| 15 | 964 | 41.48389 | -82.18194 | 8 |  | 18:44 | 1 | CTD/rosette 1m pump Box Core | 1.53 |
| 16 | 962 | 41.71667 | -82.18444 | 18 |  | 21:15 | 1 | CTD/rosette2e 1m pump Zooplankton | 1.40 |
| 17 | 412 | 42.09972 | -82.18972 |  | 13-May | 0:24 | 0.75 | CTD/rosette2e 1m pump | 2.30 |
| 18 | e42 | 41.96500 | -82.04170 | 22 |  | 2:21 | 0.75 | CTD/rosette 1m pump | 1.08 |
| 19 | e43 | 41.78833 | -81.94500 | 23 |  | 4:51 | 1.25 | CTD/rosette2e 1m pump Zooplankton | 1.16 |
| 20 | e73 | 41.97778 | -81.75690 | 24 |  | 7:09 | 0.75 | CTD/rosette4e,2m,4h 1m pump | 1.45 |
| 21 | e36 | 41.93500 | -81.47830 | 23 |  | 9:51 | 1.25 | CTD/rosette 1m pump Zooplankton | 1.36 |
| 22 | e37 | 42.11000 | -81.57500 | 24 |  | 12:22 | 1.25 | CTD/rosette2e 1m pump Satlantic | 1.15 |
| 23 | e38 | 42.28167 | -81.67170 |  |  | 14:51 | 1.25 | CTD/rosette 1m pump satlantic | 1.13 |
| 24 | 950 | 42.58694 | -81.44250 |  |  | 17:50 | 0.75 | CTD/rosette2e 1m pump | 2.14 |
| 25 | e30 | 42.43000 | -81.20500 | 21 |  | 20:12 | 0.75 | CTD/rosette 1m pump | 1.48 |
| 26 | e31 | 42.25333 | -81.10670 | 21 |  | 22:12 | 0.75 | CTD/rosette 1m pump | 1.16 |
| 27 | e78M | 42.11667 | -81.25000 | 23 | 14-May | 1:21 | 2 | CTD/rosette5e 1m pump Zooplankton Box Core | 1.07 |
| 28 | e32 | 42.08167 | -81.01170 | 22 |  | 3:54 | 1.25 | CTD/rosette 1m pump Zooplankton | 1.16 |
| 29 | 1003 | 42.28417 | -80.64028 |  |  | 7:25 | 1.25 | CTD/rosette 1m pump Zooplankton | 2.16 |
| 30 | e63 Eastern Basin | 42.41667 | -79.80000 | 45 |  | 12:55 | 1.25 | CTD/rosette 1m pump Satlantic | 4.11 |
| 31 | e15m | 42.51667 | -79.89330 | 60 |  | 15:09 | 1.25 | CTD/rosette4e,2m,4h 1m pump satlantic | 0.75 |
| 32 | 1108 | 42.71667 | -80.14139 |  |  | 18:26 | 1.5 | CTD/rosette 1m pump zooplankton Box Core | 1.69 |
| 33 | 449 | 42.76111 | -79.98889 |  |  | 20:21 | 1 | CTD/rosette2e 1m pump Zooplankton | 0.78 |
| 34 | E10 | 42.68000 | -79.69170 | 32 |  | 22:41 | 0.75 | CTD/rosette 1m pump | 1.51 |
| 35 | E09 | 42.53833 | -79.61670 | 47 | 15-May | 0:57 | 1.25 | CTD/rosette 1m pump Box Core (?) | 0.92 |
| 36 | 932 | 42.79194 | -79.21056 | 21 |  | 4:31 | 1 | CTD/rosette 1m pump Box Core | 2.47 |
| 37 | 931 Buffalo | 42.84972 | -78.94222 | 10 |  | 6:30 | 0.5 | CTD/rosette 1m pump | 1.33 |
| 38 | 936 | 42.47417 | -79.40750 | <10 |  | 10:46 | 1 | CTD/rosette 1m pump Satlantic | 3.17 |
| 39 | 942 Central Basin | 42.26000 | -79.83000 | <10 |  | 14:20 | 1 | CTD/rosette3e 1m pump satlantic | 2.40 |
| 40 | 489 | 42.16639 | -80.30028 | 22 |  | 17:19 | 0.5 | CTD/rosette 1m pump | 2.33 |
| 41 | 947 | 41.99028 | -80.64111 | 13 |  | 19:53 | 0.5 | CTD/rosette 1m pump | 1.95 |
| 42 | 956 | 41.68833 | -81.44917 | 7 |  | 0:46 | 0.5 | CTD/rosette 1m pump | 4.28 |
| 43 | 958 Cleveland | 41.52500 | -81.70780 | 8 | 16-May | 3:04 | 0.5 | CTD/rosette3e 1m pump | 1.58 |
| 44 | 311 | 41.66667 | -82.50000 | 13 |  | 7:33 | 0.5 | CTD/rosette 1m pump | 3.90 |
| 0 | Monroe | 41.90000 | -83.35833 | - |  | 12:05 | 0 |  | 4.35 |

*  Transit time is estimated assuming 10 knots/ hr

- CTD/Rosette bottles will be fired at 2m and 2m above bottom in the western basin.   Bottles will be fired at 2m (epi), 2m above bottom (hypo),  and mid depth in the eastern and central basin.  Superscripts indicate when additional bottles are needed at the epi, meta, or hypolimnion.

- 1 m pump will be used to fill a 23L carboy off the fantail.  We would like to do this simultaneously with the Rosette to save time (fill time is 2-3 minutes) at all stations. At selected stations (Zooplankton stations), we may need to collect an additional 20 L carboy at depth < 8m.   This will be done after the Rosette is back on board.