POLAR Spacecraft Status As of: Tues, 01 Nov, 16:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM 16:56=AN STIP data only | NOAA-14J AM: 20:57=AN STIP data only | NOAA-15K AM: 17:57=AN GAC data only | NOAA-16L PM: 14:54=AN GAC&LAC data | NOAA-17M AM: 22:24=AN GAC&LAC data | NOAA-18N PM 13:54=AN GAC & LAC data |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 Recursive SCT | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 XSU1 TOAR 444 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO | NO |
| ADACS X=Yaw Y=Roll Z=Pitch | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ Investigating instability | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | RGYRO Mode Estimate pitch Rgmode=PASSIVE Gyro-1 Off 10/24/05 Gyro-3 Off 6/10/04 Gyro chans X-Z only TOAR 454 generated | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB Gyro-2 investigation | Nominal Mode Gyro-A MIMU-2 Z-wheel -Pitch TOAR 447 |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mS +100 mS 31Aug04 | PRI Daily Bias –5.5 mS -100 mS 31Aug04 | PRI Daily Bias –3 mS | PRI No daily bias |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase Enabled | External Synch Rephase each orbit | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 1 | 1 | 2 (since 4/3/03) #2 has 3 chans inop | 2 since 4/18/05 | 1 Analog telem drifting | 1 |
| Recorders (DTR, SSR) | DTRs 3A, 4, 5B Safestate 5B | DTRs 1, 2B, 5 Safestate- 1B | DTRs 1, 2, 3, 4 Safestate 1B EOT | DTRs 1, 2, 3, 4A Safestate 3A 4B STIP only | DTR 1,3,4 / SSR 2 Safestate=SSR 2B 2.66 Mbps reverse playback 18 Oct | SSRs 1,2,3,4,5 Safestate=5B Current spikes TOAR 450 |
| VTX (APT data) | #1 ON 137.50 MHZ | OFF (nominal) Since 8/2/05 | #1 ON 137.50 MHZ Conflict with N12 TurnOFF 11/13/05 | INOP/Off OFF since 11/15/00 | #2 ON 137.62 MHZ | #2 ON 137.9125 MHZ |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #2 137.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ |
| STX 1 = rcp 1698.0 mhz 2 = lcp 1702.5 mhz 3= rcp 1707.0 mhz 4= rcp 2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT 2 omni=rcp Power drop TOAR 446 4-Playback 1,2,3-Degraded | 2 – HRPT 1– Playback 4 – Playback & MCM usage 3 low power unused | 3 – HRPT TOAR424 low power 2 & 4 Playback 1-Standby STX-1 Power drop TOAR 443. | 1 - HRPT 3 - Playback 2-Playback 4-Test & Standby |
| POWER (Array offset and CANT angle, charge & V/T rates, eclipse states and sun angle) Solar eclipse occurred intermittently for 5 hours on 3 Oct 05 no impact | ArrayOff +60 since 6/23/05 Full Sun Sun Angle 12 end downtrend Batts 1&2=LRC Batt 1&2 V/T=4 Shunt degraded SA CANT=37 degs | Array Off -45 Since 10/19/05 Eclipse all year Sun angle 48 Steady trend Batts 1-3= LRC Batts 1&3V/T=6/9 Batt2 VT=7/9 VT change 10/19 Degraded shunts SA CANT=22 degs | Array Off -45 Since 1/25/01 Full Sun Sun Angle 6 Uptrend to 15 in mid-Dec 05 Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 41 End Downtrend Batts 1-3= LRC V/T=4/8 SA CANT=22 degs | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 68 Steady trend Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs | Array Off. -40 Since 6/6/05 Array 360 slew test on 21 & 22 Sept Eclipse all year TOAR 453 on Batt C/D ratio Batts 1-3=LRC Batts 1-3 V/T=4/8 SADE -1 7/29/05 SA CANT=22 |
| AVHRR | Nominal | Erratic Scan motor current surged 27 Sept Frequent imagery bar codes Red Status 29 Sep Channels 2&4 APT | Nominal Rare major scan motor surges. Last Incident 11/18/04 | Improved No bar codes since 12 Oct. Status upgraded 10/18/05 TCE24 OFF 4/14/04 Channel 3B only. | Nominal 3A-B switch enabled | Nominal 3A-B switch Disabled 8/05/05 Channel 3B only |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Full Scan mode |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal | Nominal Full scan mode |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges most recent 11/14/04 degraded data on Chan-3 since 4/30 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal | Replaced by MHS |
| HIRS | OFF/Inop Turned off 6/23/05 For power balance Filter Wheel turned OFF 10/17/02. | NOMINAL Operational Occasional loss of Fwheel synch | NOMINAL Yellow status Since 16 May 05 FW Abrupt return to nominal 7/12/05 FW mode=Hi Powr | Operational Imagery high levels radiometric noise TOAR 441 open Occasional major FM surges, most recent 12/9/04 | NOMINAL 1 Pixel cross track misalignment . | Operational Status downgraded to Yellow 15 Aug 05 LW channel 1-12 noise TOAR 448 LW Noise improved since 14 Oct |
| MHS/MIU |  |  |  |  |  | Nominal Space View=0 |
| MSU | OFF/Inop Turned off for power balance 6/23/05 | Operational Scan motor and antenna problems End of life test plans underway |  |  |  |  |
| SSU |  | Nominal |  |  |  |  |
| DCS | Nominal | Nominal | Nominal | Nominal | Nominal | Nominal DRU’s 1-7 On DRU8 off TOAR 449 |
| SARR |  | Nominal | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Mode =AA A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | Nominal A-Side All AGC Mode Since 15 Aug 05 |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | Nominal A-side 23 May |
| SEM | ON/Nominal Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 TED level=3 as of 27 Sept | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Tscopes inop Autonomous TED shutdown 24 Sept | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=5 P-CDEM-HVPS=4 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 | Nominal Turned on 6 June at 14:05z |
| SBUV |  | Degraded Grate motor sticks Flex memory 3 (giant step) ops suspended 12/2/03 Reduced operations Transient anomaly 1 Sept 05 |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops Procedure changes forthcoming | Nominal Anode mode since 6 July 13:30z |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled Timer =12 mins |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 Thermal downtrend ended 10 Oct | Nominal TCE24 OFF 4/14 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 TOAR 428 CLOSED 9/14/04 no corrective action possible. AMSU-A1 survival heaters on 10/29/03 | All TCE’s active |
|  | N12 | N14 | N15 | N16 | N17 | N18 |

COMMENTS/CHANGES:

NOAA-12:	There were no changes to N12 during the past reporting period.

NOAA-14:	The N14 AVHRR continues to perform very erratically with the scan motor current frequently spiking by as much as

100 mAmps before quickly falling back to more nominal values and then spiking again (illustration 1).  Synch delta values are also relatively erratic despite the MIRP rephase enable command being implemented out of stored commands once per rev over the South Pole.  The affect of this rephase operation is difficult to ascertain since N14 has no GAC (and thus the rephase effect cannot be seen) and there are long gaps between supports that result in less synch delta information being processed by EMOSS engineers.  However, analysis of HRPT imagery continues to intermittently observe bar codes N14 HRPT images.  However, this problem also appears intermittent, not continuous as it was in past weeks.  Therefore engineers are assuming that the rephase enable operation may actually be helping increase the percentage of nominal images (illustration 2).

The N14 EPS subsystem has been relatively nominal since its major reconfiguration on 19 Oct.  Engineers are closely

monitoring the bus and partial shunt voltages to ensure that both remain stable and nominal.  Presently, the bus voltage is running at a higher daily standard deviation that at any time during its mission which can be indicative of less stability.  Much of this can be accounted for by the fact that N14 is now in a permanent eclipse season and the shunts appear to be operating within acceptable norms.  However, these components will continue to be closely monitored to ensure that the bus voltage does not surge and the shunts do not degrade further than they already have (illustration 3and 4).

There was no additional coordination or discussion that ensued on the proposed N14 “Pitch Over” test for MSU end-of-life space view calibration during the past week.   Implementation of a recursive stored command table into the N14 operations remain TBD.

NOAA-15:	N15 is approaching the start of a new VTX (APT data) RF conflict period with N12.  On 13 Nov the N15 VTX-1 will be turned off until the conflict ends on 13 Dec.  Otherwise there were no significant changes to N15 in the past week (except for a small change in AVHRR scan motor current operating profile) and all subsystems appear to be operating nominally (illustrations 6-9) .

NOAA-16:	N16 payloads were nominal during the past week (illustration 10).  The N16 AVHRR scan motor current was much

improved last week with the scan motor current approaching its nominal range, synch delta values remaining below MIRP rephase trigger thresholds and imagery remaining free of bar codes and MIRP rephase frame losses.  HRPT imagery does continue to show some wave patterns but even these are less pronounced than has been the case for several months (illustrations 11-13).

There was basically no change to the N16 ADACS-gyro situation during the past week.  Tiger team meetings continue

and TOAR 454 was submitted but no resolution has yet been determined.  The subsystem continues to operate in Reduced Gyro mode (passive monitoring) with roll being estimated.  Most ADACS values have been stable since

gyro-1 was turned off although many of them are operating in different ranges than before the anomaly (i.e.  The Y-axis reaction wheel is operating at significantly higher motor currents than previously)  although all of these values have been determined to be within acceptable limits.  Controllers continue to monitor N16 on every orbit and are prepared to take contingency actions in the event there is a mission threatening event on the spacecraft related to the IMU.   To ensure maximum contact with N16, STX-4 is being turned on over McMurdo.  MCM is being used to cover the N-16 CDA blind orbits.

The N16 gyro-1 component remains RED in status while the ADACS subsystem remains YELLOW.  See illustrations 14-16 for graphical depictions of N16 ADACS performance over the past 10 days and illustrations 17-18  for performance during the past half day.

NOAA-17:	The gyros on N17 were relatively stable last week and EMOSS continues to monitor them closely, especially in light of

the situation which just occurred on N16 gyro-1.  The AVHRR scan motor current fell slightly this week (improved?)  continuing a trend that began last week, reaching its lowest level in over a year last with synch delta following suit (illustrations 19 & 20).  In general lower currents are considered better, conversely, operational profile changes can sometimes be a harbinger of imminent problems and so closer scrutiny is warranted.  Otherwise N17 ADACS was nominal last week (illustration 21) nor were there any other changes of note to N17 status or configuration.

NOAA-18:	EMOSS engineers were notified that the long wave channel noise on N18 HIRS had a significantly improved in the

past 2 weeks, see illustration 22 for a comparison of before and after imagery.  Otherwise there was no change to the HIRS, AVHRR or AMSU’s engineering data during this time (illustration 23) and the ADACS on N18 was also stable throughout the reporting period (illustrations 24 and 25).

Illustration 1:  NOAA-14 AVHRR Health Analysis

(The large current spikes continue affecting the scan motor. At times the value is nominally within the 150 mAmps range.  It just hasn’t been able to stabilize there.)

Illustration 2:  N14 AVHRR Imagery & Synch Delta Analysis

(Imagery is intermittently bar coded in concert with the frequent scan motor current surges.  It appears that the rephase enabled operations now being performed once per orbit over the South Pole, has been useful at increasing the number of nominal images between current surges.  The red colored “RE” in the top synch delta plot indicates when rephase enable operations began every orbit on N14.)

Illustration 3:  N14 EPS Analysis (Part 1)

(A little less stable on the bus voltage which is actually running at the highest DAILY standard deviation in its history, see upper right plot, while the shunts are now working a little harder.  Batteries low darkness voltages all remain comfortably above power survival safestate threshold.  This spacecraft configuration may require closer scrutiny than the pass load currently allows.)

Illustration 4:  N14 EPS Analysis (Part 2)

(Battery temps seemed to have stabilized.  At a glance, the bus current, upper right plot, shows a similar profile as the AVHRR scan motor, although the surges are nothing more than transmitter on commands.)

Illustration 5:  N14 AVHRR Scan Motor vs. Bus Current Analysis

(It was observed that bus current and AVHRR scan motor current had similar “surge profiles”.  Plot above connecting each with a red line shows them to not be correlated.)

Illustration 6:  N15 Payload Motor Current Analysis

(Solidly nominal although the AVHRR scan motor is again rising and has shown somewhat less stability in recent weeks, although nothing approaching its previous anomalous behaviors.)

Illustration 7:  N15 Payload Thermal Analysis

(All payload, and many other spacecraft components temperatures have been rising in recent weeks now that the sun angle trend is back up. )

Illustration 8:  N15 AVHRR Imagery & Synch Delta Analysis

(Everything appears nominal although synch delta appears to also be on the increase along with the scan motor current, again to only a relatively minor degree.)

ILLUSTRATION 9:  N15 ADACS Analysis

(Nominal although gyro-1 current is slightly less stable than desired.  Subsystem is now under a lot closer scrutiny because of the similarity with and problems of  N16 gyros..)

N16 (NOT 15)

NOTE: ALL PLOTS ARE N16 NOTHWITHSTANDING THE LABLES

ILLUSTRATION 10:  N16 Payload Motor Current Analysis

(Nominal and stable relative to recent performance.)

Illustration 11:  N16 AVHRR Health Analysis

(Improved since last week and now approaching nominal range.)

Illustration 12:  N16 Synch Delta Analysis

(Improved from previous weeks to the point that MIRP rephasing is no longer occurring when rephase is enabled.)

Illustration 13:  N16 AVHRR Imagery Analysis

(Also improved from previous weeks to the point that there are no longer frame losses caused by MIRP rephasing (RE) when rephase I enabled and wave patterns on HRPT images are less prominent than previous weeks.)

Illustration 14:  N16 Gyro and Wheel Currents.  Before, During and After Gyro-1 Anomaly

(Little changed since gyro-1 was turned off on JDAY 297, 24 Oct.)

Illustration 15:   N16 IMU, Wheel Temps and Yaw Updates.  Before, During and After Gyro-1 Anomaly

(Little changed since gyro-1 was turned off on JDAY 297, 24 Oct.)

Illustration 16:  N16 Axis momentums and errors

(Little changed since gyro-1 was turned off on JDAY 297, 24 Oct.)

Illustration 17:  N16 Recent (today) RWheel health

(Y-wheel current looks to be improving somewhat.  Sustainable?)

Illustration 18:  N16 Recent (today) axis performance

(No apparent changes from previous days,)

Illustration 19:  N17 Payload Motor Current Analysis

(All stable and nominal, AVHRR continues to fall.  Is this change in operational profile an improvement?  Lower scan motor current values are usually considered to be a positive development but operational changes can also be a harbinger of potential instabilities.)

Illustration 20:  N17 AVHRR Synch Delta and Imagery Analysis

(Imagery remains nominal, synch delta, like scan motor current has been falling recently and is now approaching zero.  Typically such a development would be considered positive but concerns about stability of this value, like the scan motor current, may also be warranted.)

Illustration 21:  N17 ADACS Health Analysis

(N17 has similar gyro problems as those exhibited by N16.  In addition, N17 gyro-2 recently had a spin motor current surge that resulted in a TOAR being generated.  Closer scrutiny will be maintained on this subsystem into the foreseeable future.  This week was relatively stable and nominal.)

1              2		 3		     4		         5		           6	         7

Illustration 22:  N18 HIRS Long Wave Channel Comparison

(Noise improvements were noted by Products personnel starting on or about 14 Oct.  The most recent image, bottom, appears completely nominal especially compared to previous images.)

Illustration 23:  N18 Payload Motor Current Analysis

(Stable and nominal last week.)

Illustration 24:  N18 ADACS RWheel Analysis

(About the same as last week; generally nominal, notwithstanding the TOAR on the

Z-wheel.)

Illustration 25:  N18 ADACS Axis Analysis

(About the same as last week; generally nominal.)

# POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING October 28, 2005

| DAY/DATE | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 | NOAA-18 |
| --- | --- | --- | --- | --- | --- | --- |
| FRI. 10/21 | -866 msec | +260 msec | -321 msec | +200 msec | +144 msec | +077 msec |
| SAT. 10/22 | -865 msec | +259 msec | -322 msec | +203 msec | +146 msec | +079 msec |
| SUN. 10/23 | -866 msec | +258 msec | -323 msec | +204 msec | +147 msec | +080 msec |
| MON. 10/24 | -866 msec | +258 msec | -325 msec | +204 msec | +146 msec | +083 msec |
| TUE. 10/25 | -869 msec | +259 msec | -326 msec | +328 msec | +148 msec | +082 msec |
| WED. 10/26 | -875 msec | +260 msec | -326 msec | +329 msec | +150 msec | +083 msec |
| THU. 10/27 | -870 msec | +263 msec | -326 msec | +323 msec | +152 msec | +084 msec |

NOAA-14:  As of 12/23/03 the TIP clock is corrected daily by –7.0 msec to compensate for drift.

NOAA-15:  As of 04/22/03 the TIP clock is corrected daily by –8.0 msec to compensate for drift.

NOAA-16:  As of 12/23/03 the TIP clock is corrected daily by -5.5 msec to compensate for drift.

NOAA-17:  As of 12/23/03 the TIP clock is corrected daily by –3.0 msec to compensate for drift.

NOAA-12:  As of 12/10/03 the TIP clock is corrected daily by +6.5 msec to compensate for drift.

*    A clock jump of +500 milliseconds on 07/01/05 due to fractional second daily ETCUP. A clock

jump of -500 milliseconds on 09/15/05 due to fractional second daily ETCUP. Alternating +/-

500 millisecond clock jumps will ccur at 76-day intervals as long as fractional second daily

ETCUP is utilized to manage clock drift. The next +500 millisecond jump is expected on 11/30/05.

# Text boxes

Gyro#1 off

Gyro#1 off

Gyro#1 off