Monthly Zonal and Global Radiative Fluxes and Clouds (ZAVG)

The Monthly Zonal and Global Radiative Fluxes and Clouds (ZAVG) product are the zonal and global averages of the monthly Regional Radiative and Clouds (AVG) product.  This product is the CERES equivalent of the zonal and global averages in the ERBE ES-4 product of the CERES untuned and tuned radiative transfer modeled fluxes.  This product is written in HDF_EOS and contains meta data as well as gridded science data.

The ZAVG contains the following apriori and observed input:

Zonal/Global data

Cloud category properties for four (low, lower middle, upper middle and high) cloud layers

Observed CERES TOA clear-sky and all-sky fluxes

MODIS based spectral aerosol optical depths

The ZAVG contains the following constrained (tuned) vertical flux profiles for both clear-sky and total-sky conditions evaluated at the TOA, 70mb, 200mb, 500mb, and surface:

Longwave, Shortwave, and Window channels upward and downward.

The constrained (tuned) and initial (untuned) profiles for the following are included for pristine (clear-sky no-aerosol), clear-sky, total-sky-no-aerosol, and total-sky conditions:

Longwave upward at the surface and TOA.

Longwave downward at the surface.

Shortwave upward at the surface and TOA.

Shortwave downward at the surface.

Window channel upward at the surface and TOA.

Window channel downward at the surface.

The adjustments to the radiative transfer model input parameters between the initial and the constrained (adjusted) passes are also contained on the ZAVG.  These parameters include:

Surface albedo and skin temperature

Total column precipitable water, upper tropospheric relative humidity, and column ozone

Aerosol optical depth

Cloud optical depth, fractional area, and effective temperature

The ZAVG contains the direct and diffuse shortwave surface fluxes for total-sky, clear-sky, pristine and actinic conditions.  The ZAVG also contains surface UVA and UVB downwelling and direct diffuse ratios for total-sky, clear-sky, pristine, and total-sky-no-aerosol conditions.

A complete listing of metadata and science parameters for this data product can be found in Table 2.12-1 and Table 2.12-3.

Level:  3

Frequency:  Monthly

Portion of Atmosphere Covered:  Surface to TOA

Time Interval Covered:		Portion of Globe Covered:

File:  1 Month			File:  Entire Global

Record:  1 Month			Record:  Zonal or Global

Product Version:

TRMM:  N/A

Terra:  Beta5, Beta6, Edition2C, Edition2F

Aqua:  Beta6, Edition2B, Edition2C

ZAVG Metadata

The types of ZAVG metadata are summarized in Table 2.12-1 and contain information which need only be recorded once per product.  The CERES metadata are listed in Appendix B.

| ZAVG Metadata Summary |
| --- |
| HDF Name | Description Table | Records | Number of Fields |
| CERES Baseline Header Metadata | Table B-1 | 1 | 36 |
| CERES_metadata science data | Table B-2 | 1 | 14 |

| List of the Vgroups for different Gridded Categories |
| --- |
| Vgroup Number | Vgroup Name | Description | Number of Records |
| 2 | 1.0 Degree Zonal | See Table 2.12-3 | 180 |
| 3 | Global | See Table 2.12-3 | 1 |

| List of the Vgroups contained in 1.0 Degree Zonal and Global Vgroups |
| --- |
| Vgroup Number | Vgroup Name | Monthly 3-Hourly Averages / Monthly (Hour) Averages |
| 1 | Monthly Hourly Averages | See Table 2.12-4 |
| 2 | Monthly Averages | See Table 2.12-4 |

| List of the Vgroups contained in the Monthly 3-Hourly Averages and Monthly Averages Vgroups in ZAVG |
| --- |
| Vgroup Number | Vgroup Name | Monthly 3-Hourly Averages / Monthly (Hour) Averages |
| 1 | Observed TOA Fluxes | See Table 2.12-6(a) & (b) |
| 2 | Cloud Layer - High | See Table 2.12-7(a) & (b) |
| 3 | Cloud Layer - UpperMid | See Table 2.12-7(a) & (b) |
| 4 | Cloud Layer - LowerMid | See Table 2.12-7(a) & (b) |
| 5 | Cloud Layer - Low | See Table 2.12-7(a) & (b) |
| 6 | Stowe-Ignatov Aerosol Optical Depth | See Table 2.12-8(a) & (b) |
| 7 | MODIS Aerosol Optical Depth | See Table 2.12-9(a) & (b) |
| 8 | Tuned Pristine Fluxes | See Table 2.12-10(a) & (b) |
| 9 | Tuned ClearSky Flux Profiles | See Table 2.12-11(a) & (b) |
| 10 | Tuned TotalSky-NoAerosol Fluxes | See Table 2.12-12(a) & (b) |
| 11 | Tuned TotalSky Flux Profiles | See Table 2.12-13(a) & (b) |
| 12 | Untuned Pristine Fluxes | See Table 2.12-14(a) & (b) |
| 13 | Untuned ClearSky Fluxes | See Table 2.12-15(a) & (b) |
| 14 | Untuned TotalSky-NoAerosol Fluxes | See Table 2.12-16(a) & (b) |
| 15 | Untuned TotalSky Fluxes | See Table 2.12-17(a) & (b) |
| 16 | Satellite Emulated WN TOA Fluxes | See Table 2.12-18(a) & (b) |
| 17 | TOA Flux Error | See Table 2.12-19(a) & (b) |
| 18 | Constrainment Adjustments | See Table 2.12-20(a) & (b) |
| 19 | Surface SW Direct/Diffuse Fluxes | See Table 2.12-21(a) & (b) |
| 20 | UVA - UVB Fluxes | See Table 2.12-22(a) & (b) |
| 21 | PAR Fluxes | See Table 2.12-23(a) & (b) |
| 22 | Pristine-Sky SW MultiStream Correction | See Table 2.12-24(a) & (b) |

ZAVG Science Data

The Scientific Data Sets (SDS) are divided into tables which map to Vgroups of the same name.  All of the ZAVG science data are organized into the HDF-EOS Grid data type, which is shown in Table 2.12-6(a) and (b) below.  All parameter (a) tables contain a list of the gridded parameters, which includes the field number, the field name, the data type, the units, the range, and the number of elements within each field.  The No. of Elements or Dimensions are defined in the first set of tables.  All parameter (b) tables contain the list of SDS indices, which are grouped into zonal monthly 3-hourly, zonal monthly, global monthly 3-hourly, and global monthly means.  The first 2 dimensions Nlat and Nlon corresponds to the CERES region index, the next dimension is Ngmt and refers to the time index, the last dimension is Ns and contains the mean and the standard deviation (temporal).  On a few parameters, the last dimension is Nlev and defines the atmospheric profile levels.  This ordering is used by the C programming language and most HDF viewers, such as IDL.  In FORTRAN, the dimensions are reversed such that the number of regions becomes the last dimension and the first dimension is the number of parameters in the SDS.

Nlat, Nlon dimensions that define the CERES equal angle 1° latitude by longitude grid.  Nlon is always 1 for zonal and global parameters.  Nlat is 1 for global parameters.

| Dimension | No of Indices | Definition |
| --- | --- | --- |
|  | Zonal | Global |  |
| Nlat | 180 | 1 | Index #1 is defined at 89.5°N and #180 is at 89.5°S |
| Nlon | 1 | 1 | Index #1 is defined at 179.5°W and #360 is at 179.5°E |

Ngmt dimension that defines the 8 Monthly 3-hourly GMT time increments.  For the Monthly Ngmt only has one index.

| Ngmt Index | Monthly 3-hourly | Monthly |
| --- | --- | --- |
| 1 | 00-03 GMT | 00-24 GMT Monthly |
| 2 | 03-06 GMT | - |
| 3 | 06-09 GMT | - |
| 4 | 09-12 GMT | - |
| 5 | 12-15 GMT | - |
| 6 | 15-18 GMT | - |
| 7 | 18-21 GMT | - |
| 8 | 21-24 GMT | - |

NS dimension that define the parameter statistics for individual grid cell.

| Ns | Statistic |
| --- | --- |
| 1 | Mean |
| 2 | Standard deviation |

Nlev dimension that define the atmospheric profile levels.

| Nlev | Atmospheric level |
| --- | --- |
| 1 | TOA (30 km) |
| 2 | 70mb |
| 3 | 200mb |
| 4 | 500mb |
| 5 | Surface |

| Observed TOA Fluxes |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| SW TOA Total-Sky | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| LW TOA Total-Sky | 32-bit real | W m-2 | 0 .. 500 | Nlon*Nlat*Ngmt*Ns |
| WN TOA Total-Sky | 32-bit real | W m-2 μm-1 | 2 .. 50 | Nlon*Nlat*Ngmt*Ns |
| SW TOA Clear-Sky | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| LW TOA Clear-Sky | 32-bit real | W m-2 | 0 .. 500 | Nlon*Nlat*Ngmt*Ns |
| WN TOA Clear-Sky | 32-bit real | W m-2 μm-1 | 2 .. 50 | Nlon*Nlat*Ngmt*Ns |

| SDS Index of Observed TOA Fluxes |
| --- |
| SDS Name | Zonal Monthly 3-Hourly | Zonal Monthly | Global Monthly 3-Hourly | Global Monthly |
| SW TOA Total-Sky | 0 | 212 | 424 | 636 |
| LW TOA Total-Sky | 1 | 213 | 425 | 637 |
| WN TOA Total-Sky | 2 | 214 | 426 | 638 |
| SW TOA Clear-Sky | 3 | 215 | 427 | 639 |
| LW TOA Clear-Sky | 4 | 216 | 428 | 640 |
| WN TOA Clear-Sky | 5 | 217 | 429 | 641 |

| Cloud Properties for Four Cloud Layers |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| Area Fraction Percentage | 32-bit real | Percent | 0 .. 100 | Nlon*Nlat*Ngmt*Ns |
| Vis. Opt. Depth (linear) | 32-bit real | N/A | 0 .. 400 | Nlon*Nlat*Ngmt*Ns |
| Vis. Opt. Depth (log) | 32-bit real | N/A | -6 .. 6 | Nlon*Nlat*Ngmt*Ns |
| Infrared Emissivity | 32-bit real | N/A | 0 .. 1 | Nlon*Nlat*Ngmt*Ns |
| Liquid Water Path | 32-bit real | g m-2 | 0 .. 10000 | Nlon*Nlat*Ngmt*Ns |
| Ice Water Path | 32-bit real | g m-2 | 0 .. 10000 | Nlon*Nlat*Ngmt*Ns |
| Top Pressure | 32-bit real | hPa | 0 .. 1100 | Nlon*Nlat*Ngmt*Ns |
| Effective Pressure | 32-bit real | hPa | 0 .. 1100 | Nlon*Nlat*Ngmt*Ns |
| Effective Temperature | 32-bit real | K | 100 .. 350 | Nlon*Nlat*Ngmt*Ns |
| Effective Height | 32-bit real | km | 0 .. 20 | Nlon*Nlat*Ngmt*Ns |
| Bottom Pressure | 32-bit real | hPa | 0 .. 1100 | Nlon*Nlat*Ngmt*Ns |
| Liquid Particle Radius | 32-bit real | μm | 0 .. 40 | Nlon*Nlat*Ngmt*Ns |
| Ice Particle Diameter | 32-bit real | μm | 0 .. 300 | Nlon*Nlat*Ngmt*Ns |
| Particle Phase | 32-bit real | N/A | 1 .. 2 | Nlon*Nlat*Ngmt*Ns |
| Vertical Aspect Ratio | 32-bit real | N/A | 0 .. 20 | Nlon*Nlat*Ngmt*Ns |

SDS Index of High, Uppermid, Lowermid, Low (mean, stdev, num obs) in Cloud Properties

| SDS Name | Zonal Monthly 3-Hourly | Zonal Monthly | Global Monthly 3-Hourly | Global Monthly |
| --- | --- | --- | --- | --- |
| Area Fraction Percentage |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Vis. Opt. Depth (linear) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Vis. Opt. Depth (log) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Infrared Emissivity |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Liquid Water Path |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Ice Water Path |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Top Pressure |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Effective Pressure |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Effective Temperature |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Effective Height |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Bottom Pressure |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Liquid Particle Radius |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Ice Particle Diameter |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Particle Phase |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Vertical Aspect Ratio |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

Color Red	-	High Cloud

Color Green	-	Uppermid Cloud

Color Blue	-	Lowermid Cloud

Color Black	-	Low Cloud

| Stowe-Ignatov Aerosol Optical Depth |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| Aerosol visible optical depth - 0.63 m | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt*Ns |
| Aerosol visible optical depth - 1.6 m | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt*Ns |

SDS Index of Stowe-Ignatov Aerosol Optical Depth

| SDS Name | Zonal Monthly 3-Hourly | Zonal Monthly | Global Monthly 3-Hourly | Global Monthly |
| --- | --- | --- | --- | --- |
| Aerosol visible optical depth - 0.63 m | 66 | 278 | 490 | 702 |
| Aerosol visible optical depth - 1.6 m | 67 | 279 | 491 | 703 |

| MODIS Aerosol Optical Depth |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| Initial Aerosol Optical Depth | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt*Ns |
| Aerosol Opt. Depth at 0.47 m in Land | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt*Ns |
| Aerosol Opt. Depth at 0.55 m in Land | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt*Ns |
| Aerosol Opt. Depth at 0.66 m in Land | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt*Ns |
| Aerosol Opt. Depth at 0.47 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt*Ns |
| Aerosol Opt. Depth at 0.55 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt*Ns |
| Aerosol Opt. Depth at 0.66 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt*Ns |
| Aerosol Opt. Depth at 0.87 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt*Ns |
| Aerosol Opt. Depth at 1.24 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt*Ns |
| Aerosol Opt. Depth at 1.64 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt*Ns |
| Aerosol Opt. Depth at 2.13 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt*Ns |

SDS Index of MODIS Aerosol Optical Depth

| SDS Name | Zonal Monthly 3-Hourly | Zonal Monthly | Global Monthly 3-Hourly | Global Monthly |
| --- | --- | --- | --- | --- |
| Initial Aerosol Optical Depth | 68 | 280 | 492 | 704 |
| Aerosol Opt. Depth at 0.47 m in Land | 69 | 281 | 493 | 705 |
| Aerosol Opt. Depth at 0.55 m in Land | 70 | 282 | 494 | 706 |
| Aerosol Opt. Depth at 0.66 m in Land | 71 | 283 | 495 | 707 |
| Aerosol Opt. Depth at 0.47 m in Ocean | 72 | 284 | 496 | 708 |
| Aerosol Opt. Depth at 0.55 m in Ocean | 73 | 285 | 497 | 709 |
| Aerosol Opt. Depth at 0.66 m in Ocean | 74 | 286 | 498 | 710 |
| Aerosol Opt. Depth at 0.87 m in Ocean | 75 | 287 | 499 | 711 |
| Aerosol Opt. Depth at 1.24 m in Ocean | 76 | 288 | 500 | 712 |
| Aerosol Opt. Depth at 1.64 m in Ocean | 77 | 289 | 501 | 713 |
| Aerosol Opt. Depth at 2.13 m in Ocean | 78 | 290 | 502 | 714 |

| Tuned Pristine Fluxes |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| Tuned Pristine SW Surface Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Tuned Pristine SW Surface Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Tuned Pristine SW TOA Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Tuned Pristine LW Surface Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt*Ns |
| Tuned Pristine LW Surface Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ngmt*Ns |
| Tuned Pristine LW TOA Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt*Ns |
| Tuned Pristine WN Surface Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns |
| Tuned Pristine WN Surface Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns |
| Tuned Pristine WN TOA Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns |

SDS Index of Tuned Pristine Fluxes

| SDS Name | Zonal Monthly 3-Hourly | Zonal Monthly | Global Monthly 3-Hourly | Global Monthly |
| --- | --- | --- | --- | --- |
| Tuned Pristine SW Surface Up | 79 | 291 | 503 | 715 |
| Tuned Pristine SW Surface Down | 80 | 292 | 504 | 716 |
| Tuned Pristine SW TOA Up | 81 | 293 | 505 | 717 |
| Tuned Pristine LW Surface Up | 82 | 294 | 506 | 718 |
| Tuned Pristine LW Surface Down | 83 | 295 | 507 | 719 |
| Tuned Pristine LW TOA Up | 84 | 296 | 508 | 720 |
| Tuned Pristine WN Surface Up | 85 | 297 | 509 | 721 |
| Tuned Pristine WN Surface Down | 86 | 298 | 510 | 722 |
| Tuned Pristine WN TOA Up | 87 | 299 | 511 | 723 |

| Tuned ClearSky Flux Profiles, Table 2.12-5(d) defines Nlev |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| Tuned Clear-Sky SW Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns*Nlev |
| Tuned Clear-Sky SW Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns*Nlev |
| Tuned Clear-Sky LW Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt*Ns*Nlev |
| Tuned Clear-Sky LW Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ngmt*Ns*Nlev |
| Tuned Clear-Sky WN Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns*Nlev |
| Tuned Clear-Sky WN Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns*Nlev |

SDS Index of Tuned ClearSky Flux Profiles

| SDS Name | Zonal Monthly 3-Hourly | Zonal Monthly | Global Monthly 3-Hourly | Global Monthly |
| --- | --- | --- | --- | --- |
| Tuned Clear-Sky SW Up | 88 | 300 | 512 | 724 |
| Tuned Clear-Sky SW Down | 89 | 301 | 513 | 725 |
| Tuned Clear-Sky LW Up | 90 | 302 | 514 | 726 |
| Tuned Clear-Sky LW Down | 91 | 303 | 515 | 727 |
| Tuned Clear-Sky WN Up | 92 | 304 | 516 | 728 |
| Tuned Clear-Sky WN Down | 93 | 305 | 517 | 729 |

| Tuned TotalSky-NoAerosol Fluxes |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| Tuned Total-Sky-NoAerosol SW Surface Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Tuned Total-Sky-NoAerosol SW Surface Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Tuned Total-Sky-NoAerosol SW TOA Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Tuned Total-Sky-NoAerosol LW Surface Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt*Ns |
| Tuned Total-Sky-NoAerosol LW Surface Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ngmt*Ns |
| Tuned Total-Sky-NoAerosol LW TOA Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt*Ns |
| Tuned Total-Sky-NoAerosol WN Surface Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns |
| Tuned Total-Sky-NoAerosol WN Surface Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns |
| Tuned Total-Sky-NoAerosol WN TOA Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns |

SDS Index of Tuned TotalSky-NoAerosol Fluxes

| SDS Name | Zonal Monthly 3-Hourly | Zonal Monthly | Zonal Monthly 3-Hourly | Zonal Monthly |
| --- | --- | --- | --- | --- |
| Tuned Total-Sky-NoAerosol SW Surface Up | 94 | 306 | 518 | 730 |
| Tuned Total-Sky-NoAerosol SW Surface Down | 95 | 307 | 519 | 731 |
| Tuned Total-Sky-NoAerosol SW TOA Up | 96 | 308 | 520 | 732 |
| Tuned Total-Sky-NoAerosol LW Surface Up | 97 | 309 | 521 | 733 |
| Tuned Total-Sky-NoAerosol LW Surface Down | 98 | 310 | 522 | 734 |
| Tuned Total-Sky-NoAerosol LW TOA Up | 99 | 311 | 523 | 735 |
| Tuned Total-Sky-NoAerosol WN Surface Up | 100 | 312 | 524 | 736 |
| Tuned Total-Sky-NoAerosol WN Surface Down | 101 | 313 | 525 | 737 |
| Tuned Total-Sky-NoAerosol WN TOA Up | 102 | 314 | 526 | 738 |

| Tuned TotalSky Flux Profiles, Table 2.12-5(d) defines Nlev |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| Tuned Total-Sky SW Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns*Nlev |
| Tuned Total-Sky SW Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns*Nlev |
| Tuned Total-Sky LW Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt*Ns*Nlev |
| Tuned Total-Sky LW Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ngmt*Ns*Nlev |
| Tuned Total-Sky WN Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns*Nlev |
| Tuned Total-Sky WN Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns*Nlev |

SDS Index of Tuned TotalSky Flux Profiles

| SDS Name | Zonal Monthly 3-Hourly | Zonal Monthly | Global Monthly 3-Hourly | Global Monthly |
| --- | --- | --- | --- | --- |
| Tuned Total-Sky SW Up | 103 | 315 | 527 | 739 |
| Tuned Total-Sky SW Down | 104 | 316 | 528 | 740 |
| Tuned Total-Sky LW Up | 105 | 317 | 529 | 741 |
| Tuned Total-Sky LW Down | 106 | 318 | 530 | 742 |
| Tuned Total-Sky WN Up | 107 | 319 | 531 | 743 |
| Tuned Total-Sky WN Down | 108 | 320 | 532 | 744 |

| Untuned Pristine Fluxes |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| Untuned Pristine SW Surface Up | 32-bit real | W m-2 | 0 .. 1500 | Nlon*Nlat*Ngmt*Ns |
| Untuned Pristine SW Surface Down | 32-bit real | W m-2 | 0 .. 1500 | Nlon*Nlat*Ngmt*Ns |
| Untuned Pristine SW TOA Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Untuned Pristine LW Surface Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt*Ns |
| Untuned Pristine LW Surface Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ngmt*Ns |
| Untuned Pristine LW TOA Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt*Ns |
| Untuned Pristine WN Surface Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns |
| Untuned Pristine WN Surface Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns |
| Untuned Pristine WN TOA Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns |

| SDS Index of Untuned Pristine Fluxes |
| --- |
| SDS Name | Zonal Monthly 3-Hourly | Zonal Monthly | Global Monthly 3-Hourly | Global Monthly |
| Untuned Pristine SW Surface Up | 109 | 321 | 533 | 745 |
| Untuned Pristine SW Surface Down | 110 | 322 | 534 | 746 |
| Untuned Pristine SW TOA Up | 111 | 323 | 535 | 747 |
| Untuned Pristine LW Surface Up | 112 | 324 | 536 | 748 |
| Untuned Pristine LW Surface Down | 113 | 325 | 537 | 749 |
| Untuned Pristine LW TOA Up | 114 | 326 | 538 | 750 |
| Untuned Pristine WN Surface Up | 115 | 327 | 539 | 751 |
| Untuned Pristine WN Surface Down | 116 | 328 | 540 | 752 |
| Untuned Pristine WN TOA Up | 117 | 329 | 541 | 753 |

| Untuned ClearSky Fluxes |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| Untuned Clear-Sky SW Surface Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Untuned Clear-Sky SW Surface Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Untuned Clear-Sky SW TOA Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Untuned Clear-Sky LW Surface Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt*Ns |
| Untuned Clear-Sky LW Surface Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ngmt*Ns |
| Untuned Clear-Sky LW TOA Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt*Ns |
| Untuned Clear-Sky WN Surface Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns |
| Untuned Clear-Sky WN Surface Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns |
| Untuned Clear-Sky WN TOA Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns |

| SDS Index of Untuned ClearSky Fluxes |
| --- |
| SDS Name | Zonal Monthly 3-Hourly | Zonal Monthly | Global Monthly 3-Hourly | Global Monthly |
| Untuned Clear-Sky SW Surface Up | 118 | 330 | 542 | 754 |
| Untuned Clear-Sky SW Surface Down | 119 | 331 | 543 | 755 |
| Untuned Clear-Sky SW TOA Up | 120 | 332 | 544 | 756 |
| Untuned Clear-Sky LW Surface Up | 121 | 333 | 545 | 757 |
| Untuned Clear-Sky LW Surface Down | 122 | 334 | 546 | 758 |
| Untuned Clear-Sky LW TOA Up | 123 | 335 | 547 | 759 |
| Untuned Clear-Sky WN Surface Up | 124 | 336 | 548 | 760 |
| Untuned Clear-Sky WN Surface Down | 125 | 337 | 549 | 761 |
| Untuned Clear-Sky WN TOA Up | 126 | 338 | 550 | 762 |

| Untuned TotalSky-NoAerosol Fluxes |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| Untuned Total-Sky-NoAerosol SW Surface Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Untuned Total-Sky-NoAerosol SW Surface Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Untuned Total-Sky-NoAerosol SW TOA Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Untuned Total-Sky-NoAerosol LW Surface Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt*Ns |
| Untuned Total-Sky-NoAerosol LW Surface Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ngmt*Ns |
| Untuned Total-Sky-NoAerosol LW TOA Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt*Ns |
| Untuned Total-Sky-NoAerosol WN Surface Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns |
| Untuned Total-Sky-NoAerosol WN Surface Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns |
| Untuned Total-Sky-NoAerosol WN TOA Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns |

SDS Index of Untuned TotalSky-NoAerosol Fluxes

| SDS Name | Zonal Monthly 3-Hourly | Zonal Monthly | Global Monthly 3-Hourly | Global Monthly |
| --- | --- | --- | --- | --- |
| Untuned Total-Sky-NoAerosol SW Surface Up | 127 | 339 | 551 | 763 |
| Untuned Total-Sky-NoAerosol SW Surface Down | 128 | 340 | 552 | 764 |
| Untuned Total-Sky-NoAerosol SW TOA Up | 129 | 341 | 553 | 765 |
| Untuned Total-Sky-NoAerosol LW Surface Up | 130 | 342 | 554 | 766 |
| Untuned Total-Sky-NoAerosol LW Surface Down | 131 | 343 | 555 | 767 |
| Untuned Total-Sky-NoAerosol LW TOA Up | 132 | 344 | 556 | 768 |
| Untuned Total-Sky-NoAerosol WN Surface Up | 133 | 345 | 557 | 769 |
| Untuned Total-Sky-NoAerosol WN Surface Down | 134 | 346 | 558 | 770 |
| Untuned Total-Sky-NoAerosol WN TOA Up | 135 | 347 | 559 | 771 |

| Untuned TotalSky Fluxes |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| Untuned Total-Sky SW Surface Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Untuned Total-Sky SW Surface Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Untuned Total-Sky SW TOA Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Untuned Total-Sky LW Surface Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt*Ns |
| Untuned Total-Sky LW Surface Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ngmt*Ns |
| Untuned Total-Sky LW TOA Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt*Ns |
| Untuned Total-Sky WN Surface Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns |
| Untuned Total-Sky WN Surface Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns |
| Untuned Total-Sky WN TOA Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Ns |

SDS Index of Untuned TotalSky Fluxes

| SDS Name | Zonal Monthly 3-Hourly | Zonal Monthly | Global Monthly 3-Hourly | Global Monthly |
| --- | --- | --- | --- | --- |
| Untuned Total-Sky SW Surface Up | 136 | 348 | 560 | 772 |
| Untuned Total-Sky SW Surface Down | 137 | 349 | 561 | 773 |
| Untuned Total-Sky SW TOA Up | 138 | 350 | 562 | 774 |
| Untuned Total-Sky LW Surface Up | 139 | 351 | 563 | 775 |
| Untuned Total-Sky LW Surface Down | 140 | 352 | 564 | 776 |
| Untuned Total-Sky LW TOA Up | 141 | 353 | 565 | 777 |
| Untuned Total-Sky WN Surface Up | 142 | 354 | 566 | 778 |
| Untuned Total-Sky WN Surface Down | 143 | 355 | 567 | 779 |
| Untuned Total-Sky WN TOA Up | 144 | 356 | 568 | 780 |

| Satellite Emulated WN TOA Fluxes |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| Untuned Satellite Emulated WN TOA | 32-bit real | W m-2 | -1400 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Tuned Satellite Emulated WN TOA | 32-bit real | W m-2 | -1400 .. 1400 | Nlon*Nlat*Ngmt*Ns |

SDS Index of Satellite Emulated WN TOA Fluxes

| SDS Name | Zonal Monthly 3-Hourly | Zonal Monthly | Global Monthly 3-Hourly | Global Monthly |
| --- | --- | --- | --- | --- |
| Untuned Satellite Emulated WN TOA | 145 | 357 | 569 | 781 |
| Tuned Satellite Emulated WN TOA | 146 | 358 | 570 | 782 |

| TOA Flux Error |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| Tuned Minus Observed SW TOA | 32-bit real | W m-2 | -1400 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Untuned Minus Observed SW TOA | 32-bit real | W m-2 | -1400 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Tuned Minus Observed LW TOA | 32-bit real | W m-2 | -600 .. 600 | Nlon*Nlat*Ngmt*Ns |
| Untuned Minus Observed LW TOA | 32-bit real | W m-2 | -600 .. 600 | Nlon*Nlat*Ngmt*Ns |

| SDS Index of TOA Fluxes Error |
| --- |
| SDS Name | Zonal Monthly 3-Hourly | Zonal Monthly | Global Monthly 3-Hourly | Global Monthly |
| Tuned Minus Observed SW TOA | 147 | 359 | 571 | 783 |
| Untuned Minus Observed SW TOA | 148 | 360 | 572 | 784 |
| Tuned Minus Observed LW TOA | 149 | 361 | 573 | 785 |
| Untuned Minus Observed LW TOA | 150 | 362 | 574 | 786 |

| Constrainment Adjustments, Table 2.12-5(d) defines Nlev |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| Total column precipitable water - initial | 32-bit real | cm | 0 .. 10 | Nlon*Nlat*Ngmt*Ns |
| Total column precipitable water - adjusted | 32-bit real | cm | -10 .. 10 | Nlon*Nlat*Ngmt*Ns |
| Upper tropospheric precipitable water - initial | 32-bit real | cm | 0 .. 10 | Nlon*Nlat*Ngmt*Ns |
| Upper tropospheric precipitable water - adjusted | 32-bit real | cm | 0 .. 10 | Nlon*Nlat*Ngmt*Ns |
| Upper tropospheric humidity - initial | 32-bit real | N/A | 0.0 ..100.0 | Nlon*Nlat*Ngmt*Ns |
| Upper tropospheric humidity - adjusted | 32-bit real | N/A | 0.0 .. 100.0 | Nlon*Nlat*Ngmt*Ns |
| Aerosol optical depth - initial | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt*Ns |
| Aerosol optical depth - adjusted | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt*Ns |
| Skin temperature - initial | 32-bit real | K | 175 .. 375 | Nlon*Nlat*Ngmt*Ns |
| Skin temperature - adjusted | 32-bit real | K | 175 .. 375 | Nlon*Nlat*Ngmt*Ns |
| Surface pressure | 32-bit real | hPa | 0 .. 800 | Nlon*Nlat*Ngmt*Ns |
| Column ozone - initial | 32-bit real | du | 0 .. 800 | Nlon*Nlat*Ngmt*Ns |
| Mean visible optical depth- adjusted | 32-bit real | N/A | 0 .. 400 | Nlon*Nlat*Ngmt*Ns*Nlev |
| Mean cloud fractional area - adjusted | 32-bit real | % | 0 .. 100 | Nlon*Nlat*Ngmt*Ns*Nlev |
| Mean cloud effective temperature - adjusted | 32-bit real | K | 175 .. 375 | Nlon*Nlat*Ngmt*Ns*Nlev |

| SDS Index of Constrainment Adjustments |
| --- |
| SDS Name | Zonal Monthly 3-Hourly | Zonal Monthly | Global Monthly 3-Hourly | Global Monthly |
| Total column precipitable water - initial | 151 | 363 | 575 | 787 |
| Total column precipitable water - adjusted | 152 | 364 | 576 | 788 |
| Upper tropospheric precipitable water - initia | 153 | 365 | 577 | 789 |
| Upper tropospheric precipitable water - adjusted | 154 | 366 | 578 | 790 |
| Upper tropospheric humidity - initial | 155 | 367 | 579 | 791 |
| Upper tropospheric humidity - adjusted | 156 | 368 | 580 | 792 |
| Aerosol optical depth - initial | 157 | 369 | 581 | 793 |
| Aerosol optical depth - adjusted | 158 | 370 | 582 | 794 |
| Skin temperature - initial | 159 | 371 | 583 | 795 |
| Skin temperature - adjusted | 160 | 372 | 584 | 796 |
| Surface pressure | 161 | 373 | 585 | 797 |
| Column ozone - initial | 162 | 374 | 586 | 798 |
| Mean visible optical depth- adjusted | 163 | 375 | 587 | 799 |
| Mean cloud fractional area - adjusted | 164 | 376 | 588 | 800 |
| Mean cloud effective temperature - adjusted | 165 | 377 | 589 | 801 |

| Surface SW Direct/Diffuse Fluxes |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| Total-Sky SW flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Clear-sky SW flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Pristine-Sky SW flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Actinic-Sky SW flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Total-Sky SW flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Clear-sky SW flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Pristine-Sky SW flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Actinic-Sky SW flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |

| SDS Index of Surface SW Direct/Diffuse Fluxes |
| --- |
| SDS Name | Zonal Monthly 3-Hourly | Zonal Monthly | Global Monthly 3-Hourly | Global Monthly |
| Total-Sky SW flux - Diffuse | 166 | 378 | 590 | 802 |
| Clear-sky SW flux - Diffuse | 167 | 379 | 591 | 803 |
| Pristine-Sky SW flux - Diffuse | 168 | 380 | 592 | 804 |
| Actinic-Sky SW flux - Diffuse | 169 | 381 | 593 | 805 |
| Total-Sky SW flux - Direct | 170 | 382 | 594 | 806 |
| Clear-sky SW flux - Direct | 171 | 383 | 595 | 807 |
| Pristine-Sky SW flux - Direct | 172 | 384 | 596 | 808 |
| Actinic-Sky SW flux - Direct | 173 | 385 | 597 | 809 |

| UVA - UVB Fluxes |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| TOA Downwelling UVB Flux | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| TOA Downwelling UVA Flux | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Pristine UVB Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Pristine UVB Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Pristine UVA Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Pristine UVA Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Clear-Sky UVB Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Clear-Sky UVB Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Clear-Sky UVA Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Clear-Sky UVA Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Total-Sky-NoAerosol UVB Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Total-Sky-NoAerosol UVB Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Total-Sky-NoAerosol UVA Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Total-Sky-NoAerosol UVA Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Total-Sky UVB Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Total-Sky UVB Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Total-Sky UVA Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Total-Sky UVA Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Total-Sky Surface UV Index | 32-bit real | N/A | 0 .. 30 | Nlon*Nlat*Ngmt*Ns |
| Clear-Sky Surface UV Index | 32-bit real | N/A | 0 .. 30 | Nlon*Nlat*Ngmt*Ns |
| Pristine Surface UV Index | 32-bit real | N/A | 0 .. 30 | Nlon*Nlat*Ngmt*Ns |
| Total-Sky-NoAerosol Surface UV- Index | 32-bit real | N/A | 0 .. 30 | Nlon*Nlat*Ngmt*Ns |
| Total-Sky UVB Surface Up | 32-bit real | W m-2 | 0 .. 5 | Nlon*Nlat*Ngmt*Ns |
| Snow Grain Size | 32-bit real | m | 50 .. 2000 | Nlon*Nlat*Ngmt*Ns |
| Match Total Aerosol Optical Depth at 0.55 m | 32-bit real | N/A | 0 .. 10 | Nlon*Nlat*Ngmt*Ns |

| SDS Index of UVA – UVB Fluxes |
| --- |
| SDS Name | Zonal Monthly 3-Hourly | Zonal Monthly | Global Monthly 3-Hourly | Global Monthly |
| TOA Downwelling UVB Flux | 174 | 386 | 598 | 810 |
| TOA Downwelling UVA Flux | 175 | 387 | 599 | 811 |
| Pristine UVB Surface flux - Direct | 176 | 388 | 600 | 812 |
| Pristine UVB Surface flux - Diffuse | 177 | 389 | 601 | 813 |
| Pristine UVA Surface flux - Direct | 178 | 390 | 602 | 814 |
| Pristine UVA Surface flux - Diffuse | 179 | 391 | 603 | 815 |
| Clear-Sky UVB Surface flux - Direct | 180 | 392 | 604 | 816 |
| Clear-Sky UVB Surface flux - Diffuse | 181 | 393 | 605 | 817 |
| Clear-Sky UVA Surface flux - Direct | 182 | 394 | 606 | 818 |
| Clear-Sky UVA Surface flux - Diffuse | 183 | 395 | 607 | 819 |
| Total-Sky-NoAerosol UVB Surface flux - Direct | 184 | 396 | 608 | 820 |
| Total-Sky-NoAerosol UVB Surface flux - Diffuse | 185 | 397 | 609 | 821 |
| Total-Sky-NoAerosol UVA Surface flux - Direct | 186 | 398 | 610 | 822 |
| Total-Sky-NoAerosol UVA Surface flux - Diffuse | 187 | 399 | 611 | 823 |
| Total-Sky UVB Surface flux - Direct | 188 | 400 | 612 | 824 |
| Total-Sky UVB Surface flux - Diffuse | 189 | 401 | 613 | 825 |
| Total-Sky UVA Surface flux - Direct | 190 | 402 | 614 | 826 |
| Total-Sky UVA Surface flux - Diffuse | 191 | 403 | 615 | 827 |
| Total-Sky Surface UV Index | 192 | 404 | 616 | 828 |
| Clear-Sky Surface UV Index | 193 | 405 | 617 | 829 |
| Pristine Surface UV Index | 194 | 406 | 618 | 830 |
| Total-Sky-NoAerosol Surface UV- Index | 195 | 407 | 619 | 831 |
| Total-Sky UVB Surface Up | 196 | 408 | 620 | 832 |
| Snow Grain Size | 197 | 409 | 621 | 833 |
| Match Total Aerosol Optical Depth at 0.55 m | 198 | 410 | 622 | 834 |

| PAR Fluxes |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| TOA Downwelling PAR Flux | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Total-Sky PAR Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Total-Sky PAR Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Total-Sky PAR PURV Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Total-Sky PAR PURV Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Total-Sky PAR ChlorA Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Total-Sky PAR ChlorA Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Clear-Sky PAR Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Clear-Sky PAR Surface Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Pristine PAR Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |
| Pristine PAR Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Ns |

SDS Index of PAR Fluxes

| SDS Name | Zonal Monthly 3-Hourly | Zonal Monthly | Global Monthly 3-Hourly | Global Monthly |
| --- | --- | --- | --- | --- |
| TOA Downwelling PAR Flux | 199 | 411 | 623 | 835 |
| Total-Sky PAR Surface flux - Direct | 200 | 412 | 624 | 836 |
| Total-Sky PAR Surface flux - Diffuse | 201 | 413 | 625 | 837 |
| Total-Sky PAR PURV Surface flux - Direct | 202 | 414 | 626 | 838 |
| Total-Sky PAR PURV Surface flux - Diffuse | 203 | 415 | 627 | 839 |
| Total-Sky PAR ChlorA Surface flux - Direct | 204 | 416 | 628 | 840 |
| Total-Sky PAR ChlorA Surface flux - Diffuse | 205 | 417 | 629 | 841 |
| Clear-Sky PAR Surface flux - Direct | 206 | 418 | 630 | 842 |
| Clear-Sky PAR Surface Surface flux - Diffuse | 207 | 419 | 631 | 843 |
| Pristine PAR Surface flux - Direct | 208 | 420 | 632 | 844 |
| Pristine PAR Surface flux - Diffuse | 209 | 421 | 633 | 845 |

| Pristine-Sky SW MultiStream Correction |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| SW TOA Flux - Up - Pristine-Sky - Corrected | 32-bit real | W m-2 | 0 .. 1000 | Nlon*Nlat*Ngmt*Ns |
| SW Surface Flux - Down- Pristine-Sky - Corrected | 32-bit real | W m-2 | 0 .. 1000 | Nlon*Nlat*Ngmt*Ns |

SDS Index of Pristine-Sky SW MultiStream Correction

| SDS Name | Zonal Monthly 3-Hourly | Zonal Monthly | Global Monthly 3-Hourly | Global Monthly |
| --- | --- | --- | --- | --- |
| SW TOA Flux - Up - Pristine-Sky - Corrected | 210 | 422 | 634 | 846 |
| SW Surface Flux - Down- Pristine-Sky - Corrected | 211 | 423 | 635 | 847 |

Total Bits / Record:		150144

Total Bytes / Record:			18768

Total Records / File:		181

Total Bytes / File:		3,397,008

Total MBytes / File:		3.40

ZAVG Revision Record

The product Revision Record contains information pertaining to approved section changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The authors are listed on the document cover.

| ZAVG Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| N/A | R3V1 | N/A | Updated format to comply with standards. | All |
| 11/15/06 | R3V2 | 639 | Updated to change all tables and added SDS Index tables. | All |
|  |  |  | The EOSDIS Product Code line was removed from the document. (6/17/2008) | Sec. 2.11 |
| 02/08/08 | R3V3 | 667 | Updated to add three parameters. (08/20/2008) | Table 2.11-21(a) |
|  |  |  | Changed SDS Index tables. (08/20/2008) | Tables 2.11-5(b) to 2.11-23(b) |
|  |  |  | Section numbering was changed due to insertion of the ISCCP D2-like DPC. (09/23/2008) | All |
| 11/12/08 | R5V1 | 689 | Updated “Product Version” category. | Sec. 2.12 |
|  |  |  | Removed Beta3 from “Product Version” category. (11/17/2008) | Sec. 2.12 |
|  |  |  | Corrected the Terra and Aqua product versions. (12/08/2008) | Sec. 2.12 |
|  |  |  | Corrected the Terra and Aqua product versions. (12/16/2008) | Sec. 2.12 |
|  |  |  | Reorganized tables for clarity. (02/07/2009) | All |