ADVISORY CIRCULAR

| U.S. Department of Transportation Federal Aviation Administration | Advisory Circular |
| --- | --- |

AC 120-41

DATE: 11/07/1983

AC No:  120-41

Date:  11/7/83

Initiated

by:  AFO-210

Subject:  CRITERIA FOR OPERATIONAL APPROVAL

OF AIRBORNE WIND SHEAR ALERTING

AND FLIGHT GUIDANCE SYSTEMS

1.  PURPOSE.  This advisory circular establishes an acceptable

means, but not the only means, of obtaining operational approval

of an airborne wind shear alerting and flight guidance system.

It describes acceptable simulation test criteria, wind field

modeling data, and minimum performance parameters for evaluating

candidate systems.

2.  FOCUS.  The criteria contained in this advisory circular are

applicable to operators holding operating certificates issued

under Parts 121, 125, and 135 of the Federal Aviation

Regulations.

3.  BACKGROUND.

a.  Since July 1973 there have been 10 U.S. air carrier

accidents attributed to encounters with severe low-level wind

shear during terminal area flight operations.  From 1964 to 1976

there were 25 transport category airplane takeoff or approach-

and-landing accidents in which low-level wind shear was a

possible causal factor.  Investigative studies concerning some of

these accidents, as well as other efforts designed to

characterize wind shear and document its influence on

pilot/aircraft performance and control, have increased awareness

of the potential hazard posed by low-level wind shear in the

airport terminal area.

b.  The Federal Aviation Administration (FAA) research and

development investigations into wind shear causation and

potential solutions have taken a threefold approach to the

problem:  (1) development and implementation of improved

forecasting techniques and procedures for predicting and

reporting low-level wind shear in the terminal area, (2)

placement of wind shear detection equipment on the ground and

transmitting the information to the pilot, (3) installation of

airborne wind shear alerting and flight guidance equipment, or

detection and avoidance equipment, to provide the pilot with

"real time" information if a wind shear phenomena is encountered.

Implementation of improved forecasting techniques and ground-

based low-level wind shear detection equipment affords the

flightcrew the advantage of environmental awareness on which

sound operational decisions can be predicated.  Utilization of

airborne devices will enhance safety to even a greater margin

over that which is provided by forecasting techniques, and the

ground-based detection equipment by affording the pilot early,

reliable recognition of the wind shear phenomena, and providing a

means by which the pilot can utilize all remaining performance

capability, if required, to safely exit any shear inadvertently

encountered.  In combination, this approach to solving the wind

shear hazard in the terminal area will provide flightcrews with

both preflight information and inflight information to help them

cope with the low-level wind shear phenomena.

4.  DEFINITIONS.  The following definitions are applicable to

this advisory circular.

a.  Airborne Wind Shear Alerting System.  A device or system

which identifies the presence of wind shear once the phenomena is

encountered.  An alerting device of this type does not provide

guidance information to the pilot to satisfy the criteria for

alerting and flight guidance systems.

b.  Airborne Wind Shear Alerting and Flight Guidance System.

A device or system which identifies the presence of a severe wind

shear phenomena and provides the pilot with timely alert and

adequate flight guidance for the following:

(1)  Approach/Missed Approach.  To permit the aircraft to

be flown using the maximum performance capability available

without inadvertent loss of control, stall, and without ground

contact.

(2)  Takeoff and Climbout.  To permit the aircraft to be

flown during the initial or subsequent climb segments using the

maximum performance capability available without inadvertent loss

of control or ground contact with excess energy still available.

c.  Airborne Wind Shear Detection and Avoidance System.  A

device or system which detects a potentially severe wind shear

phenomena far enough in advance of the encounter in both the

takeoff/climbout profile and the approach/landing profile to

allow the pilot to successfully avoid the phenomena and thereby

alleviate a flight hazard.

d.  Severe Wind Shear.  A wind shear of such intensity and

duration which would exceed the performance capability of a

particular aircraft type, and cause inadvertent loss of control

or ground contact if the pilot did not have information available

from an airborne wind shear alerting and flight guidance system

which meets the criteria of paragraph 4b.

e.  Proof-of-Concept Testing.  Proof-of-concept testing is

defined as a generic demonstration in a full operational

environment of facilities, weather, crew complement, aircraft

systems, environmental systems, and any other relevant parameters

necessary to show concept validity in terms of performance,

system reliability, repeatability, and typical pilot response to

failure as well as to demonstrate that an equivalent level of

safety is provided.  Proof-of-concept may be established by a

combination of analysis, simulation, and/or flight demonstrations

in an operational environment.

5.  SCOPE.  This advisory circular describes three types of

airborne wind shear systems:  (1) alerting systems, (2) alerting

and flight guidance systems, and (3) detection and avoidance

systems.  The criteria outlined in this document are proposed for

operational approval of alerting and flight guidance systems.

These criteria are designed to permit acceptance of concepts

which provide alerting of the presence of wind shear, and

guidance to the pilot which will enable him to maximize the

remaining performance capability of his aircraft in an effort to

safely exit the shear.  These criteria are intended to be

sufficiently comprehensive to encourage the use of an airborne

wind shear alerting and flight guidance system to enhance flight

safety without unduly restricting technical innovations, or

limiting the integration of existing aircraft equipment as

airborne wind shear alerting devices.  Although current

technology does not permit a description of detailed criteria for

testing and operational approval of detection and avoidance

systems at this time, the agency encourages industry to develop

such technology to provide flightcrews with "predictive" wind

shear information so that potentially hazardous encounters can be

detected and avoided.

6.  SYSTEM APPROVAL.  The type of airborne wind shear alerting

and flight guidance system which may be considered for

operational approval in accordance with the criteria in this

advisory circular is not limited to a specific system or specific

type of system.  Operational approval may be granted to any

system which meets the objectives of this advisory circular and

provides the alerting and flight guidance capabilities described

in paragraph 4b, or any system for which "proof-of-concept

testing" has demonstrated an equivalent level of safety.

7.  TEST METHODS.  One acceptable method for evaluation of an

airborne wind shear alerting and flight guidance system is in a

simulator specifically approved for this purpose by the FAA and

piloted by company line crewmembers.  The following is provided

as an acceptable means of obtaining operational approval for the

candidate wind shear system.  Tests should be conducted to

demonstrate the effectiveness of the proposed system, or

combination of systems, and pilot procedures to successfully

alleviate the hazardous effects of "severe" wind shear during

takeoff and landing.  Since operation in hazardous wind shear

conditions must be evaluated, ground-based piloted simulation is

the safest means of demonstrating compliance.  Inflight tests may

be acceptable if an airborne evaluation can be conducted using

suitable precautions necessary to safeguard the test aircraft and

crew and still provide the necessary data to demonstrate

compliance with the criteria in this advisory circular.

a.  Simulator Equipment.  Simulators used for system

qualification should be specifically approved for this purpose by

the FAA's National Simulator Evaluation Team.  These simulators

should be capable of representing the essential parameters

related to evaluating the proposed wind shear system's

effectiveness.  The simulator should be capable of full mission,

pilot-in-the-loop simulation, with appropriate visual systems,

instrumentation, recording systems, and appropriate dynamic

modeling of the wind shear conditions to be encountered.

Simulators approved for this purpose must meet or exceed all

basic performance required of Phase I equipment (refer to AC 120-

40, Airplane Simulator and Visual System Evaluation).

Alternatives to ground-based simulation must consider and account

for all factors listed above.  Testing should be specific by

aircraft type unless the applicant can show that one satisfactory

test set can be extended to a similar type aircraft with equal or

better effectiveness.  Differences in related systems, flight

dynamics, and aircraft specific procedures should be accounted

for.

b.  Recording Parameters.  The applicant should provide data

in graphic or tabular form for each test run and statistical

summaries of the tests including:  wind shear conditions used,

flightpath records, touchdown dispersions, vertical speed,

aircraft heading and altitude, power settings, aircraft

configurations, visibility and ceiling conditions, and other

relevant parameters which may be necessary to evaluate the

particular system in question.

c.  "Severe" Wind Field Profiles.  Severe wind fields, as

defined in paragraph 4d, are those which would exceed the total

performance capability of a specific airframe and powerplant

combination, unless timely alerting warns the pilot of the

presence of wind shear and adequate flight guidance is available

which would allow the pilot to maneuver the aircraft using the

maximum performance available without inadvertent loss of control

or stall.

(1)  The profiles may either be derived using aircraft

manufacturer performance data for the particular aircraft on

which the approval will take place, or selected from those

profiles in Appendix 1 which meet the definition of "severe" in

paragraph 4d for the aircraft on which the equipment will be

evaluated.

(2)  The profiles which are presented in Appendix 1 are

not necessarily representative of "severe" wind shear values for

any particular type of aircraft, but are included as samples of

wind field profile format acceptable as a method of developing

specific types of wind shear for a particular aircraft and

powerplant combination.  These wind fields have been generated

based on actual data measured and recorded during wind tower

collection efforts and from known accident scenarios.  They are

represented in three-dimensional geometry, except for the

turbulence data which is presented as a function of altitude

alone.  Further research is currently being performed in the area

of wind field modeling and it is anticipated that models specific

to particular types of aircraft and engine combinations will be

available in the future.  Appendix 1 will be updated as that

information becomes available.

8.  TEST SCENARIOS.  The scenarios used for these tests should

represent realistic operating environments expected to be

encountered in line service.  The tests should account for the

fact that wind shear encounters are rare and should be designed

to remove any training bias which might occur because of crew

exposure to repeated severe wind shear profiles in a short period

of time.  For example, it can be expected that crews would

anticipate a severe wind shear and develop an unrealistically

high degree of proficiency with the proposed system in an

evaluation in which a large number of severe wind shear

encounters occur in one simulation period.  In contrast, in

actual service, the wind shear encounter may be unexpected and

the crew may not have had the occasion to use the wind shear

system since the last period of recurrent training.  The result

of such a biased test is likely to cause an apparent increase in

effectiveness of the proposed system either because of

anticipation or unrealistic levels of proficiency.

9.  TEST CREWS.  Pilots used in the evaluation should consist of

appropriately rated and current pilots representative of those

used by an air carrier in line service.  A sufficient number of

crews should be used to ensure that the results are

representative of typical line pilot performance and are not

biased by a select group.

10.  FAA EVALUATIONS.  Test time should be made available for air

carrier operations inspectors representing the Director of Flight

Operations to participate in the evaluation and make

recommendations.

11.  TEST CRITERIA.  For operational approval of an airborne wind

shear alerting and flight guidance system, the evaluation must

conclusively demonstrate the capability of a candidate to alert

the pilot of severe wind shear conditions and provide the pilot

with adequate flight guidance to safely transit or avoid the

hazardous conditions.  These tests should be conducted during the

takeoff, climbout, approach, and landing phases of flight and

should evaluate the system's performance in severe wind shear

conditions which represent a realistic variation of turbulence,

ceiling, visibility, and other relevant conditions expected in

line service.

a.  Takeoff and Climbout.  During takeoff phase tests for an

airborne wind shear alerting and flight guidance system, in

severe wind shear conditions, the system should provide the pilot

sufficient information to permit the aircraft to be flown during

initial or subsequent climb segments using the maximum

performance capability available without inadvertent loss of

control, stall, or ground contact with excess energy still

available.

b.  Approach and Landing.

(1)  During landing phase tests for an airborne wind

shear altering and flight guidance system, in severe wind shear

conditions, the system should alert the pilot to the presence of

a severe wind shear when sufficient performance still remains to

successfully accomplish a go-around.

(2)  The system should provide sufficient information to

the flightcrew during a go-around to allow the aircraft to be

flown using the maximum performance capability available to avoid

ground contact and to climb out of the wind shear condition in a

flight attitude that would preclude an aerodynamic stall.

12.  APPROVAL.

a.  Operational approval for the use of an airborne wind

shear alerting and flight guidance system will be made by the

Director of Flight Operations (AFO-1) after the system receives

supplemental type certificate (STC) airworthiness approval from

the appropriate engineering and manufacturing office.

b.  Operational approval of a new airborne wind shear

alerting and flight guidance system will be based upon the

criteria contained in this advisory circular.  Approvals of

modified wind shear systems (version of systems previously

approved), application of approved systems to similar types of

classes of aircraft, and air carriers using similar equipment

previously approved may be based upon some or all of the

following:  limited flight evaluation, simulation, analysis, and

equivalence to the similar system already approved.

c.  Applicants desiring operational approval of an airborne

wind shear alerting and flight guidance system should submit an

application containing the following material to the appropriate

FAA certificate-holding district office.

(1)  Evidence of an FAA airworthiness (STC) approval of

the system to be operationally evaluated including a description

of the system installation.

(2)  A description of the test methods and wind profiles

to be utilized during the evaluation scenarios.

(3)  Evidence of capability to comply with paragraph 7a.

d.  The principal operations inspector responsible for the

applicant's operating certificate should review the application

to ensure that the proposed evaluation program meets the general

criteria of this advisory circular.  The application should then

be forwarded through the regional Flight Standards Division to

the Office of Flight Operations, AFO-1, for further action.

/s/ Kenneth S. Hunt

Director of Flight Operations

APPENDIX 1.  WIND FIELD DEFINITION AND GENERATION

1.  ABSTRACT.  This appendix details wind shear data that has

been used by the Federal Aviation Administration (FAA) for

conducting aircraft simulations of wind shear encounters.  The

data presented is not necessarily representative of "severe" wind

shear profiles for any specific type of aircraft, but are

included so that interested parties may use the same format in

formulating their own wind field for the purpose of obtaining

operational approval of an airborne wind shear alerting and

flight guidance system, or a detection and avoidance system.

Mean wind (longitudinal, lateral, and vertical) data, in knots,

is a function of altitude and distance from the glidepath

intercept point (in feet); Dryden turbulence data is a function

of altitude only.  Methods for using the data are also outlined.

An explanation of the salient features of the wind field geometry

is also included.

2.  INTRODUCTION.

a.  The wind fields listed in Appendices 2 through 7 are

functions of both distance from the glidepath intercept point

(GPIP) and altitude.  The spacing between each altitude and

distance point is not uniform and is not necessarily the same

from one wind field to the next.  The reason for using nonuniform

spacing is to minimize the storage requirements for the data

base, without compromising the wind shear rate information.

(Note:  If uniform spacing of the wind fields is necessary, then

the grid spacing should collocate with the spacing of the data

bases in Appendices 2 through 7.)  At each distance and altitude

there are three mean windspeeds (longitudinal, lateral, and

vertical--u, v, and w).

b.  At the end of Appendices 2 through 7 is the turbulence

table for each wind field.  The turbulence data is only a

function of altitude.  The altitude spacing is not uniform, nor

does it correspond to the associated mean wind altitude spacing.

The turbulence data at each altitude point includes the root-

mean-squared (RMS) Dryden turbulence intensities and the Dryden

turbulence scale lengths.

3.  COMPUTING THE MEAN WINDS.

a.  Mean windspeeds (u, v, and w) can be linearly

interpolated given an aircraft position referenced to the

intended touchdown point (the GPIP).

b.  If an aircraft's position is outside the limits of the

particular wind field, then an extrapolation is not used.

Instead, the data closest to the given position is used.

Table 1.  Distance Index

Number    Distance from GPIP (+ past/- before) (feet)

1       +40,000

2             0

3        -2,000

4        -4,000

5        -6,000

6        -8,000

7        -9,000

8       -10,000

9       -11,000

10       -12,000

11       -13,000

12       -14,000

13       -16,000

14       -40,000

Using Wind Field 10 (Appendix 7) as an example, the distance

indices are shown in Table. 1.  If an aircraft distance point is

30,000 feet in front of the GPIP, then the windspeeds versus

altitude is interpolated between 13 and 14 from Table 1.  If the

distance exceeds the boundary (i.e., greater than 40,000 feet or

less than -40,000 feet), then the data will be used as if it were

at those distance points.  For example, if an aircraft is 10

nautical miles (approximately 60,000 feet) in front of the GPIP,

then the data at -40,000 feet should be used.

c.  The altitude vectors are determined in a similar manner.

The altitude indices for Wind Field 10 (Appendix 7) are shown in

Table 2.

Table 2.  Altitude Index

Number    Height Above Runway (feet)

1       1,500

2       1,200

3         800

4         650

5         550

6         450

7         350

8         250

9         150

10          20

d.  Using Wind Field 10 (Appendix 7), consider the case of an

aircraft at 30,000 feet in front of the GPIP and at an altitude

of 1,000 feet above the runway height.  The first step is to

define the boundaries to interpolate the three wind components.

The boundaries for this case are between -16,000 and -40,000 feet

distance (numbers 13 and 14 in Table 1), and 1,200 and 800 feet

altitude (numbers 2 and 3 in Table 2).  Finally, interpolate the

three wind components with respect to the boundaries.

In extreme cases, for example, an aircraft 60,000 feet in front

of the GPIP, at an altitude of 2,000 feet, the data is used at -

40,000 feet distance (number 14 in Table 1) and 1,500 feet

altitude (number 1 in Table 2).

Table 3.  Dryden Turbulence Filters

Fu(S) = SIGMAu * SQRT (TAUu/PI) * 1/(1+TAUu*S)

(1+SQRT3*TAUv*S)

Fv(S) = SIGMAv * SQRT (TAUv/PI2) * ---------------------

(1+TAUv*s)*(1+TAUv*S)

(1+SQRT3*TAUw*S)

Fw(S) = SIGMAw * SQRT (TAUw/PI2) * ---------------------

(1+TAUw*S)*(1+TAUw*S)

where:

SIGMAu, SIGMAv, SIGMAw are the RMS intensities;

TAUu = Lu/VA;

TAUv = Lv/VA;

TAUw = Lw/VA;

Lu, Lv, Lw are the turbulence scale lengths;

VA is the aircraft's true airspeed;

PI = 3.1415926535;

PI2 = 6.2831853070 (2 times PI);

SQRT3 = 1.732050808 (square root of 3); and

S is the Laplace transform variable.

The turbulence data is provided at the end of Appendices 2

through 7, and lists SIGMAu, SIGMAv, SIGMAw, Lu, Lv, and Lw

versus altitude.  If the aircraft's altitude is outside the

bounds of the turbulence list, then the data at the boundary is

used.  As with the mean winds, extrapolation is not to be used.

5.  DATA TO BE MADE AVAILABLE FOR REVIEW.

a.  The following items will be made available for each

simulated approach made through any wind field:

(1)  Altitude vs. time;

(2)  Distance from the GPIP vs. time;

(3)  u, v, and w vs. time (mean windspeeds, including

turbulence);

(4)  The partial derivatives of u, v, and w with respect

to altitude vs. time;

(5)  The partial derivatives of u, v, and w with respect

to distance vs. time; and

(6)  The partial derivatives of u, v, and w with respect

to time vs. time.

b.  Items a(4), a(5), and a(6) are the partial derivatives of

the mean windspeeds before turbulence has been added; items a(4)

and a(5) are terms that are used to interpolate for the specific

windspeeds.  Item a(6) can be found by taking item a(4)

multiplied by the rate of descent and added to item a(5)

multiplied by the groundspeed.

6.  INDEX.  The following list shows the titles for Appendices 2

through 7.  The numbering of the "wind field" represents the

labels used by the FAA during its wind shear research and

development program.  Wind fields 1, 2, 3, and 5 are considered

obsolete and are not included.

a.  Wind Field 4 (Appendix 2) - Pages 1-7

b.  Wind Field 6 (Appendix 3) - Pages 1-6

c.  Wind Field 7 (Appendix 4) - Pages 1-7

d.  Wind Field 8 (Appendix 5) - Pages 1-7

e.  Wind Field 9 (Appendix 6) - Pages 1-7

f.  Wind Field 10 (Appendix 7) - Pages 1-6

Wind Field 4

12,900.0 feet beyond the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           12.50              0.00            0.00

75.00           12.50              0.00            0.00

100.00           12.50              0.00            0.00

150.00           12.50              0.00            0.00

200.00           12.50              0.00            0.00

300.00           12.50              0.00            0.00

400.00           12.50              0.00            0.00

500.00           12.50              0.00            0.00

600.00           12.50              0.00            0.00

700.00           12.50              0.00            0.00

800.00           12.50              0.00            0.00

1500.00           12.50              0.00            0.00

10,500.0 feet beyond the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           -7.00              0.00            0.00

75.00           -7.00              0.00            0.00

100.00           -7.00              0.00            0.00

150.00           -6.00              0.00            0.00

200.00           -5.00              0.00            0.00

300.00           -4.00              0.00            0.00

400.00           -2.00              0.00            0.00

500.00           -1.00              0.00            0.00

600.00            0.00              0.00            0.00

700.00            2.00              0.00            0.00

800.00            5.00              0.00            0.00

1500.00            5.00              0.00            0.00

9,500.0 feet beyond the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00          -27.50              0.00            0.00

75.00          -27.50              0.00            0.00

100.00          -27.50              0.00            0.00

150.00          -26.00              0.00            0.00

200.00          -24.00              0.00            0.00

300.00          -20.00              0.00            0.00

400.00          -17.00              0.00            0.00

500.00          -13.00              0.00            0.00

600.00           -9.00              0.00            0.00

700.00            1.00              0.00            0.00

800.00            5.00              0.00            0.00

1500.00            5.00              0.00            0.00

9,000.0 feet beyond the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00          -27.50              0.00            0.00

75.00          -27.50              0.00            0.00

100.00          -27.50              0.00            0.00

150.00          -25.50              0.00            0.00

200.00          -24.00              0.00            0.00

300.00          -20.00              0.00            0.00

400.00          -16.00              0.00            0.00

500.00          -13.00              0.00            0.00

600.00           -9.00              0.00            0.00

700.00           -1.00              0.00            0.00

800.00            5.00              0.00            0.00

1500.00            5.00              0.00            0.00

3,500.0 feet beyond the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00          -27.00              0.00            0.00

75.00          -27.00              0.00            0.00

100.00          -27.00              0.00            0.00

150.00          -27.00              0.00            0.00

200.00          -27.00              0.00            0.00

300.00          -24.00              0.00            0.00

400.00          -23.00              0.00            0.00

500.00          -18.50              0.00            0.00

600.00           -9.00              0.00            0.00

700.00           -1.00              0.00            0.00

800.00            5.00              0.00            0.00

1500.00            5.00              0.00            0.00

1,500.0 feet beyond the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00          -27.50              0.00            0.00

75.00          -27.50              0.00            0.00

100.00          -27.50              0.00            0.00

150.00          -27.50              0.00            0.00

200.00          -24.00              0.00            0.00

300.00          -19.00              0.00            0.00

400.00          -15.00              0.00            0.00

500.00           -8.00              0.00            0.00

600.00           -4.00              0.00            0.00

700.00           -1.00              0.00            0.00

800.00            5.00              0.00            0.00

1500.00            5.00              0.00            0.00

500.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           -3.00              0.00            0.00

75.00           -3.00              0.00           -5.90

100.00           -3.00              0.00           -8.90

150.00           -5.00              0.00          -11.90

200.00           -8.00              0.00          -11.90

300.00            7.00              0.00          -11.90

400.00            7.50              0.00          -11.90

500.00            8.00              0.00          -11.90

600.00            9.00              0.00          -11.90

700.00            9.00              0.00          -11.90

800.00           10.00              0.00          -11.90

1500.00           10.00              0.00          -11.90

1,500.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           -7.00              0.00            0.00

75.00           -7.00              0.00           -5.90

100.00           -6.00              0.00           -8.90

150.00           -5.00              0.00          -11.90

200.00            0.00              0.00          -11.90

300.00            7.50              0.00          -11.90

400.00            9.00              0.00          -11.90

500.00           10.00              0.00          -11.90

600.00           10.00              0.00          -11.90

700.00           10.00              0.00          -11.90

800.00           11.00              0.00          -11.90

1500.00           11.00              0.00          -11.90

2,500.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           20.00              0.00            0.00

75.00           20.00              0.00           -5.90

100.00           20.00              0.00           -8.90

150.00           20.00              0.00          -11.90

200.00           25.00              0.00          -11.90

300.00           12.00              0.00          -11.90

400.00           12.00              0.00          -11.90

500.00           12.00              0.00          -11.90

600.00           12.00              0.00          -11.90

700.00           12.00              0.00          -11.90

800.00           12.00              0.00          -11.90

1500.00           12.00              0.00          -11.90

3,500.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           36.00              0.00            0.00

75.00           36.00              0.00           -5.90

100.00           36.00              0.00           -8.90

150.00           36.00              0.00          -11.90

200.00           36.00              0.00          -11.90

300.00           25.00              0.00          -11.90

400.00           21.00              0.00          -11.90

500.00           18.00              0.00          -11.90

600.00           17.00              0.00          -11.90

700.00           16.00              0.00          -11.90

800.00           14.00              0.00          -11.90

1500.00           14.00              0.00          -11.90

4,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           41.00              0.00            0.00

75.00           41.00              0.00           -5.90

100.00           41.00              0.00           -8.90

150.00           40.00              0.00          -11.90

200.00           39.00              0.00          -11.90

300.00           30.00              0.00          -11.90

400.00           25.00              0.00          -11.90

500.00           22.00              0.00          -11.90

600.00           20.00              0.00          -11.90

700.00           18.00              0.00          -11.90

800.00           16.00              0.00          -11.90

1500.00           16.00              0.00          -11.90

6,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           53.00              0.00            0.00

75.00           53.00              0.00            0.00

100.00           53.00              0.00            0.00

150.00           53.00              0.00            0.00

200.00           50.00              0.00            0.00

300.00           45.00              0.00            0.00

400.00           40.00              0.00            0.00

500.00           35.00              0.00            0.00

600.00           30.00              0.00            0.00

700.00           25.00              0.00            0.00

800.00           20.00              0.00            0.00

1500.00           20.00              0.00            0.00

7,500.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           53.00              0.00            0.00

75.00           53.00              0.00            0.00

100.00           53.00              0.00            0.00

150.00           53.00              0.00            0.00

200.00           53.00              0.00            0.00

300.00           49.00              0.00            0.00

400.00           47.50              0.00            0.00

500.00           43.00              0.00            0.00

600.00           34.00              0.00            0.00

700.00           25.50              0.00            0.00

800.00           20.00              0.00            0.00

1500.00           20.00              0.00            0.00

12,500.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           53.00              0.00            0.00

75.00           53.00              0.00            0.00

100.00           53.00              0.00            0.00

150.00           51.00              0.00            0.00

200.00           48.00              0.00            0.00

300.00           46.00              0.00            0.00

400.00           42.00              0.00            0.00

500.00           38.00              0.00            0.00

600.00           34.00              0.00            0.00

700.00           25.50              0.00            0.00

800.00           20.00              0.00            0.00

1500.00           20.00              0.00            0.00

14,500.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           35.00              0.00            0.00

75.00           35.00              0.00            0.00

100.00           35.00              0.00            0.00

150.00           34.00              0.00            0.00

200.00           33.00              0.00            0.00

300.00           32.00              0.00            0.00

400.00           28.50              0.00            0.00

500.00           27.50              0.00            0.00

600.00           25.00              0.00            0.00

700.00           22.00              0.00            0.00

800.00           20.00              0.00            0.00

1500.00           20.00              0.00            0.00

17,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           12.50              0.00            0.00

75.00           12.50              0.00            0.00

100.00           12.50              0.00            0.00

150.00           12.50              0.00            0.00

200.00           12.50              0.00            0.00

300.00           12.50              0.00            0.00

400.00           12.50              0.00            0.00

500.00           12.50              0.00            0.00

600.00           12.50              0.00            0.00

700.00           12.50              0.00            0.00

800.00           12.50              0.00            0.00

1500.00           12.50              0.00            0.00

Wind Field 4

Dryden Turbulence Data

Altitude       Rms Intensities             Scale Lengths

(feet)           (Kts)                      (feet)

Long       Lat     Vert     Long      Lat     Vert

20.00    3.40      2.70     2.34   105.70    49.70    10.40

100.00    4.05      3.46     3.53   216.70   134.20    53.00

200.00    4.43      3.95     4.35   306.50   213.50   106.00

400.00    4.85      4.50     5.36   433.50   339.60   212.00

600.00    5.11      4.86     6.05   530.90   445.60   318.00

1500.00    5.74      5.78     7.94   840.90   824.50   795.30

Wind Field 6

40,000.0 feet beyond the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00          -16.90              3.00            0.00

150.00          -19.40              7.50           -0.20

250.00          -20.10              8.00           -0.70

350.00          -23.60              9.00            2.20

450.00          -20.80             10.00           14.70

550.00          -26.70             11.00           -9.70

650.00          -13.50             12.00           -9.70

800.00           -4.60             12.80           -6.50

1200.00           -4.00             11.20           -3.30

1500.00           -4.80             10.00           -3.40

5,000.0 feet beyond the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00          -16.90              3.00            0.00

150.00          -19.40              7.50           -0.20

250.00          -20.10              8.00           -0.70

350.00          -23.60              9.00            2.20

450.00          -20.80             10.00           14.70

550.00          -26.70             11.00           -9.70

650.00          -13.50             12.00           -9.70

800.00           -4.60             12.80           -6.50

1200.00           -4.00             11.20           -3.30

1500.00           -4.80             10.00           -3.40

3,000.0 feet beyond the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00          -15.50              3.00            0.00

150.00          -20.30              7.50           -0.40

250.00          -21.40              8.00           -2.50

350.00          -23.80              9.00           -1.10

450.00          -26.60             10.00           -2.50

550.00          -26.00             11.00           -8.00

650.00          -23.50             12.00          -12.90

800.00           -5.60             12.80           -7.70

1200.00           -3.10             11.20           -7.40

1500.00           -2.30             10.00           -6.10

1,000.0 feet beyond the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00          -13.20              3.00            0.00

150.00          -19.90              7.50            0.00

250.00          -22.20              8.00           -3.60

350.00          -20.80              9.00           -6.00

450.00          -25.60             10.00            0.00

550.00          -28.40             11.00            0.00

650.00          -23.10             12.00          -11.40

800.00           -9.10             12.80          -10.90

1200.00           -2.70             11.20           -8.40

1500.00           -2.40             10.00           -9.00

1,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           -5.50              3.00            0.00

150.00           -9.90              7.50           -0.90

250.00          -10.40              8.00           -6.10

350.00          -10.40              9.00          -17.90

450.00          -11.10             10.00          -27.70

550.00           -7.00             11.00          -30.60

650.00           -4.10             12.00          -27.00

800.00            0.00             12.80          -16.60

1200.00            0.00             11.20          -14.80

1500.00            0.00             10.00          -14.80

3,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00            5.50              3.00            0.00

150.00            9.90              7.50           -0.90

250.00           10.40              8.00           -6.10

350.00           10.40              9.00          -17.90

450.00           11.10             10.00          -27.70

550.00            7.00             11.00          -30.60

650.00            4.10             12.00          -27.70

800.00            0.00             12.80          -16.60

1200.00            0.00             11.20          -14.80

1500.00            0.00             10.00          -14.80

4,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           11.90              3.00            0.00

150.00           17.50              7.50           -0.70

250.00           18.80              8.00           -6.10

350.00           20.80              9.00          -10.30

450.00           18.80             10.00          -12.30

550.00           17.40             11.00          -24.00

650.00            6.20             12.00          -24.60

800.00            5.60             12.80          -13.40

1200.00            2.40             11.20          -14.00

1500.00            1.50             10.00          -12.30

5,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           13.20              3.00            0.00

150.00           19.90              7.50            0.00

250.00           22.20              8.00           -3.60

350.00           20.80              9.00           -6.00

450.00           25.60             10.00            0.00

550.00           28.40             11.00            0.00

650.00           23.10             12.00          -11.40

800.00            9.10             12.80          -10.90

1200.00            2.70             11.20           -8.40

1500.00            2.40             10.00           -9.00

6,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           14.50              3.00            0.00

150.00           20.80              7.50           -0.40

250.00           21.50              8.00           -2.60

350.00           23.10              9.00           -4.10

450.00           29.00             10.00            2.30

550.00           28.40             11.00            0.00

650.00           25.40             12.00           11.90

800.00            7.80             12.80            9.70

1200.00            3.20             11.20            8.90

1500.00            2.40             10.00            7.00

7,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           15.50              3.00            0.00

150.00           20.30              7.50           -0.40

250.00           21.40              8.00           -2.50

350.00           23.80              9.00           -1.10

450.00           26.60             10.00            2.50

550.00           26.00             11.00           -8.00

650.00           23.50             12.00          -12.90

800.00            5.60             12.80           -7.70

1200.00            3.10             11.20           -7.40

1500.00            2.30             10.00           -6.10

8,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           16.80              3.00            0.00

150.00           20.10              7.50           -0.20

250.00           20.80              8.00           -0.90

350.00           23.80              9.00            0.00

450.00           25.50             10.00            6.00

550.00           25.30             11.00          -12.90

650.00           20.80             12.00          -12.90

800.00            4.90             12.80           -8.10

1200.00            3.30             11.20           -5.60

1500.00            6.10             10.00           -4.40

9,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           16.90              3.00            0.00

150.00           19.40              7.50           -0.20

250.00           20.10              8.00           -0.70

350.00           23.60              9.00            2.20

450.00           20.80             10.00           14.70

550.00           26.70             11.00           -9.70

650.00           13.50             12.00           -9.70

800.00            4.60             12.80           -6.50

1200.00            4.00             11.20           -3.30

1500.00            4.80             10.00           -3.40

11,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           17.10              3.00            0.00

150.00           19.30              7.50            0.00

250.00           20.00              8.00           -0.20

350.00           23.20              9.00            2.20

450.00           26.60             10.00           -2.50

550.00           17.80             11.00           -4.40

650.00           15.60             12.00           -3.00

800.00            6.60             12.80           -1.90

1200.00            6.10             11.20           -1.50

1500.00            5.80             10.00           -0.90

50,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00            9.60              3.00            0.00

150.00           19.10              7.50            0.00

250.00           20.10              8.00            0.00

350.00           22.90              9.00            0.00

450.00           26.70             10.00            0.00

550.00           19.00             11.00            0.00

650.00           15.80             12.00            0.00

800.00            7.00             12.80            0.00

1200.00            6.50             11.20            0.00

1500.00            6.00             10.00            0.00

Wind Field 6

Dryden Turbulence Data

Altitude       Rms Intensities             Scale Lengths

(feet)           (Kts)                      (feet)

Long       Lat     Vert     Long      Lat     Vert

20.00    3.40      2.70     2.34   105.70    49.70    10.40

100.00    4.05      3.46     3.53   216.70   134.20    53.00

200.00    4.43      3.95     4.35   306.50   213.50   106.00

400.00    4.85      4.50     5.36   433.50   339.60   212.00

600.00    5.11      4.86     6.05   530.90   445.60   318.00

1500.00    5.74      5.78     7.94   840.90   824.50   795.30

Wind Field 7

50,000.0 feet beyond the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           10.69              4.86            0.00

164.04           11.66              3.89            0.39

328.08           12.24              2.92            1.94

492.12           12.63              0.58            2.92

656.17           13.22             -0.49            3.89

820.21           14.58             -1.94            5.83

984.25           13.02             -3.89            7.39

1148.29           12.44             -4.28            7.97

1312.33           12.44             -4.28            7.77

1476.37           12.44             -4.47            6.80

1640.42           12.24             -4.47            5.83

4,000.0 feet beyond the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           10.69              4.86            0.00

164.04           11.66              3.89            0.39

328.08           12.24              2.92            1.94

492.12           12.63              0.58            2.92

656.17           13.22             -0.49            3.89

820.21           14.58             -1.94            5.83

984.25           13.02             -3.89            7.39

1148.29           12.44             -4.28            7.97

1312.33           12.44             -4.28            7.77

1476.37           12.44             -4.47            6.80

1640.42           12.24             -4.47            5.83

2,633.0 feet beyond the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00            9.23              7.09            0.00

164.04           10.92              5.54           -0.39

328.08           12.63              3.41           -1.85

492.12           12.50              0.29           -2.14

656.17           15.69             -0.19           -2.04

820.21           16.04             -3.40           -2.92

984.25           15.94             -3.98           -3.30

1148.29           15.49             -4.18           -3.89

1312.33           15.49             -5.54           -4.08

1476.37           14.89             -6.12           -4.08

1640.42           14.81             -6.51           -4.08

1,266.0 feet beyond the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00            3.89              7.77            0.00

164.04            5.25              7.19            0.00

328.08            8.75              3.89           -0.39

492.12           12.38              0.97           -0.68

656.17           15.55              0.00            0.78

820.21           18.46             -2.33            0.97

984.25           20.41             -3.89            1.17

1148.29           20.60             -5.05            1.94

1312.33           20.41             -6.80            2.14

1476.37           19.83             -7.77            2.33

1640.42           18.46             -9.14            2.33

101.1 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           10.69              7.77            0.00

164.04           11.72              6.51           -0.37

328.08           12.63              4.47           -1.94

492.12           12.24              3.50           -2.92

656.17           15.55              2.62           -3.11

820.21           13.61              0.58           -5.83

984.25           13.02             -1.94           -6.03

1148.29           12.63             -4.28           -5.83

1312.33           12.24             -6.51           -4.28

1476.37           13.90             -8.94           -4.08

1640.42            8.36            -11.66           -3.89

1,468.1 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           16.52              5.64            0.00

164.04           18.56              4.66           -0.31

328.08           20.41              4.47           -1.36

492.12           19.79              4.08           -1.94

656.17           19.86              3.89           -2.14

820.21           19.71              3.30           -2.14

984.25           24.49              1.94           -1.94

1148.29           21.77              0.00           -0.74

1312.33           20.41             -2.92           -0.58

1476.37           16.52             -5.83            0.00

1640.42           14.48             -7.77            1.01

2,835.1 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           24.30              1.36            0.00

164.04           24.68              1.36           -0.23

328.08           24.68              1.26           -1.03

492.12           24.68              1.94           -0.58

656.17           24.88              1.94            0.00

820.21           24.49              1.36            0.19

984.25           24.61              0.78            0.49

1148.29           23.85              0.97            1.13

1312.33           21.87             -0.68            1.94

1476.37           20.31             -2.33            2.47

1640.42           20.60             -4.28            3.46

4,202.2 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           20.60             -2.92            0.00

164.04           21.48             -1.55           -0.17

328.08           21.48             -1.55           -0.70

492.12           23.27             -1.55           -0.41

656.17           23.27             -1.36           -0.23

820.21           22.45             -0.97            0.00

984.25           23.56             -0.58            0.00

1148.29           22.88             -0.58            0.58

1312.33           20.47             -0.97            0.72

1476.37           20.60             -1.55            1.65

1640.42           20.60             -1.94            2.57

5,569.2 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           20.60             -3.89            0.00

164.04           20.49             -3.01           -0.12

328.08           20.51             -2.62           -0.37

492.12           21.83             -1.55           -0.23

656.17           21.67             -0.68           -0.31

820.21           20.41              0.00           -0.19

984.25           20.21              0.00           -0.19

1148.29           19.38              0.10           -0.14

1312.33           18.33              0.00            0.10

1476.37           16.99             -0.29            0.19

1640.42           17.55             -0.39            0.00

6,936.2 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           19.63             -3.89            0.00

164.04           20.60             -3.50           -0.04

328.08           19.24             -2.72           -0.02

492.12           20.41             -1.36           -0.06

656.17           18.76              0.00           -0.08

820.21           18.37              0.00            1.40

984.25           17.45              0.00            0.00

1148.29           16.33              0.00            2.00

1312.33           12.83              0.00            3.89

1476.37           10.05              0.00            5.97

1640.42            6.71             -2.92            9.72

8,303.2 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           16.72             -5.54            0.00

164.04           15.10             -5.15            0.04

328.08           14.58             -4.86            1.75

492.12           10.50             -4.66            2.92

656.17            9.00             -4.28            3.89

820.21           10.15             -4.08            4.86

984.25            9.52             -4.18            5.83

1148.29            5.91             -4.28            5.93

1312.33            2.33             -4.47            6.90

1476.37           -0.97             -4.08            6.32

1640.42           -3.85             -6.51            7.00

9,670.3 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           12.42             -7.97            0.00

164.04           10.86             -7.19            0.14

328.08            8.75             -7.00            1.26

492.12            7.39             -6.61            2.04

656.17            3.01             -5.44            1.73

820.21            0.58             -5.44            2.92

984.25           -0.97             -5.64            1.75

1148.29            3.27             -6.22            2.14

1312.33           -3.63             -6.61            3.11

1476.37           -4.18             -6.03            2.92

1640.42           -6.06             -7.77            3.62

11,037.3 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00            8.12             -7.58            0.00

164.04            6.63             -7.58            0.17

328.08            3.89             -7.48            0.80

492.12            4.28             -7.19            1.17

656.17            0.00             -6.22            1.07

820.21           -0.91             -6.32            0.97

984.25           -2.04             -6.71            1.34

1148.29           -3.19             -7.19            1.40

1312.33           -5.23             -7.48            1.57

1476.37           -0.14             -7.48            2.08

1640.42           -7.06             -7.77            2.78

12,404.3 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00            3.83             -6.80            0.00

164.04            2.39             -7.19            0.10

328.08            0.97             -7.19            0.31

492.12            1.17             -7.39            0.29

656.17           -2.92             -7.00            0.41

820.21           -2.41             -7.19            0.72

984.25           -3.11             -7.39            0.93

1148.29           -3.30             -7.58            0.97

1312.33           -6.80             -7.77            1.07

1476.37           -8.26             -7.77            1.61

1640.42           -8.94             -7.97            1.94

13,771.3 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00            0.00             -6.22            0.00

164.04           -1.22             -6.61            0.02

328.08           -1.94             -6.90            0.10

492.12           -3.34             -7.39            0.00

656.17           -5.83             -7.58            1.22

820.21           -6.16             -7.87            0.47

984.25           -7.33             -7.97            0.52

1148.29           -7.68             -7.87            0.54

1312.33           -9.72             -8.07            0.56

1476.37          -10.38             -8.07            0.84

1640.42          -10.88             -8.07            0.91

50,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00            0.00             -6.22            0.00

164.04           -1.22             -6.61            0.02

328.08           -1.94             -6.90            0.10

492.12           -3.34             -7.39            0.00

656.17           -5.83             -7.58           -1.22

820.21           -6.16             -7.87            0.47

984.25           -7.33             -7.97            0.52

1148.29           -7.68             -7.87            0.54

1312.33           -9.72             -8.07            0.56

1476.37          -10.38             -8.07            0.84

1640.42          -10.88             -8.07            0.91

Wind Field 7

Dryden Turbulence Data

Altitude       Rms Intensities             Scale Lengths

(feet)           (Kts)                      (feet)

Long       Lat     Vert     Long      Lat     Vert

20.00    3.40      2.70     2.34   105.70    49.70    10.40

100.00    4.05      3.46     3.53   216.70   134.20    53.00

200.00    4.43      3.95     4.35   306.50   213.50   106.00

400.00    4.85      4.50     5.36   433.50   339.60   212.00

600.00    5.11      4.86     6.05   530.90   445.60   318.00

1500.00    5.74      5.78     7.94   840.90   824.50   795.30

Wind Field 8

50,000.0 feet beyond the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00            5.17             15.45            0.00

164.04            4.98             15.74            0.06

328.08            5.01             16.04            0.12

492.12            5.01             16.13            0.39

656.17            5.05             17.49            0.52

820.21            5.05             18.46            0.64

984.25            4.86             18.85            0.43

1148.29            4.86             19.05            0.64

1312.33            4.80             18.85            0.72

1476.37            5.00             18.76            0.70

1640.42            4.33             18.56            0.97

3,000.0 feet beyond the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00            5.17             15.45            0.00

164.04            4.98             15.74            0.06

328.08            5.01             16.04            0.12

492.12            5.01             16.13            0.39

656.17            5.05             17.49            0.52

820.21            5.05             18.46            0.64

984.25            4.86             18.85            0.43

1148.29            4.86             19.05            0.64

1312.33            4.80             18.85            0.72

1476.37            5.00             18.76            0.70

1640.42            4.33             18.56            0.97

1,177.3 feet beyond the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00            4.94             15.35            0.00

164.04            4.74             15.55            0.21

328.08            4.90             15.94            0.49

492.12            4.90             16.91            1.55

656.17            5.05             18.85            1.54

820.21            5.05             19.63            1.94

984.25            4.86             20.21            1.11

1148.29            4.86             20.99            1.42

1312.33            4.66             20.60            1.69

1476.37            3.89             20.41            1.63

1640.42            2.74             19.83            2.39

645.5 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           -3.40             17.10            0.00

164.04           -5.58             16.33            0.39

328.08           -5.25             18.17            0.86

492.12           -3.21             18.17            0.97

656.17           -2.24             20.60            2.53

820.21           -2.04             20.89            3.25

984.25           -1.46             22.06            3.11

1148.29           -0.97             23.03            3.89

1312.33           -0.97             22.16            4.96

1476.37            0.97             21.87            5.54

1640.42            1.17             20.99            5.93

2,468.2 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00          -22.35             23.13            0.00

164.04          -22.55             20.21           -0.14

328.08          -22.55             23.32            0.06

492.12          -18.21             22.35           -0.19

656.17          -17.63             27.21            0.52

820.21          -17.49             25.66            1.17

984.25          -22.35             27.40            0.00

1148.29          -22.35             25.85            0.97

1312.33          -22.35             27.21            1.55

1476.37          -20.41             25.07            1.94

1640.42          -18.46             23.90            3.69

4,290.9 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00          -21.48             27.21            0.00

164.04          -21.77             28.57            0.06

328.08          -22.02             26.82           -0.14

492.12          -22.35             27.89           -0.29

656.17          -22.55             28.47           -0.19

820.21          -22.84             29.64           -0.19

984.25          -24.20             27.60           -0.19

1148.29          -24.33             27.30           -0.10

1312.33          -24.68             26.53            0.00

1476.37          -24.06             24.59            0.00

1640.42          -24.30             23.42            0.00

6,113.7 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00          -21.57             39.06            0.00

164.04          -21.38             38.87            1.36

328.08          -21.87             37.50            1.94

492.12          -22.35             35.37            1.94

656.17          -23.36             34.60            1.94

820.21          -24.49             29.93            1.94

984.25          -26.04             27.79            1.85

1148.29          -27.79             27.21            1.94

1312.33          -28.82             24.30            2.14

1476.37          -30.13             23.52            1.94

1640.42          -32.59             23.52            1.94

7,936.4 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00          -25.07             38.97            0.00

164.04          -24.30             36.83            1.55

328.08          -25.21             34.69            3.40

492.12          -25.85             32.17            4.16

656.17          -26.98             29.06            5.89

820.21          -29.93             24.98            5.44

984.25          -29.35             22.45            5.93

1148.29          -32.85             20.51            8.36

1312.33          -34.21             18.66            6.94

1476.37          -36.35             15.84            8.36

1640.42          -38.29             13.51            8.36

9,759.1 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00          -22.35             27.21            0.00

164.04          -24.80             26.43            1.75

328.08          -25.66             25.66            2.92

492.12          -26.71             21.77            4.18

656.17          -27.48             17.49            5.83

820.21          -28.36             13.41            6.45

984.25          -30.36             11.66            6.80

1148.29          -31.78             10.30            5.66

1312.33          -33.53              5.83            6.80

1476.37          -34.95              3.89            6.74

1640.42          -37.41              3.10            6.47

11,581.9 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00          -22.16             14.58            0.00

164.04          -22.35             13.90           -0.04

328.08          -24.30             13.41            0.00

492.12          -26.24             10.39            1.03

656.17          -26.43              7.09            1.46

820.21          -26.76              6.80            1.94

984.25          -29.93              3.89            2.33

1148.29          -30.71              2.33            2.95

1312.33          -32.07              2.33            3.17

1476.37          -33.37              1.94            3.89

1640.42          -35.96              0.77            3.89

13,404.6 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00          -18.46             19.44            0.00

164.04          -19.30             16.13           -0.39

328.08          -21.07             13.41           -0.58

492.12          -22.74             10.69           -0.39

656.27          -24.68              7.77            0.00

820.21          -24.49              4.66            1.26

984.25          -26.34              2.53            1.50

1148.29          -26.47             -0.58            1.50

1312.33          -30.61             -3.89            1.65

1476.37          -31.43             -4.66            1.36

1640.42          -34.50             -7.77            1.36

15,227.3 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00          -15.45             17.49            0.00

164.04          -16.42             16.23           -0.04

328.08          -19.16             11.95            0.00

492.12          -20.80              8.36            0.00

656.17          -22.93              4.86            0.39

820.21          -24.43              1.94            1.09

984.25          -26.36             -0.39            1.71

1148.29          -26.61             -2.04            1.94

1312.33          -29.35             -3.89            2.33

1476.37          -29.78             -6.51            2.33

1640.42          -30.13             -7.77            2.08

17,050.1 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00          -14.58             13.61            0.00

164.04          -18.08             11.66            0.10

328.08          -19.30              7.77            0.19

492.12          -22.16              5.44            0.19

656.17          -22.84              2.92            0.78

820.21          -24.39             -0.19            0.39

984.25          -26.24             -1.55            0.43

1148.29          -26.74             -3.50            0.66

1312.33          -28.18             -5.25            0.97

1476.37          -28.73             -5.83            1.75

1640.42          -29.02             -7.58            1.75

18,872.8 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00          -20.02             11.76            0.00

164.04          -20.31             10.30           -0.19

328.08          -22.06              7.77           -0.39

492.12          -22.60              3.89           -0.39

656.17          -23.58              1.46           -0.39

820.21          -24.33             -1.10           -0.19

984.25          -24.92             -3.11            0.00

1148.29          -26.38             -4.37            0.00

1312.33          -27.02             -6.71            0.14

1476.37          -27.68             -7.29            1.17

1640.42          -27.93             -7.68            0.87

20,695.5 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00          -22.35             12.24            0.00

164.04          -22.55             11.66            0.00

328.08          -22.74              7.77            0.19

492.12          -22.93              3.89            0.19

656.17          -24.30              0.00            0.39

820.21          -24.30             -1.94            0.39

984.25          -26.24             -4.86            0.58

1148.29          -26.43             -5.25            0.58

1312.33          -26.63             -5.83            0.58

1476.37          -26.63             -6.22            0.58

1640.42          -26.82             -7.19            0.00

50,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00          -22.35             12.24            0.00

164.04          -22.55             11.66            0.00

328.08          -22.74              7.77            0.19

492.12          -22.93              3.89            0.19

656.17          -24.30              0.00            0.39

820.21          -24.30             -1.94            0.39

984.25          -26.24             -4.86            0.58

1148.29          -26.43             -5.25            0.58

1312.33          -26.63             -5.83            0.58

1476.37          -26.63             -6.22            0.58

1640.42          -26.82             -7.19            0.00

Wind Field 8

Dryden Turbulence Data

Altitude       Rms Intensities             Scale Lengths

(feet)           (Kts)                      (feet)

Long       Lat     Vert     Long      Lat     Vert

20.00    3.40      2.70     2.34   105.70    49.70    10.40

100.00    4.05      3.46     3.53   216.70   134.20    53.00

200.00    4.43      3.95     4.35   306.50   213.50   106.00

400.00    4.85      4.50     5.36   433.50   339.60   212.00

600.00    5.11      4.86     6.05   530.90   445.60   318.00

1500.00    5.74      5.78     7.94   840.90   824.50   795.30

Wind Field 9

50,000.0 feet beyond the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           13.61             -0.19            0.00

164.04           12.44              0.00           -1.75

328.08           10.69              0.00           -1.94

492.12            9.72              1.94           -2.14

656.17            9.33              3.88           -2.53

820.21            9.14              4.08           -2.92

984.25            9.14              4.08           -2.92

1148.29            8.94              4.08           -2.92

1312.33            8.94              4.08           -3.11

1476.37            8.94              4.08           -3.50

1640.42            8.75              4.08           -3.50

1,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           13.61             -0.19            0.00

164.04           12.44              0.00           -1.75

328.08           10.69              0.00           -1.94

492.12            9.72              1.94           -2.14

656.17            9.33              3.88           -2.53

820.21            9.14              4.08           -2.92

984.25            9.14              4.08           -2.92

1148.29            8.94              4.08           -2.92

1312.33            8.94              4.08           -3.11

1476.37            8.94              4.08           -3.50

1640.42            8.75              4.08           -3.50

1,806.8 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           25.46              3.11            0.00

164.04           23.81              1.94           -0.87

328.08           22.35              2.92           -0.78

492.12           21.38              1.07           -0.97

656.17           19.44              0.68           -1.17

820.21           18.08              0.00           -1.36

984.25           17.49             -0.10           -1.94

1148.29           17.10             -0.97           -2.24

1312.33           16.13             -0.78           -2.20

1476.37           15.74             -0.58           -2.72

1640.42           14.91             -0.49           -2.58

2,613.6 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           21.96              0.00            0.00

164.04           21.96              0.00            1.55

328.08           21.38              0.19            0.19

492.12           22.02              0.19            0.97

656.17           21.38              0.00            0.97

820.21           20.54             -0.97           -0.17

984.25           19.05             -0.39            0.58

1148.29           18.17             -3.11            0.19

1312.33           17.49             -2.72            0.00

1476.37           17.10             -1.55           -1.81

1640.42           16.33             -1.55           -1.46

3,420.4 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           17.49             -3.30            0.00

164.04           19.92             -4.08           -0.58

328.08           20.08             -4.08           -0.23

492.12           22.35             -4.18           -0.19

656.17           21.96             -3.50           -0.10

820.21           19.96             -3.40            0.00

984.25           20.47             -3.89            0.45

1148.29           21.38             -3.30           -0.10

1312.33           20.08             -2.82           -0.43

1476.37           18.02             -1.17            0.10

1640.42           18.52             -0.29            0.00

4,227.2 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           22.35             -4.08            0.00

164.04           22.16             -4.08           -1.55

328.08           21.71             -3.69           -1.17

492.12           22.02             -4.08           -0.97

656.17           22.08             -4.08           -0.58

820.21           19.63             -3.69           -0.39

984.25           17.49             -3.11           -0.06

1148.29           18.08             -2.72            0.23

1312.33           17.10             -2.72            0.00

1476.37           17.49             -0.97            1.11

1640.42           17.10              0.00            2.04

5,034.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           19.20             -3.50            0.00

164.04           21.69             -3.30           -0.02

328.08           22.12             -3.40           -0.10

492.12           21.90             -3.30           -0.10

656.17           21.38             -3.30            0.00

820.21           19.69             -3.40            0.00

984.25           17.49             -3.21            0.78

1148.29           14.97             -2.62            0.91

1312.33           14.38             -2.53            1.94

1476.37           13.80             -1.46            1.94

1640.42           11.80              -0.97            2.47

5,840.7 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           12.63             -5.25            0.00

164.04           18.46             -4.86            0.80

328.08           21.38             -5.83            1.67

492.12           20.35             -4.08            1.94

656.17           21.38             -3.89            2.29

820.21           19.05             -3.89            2.72

984.25           17.49             -3.50            2.84

1148.29           12.69             -0.58            3.40

1312.33            9.72              0.97            3.89

1476.37            5.83              3.11            4.72

1640.42            5.19              0.39            5.35

6,647.5 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           14.38             -8.07            0.00

164.04           13.80             -6.90            0.86

328.08           15.84             -7.77            1.73

492.12           15.55             -5.83            1.94

656.17           14.58             -4.28            2.82

820.21           11.66             -2.92            3.30

984.25            9.33              0.29            3.89

1148.29            5.83              5.44            4.31

1312.33            4.80              8.16            5.35

1476.37            3.50             12.44            7.13

1640.42            2.92             14.09            7.91

7,454.3 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           11.66             -3.89            0.00

164.04           11.27             -4.08            0.89

328.08           10.50             -5.25            1.77

492.12            8.75             -1.75            1.94

656.17            5.83              1.75            3.36

820.21            4.28              3.69            3.89

984.25            3.50              7.77            4.76

1148.29            1.94             13.61            4.98

1312.33            1.85             16.52            6.80

1476.37            1.30             20.41            7.77

1640.42            0.78             23.32            8.36

8,261.1 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           12.24              1.94            0.00

164.04            9.33              0.00            0.95

328.08            6.32              2.33            1.83

492.12            4.41              5.34            1.94

656.17            3.01             10.00            3.89

820.21            2.72             13.50            3.63

984.25            1.17             16.62            5.64

1148.29           -0.25             20.89            5.62

1312.33           -0.87             22.25            6.32

1476.37           -0.97             23.32            7.77

1640.42           -1.26             24.30            8.01

9,067.9 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00            5.83              0.00            0.00

164.04            3.89              3.88            0.93

328.08            2.53              9.33            1.87

492.12            1.22             11.85            1.94

656.17            0.39             17.49            3.89

820.21           -0.97             21.18            3.38

984.25           -1.94             23.52            5.05

1148.29           -3.25             25.26            5.40

1312.33           -3.50             25.46            5.83

1476.37           -3.50             26.24            7.09

1640.42           -3.79             26.43            7.44

9,874.7 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           -0.19              8.74            0.00

164.04            0.00             11.08            0.87

328.08           -0.97             14.28            1.89

492.12           -1.71             19.14            2.00

656.17           -4.18             23.22            3.89

820.21           -3.89             25.85            3.13

984.25           -4.86             26.63            4.47

1148.29           -5.97             27.21            4.74

1312.33           -6.10             27.40            5.25

1476.37           -5.13             27.21            6.06

1640.42           -5.54             27.21            6.47

10,681.5 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           -3.11             11.85            0.00

164.04           -3.36             15.55            0.84

328.08           -3.50             20.79            1.92

492.12           -4.28             24.10            2.08

656.17           -5.05             27.40            3.21

820.21           -5.83             27.40            2.90

984.25           -6.80             27.40            3.89

1148.29           -6.41             27.21            4.10

1312.33           -6.34             27.21            4.66

1476.37           -6.41             27.40            5.05

1640.42           -5.83             27.21            5.19

11,488.3 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           -5.34             14.87            0.00

164.04           -5.44             18.46            0.78

328.08           -5.25             23.42            1.55

492.12           -5.93             26.63            2.14

656.17           -5.64             27.41            2.04

820.21           -6.26             27.41            2.18

984.25           -7.19             27.41            2.37

1148.29           -6.71             27.40            2.33

1312.33           -6.55             27.40            2.20

1476.37           -6.71             27.40            2.57

1640.42           -6.84             27.40            2.53

40,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

0.00           -5.34             14.87            0.00

164.04           -5.44             18.46            0.78

328.08           -5.25             23.42            1.55

492.12           -5.93             26.63            2.14

656.17           -5.64             27.41            2.04

820.21           -6.26             27.41            2.18

984.25           -7.19             27.41            2.37

1148.29           -6.71             27.40            2.33

1312.33           -6.55             27.40            2.20

1476.37           -6.71             27.40            2.57

1640.42           -6.84             27.40            2.53

Wind Field 9

Dryden Turbulence Data

Altitude       Rms Intensities             Scale Lengths

(feet)           (Kts)                      (feet)

Long       Lat     Vert     Long      Lat     Vert

20.00    3.40      2.70     2.34   105.70    49.70    10.40

100.00    4.05      3.46     3.53   216.70   134.20    53.00

200.00    4.43      3.95     4.35   306.50   213.50   106.00

400.00    4.85      4.50     5.36   433.50   339.60   212.00

600.00    5.11      4.86     6.05   530.90   445.60   318.00

1500.00    5.74      5.78     7.94   840.90   824.50   795.30

Wind Field 10

40,000.0 feet beyond the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           -9.70              3.00            0.00

150.00          -12.20              7.50           -0.20

250.00          -12.90              8.00           -0.70

350.00          -16.40              9.00            2.20

450.00          -13.60             10.00           14.70

550.00          -19.50             11.00           -9.70

650.00           -6.30             12.00           -9.70

800.00            2.60             12.80           -6.50

1200.00            3.20             11.20           -3.30

1500.00            2.40             10.00           -3.40

At the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           -9.70              3.00            0.00

150.00          -12.20              7.50           -0.20

250.00          -12.90              8.00           -0.70

350.00          -16.40              9.00            2.20

450.00          -13.60             10.00           14.70

550.00          -19.50             11.00           -9.70

650.00           -6.30             12.00           -9.70

800.00            2.60             12.80           -6.50

1200.00            3.20             11.20           -3.30

1500.00            2.40             10.00           -3.40

2,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           -8.30              3.00            0.00

150.00          -13.10              7.50           -0.40

250.00          -14.20              8.00           -2.50

350.00          -16.60              9.00           -1.10

450.00          -19.50             10.00           -2.50

550.00          -18.80             11.00           -8.00

650.00          -16.30             12.00          -12.90

800.00            1.60             12.80           -7.70

1200.00            4.10             11.20           -7.40

1500.00            4.90             10.00           -6.10

4,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           -6.00              3.00            0.00

150.00          -12.70              7.50            0.00

250.00          -15.00              8.00           -3.60

350.00          -13.60              9.00           -6.00

450.00          -18.40             10.00            0.00

550.00          -21.20             11.00            0.00

650.00          -15.90             12.00          -11.40

800.00           -1.90             12.80          -10.90

1200.00            4.50             11.20           -8.40

1500.00            4.80             10.00           -9.00

6,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00            1.70              3.00            0.00

150.00           -2.70              7.50           -0.90

250.00           -3.20              8.00           -6.10

350.00           -3.20              9.00          -17.90

450.00           -3.90             10.00          -27.70

550.00            0.20             11.00          -30.60

650.00            3.10             12.00          -27.00

800.00            7.20             12.80          -16.60

1200.00            7.20             11.20          -14.80

1500.00            7.20             10.00          -14.80

8,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           12.70              3.00            0.00

150.00           17.10              7.50           -0.90

250.00           17.60              8.00           -6.10

350.00           17.60              9.00          -17.90

450.00           18.30             10.00          -27.70

550.00           14.20             11.00          -30.60

650.00           11.30             12.00          -27.70

800.00            7.20             12.80          -16.60

1200.00            7.20             11.20          -14.80

1500.00            7.20             10.00          -14.80

9,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           19.10              3.00            0.00

150.00           24.70              7.50           -0.70

250.00           26.00              8.00           -6.10

350.00           28.00              9.00          -10.30

450.00           26.00             10.00          -12.30

550.00           24.60             11.00          -24.00

650.00           13.40             12.00          -24.60

800.00           12.80             12.80          -13.40

1200.00            9.60             11.20          -14.00

1500.00            8.70             10.00          -12.30

10,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           20.40              3.00            0.00

150.00           27.10              7.50            0.00

250.00           29.40              8.00           -3.60

350.00           28.00              9.00           -6.00

450.00           32.80             10.00            0.00

550.00           35.60             11.00            0.00

650.00           30.30             12.00          -11.40

800.00           16.30             12.80          -10.90

1200.00            9.90             11.20           -8.40

1500.00            9.60             10.00           -9.00

11,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           21.70              3.00            0.00

150.00           28.00              7.50           -0.40

250.00           28.70              8.00           -2.60

350.00           30.30              9.00           -4.10

450.00           36.20             10.00            2.30

550.00           35.60             11.00            0.00

650.00           32.60             12.00           11.90

800.00           15.00             12.80            9.70

1200.00           10.40             11.20            8.90

1500.00            9.60             10.00            7.00

12,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           22.70              3.00            0.00

150.00           27.50              7.50           -0.40

250.00           28.60              8.00           -2.50

350.00           31.00              9.00           -1.10

450.00           33.80             10.00            2.50

550.00           33.20             11.00           -8.00

650.00           30.70             12.00          -12.90

800.00           12.80             12.80           -7.70

1200.00           10.30             11.20           -7.40

1500.00            9.50             10.00           -6.10

13,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           24.00              3.00            0.00

150.00           27.30              7.50           -0.20

250.00           28.00              8.00           -0.90

350.00           31.00              9.00            0.00

450.00           32.70             10.00            6.00

550.00           32.50             11.00          -12.90

650.00           28.00             12.00          -12.90

800.00           12.10             12.80           -8.10

1200.00           10.50             11.20           -5.60

1500.00           13.30             10.00           -4.40

14,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           24.10              3.00            0.00

150.00           26.60              7.50           -0.20

250.00           27.30              8.00           -0.70

350.00           30.80              9.00            2.20

450.00           28.00             10.00           14.70

550.00           33.90             11.00           -9.70

650.00           20.70             12.00           -9.70

800.00           11.80             12.80           -6.50

1200.00           11.20             11.20           -3.30

1500.00           12.00             10.00           -3.40

16,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           24.30              3.00            0.00

150.00           26.50              7.50            0.00

250.00           27.20              8.00           -0.20

350.00           30.40              9.00            2.20

450.00           33.80             10.00           -2.50

550.00           25.00             11.00           -4.40

650.00           22.80             12.00           -3.00

800.00           13.80             12.80           -1.90

1200.00           13.30             11.20           -1.50

1500.00           13.00             10.00           -0.90

40,000.0 feet in front of the GPIP

Mean Winds (Knots)

Altitude (feet)   Longitudinal        Lateral        Vertical

20.00           16.80              3.00            0.00

150.00           26.30              7.50            0.00

250.00           27.30              8.00            0.00

350.00           30.10              9.00            0.00

450.00           33.90             10.00            0.00

550.00           26.20             11.00            0.00

650.00           23.00             12.00            0.00

800.00           14.20             12.80            0.00

1200.00           13.70             11.20            0.00

1500.00           13.20             10.00            0.00

Wind Field 10

Dryden Turbulence Data

Altitude       Rms Intensities             Scale Lengths

(feet)           (Kts)                      (feet)

Long       Lat     Vert     Long      Lat     Vert

20.00    3.40      2.70     2.34   105.70    49.70    10.40

100.00    4.05      3.46     3.53   216.70   134.20    53.00

200.00    4.43      3.95     4.35   306.50   213.50   106.00

400.00    4.85      4.50     5.36   433.50   339.60   212.00

600.00    5.11      4.86     6.05   530.90   445.60   318.00

1500.00    5.74      5.78     7.94   840.90   824.50   795.30