Publication–National Ocean Service–U.S. Coast Pilot 7, Pacific Coast: California, Oregon, Washington, Hawaii, and Pacific Islands, 2009 (41st) Edition. Change No. 07.

Coast Pilot 7 41st 2009								Corrections

Page 275-Paragraph 146, lines 1-6; read:

In July 2008, the controlling depths were 15 feet in the entrance (except for lesser depths along the S breakwater, thence 11 feet in the channel that leads WNW to the W basin (except for shoaling to bare in the SW half of the channel opposite Daybeacon 14); the channel to the E basin had a depth of 10 feet. The harbor …

(DD 12171)

Page 295-Paragraph 431, lines 3-6; read:

is just N of the entrance basin. In July-September 2008, the controlling depths were 12 feet in the entrance channel (except for shoaling to 2 feet along the right edge of the channel near Light 4), thence depths of 13 to 16 feet were available in the entrance basin and depths of 8 to 9 feet were available in the inner basin.

(DD 12461; DD 12141)

Page 340-Paragraph 120: Delete.

(CL 82/09; CL 1374/06)

Page 346-Paragraph 188, line 5; read:

equipped with a racon.

Blossom Rock, covered 40 feet and marked on the W side by a lighted bell buoy, is about 1 mile SE of Alcatraz Island. Another rock, covered 43 feet, is 0.3 mile S of Blossom Rock.

(NOS 18650; DD 12928; CL 17/09)

Page 349-Paragraph 237, lines 3-7; read:

depth of 35 feet is off the entrance. Two bascule bridges, the Illinois Street Bridge and the 3rd Street Bridge, cross the creek about 0.6 mile above the mouth; both have clearances of 4 feet. (See 117.59 and 117.163, chapter 2, for drawbridge regulations.) The bridgetender at the 3rd Street Bridge monitors VHF-FM channel 16 and uses …

(CL 1381/08)

Page 349-Paragraph 244, line 8; read:

docks on the Oakland side.

Ferries

There are several passenger ferries that operate in and around San Francisco Bay with a heavy concentration in the waters surrounding the Ferry building, the terminus for many of the ferry routes. Mariners are cautioned when transiting these waters around the Ferry building as ferries will be maneuvering and loading/unloading passengers. Mariners are further cautioned that ferries operating in San Francisco Bay may deviate from their routes due to inclement weather, traffic conditions, navigational hazards, or other emergency conditions.

The San Francisco Harbor Safety Committee, in conjunction with the Coast Guard, has established a Ferry Traffic Routing Protocol for: the area surrounding the Ferry building terminal along the waterfront of San Francisco, the waters of Central San Francisco Bay, and the waters of San Pablo Bay. The protocol is intended to increase safety in the area by reducing traffic conflicts. Ferryboat operators and other mariners should be aware of these safety measures and adhere to the procedures set forth in the protocol. For additional information, see the San Francisco Vessel Traffic Service website http://www.uscg.mil/d11/vtssf.

(CL 82/09; CL 1374/06)

Page 491-Paragraph 162, line 21; read:

moorage in the basin and can be contacted at 360-417-3440; VHF-FM is not monitored.

(DB 17114)

Page 593-Paragraph 449, lines 3-11; read:

wide. The entrance is through a break in the reef from the SE. A privately dredged channel continues from the harbor to a three-fingered boat lagoon called Pukoo Lagoon. The entrance to the lagoon is a 60-yard opening through a rock seawall. A depth of 12 feet can be carried across the harbor entrance to the lagoon channel. The lagoon channel has a depth of 6 feet with a depth of 4 feet inside. The lagoon offers excellent protection …

(BP 192728; NOS 19353)

Page 594-Paragraph 452, lines 5-11; read:

into the reef. The entrance to the harbor is through a break in an outer reef. The outer reef has general depths of 1 to 6 feet and the entrance through the break has a least depth of 11 feet. A lighted buoy is off the entrance. The coral reef marking the limits of deep …

(BP 192727; NOS 19353)

Page 595-Paragraph 466, read:

An abandoned barge harbor (Lono Harbor) is at Haleolono Point. The entrance is marked by a 345° private unlighted range. Two breakwaters provide protection for the harbor. Local knowledge is advisable for entering.

(NOS 19353; CL 562/02; NM 06/04)