Target Generation Facility (TGF)

ATO-P

Office of Integrated Engineering Services

Laboratory Division

Simulation

Project Summary

Fiscal Year 2005

Dan Warburton

2005-10-25

Table of Contents

Table of Contents	2

TGF Project Summary FY 2005	2

Executive Summary	2

Section 1 – Simulation Projects Supported	3

1.1 Simulation:  Required Navigational Performance  (HFL)	3

1.2 Simulation: Tracon Controller Weather Information Needs - WIDS (HFL)	3

1.3 Simulation: TMA_2 (HFL)	4

1.4 Simulation: Domestic Reduced Vertical Separation Minima (DRVSM)	4

1.5 Simulation: STARS - FMA	5

1.6 Simulation: STARS – Standard Terminal Automation Replacement System	6

1.7 Simulation: SATS (Small Airport Transportation System)	6

1.8 Simulation: Free Flight Technology Integration Laboratory (FFTIL)	7

Section 2 – Technical Summary	8

2.1 QVPD Development	8

2.2 Linux Based Display Drivers	8

2.3 Visual Simulation Development	8

2.4 Voice over IP system for AFTIL Lab.	8

2.5 TGF Ground Simulation	8

2.6 Pilot workstation Hardware refresh	8

2.6 Decommission Router Five	8

TGF Acronyms and Abbreviations	10

TGF Airports and Centers	12

# TGF Project Summary FY 2005

## Executive Summary

The Target Generation Facility (TGF) completed another successful simulation year. All simulations were provided on-time and met or exceeded customer expectations.  In addition to completing these simulations many enhancements were added to the Target Generation Facility's aircraft dynamics engine, simulation pilot workstation and hardware

Infrastructure.

## Section 1 – Simulation Projects Supported

This section summarizes the simulation efforts supported by the Target Generation Facility during the fiscal year.

### 1.1 Simulation:  Required Navigational Performance  (HFL)

Simulation Dates:	October 2003 – December 2004,

Program Office:	ATP 500

Contacts:	Jeff Williams, ATP 500

Simulation Summary

The purpose of this simulation was to identify the possibility of utilizing the ASR9 display to identify blunder aircraft during a simultaneous instrument approach operation.

The airspace adapted for the simulation was Northern California TraCon, Sector B (San Francisco Arrival).

The airspace simulated in this project was Northern California TraCon, Sector B (San Francisco Arrival).

### 1.2 Simulation: Tracon Controller Weather Information Needs - WIDS (HFL)

Simulation Dates:	December 2003 – October, 2004

Program Office:	AAR100

Contacts:		Dino Piccione

Simulation Summary

This simulation was run to identify controller needs for displayed weather information.

The airspace used in the project was the HFL’s Genera Tracon.  TGF adapted the sim-pilot workstation displays to display weather in conjunction with simulation events.

### 1.3 Simulation: TMA_2 (HFL)

Simulation Dates:	August 2004 – November 2004

Program Office:	Air Traffic Organization – En Route (ATO-E)

Contacts: 		Rob Williams AOZ 500

Simulation Summary

This simulation was run to evaluate location and format of TMA data on the ATC display.  The airspace used in this project was the HFL’s Genera Center, Sector 08.

### 1.4 Simulation: Domestic Reduced Vertical Separation Minima (DRVSM)

Simulation Dates:	February 9, 2004 – March 25, 2004

Program Office:	ATP-6 Domestic Reduced Vertical Separation Minima (DRVSM)

Contacts:		Steve Creamer ATP-6 Domestic Reduced Separation Minima

Jerry Hadley ACB-330

Simulation Summary

This simulation of the Indianapolis Center is a continuation of the DRVSM 2 study.  The study continues to focus on the FL290 – FL410 altitude band to compare the various approaches to implementation.  A further goal for this study was to determine the effect of non-RVSM equipped aircraft.  This en route simulation involved four sectors of Indianapolis Center: 87, 88, 97, and 98. The DRVSM procedure is scheduled for activation in late 2004 to early 2005 time frame and TGF provides an excellent environment in which the controller’s workload can be evaluated.

### 1.5 Simulation: STARS - FMA

Simulation Dates:	March 23-25th, 2004 (Interim)

March 29 – April, 1 (PHL)

Program Office:	STARS ATO-T

Contacts:	Leroy H. Harnett ATO-T (ATB232B)

FMA AT Test Lead

Simulation Summary

This simulation required the adaptation of the Denver TRACON and the re-use of the PHL TRACON originally adapted for the Full Service 1 build of the STARS system.

The Interim simulation was run in the Denver TRACON and the native simulation was run in the PHL TRACON.

The PHL scenarios made use of eight sectors:

Sector			Frequency	Sector			Frequency

SA			126.600	Y			123.800

FV			125.400	SD			119.750

NA			128.400	ND			124.350

W			127.350	PHL Tower		118.500

The scenarios ranged in size from 39 to 179 flight plans. Each one was designed to exercise a specific aspect of the STARS FS1 system. These scenarios were all designed to last approximately 1 hour. The simulations required 11 – 14 simpilots to fly the 8 sectors. Each simulation had the PHL ASR9 radar configured.

The Denver simulation made use of 10 sectors with working names as follows:

Sector			Frequency	Sector			Frequency

Final Radar One	123.850	Local Control One	124.300

Final Radar Two	120.800	Local Control Two	133.300

Final Radar Three	125.750	Local Control Three	132.350

Arrival Radar One	120.350	Local Control Four	145.300

Arrival Radar Two	119.300

Arrival Radar Three	124.950

There were two scenarios.  One North flow and one South flow.  The South flow scenario contained 123 flights and was designed to last 1 hour, the North flow scenario also was designed to run 1 hour but had 63 flights total.

### 1.6 Simulation: STARS – Standard Terminal Automation Replacement System

Simulation Dates	August 12, 2004

Program Office:	ATO-T STARS

Contacts:	David Cognata	ATO-T Sr. Air Traffic Control Specialist

609-485-9198

Gary Miller	ATO-T STARS

609-485-7175

Ed Gaguski	ATO-T STARS

Simulation Summary

This simulation of PHL TRACON was performed to exercise the FS2 LCM Release 8.

It will re-use all of the previously built scenarios

### 1.7 Simulation: SATS (Small Airport Transportation System)

Simulation Dates:	October, November,December, 2004

Program Office:	NASA Langley Research Center SATS-HVO

(Higher Volume Operations)

Contacts:	Brian Baxley	Level 3 Project Manager

SATS HVO

(757) 864-7317

Simulation Summary

This simulation is a joint project between NASA Langley Research Center and the FAA.

The project’s purpose is to evaluate controller workload and procedures for an SCA (Self-Controlled Area) around a non-towered airport, as part of the SATS HVO program.

The TGF integrated NASA’s AMM (Airport Management Module) software into the simulator providing the same sequencing messages to the simulated flights as they would in the field.  Both types of air traffic environment (Center and TRACON) were studied, specifically, Washington Center ZDC – Danville Airport and PHL TRACON – Chester County Airport 40N.  A third study utilizing NASA’s cockpit simulators was conducted re-using the ZDC – Danville airport scenarios.

### 1.8 Simulation: Free Flight Technology Integration Laboratory (FFTIL)

TGF system use 2005

The Free Flight Technology Integration Laboratory (FFTIL) conducts simulations to test various builds and adaptations associated with the Center-TRACON Automation System (CTAS).  This testing required the use of TGF’s RADAR & Interfacility emulators.  This activity included but not restricted to the following:

- Non-interference testing with ARTS IIIE & A Systems

- Functionality testing of new CTAS builds & adaptations using both ARTS3E ARTS3A and STARS Terminal systems.

- Integration and functionality testing using the Host with STARS & the Host with ARTS.

- Field problem resolution in support of AOS.

All of these various activities were completed without delay due to the stability, dependability, and availability, of the TGF radar systems.

## Section 2 – Technical Summary

# This section summarizes the technical achievements of the TGF during the fiscal year.

### 2.1 QVPD Development

The venerable xpvd was re-written in C++ /QT and deployed for general use in TGF. This software enables TGF to display targets and routes on internal displays and pilot

Workstations.

### 2.2 Linux Based Display Drivers

TGF’s six BARCO 2k x 2k displays are now driven using Linux workstations replacing older Sun systems.

### 2.3 Visual Simulation Development

The initial implementation of a Visual Simulation capability was developed using open source products CIGI/OpenSceneGraph and MPV along with in-house developed software.

### 2.4 Voice over IP system for AFTIL Lab.

As part of the TGF / AFTIL integration capability a VIOP system based on TELEX and cisco equipment was developed and deployed to the AFTIL Laboratory. This enables

Voice communications in the AFTIL lab (required for real-time simulations).

## 2.5 TGF Ground Simulation

Initial implementations of a ground simulation capability were developed.

## 2.6 Pilot workstation Hardware refresh

The second half of the pilot lab displays were refreshed to Viewsonic VX2000 LCD displays. New graphic cards are planned for FY06.

## 2.6 Decommission Router Five

TGF reduced network router recurring maintenance costs by decommissioning TGF's router5 at a rate 12k/year.  About 12 networks routed through router5 were moved to the TC's backbone routers (p1 and P2) via fiber optic cable changes.  TGF Received a 6.1k purchasing credit from Cisco Systems for trading in router5 against new network equipment to support the RCS, Bytex and VoIP infrastructure inprovements.

# TGF Acronyms and Abbreviations

ADAR	ARTS Data Acquisition & Router

AGW	ARTS GateWay

ARTS	Automated Radar Terminal System

ATCT	Air Traffic Control Tower

CAS	Controller Awareness Study

CTAS	Center TRACON Automation System

CHI	Computer Human Interface

CPDLS	Controller Pilot Data Link Communications

DFS	Deutsche Flugsicherung (German Simulation)

DIS	Distributed Interactive Simulation

DRVSM	Domestic Reduced Vertical Separation Minimum

DSR	Display System Replacement

EDC	Early Display Configuration

ETVS	Enhanced Terminal Voice Switch

FAST	Final Approach Spacing Tool

FFP	Free Flight Phase

FS1, 2/2+	Full Service 1, 2/2+

GAO	Government Accounting Office

GOERS	GPS Outage En route Simulation

GPS	Global Positioning System

HAD	High Altitude Demonstration

HAT	High Altitude Test

HFL	Human Factors Laboratory

HLA	High Level Architecture

IIF	Integration and Interoperability Facility

LAAEP	LA Arrival Enhancement Project

McTMA	Multi-Center Traffic Management Advisor

NAS	National Airspace System

NATCA	National Air Traffic Controllers Association

PARR	Problem Analysis Resolution and Ranking

PAS	Pseudo Aircraft System

PDU	Protocol Data Units

PTR	Program Trouble Reports

RDHFL	Research Development and Human Factors Laboratory

RNAV	Area Navigation

RVSM	Reduced Vertical Separation Minimum

STARS	Stand Alone Terminal ARTS Replacement System

TATCA	Terminal Air Traffic Control Automation

TFM	Traffic Flow Management

TGF	Target Generation Facility

TMA	Traffic Management Advisor

TRACON	Terminal Radar Approach CONtrol

URET	User Request Evaluation Tool

WJHTC	William J. Hughes Technical Center

XPVD	X-windows Planned View Display

# TGF Airports and Centers

ADW	Andrews Air Force Base

DCA	Ronald Reagan International Airport

EWR	Newark International Airport

Genera	Generic airspace generated for HFL studies

JFK	John F. Kennedy International Airport

PHL	Philadelphia International Airport

ZDC	Washington Center

ZID	Indianapolis Center

ZJX	Jacksonville Center

ZNY	New York Center

ZOB	Cleveland Center