DOOR HARDWARE SCHEDULE

NOTE:    	FOR ALL DOORS COMPLY WITH SANDIA STANDARD SPECIFICATIONS FOR FINISH HARDWARE.  PROVIDE EXCEPTIONS OR ADDITIONS TO SANDIA STANDARDS AS NOTED IN DOOR HARDWARE SUPPLEMENTAL NOTES ON DOOR SCHEDULE FOR SPECIFIC DOORS.

DOOR HARDWARE SUPPLEMENTAL NOTES (SEE DOOR SCHEDULE)

1.   	SUBSTITUTE LATCHSET IN LIEU OF STANDARD PUSH-PULL DEVICE.

2.   	ADD CLOSER TO HARDWARE SPECIFIED FOR THIS DOOR.

3.   	ADD LOCKSET TO HARDWARE SPECIFIED FOR THIS DOOR.

4.   	OVERHEAD COILING DOOR - MANUFACTURER'S STANDARD HARDWARE FOR MANUAL OPERATION.

5.   	ADD ALARM TO HARDWARE SPECIFIED FOR THIS DOOR.  FOR DOUBLE DOORS, ALARM BOTH LEAVES. (SEE ELECTRICAL INTRUSION ALARM DRAWINGS.)

6.   	ADD PANIC DEVICE TO HARDWARE SPECIFIED FOR THIS DOOR.

7.   	ADD COMBINATION LOCK TO HARDWARE SPECIFIED FOR THIS DOOR.

8.   	THIS DOOR IS ACTIVE ONLY FROM THE INSIDE OF THE ROOM.  OUTSIDE FACE OF DOOR WILL BE BLANK.

9.   	ADD HIRSCH PAD TO HARDWARE SPECIFIED FOR THIS DOOR.  (SEE ELECTRICAL ACCESS CONTROL DRAWINGS.)

10.  	ADD ELECTRIC STRIKE AS SPECIFIED ON ACCESS CONTROL EQUIPMENT SCHEDULE TO HARDWARE SPECIFIED FOR THIS DOOR. (SEE ELECTRICAL ACCESS CONTROL DRAWINGS.)

11.  	ADD ELECTRIC HINGE FOLGER ADAMS MODEL NO. 4-1/2EH TO HARDWARE SPECIFIED FOR THIS DOOR.  (SEE ELECTRICAL ACCESS CONTROL DRAWINGS.)

12.  	ADD ELECTRIC PANIC DEVICE SPECIFIED ON ACCESS CONTROL EQUIPMENT SCHEDULE TO HARDWARE SPECIFIED FOR ONE LEAF OF THIS DOOR (SEE ELECTRICAL ACCESS CONTROL DRAWINGS).

13.  	ADD PUSH-PULL DEVICE TO HARDWARE SPECIFIED FOR THIS DOOR.  FOR DOUBLE DOORS, ADD A DEVICE TO EACH LEAF.

14.  	ADD LOCK ASTRAGAL TO HARDWARE SPECIFIED FOR THIS DOOR.

15.  	STOREFRONT DOORS ON SOUTH AND NORTH ENTRIES F01 AND F17:

STOREFRONT MANUFACTURER TO PROVIDE THE FOLLOWING HARDWARE FOR THE STOREFRONT DOORS:

CLOSERS

HINGES

WEATHERSTRIPPING

HARDWARE SUPPLIER TO COORDINATE WITH STOREFRONT MANUFACTURER AND PROVIDE THE FOLLOWING ADDITIONAL HARDWARE FOR THESE DOORS.

ALARMS - ALARM BOTH LEAVES (SEE ELECTRICAL INTRUSION ALARM DRAWINGS).

HIRSCH PADS - SEE ELECTRICAL ACCESS CONTROL DRAWINGS.

ELECTRIC HINGE, FOLGER ADAMS MODEL NO. 4-1/2EH (SEE ELECTRICAL ACCESS CONTROL DRAWINGS).

ONE ELECTRIC PANIC DEVICE AS SPECIFIED ON ACCESS CONTROL EQUIPMENT SCHEDULE FOR ONE LEAF ONLY (SEE ELECTRIC ACCESS CONTROL DRAWINGS).

ONE NON-ELECTRIC PANIC DEVICE TO MATCH THE ELECTRIC PANIC DEVICE.

16.  	ADD THRESHOLD TO THIS DOOR.

17.  	ADD AUTOMATIC DOOR BOTTOM & WEATHERSTRIPPING TO THIS DOOR.