SPECIAL SPECIFICATION

SECTION 10500

METAL LOCKERS

Page

PART 1 - GENERAL

1.01	Related Documents ..............................................................................	2

1.02	Summary .........................................................................................	2

1.03	Submittals ........................................................................................	2

1.04	Quality Assurance ...............................................................................	3

1.05	Job Conditions ...................................................................................	3

PART 2 - PRODUCTS

2.01	Manufacturers ....................................................................................	3

2.02	Materials ..........................................................................................	3

2.03	Fabrication, General ............................................................................	4

2.04	Wardrobe Lockers (12-Inch Wide X 18-Inch Deep) ........................................	4

2.05	Locker Accessories ..............................................................................	5

PART 3 - EXECUTION

3.01	Installation .......................................................................................	5

3.02	Adjust and Clean ................................................................................	6

SPECIAL SPECIFICATION

SECTION 10500

METAL LOCKERS

PART 1 - GENERAL

1.01	RELATED DOCUMENTS

A.	Drawings and general provisions of Contract, including General and Supplementary Conditions and Division 1 Specification Sections, apply to this Section.

1.02	SUMMARY

A.	This Section includes metal lockers and related equipment as indicated on drawings.

B.	Types of products in this section include the following:

1.	Standard wardrobe lockers.

a.	Single-tier.

b.	Double-tier.

1.03	SUBMITTALS

A.	Submit the following in accordance with Conditions of Contract and Division Specification sections.

B.	Product data and installation instructions for metal locker units.

C.	Color Samples on squares of same metal to be used for fabrication of lockers.

D.	Shop Drawings that show metal lockers in dimensioned relation to adjacent surfaces.  Show lockers in detail, method of installation, fillers, trim, base, and accessories.  Include locker numbering sequence information.

1.04	QUALITY ASSURANCE

A.	Uniformity:  Provide metal lockers that are standard products of single manufacturer, with interchangeable like parts.  Include necessary mounting accessories, fittings, and fastenings.

B.	All materials used shall not contain asbestos fibers or lead.

1.05	JOB CONDITIONS

A.	Do not deliver metal lockers until building is enclosed and ready for locker installation.  Protect from damage during delivery, handling, storage, and installation.

PART 2 - PRODUCTS

2.01	MANUFACTURERS

A.	Manufacturer:  Subject to compliance with requirements, provide products of one of the following:

De Bourgh Manufacturing Co.

The Interior Steel Equipment Co.

List Industries Inc.

Lyon Metal Products

Medart Inc.

Penco Products Inc.

Republic Storage Systems

2.02	MATERIALS

A.	Sheet Steel:  Mild cold-rolled and leveled furniture steel, free from buckle, scale, and surface imperfections.

B.	Fasteners:  Cadmium, zinc, or nickel-plated steel; exposed bolt heads, slotless type; self-locking nuts or lock washers for nuts on moving parts.

C.	Equipment:  Hooks and hang rods of cadmium-plated or zinc-plated steel.

2.03	FABRICATION, GENERAL

A.	Construction:  Fabricate lockers square, rigid, and without warp, with metal faces flat and free of dents or distortion.  Make exposed metal edges safe to touch.  Weld frame members together to form rigid, one-piece structure.  Weld, bolt, or rivet other joints and connections.  Grind exposed welds flush.  Do not expose bolts or rivet heads on fronts of locker doors or frames.

B.	Frames:  Fabricate of 16-gage channels or 12-gage angles, minimum, with continuous stop/strike formed on vertical members.

C.	Finishing:  Chemically pretreat metal with degreasing and phosphatizing process.  Apply baked-on enamel finish to all surfaces, exposed and concealed, except plates and nonferrous metal.

1.	Color:  Provide locker units in color(s) selected by Sandia Delegated Representative (SDR) from manufacturer's standards.  Concealed parts may be manufacturer's standard neutral color.

2.04	WARDROBE LOCKERS (12-INCH WIDE X 18-INCH DEEP)

A.	Body:  Fabricate back and sides of minimum 24-gage steel, with double-flanged connections extending full height.  Form top and bottom of not less than 24-gage steel, with flanged edges.

1.	Provide 24-gage steel sheet shelf.

2.	Form exposed ends of lockers of minimum 16-gage steel.

B.	Door:  One-piece, minimum 18-gage sheet steel, flanged at all edges, constructed to prevent springing when opening or closing.  Fabricate to swing 180 degrees.

1.	Ventilation:  Provide stamped, louvered vents in door face, as follows:

a.	Single-Tier Lockers:  Not fewer than 6 louver openings top and bottom.

b.	Double-Tier Lockers:  Not fewer than 3 louver openings top and bottom.

2.	Hinges:  Steel, full-loop, 5-knuckle, tight pin.  Weld to inside of frame and secure to door with not less than 2 factory-installed fasteners that are completely concealed and tamperproof when door is closed.

a.	Provide at least 3 hinges for each door over 42 inches high; at least 2 hinges for each door 42 inches high or less.

C.	Projecting Handle and Latch:  Positive automatic, prelocking, pry-resistant latch and pull with rubber silencers; chromium-plated, heavy-duty, vandalproof lift-up handle, containing strike and eye for padlock; and with latching action as follows:

1.	Single-Tier Lockers:  Not less than 3-point latching.

2.	Double-Tier Lockers:  Not less than 2-point latching.

2.05	LOCKER ACCESSORIES

A.	Equipment:  Furnish each locker with the following items, unless otherwise shown:

1.	Single-Tier and Double-Tier Units:  Shelf, hang rod, and not less than 2 single-prong wall hooks.

B.	Number Plates:  Manufacturer's standard etched, embossed, or stamped, nonferrous metal number plates with numerals not less than 3/8 inches high.  Number lockers in sequence as directed by Sandia Delegated Representative (SDR).  Attach plates to each locker door, near top, centered, with at least 2 fasteners of same finish as number plate.

C.	Continuous Sloping Tops:  Not fewer than 20-gage sheet steel, approximately 25 degrees pitch, in lengths as long as practicable but not less than 4 lockers.  Provide closures at ends.  Finish to match lockers.

D.	Separators:  Provide horizontal dividers of not less than 16-gage sheet steel between doors of multiple-tier lockers to ensure rigidity.

E.	Filler Panels:  Provide filler panels of not less than 18-gage steel sheet, factory fabricated and finished to match locker units.

PART 3 - EXECUTION

3.01	INSTALLATION

A.	Install metal lockers at locations shown in accordance with manufacturer's instructions for plumb, level, rigid, and flush installation.

B.	Space fastenings about 48 inches o.c., unless otherwise recommended by manufacturer, and apply through backup reinforcing plates where necessary to avoid metal distortion, using concealed fasteners.

C.	Install trim, sloping top units, and metal filler panels and end panels, using concealed fasteners.  Provide flush, hairline joints against adjacent surfaces.

3.02	ADJUST AND CLEAN

A.	Adjust doors and latches to operate easily without binding.  Verify that integral locking devices are operating properly.

B.	Touch up marred finishes, but replace units that cannot be restored to factory-finished appearance.  Use only materials and procedures recommended or furnished by locker manufacturer.

END OF SECTION