# STEREO/HET Housekeeping

Version 1.1

# Raw Data to Engineering Units Conversion Algorithms

All offsets noted in this document are relative to the packet definitions specified below which are produced by the HET flight software and received by SEP Central.  Please note that the offsets defined in the HET housekeeping packet (ApId 598) will need to be adjusted (add 26 to each offset since HET HK starts in byte 37) to extract the correct housekeeping bytes from the SEP housekeeping packet (ApId 577).

# Status and Singles Rate Packet (ApID: 591 (dec)  24f (hex)):

| Offset | Bytes | B-packet contents |
| --- | --- | --- |
| 0 | 11 | CCSDS header |
| 11 | 1 | HET mode byte |
| 12 | 2 | TBD |
| 14 | 2 | Major frame number |
| 16 | 28 | 14 Single detector rates |
| 44 | 2 | Last command number |
| 46 | 4 | Last command ID |
| 50 | 14 | Offsets for current selected channels (h1i logain=0, h1i logain=1, h1o logain=0, h1o logain=1, h2 logain=0, h2 logain=1, h3 logain=0, h3 logain=1... h6 logain=0, h6 logain=1) |
| * 64 | 7 | h1i chip=0 addr, h1o chip=0 addr, h2 chip=1, addr, h2 chip chip =1 addr..h6 chip=1 addr |
| 71 | 3 | Status Bytes (TBD) |
| 74 | 100 | 50 sample H1-only PHs |
| 174 | 96 | STIM PH events |
| 270 | 1 | N stimulus events in packet |
| 271 | 1 | Checksum |

* offset 64 through offset 70 = H1i, H1o, H2, H3, H4, H5, and H6 channel index numbers (range 0 -31).

# Housekeeping Packet (ApID: 598 (dec)  256 (hex)):

| Offset | Bytes | G-packet contents |
| --- | --- | --- |
| 0 | 11 | CCSDS header |
| 11 | 1 | ADC Temp 1 |
| 12 | 1 | ADC Temp 2 |
| 13 | 1 | PHASIC 0 PH channel ID |
| 14 | 1 | PHASIC 0 ADC Preamp |
| 15 | 2 | PHASIC 0 high gain threshold |
| 17 | 2 | PHASIC 0 low gain threshold |
| 19 | 2 | PHASIC 0 leakage current DAC setting |
| 21 | 1 | PHASIC 1 PH channel ID |
| 22 | 1 | PHASIC 1 ADC Preamp |
| 23 | 2 | PHASIC 1 high gain threshold |
| 25 | 2 | PHASIC 1 low gain threshold |
| 27 | 2 | PHASIC 1 leakage current DAC setting |
| 29 | 2 | Error Flags (16 bits) |
| 31 | 2 | Software version ID (16 bits) |
| 23 | 2 | N invalid token |
| 35 | 2 | N invalid trigger |
| 37 | 2 | N lost raw events |
| 39 | 2 | Major frame number |
| 41 | 3 | Table checksum |
| 44 | 1 | 24-bit DAC value, bits 0:7 (PHASIC 0 DAC) |
| 45 | 1 | 24-bit DAC value, bits 8:15 (PHASIC 1 DAC) |
| 46 | 1 | 24-bit DAC value, bits 16:23 (un:4, mux:2, rng1:1, rng0:1) |
| 47 | 5 | Available (TBD) |
| 52 | 219 | Not available for use |
| 271 | 1 | Checksum |

Temperature 1 conversion (degrees C):

39.4 * tan (.0085 * (offset 11, ApId 598) – 116)) + 10

Temperature 2 conversion (degrees C):

39.4 * tan (.0085 * (offset 12, ApId 598) – 116)) + 10

Conversion for PHASIC 0 ADC Preamp (offset 14, ApId 598) and

PHASIC 1 ADC Preamp (offset 22, ApId 598):

Preamp0 = 0.01953 * (255 – (offset 14, ApId 598))

Preamp1 = 0.01953 * (255 – (offset 22, ApId 598))

In order to determine the channel number index (range 0-6) for H1i, H1o, H2, H3, H4, H5 and H6, you need to look at the 2 packets with ApIds 591 and 598 and do a comparison as follows:

H1i (0 channel index number):      (offset 13, ApId 598) =    (offset 64, ApId 591)

H1o (1 channel index number):     (offset 13, ApId 598) =     (offset 65, ApId 591)

H2   (2 channel index number):     (offset 13, ApId 598) = ((offset 66, ApId 591)-16)

H3   (3 channel index number):     (offset 13, ApId 598) = ((offset 67, ApId 591)-16)

H4   (4 channel index number):     (offset 13, ApId 598) = ((offset 68, ApId 591)-16)

H5   (5 channel index number):     (offset 13, ApId 598) = ((offset 69, ApId 591)–16)

H6   (6 channel index number):     (offset 13, ApId 598) = ((offset 70, ApId 591)-16)

Use the following parameters in the formulas to convert the PHASIC 0 leakage current DAC (offset 19, ApId 598) and PHASIC 1 leakage current DAC (offset 27, ApId 598):

K0 = 0.05859

K1 = 0.1172

N0 = 5 LSBs of PHASIC 0 leakage current DAC setting (offset 19, ApId 598)

N1 = 5 MSBs of PHASIC 0 leakage current DAC setting (offset 19, ApId 598)

N2 = 5 LSBs of PHASIC 1 leakage current DAC setting (offset 27, ApId 598)

N3 = 5 MSBs of PHASIC 1 leakage current DAC setting (offset 27, ApId 598)

Conversion for PHASIC 0 leakage current DAC setting (offset 19, ApId 598) for H1i and H1o channel index number (0 or 1 as determined in the comparison formula given above for H1i and H1o):

N1 + (0.03906 * N0) – (K0 * (50 – offset 14, ApId 598))

Conversion for PHASIC 1 leakage current DAC setting (offset 27, ApId 598) for H2 and H6 channel index number (2 or 6, as determined in the comparison formula given above for H2 and H6):

N3 + (0.03906 * N2) – (K0 * (50 – offset 22, ApId 598))

Conversion for PHASIC 1 leakage current DAC setting (offset 27, ApId 598) for H3, H4 and H5 channel index number (3, 4 or 5, as determined in the comparison formula given above for H3, H4 and H5):

N3 + (0.03906 * N2) – (K1 * (50 – offset 22, ApId 598))