Proposed Updates to FMH-3

December, 2007

Input received October 2007

Page	Chapter/Subsection	Change

14	Appendix E		Definition for vbvb should read:

“Absolute value of the vector difference between the maximum wind and

the wind blowing at 1 km below the level of maximum wind, in units

indicated by YY.”

28	Appendix E		Definition for vbvb should read:

“Absolute value of the vector difference between the maximum wind and

the wind blowing at 1 km below the level of maximum wind, in units

indicated by YY.”

25	Appendix E		In section E-II, 2.2 under the heading Regulations: (Continued), include a

paragraph (c) that reads “Refer to Table 5300 on page E-62 for coding of

PnPnhnhnhn.”

Input received from NWS Observing Services Division in 2005

Page	Chapter/Subsection	Change

2-3	Para 2			Remove the entire paragraph.

2-4	2.3.3.1			Remove sentences referring to a hypsometer.

2-7	2.4.1.1			Replace this sentence:

“A Radio Direction Finding (RDF) antenna is designed to track a

radiosonde transmitting in the 1680 MHZ Meteorological Aids band.”

With this sentence:

“A Radio Direction Finding (RDF) antenna is designed to track a

radiosonde transmitting in the 1675-1700 MHZ Meteorological Aids

band.  Because of possible interference with GOES downlinks, sites

should transmit/receive no higher than 1683MHZ.”

2-8	Table 2-2		Eliminate the lines in the table for transponders and VLF and add in a

line for NAVAID GPS 1680 MHZ ± 1 MHZ.

3-1	3.2			Eliminate mention of natural gas.

3-5	3.6			Add this note:  “NWS sites are allowed to release up to 60 min prior to

the 00 and 12 UTC synoptic times to ensure all messages are received

for models run at NCEP.

4-8	4.5.1.4			Eliminate section 4.5.1.4 titled Transponder-Related Problems.

5-3	5.2.2.2			Replace this sentence: “There are three cases where a reascending level

shall not be selected following a descending level:”

With this sentence: “There are two cases where a reascending level

shall not be selected following a descending level:”

Remove this bullet: “If the reascending level coincides with a

standard pressure, the standard level shall be selected because these

levels have higher priority.”

5-5	5.2.3			Replace this sentence: “The data between standard and mandatory

significant levels shall be examined for the additional levels and

included in the coded message in Parts B and D. [E-II.1].”

With this sentence: “The data shall be examined for additional levels

independent of standard and mandatory significant levels and included

in the coded message in Parts B and D. [E-II.1].”

5-5	5.2.3.2			Replace this sentence:  “A temperature level shall be selected if the GDL

exceeds ± 1.0°C for pressures from surface to 100 hPa and ±2.0°C for

pressures from 100 hPa to termination.  A relative humidity level shall

be selected if the GDL exceeds ± 10% for all pressures.”

With this sentence:  “A temperature level shall be selected if the GDL

exceeds ± 0.5°C for pressures from surface to 100 hPa and ±1.0°C for

pressures from 100 hPa to termination.  A relative humidity level shall

be selected if the GDL exceeds ± 5% for all pressures.”

5-9	5.4			Update this section with WMO description of defining tropopause levels.

6-1	6.2			Replace this sentence: “In a pilot balloon observation (pibal), a balloon

which is inflated with either hydrogen or helium to provide a fixed free

lift is tracked visually with an optical theodolite.”

With this sentence:  “In a pilot balloon observation (pibal), a balloon

is inflated with helium to provide a fixed free lift, and is tracked visually

with an optical theodolite.”

6-2	Table 6-1		Update note at bottom of Table 6-1

7-1	7.2.2			Replace each instance of AFOS with AWIPS

7-2	7.3.2			Change organization code from W/OSO242 to W/OCI011.

7-3	7.4			Add 06 and 18 UTC times and get wording for before and after times

8-3	Table 8-1		Update table.

A-1	5.			Remove “Amendment 101-5, 56 FR 65662, 17 Dec 1991.”

And replace it with “26 November 2001.”

A-1	9.			Replace “Vols. 1 & 2, 1995.” with “Vol 1, 1995, and Vol 2, 1998.”

B-1	B.2			Add the following paragraph at the end of section B.2 “For those units

using GPS tracking, determing the location of the antenna to the nearest

meter for height and second for location of baseline and release point.

Resolution should be to the nearest 0.1 second.”

Question for WG/MC:  Does anyone still use radar tracking?

C-1	Table C-1		Update with new NWS info.  Request USAF, USA, and Navy update

their data.

D-1	Entire Appendix	Replace with RWS of August 2000.  (WHAT IS RWS?)

E-58	Table 3845		Change Code Figure 2 to 9.