MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A06858 | In-Flight Anomaly Number -- | Contractor Report Number S-062 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title MISALIGNMENT SRB FITTINGS, EB-1 TO EB-7 |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1 |
| HCRIT -- | Sys_Lvl N | Misc Codes A (0) B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE EXTERNAL TANK | PART# 82601000000 | SER/LOT# LWT-6 | MANUFACTURER MMC |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE LH2 TANK | PART# 80911000000 | SER/LOT# LWT-6 | MANUFACTURER MMC |
| Test/Operation M - MFG | Prevailing Condtion N - INSPECTION | F / U UC | Fail Mode MS - STRUCT | Cause DH - DES-HDW |
| System STRUCTURAL | Defect MD - M SIZE | Material S - STRUCT | Work Contact C. VOGEL | Fail Date 05/03/1983 |
| Received at MSFC 07/18/1983 | Date Isolated -- | FMEA Reference 1.1.1 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom MU - MECH TOLRNCE | Time Cycle -- |
| Effectivity Text LWT-6 AND SUBS |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 02/10/1995 | CN RSLV SBMT 08/21/1987 | Defer Date -- | Add Date -- | R/C Codes 2 - MFG -- -- |
| Assignee |
| Design J. WHITE | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| Approval |
| Design B. DAVIS | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| PAC Assignee J.EL-IBRAHIM | PAC Review Complete JE | MSFC Closure Date 09/24/1987 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description REF: 1) INTERTANK/LH2 MISALIGNMENT WAS DISCOVERED IN CELL 'A'. THE FWD SRB FITTING (EB-1) WAS MIS- ALIGNED WITH THE AFT SRB FITTING (EB-7) OUT-OF-TOL BY .090. 2) LH2 TANK WELDMENT MISALIGNMENT, BARRELS RELATIVE TO AFT DOME & FWD DOME RELATIVE TO AFT DOME WERE FOUND MISALIGNED SUBSEQUENTLY LH2 BARREL #3 WAS FOUND MISCLOCKED .270 & THE FWD DOME MIS- CLOCKED BY .164 ON LWT-8 |
| Contractor Investigation/Resolution R/C: 1) MMC HAS IMPROVED CLOCKING AND TACK WELDING PROCEDURES DURING MANUFACTURING 2) MMC HAS IMPLEMENTED SCRIBE LINE CLOCKING PROCEDURE TO PREVENT MISALIGNMENT. CAUSE: 1) THE CAUSE OF MISALIGNMENT OF THE SRB FITTINGS, FORWARD TO AFT, WAS DETERMINED TO BE MISCLOCKING OF THE LH2 FORWARD DOME. 2) MISALIGNMENT SEEN IN THE LH2 BARREL AND T-RING ASSEMBLY WAS CAUSED BY INADEQUATE ASSEMBLY PROCEDURE. OPTICAL ALIGNMENT OF BARRELS AND T-RINGS WAS SUS- CEPTIBLE TO MISALIGNMENT DUE TO THE AWKWARD POSITIONING OF THE INSTRUMENTS. THE ACCURACY OF THE LINE OF SIGHT USED BY INSPECTION AFTER COMPLETION OF ASSEMBLY WAS AFFECTED BY THE POSITIONING OF THE.875 FEEDLINE HOLE ON THE FORWARD DOME. 9/6/84 - PRB STATUS, MMC TO HOLD CAPS OPEN TO REVIEW LWT 23 & 24 TECHNIQUE & ALIGNMENT. CHECKING MISUSE OF TOOLING. 3/6/85 STATUSED AT PRB MTG 2-25-85 AS FOLLOWS - MFG NOW USING REVISED CLOCKING PROCEDURE. MMC WANTS TO MONITOR ONE MORE TANK TO ASSURE PROCEDURES ARE OK. ECD FOR CLOSURE IS APPROX 5-6 WKS. 3/13/85 ET CLEARANCES - LWT-6 CLEARED USE AS IS, DAR MMC-ET-153 ISSUED LWT-7 NO MARS LWT-8,9, & 11 THE LH2 TANK MISCLOCKING WAS ACCEPTABLE WITH SPECIAL SRB FITTINGS & LO2 FEEDLINE FITTINGS. LWT-10 THE LH2 TANK MISCLOCKING WAS ACCEPTABLE WITH USE-AS-IS MRB DISPOSITION. LWT-12 LH2 TANK FWD DOME CLOCKED WITHIN TOLERANCES LWT-13 LH2 TANK FWD DOME CLOCKED WITHIN TOLERANCES. LWT-14 LH2 TANK FWD DOME CLOCKED WITHIN TOLERANCE 1871, T-FRAME MISCLOCKED (USE-AS-IS) LWT-15 LH2 TANK FWD DOME CLOCKED OUT OF TOLERANCE; (MRB UA1) LWT-16 LH2 TANK FWD DOME CLOCKED WITHIN TOLERANCE; 1623 T-FRAME & BBL. #1 MISCLOCKED (USE-AS-IS). LWT-17 LH2 TANK FWD DOME CLOCKED WITHIN TOLERANCE; T-FRAMED BARREL MISCLOCKING (USE-AS-IS). LWT-18 LH2 FWD DOME CLOCKED WITHIN TOLERANCE; T-FRAME & BARREL MISCLOCKED (USE-AS-IS WITH SPECIAL LO2 FEEDLINE FITTING). LWT-19 LH2 FWD DOME CLOCKED WITHIN TOLERANCE; T-FRAME & BARREL MISCLOCKED (UAI WITH SPECIAL LO2 FEEDLINE FITTINGS). LWT-20 LH2 FWD DOME CLOCKED WITHIN TOLERANCE; ALL T-FRAMES CLOCKED WITHIN TOLERANCE; ONE BARREL LOCATION CLOCKED SLIGHTLY OUT (UAI). LWT-21 LH2 FWD DOME CLOCKED WITHIN TOLERANCE; ALL T-FRAMES & BARRELS CLOCKED WITHIN TOLERANCE. LWT-22 LH2 FWD DOME CLOCKED WITHIN TOLERANCE; TWO T-FRAMES OUT OF TOLERANCE, ONE BARREL SLIGHTLY OUT OF TOLERANCE (USE-AS-IS). LWT-23 LH2 FWD DOME CLOCKED WITHIN TOLERANCE; TWO T-FRAME OUT-OF-TOLERANCE, THREE BARRELS OUT-OF-TOLERANCE. LWT-24 LH2 FWD DOME CLOCKED WITHIN TOLERANCE. THREE RING FRAMES OUT-OF-TOLERANCE, THREE BARRELS OUT-OF-TOLERANCE. LWT-25 LH2 FWD DOME CLOCKED WITHIN TOLERANCE. T-RING STA. 1623 .019 00T & BB1. #3 .032 00T (BOTH UAI). 6/5/85 PRB STATUS 4-16-85 MTG - THIS PROBLEM HAS BEEN IDENTIFIED AS A .375 IN. DIA. HOLE BEING MISLOCATED. WILL CHANGE FORWARD DOME CLOCKING & TACK WELDING PROCEDURES. TO REMAIN OPEN UNTIL FIX IS VERIFIED. 6/5/85 PRB STATUS 5-16-85 MTG - FIRST PROBLEM ON CAPS RELATIVE TO MATING WITH SRB HAS BEEN COR- RECTED. THE 2ND PROBLEM INVOLVING LH2 TANK WELDMENT MISALIGNMENT/MISCLOCKING HAS NOT BEEN RESOLVED CAUSE(S) ARE UNKNOWN . 7/2/85 STATUSED AT PRB MTG 6-20-85 AS FOLLOWS - THERE IS AN ECR PENDING AGAINST THE BARREL PANELS. AT THE 5-16-85 PRB MTG AN ACTION ITEM (PRB ET-38) WAS GIVEN TO H JACOB/MMC/D3741 TO PREPARE A PRESENTATION TO CLARIFY THE CAUSE(S) OF THE LH2 TANK WELDMENT MISALIGNMENT/MISCLOCKING PROBLEM & TO BETTER DEFINE THE R/C ACTIONS. MR. JACOBS/MMC HAS PREPARED THE DATA, & MSFC WILL TRY TO ARRANGE FOR IT TO BE PRESENTED TO MR. J. NICHOLS/EE31 AT MMC ON 6-21-85. 8/15/85 PRB STATUS - CAPS ACTION ITEM TO INVESTIGATE SCRIBE-LINE ALIGNMENT TECHNIQUE INSTEAD OF OPTICS METHOD IS STILL OPEN MR. J. FINCHER/MMC TO ARRANGE MEETING WITH MR. NICHOLS/MSFC FOR BRIEFING ON R/C ACTIONS. ECD FOR CLOSURE OF THIS CAPS IS 10-20-85 10/25/85 PRB STATUS 10-17-85 - EACH DISCREPANCY IS WORKED ON A MARS HAVE TO CUSTOM MAKE PARTS TO ATTAIN PROPER ALIGNMENT. LATEST ACTION REQUIRES USE OF SCRIBE LINES ON COMPONENTS TO AID IN CLOCKING OF BARRELS. ECD IS 11-30-85. 11/21/85 PRB STATUS - SCRIBE LINE TOOLING IS COMPLETE AND WILL BE VERIFIED ON LWT-39. ECD IS FEBRUARY 1986. 1/16/86 PRB STATUS - NO CHANGE FROM STATUS OF 11-21-85 ABOVE ALTHOUGH ECD IS CHANGED TO 2-28-86. 3/20/86 PRB STATUS - SCRIBE LINE TECHNIQUE DID NOT SOLVE PROBLEM. FIRST LH2 TANK WELDED AFTER IMPLEMENTATION OF SCRIBE LINE PRODUCED AN OUT-OF-TOLERANCE TANK. MMC NOW INVESTIGATING A METHOD FOR VERIFYING CLOCKING BY USING THE FEEDLINE HOLES IN THE FORWARD AND AFT DOMES AS REFERENCE POINTS. ECD IS 5-30-86. 4/17/86 PRB STATUS - NEW TASKS OPENED TO INVESTIGATE SCRIBE LINE CLOCKING OF BARRELS AND T-RINGS; VERIFICATION OF HOLE ALIGNMENT - DOME FIXTURES; AND FORWARD DOME CHECK TOOL. ECD IS 6-18-86. 5/15/86 PRB STATUS - INVESTIGATION IS ONGOING. ECD CHANGED TO JULY 1986. 6/19/86 PRB STATUS - DEFERRED UNTIL NEXT PRB. MEETING RAN OUT OF TIME. 7/15/86 PRB STATUS - LWT-40 IS COMPLETED. PUTTING FWD DOME ON LWT-41. VERIFYING HOLE ALIGNMENT ON AFT DOME. THIS IS A PRODUCTION PROBLEM. CHECKED TWO DOMES, NEED ONE MORE CHECK TO VERIFY PROCEDURE. 5/28/87 - STATUS UPDATE - ASSESSMENT OF TOOLS, OPERATIONS, AND ENGINEERING RELATED TO CLOCKING OF BARRELS, DOMES, AND T-RINGS. ECD 7/25/87. 8/24/87 CLOSURE UPDATE - REF. CAPS S-062 C. TASK I GENERAL A. LWT-6 EXTERNAL TANK WAS FOUND TO BE MISCLOCKED IN CELL "A". A SHOP AID WAS THEN FABRICATED AND THE SRB BEAM WAS MEASURED RELATIVE TO THE INTERTANK FLANGE; THE +Y SIDE WAS .015 FROM NOMINAL AND THE -Y WAS .080. THE RELIABILITY OF THIS MEASUREMENT IS, HOWEVER, UNKNOWN BECAUSE IT WAS BASED UPON A NEWLY DESIGNED AND FABRICATED SHOP AID. THIS SHOP AID WAS SUBSEQUENTLY USED TO CHECK AN INTERTANK SUBASSEMBLY DURING FABRICATION, THE SRB BEAM WAS VERIFIED TO BE ALIGNED WITH .015. THE PROCEDURES THAT ALIGN THE BEAM IN THE INTERTANK INVOLVE HARD TOOLING, THUS MINI- MIZING THE LIKELIHOOD OF ERROR. PROCEDURES THAT ALIGN THE HYDROGEN TANK FORWARD DOME INVOLVE OPTICS BEFORE TACKING. AN OPTICAL CHECK IS ALSO MADE AFTER WELDING IS COMPLETED. ON LWT-6, THE ORIGINAL ALIGNMENT WAS WITHIN .020 AND THE CHECK AFTER WELDING WAS VERIFIED PER REQUIREMENTS TO BE WITHIN .075. B LWT-8 LH2 TANK WELDMENT WAS CHECKED AND THE FOLLOWING MISALIGNMENTS RELATIVE TO THE AFT DOME WERE VERIFIED: POSITION MISALIGNMENT TOLERANCE FORWARD DOME .164 .075 BARREL NO. 3 .270 +/-.120 1623.8 CHORD .3 (APPROXIMATELY) +/-.120 THE FORWARD DOME ALIGNMENT TECHNIQUE BASICALLY ALIGNS REFERENCE POINTS NEAR +Y AND -Y PARALLEL TO THE AFT DOME REFERENCE PLANE. THE DOME IS THEN LOCKED IN PLACE ON ONE SIDE (+Y) WITH A PAIR OF TACK WELDS AND ALIGNMENT IS VERIFIED. TACK WELDING THEN PROCEEDS AROUND THE CIRCUM- FERENCE. WITH THIS PROCEDURE, IT IS ESSENTIAL THAT THE OFF-SET BETWEEN THE COMPONENTS TO BE WELDED BE MINIMIZED OVER THE LENGTH OF THE WELD PRIOR TO ALIGNING. THIS MAY BE VERY DIFFICULT TO ACCOMPLISH AND MISALIGNMENT CAN OCCUR. THE ALIGNING OF LWT-9 FORWARD DOME WAS MONITORED. AN OFF-SET OF APPROXIMATELY .200 AT THE BOTTOM WAS NOTED DURING ALIGNMENT. THIS MAY HAVE BEEN SIGNIFICANT SINCE A MISCLOCKING OF .150 WAS FOUND AFTER TACKING AND WELDING. THE ABOVE IS CONSIDERED TO BE ONE OF MANY POSSIBLE CAUSES FOR MISALIGNMENT THAT NEEDS TO BE INVESTIGATED. TASK II LH2 ALIGNMENT THE FORWARD TO AFT DOME PROCEDURES FOR LWT-6 WERE ACCOMPLISHED ON THE 5019 FIXTURE. THE COMPLETED WELDMENT WAS THEN RECHECKED WITH EXTERNAL OPTICS AND FOUND TO BE WITHIN .020. ALIGNMENT PROCEDURES HAVE SINCE CHANGED SUCH THAT THE INITIAL ALIGNMENT IS ACCOMPLISHED ON THE 5068 WITH EXTERNAL OPTICS. LWT-8, WHICH FOLLOWED THIS PROCEDURE, WAS INITIALLY ALIGNED WITHIN .015 BEFORE TACKING. THE RECHECK AFTER WELDING DETERMINED THAT THE FORWARD DOME WAS MISCLOCKED WITH A READING OF .164 THIS CAPS SHALL BE CONCERNED WITH LH2 FORWARD DOME AND BARREL ALIGNMENT PROCEDURES FOR LWT-8 AND UP. INVESTIGATIONS INCLUDED THE FOLLOWING: A DETERMINED POSSIBLE FAILURE MODES IN THE OPTICAL ALIGNMENT TECHNIQUE THAT CAN INTRODUCE ERROR IN CLOCKING. B. INVESTIGATED THE AFFECTS OF TACKING AND WELDING ON ALIGNMENT. C. INVESTIGATED THE LOWER AFT SRB ALIGNMENT RELATIVE TO THE UPPER. CLOSURE STATEMENT CLOCKING AND TACKING PROCEDURES HAVE BEEN CHANGED ON THE FORWARD DOME INSTALLATION. THE PROBLEM HAS BEEN CORRECTED SINCE LWT-12 (REFERENCE MPP 80914000000, LWT-12). TASK III SRB - INTERTANK ALIGNMENT THE SRB IS ALIGNED TO THE INTERTANK WITH HARD TOOLING. INSPECTION OF THIS TOOLING WITH EXTERNAL OPTICS TO VERIFY ITS ALIGNMENT (MAY BE DONE IN CONJUNCTION WITH THE PI AND PM OF MAY, 1983). INSPECT THE INTERTANK - SRB ALIGNMENT FOR THE DURATION OF THIS CAPS UTILIZING THE SHOP AID WHICH ATTACHES TO THE FLANGE AT +Y AND -Y (THIS MEASUREMENT IS TO BE MADE IN THE 1ST POSITION ASSEMBLY). CLOSURE STATEMENT NO ALIGNMENT PROBLEM WITHIN THE INTERTANK WAS DETECTED (REFERENCE MEMORANDUM FROM G. SCARBOROUGH TO C. VOGEL, DATE JUNE 4, 1987). TASK IV CELL A - ALIGNMENT PROCEDURE EVALUATE TOOLING SETUP AND PROCEDURES FOR PROBLEM AREAS AND RECOMMEND IMPROVEMENT. CLOSURE STATEMENT TOOLING CHANGES WERE MADE IN THE PLUMB BOB FIXTURING USED WITH OPTICS (REFERENCE MEMORANDUM FROM T. CLAUSING TO C. VOGEL, DATED JUNE 11, 1987). TASK V T-RING AND BARREL ALIGNMENT SINGLE POINT UNDER THE FIXTURE OPTICS WAS ADDED TO THE 5019 WELD FIXTURE TO PROVIDE MORE ACCURATE T-RING AND BARREL ALIGNMENT. AN IMPROVEMENT WAS SEEN SUBSEQUENT TO THE CHANGE (LTS 20 AND 21). LATER EFFECTIVITIES, HOWEVER, AGAIN SHOWED A PROBLEM. IT IS SUSPECTED THAT THIS WAS RELATED TO PROCEDURES, THUS, THE FOLLOWING CHANGES SHALL BE MADE: PHASE I. THE LWT-25 LH2 (80914090960) MPP SHALL BE REDLINED TO SPECIFICALLY REQUIRE THAT THE CLOCKING SCRIBE MARKS INSTALLED DURING OPTICAL ALIGNMENT BE PLACED AT THE BOTTOM NEAR THE LINE OF SIGHT. THE SCRIBE LINE SHALL BE APPLIED WITH A VIBRO MARKER AND SHALL BE APPROXIMATELY 2" LONG. A REDLINE SHALL ALSO STIPULATE HOW THE TACK WELDING OPERATION SHALL BE DONE. PHASE II. THE LWT-25 MPP, IN CONJUNCTION WITH PHASE I ABOVE, SHALL BE REDLINED FOR QC INSPECTION VERIFICATION OF THE FOLLOWING: - PROPER SCRIBE LINE APPLICATION PRIOR TO ANY ROTATION - SCRIBE LINE ALIGNMENT AFTER TACKING - SCRIBE LINE ALIGNMENT AFTER WELDING CLOSURE STATEMENT LWT-25 MPP WAS REDLINED AS INSTRUCTED. THE CABLE TRAY HOLES AND FEEDLINE HOLES WERE GROUPED TIGHTERTO THE LINE OF SIGHT FOR LT-25 THAN ON LWTS 22, 23, AND 24. THE MPPS FOR SUBSEQUENT BUILDS REFLECT THAT THE SCRIBE LINE BE APPLIED NEAR THE LINE OF SIGHT, MPPS HAVE ALWAYS, HOWEVER, REFLECTED THAT SCRIBE LINES BE VERIFIED AFTER TACKING FOR RELATIVE MOVEMENT (AND THIS HAS NOT BEEN A PROBLEM) (RE- FERENCE MPP 80914090960, LWT-25). TASK VI SCRIBE LINE CLOCKING OF BARRELS AND T-RINGS ALIGNMENT PROCEDURES WERE TIGHTENED UP AS OF LWT-25, HOWEVER, THIS PROVED TO BE INSUFFICIENT TO PROVIDE A CONSISTENTLY ACCEPTABLE PRODUCT. LWT-28 WAS CHECKED ON THE 5068 FIXTURE FROM TWO POSITIONS TO VERIFY THAT THE ORIENTATION OF THE INSTRUMENTS WAS NOT PROVIDING ERRONEOUS INFORMA- TION (IT WAS GOOD). AS OF LWT-30, CLOCKING DATA FROM LWT-17 AND UP WERE ANALYZED FOR FEASIBILITY OF CLOCKING WITH REAPPLIED SCRIBE LINES. TOOLING WAS ORDERED FOR THIS AND THE SCRIBE LINES WERE ADDED SUPPLEMENTARY TO OPTICS ON LWT-39 FOR EVALUATION. PRELIMINARY RESULTS ON LWT-39 SHOWS THAT THE SCRIBE LINES ARE A VIABLE FORM OF CLOCKING. THE SCATTER OF THE HOLE PATTERN IS ACCEPTABLE BUT THE PATTERN MOVES OFF AWAY FROM THE LINE OF SIGHT, THUS, CREATING AN OUT OF TOLERANCE CONDITION (THE SAME EFFECT OCCURRED WITH OPTICAL CLOCKING). THIS DRAWS SUSPICION TO THE PLACEMENT OF .875 AND.375 HOLES IN THE FORWARD AND AFT DOME CHORDS. EVALUATE THE EFFECTIVENESS OF PREAPPLIED SCRIBE LINES FOR CLOCKING BARRELS AND T-RINGS. REDLINE MPPS AND LWTS 40 AND 41 TO ACCOMPLISH THE EVALUATION CLOSURE STATEMENT REVISIONS WERE MADE TO LWTS 40 AND 41 MPPS EVALUATION SHOWS THAT SCRIBE LINE ALIGNMENT IS A VIABLE PROCESS (REFERENCE MPP 80914090960 M009, ATTACHMENTS). TASK VII VERIFICATION OF HOLE ALIGNMENT - DOME FIXTURES THE .875 DIAMETER HOLE ON THE FORWARD DOME CHORD AND THE .375 DIAMETER HOLE ON THE AFT DOME CHORD ARE USED IN CLOCKING THE BARRELS AND T-RINGS. THE POSITIONS OF THESE HOLES RELATIVE TO OTHER FEATURES ON THEIR RESPECTIVE DOMES MAY HAVE AN EFFECT ON THE OVERALL CLOCKING READINGS MADE ON THE LH2 TANK. THE POSITIONING OF THE .875 HOLE RELATIVE TO THE Y AXIS BOLTING RING HOLES ON THE FORWARDDOME, AND THE .375 HOLE RELATIVE TO THE SRB ATTACH POINTS ON THE AFT DOME, DETERMINE THE CLOCKING RELATIONSHIP BETWEEN TWO SETS OF REFERENCES 1) .875 AND .375 HOLES FOR BARREL AND T-RING CLOCKING, AND 2) BOLTING RING HOLES AND SRB ATTACH POINTS FOR DOME CLOCKING. THE RELATED TOOLING USED IN DRILLING THE FORWARD AND AFT DOMES SHALL BE CHECKED USING A THEODOLITE INSTRUMENT AT THE FOLLOWING LOCATIONS: T02A7016: PROVIDE ANGLE READINGS FROM THE CENTER LINE OF THE FOLLOWING LOCATIONS TO +Z: S-2-3, S-3-3, R-14-5, R-13-5, R-14-4, R-15-4, -Z T02A7018: PROVIDE ANGLE READINGS FROM THE CENTER LINE OF THE FOLLOWING LOCATIONS TO +Z: +Y LOWER SRB PINHOLE; +Y UPPER SRB PINHOLE; .375 DIAMETER HOLE (REFERENCE 80914961960, SHEET 9, SECTION U-U), -Y LOWER SRB PINHOLE, -Y UPPER SRB PINHOLE. CLOSURE STATEMENT ANGULAR READINGS ON THE GIVEN FEATURES WERE TAKEN. NO SIGNIFICANT DEVIATIONS FROM NOMINAL WERE SEEN ON THE 7018. ON THE 7016 FIXTURE, REFERENCING OFF OF THE Z AXIS, ALL OTHER POINTS IDENTIFIED TO BE CHECKED RANGED FROM .0080 DEGREES TO .0149 DEGREES FROM NOMINAL (REFERENCE PA WORKSHEETS 96159 AND 123936) TASK VIII FORWARD DOME CHECK TOOL (.0875 HOLE) DESIGN AND FABRICATE A CHECK TOOL (SHOP AID) THAT WILL VERIFY THE PROPER LOCATION OF THE .875 DIAMETER HOLE IN THE 1129 CHORD TO THE S-2-3 AND S-3-3 HOLES IN THE BOLTING RING. VERIFY HOLE LOCATION ON LWTS 39, 40, AND 41 WITH THIS TOOL. CLOSURE STATEMENT THE .875 DIAMETER FEEDLINE PINHOLE ON LWTS 39, 40, AND 41 WAS CHECKED WITH THE FABRICATED TOOL. OFFSETS TOWARDS THE +Y AXIS OF .027, .070, AND .087 WERE FOUND, RESPECTIVELY (REFERENCE MPPS 80914004000-020 AND 80914001950-009). TASK IX IMPROVEMENTS TO BARREL SCRIBE LINE APPLICATION TOOL EVALUATE THE EFFECTIVENESS OF THE BARREL SCRIBE LINE TOOL, T05A5102-24-101, GIVEN THAT THE TOOLING HOLE IN THE TRIMOFF AREA IS NOT EXISTENT IN SOME PANELS. THE TOOLING HOLE IS IN LINE WITH THE CABLETRAY HOLES AND IS AN ADDITIONAL FEATURE AIDING IN SETTING UP THE TOOL. CLOSURE STATEMENT THE NEW SCRIBE LINE TOOL, T05A5102-24-101, APPLIES A SCRIBE LINE WITH AN ACCURACY OF +/- .03 EVEN WITHOUT THE USE OF THE TOOLING HOLE. THE OLD TOOL HAD AN ACCURACY OF APPROXIMATELY +/- .180 DUE TO DIFFICULTIES IN HANDLING IT. THE INCONSISTENCY IN PROVIDING THE ADDITIONAL TOOLING HOLE IN SOME PANELS HAS BEEN CORRECTED FOR LWT-53 AND UP (ALL PANELS SHALL HAVE THAT TOOLING HOLE), REFERENCE MEMORANDUM DATED 1/5/87, FROM R. WHITE TO C VOGEL). TASK X VERIFICATION OF SCRIBE LINE CLOCKING ON LWT-45 ANALYSIS FROM TASK VI ON PREAPPLIED SCRIBE LINE VERSUS OPTICAL ALIGNMENT INDICATED THAT ALIGNMENT SOLELY BY SCRIBE LINE FROM THE AFT DOME, UP TO AND INCLUDING BARREL 4, WOULD BE AN IMPROVEMENT OVER OPTICAL ALIGNMENT ANALYSIS OF HISTORICAL DATA BACK TO LWT-20 ALSO SUPPORTS THIS POSITION BY A PURELY ANALYTICAL ANALYSIS, THE OPTICAL METHOD WOULD BE IDEAL, HOWEVER, THERE PROVES TO BE COM- PROMISING FACTORS ASSOCIATED WITH THE ACTUAL PERFORMANCE OF THE TASK ON THE 5019 WELD FIXTURE THAT ULTIMATELY AFFECTS THE OUTCOME. SCRIBE LINE ALIGNMENT SHALL BE INCORPORATED INTO THE BUILD OF LWT-45 LH2 AFT DOME/BARREL WELDMENT. EVALUATE THE EFFECTIVENESS OF SCRIBE LINE ALIGNMENT. THE EVALUATION SHALL BE ALLOWED TO CONSIDER THE ADDITIONAL EFFECTS OF HOLE POSITIONING ON THE FORWARD AND AFT DOMES. CLOSURE STATEMENT LWT-45 WAS CLOCKED BY SCRIBE LINE (BARRELS AND T-RINGS). VERIFICATION OF CLOCKING AFTER COMPLETION OF ASSEMBLY DETERMINED THAT ALL POSITIONS WERE IN TOLERANCE. IN ADDITION TO IMPLEMENTINGSCRIBE LINE CLOCKING, A MEASUREMENT TO VERIFY THE RELATIVE POSITION OF THE .875 FEEDLINE HOLE ON THE FORWARD DOME (STATION 1129) RELATIVE TO THE INTERFACE BOLTING FLANGE WAS IMPLEMENTED. THIS MEASUREMENT PROVIDED MORE ACCURATE PLACEMENT OF THE STATION 1129 REFERENCE POINT FOR THE LINE-OF- SIGHT USED IN VERIFYING CLOCKING (REFERENCE MPP 80914090960 M009, LWT-45. TASK XI MEASUREMENT ON LWT-46 AFT DOME MAKE A MESUREMENT DETERMINING THE DISTANCE BETWEEN THE .375 HOLE (USED AS A REFERENCE IN CLOCKING BARRELS AND T-RINGS) AND THE 3.250 UPPER SRB HOLE (USED AS A REFERENCE IN CLOCKING THE FORWARD DOME). NOTE: THE CLOCKING SCRIBE LINE IS APPLIED TO THE AFT DOME BY THE T02A7512 TOOL SECURED TO THE .375 HOLE. CLOSURE STATEMENT THE LENGTH BETWEEN THE .375 AND 3.250 HOLES ON LWT-46 WAS MEASURED AT 112.371 THIS DOME HAD A MEASURED CIRCUMFERENCE OF 1040.280, THUS THE NOMINAL SHOULD BE 112.324. THE DELTA FROM NOMINAL (.047) WAS WITHIN THE STACKUP OF TOLERANCES (+/- .070; REFERENCE PA WORKSHEET 132593). TASK XII VERIFICATION OF TOLERANCES ON FORWARD DOME ENGINEERING SHALL VERIFIY THE TOLERANCES ON THE FORWARD DOME FOR THE POSITION OF THE .875 FEEDLINE HOLE RELATIVE TO THE INTERFACE BOLTING FLANGE HOLES, AND THE BIPOD HOLES RELATIVE TO THE FLANGE HOLES, AND THE .875 HOLE RELATIVE TO THE BIPOD HOLES. VERIFICATION OF ICD REQUIREMENTS SHALL ALSO BE MADE ON THE BIPOD ATTACH POINTS. CLOSURE STATEMENT THE FORWARD DOME TOLERANCES ARE THE FOLLOWING F/L TO BOLT FLANGE HOLE (+/- .050), BIPOD TO BOLT FLANGE HOLE (+/- .050), F/L TO BIPOD (+/- .060) (REFERENCE MEMORANDUM FROM D. WHITCHURCH TO C. VOGEL, DATED JULY 9, 1987). CAUSE AND CORRECTIVE ACTION SUMMARY THIS CAPS ADDRESSED TWO PRIMARY PROBLEMS. THE MISALIGNMENT OF THE FORWARD TO AFT SRB FITTINGS, AND THE MISALIGNMENT OF THE BARRELS AND T-RINGS IN THE LH2 TANK. THE FIRST, SRB MISALIGNMENT, WAS CAUSED BY MISCLOCKING THE LH2 FORWARD DOME. THE PROBLEM WAS CORRECTED BY IMPROVING CLOCKING AND TACK WELDING PROCEDURES. HIGHER MANDREL PRESSURES WERE IMPLEMENTED TO MINIMIZE OFFSET BETWEEN THE FORWARD DOME AND BARREL #4 PRIOR TO TACK WELDING TACK WELDING WAS CHANGED TO BEGIN DIRECTLY AT THE BOTTOM AND WORK UPWARDS SYMMETRICALLY ON EITHER SIDE AS FAR AS POSSIBLE PRIOR TO ROTATING THE TANK. CORRECTIVE ACTION WAS IMPLEMENTED AS OF LWT-12. THE SECOND PROBLEM, LH2 BARREL AND T-RING MISALIGNMENT, WAS CAUSED BY MULTIPLE FACTORS. THE OPTICAL ALIGNMENT USED IN THE 5019 WELD FIXTURE WAS INADEQUATE. IT WAS IMPROVED WITH A REDESIGN AS OF LWT-20, BUT THAT EFFORT ALSO PROVED TO BE INADEQUATE. REPEATABILITY WAS POOR, POSSIBLY DUE TOTHE AWKWARD POSITION OF THE INSTRUMENTS DIRECTLY UNDERNEATH THE TANK. CORRECTIVE ACTION WAS TAKEN BY IMPLEMENTING SCRIBE LINE CLOCKING (IMPLEMENTED LWT-45). ANOTHER FACTOR RELATING TO THE PROBLEM WAS THAT THE .875 FEEDLINE HOLE ON THE FORWARD DOME WAS OFFSET RELATIVE TO THE INTERFACE BOLTING FLANGE HOLES. THE OFFSET WAS SUFFICIENT ENOUGH TO CONTRIBUTE TO THE MISCLOCKING PROBLEM. CORRECTIVE ACTION WAS TAKEN BY IMPLEMENTING A CHECK TO DETERMINE THE ACTUAL OFFSET OF THE .875 HOLE ON THE FORWARD DOME. THE READING WAS INCORPORATED INTO THE REFERENCE LINE FROM WHICH THEN CLOCKING IS MEASURED. CORRECTIVE ACTION WAS IMPLEMENTED AS OF LWT-45. CONCURRENTLY, PRODUCTION IMPLEMENTED STEPS TO ASSURE IMPROVED ALIGNMENT BETWEEN THE .875 FEEDLINE HOLE AND THE INTERFACE BOLTING FLANGE HOLES ON THE FORWARD DOME. THE AFFECTIVENESSS OF THE CORRECTIVE ACTION TAKEN FOR THE FIRST PROBLEM, SRB MISALIGNMENT, WAS CON- FIRMED BY NUMEROUS BUILDS FROM LWTS 12 THROUGH 45. THE CORRECTIVE ACTION TAKEN FOR THE SECOND PRO- BLEM, LH2 BARREL AND T-RING MISALIGNMENT, IS DEEMED TO BE AFFECTIVE BASED UPON EVIDENCE SEEN ON LWT-45. THE MEASUREMENTS TAKEN ON LWT-45 CONFIRMED THAT THE PROCESS WAS BROUGHT UNDER CONTROL. LWT-45 WAS IN TOLERANCE FOR ALL BARRELS AND T-RINGS AND NO LONGER WAS THERE DATA POINT SCATTER AS SEEN ON PRIOR EFFECTIVITIES. THERE ARE FOURTEEN DATA POINTS PER EFFECTIVITY MEASURED IN DETERMINING CLOCK- ING OF BARRELS AND T-RINGS. THE LARGE NUMBER OF DATA POINTS REFLECTS RATHER ACCURATELY THE LEVEL OF CONTROL THE CLOCKING PROCESS HAS. THUS, LWT-45 PROVIDES SUFFICIENT EVIDENCE OF CORRECTIVE ACTION |
| MSFC Response/Concurrence |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A06858 | IFA# -- | Contractor RPT# S-062 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 80911000000 | Asmnt Part Name LH2 TANK | Asmnt Serial/Lot# LWT-6 |
| HCRIT CD -- | FCRIT CD 1 | CAUSE CD DH - DES-HDW | FAIL MODE MS - STRUCT |
| Asmnt FMEA 6.2.1.1 | Asmnt FM 1 | FMEA CSE D | FMEA SCSE 2 |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |