A-FRAME PREUSE INSPECTION CHECKSHEET SAMPLE

A-Frame Identification:  	 Date:  	/ 	/

The user shall perform the following checklist prior to performing hoisting and rigging operations with this A-Frame. Correct Unsat items found during this inspection before using this equipment.  If Unsat items can not be corrected, tag the equipment out of use.  Mark not applicable (N/A) for items not contained or applicable to this A-Frame.

| A-Frame Inspection Areas | N/A | SAT | UNSAT |
| --- | --- | --- | --- |
| Manufacturers’ instructions for use are posted in the area of use or on the portable A-Frame. |  |  |  |
| Look for bent, broken, damaged, corroded, cracked, or missing parts. |  |  |  |
| Verify required markings are installed and legible: Rated capacity legibly marked on the structure on each side of the primary beam, and a tag indicating the due date of the next inspection is attached to the trolley, A-Frame, and any attached hoist. |  |  |  |
| Ensure the trolley, beam clamp, or hoist working load limits do not exceed the capacity rating of the A-Frame. |  |  |  |
| Perform a function test of the trolley and hoist to ensure proper operation. |  |  |  |
| If adjustments or repairs are necessary or any defects are found that affect safe operation, stop work and report deficiencies to the equipment custodian. |  |  |  |
| Operator is qualified in accordance with the Hanford Site Hoisting and Rigging manual to perform H& R operational activities. |  |  |  |

Type of hoist used on the A-Frame:	None  	       Air          Manual  	         Electric  	___

| Hoist Inspection Areas | N/A | SAT | UNSAT |
| --- | --- | --- | --- |
| Unusual sounds. |  |  |  |
| Brakes working properly. |  |  |  |
| Hooks inspected in accordance with H&R Manual “Hooks” Section. |  |  |  |
| Housing integrity intact. |  |  |  |
| Supporting structure sound. |  |  |  |
| Load bearing parts (Yoke, Clevis). |  |  |  |
| Cable/Chain in operating condition. |  |  |  |
| Operating controls respond properly. |  |  |  |
| Load limiting devices functional. |  |  |  |
| Limit switches work properly. |  |  |  |
| Warning labels installed in accordance with H&R Manual “Hoists, Jib Cranes, and Monorails” Maintenance section. |  |  |  |
| Sheaves and Drums inspected for damage/wear. |  |  |  |
| Lubrication in accordance with manufacturers’ instruction manual. |  |  |  |
| Collectors/Load chain buckets properly affixed. |  |  |  |
| Evidence of wiring wear or damage. |  |  |  |
| Supply air system at rated air pressure. |  |  |  |

COMMENTS: