Atlanta Hartsfield (ATL) - PSOTATL08003

ASQ876/CRJ2 “Acey 876” was taxing eastbound on taxiway Mike.  The pilot was instructed to taxi via M (Mike), to D (Dixie) and hold short of runway 27R.  DAL261/B752 “Delta 261” was cleared for takeoff on runway 27R.  ASQ876 turned right on taxiway Dixie, and crossed runway 27R at taxiway D as DAL261 was on departure roll.  As DAL261’s speed increased past 44 knots, ASDE-X safety logic alerted “Runway 27R occupied!”  ASQ876 was clear of the runway at taxiway D as DAL261 was abeam taxiway M16.  DAL261 continued to depart as ACY876 cleared the runway.  The closest proximity was 1,640’.

At some point after DAL261 was issued a takeoff clearance, an unidentified voice can be heard on the frequency advising “You guys better hurry.”, “You got somebody crossing the runway…at Dixie.”, “Holy smokes.”  It is undetermined at this point where these transmissions came from.