652.0203	Explanation of Tables and Databases

The majority of current Oregon soil survey data are contained in electronic databases that are best accessed via the internet.  Limited printed copies of soils survey data are available for some areas that have been surveyed and for which data have not been included in the electronic database.

The recommended approach is to access soil survey data using the Web Soil Survey which can be accessed at:

http://websoilsurvey.nrcs.usda.gov/app/

Using the Web Soil Survey, a soils map of the design area can be obtained and printed along with pertinent soils data.  An example soils map and accompanying map unit legend summary are shown in Figure OR2-10, and a copy of soil physical properties for the site is shown in Table OR2-15.

Oregon Soil Survey Reports, Maps, and Data are also accessible at the following site:

http://www.or.nrcs.usda.gov/pnw_soil/or_data.html

Detailed information that can be downloaded and accessed for each county in Oregon includes the following:

Online Soil Maps – View and print soil maps for a selected area with aerial photograph or topographic map background.

Map Unit Symbol Legend – table with map unit symbols and names in PDF format.

Report Text – published soil survey report text excluding tables and soil maps in PDF format.

Online Soil Data Reports – create reports of soil properties and interpretations by selecting soil map units and report options.  Links in this column will take you to the Soil Data Mart web site.   Reports can be printed or saved as PDF or Rich Text format.

Tabular Data – compressed file of tables containing soil properties and interpretations.  Links in this column will take you to the Soil Data Mart web site.  The tabular data can be downloaded and imported into a Microsoft Access template file, which is also available at the Soil Data Mart web site.

Spatial Data - compressed file containing soil survey spatial data for geographic information system software.  Links in this column will take you to the Soil Data Mart web site.   Spatial data can be downloaded in a variety of formats and projections.

Hydric Soil List – table with soil mapunit symbols, component names, and hydric soil ratings in PDF format.

Figure OR2-10	Example soils map and accompanying map unit legend summary from Web Soil Survey for a farm unit in central Oregon

Table OR2-15	Example soil physical properties summary from Web Soil Survey for a farm unit in central Oregon

OR652.0204	State supplement

- Soil surveys

As described in Section 652.203, most soil survey information for Oregon can be accessed via the internet.  Soil information and field interpretations are also available in Section II of the Field Office Technical Guide, the electronic version of which is available online.

- Computational tools

The NRCS Soil Texture Calculator can be used to show the soil texture on the soil texture triangle if the percentages of sand, silt, and/or clay are known.  The URL for the Calculator is:

http://soils.usda.gov/technical/investigations/texture/

Estimates of soil water characteristics based on soil texture can be obtained using the soil feature of the SPAW model.  (The SPAW – Soil-Plant-Air-Water – model is CCE compatible for use on CCE computers, and a non-CCE version is also available.)  Soil water characteristics for a given soil texture include

  - Wilting Point (% vol),

  - Field Capacity (% vol),

  - Saturation (% vol),

  - Available Water (in/ft),

  - Saturated Hydraulic Conductivity (in/hr),

  - Bulk Density (lb/ft3),

and for a given moisture content

- Matic Potential (bar), and

- Hydraulic Conductivity (in/hr).

- Intake characteristics for selected soils in Oregon

Soil water intake characteristics are described in Section 652.0202(c) with general ranges of values listed in Tables 2-6 and 2-7.

Intake characteristic data have been obtained for a large number of irrigated soils in Oregon from numerous on-site tests and observations.  This information includes Basic Sprinkler Intake Rate and Intake Family for surface irrigation for specific soil series.  These data are listed in Table OR2-16.  The values listed are general for the soils listed and can vary significantly due to site-specific conditions.

NOTE:  Many values are missing for the soils listed in Table OR2-16.  If additional observed data are obtained, please supply this information to the NRCS Oregon State Conservation Engineer.  Likewise, observed discrepancies in tabled data should also be reported.

- On-site field observations

Soil survey data are key elements in irrigation system design and irrigation water management.  However, as the name implies, it is survey information, and site-specific conditions may vary within area boundaries of the published information.  This fact is especially true in areas where conditions may change rapidly within a short distance.  When in doubt, a field visit is recommended to investigate and verify on-site conditions.

Table OR2-16	Soil intake parameters for selected soils in Oregon

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 1B | ABEGG | GR-L | 0.3 | 4.0 |
| 1C | ABEGG | GRV-SL | 0.25 | 3.0 |
| 1D | ABEGG | GR-L | 0.2 | 4.0 |
| 1E | ABEGG | GRV-SL | 0.15 | 3.0 |
| 2A | ABIN | SICL | 0.15 | 0.35 |
| 1A | ABIQUA | SICL | 0.25 | 0.35 |
| 1B | ABIQUA | SICL | 0.25 | 0.35 |
| AbA | ABIQUA | SICL | 0.25 | 0.35 |
| AbB | ABIQUA | SICL | 0.25 | 0.35 |
| 1B | ADKINS | FSL | 0.75 | 1.5 |
| 1C | ADKINS | FSL | 0.7 | 1.5 |
| 2B | ADKINS | FSL | 1 | 1.5 |
| 2C | ADKINS | FSL | 0.9 | 1.5 |
| 3A | ADKINS | FSL | 1 | 1.5 |
| 3C | ADKINS | FSL | 0.9 | 1.5 |
| 4B | ADKINS | FSL | 0.75 | 1.5 |
| 6B | AGATE | L | 0.2 | 0.9 |
| 151C | AGATE | L | 0.2 | 0.9 |
| 1A | AGENCY | SL | 0.25 | 2.0 |
| 2A | AGENCY | L | 0.25 | 2.0 |
| 2B | AGENCY | L | 0.25 | 2.0 |
| 2C | AGENCY | L | 0.2 | 2.0 |
| 3B | AGENCY | L | 0.25 | 2.0 |
| 3C | AGENCY | L | 0.2 | 2.0 |
| AgC | AGENCY | L | 0.25 | 2.0 |
| 1 | ALGOMA | SIL | 0.6 | 1.5 |
| 1B | ALICEL | FSL | 0.35 | 1.5 |
| 2B | ALICEL | L | 0.35 | 0.9 |
| 3C | ALICEL | SIL | 0.3 | 0.7 |
| 1 | ALOHA | SIL | 0.3 | 0.8 |
| 1A | ALOHA | SIL | 0.3 | 0.8 |
| 1B | ALOHA | SIL | 0.25 | 0.8 |
| 2A | ALOHA | SIL | 0.3 | 0.8 |
| Ah | ALOHA | SIL | 0.3 | 0.8 |
| 2B | ALSPAUGH | CL | 0.2 | 0.5 |
| 2C | ALSPAUGH | CL | 0.2 | 0.5 |
| 2 | AMITY | SIL | 0.3 | 0.7 |
| 3 | AMITY | SIL | 0.3 | 0.7 |
| Am | AMITY | SIL | 0.3 | 0.7 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 1C | ANDERLY | SIL | 0.25 | 0.65 |
| 6B | ANDERLY | SIL | 0.25 | 0.65 |
| 6C | ANDERLY | SIL | 0.25 | 0.65 |
| 7C | ANDERLY | SIL | 0.25 | 0.65 |
| 4B | APPLEGATE | SIL | 0.3 | 0.3 |
| 4C | APPLEGATE | SIL | 0.3 | 0.3 |
| AsC | ASTORIA | SIL | 0.3 | 0.6 |
| 8B | ATHENA | SIL | 0.2 | 0.7 |
| 8C | ATHENA | SIL | 0.2 | 0.7 |
| 5 | AWBRIG | SICL | 0.3 | 0.5 |
| 6 | AWBRIG | SICL | 0.3 | 0.5 |
| 7 | AWBRIG | SICL | 0.3 | 0.5 |
| 66 | AYRES | CBV-L | 0.3 | 1.0 |
| 67 | AYRES | CBV-L | 0.3 | 1.0 |
| 75 | AYRES | CBV-L | 0.3 | 1.0 |
| 76 | AYRES | CBV-L | 0.3 | 1.0 |
| 147 | AYRES | CBV-L | 0.3 | 1.0 |
| 11A | BAKER | SIL | 0.35 | 2.0 |
| 11B | BAKER | SIL | 0.3 | 2.0 |
| 12A | BAKER | SIL | 0.35 | 2.0 |
| 12B | BAKER | SIL | 0.3 | 2.0 |
| 1B | BANDON | SL | 0.5 | 0.4 |
| 1C | BANDON | SL | 0.45 | 0.4 |
| 2C | BANDON | SL | 0.45 | 0.4 |
| 7B | BANDON | SL | 0.5 | 0.4 |
| 7C | BANDON | SL | 0.4 | 0.4 |
| 38B | BANDON | SL | 0.5 | 0.4 |
| 38D | BANDON | SL | 0.4 | 0.4 |
| 4 | BANNING | L | 0.2 | 0.9 |
| 14A | BANNING | L | 0.2 | 0.9 |
| 2A | BARKLEY | L | 0.4 | 0.9 |
| 2B | BARKLEY | L | 0.4 | 0.9 |
| 5B | BARRON | COSL | 0.58 | 3.0 |
| 5C | BARRON | COSL | 0.53 | 3.0 |
| 10B | BARRON | COSL | 0.58 | 3.0 |
| 10C | BARRON | COSL | 0.53 | 3.0 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 6A | BASHAW | SICL | 0.25 |  |
| 6C | BASHAW | SIC | 0.15 |  |
| 7 | BASHAW | C | 0.15 | 0.2 |
| 8 | BASHAW | C | 0.15 | 0.2 |
| 8 | BASHAW | SIC | 0.2 |  |
| 9 | BASHAW | C | 0.15 | 0.2 |
| 15A | BASHAW | C | 0.15 | 0.2 |
| Ba | BASHAW | C | 0.15 | 0.2 |
| Ba | BASHAW | SICL | 0.25 |  |
| Bc | BASHAW | C | 0.1 | 0.2 |
| 16C | BATEMAN | SIL | 0.3 | 0.8 |
| 3 | BEDNER | CL | 0.2 | 0.45 |
| 39 | BEDNER | CL | 0.2 | 0.45 |
| 8C | BELLPINE | SICL | 0.3 |  |
| 8D | BELLPINE | SICL | 0.25 |  |
| 9C | BELLPINE | SICL | 0.3 |  |
| 9D | BELLPINE | SICL | 0.25 |  |
| 11C | BELLPINE | SICL | 0.3 |  |
| 11D | BELLPINE | SICL | 0.25 |  |
| BeC | BELLPINE | SICL | 0.3 |  |
| BeD | BELLPINE | SICL | 0.25 |  |
| 13C | BLY | L | 0.3 | 0.9 |
| 4A | BLY | L | 0.3 | 0.9 |
| 4B | BLY | L | 0.3 | 0.9 |
| 99B | BLY | L | 0.3 | 0.9 |
| 8B | BORNSTEDT | SIL | 0.3 |  |
| 8C | BORNSTEDT | SIL | 0.25 |  |
| 8D | BORNSTEDT | SIL | 0.2 |  |
| 20 | BOYCE | SIL | 0.2 | 1.0 |
| 23A | BOYCE | SIL | 0.2 | 1.0 |
| 17C | BRADER | L | 0.2 | 0.9 |
| 44C | BRADER | L | 0.2 | 0.9 |
| 51C | BRADER | L | 0.2 | 0.9 |
| 102B | BRADER | L | 0.2 | 0.9 |
| 102D | BRADER | L | 0.15 | 0.9 |
| 29A | BRAND | SICL | 0.2 | 0.6 |
| 11B | BROCKMAN | CL | 0.15 | 0.45 |
| 11C | BROCKMAN | CL | 0.1 | 0.45 |
| 12B | BROCKMAN | CB-CL | 0.15 | 0.45 |
| 12D | BROCKMAN | CB-CL | 0.1 | 0.45 |
| 23A | BUCKBERT | SL | 0.35 | 1.5 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 3 | BULLY | SIL | 0.25 | 1.5 |
| 3A | BULLY | SIL | 0.25 | 1.5 |
| 751A | CALABAR | SIL | 0.15 |  |
| 5 | CALDER | SIL | 0.3 | 0.7 |
| 6A | CALIMUS | FSL | 0.5 | 1.5 |
| 6B | CALIMUS | FSL | 0.5 | 1.5 |
| 6C | CALIMUS | FSL | 0.45 | 1.5 |
| 7A | CALIMUS | L | 0.35 | 2.0 |
| 7B | CALIMUS | L | 0.35 | 2.0 |
| 7C | CALIMUS | L | 0.3 | 2.0 |
| 8D | CALIMUS | L | 0.3 | 2.0 |
| 51E | CALIMUS | L | 0.25 | 2.0 |
| 11 | CAMAS | GR-SL | 0.5 | 3.0 |
| 13 | CAMAS | GR-SL | 0.5 | 3.0 |
| 14 | CAMAS | GR-SL | 0.5 | 3.0 |
| 15 | CAMAS | GR-SL | 0.5 | 3.0 |
| 18 | CAMAS | GR-SL | 0.5 | 3.0 |
| 21A | CAMAS | SL | 0.45 | 2.0 |
| 22 | CAMAS | GR-SL | 0.5 | 3.0 |
| 22A | CAMAS | GR-SL | 0.5 | 3.0 |
| 23 | CAMAS | GR-SL | 0.5 | 3.0 |
| 34A | CAMAS | GRV-SL | 0.5 | 3.0 |
| Ca | CAMAS | GR-SL | 0.5 | 3.0 |
| 12B | CANTALA | SIL | 0.15 |  |
| 12C | CANTALA | SIL | 0.15 |  |
| 12D | CANTALA | SIL | 0.15 |  |
| 12E | CANTALA | SIL | 0.1 |  |
| 16B | CANTALA | SIL | 0.15 |  |
| 16C | CANTALA | SIL | 0.15 |  |
| 16D | CANTALA | SIL | 0.1 |  |
| 16E | CANTALA | SIL | 0.1 |  |
| 9A | CAPONA | L | 0.4 | 0.9 |
| 9B | CAPONA | L | 0.4 | 0.9 |
| 9C | CAPONA | L | 0.35 | 0.9 |
| 74B | CAPONA | L | 0.4 | 0.9 |
| 27B | CARNEY | C | 0.15 | 0.1 |
| 27D | CARNEY | C | 0.1 | 0.1 |
| 7 | CATHERINE | SIL | 0.3 | 3.0 |
| 21 | CATHERINE | SIL | 0.3 | 3.0 |
| 17A | CATHERINE | SIL | 0.3 | 3.0 |
| 35A | CATHERINE | SIL | 0.3 | 3.0 |
| 17A | CATHERINE VARIANT | SIL | 0.3 | 3.0 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 9B | CAZADERO | SICL | 0.3 |  |
| 9C | CAZADERO | SICL | 0.3 |  |
| 15B | CAZADERO | SICL | 0.3 |  |
| 15C | CAZADERO | SICL | 0.25 |  |
| 4A | CENCOVE | FSL | 0.65 | 4.0 |
| 4B | CENCOVE | FSL | 0.65 | 4.0 |
| 4C | CENCOVE | FSL | 0.6 | 4.0 |
| 4D | CENCOVE | FSL | 0.55 | 4.0 |
| 16 | CENTRAL POINT | SL | 0.4 | 2.0 |
| 31A | CENTRAL POINT | SL | 0.4 | 2.0 |
| 8C | CHEHALEM | SICL | 0.3 | 0.55 |
| 20C | CHEHALEM | SIL | 0.5 | 0.7 |
| CeC | CHEHALEM | SIL | 0.5 | 0.7 |
| CeC | CHEHALEM | SICL | 0.3 | 0.55 |
| 9 | CHEHALIS | SICL | 0.35 | 0.35 |
| 10 | CHEHALIS | SIL | 0.5 |  |
| 14 | CHEHALIS | SICL | 0.35 | 0.35 |
| 21 | CHEHALIS | SICL | 0.35 | 0.35 |
| 26 | CHEHALIS | SICL | 0.35 | 0.35 |
| 27 | CHEHALIS | SICL | 0.35 | 0.35 |
| Ch | CHEHALIS | SICL | 0.35 | 0.35 |
| Ck | CHEHALIS | SICL | 0.35 | 0.35 |
| 13B | CHENOWETH | L | 0.25 |  |
| 13C | CHENOWETH | L | 0.25 |  |
| 13D | CHENOWETH | L | 0.2 |  |
| 13E | CHENOWETH | L | 0.15 |  |
| 14B | CHERRYHILL | SIL | 0.2 |  |
| 14C | CHERRYHILL | SIL | 0.2 |  |
| 14D | CHERRYHILL | SIL | 0.15 |  |
| 14E | CHERRYHILL | SIL | 0.1 |  |
| 16D | CHERRYHILL | SIL | 0.15 |  |
| 45 | CHESNIMNUS | SIL | 0.3 |  |
| 46 | CHESNIMNUS | GR-L | 0.5 |  |
| 5A | CHILCOTT | SIL |  | 1.0 |
| 5B | CHILCOTT | SIL |  | 1.0 |
| 5C | CHILCOTT | SIL |  | 1.0 |
| 10 | CHILOQUIN | L | 0.4 | 0.9 |
| 33 | CHOCK | L | 0.3 | 0.9 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 17 | CLACKAMAS | SIL | 0.5 |  |
| 18 | CLACKAMAS | GR-L | 3 |  |
| 23 | CLACKAMAS | GR-SIL | 0.6 |  |
| Ck | CLACKAMAS | GR-L | 3 |  |
| 17B | CLAWSON | SL | 0.4 | 2.0 |
| 32B | CLAWSON | SL | 0.4 | 2.0 |
| 13 | CLOQUATO | SIL | 0.35 | 0.7 |
| 17 | CLOQUATO | SIL | 0.35 | 0.7 |
| 19 | CLOQUATO | SIL | 3 | 0.7 |
| 25 | CLOQUATO | SIL | 0.35 | 0.7 |
| 29 | CLOQUATO | SIL | 0.35 | 0.7 |
| 30 | CLOQUATO | SIL | 0.35 | 0.7 |
| Cm | CLOQUATO | SIL | 0.35 | 0.7 |
| 27A | CLOVKAMP | LS | 0.8 | 2.0 |
| 28A | CLOVKAMP | LS | 0.8 | 2.0 |
| 18 | COBURG | SICL | 0.35 | 0.6 |
| 19 | COBURG | SICL | 0.35 | 0.6 |
| 20 | COBURG | SICL | 0.35 | 0.6 |
| 26 | COBURG | SICL | 0.35 | 0.6 |
| 31 | COBURG | SICL | 0.35 | 0.6 |
| 32 | COBURG | SICL | 0.35 | 0.6 |
| 42B | COBURG | SICL | 0.35 | 0.6 |
| 43A | COBURG | SICL | 0.35 | 0.6 |
| Cn | COBURG | SICL | 0.35 | 0.6 |
| 33A | COKER | C | 0.15 | 0.1 |
| 33C | COKER | C | 0.1 | 0.1 |
| 34B | COLEMAN | L | 0.2 | 0.9 |
| 20 | CONCORD | SIL | 0.25 | 0.7 |
| 21 | CONCORD | SIL | 0.25 | 0.7 |
| 27 | CONCORD | SIL | 0.25 | 0.7 |
| Co | CONCORD | SIL | 0.25 | 0.7 |
| Co | CONCORD | SIL | 0.25 | 0.7 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 2D | CONDON | SIL | 0.15 |  |
| 3D | CONDON | SIL | 0.15 |  |
| 5B | CONDON | SIL | 0.15 |  |
| 5C | CONDON | SIL | 0.15 |  |
| 17B | CONDON | SIL | 0.15 |  |
| 17C | CONDON | SIL | 0.15 |  |
| 18B | CONDON | SIL | 0.15 |  |
| 18C | CONDON | SIL | 0.15 |  |
| 18D | CONDON | SIL | 0.1 |  |
| 21D | CONDON | SIL | 0.1 |  |
| 370B | CONDON | SIL | 0.15 |  |
| 460D | CONDON | SIL | 0.1 |  |
| 461D | CONDON | SIL | 0.1 |  |
| BcC | CONDON | SIL | 0.15 |  |
| CnC | CONDON | SIL | 0.15 |  |
| CoC | CONDON | SIL | 0.15 |  |
| 12 | COQUILLE | SIL | 0.4 | 0.5 |
| 12A | COQUILLE | SIL | 0.4 | 0.5 |
| 13A | COQUILLE | SIL | 0.4 | 0.5 |
| 46A | COQUILLE | SIL | 0.4 | 0.5 |
| Co | COQUILLE | SIL | 0.4 | 0.5 |
| 13A | COQUILLE VARIANT | SIL | 0.4 | 0.5 |
| 10A | COUGHANOUR | SIL | 0.3 |  |
| 10B | COUGHANOUR | SIL | 0.3 |  |
| 10C | COUGHANOUR | SIL | 0.25 |  |
| CrB | COURT | SL | 0.35 |  |
| 29 | COURTNEY | GR-SICL | 0.25 | 0.35 |
| 34 | COURTNEY | GR-SICL | 0.25 | 0.35 |
| Cu | COURTNEY | GR-SICL | 0.25 | 0.35 |
| 6B | COURTROCK | L | 0.35 |  |
| 40B | COURTROCK | L | 0.35 |  |
| 42D | COURTROCK | L | 0.25 |  |
| 430B | COURTROCK | L | 0.35 |  |
| 431D | COURTROCK | L | 0.25 |  |
| 14 | COVE | C | 0.1 | 0.1 |
| 22 | COVE | SICL | 0.15 | 0.3 |
| 35A | COVE | C | 0.1 | 0.1 |
| Cv | COVE | C | 0.1 | 0.1 |
| 13A | CRUME | L | 0.4 | 0.9 |
| 13B | CRUME | L | 0.4 | 0.9 |
| 14B | CRUME VARIANT | SL | 0.5 | 1.5 |
| 182C | CUPPER | SIL | 0.35 |  |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 760A | DAMON | SICL | 0.35 |  |
| 765B | DAMON | SICL | 0.35 |  |
| 43B | DAROW | SICL | 0.15 | 0.35 |
| 43D | DAROW | SICL | 0.1 | 0.35 |
| 43E | DAROW | SICL | 0.1 | 0.35 |
| 15 | DAYTON | SIL | 0.25 | 0.7 |
| 16 | DAYTON | SIL | 0.25 | 0.7 |
| 25 | DAYTON | SIL | 0.25 | 0.7 |
| 29 | DAYTON | SIL | 0.25 | 0.7 |
| 33 | DAYTON | SIL | 0.25 | 0.7 |
| 38 | DAYTON | SIL | 0.25 | 0.7 |
| Da | DAYTON | SIL | 0.25 | 0.7 |
| Dc | DAYTON | SIL | 0.2 | 0.7 |
| 9 | DAYVILLE | SIL | 0.3 | 1.0 |
| 9P | DAYVILLE | SIL | 0.3 | 1.0 |
| 50A | DAYVILLE | SIL | 0.3 | 1.0 |
| 270A | DAYVILLE | SIL | 0.3 | 1.0 |
| 17C | DEBENGER | L | 0.4 | 0.9 |
| 27C | DEBENGER | L | 0.4 | 0.9 |
| 44C | DEBENGER | L | 0.4 | 0.9 |
| 51C | DEBENGER | L | 0.4 | 0.9 |
| 31A | DESCHUTES | SL | 0.3 | 2.0 |
| 31B | DESCHUTES | SL | 0.3 | 2.0 |
| 32A | DESCHUTES | SL | 0.3 | 2.0 |
| 32Am | DESCHUTES | ASHY-SL | 0.3 | 2.0 |
| 33B | DESCHUTES | SL | 0.3 | 2.0 |
| 34C | DESCHUTES | SL | 0.25 | 2.0 |
| 35B | DESCHUTES | SL | 0.3 | 2.0 |
| 35Bm | DESCHUTES | ASHY-SL | 0.3 | 2.0 |
| 105C | DESCHUTES | SL | 0.3 | 2.0 |
| 140Bm | DESCHUTES | ASHY-SL | 0.3 | 2.0 |
| 142Bm | DESCHUTES | ASHY-SL | 0.3 | 2.0 |
| 36A | DESKAMP | LS | 0.8 | 4.0 |
| 36B | DESKAMP | LS | 0.8 | 4.0 |
| 38B | DESKAMP | LS | 0.8 | 4.0 |
| 37B | DESKAMP | SL | 0.5 | 2.0 |
| 59Cm | DESKAMP | ASHY-LS | 0.8 | 4.0 |
| 17A | DETER | CL | 0.3 | 0.5 |
| 17B | DETER | CL | 0.3 | 0.5 |
| 64B | DETER | L | 0.3 | 0.5 |
| 64C | DETER | L | 0.3 | 0.5 |
| 65B | DETER | L | 0.3 | 0.5 |
| 65C | DETER | L | 0.3 | 0.5 |
| 34 | DILMAN | SICL | 0.3 | 0.35 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 18A | DODES | L | 0.3 | 0.9 |
| 18B | DODES | L | 0.3 | 0.9 |
| 73B | DREWS | L | 0.35 | 3.0 |
| 73C | DREWS | L | 0.35 | 3.0 |
| 73E | DREWS | L | 0.3 | 3.0 |
| 74C | DREWS | CB-L | 0.35 | 3.0 |
| 75B | DREWS | L | 0.35 | 3.0 |
| 76B | DREWSGAP | L | 0.35 | 3.0 |
| 76C | DREWSGAP | L | 0.35 | 3.0 |
| 22B | DUFUR | SIL | 0.3 |  |
| 22C | DUFUR | SIL | 0.3 |  |
| 22D | DUFUR | SIL | 0.25 |  |
| 15B | EILERTSEN | SIL | 0.45 | 0.2 |
| 17A | EILERTSEN | SIL | 0.45 | 0.2 |
| 17B | EILERTSEN | SIL | 0.45 | 0.2 |
| 20 | EILERTSEN | SIL | 0.45 | 0.2 |
| 46 | EILERTSEN | SIL | 0.45 | 0.2 |
| 59 | EILERTSEN | SIL | 0.45 | 0.2 |
| 106B | EILERTSEN | SIL | 0.45 | 0.2 |
| 24B | ELLISFORDE | SIL | 0.25 |  |
| 24C | ELLISFORDE | SIL | 0.25 |  |
| 25C | ELLISFORDE | SIL | 0.25 |  |
| 25C | ELLISFORDE | VFSL | 0.5 |  |
| 11 | ENDERSBY | FSL | 0.75 |  |
| 24 | ENDERSBY | L | 0.35 |  |
| 11A | ENDERSBY | FSL | 0.75 |  |
| 12A | ENDERSBY | FSL | 0.75 |  |
| 44B | ERA | SL | 0.35 |  |
| 45A | ERA | SL | 0.35 |  |
| ErB | ERA | SL | 0.35 |  |
| 23A | EVANS | L | 0.4 | 4.0 |
| 34 | EVANS | L | 0.4 | 4.0 |
| 55A | EVANS | L | 0.4 | 4.0 |
| 78A | EVANS | L | 0.4 | 4.0 |
| 8A | FELTHAM | LFS | 0.85 | 4.0 |
| 8B | FELTHAM | LFS | 0.85 | 4.0 |
| 8C | FELTHAM | LFS | 0.8 | 4.0 |
| 9B | FELTHAM | SL | 0.75 | 2.0 |
| 9C | FELTHAM | SL | 0.7 | 2.0 |
| 9D | FELTHAM | SL | 0.65 | 2.0 |
| 10 | FELTHAM VARIANT | LFS | 0.85 | 4.0 |
| 10A | FELTHAM VARIANT | LFS | 0.85 | 4.0 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 38A | FOEHLIN | GR-L | 0.3 | 1.0 |
| 38C | FOEHLIN | GR-L | 0.25 | 1.0 |
| 61A | FOEHLIN | GR-L | 0.3 | 1.0 |
| 81A | FOEHLIN | GR-L | 0.3 | 1.0 |
| 81C | FOEHLIN | GR-L | 0.25 | 1.0 |
| 19A | FORDNEY | LFS | 1 | 4.0 |
| 19C | FORDNEY | LFS | 0.95 | 4.0 |
| 20A | FORDNEY | LFS | 1 | 4.0 |
| 11A | FROHMAN | SIL | 0.25 | 1.5 |
| 11B | FROHMAN | SIL | 0.25 | 1.5 |
| 11C | FROHMAN | SIL | 0.2 | 1.5 |
| 11D | FROHMAN | SIL | 0.2 | 1.5 |
| 11E | FROHMAN | SIL | 0.15 | 1.5 |
| 11F | FROHMAN | GR-SIL | 0.15 | 1.5 |
| 12A | GARBUTT | SIL | 0.25 | 0.3 |
| 12B | GARBUTT | SIL | 0.25 | 0.3 |
| 12C | GARBUTT | SIL | 0.2 | 0.3 |
| 12D | GARBUTT | SIL | 0.2 | 0.3 |
| 24 | GARDINER | SL | 1.3 | 3.0 |
| 55B | GOODRICH | GR-L | 0.3 | 2.0 |
| 38B | GOSNEY | ST-LS | 0.3 | 2.0 |
| 59Cm | GOSNEY | ST-ASHY-LS | 0.3 | 2.0 |
| 13A | GREENLEAF | SIL | 0.2 | 0.3 |
| 13B | GREENLEAF | SIL | 0.2 | 0.3 |
| 76A | GREGORY | SICL | 0.15 | 0.35 |
| 16A | HACK | L | 0.3 |  |
| 16B | HACK | L | 0.3 |  |
| 16C | HACK | L | 0.25 |  |
| 17C | HACK | GR-L | 0.25 |  |
| 70A | HACK | L | 0.3 |  |
| 71B | HACK | L | 0.3 |  |
| 74C | HACK | L | 0.25 |  |
| 76C | HACK | GR-L | 0.25 |  |
| 230A | HACK | L | 0.3 |  |
| 230B | HACK | L | 0.3 |  |
| 63A | HALFWAY | C | 0.3 | 3.0 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 14 | HARANA | SIL | 0.2 | 0.5 |
| 14A | HARANA | SIL | 0.2 | 0.5 |
| 15 | HARANA | SICL | 0.2 | 0.5 |
| 15A | HARANA | SICL | 0.2 | 0.5 |
| 15B | HARANA | SICL | 0.2 | 0.5 |
| 16 | HARANA | SICL | 0.2 | 0.5 |
| 16A | HARANA | SICL | 0.2 | 0.5 |
| 22A | HARRIMAN | LFS | 0.5 | 2.0 |
| 23A | HARRIMAN | L | 0.3 | 1.5 |
| 23B | HARRIMAN | L | 0.3 | 1.5 |
| 23C | HARRIMAN | L | 0.25 | 1.5 |
| 109B | HARRIMAN | L | 0.3 | 1.5 |
| 109C | HARRIMAN | L | 0.25 | 1.5 |
| 29C | HAZELAIR | SIL | 0.3 | 0.7 |
| 29D | HAZELAIR | SIL | 0.25 | 0.7 |
| 35C | HAZELAIR | SICL | 0.25 | 0.35 |
| 43B | HAZELAIR | SICL | 0.25 | 0.35 |
| 43C | HAZELAIR | SICL | 0.25 | 0.35 |
| 43D | HAZELAIR | SICL | 0.2 | 0.35 |
| 52B | HAZELAIR | SICL | 0.25 | 0.35 |
| 52D | HAZELAIR | SICL | 0.2 | 0.35 |
| 127C | HAZELAIR | SICL | 0.25 | 0.35 |
| HaB | HAZELAIR | SIL | 0.2 | 0.7 |
| HaC | HAZELAIR | SIL | 0.25 | 0.7 |
| HaD | HAZELAIR | SIL | 0.15 | 0.7 |
| HcB | HAZELAIR | SICL | 0.25 | 0.35 |
| HcD | HAZELAIR | SICL | 0.2 | 0.35 |
| HeC | HAZELAIR | SIL | 0.25 | 0.7 |
| HeD | HAZELAIR | SIL | 0.2 | 0.7 |
| 25 | HENLEY | LFS | 1 | 2.0 |
| 26 | HENLEY | L | 0.4 | 2.0 |
| 27 | HENLEY | SL | 0.8 | 1.5 |
| 28 | HENLEY | L | 0.4 | 2.0 |
| 40 | HENLEY | L | 0.4 | 2.0 |
| 29 | HENLEY VARIANT | L | 0.4 | 2.0 |
| 1A | HERMISTON | SIL | 0.25 | 1.0 |
| 11 | HERMISTON | SIL | 0.25 | 1.0 |
| 12A | HERMISTON | SIL | 0.25 | 1.0 |
| 13A | HERMISTON | SIL | 0.25 | 1.0 |
| 26 | HERMISTON | SIL | 0.25 | 1.0 |
| 39A | HERMISTON | SIL | 0.25 | 1.0 |
| 33 | HOLCOMB | SIL | 0.3 | 0.7 |
| 46 | HOLCOMB | SIL | 0.3 | 0.7 |
| 56 | HOLCOMB | SICL | 0.2 | 0.35 |
| Ho | HOLCOMB | SIL | 0.3 | 0.7 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 12A | HOOD | L | 0.6 |  |
| 12B | HOOD | L | 0.6 |  |
| 12C | HOOD | L | 0.55 |  |
| 12D | HOOD | L | 0.5 |  |
| 23 | HOOPAL | FSL | 0.5 | 2.0 |
| 75A | HOOPAL | SIL | 0.3 | 0.7 |
| 24 | HOOPAL VARIANT | SIL | 0.3 | 0.7 |
| 31 | HOSLEY | L | 0.1 | 0.1 |
| 25 | HOT LAKE | SIL | 0.25 | 0.7 |
| 29 | HOUSTAKE | ASHY-SL | 0.3 | 2.0 |
| 33B | HOUSTAKE | SL | 0.3 | 2.0 |
| 65A | HOUSTAKE | SL | 0.3 | 2.0 |
| 66A | HOUSTAKE | SL | 0.3 | 2.0 |
| 67A | HOUSTAKE | SL | 0.3 | 2.0 |
| 85A | HOXIE | SIL | 0.2 | 0.7 |
| 86C | HUKILL | GR-L | 0.2 | 1.0 |
| 26B | HUTCHINSON | SIL | 0.3 |  |
| 26C | HUTCHINSON | SIL | 0.25 |  |
| 21B | IRRIGON | FSL | 0.25 |  |
| 21C | IRRIGON | FSL | 0.25 |  |
| 46 | JEROME | SL | 0.4 | 0.3 |
| 31 | JETT | SIL | 0.25 | 1.0 |
| 45A | JETT | SIL | 0.25 | 1.0 |
| 84D | JETT | SIL | 0.2 | 1.0 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 23B | JORY | SICL | 0.3 | 0.35 |
| 23C | JORY | SICL | 0.25 | 0.35 |
| 23D | JORY | SICL | 0.2 | 0.35 |
| 23E | JORY | SICL | 0.15 | 0.35 |
| 35C | JORY | SIL | 0.4 | 0.7 |
| 35D | JORY | SIL | 0.35 | 0.7 |
| 35E | JORY | SIL | 0.3 | 0.7 |
| 36C | JORY | SICL | 0.3 | 0.35 |
| 36D | JORY | SICL | 0.25 | 0.35 |
| 36E | JORY | SICL | 0.2 | 0.35 |
| 37D | JORY | SICL | 0.25 | 0.35 |
| 45B | JORY | SICL | 0.3 | 0.35 |
| 45C | JORY | SICL | 0.25 | 0.35 |
| 45D | JORY | SICL | 0.2 | 0.35 |
| 46B | JORY | ST-SIL | 0.4 | 0.7 |
| 46C | JORY | ST-SIL | 0.35 | 0.7 |
| 46D | JORY | ST-SIL | 0.3 | 0.7 |
| 51C | JORY | SICL | 0.3 | 0.35 |
| 51D | JORY | SICL | 0.25 | 0.35 |
| 51E | JORY | SICL | 0.2 | 0.35 |
| 63C | JORY | SICL | 0.3 | 0.35 |
| 63D | JORY | SICL | 0.25 | 0.35 |
| 63E | JORY | SICL | 0.2 | 0.35 |
| 113C | JORY | SICL | 0.3 | 0.35 |
| 113D | JORY | SICL | 0.25 | 0.35 |
| 113E | JORY | SICL | 0.2 | 0.35 |
| 249E | JORY | SICL | 0.2 | 0.35 |
| JoB | JORY | SICL | 0.3 | 0.35 |
| JoC | JORY | SICL | 0.25 | 0.35 |
| JoD | JORY | SICL | 0.2 | 0.35 |
| JoE | JORY | SICL | 0.15 | 0.35 |
| JrB | JORY | CL | 0.2 | 0.45 |
| JrC | JORY | CL | 0.15 | 0.45 |
| JrD | JORY | CL | 0.15 | 0.45 |
| JRE | JORY | SICL | 0.15 | 0.35 |
| JrE | JORY | CL | 0.1 | 0.45 |
| 40C | KAHLER | SIL | 0.35 | 0.7 |
| 510D | KAHLER | SIL | 0.35 | 0.7 |
| 570C | KAHLER | SIL | 0.35 | 0.7 |
| 36C | KEATING | SIL | 0.3 | 0.5 |
| 73C | KEATING | SIL | 0.3 | 0.5 |
| 131C | KEATING | SIL | 0.3 | 0.5 |
| 52 | KERBY | L | 0.4 | 0.9 |
| 97A | KERBY | L | 0.4 | 0.9 |
| 98A | KERBY | L | 0.4 | 0.9 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 10A | KIMBERLY | SL | 0.3 | 2.0 |
| 13 | KIMBERLY | FSL | 0.6 | 1.5 |
| 18 | KIMBERLY | FSL | 0.6 | 1.5 |
| 18A | KIMBERLY | FSL | 0.6 | 1.5 |
| 20A | KIMBERLY | SL | 0.3 | 2.0 |
| 22 | KIMBERLY | FSL | 0.6 | 1.5 |
| 42A | KIMBERLY | FSL | 0.6 | 1.5 |
| 43A | KIMBERLY | SIL | 0.3 | 2.0 |
| 170A | KIMBERLY | SL | 0.3 | 2.0 |
| 32 | KIRK | L | 0.3 | 0.9 |
| 33 | KIRK | L | 0.3 | 0.9 |
| 34 | KLAMATH | SIC | 0.3 | 0.35 |
| 99A | KLAMATH | SIL | 0.2 | 0.7 |
| 35 | KLAMATH VARIANT | CL | 0.3 | 0.45 |
| 26B | KOEHLER | LFS | 0.8 | 2.0 |
| 26C | KOEHLER | LFS | 0.8 | 2.0 |
| 47B | KOEHLER | LFS | 0.8 | 2.0 |
| 100A | KUBLI | L | 0.2 | 0.9 |
| 100B | KUBLI | L | 0.15 | 0.9 |
| 36 | LA GRANDE | SIL | 0.25 | 1.0 |
| 37 | LA GRANDE | SICL | 0.2 | 0.35 |
| 63 | LA GRANDE | SIL | 0.25 | 1.0 |
| 80A | LA GRANDE | SIL | 0.25 | 1.0 |
| 91A | LA GRANDE | SIL | 0.25 | 1.0 |
| 90B | LADD | L | 0.25 | 1.5 |
| 71A | LAFOLLETTE | SL | 0.3 | 1.5 |
| 71B | LAFOLLETTE | SL | 0.3 | 1.5 |
| 36 | LAKEVIEW | SICL | 0.25 | 1.5 |
| 124A | LAKEVIEW | L | 0.25 | 1.0 |
| 125A | LAKEVIEW | SICL | 0.25 | 1.5 |
| 126A | LAKEVIEW | SICL | 0.25 | 1.5 |
| 127A | LAKEVIEW | SICL | 0.25 | 1.5 |
| 128A | LAKEVIEW | SICL | 0.25 | 1.5 |
| 27 | LAKI | FSL | 0.75 | 1.5 |
| 28 | LAKI | L | 0.3 | 2.0 |
| 37 | LAKI | FSL | 0.75 | 1.5 |
| 38 | LAKI | L | 0.3 | 2.0 |
| 39 | LAKI | L | 0.3 | 2.0 |
| 40 | LAKI | L | 0.3 | 2.0 |
| 41C | LAKI VARIANT | L | 0.3 | 2.0 |
| 64 | LAMONTA | GR-L | 0.35 | 0.9 |
| LaC | LAMONTA | CB-L | 0.35 | 0.9 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 101E | LANGELLAIN | L | 0.15 | 0.9 |
| 102B | LANGELLAIN | L | 0.25 | 0.9 |
| 102D | LANGELLAIN | L | 0.2 | 0.9 |
| 103E | LANGELLAIN | L | 0.15 | 0.9 |
| 34 | LANGLOIS | SICL | 0.5 | 0.4 |
| 35 | LANGLOIS | PT-SICL | 0.5 | 0.4 |
| 164A | LANGLOIS | SICL | 0.5 | 0.4 |
| 46 | LATHER | MUCK | 0.6 | 1.5 |
| 28B | LAURELWOOD | SIL | 0.3 | 0.7 |
| 28C | LAURELWOOD | SIL | 0.25 | 0.7 |
| 28D | LAURELWOOD | SIL | 0.2 | 0.7 |
| 28E | LAURELWOOD | SIL | 0.15 | 0.7 |
| 29E | LAURELWOOD | SIL | 0.15 | 0.7 |
| 54B | LAURELWOOD | SIL | 0.3 | 0.7 |
| 54C | LAURELWOOD | SIL | 0.25 | 0.7 |
| 54D | LAURELWOOD | SIL | 0.2 | 0.7 |
| LuC | LAURELWOOD | SIL | 0.25 | 0.7 |
| LuD | LAURELWOOD | SIL | 0.2 | 0.7 |
| LUE | LAURELWOOD | SIL | 0.15 | 0.7 |
| LuE | LAURELWOOD | SIL | 0.15 | 0.7 |
| 380B | LEGLER | SIL | 0.3 | 0.7 |
| 47A | LOBERT | SL | 1 | 1.5 |
| 47B | LOBERT | SL | 1 | 1.5 |
| 48A | LOBERT | L | 0.5 | 0.9 |
| 48B | LOBERT | L | 0.5 | 0.9 |
| 48C | LOBERT | L | 0.45 | 0.9 |
| 48D | LOBERT | L | 0.4 | 0.9 |
| 106C | LOBERT | SL | 0.9 | 2.0 |
| 138C | LOBERT | L | 0.45 | 0.9 |
| 49C | LORELLA | L | 0.3 | 0.9 |
| 3B | MADRAS | L | 0.25 | 0.45 |
| 3C | MADRAS | L | 0.2 | 0.45 |
| 77 | MADRAS | L | 0.25 | 0.5 |
| 78 | MADRAS | L | 0.25 | 0.5 |
| 86A | MADRAS | SL | 0.3 | 0.6 |
| 86B | MADRAS | SL | 0.3 | 0.6 |
| 87A | MADRAS | L | 0.25 | 0.45 |
| 87B | MADRAS | L | 0.25 | 0.45 |
| 87C | MADRAS | L | 0.2 | 0.45 |
| 610B | MADRAS | CB-L | 0.25 | 0.45 |
| MaC | MADRAS | L | 0.2 | 0.45 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 45 | MALABON | SICL | 0.3 | 0.35 |
| 46 | MALABON | SICL | 0.3 | 0.35 |
| 55 | MALABON | SICL | 0.3 | 0.35 |
| 63 | MALABON | SICL | 0.3 | 0.35 |
| 75 | MALABON | SICL | 0.3 | 0.35 |
| 76 | MALABON | SICL | 0.3 | 0.35 |
| 144A | MALABON | SICL | 0.3 | 0.35 |
| 145A | MALABON | SICL | 0.3 | 0.35 |
| Ma | MALABON | SICL | 0.3 | 0.35 |
| 64 | MALABON VARIANT | L | 0.5 | 0.9 |
| 23A | MALHEUR | SIL | 0.25 | 0.49 |
| 23B | MALHEUR | SIL | 0.25 | 0.49 |
| 23C | MALHEUR | SIL | 0.2 | 0.49 |
| 53 | MALIN | CL | 0.15 | 0.4 |
| 152A | MALIN | SICL | 0.3 | 0.35 |
| 54 | MALIN VARIANT | SIL | 0.3 | 0.7 |
| 53B | MANITA | L | 0.2 | 0.9 |
| 53C | MANITA | L | 0.15 | 0.9 |
| 53D | MANITA | L | 0.1 | 0.9 |
| 108B | MANITA | L | 0.2 | 0.9 |
| 108D | MANITA | L | 0.15 | 0.9 |
| 790C | MARSDEN | SIL | 0.25 | 0.7 |
| 4C | MAUPIN | L | 0.25 | 1.0 |
| 8 | MAUPIN | SIL | 0.3 | 1.0 |
| 32A | MAUPIN | L | 0.3 | 1.0 |
| 32B | MAUPIN | L | 0.3 | 1.0 |
| 80 | MAUPIN | SIL | 0.3 | 1.0 |
| 33 | MAUPIN VARIANT | L | 0.3 | 1.0 |
| 48A | MCALPIN | SICL | 0.15 | 0.35 |
| 48B | MCALPIN | SICL | 0.15 | 0.35 |
| 66B | MCALPIN | SICL | 0.15 | 0.35 |
| 78 | MCALPIN | SICL | 0.15 | 0.35 |
| MaA | MCALPIN | SICL | 0.15 | 0.35 |
| MaB | MCALPIN | SICL | 0.15 | 0.35 |
| Mn | MCALPIN | SICL | 0.15 | 0.35 |
| 19A | MCLOUGHLIN | SIL | 0.25 | 0.8 |
| 19B | MCLOUGHLIN | SIL | 0.25 | 0.8 |
| 19C | MCLOUGHLIN | SIL | 0.2 | 0.8 |
| 360B | MCLOUGHLIN | SICL | 0.22 | 0.8 |
| 364D | MCLOUGHLIN | SICL | 0.2 | 0.8 |
| 120B | MEDCO | CL | 0.15 | 0.4 |
| 120C | MEDCO | CL | 0.1 | 0.4 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 127A | MEDFORD | SICL | 0.3 | 0.35 |
| 128B | MEDFORD | CL | 0.15 | 0.4 |
| 15 | METOLIUS | ASHY-SL | 0.35 | 2.0 |
| MtB | METOLIUS | SL | 0.35 | 2.0 |
| 28 | MOAG | SICL | 0.35 | 0.35 |
| 58A | MODOC | FSL | 0.4 | 2.0 |
| 58B | MODOC | FSL | 0.4 | 2.0 |
| 58C | MODOC | FSL | 0.35 | 2.0 |
| 3D | MORROW | SIL | 0.15 | 0.7 |
| 18B | MORROW | SIL | 0.15 | 0.7 |
| 18C | MORROW | SIL | 0.15 | 0.7 |
| 31B | MORROW | SIL | 0.15 | 0.7 |
| 31C | MORROW | SIL | 0.15 | 0.7 |
| 51B | MORROW | SIL | 0.15 | 0.7 |
| 52C | MORROW | SIL | 0.15 | 0.7 |
| 56B | MORROW | SIL | 0.15 | 0.7 |
| 56C | MORROW | SIL | 0.15 | 0.7 |
| 56D | MORROW | SIL | 0.15 | 0.7 |
| 40 | NEHALEM | SIL | 0.45 | 0.2 |
| 40A | NEHALEM | SIL | 0.45 | 0.2 |
| 51A | NEHALEM | SIL | 0.45 | 0.2 |
| 88 | NEHALEM | SIL | 0.45 | 0.2 |
| 183A | NEHALEM | SIL | 0.45 | 0.2 |
| Ne | NEHALEM | SIL | 0.45 | 0.2 |
| NeB | NEHALEM | SIL | 0.45 | 0.2 |
| 41 | NESTUCCA | SIL | 0.5 | 0.4 |
| 42 | NESTUCCA | SIL | 0.5 | 0.4 |
| 46A | NESTUCCA | SIL | 0.5 | 0.4 |
| 52A | NESTUCCA | SIL | 0.5 | 0.4 |
| 93 | NESTUCCA | SIL | 0.5 | 0.4 |
| 162A | NESTUCCA | SIL | 0.5 | 0.4 |
| 185A | NESTUCCA | SIL | 0.5 | 0.4 |
| Ns | NESTUCCA | SIL | 0.5 | 0.4 |
| NsA | NESTUCCA | SIL | 0.5 | 0.4 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 15 | NEWBERG | FSL | 0.55 | 4.0 |
| 23A | NEWBERG | FSL | 0.55 | 4.0 |
| 34A | NEWBERG | FSL | 0.55 | 4.0 |
| 53 | NEWBERG | FSL | 0.55 | 4.0 |
| 54 | NEWBERG | L | 0.55 | 4.0 |
| 57 | NEWBERG | FSL | 0.55 | 4.0 |
| 67 | NEWBERG | FSL | 0.55 | 4.0 |
| 68 | NEWBERG | L | 0.55 | 4.0 |
| 73 | NEWBERG | FSL | 0.55 | 4.0 |
| 95 | NEWBERG | FSL | 0.55 | 4.0 |
| 96 | NEWBERG | L | 0.55 | 4.0 |
| 97 | NEWBERG | FSL | 0.55 | 4.0 |
| 133A | NEWBERG | FSL | 0.55 | 4.0 |
| 164A | NEWBERG | FSL | 0.55 | 4.0 |
| 165A | NEWBERG | LS | 0.55 | 4.0 |
| Ng | NEWBERG | FSL | 0.55 | 4.0 |
| Nm | NEWBERG | L | 0.55 | 4.0 |
| Nu | NEWBERG | FSL | 0.55 | 4.0 |
| Nw | NEWBERG | SIL | 0.55 | 4.0 |
| 43C | NORTH POWDER | L | 0.35 | 1.0 |
| 114C | NORTH POWDER | L | 0.35 | 1.0 |
| 21A | NYSSA | SIL | 0.25 | 1.0 |
| 21B | NYSSA | SIL | 0.25 | 1.0 |
| 21C | NYSSA | SIL | 0.2 | 1.0 |
| 21D | NYSSA | SIL | 0.2 | 1.0 |
| 21E | NYSSA | SIL | 0.15 | 1.0 |
| 22A | NYSSA | SIL | 0.25 | 1.0 |
| 22B | NYSSA | SIL | 0.25 | 1.0 |
| 22C | NYSSA | SIL | 0.2 | 1.0 |
| 22D | NYSSA | SIL | 0.2 | 1.0 |
| 22E | NYSSA | SIL | 0.15 | 1.0 |
| 23A | NYSSA | SIL | 0.25 | 1.0 |
| 23B | NYSSA | SIL | 0.25 | 1.0 |
| 23C | NYSSA | SIL | 0.2 | 1.0 |
| 16B | OAK GROVE | L | 0.7 | 0.9 |
| 16C | OAK GROVE | L | 0.65 | 0.9 |
| 16D | OAK GROVE | L | 0.6 | 0.9 |
| 16E | OAK GROVE | L | 0.55 | 0.9 |
| 169C | OAKLAND | SIL | 0.3 | 0.7 |
| 170C | OAKLAND | SIL | 0.3 | 0.7 |
| 170D | OAKLAND | SIL | 0.3 | 0.7 |
| 236C | OAKLAND | SIL | 0.3 | 0.7 |
| 123 | OCHOCO | ASHY-SL | 0.35 | 2.0 |
| 133 | OCHOCO | ASHY-SL | 0.35 | 2.0 |
| 34 | ONTKO | SICL | 0.3 | 0.35 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 35 | ONYX | SIL | 0.3 | 2.0 |
| 63A | ONYX | SIL | 0.3 | 2.0 |
| 24 | OTOOLE | SIL | 0.3 | 4.0 |
| 24A | OTOOLE | SIL | 0.3 | 4.0 |
| 25A | OWYHEE | SIL | 0.25 | 1.5 |
| 25B | OWYHEE | SIL | 0.25 | 1.5 |
| 25C | OWYHEE | SIL | 0.2 | 1.5 |
| 25D | OWYHEE | SIL | 0.2 | 1.5 |
| 25E | OWYHEE | SIL | 0.15 | 1.5 |
| 30B | OXBOW | STV-SICL | 0.15 | 0.35 |
| 90B | OXBOW | STV-SICL | 0.15 | 0.35 |
| 121C | OZAMIS | CL, SIC | 0.25 | 1.5 |
| 139A | PADIGAN | C | 0.1 | 0.1 |
| 17B | PARKDALE | L | 0.55 | 0.9 |
| 17C | PARKDALE | L | 0.5 | 0.9 |
| 17D | PARKDALE | L | 0.45 | 0.9 |
| 17E | PARKDALE | L | 0.4 | 0.9 |
| 35 | PEDIGO | SIL | 0.15 | 2.0 |
| 36 | PEDIGO | SIL | 0.15 | 2.0 |
| 22A | PEDIGO | SIL | 0.15 | 2.0 |
| 65A | PEDIGO | LFS | 0.75 | 2.0 |
| 66A | PEDIGO | SIL | 0.15 | 2.0 |
| 141A | PHOENIX | C | 0.1 | 0.1 |
| 67B | PILOT ROCK | SIL | 0.25 | 0.7 |
| 67C | PILOT ROCK | SIL | 0.25 | 0.7 |
| 61 | PIT | SIC | 0.2 | 4.0 |
| 202A | PIT | SICL | 0.2 | 4.0 |
| 203A | PIT | SIC | 0.2 | 4.0 |
| 204A | PIT | SIC | 0.2 | 4.0 |
| 98A | PLAINVIEW | SL | 0.35 | 2.0 |
| 98B | PLAINVIEW | SL | 0.35 | 2.0 |
| 62 | POE | LFS | 1 | 1.5 |
| 63 | POE | FSL | 0.6 | 1.5 |
| 64 | POE VARIANT | LFS | 1.2 | 2.0 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 61B | POLLARD | L | 0.2 | 0.9 |
| 61C | POLLARD | L | 0.15 | 0.9 |
| 61D | POLLARD | L | 0.15 | 0.9 |
| 61E | POLLARD | L | 0.1 | 0.9 |
| 63F | POLLARD | GR-L | 0.1 | 0.9 |
| 73E | POLLARD | L | 0.1 | 0.9 |
| 90E | POLLARD | L | 0.1 | 0.9 |
| 91E | POLLARD | L | 0.1 | 0.9 |
| 149B | POLLARD | L | 0.2 | 0.9 |
| 149D | POLLARD | L | 0.15 | 0.9 |
| 192E | POLLARD | GR-L | 0.1 | 0.9 |
| 14 | POWDER | SIL | 0.35 | 1.0 |
| 26 | POWDER | SIL | 0.35 | 1.0 |
| 27 | POWDER | SIL | 0.35 | 1.0 |
| 34 | POWDER | SIL | 0.35 | 1.0 |
| 72A | POWDER | SIL | 0.35 | 1.0 |
| 124 | POWDER | L | 0.5 | 0.9 |
| 123 | PRINEVILLE | ASHY-SL | 0.35 | 2.0 |
| 133 | PRINEVILLE | ASHY-SL | 0.35 | 2.0 |
| 151C | PROVIG | GRV-L | 0.3 | 1.5 |
| 37A | QUATAMA | L | 0.3 | 0.9 |
| 37A | QUATAMA | L | 0.3 | 0.9 |
| 37B | QUATAMA | L | 0.3 | 0.9 |
| 37C | QUATAMA | L | 0.3 | 0.9 |
| 37D | QUATAMA | L | 0.2 | 0.9 |
| 38A | QUATAMA | L | 0.3 | 0.9 |
| 40A | QUATAMA | SIL | 0.3 | 0.7 |
| 40B | QUATAMA | SIL | 0.3 | 0.7 |
| 40C | QUATAMA | SIL | 0.25 | 0.7 |
| 54B | QUATAMA | L | 0.3 | 0.9 |
| 54C | QUATAMA | L | 0.25 | 0.9 |
| 71A | QUATAMA | L | 0.3 | 0.9 |
| 71B | QUATAMA | L | 0.3 | 0.9 |
| 71C | QUATAMA | L | 0.25 | 0.9 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 28C | QUINCY | FS | 0.75 | 4.0 |
| 39C | QUINCY | FS | 0.8 | 4.0 |
| 28A | QUINCY | LFS | 0.8 | 4.0 |
| 28B | QUINCY | LFS | 0.8 | 4.0 |
| 29D | QUINCY | LFS | 0.75 | 4.0 |
| 40C | QUINCY | LFS | 0.8 | 4.0 |
| 74B | QUINCY | FS | 0.8 | 4.0 |
| 75B | QUINCY | LFS | 0.8 | 4.0 |
| 75E | QUINCY | LFS | 0.7 | 4.0 |
| 76B | QUINCY | LFS | 0.8 | 4.0 |
| 77C | QUINCY | LFS | 0.8 | 4.0 |
| 78B | QUINCY | FS | 0.8 | 4.0 |
| 120C | QUINCY | FS | 0.8 | 4.0 |
| 36 | QUINCY VARIANT | LFS | 0.8 | 4.0 |
| 40 | RAFTON | SIL | 0.35 | 0.7 |
| 41 | RAFTON | SIL | 0.35 | 0.7 |
| 42 | RAFTON | SIL | 0.35 | 0.7 |
| 47A | RAFTON | SIL | 0.35 | 0.7 |
| 239 | REAVIS | SIL | 0.25 | 0.7 |
| 143 | REDMOND | CB-ASHY-SL | 0.3 | 2.0 |
| 144 | REDMOND | ASHY-SL | 0.3 | 2.0 |
| 104A | REDMOND | SL | 0.3 | 2.0 |
| 104Am | REDMOND | ASHY-SL | 0.3 | 2.0 |
| 240 | REDMOUNT | SIL | 0.25 | 0.7 |
| 241 | REDMOUNT | SIL | 0.25 | 0.7 |
| 242 | REDMOUNT | GR-SIL | 0.25 | 0.7 |
| 243 | REDMOUNT | SIL | 0.25 | 0.7 |
| 35 | RICCO | SICL | 0.15 | 0.35 |
| 35 | RICCO | SICL | 0.15 | 0.35 |
| 120A | RICCO | SICL | 0.15 | 0.35 |
| 472A | RICCO | SICL | 0.15 | 0.35 |
| 250B | RITTER | L | 0.35 | 0.9 |
| 270D | RITTER | L | 0.3 | 0.9 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 31B | RITZVILLE | VFSL | 0.3 | 1.0 |
| 31C | RITZVILLE | VFSL | 0.25 | 1.0 |
| 31D | RITZVILLE | VFSL | 0.2 | 1.0 |
| 31E | RITZVILLE | VFSL | 0.15 | 1.0 |
| 32A | RITZVILLE | SIL | 0.25 | 0.5 |
| 32B | RITZVILLE | SIL | 0.2 | 0.5 |
| 32C | RITZVILLE | SIL | 0.2 | 0.5 |
| 32D | RITZVILLE | SIL | 0.15 | 0.5 |
| 33E | RITZVILLE | SIL | 0.1 | 0.5 |
| 34E | RITZVILLE | SIL | 0.1 | 0.5 |
| 44B | RITZVILLE | VFSL | 0.3 | 1.0 |
| 44C | RITZVILLE | VFSL | 0.3 | 1.0 |
| 44D | RITZVILLE | VFSL | 0.25 | 1.0 |
| 45A | RITZVILLE | FSL, SIL | 0.2 | 0.5 |
| 45A | RITZVILLE | SIL | 0.25 | 0.5 |
| 45B | RITZVILLE | FSL, SIL | 0.1 | 0.5 |
| 45B | RITZVILLE | SIL | 0.25 | 0.5 |
| 45C | RITZVILLE | SIL | 0.2 | 0.5 |
| 45D | RITZVILLE | SIL | 0.15 | 0.5 |
| 46E | RITZVILLE | SIL | 0.1 | 0.5 |
| 47E | RITZVILLE | SIL | 0.1 | 0.5 |
| 79B | RITZVILLE | VFSL | 0.3 | 1.0 |
| 79C | RITZVILLE | VFSL | 0.3 | 1.0 |
| 79D | RITZVILLE | VFSL | 0.25 | 1.0 |
| 79E | RITZVILLE | VFSL | 0.2 | 1.0 |
| 80B | RITZVILLE | SIL | 0.25 | 0.5 |
| 80C | RITZVILLE | SIL | 0.2 | 0.5 |
| 80D | RITZVILLE | SIL | 0.15 | 0.5 |
| 81E | RITZVILLE | SIL | 0.1 | 0.5 |
| 82E | RITZVILLE | SIL | 0.1 | 0.5 |
| 83C | RITZVILLE | SIL | 0.2 | 0.5 |
| 25D | ROLOFF | SIL | 0.2 | 0.7 |
| 38A | ROLOFF | SIL | 0.25 | 0.7 |
| 38B | ROLOFF | SIL | 0.25 | 0.7 |
| 38C | ROLOFF | SIL | 0.25 | 0.7 |
| 39D | ROLOFF | SIL | 0.2 | 0.7 |
| 214A | ROSEBURG | L | 0.4 | 0.9 |
| 215C | ROSEHAVEN | L | 0.3 | 0.9 |
| 51B | ROYAL | LFS | 0.75 | 0.5 |
| 51C | ROYAL | LFS | 0.7 | 0.5 |
| 52B | ROYAL | FSL | 0.75 | 0.5 |
| 52C | ROYAL | FSL | 0.7 | 0.5 |
| 53A | ROYAL | SIL | 0.5 | 0.7 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 67B | RUCH | GR-SIL | 0.5 | 1.0 |
| 67C | RUCH | GR-SIL | 0.4 | 1.0 |
| 157B | RUCH | SIL | 0.35 | 0.7 |
| 158B | RUCH | GR-SIL | 0.5 | 1.0 |
| 158D | RUCH | GR-SIL | 0.35 | 1.0 |
| 30A | SAGEHILL | FSL | 0.8 | 4.0 |
| 30B | SAGEHILL | FSL | 0.8 | 4.0 |
| 30C | SAGEHILL | FSL | 0.75 | 4.0 |
| 40B | SAGEHILL | FSL | 0.8 | 4.0 |
| 40C | SAGEHILL | FSL | 0.75 | 4.0 |
| 41B | SAGEHILL | FSL | 0.8 | 4.0 |
| 41C | SAGEHILL | FSL | 0.75 | 4.0 |
| 54B | SAGEHILL | FSL | 0.8 | 4.0 |
| 54C | SAGEHILL | FSL | 0.8 | 4.0 |
| 55B | SAGEHILL | FSL | 0.8 | 4.0 |
| 55C | SAGEHILL | FSL | 0.8 | 4.0 |
| 87B | SAGEHILL | FSL | 0.8 | 4.0 |
| 87C | SAGEHILL | FSL | 0.8 | 4.0 |
| 62B | SALEM | SIL | 0.3 | 0.8 |
| 63B | SALEM | GR-SIL | 0.3 | 0.8 |
| 76B | SALEM | SIL | 0.3 | 0.8 |
| 76C | SALEM | SIL | 0.25 | 0.8 |
| 77B | SALEM | GR-SIL | 0.3 | 0.8 |
| 87 | SALEM | GR-SIL | 0.3 | 0.8 |
| 118 | SALEM | GR-SIL | 0.3 | 0.8 |
| 119 | SALEM | GR-SIL | 0.3 | 0.8 |
| Sa | SALEM | GR-SIL | 0.3 | 0.8 |
| 190B | SALISBURY | L | 0.15 | 0.3 |
| 243B | SALISBURY | L | 0.15 | 0.3 |
| 243C | SALISBURY | L | 0.15 | 0.3 |
| 120B | SALKUM | SIL | 0.3 | 0.7 |
| 121B | SALKUM | SICL | 0.3 | 0.35 |
| 121C | SALKUM | SICL | 0.25 | 0.35 |
| 64B | SALKUM | SICL | 0.3 | 0.35 |
| 64C | SALKUM | SICL | 0.3 | 0.35 |
| 88B | SALKUM | SICL | 0.3 | 0.35 |
| 88C | SALKUM | SICL | 0.25 | 0.35 |
| SkB | SALKUM | SICL | 0.3 | 0.35 |
| SkD | SALKUM | SICL | 0.25 | 0.35 |
| SlB | SALKUM | SICL | 0.3 | 0.35 |
| 45 | SAUVIE | SIL | 0.35 | 0.7 |
| 46 | SAUVIE | SICL | 0.35 | 0.35 |
| 47 | SAUVIE | SIL | 0.35 | 0.7 |
| 47A | SAUVIE | SIL | 0.35 | 0.7 |
| 48 | SAUVIE | SICL | 0.35 | 0.35 |
| 70 | SCHERRARD | CL | 0.1 | 0.4 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 42B | SCHRIER | SIL | 0.35 | 0.7 |
| 42C | SCHRIER | SIL | 0.3 | 0.7 |
| 270 | SCHRIER | SIL | 0.35 | 0.7 |
| 68B | SELMAC | L | 0.2 | 0.9 |
| 68D | SELMAC | L | 0.15 | 0.9 |
| 162B | SELMAC | L | 0.2 | 0.9 |
| 162D | SELMAC | L | 0.15 | 0.9 |
| 163A | SEVENOAKS | LS | 0.58 | 3.0 |
| 164B | SHEFFLEIN | L | 0.2 | 0.9 |
| 41A | SILVIES | SIL | 0.2 | 0.5 |
| 90A | SILVIES | SIL | 0.2 | 0.5 |
| 320B | SILVIES | SIL | 0.2 | 0.5 |
| 767A | SILVIES | C | 0.15 | 0.1 |
| 31 | STANFIELD | SIL | 0.3 | 2.0 |
| 31A | STANFIELD | SIL | 0.3 | 2.0 |
| 44 | STANFIELD | FSL | 0.75 | 2.0 |
| 91A | STANFIELD | SIL | 0.3 | 2.0 |
| 92A | STANFIELD | SIL | 0.3 | 2.0 |
| 127A | STATZ | SL | 0.3 | 2.0 |
| 34C | STUKEL | SL | 0.25 | 2.0 |
| 35B | STUKEL | SL | 0.3 | 2.0 |
| 35Bm | STUKEL | ASHY-SL | 0.3 | 2.0 |
| 35Bm | STUKEL | ASHY-SL, CB-ASHY-SL | 0.3 | 2.0 |
| 35Bm | STUKEL | ASHY-SL, GR-ASHY-SL | 0.3 | 2.0 |
| 35Bm | STUKEL | UWB | 0.3 | 2.0 |
| 74B | STUKEL | L | 0.4 | 0.9 |
| 105C | STUKEL | SL | 0.25 | 2.0 |
| 138A | STUKEL | SL | 0.3 | 2.0 |
| 139Am | STUKEL | ASHY-SL | 0.3 | 2.0 |
| 140Bm | STUKEL | ASHY-SL | 0.3 | 2.0 |
| 142Bm | STUKEL | ASHY-SL | 0.3 | 2.0 |
| 295 | STURGILL | SIL | 0.2 | 0.5 |
| 296 | STURGILL | SIL | 0.2 | 0.5 |
| 174E | SUTHERLIN | SIL | 0.1 | 0.7 |
| 175E | SUTHERLIN | SIL | 0.1 | 0.7 |
| 235C | SUTHERLIN | SIL | 0.2 | 0.7 |
| 235D | SUTHERLIN | SIL | 0.15 | 0.7 |
| 235E | SUTHERLIN | SIL | 0.1 | 0.7 |
| 236C | SUTHERLIN | SIL | 0.2 | 0.7 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 75 | SYCAN | LS | 1 | 3.0 |
| 76 | SYCAN VARIANT | LCOS | 1 | 3.0 |
| 73 | TAKILMA | CB-L | 0.5 | 1.0 |
| 187A | TAKILMA | CB-L | 0.5 | 1.0 |
| 77 | TEETERS | SIL | 0.5 | 1.0 |
| 192A | TERRABELLA | CL | 0.16 | 0.4 |
| 58 | TETHEROW | GRV-SL | 0.3 | 2.0 |
| 59 | TETHEROW | GRV-SL | 0.3 | 2.0 |
| 150A | TETHEROW | SL | 0.3 | 2.0 |
| 150B | TETHEROW | SL | 0.3 | 2.0 |
| 60C | TOLO | SIL | 0.4 | 0.7 |
| 97C | TOLO | SIL | 0.4 | 0.7 |
| 98C | TOLO | SIL | 0.4 | 0.7 |
| 264BC | TOLO | SIL | 0.4 | 0.7 |
| 327 | TOLO | SIL | 0.4 | 0.7 |
| 328 | TOLO | SIL | 0.4 | 0.7 |
| 329 | TOLO | SIL | 0.4 | 0.7 |
| 46C | TUB | GR-CL | 0.2 | 0.5 |
| 47 | TUB | GR-CL | 0.2 | 0.5 |
| 49D | TUB | ST-CL | 0.2 | 0.5 |
| 112 | TUB | L | 0.5 | 0.9 |
| 150A | TUB | CL | 0.2 | 0.5 |
| 150B | TUB | CL | 0.2 | 0.5 |
| 150D | TUB | CL | 0.2 | 0.5 |
| TgC | TUB | GR-CL | 0.2 | 0.5 |
| 253A | TULANA | MK-SICL | 0.3 | 1.0 |
| 152A | TUMALO | SL | 0.5 | 3.0 |
| 152B | TUMALO | SL | 0.5 | 3.0 |
| 33A | TURBYFILL | FSL | 0.5 | 1.5 |
| 33B | TURBYFILL | FSL | 0.5 | 1.5 |
| 33C | TURBYFILL | FSL | 0.45 | 1.5 |
| 33D | TURBYFILL | FSL | 0.4 | 1.5 |
| 132A | TURBYFILL | FSL | 0.5 | 1.5 |
| 132B | TURBYFILL | FSL | 0.5 | 1.5 |
| 132BC | TURBYFILL | FSL | 0.5 | 1.5 |
| 44 | TYGH | FSL | 0.65 | 1.5 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 47C | UKIAH | CB-SICL | 0.2 | 0.35 |
| 50B | UKIAH | ST-SICL | 0.2 | 0.35 |
| 60D | UKIAH | SICL | 0.2 | 0.35 |
| 169D | UKIAH | SICL | 0.2 | 0.35 |
| 345D | UKIAH | ST-SICL | 0.2 | 0.35 |
| 347C | UKIAH | ST-SICL | 0.2 | 0.35 |
| 34 | UMAPINE | SIL | 0.15 | 0.3 |
| 106A | UMAPINE | SIL | 0.15 | 0.3 |
| 920B | UTLEY | L | 0.4 | 0.9 |
| 5B | VALBY | SIL | 0.15 | 0.7 |
| 5C | VALBY | SIL | 0.15 | 0.7 |
| 6D | VALBY | SIL | 0.1 | 0.7 |
| 7D | VALBY | SIL | 0.1 | 0.7 |
| 63B | VALBY | SIL | 0.15 | 0.7 |
| 63C | VALBY | SIL | 0.15 | 0.7 |
| 64D | VALBY | SIL | 0.1 | 0.7 |
| 65D | VALBY | SIL | 0.1 | 0.7 |
| 23B | VAN HORN | FSL | 0.3 | 1.5 |
| 23C | VAN HORN | FSL | 0.25 | 1.5 |
| 45B | VAN HORN | L | 0.3 | 0.9 |
| 45C | VAN HORN | L | 0.3 | 0.9 |
| 45D | VAN HORN | L | 0.25 | 0.9 |
| 45E | VAN HORN | L | 0.2 | 0.9 |
| 24B | VANHORN VARIANT | L | 0.3 | 0.9 |
| 53 | VEAZIE | L | 0.35 | 0.9 |
| 53 | VEAZIE | CBX-S, GRV-LS, GRV-S | 0.2 |  |
| 62A | VEAZIE | GR-L | 0.35 | 0.9 |
| 65 | VEAZIE | L | 0.35 | 0.9 |
| 66 | VEAZIE | L | 0.35 | 0.9 |
| 67 | VEAZIE | L | 0.35 | 0.9 |
| 109A | VEAZIE | SIL | 0.3 | 0.7 |
| 110A | VEAZIE | CB-L | 0.35 | 0.9 |
| 201A | VEAZIE | L | 0.35 | 0.9 |
| 202A | VEAZIE | L | 0.35 | 0.9 |
| 128B | VENETA | L | 0.3 | 0.9 |
| 255C | VENETA | L | 0.3 | 0.9 |
| 255D | VENETA | L | 0.3 | 0.9 |
| VeB | VENETA | SIL | 0.3 | 0.7 |
| VeD | VENETA | SIL | 0.3 | 0.7 |
| 129B | VENETA VARIANT | SIL | 0.3 | 0.7 |
| VnB | VENETA VARIANT | L | 0.3 | 0.9 |
| VnD | VENETA VARIANT | L | 0.3 | 0.9 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 35A | VIRTUE | SIL | 0.15 | 0.5 |
| 35B | VIRTUE | SIL | 0.15 | 0.5 |
| 35C | VIRTUE | SIL | 0.1 | 0.5 |
| 171B | VIRTUE | SIL | 0.15 | 0.5 |
| 172B | VIRTUE | GRV-SIL | 0.15 | 0.5 |
| 516C | VIRTUE | SIL | 0.1 | 0.5 |
| 560BC | VIRTUE | SIL | 0.15 | 0.5 |
| 48B | WAHA | SIL | 0.25 | 0.7 |
| 49D | WAHA | SIL | 0.2 | 0.7 |
| 50D | WAHA | SIL | 0.2 | 0.7 |
| 66B | WAHA | SIL | 0.25 | 0.7 |
| 67D | WAHA | SIL | 0.2 | 0.7 |
| 68D | WAHA | SIL | 0.2 | 0.7 |
| 69D | WAHA | SIL | 0.2 | 0.7 |
| 112B | WAHA | SICL | 0.3 | 0.7 |
| 112D | WAHA | SICL | 0.25 | 0.7 |
| 290B | WAHA | SIL | 0.25 | 0.7 |
| 290B | WAHA | SICL, SIL | 0.2 |  |
| 291D | WAHA | SIL | 0.2 | 0.7 |
| 31B | WALLA WALLA | SIL | 0.3 | 0.7 |
| 31C | WALLA WALLA | SIL | 0.3 | 0.7 |
| 32D | WALLA WALLA | SIL | 0.25 | 0.7 |
| 46B | WALLA WALLA | SIL | 0.3 | 0.7 |
| 46C | WALLA WALLA | SIL | 0.3 | 0.7 |
| 46D | WALLA WALLA | SIL | 0.25 | 0.7 |
| 47D | WALLA WALLA | SIL | 0.25 | 0.7 |
| 47E | WALLA WALLA | SIL | 0.15 | 0.7 |
| 48E | WALLA WALLA | SIL | 0.15 | 0.7 |
| 52B | WALLA WALLA | SIL | 0.3 | 0.7 |
| 52C | WALLA WALLA | SIL | 0.25 | 0.7 |
| 53D | WALLA WALLA | SIL | 0.2 | 0.7 |
| 53E | WALLA WALLA | SIL | 0.15 | 0.7 |
| 54D | WALLA WALLA | SIL | 0.2 | 0.7 |
| 114B | WALLA WALLA | SIL | 0.3 | 0.7 |
| 114B | WALLA WALLA | SIL | 0.25 |  |
| 114B | WALLA WALLA | SI, SIL | 0.2 |  |
| 114C | WALLA WALLA | SIL | 0.25 | 0.7 |
| 115D | WALLA WALLA | SIL | 0.2 | 0.7 |
| 115E | WALLA WALLA | SIL | 0.15 | 0.7 |
| 116D | WALLA WALLA | SIL | 0.2 | 0.7 |
| 117D | WALLA WALLA | SIL | 0.2 | 0.7 |
| 118B | WALLA WALLA | SIL | 0.3 | 0.7 |
| 49B | WAMIC | L | 0.25 | 0.5 |
| 49C | WAMIC | L | 0.25 | 0.5 |
| 50C | WAMIC | L | 0.25 | 0.5 |
| 50D | WAMIC | L | 0.2 | 0.5 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 43 | WAPATO | SICL | 0.3 | 0.3 |
| 55 | WAPATO | SIL | 0.3 | 0.7 |
| 63 | WAPATO | SIL | 0.3 | 0.7 |
| 73 | WAPATO | SICL | 0.3 | 0.3 |
| 83 | WAPATO | SIL | 0.3 | 0.7 |
| 83 | WAPATO | SIL | 0.3 | 0.7 |
| 84 | WAPATO | SICL | 0.3 | 0.3 |
| 99 | WAPATO | SICL | 0.3 | 0.3 |
| 134 | WAPATO | SICL | 0.3 | 0.3 |
| Wc | WAPATO | SICL | 0.25 | 0.3 |
| Wc | WAPATO | SICL | 0.25 | 0.3 |
| 54B | WAPINITIA | SIL | 0.3 | 2.0 |
| 54C | WAPINITIA | SIL | 0.3 | 2.0 |
| 54D | WAPINITIA | SIL | 0.25 | 2.0 |
| 54E | WAPINITIA | SIL | 0.2 | 2.0 |
| 149 | WAPINITIA | SIL | 0.3 | 2.0 |
| 53E | WARDEN | SIL | 0.25 | 0.23 |
| 55B | WARDEN | SIL | 0.25 | 0.23 |
| 55C | WARDEN | SIL | 0.2 | 0.23 |
| 55D | WARDEN | SIL | 0.15 | 0.23 |
| 70B | WARDEN | VFSL | 0.65 | 1.2 |
| 70C | WARDEN | VFSL | 0.65 | 1.2 |
| 70D | WARDEN | VFSL | 0.6 | 1.2 |
| 71A | WARDEN | SIL | 0.25 | 0.23 |
| 71B | WARDEN | SIL | 0.25 | 0.23 |
| 71C | WARDEN | SIL | 0.2 | 0.23 |
| 71D | WARDEN | SIL | 0.2 | 0.23 |
| 72C | WARDEN | SIL | 0.25 | 0.23 |
| 72D | WARDEN | SIL | 0.2 | 0.23 |
| 5C | WATAMA | SIL | 0.25 | 0.7 |
| 54B | WATAMA | SIL | 0.25 | 0.7 |
| 54C | WATAMA | SIL | 0.25 | 0.7 |
| 114 | WATAMA | SIL | 0.25 | 0.7 |
| 150 | WATAMA | SIL | 0.25 | 0.7 |
| 151 | WATAMA | SIL | 0.25 | 0.7 |
| 152 | WATAMA | GR-SIL | 0.25 | 0.7 |
| 351 | WATAMA | SIL | 0.25 | 0.7 |
| 352 | WATAMA | SIL | 0.25 | 0.7 |
| 353 | WATAMA | SIL | 0.25 | 0.7 |
| 210B | WATAMA | SIL | 0.25 | 0.7 |
| 247D | WATAMA | SIL | 0.25 | 0.7 |
| 272C | WATAMA | SIL | 0.25 | 0.7 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 74C | WILLAKENZIE | SICL | 0.3 | 0.35 |
| 74D | WILLAKENZIE | SICL | 0.3 | 0.35 |
| 101C | WILLAKENZIE | CL | 0.3 | 0.45 |
| 101D | WILLAKENZIE | CL | 0.3 | 0.45 |
| 135C | WILLAKENZIE | CL | 0.3 | 0.45 |
| 135D | WILLAKENZIE | CL | 0.3 | 0.45 |
| WeC | WILLAKENZIE | SICL | 0.3 | 0.35 |
| WeD | WILLAKENZIE | SICL | 0.25 | 0.35 |
| WkB | WILLAKENZIE | SICL | 0.3 | 0.35 |
| WkD | WILLAKENZIE | SICL | 0.25 | 0.35 |
| 44A | WILLAMETTE | SIL | 0.3 | 0.7 |
| 44B | WILLAMETTE | SIL | 0.3 | 0.7 |
| 44C | WILLAMETTE | SIL | 0.25 | 0.7 |
| 44D | WILLAMETTE | SIL | 0.2 | 0.7 |
| 75A | WILLAMETTE | SIL | 0.3 | 0.7 |
| 75C | WILLAMETTE | SIL | 0.25 | 0.7 |
| 75D | WILLAMETTE | SIL | 0.2 | 0.7 |
| 86A | WILLAMETTE | SIL | 0.3 | 0.7 |
| 86B | WILLAMETTE | SIL | 0.25 | 0.7 |
| 86C | WILLAMETTE | SIL | 0.2 | 0.7 |
| 87A | WILLAMETTE | SIL | 0.3 | 0.7 |
| 88A | WILLAMETTE | SIL | 0.3 | 0.7 |
| 88B | WILLAMETTE | SIL | 0.25 | 0.7 |
| 102 | WILLAMETTE | SIL | 0.3 | 0.7 |
| WeA | WILLAMETTE | SIL | 0.3 | 0.7 |
| WeC | WILLAMETTE | SIL | 0.25 | 0.7 |
| WIA | WILLAMETTE | SIL | 0.3 | 0.7 |
| WIC | WILLAMETTE | SIL | 0.25 | 0.7 |
| WID | WILLAMETTE | SIL | 0.2 | 0.7 |
| 42 | WILLANCH | FSL | 1.5 | 2.0 |
| 62 | WILLANCH | FSL | 1.5 | 2.0 |
| 127A | WILLANCH | FSL | 1.5 | 2.0 |
| 136 | WILLANCH | FSL | 1.5 | 2.0 |
| 261A | WILLANCH | FSL | 1.5 | 2.0 |
| 94 | WILLOWDALE | L | 0.3 | 0.9 |
| 156 | WILLOWDALE | L | 0.3 | 0.9 |
| 15A | WILLOWDALE | L | 0.3 | 0.9 |
| Wd | WILLOWDALE | L | 0.25 | 0.9 |
| 76C | WINCHESTER | S | 0.9 | 4.0 |
| 122B | WINCHESTER | S | 1 | 4.0 |
| 123B | WINCHESTER | S | 1 | 4.0 |
| 124B | WINCHESTER | S | 1 | 4.0 |

Table OR2-16	Soil intake parameters for selected soils in Oregon (continued)

| MAP UNIT SYMBOL | SOIL COMPONENT NAME | SURFACE TEXTURE | Basic Sprinkler Intake Rate (in/hr) | Intake Family |
| --- | --- | --- | --- | --- |
| 26B | WIND RIVER | FSL | 0.5 | 1.5 |
| 26C | WIND RIVER | FSL | 0.45 | 1.5 |
| 56B | WIND RIVER | FSL | 0.5 | 1.5 |
| 56C | WIND RIVER | FSL | 0.5 | 1.5 |
| 27B | WINDRIVER VARIANT | GR-SL | 0.5 | 1.5 |
| 27E | WINDRIVER VARIANT | GR-SL | 0.35 | 1.5 |
| 71 | WINGVILLE | SIL | 0.3 | 0.3 |
| 52A | WINGVILLE | SIL | 0.3 | 0.3 |
| 176A | WINGVILLE | SIL | 0.3 | 0.3 |
| 6B | WINLO | GRV-CL | 0.2 | 0.9 |
| 198A | WINLO | GRV-CL | 0.2 | 0.9 |
| 199C | WOLFPEAK | SL | 0.27 | 1.5 |
| 45A | WOODBURN | SIL | 0.3 | 0.7 |
| 45B | WOODBURN | SIL | 0.3 | 0.7 |
| 45C | WOODBURN | SIL | 0.25 | 0.7 |
| 45D | WOODBURN | SIL | 0.2 | 0.7 |
| 77A | WOODBURN | SIL | 0.3 | 0.7 |
| 77C | WOODBURN | SIL | 0.25 | 0.7 |
| 77D | WOODBURN | SIL | 0.2 | 0.7 |
| 91A | WOODBURN | SIL | 0.3 | 0.7 |
| 91B | WOODBURN | SIL | 0.3 | 0.7 |
| 91C | WOODBURN | SIL | 0.25 | 0.7 |
| 106A | WOODBURN | SIL | 0.3 | 0.7 |
| 106C | WOODBURN | SIL | 0.25 | 0.7 |
| 139 | WOODBURN | SIL | 0.3 | 0.7 |
| WoA | WOODBURN | SIL | 0.3 | 0.7 |
| WoC | WOODBURN | SIL | 0.25 | 0.7 |
| WuA | WOODBURN | SIL | 0.3 | 0.7 |
| WuB | WOODBURN | SIL | 0.3 | 0.7 |
| WuC | WOODBURN | SIL | 0.25 | 0.7 |
| WuD | WOODBURN | SIL | 0.2 | 0.7 |
| 86C | YAINAX | L | 0.4 | 0.9 |
| 57B | YANCY | CL | 0.2 | 0.4 |
| 87A | YANCY | CL | 0.2 | 0.4 |
| 87B | YANCY | CL | 0.2 | 0.4 |
| 89 | YONNA | L | 0.3 | 0.9 |
| 326 | ZUMWALT | SIL | 0.25 | 0.7 |
| 358 | ZUMWALT | SIL | 0.25 | 0.7 |
| 359 | ZUMWALT | SIL | 0.25 | 0.7 |