MSFC PRACA : 2003-02-12 08:41

MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A17800 | In-Flight Anomaly Number -- | Contractor Report Number S-088 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title LH2 AFT DOME GORE PANELS WERE MARKED WITH THE INCORRECT LOCKHEED MARTIN PART NO. & SERIAL NUMBER |
| EICN# -- | ELEMENT ET | Contractor -- | FSCM# -- | FCRIT 1 |
| HCRIT 1 | Sys_Lvl -- | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE LRU | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE LH2 AFT DOME ASSEMBL | PART# 80914900900-509 | SER/LOT# 1247810 | MANUFACTURER AHF |
| Test/Operation MI - MFI | Prevailing Condtion N - INSPECTION | F / U UC | Fail Mode MU - MECH TOLRNCE | Cause MW - MFG-WORK |
| System STRUCTURAL | Defect PR - WRONG | Material S - STRUCT | Work Contact M. PENO | Fail Date 06/17/2002 |
| Received at MSFC 08/15/2002 | Date Isolated 06/17/2002 | FMEA Reference 6.2.1.1 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom MU - MECH TOLRNCE | Time Cycle -- |
| Effectivity Text ET-93, ET-94, ET-113, ET-115 THROUGH ET-132 |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 08/28/2002 | CN RSLV SBMT 08/15/2002 | Defer Date -- | Add Date 08/15/2002 | R/C Codes 2 - MFG 3 - F/TE 5 - TRNG |
| Assignee |
| Design S. AVANS | Chief Engineer N. OTTE | S & MA A. DANIELS | Project -- | Project MGR J. SMELSER |
| Approval |
| Design S. AVANS | Chief Engineer N. OTTE | S & MA A. DANIELS | Project -- | Project MGR J. SMELSER |
| PAC Assignee T. WHITE | PAC Review Complete TW | MSFC Closure Date 08/26/2002 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type NC - PROB RPT | Related Document ID N057622 |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description 1. LH2 AFT DOME GORE PANELS 80914980994-004, S/N 00000008150 AND 80914980997-002, S/N 0000007804 WERE MARKED WITH THE INCORRECT LOCKHEED MARTIN PART NUMBER AND SERIAL NUMBER AT THE SUPPLIER FACILITY (AHF DUCOMMUN). 2. THE HAG-2 (HYDROGEN AFT GORE WELD NUMBER 2) AND (HAG-3) WELD LAND WIDTH INSPECTION AT THE 80914980955-020 QUARTER PANEL ASSEMBLY LEVEL DID NOT REJECT NONCONFORMING GORE PANEL 80914980994-004, S/N 00000008150 FOR MINIMUM WELD LAND WIDTH VIOLATION. THE DISCREPANT PANEL WAS NOT DISCOVERED UNTIL THE HAG-4 AND HAG-10 INSPECTIONS ON THE COMPLETED DOME (80914900900-509). THIS CAP IS CRITICALITY 1 DUE TO THE POTENTIAL FOR OVERSTRESS. THIS IS A PROCESS ESCAPE. |
| Contractor Investigation/Resolution 08/15/2002 - CONTRACTOR SUBMITTED PROBLEM REPORT OPENER/CLOSURE REQUEST AS FOLLOWS: PROBLEM ------- 1. LH2 AFT DOME GORE PANELS 80914980994-004, S/N 00000008150 AND 80914980997-002, S/N 0000007804 WERE MARKED WITH THE INCORRECT LOCKHEED MARTIN PART NUMBER AND SERIAL NUMBER AT THE SUPPLIER FACILITY (AHF DUCOMMUN). 2. THE HAG-2 (HYDROGEN AFT GORE WELD NUMBER 2) AND (HAG-3) WELD LAND WIDTH INSPECTION AT THE 80914980955-020 QUARTER PANEL ASSEMBLY LEVEL DID NOT REJECT NONCONFORMING GORE PANEL 80914980994-004, S/N 00000008150 FOR MINIMUM WELD LAND WIDTH VIOLATION. THE DISCREPANT PANEL WAS NOT DISCOVERED UNTIL THE HAG-4 AND HAG-10 INSPECTIONS ON THE COMPLETED DOME (80914900900-509). THIS CAPS IS CRITICALITY 1 DUE TO THE POTENTIAL FOR OVERSTRESS. THIS IS A PROCESS ESCAPE. GENERAL ------- THE LH2 AFT DOME CONSISTS OF 12 GORE PANELS OF VARYING THICKNESS AND CONFIGURATIONS, DEPENDING ON THE LOCATION OF THE PANEL ON THE DOME ASSEMBLY. THE PANEL THICKNESS RANGES FROM .076" TO .200". ADDITIONALLY, ALL GORE PANELS HAVE A WELD LAND ALONG EACH OF ITS FOUR SIDES. THE LAND WIDTH ON EACH SIDE USED TO FORM THE HAG WELDS VARIES BETWEEN PANELS FROM 1.62" TO 2.12". THE WELD LAND GIVES THE PANEL STRENGTH, STABILITY AND IS TYPICALLY THICKER THAN THE REMAINING ACREAGE OF THE GORE PANEL. THIS INCREASED THICKNESS IS REQUIRED FOR THE WELDING PROCESS. BACKGROUND ----------- 0 QUALITY CONTROL REPORTED THAT THE ET-129 LH2 AFT DOME ASSEMBLY CONTAINED TWO GORE PANELS THAT WERE MISIDENTIFIED, RESULTING IN A NONCONFORMING DOME CONFIGURATION. NCD NUMBER N057622 WAS GENERATED TO DOCUMENT THE NONCONFORMANCE. 0 QUALITY CONTROL WAS INSPECTING THE HAG-4 AND HAG-10 WELD LANDS WHEN THE PROBLEM WITH THE HAG-2 AND HAG-3 WAS DISCOVERED. 0 BOTH GORE PANELS WERE VIBRO-MARKED ON 9/25/01 AT AHF DUCOMMUN BY THE SAME TECHNICIAN. - THE TECHNICIAN THAT MARKED THE PARTS WAS NOT THE PRIMARY PRACTITIONER FOR MARKING PARTS. - THE TECHNICIAN IS NO LONGER EMPLOYED BY AHF DUCOMMUN. 0 AHF DUCOMMUN HAS SUPPLIED LO2 FORWARD & AFT OGIVES, LO2 DOME GORES AND LH2 FORWARD AND AFT DOME GORES FOR THE DURATION OF THE EXTERNAL TANK PROGRAM. 0 FOR THE PURPOSE OF THIS INVESTIGATION, LO2 DOME GORE PANELS WERE EXCLUDED DUE TO THEIR INTERCHANGEABILITY. TASK I. FAILURE INVESTIGATION --------------------- A. REVIEW PROCESS FLOW TO DETERMINE WHERE THE ERROR OCCURRED. RESPONSIBILITY: M. HEINSZ/3761 - S. PARIKH/3760 ECD: 6/18/2002 CLOSED: 6/18/2002 CLOSURE STATEMENT: ------------------ REVIEW OF THE PROCESS FLOW CONFIRMED THE MARKING ERROR OCCURRED AT AHF DUCOMMUN. B. PROVIDE NOMENCLATURE FOR ALL HARDWARE SUPPLIED BY AHF. RESPONSIBILITY: M. HEINSZ/3761 - S. PARIKH/3760 ECD: 6/18/2002 CLOSED: 6/18/2002 CLOSURE STATEMENT: ------------------ AHF SUPPLIES THE FOLLOWING HARDWARE TO MAF: 0 LH2 & LO2 INNER AND OUTER CHORDS 0 LO2 DOME GORES 0 LH2 FWD AND AFT DOME GORES 0 LO2 FWD AND AFT OGIVES 0 SPLASH PLATES 0 I/T DOUBLERS 0 I/T SKIN PANELS 0 I/T CHORDS 0 SRB BEAM UPPER AND LOWER CHORDS C. DETERMINE WHEN THE PRACTITIONER RESPONSIBLE FOR MIS- IDENTIFICATION OF THE GORE PANELS STARTED TO WORK IN THE INSPECTION AREA. RESPONSIBILITY: M. HEINSZ/3761 - S. PARIKH/3760 ECD: 6/18/2002 COMPLETE: 6/18/2002 CLOSURE STATEMENT: ------------------ THE PRACTITIONER RESPONSIBLE FOR MISIDENTIFICATION OF THE PARTS WAS HIRED AT AHF ON 11/7/88. AHF STATED THAT HE WAS FAMILIAR WITH READING PRINTS AND MYLAR'S. ON 2/15/99 HE WAS TRANSFERRED TO THE CALIBRATION LAB AND RECEIVED A QUALITY STAMP. APPROXIMATELY 2 MONTHS LATER THE PRACTITIONER WAS ASSIGNED TO THE PRODUCTION AREA AS A TEMPORARY INSPECTOR. THE PRACTITIONER LEFT THE COMPANY VOLUNTARILY ON 11/02/01. (REFERENCE E-MAIL FROM DAN CAUSKY TO MARK HEINSZ DATED 6/18/02) D. PROVIDE PART NUMBERS OF GORES/OGIVE PANELS DELIVERED BY AHF FROM 8/01 THROUGH 10/01. RESPONSIBILITY: M. HEINSZ/3761 - S. PARIKH/3760 ECD: 6/18/2002 COMPLETE: 6/18/2002 CLOSURE STATEMENT: ------------------ THERE WERE 55 PANELS SHIPPED BY AHF TO MAF DURING THE 3-MONTH TIME FRAME FROM 8/01-10/01. E. PROVIDE DETAILS ON WHICH AHF PRACTITIONER MARKED EACH PART IDENTIFIED IN TASK I.D ABOVE (PARTS SHIPPED 8/01 THROUGH 10/01). RESPONSIBILITY: M. HEINSZ/3761 - S. PARIKH/3760 ECD: 6/21/2002 COMPLETE: 6/21/2002 CLOSURE STATEMENT: ------------------ PART MARKING PRACTITIONERS HAVE BEEN IDENTIFIED FOR THE 55 PARTS DELIVERED IN THIS 3-MONTH TIME FRAME. THE PRACTITIONER RESPONSIBLE FOR THE PART MARKING DISCREPANCY IDENTIFIED 8 PANELS DURING THE THREE-MONTH TIME FRAME FROM 8/01-10/01. OF THESE 55 PARTS, QC INSPECTED ALL OF THE PARTS RELEASED (36 OF 55) FROM INVENTORY AND FOUND NO OTHER DISCREPANCIES. THE REMAINING 19 PARTS ARE IN INVENTORY. ALL OF THE PARTS MARKED BY THE PRACTITIONER RESPONSIBLE FOR MISIDENTIFYING THE 2 PANELS WERE INCLUDED IN THE QC INSPECTIONS. REFERENCE QC INSPECTION SPREADSHEET DATED 6/21/02. F. DETERMINE VISUAL AND DIMENSIONAL DISTINGUISHING CHARACTERISTICS FOR LO2 AND LH2 OGIVE PANELS/GORES. RESPONSIBILITY: M. PENO/3741 - D. WESTPHAL/3740 J. SPRAY/3724 D. OWENS/3720 ECD: 6/18/2002 CLOSED: 6/18/2002 CLOSURE STATEMENT: ------------------- RELIABILITY ASSURANCE REVIEWED ALL GORE PANEL ENGINEERING DRAWINGS AND IDENTIFIED THE VISUAL AND DIMENSIONAL CHARACTERISTICS UNIQUE TO EACH PANEL. THESE DISCRIMINATING FACTORS CAN BE USED TO VERIFY GORE PANEL CONFIGURATION BASED ON PART THICKNESS AND/OR VISUAL CHARACTERISTICS, I.E. PENETRATION HOLES, WELD LUG PADS, ETC. G. DETERMINE POSSIBLE SCREENS/GATES IN THE BUILD PROCESS THAT WOULD HAVE DETECTED THE MISLOCATED GORE PANELS ON ET-129. RESPONSIBILITY: C. CULVER/3743- D. WESTPHAL/3740 M. PENO/3741 - D. WESTPHAL/3740 ECD: 6/25/2002 CLOSED: 6/25/2002 CLOSURE STATEMENT: ------------------ WELD LAND WIDTH INSPECTION IS PERFORMED IN 7 DIFFERENT PLANS (4 QUARTERS, 2 HALVES, 1 WHOLE). THE HAG-2 AND HAG-3 WELD LAND WIDTH INSPECTION, QUARTER PANEL LEVEL (GORE PANEL - 80914980994-004), SHOULD HAVE REJECTED THE GORE FOR MINIMUM WELD LAND WIDTH VIOLATION. THE HAG- 7 AND HAG-8 INSPECTION WAS NOT A SCREEN, AS THE WELD LAND (ASSOCIATED WITH GORE PANEL 80914980997-002) WOULD HAVE MET THE MINIMUM DIMENSION. THE LH2 AFT DOME INTERNAL HARNESS INSTALLATION (MPP 80934003719-500) PERFORMED IN VAB CELL E WOULD HAVE ADEQUATELY SCREENED ET-129 MISLOCATED GORE PANELS BY THE UTILIZATION OF SHOP AID TL10023299. H. IDENTIFY AND LOCATE ALL PARTS MARKED BY THE PRACTITIONER RESPONSIBLE FOR THE MISIDENTIFICATION OF THE GORE PANELS. RESPONSIBILITY: M. PENO/3741 - T. MCKEOUGH/3741 ECD: 6/26/2002 CLOSED: 6/26/2002 CLOSURE STATEMENT: ------------------ THE PRACTITIONER MARKED 42 DOME GORES AND OGIVE PANELS DURING THE DURATION OF HIS EMPLOYMENT AT AHF. SEVEN OF THESE PARTS FLEW ON ET-112, ONE PART IS ON ET-119 AFT DOME, TWO ARE LOCATED ON ET-120 AFT DOME, ONE IS ON ET-122 AFT OGIVE, FOUR ARE ON ET-123 AFT OGIVE, ONE IS ON ET-124 AFT OGIVE, THREE ARE ON ET-126 LOX DOME, ONE IS ON ET-127 FORWARD DOME, ONE IS ON ET-128 FORWARD DOME, ONE IS ON ET-128 AFT DOME, FIVE ARE ON ET-129 AFT DOME (INCLUDING THE 2 DISCREPANT PANELS), AND 15 PANELS ARE LOCATED IN INVENTORY STORES. I. PERFORM INSPECTION OF PARTS IDENTIFIED IN TASK I.H. RESPONSIBILITY: J. SPRAY/3724 - D. OWENS/3720 M. HEINSZ/3761 -S. PARIKH/3760 ECD: 06/28/2002 CLOSED: 6/26/2002 CLOSURE STATEMENT: ------------------ THE CONFIGURATION OF ALL 42 PANELS MARKED BY THE PRACTITIONER IN TASK I.H WERE VERIFIED AT MAF BY QUALITY CONTROL INSPECTIONS (8 PARTS) AND/OR INITIAL VERIFICATION BY LOCKHEED MARTIN SOURCE INSPECTOR PRIOR TO DELIVERY TO MAF (32 PARTS). NO IDENTIFICATION DISCREPANCIES WERE NOTED OTHER THAN THE INITIAL TWO DISCREPANT PARTS DOCUMENTED ON NCD N057622. REFERENCE QC INSPECTION SPREADSHEET (8 PARTS), AND E-MAIL FROM D. CAUSKY DATED 6/25/02. J. PERFORM A STATISTICAL ANALYSIS TO DETERMINE RELIABILITY CONFIDENCE LEVEL. RESPONSIBILITY: M. KELLEY/4210 - M. SIMPSON/4210 ECD: 6/28/02 CLOSED: 6/28/02 CLOSURE STATEMENT: ------------------- THROUGHOUT THE DURATION OF THIS INVESTIGATION, THE ACCEPTABILITY OF 2087 PARTS WAS VERIFIED. BASED ON 2085 OF 2087 ACCEPTABLE PARTS, A DEMONSTRATED RELIABILITY OF .997, WITH A CONFIDENCE LEVEL OF .95 IS REALIZED. REFERENCE E-MAIL FROM M. KELLEY DATED 6/25/02. K. TECH. OPS TO PERFORM ANALYSIS REGARDING INTERCHANGEABILITY OF ALL PARTS IDENTIFIED IN TASK I.B STARTING WITH LH2 GORE PANELS. ALSO PROVIDE RATIONALE TO SUPPORT ANY DISCRIMINATING ATTRIBUTES THAT WOULD CLEAR ANY OF THE HARDWARE LISTED. RESPONSIBILITY: G. WADGE/4420 - E. SWEET/4400 J. PILET/4130 - F. MANTO/4100 J. MCALLISTER/4110 - F. MANTO/4100 ECD: 6/28/2002 CLOSED: 6/25/2002 CLOSURE STATEMENT: ------------------- TECHNICAL OPERATIONS ASSESSMENT WAS PROVIDED THAT CONTAINED PHYSICAL AND DIMENSIONAL DISCRIMINATING FACTORS FOR EACH DOME AND OGIVE GORE PANEL. THIS INFORMATION WAS USED AS A SCREEN FOR PANELS TO VERIFY ACCEPTABILITY BASED ON CONFIGURATION. FOR EXAMPLE, TWO PANELS MARKED ON THE SAME DAY BY THE SAME PRACTITIONER ARE ACCEPTABLE IF THE PART CONFIGURATIONS ARE DIFFERENT AND THEY ARE NOT PHYSICALLY INTERCHANGEABLE. L. AHF TO PROVIDE RATIONALE PERTAINING TO POSSIBLE DISCRIMINATING ATTRIBUTES THAT WOULD EXONERATE ANY OF THE HARDWARE LISTED IN TASK I.B FOR MISIDENTIFICATION OF PARTS. RESPONSIBILITY: C. PEMBO/3761 - S. PARIKH/3760 J. BURKE/3830 - M. COMBS/3830 AHF ECD: 6/27/2002 CLOSED: 6/19/2002 CLOSURE STATEMENT: ------------------ 1. ALL HARDWARE SUPPLIED BY AHF OTHER THAN DOME AND OGIVE GORE PANELS RECEIVED SECONDARY VERIFICATION OF PART NUMBER AND SERIAL NUMBER MARKING. REFERENCE E-MAIL FROM C. PEMBO DATED 6/27/02, CONTAINING ATTACHMENT TITLED "AHF PART ID AND INSPECTION PRACTICES AS EXPLAINED BY DAN CAUSKY 6/26/02. 2. AHF HAS PROVIDED A LETTER FROM THE DIRECTOR OF QUALITY ASSURANCE CERTIFYING THE ACCEPTABILITY OF PARTS MARKED BY OTHER PRACTITIONERS BASED ON INTERVIEWS CONCERNING MARKING AND VERIFICATION TECHNIQUES. REFERENCE LETTER FROM PAUL WRIGHT TO DAN CAUSKY DATED 7/9/02. M. AHF TO PROVIDE A LISTING OF ALL PANELS INSPECTED AT THEIR FACILITY AS A RESULT OF THIS INVESTIGATION. RESPONSIBILITY: C. PEMBO/3761 - S. PARIKH/3760 J. BURKE/3830 - M. COMBS/3830 AHF ECD: 6/25/02 CLOSED: 6/25/02 CLOSURE STATEMENT: ------------------ ALL IN-PROCESS GORE PANELS AT AHF HAVE BEEN INSPECTED AND ARE ACCEPTABLE. REFERENCE E-MAIL CORRESPONDENCE FROM DAN CAUSKY TO CHRIS PEMBO DATED 6/25/02. N. DETERMINE IF ANY PARTS INSTALLED ON ET-93 & ET-115 WERE MARKED AT THE SAME TIME/LOCATION AS LIKE PARTS IN THE BUILD PROCESS AT AHF. RESPONSIBILITY: C. PEMBO/4210 - S. PARIKH/3760 J. BURKE/3830 - M. COMBS/3830 AHF ECD: 6/27/2002 CLOSED: 6/27/2002 CLOSURE STATEMENT: ------------------ THE PART NUMBER IDENTIFICATION DATES FOR THE PARTS INSTALLED ON ET-93 AND ET-115 WERE PROVIDED. THESE DATES WERE USED TO PROVIDE CLEARANCE OF FLIGHT HARDWARE BASED ON DISSIMILARITY OF THE PARTS MARKED ON A SPECIFIC DAY BY A SINGLE PRACTITIONER. DISSIMILAR PARTS COULD NOT HAVE BEEN MISMARKED AS A RESULT OF SWAPPED WORK FOLDERS. 21 OF 44 PANELS ON ET-93 WERE CLEARED WITH THIS SCREEN. PART IDENTIFICATION DATES WERE NOT OBTAINED FOR ET-115 GORE PANELS AS IT WAS DETERMINED THAT THEY ARE CLEARED BY SECONDARY VERIFICATION OF PART MARKING BY THE LOCKHEED MARTIN FIELD REPRESENTATIVE. TASK CLOSED ----------- CAUSE ----- PROBLEM 1: INADEQUATE PROCESS CONTROLS/EMPLOYEE ERROR PROBLEM 2: EMPLOYEE ERROR/LACK OF ATTENTION TO DETAIL TASK II. CORRECTIVE ACTION - PROBLEM #1 A. AHF INTERIM CORRECTION: (REFERENCE SCAR 02-041) 1. ALL WORK IN PROCESS AT THE DUCOMMUN AEROSTRUCTURES AHFD, AEROCHEM ORANGE AND EL MIRAGE FACILITIES WAS VALIDATED TO ENSURE NO OTHER DEFECTS OF THIS NATURE WERE PRESENT. NO OTHER PROBLEMS WERE NOTED. 2. QUALITY ALERT # 002702 ISSUED AT AHF TO ADDRESS RECOMMENDED PRACTICE FOR MARKING/VERIFICATION OF LOCKHEED MARTIN HARDWARE. 3. 100% VERIFICATION BY LM SOURCE REPRESENTATIVE. B. AHF LONG TERM (REFERENCE SCAR 02-041) 1. REVISED AHF PLANNING TO REQUIRE THAT PRACTITIONER VERIFY PART NUMBER ON TOOLING TAB, PART AND WORK FOLDER PRIOR TO FINAL PART MARKING. 2. REVISED AHF PLANNING TO ADD A CONFIGURATION VERIFICATION STEP CONTAINING INSTRUCTIONS TO RANDOMLY VERIFY CHEM. MILL THICKNESS TO VALIDATE HARDWARE CONFIGURATION PRIOR TO PART MARKING. 3. A SECOND HARDWARE VERIFICATION STEP HAS BEEN ADDED AFTER PART MARKING OPERATIONS, WHICH IS TO BE PERFORMED BY A SECOND INDEPENDENT QUALITY INSPECTOR. 4. REVISED AEROCHEM BUILD PAPER TO VERIFY PART NUMBER ON TOOLING TAB, PART AND WORK FOLDER WHEN RECEIVED FOR FINAL CLEANING. C. MAF PROCUREMENT QUALITY ALL ET HARDWARE SUBCONTRACTORS HAVE BEEN DIRECTED TO IMPLEMENT, BY OCTOBER 1, 2002, THE FOLLOWING REQUIREMENTS: 1. PROVIDE SPECIFIC INSTRUCTIONS IN MANUFACTURING PLANNING DOCUMENTS AT MARKING OPERATIONS SUCH AS: A. THE PART NUMBER TO BE MARKED ON THE PART. B. DESCRIBE SPECIAL MARKING STEPS AS ACTUALLY PERFORMED. 2. INCLUDE AN INDEPENDENT VERIFICATION OF MARKED PART NUMBERS (MAY BE PERFORMED BY EITHER SHOP OR QC PERSONNEL). A. RECORD AS-MARKED PART NUMBERS IN TRAVELERS. B. PERFORM CONFIGURATION CHECK VIA UNIQUE FEATURE VERIFICATION. RECORD THE FEATURE(S) USED TO VERIFY PART CONFIGURATION ON THE TRAVELER AT THE IDENTIFICATION MARKING OPERATION. NOTE: IN THE INTERIM, ALL LMSSC MICHOUD OPERATIONS PROCUREMENT QUALITY CONTROL FIELD REPRESENTATIVES WILL VERIFY PART MARKING USING THESE REQUIREMENTS ON 100% OF HARDWARE PRIOR TO FINAL ACCEPTANCE. (REFERENCE MEMO TO M. COMBS FROM CHRIS PEMBO DATED 7/29/02) CORRECTIVE ACTION - PROBLEM #2 (MAF) ------------------------------------- QUALITY CONTROL HAS ADDRESSED THE QUALITY ESCAPE BY ISSUING "MAF LESSON HUDDLE GUIDE - C" THAT ADDRESSES "WELD LAND DIMENSIONAL VERIFICATION". A HUDDLE WAS HELD TO DISCUSS THE NEED FOR VERIFYING WELD LAND WIDTHS WITH THE APPROPRIATE ENGINEERING DRAWING IN HAND. ALSO STRESSED WAS THE POINT THAT ALL WORK SHALL BE WARRANTED BY INSPECTOR STAMP. TASK CLOSED ------------ TASK III. CLEARANCE OF EFFECTIVITIES THIS IS AN ISOLATED CASE. THE BASIS IS AS FOLLOWS: IN THE TIME FRAME OF 1996 - 2000, AN INDEPENDENT VERIFICATION OF PART NUMBER WAS PERFORMED BY A LOCKHEED MARTIN FIELD REPRESENTATIVE. THIS REPRESENTATIVE PERFORMED VERIFICATION OF LOCKHEED MARTIN PART NUMBER AND SERIAL NUMBER AGAINST WORK ORDER AND TOOL TAB IDENTIFICATION. DURING THIS TIME, ALL PARTS WERE SHIPPED TO MAF DIRECTLY FROM AHF. CLEANING OPERATIONS WERE PERFORMED AT AHF VS. AEROCHEM, EL MIRAGE (CURRENT PRODUCTION). 100% PART VERIFICATION WAS PERFORMED AS OPPOSED TO CURRENT SURVEILLANCE INSPECTION. (REFERENCE E-MAIL FROM M. HEINSZ DATED 7/2/02 WITH ATTACHMENT TITLED "PQCFR GORE/OGIVE SURVEILLANCE AT AHF") INDEPENDENT VERIFICATION PROVIDES CONFIDENCE FOR HARDWARE PRODUCED DURING THIS PERIOD. APPROXIMATELY 2,073 GORES AND OGIVES WERE RECEIVED FROM AHF DURING THIS TIME PERIOD. THIS VERIFICATION COMPLETELY CLEARS FLIGHT HARDWARE ON ET-115 THROUGH ET-122 AND PORTIONS OF ET-123 THROUGH CURRENT PRODUCTION, INCLUDING SOME OF THE INVENTORY PARTS. HARDWARE INSPECTIONS PERFORMED BY MAF QUALITY CONTROL DEPARTMENT (282 PARTS) WERE USED TO CLEAR ALL REMAINING PANELS ON ET-123 THROUGH CURRENT PRODUCTION. TWELVE TOTAL PARTS (OGIVES/DOME GORES) COULD NOT BE CLEARED ON ET-93 BY THIS SCREEN OR INSPECTIONS. NCD N031972 WAS GENERATED TO PERFORM INSPECTIONS ON THE AFT LH2 DOME OF ET-94 STAGED IN FINAL ASSEMBLY POSITION 2. THESE NCD DIRECTED INSPECTIONS ON ET-94 VERIFIED THE CONFIGURATION ON FOUR DOME GORE PANELS. ONE OTHER PANEL WAS CLEARED AS A RESULT OF THE TIMING OF PART MARKING AT AHF (BASED ON THE ACCEPTABILITY OF THE FOUR PANELS VERIFIED BY THIS NCD). THESE SCREENING PROCESSES AND INSPECTIONS CLEARED ALL EXCEPT 8 TOTAL PARTS ON ET-94. ENGINEERING PERFORMED A FLIGHT SAFETY RISK ASSESSMENT ON ALL REMAINING QUESTIONABLE PANELS. THIS CONSISTED OF A CONSERVATIVE "POINT- BY-POINT" SHELL STABILITY ANALYSIS. ALL PANELS DEMONSTRATED A FACTOR OF SAFETY GREATER THAN 1.0. ALL AFOREMENTIONED FLEET CLEARANCE RATIONALE IS PROVIDED HEREIN AS INFORMATION ONLY AS THIS IS AN ISOLATED CASE AND HAS BEEN PRESENTED AS SUCH TO THE ET PROJECT AND SHUTTLE MANAGEMENT. TASK CLOSED ----------- TASK IV. CAPS CLOSURE SUMMARY -------------------- QUALITY CONTROL INSPECTION FAILED TO DETECT A VIOLATION OF MINIMUM WELD LAND WIDTH ON ET-129 LH2 AFT DOME HAG-3 WELD AT THE QUARTER PANEL LEVEL. THE CAUSE OF ISSUE #1 IS EMPLOYEE ERROR. THE FAILED INSPECTION RESULTED IN TWO PREVIOUSLY MISIDENTIFIED PANELS AT THE SUPPLIER BEING WELDED INTO A COMPLETED DOME. NCD N057622 WAS GENERATED TO DOCUMENT THE NONCONFORMING CONDITION OF THE HARDWARE. THIS NONCONFORMANCE WAS IDENTIFIED AT MAF DURING INSPECTION OF COMPLETED DOME WELD LAND WIDTHS. CORRECTIVE ACTION FOR ISSUE #1 WAS IMPLEMENTED BY QUALITY CONTROL BY THE RELEASE OF "MAF LESSON HUDDLE GUIDE-C", IN WHICH THE IMPORTANCE OF UTILIZING ENGINEERING DRAWINGS FOR WELD LAND WIDTH VERIFICATION IS MANDATORY. ALSO STRESSED WAS THE IMPORTANCE OF STAMP WARRANTY OF ALL WORK. QUALITY INVESTIGATION IDENTIFIED INCORRECT PART NUMBERING AND INADEQUATE PART NUMBER VERIFICATION AT THE DOME GORE SUPPLIER (AHF) AS THE CAUSE OF MISMARKING IN ISSUE #2. THE PRACTITIONER RESPONSIBLE FOR MARKING THE PARTS AT AHF MIXED THE WORK FOLDERS AND TRANSPOSED THE PART NUMBERS. THIS PRACTITIONER WAS WORKING TWO JOBS WITH SIMILAR AHF TRACKING NUMBERS (9090 VS. 9099) AT THE TIME THE MISIDENTIFICATION OCCURRED. CORRECTIVE ACTIONS HAVE BEEN IMPLEMENTED AT AHF TO PREVENT THE RECURRENCE OF PART MARKING DISCREPANCIES. AHF PLANNING HAS BEEN REVISED TO PROVIDE SECONDARY VERIFICATION OF PART MARKING AND TO ADD A CONFIGURATION VERIFICATION OF THE HARDWARE. ALL OTHER ET HARDWARE SUPPLIERS ARE ALSO REQUIRED TO REVISE PLANNING TO ADD SECONDARY VERIFICATION OF PART MARKING, AND TO ADD CONFIGURATION VERIFICATIONS. THE ET-129 LH2 AFT DOME GORE MISLOCATION IS AN ISOLATED CASE. A LARGE DATABASE OF SUPPORTING EVIDENCE HAS BEEN COMPILED TO SUPPORT THIS FACT. NO OTHER PART MARKING NONCONFORMANCES OF THIS TYPE HAS BEEN IDENTIFIED. OF 7,407 PARTS RECEIVED FROM AHF, ONLY THIS CASE (2 PARTS) OF PART NUMBER TRANSPOSITION HAS BEEN IDENTIFIED. INSPECTION OF REMAINING PARTS IN INVENTORY AND ON REMAINING FLIGHT HARDWARE IS NOT REQUIRED. TASK CLOSED ----------- |
| MSFC Response/Concurrence 08/26/02 - MSFC APPROVED FULL CLOSURE. SIGNATURES ARE ON FILE IN THE PAC. |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A17800 | IFA# -- | Contractor RPT# S-088 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 80914900900-509 | Asmnt Part Name LH2 AFT DOME | Asmnt Serial/Lot# 1247810 |
| HCRIT CD 1 | FCRIT CD 1 | CAUSE CD MW - MFG-WORK | FAIL MODE MU - MECH TOLRNCE |
| Asmnt FMEA 6.2.1.1 | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |