TRW Inc.	One Space Park

Space & Electronics Group	Redondo Beach CA 90278

EOS AQUA

X-BAND DIRECT BROADCAST

INTERFACE DESCRIPTION DOCUMENT

Date:  8 June 2001	No. D26699

Rev:  A

| Superseding: | New |
| --- | --- |

PREPARED FOR:	NASA GSFC

Greenbelt, MD 20771

CDRL 2208

Copyright © 1998 TRW Inc., All Rights Reserved.  This copyrighted material was generated using funding provided by the United States National Aeronautic and Space Administration under Contract No. NAS5-32954.

| TRW Space, Defense & Information Systems | One Space Park Redondo Beach, CA 90278 | TRW |
| --- | --- | --- |
| Revision/Change Record | For Document No. | D26699 A |

| SYMBOL | DATE | AUTHORIZATION | REVISION DESCRIPTION | PAGES AFFECTED |
| --- | --- | --- | --- | --- |
| New | 4/28/98 | Original PDMO | Initial Issue | All |
|  |  | Release | CDRL 2208 |  |
| A | 6/8/01 |  | Revision A Update | See Change Bars |
|  |  | ________________________ |  |  |
|  |  | G. M. Haney |  |  |
|  |  | Comm. Subsystem Mgr. |  |  |
|  |  | ________________________ |  |  |
|  |  | S. Staich |  |  |
|  |  | System Engineering Mgr. |  |  |
| (FILE DIRECTLY AFTER COVER SHEET) |

Table of Contents

1.	INTRODUCTION	2

1.1	PURPOSE	2

1.2	INTERFACE RESPONSIBILITIES	2

1.3	INTERFACE IDENTIFICATION	2

1.3.1	RF Link Definition	2

1.3.2	Functional Description	3

1.3.3	Link Calculations	3

1.3.4	Data Formats	3

2.	DOCUMENTS	4

2.1	Applicable Documents	4

2.2	Reference Documents	4

2.3	Other Related Documents	4

3.	COMMUNICATIONS FUNCTIONAL INTERFACE	5

3.1	General	5

3.1.1	Interface RF Links	5

3.1.2	Interface Functional Applicability	5

3.2	Spacecraft Communications Subsystem Overview	5

3.3	Communications Performance Characteristics	7

3.3.1	Science Data Channel BER	7

3.3.2	PRBS Test Channel BER	7

3.4	Communications Functional Characteristics	7

3.4.1	Science Data Mode	7

3.4.2	Pseudo-Random Bit Stream (PRBS) Mode	7

4.	LINK INTERFACE CHARACTERISTICS	8

4.1	Link Functional Design	8

4.1.1	Spacecraft to Ground Station Design	8

4.1.2	Spacecraft to Ground Station Functional Description	9

4.2	Signal Characteristics and Constraints	11

4.2.1	Science Frame Format	11

4.2.1.1	Reed-Solomon Coding	11

4.2.1.2	Bit Transition Generator	11

4.2.2	Signal Characteristics	12

4.2.2.1	Data Signal Format	13

4.2.2.2	Data Rate Accuracy	13

4.2.3	Modulated Signal Constraints	13

4.2.3.1	Downlink Frequency	14

4.2.3.2	Downlink Frequency Stability	14

4.2.3.3	Phase Noise	14

4.3	Downlink Acquisition and Tracking	15

4.3.1	EBS Station Characteristics	15

List of Figures

Figure 1.3-1:  RF X-band Direct Broadcast Downlink	3

Figure 3.2-1:  Communications Subsystem X-band section block diagram	6

Figure 4.1-1:  Spacecraft-to-EDBS ground station downlink configuration	9

Figure 4.2-1:  Channel Access Data Unit (Sync + coded VCDU)	11

Figure 4.2-2:  Digital data Signal Formats	13

List of Tables

Table 3.4-1:  X-band Broadcast downlink modes	8

Table 4.2-1:  X-band Downlink Signal Characteristics	12

Table 4.2-2:  X-band Downlink Signal Constraints	14

Table 4.3-1:  X-band EOS Direct Broadcast Station G/T values	15

List of Appendices

Appendix A:  Link Calculations	16

Appendix B:  X-band EC Antenna Pattern	20

Interface Description Document

for

EOS AQUA X-band Direct Broadcast

PREFACE

This EOS AQUA Spacecraft Radio Frequency (RF) Interface Description Document (IDD) describes the X-band Direct Broadcast link between EOS AQUA Spacecraft and the Earth Observing System Direct Broadcast Stations (EDBS).

A Document Change Notice (DCN) will be issued to update the document for any future approved changes.  Changes to this document will be controlled through the TRW Change Control Board (CCB).

Any changes or questions concerning this document should be addressed to:

Communications Subsystem Manager for EOS

TRW, S&LPD

One Space Park

Redondo Beach, CA  90278

# INTRODUCTION

## PURPOSE

The Interface Description Document (IDD) describes technical aspects of the Direct Broadcast (DB) radio frequency interface between the EOS AQUA spacecraft and the worldwide Earth Observing System Direct Broadcast Stations (EDBS) within line-of-sight view.  The EDBS will be used to provide DB science and engineering data service in real time via X-band downlink transmission.

## INTERFACE RESPONSIBILITIES

Interface responsibilities are defined in terms of the Goddard Space Flight Center (GSFC) EOS AQUA Project Office.  The portion identified as the EOS AQUA spacecraft is the responsibility of the GSFC EOS AQUA Project Office.  The design characteristics and parameters in this IDD are subject to the joint control of the GSFC EOS AQUA Project Office and the TRW EOS AQUA Program Office. The GSFC Operations Manager of the EOS AQUA Project and his Designee and the Designee of the TRW EOS AQUA Program Office will jointly approve this IDD upon resolution of issues and discrepancies as agreed upon by these parties.

## INTERFACE IDENTIFICATION

### RF Link Definition

The communications subsystem interface defined by this IDD is the X-band DB transmission link between the EOS AQUA spacecraft and the Earth Observing System direct broadcast ground stations.  Figure 1.3-1 depicts the RF downlink between the Spacecraft and an EOS Direct Broadcast Ground Station.

Figure 1.3-1:  RF X-band Direct Broadcast Downlink

### Functional Description

In the Broadcast mode the spacecraft continuously transmits all real-time instrument science data, real-time spacecraft engineering (housekeeping) data, ground-based attitude determination data, and instrument engineering (housekeeping) data as it travels in a sun-synchronous near circular orbit at a nominal altitude of 705 km.  The data rate is 15 Mbps at a nominal downlink frequency of 8160 MHz.  In normal operations the Broadcast mode will be used during most of the orbit.  The only time it is not used is during the approximate 8 minutes of every 99 minute orbit when the Playback or Downlink modes are active in playing back stored or real time data to the two Earth Observing System Polar Ground Stations (EPGS).  The RF interfaces between the EOS AQUA Spacecraft and the EPGS are defined in a separate RF Interface Control Document (ICD) referenced in Section 2.

### Link Calculations

The RF link calculations contained in Appendix A for the Spacecraft modes of operation are included only as supporting data and do not constitute a formal part of the IDD agreement.  The X-band earth coverage antenna pattern data provided in Appendix B are included for information purposes and are also not a formal part of this IDD.

### Data Formats

The data contents and formats are described in Section 6 of D22262 (Reference Document 2.2.a).

# DOCUMENTS

## Applicable Documents

The following documents are applicable to the E0S AQUA Spacecraft.  In the event of conflict between this IDD and the documents listed below, the documents below govern.

a.	GSFC-422-13-11-01, EOS-Common Spacecraft Specification, August 1994.

b.	SS6-0165, TRW EOS Common Spacecraft Communications Subsystem Specification, 23 June 1997

## Reference Documents

The following documents are reference documents applicable to the RF interface.  These documents do not form a part of this IDD and are not controlled by their reference herein.

a.	D22262, Interface Control Document between the EOS PM-1 Spacecraft and the EOS Ground System, October 1998.

b.	EPGS document,  Radio Frequency Interface Control Document between the EOS AQUA Spacecraft and the EOS Polar Ground Stations (EPGS) and the Wallops Island Station (WPS), February 1999, DCN 001.

c.	GSFC 422-11-12-01,  General Interface Requirement Document for EOS Common Spacecraft/Instruments, January 1994.

d.	GSFC EOS Mission Operations Concept Document, March 1993.

## Other Related Documents

The following documents are listed for the convenience of the user.  These documents do not form a part of this IDD and are not controlled by their reference herein.

a.	CCSDS 701.0-B-2  "Advanced Orbiting Systems, Networks and Data Links: Architectural Specification", Issue 1, Blue Book, Consultative Committee for Space Data Systems, November 1992.

b.	CCSDS 101.0 B-3  "Telemetry Channel Coding" Blue Book, May 1992.

# COMMUNICATIONS FUNCTIONAL INTERFACE

## General

### Interface RF Links

This section defines the required RF communication downlinks:

1.	Spacecraft-to-EDBS  X-band Direct Broadcast (DB) data link

2.	Spacecraft-to EDBS X-Band Direct Broadcast Pseudo-Random Bit Stream (PRBS) link

### Interface Functional Applicability

The RF communications interface functional and performance capabilities shall be applicable to the following project phases:

a)	RF Compatibility Testing

b)	End-to End (ETE) Testing:  Full X-band capability

c)	Pre-launch:  Check-out

d)	Orbit acquisition initialization and orbit acquisition: X-band communication links

f)	Operations Phase - Full X band communications capability

g)	End-of-Mission phase: X-band communication links

## Spacecraft Communications Subsystem Overview

A block diagram of the X-band section is shown in Figure 3.2-1.  It consists of two modulators, a hybrid coupler, two traveling wave tube amplifiers (TWTAs), two isolators, a waveguide switch, a bandpass filter, a lowpass filter, and an X-band earth coverage antenna.

Each of the identical modulators receives broadcast or playback I and Q channel data from the Formatter Multiplexer Unit (FMU) in the Command and Data Handling (C&DH) subsystem.  A clock signal is output from the active modulator to the FMU, setting the modulator input data rate.  For the AQUA mission, the data rate is 15.Mbps using the Direct Broadcast link.  The I& Q channels are balanced and alternating bits of the data stream are placed on each channel at 7.5.Mbps.  The incoming data is then directly Staggered Quadriphase Shift Key (SQPSK) modulated onto an 8160.MHz carrier. The resulting RF signal is then sent to the active TWTA via the 3 dB hybrid coupler.  The coupler provides cross strapping between the redundant modulators and redundant TWTAs.

Each X-band TWTA consists of a traveling wave tube and power converter. The power converter generates the required traveling wave tube voltages from the spacecraft DC power bus.  To prevent TWTA damage and/or performance degradation due to potential voltage reflection an isolator is used at the TWTA output.  The active TWTA amplifies the modulated input signal to a nominal saturated output power of 25.Watts (23.Watts EOL minimum).  The resulting RF signal is routed through a waveguide switch to the filters.  This switch provides a two-for-one redundancy of the RF signal path.

Prior to transmission through the earth coverage antenna, the TWTA output signal is filtered by a bandpass filter and a lowpass filter.  The purpose of the filters is twofold.  First, the bandpass filter reduces the portion of the spectrum falling within the Deep Space Research band (8400.MHz to 8450.MHz) to meet the CCIR recommended power spectral density requirement at the ground.  Second, the lowpass filter suppresses harmonic components to comply with on-board instrument noninterference requirements.

After filtering, the signal is radiated with Right Hand Circular Polarization (RHCP) through the X-band earth coverage antenna.  The antenna is mounted at the end of a boom that is developed after launch to obtain a full earth field-of-view.  Across a 63.8 degree half cone angle the reflector is shaped to provide approximately constant power density to any earth station with line-of-sight view as the spacecraft passes overhead.  Since a 5 degree ground station elevation angle corresponds to 63.8 degrees from antenna Nadir, the cone represents the nominal operating beamwidth of the antenna.

Figure 3.2-1:  Communications Subsystem X-band Section Block Diagram

## communications performance characteristics

RF link performance characteristics for the communications functional capability described in Paragraph 3.4 are defined in this section.  The EDBS communications performance characteristics are based on the presumption that the Spacecraft and EDBS each perform in accordance with the X-band performance parameters defined in Section 4.

### Science Data Channel BER

The maximum X-band downlink BER for the detected digital science data in the data channel shall be (10-3, referenced to the input of a Reed-Solomon Decoder on the ground.  This assumes the link meets the characteristics given in Sections 4.2 and 4.3.

### PRBS Test Channel BER

The maximum X-band downlink BER for the PRBS test channel shall be (10-3 referenced to the input of a Reed-Solomon decoder on the ground.  This assumes the link meets the characteristics given in Sections 4.2 and 4.3.

## Communications Functional Characteristics

Section 3.4.1 and 3.4.2 describes the Communications functional characteristics which exist between the Spacecraft and the EDBS.  This is dependent upon favorable radio line of sight conditions and when the station antenna elevation angle is greater than 5 degrees (above the local mask).  The Spacecraft X-band downlink Broadcast modes are shown in Table 3.4-1.

### Science Data Mode

Transmission from the Spacecraft to EBS of real time science and engineering data on the I and Q channels will be at a total data rate of 15 Mbps.  Science data shall be formatted in accordance with the characteristics outlined in Section.4.2.

### Pseudo-Random Bit Stream (PRBS) Mode

PRBS test data will be generated in the Formatter Multiplexer Unit (FMU) of the C&DH subsystem and sent to the X-band modulator on the I and Q channels maintaining a total data rate of 15.Mbps.  The PRBS test mode is used for the purpose of bit error rate (BER) checking, as required.  It is not a normal X-band downlink service

Table 3.4-1:  X-band Broadcast Downlink Modes

| Mode | Description | I/Q Data Rate [Mbps] | Data Type |
| --- | --- | --- | --- |
| DB | Direct Broadcast (worldwide) | 7.5 / 7.5 | All real-time S&E data |
| TB | Test Broadcast | 7.5 / 7.5 | PRBS |
| S&E: Science and Engineering |
| PRBS: Pseudo Random Bit Stream |

# LINK INTERFACE CHARACTERISTICS

This section describes the functional design of the RF Direct Broadcast link. Spacecraft and EDBS communications system performance and signal characteristics are also described.

## Link Functional Design

### Spacecraft to Ground Station Design

The X-band section provides the downlink interface for both the Direct Broadcast and Direct Broadcast Test modes.  For EDBS support of the EOS AQUA mission, the Direct Broadcast link will be utilized to transmit real time science and engineering data to the ground stations.  Therefore, Pseudo-Random Bit Stream (PRBS) test data transmission will be used only for bit error rate performance checking.  In other words, when the PRBS test mode is on, the Direct Broadcast mode will be off.

Figure 4.1-1:  Spacecraft-to-EDBS Ground Station Downlink Configuration

### Spacecraft to Ground Station Functional Description

The functional interface of this link is shown in Figure 4.1-1.  EBS configuration is shown for information purposes only.  On the Spacecraft, data from the Formatter Multiplexer Unit (FMU) in the C&DH subsystem is processed in real time at 15 Mbps.  It is bit interleaved into two streams of 7.5 Mbps (one for the I-channel and one for the Q-channel) and sent to the X-band modulators.  Each data stream is sent using the Non-Return to Zero Mark (NRZ-M) format.  In the PRBS test mode, the data is a PRBS.  This is generated in the FMU and sent also via NRZ-M format on the I and Q channels at a rate of 7.5 Mbps each.

Irrespective of the transmission mode selected, the I and Q channel data is Staggered Quadrature Phase Shift Keying (SQPSK) modulated onto the X-band carrier with an I/Q channel power ratio of 1-to-1.  The Q-channel data is modulated on the Q-carrier which is delayed by 90 degrees with respect to the I-channel data carrier.  The I-channel and Q-channel staggered data relationship is such that the Q-channel data is delayed by 0.5 ( 0.1 symbol with respect to the I-channel data.  The X-band carrier at a frequency of 8160 MHz is derived from an internal oscillator in the modulator.  The traveling wave tube amplifier (TWTA) performs amplification of the SQPSK signal received from the modulator to the nominal saturated output power of 25 Watts (23 Watts EOL minimum) for data transmission.  The X-band filters suppress harmonic components and out-of-band emissions from the TWTAs, and also suppress the portion of the X-band spectrum falling within the Deep Space Research 8.4 to 8.45 GHz frequency band.  The link uses the RHC polarized earth coverage antenna to transmit the signal to EDBS.

As illustrated in Figure 4.1-1, once the input signal at the EBS antenna is received, it is downconverted before being input to the SQPSK receiver/demodulator.  A separate tracking receiver may be utilized for antenna auto-tracking purposes.  The SQPSK receiver/demodulator demodulates the downconverted signal into separate I and Q channel data streams.  Following QPSK demodulation, the bit synchronizers recover bit clock.  The 7.5 Mbps I and Q channels Broadcast data stream may then be combined into one single stream of 15 Mbps.  For the PRBS test mode, the data may be provided to a BER test set for BER performance testing.

## Signal Characteristics and Constraints

This section provides a description of the signal characteristics and constraints of the X-band downlink signal to the EBS.

### Science Frame Format

The science and engineering data transmitted via Direct Broadcast will be formatted for transmission at 15 Mbps over the X-band link as specified in D22262 (Interface Control Document between the EOS AQUA Spacecraft and the EOS Ground System).  See Figure 4.2-1 for the downlink transfer frame format.

Figure 4.2-1:  Channel Access Data Unit (Sync + coded VCDU)

#### Reed-Solomon Coding

To provide improved bit error performance, the downlink data will have a (255,223) Reed-Solomon code with interleave depth I = 4.

#### Bit Transition Generator

a.	The pseudo-random bit stream (PRBS) is generated by the Spacecraft using the following bit transition generation function (refer to CCSDS 101.0 B-3 "Telemetry Channel Coding" Blue Book, May 1992, pp. 6-1):

h(x) = x8 + x7 + x5 + x3 + 1

b.	This bit sequence repeats after 255 bits and the randomizer is reinitialized to an all-ones states during each Synchronization Marker period.  The first 40 bits of the pseudo-random bit stream are shown below: the left-most bit is the first bit of the sequence and is exclusively ORed with the first bit of the CVCDU.

1111   1111   0100   1000   0000   1110   1100   0000   1001   1010

### Signal Characteristics

The Spacecraft X-band downlink signal characteristics are contained in Table 4.2-1.  As noted, the Balanced SQPSK modulated signal (channel power ratio of 1-to-1) is radiated using a RHC polarized (Earth Coverage) antenna on the Spacecraft.

Table 4.2-1:  X-band Downlink Signal Characteristics

| Parameter | Requirement |
| --- | --- |
| Center Frequency | 8160 MHz |
| Bandwidth (1st null-to-1st\ null) | 15 MHz* |
| Data Modulation | SQPSK |
| Data Format | NRZ-M |
| I/Q Power ratio | 1 : 1 |
| Operational Duty Cycle | 100% |
| Antenna Coverage from nadir | ±63.8° |
| Antenna Polarization | RHCP |
| Data Rate | 15 Mbps |
| Coding | Reed-Solomon (255-223) (No Convolutional Coding) |
| * Channel bandwidth (150 MHz |

#### Data Signal Format

The science data signal output from the FMU of the C&DH subsystem is in NRZ-M signal format prior to the modulator.  The format for NRZ-M data shall conform to that shown in Figure 4.2-2.

Figure 4.2-2:  Digital Data Signal Formats

#### Data Rate Accuracy

Accuracy of the Direct Broadcast 15 Mbps data rate is within ±1.8 Kbps.

### Modulated Signal Constraints

The signal constraints of the X-band Direct Broadcast link are in accordance with Table 4.2-2.  The X-band carrier is SQPSK modulated using the I and Q baseband signals.

Table 4.2-2:  X-band Downlink Signal Constraints

| Parameter | Requirement |
| --- | --- |
| Frequency Stability a) 1 second average b) 5 hour average | ±0.003  10-6 ±0.1  10-6 |
| Phase Noise 10 to 100 Hz 100 to 1000 Hz 1000 to 1 MHz | ( 7.5° RMS ( 2.0° RMS ( 2.0° RMS |
| Data Asymmetry @ 15 Mbps | ( 0.4 % |
| I/Q Data rise/fall Time | ( 2.5 nanosec. |
| Data Bit Jitter | ( 5 % |
| I/Q Data Skew (Q delayed 0.5 bit) | 0.5 ± 0.1 bit |
| SQPSK Amplitude Imbalance | ( 0.5 dB p-p |
| SQPSK Phase Imbalance | ( 4° .. |
| SQPSK Carrier Suppression | 30 dBc |
| Gain Slope† | 0.2 dB/MHz |
| AM/PM | ( 5°/dB |
| Spurious PM | < 2° RMS |
| Gain Flatness‡ | < 2.0 dB p-p |
| Phase Nonlinearity‡ | < 12° p-p |
| † Over 150 MHz bandwidth centered at 8160 MHz |
| ‡ Over 15 MHz centered at 8160 MHz |

#### Downlink Frequency

The Spacecraft X-band downlinks use a single fixed frequency reference for the transmit carrier.  The frequency reference source is generated by an internal oscillator.  The carrier frequency derived from the oscillator is 8160 MHz within the 8025-8400 MHz bandwidth.  The frequency characteristics of the oscillator are given below.

#### Downlink Frequency Stability

The frequency stability of the oscillator will be equal to or better than the value specified in Table 4.2-2.  Long term stability will be less than ±210-6/YR and the initial set tolerance will be less than  ±210-6.  Over a -20°C to +60°C temperature range the stability will be less than ±610-6.

#### Phase Noise

The carrier phase noise will be equal or better than the values specified in Table 4.2-2.

## Downlink Acquisition and Tracking

### EDBS Station Characteristics

The EDBS station parameters need to be better than or equal to the G/T values shown in Table 4.3-1 to insure the specified BER performance.

Table 4.3-1:  X-band EOS Direct Broadcast Station G/T Values

| Elevation | EDBS Ground Station G/T |
| --- | --- |
| [deg.] | [dB/K] |
| 5° | 21.0 |
| 40° | 22.5 |
| 70° | 22.7 |
| 90° | 23.4 |

Appendix A

LINK CALCULATIONS

Table A-1:  Broadcast Link Margin Summary

| Ground Elevation | Nominal Margin [dB] | Adverse Margin [dB] |
| --- | --- | --- |
| 5° elevation <=> 63.8° off-Nadir | 5.7 | 4.8 |
| 71° elevation <=> 17° off-Nadir | 4.6 | 2.6 |
| 90° elevation <=> 0° off-Nadir | 8.8 | 8.1 |

Table A-2:  Direct Broadcast Mode - 15 Mbps X-band Downlink Budget

|  | Parameter | Results at off-nadir angles,  | Units | Adverse Tolerance | Items in |
| --- | --- | --- | --- | --- | --- |
|  |  | 63.8° | 17° | 0° |  | (dB) | Table A-3 |
| 1. | TWTA Tx Output Power | 14.0 | 14.0 | 14.0 | dBW | 0.4 | Item 2 |
| 2. | Transmit Circuit loss | -3.0 | -3.0 | -3.0 | dB | 0.2 | Item 3 |
| 3. | Antenna loss/gain | 6.8 | -7.2 | -4.1 | dBi | 0.5,1.6,0.3 | Item 4 a, b, &, c |
| 4. | EOS EIRP | 17.8 | 3.8 | 6.9 | dBWi |  | ( |
| 6. | Space loss/gain | -178.9 | -168.1 | -167.6 | dB | - | Item 6 a, b, &, c |
| 7. | Atmospheric loss/gain | -0.5 | 0.0 | 0.0 | dB | - | Item 7 a, b, &, c |
| 9. | Polarization loss/gain | -0.4 | -0.5 | -0.6 | dB | 0.6,1.2,0.4 | Item 9 |
| 10. | Received isotropic power | -162.0 | -164.8 | -161.3 | dBWi |  | ( |
| 11. | User Ground Terminal G/T | 21.0 | 22.7 | 23.4 | dBi/K | - | Item 10 a, b, &, c |
| 12. | 1/Boltzmann's constant | 228.6 | 228.6 | 228.6 | dBHzK/W | - | 1.38*10^-23 W s / K |
| 13. | 1/Data rate | -71.8 | -71.8 | -71.8 | dB-sec. | - | Item 11 |
| 14. | Received Eb/No | 15.8 | 14.7 | 18.9 | dB |  | ( |
| 15. | Implementation loss/gain | -3.3 | -3.3 | -3.3 | dB | - | Item 12† |
| 16. | Required Eb/No | -6.8 | -6.8 | -6.8 | dB | - |  |
| 17. | Nominal link margin | 5.7 | 4.6 | 8.8 | dB |  |  |
|  | Adverse tolerance | -0.9 | -2.0 | -0.7 | dB | 0.9,2.0,0.7 | Adverse Tolerance |
| 18. | Adverse link margin | 4.8 | 2.6 | 8.1 | dB |  | Margin less adv. tol. |

Note:  End-to-end data rate refers to the 15 Mbps data stream at input to Reed-Solomon decoder

† Implementation loss is an estimate of spacecraft constraint loss plus ground station signal processing loss, individual user ground station loss could be higher.

Table A-3:  X-band Downlink Budget - Parameters

|  | Parameter | Units | Value | Adv. | Comments |
| --- | --- | --- | --- | --- | --- |
| 1. | Frequency | GHz | 8.1600 |  | Selected frequency in 8.025 - 8.400 GHz band |
| 2. | TWTA Transmit Output Power | dBW | 14.0 | 0.4 | 25W nominal, 23W spec. |
| 3. | Transmit Circuit Losses | dB | 3.0 | 0.2 | Current measurement |
| 4. | Antenna Gain |  |  |  |  |
|  | (a) 5° elev. <=> 63.8° off-Nadir | dBi | 6.8 | 0.5 | Measurements, avg. (SN301 Antenna) |
|  | (b) 71° elev. <=> 17° off-Nadir | dBi | -7.2 | 1.6 |  |
|  | (c) 90° elev. <=> 0° off-Nadir | dBi | -4.1 | 0.3 |  |
| 6. | Space Loss |  |  |  | From EOS to X-band ground terminal |
|  | (a) 5° elevation angle | dB | 178.9 |  | Range at 2574 km. is maximum range |
|  | (b) 71° elevation angle | dB | 168.1 |  | Range at 741 km. |
|  | (c) 90° elevation angle | dB | 167.6 |  | Range at 705 km. |
| 7. | Atmospheric loss |  |  |  | For Direct Playback and Direct Broadcast |
|  | (c) 5° elevation angle | dB | 0.50 |  | Clear air atmospheric using CCIR Specific Model |
|  | (b) 71° elevation angle | dB | 0.05 |  |  |
|  | (a) 90° elevation angle | dB | 0.05 |  |  |
|  | Ground temperature | deg C | 22.0 |  | CCIR Specific Model: ground station temp. |
|  | Water Vapor Density | g/m3 | 7.5 |  | CCIR Specific Model: water vapor density |
|  | Earth Terminal Altitude | km | 0.0 |  | CCIR Specific Model: alt. above mean sea level |
| 8. | Rain Loss |  |  |  | For Direct Playback only (Using Crane model) |
|  | (a) 5° elevation angle | dB | 0.00 |  | 95% avail. & climate A (99.7% => 0.06 dB) |
|  | (b) 71° elevation angle | dB | 0.00 |  | 95% avail. & climate A |
|  | (c) 90° elevation angle | dB | 0.00 |  | 95% avail. & climate A |
| 9. | Polarization Loss | dB |  |  |  |
|  | Ground Terminal Rx Axial Ratio (1.8) | dB |  |  | Estimate |
|  | S/C Transmit Axial Ratio: |  |  |  | AR Measurements, avg. (SN 301 Antenna) |
|  | 63.8° (4.9) | dB | 0.4 | 0.6 |  |
|  | 17° (5.7) | dB | 0.5 | 1.2 |  |
|  | 0° (6.7) | dB | 0.6 | 0.4 |  |
| 10. | User Ground Station G/T |  |  |  |  |
|  | (a) 5° elevation angle | dBi/K | 21.0 |  | Direct Broadcast (15 Mbps) §4.3.5.10† |
|  | (b) 71° elevation angle | dBi/K | 22.7 |  | ^Temperature increase due to rain is 0 dB |
|  | (c) 90° elevation angle | dBi/K | 23.4 |  |  |
| 11. | CCSDS data rate |  |  |  |  |
|  | 15 Mbps | dB-Hz | 71.8 |  |  |
| 12. | Other losses |  |  |  |  |
|  | Differential Decoding Loss |  | 0.3 |  | NRZ-M |
|  | Minimum Implementation Loss | dB | 3.0 |  | From §4.3.5.11† (DP) and §4.3.5.10† (DB) |
|  | Total | dB | 3.3 |  |  |
| 13. | Required Eb/No |  |  |  | 10^-3 BER per §4.3.5.8† |
|  | Ideal required Eb/No | dB | 6.8 |  | Ideal PSK (no coding); CCSDS700.0 G-3 Pg. A-5 |
| † EOS AQUA Common Spacecraft Specification: GSFC 422-13-11-01 |

Appendix B

X-BAND EARTH COVERAGE ANTENNA PATTERN

Figure B-1:  EOS Aqua X-band EC Antenna (S/N 301) Gain Performance