CONSTRUCTION JOB HAZARDS ANALYSIS

EXAMPLES

Contractor Name: __________________________	   Date: ____________

| Scope of Work | Potential Safety Risks/Issues | Mitigation of Potential Risks |
| --- | --- | --- |
| General, Site and work area setup |  | All work shall be in accordance with the subcontractor’s IIPP and in conformance with all LBNL policies, Federal OSHA & Cal-OSHA standards; All general safety orders shall be reviewed by subcontractors prior to starting work; All equipment shall be properly and completely inspected by its operator prior to use. Any equipment that is not fully operational and function shall be removed from service; All extension cords are to be in good working order, free from cuts and abrasions and properly grounded and of a gauge suitable for the amperage used; All power equipment shall be in good working order and only operated by trained employees; In areas where the PEL’s cannot be measured to ensure employees are not being exposed to OSHA permissive exposure limits, employees will wear OSHA and NOISH approved breathing apparatuses including particulate masks. If such apparatuses are use, employees shall be FIT tested and their certification cards shall be made available to an LBNL representative upon request; Power tools found not to be in good working order and unsafe to use shall be tagged and removed from the work area; employees using tools are to be trained in their safe use and the safety rules for them and PPE required at all times including; Hard Hats Safety Glasses Respirators as necessary Masks Proper Gloves as necessary Noise Protection |
| Carrying Objects | Striking against other objects Being struck by other objects Caught in between objects Fall to a different level Fall on the same level Slip/Trip Overexertion, strain, sprain Absorption through skin Pollution | Be aware of surroundings Wear full body harness when working 6’ above deck and secured lanyard Maintain proper footing Maintain proper body positioning at all times Wear proper protection when handling chemicals Ensure proper seals on liquids being transferred When possible keep one hand free |
| Climbing | Striking against other objects Fall to a different level Slip/trip Overexertion, strain, sprain | Be aware of surroundings Wear full body harness when working 6’ above deck with lanyard or Arrestive Fall Device (A.F.D.) Maintain Proper footing Maintain proper body positioning at all times |
| Lifting | Striking against other objects Being struck by other objects Caught in between objects Fall to a different level Fall on the same level Slip/Trip Overexertion, strain, sprain | Be aware of surroundings Maintain proper footing Maintain proper body positioning at all times Wear proper protection when handling chemicals Get assistance when needed |
| Pipe Handling | Striking against other objects Being struck by other objects Caught in between objects Fall to a different level Fall on the same level Slip/Trip Overexertion, strain, sprain Blown, chipped, splashed particles Pollution Extreme temperature or weather Cuts/Lacerations | Be aware of surroundings Wear full body harness when working 6’ above deck and secured lanyard Maintain proper footing Maintain proper body positioning at all times Wear proper eye protection Wear proper protection for extreme cold/hot temps Wear proper eye protection around welding Proper gloves as needed |
| Forklift | Inspections/Operation Improper Setup of work area Overhead Obstructions And Utilities Slips, Trips, Falls Cuts/Punctures Manual Handling of Heavy objects Housekeeping | Perform required daily inspections, including rigging equipment if used. Equipment inspections as per manufacturer’s requirements. Inspect forklifts before use. Repairs must be completed by Qualified Personnel Malfunctioning equipment must never be used until repaired or replaced Operator must be Certified on the type of forklift being used Use seatbelts on equipment which require it Wear proper PPE Ensure the work areas are secured and safe for operations Keep non-essential personnel out of the area Identify all overhead obstructions and utilities around the site before work commences Utility clearance shall conform with Fed/Cal OSHA guidelines Guard or de-energize electrical sources if necessary Be aware of surroundings Maintain proper footing Maintain proper body positioning at all times Keep area dry and clean Wear Proper hand protection i.e. gloves Beware of sharp equipment, tools, and other materials Mark, identify sharp objects and communicate the hazard to others Observe proper lifting techniques Obey sensible lifting limits Use mechanical lifting equipment (hand carts/trucks) to move heavy, large, or awkward loads Awkward loads must be secured using ropes or straps Training required for using hand trucks/carts Never move materials on ice or slick surfaces Keep unloading area free of obstructions and debris Place all trash/debris in the proper containers |
| Forklift (Continued) | General Fire/Explosion Prevention | Smoking only allowed in approved areas Fire Extinguishers must be available where/when required Flammable liquids shall be stored in approved containers Refueling of equipment at a re-fueling station per LBNL, Fed-OSHA, or Cal-OSHA guidelines. Do not wear protective coveralls when refueling. In case of fire, protective coveralls can catch fire easily and burn rapidly |
| Pushing | Striking against other objects Being struck by other objects Caught in between objects Fall to a different level Fall on the same level Slip/Trip Overexertion, strain, sprain | Be aware of surroundings Maintain proper footing Maintain proper body positioning at all times Wear proper protection when handling chemicals Get assistance when needed Wear proper eye protection |
| Using hand tools | Striking against other objects Being struck by other objects Caught in between objects Fall to a different level Fall on the same level Slip/Trip Overexertion, strain, sprain Pinch points Extreme temperature or weather | Be aware of surroundings Maintain proper footing Maintain proper body positioning at all times Wear proper protection when handling chemicals Use tools only for it’s intended purpose Wear proper eye protection Wear proper protection for extreme cold/hot temps Wear proper hand protection (gloves) Inspect tools for damage before use |
| Using power tools | Striking against other objects Being struck by other objects Caught in between objects Fall to a different level Fall on the same level Slip/Trip Overexertion, strain, sprain Pinch points Electric shock Extreme temperature or weather | Be aware of surroundings Maintain proper footing Maintain proper body positioning at all times Wear proper protection when handling chemicals Use tools only for it’s intended purpose Wear proper eye protection Wear proper protection for extreme cold/hot temps Wear proper hand protection (gloves) Inspect tools for damage before use Inspect power cords, if damaged take out of service Keep power cords out of walkways (trip hazard) when possible |
| Powder actuated tools | Striking against other objects Being struck by other objects Caught in between objects Fall to a different level Fall on the same level Slip/Trip Overexertion, strain, sprain Pinch points Extreme temperature or weather Blown, chipped, splashed particles Improper use Noise level | Only certified personnel to use Be aware of surroundings Notify anyone in area, use signage, about use of powder actuated tool, and noise and possible flying debris. Maintain proper footing Maintain proper body positioning at all times Wear proper protection when handling chemicals Wear proper eye protection Wear proper protection for extreme cold/hot temps Wear proper hand protection (gloves) Inspect tools for damage before use Use proper hearing protection A powder-actuated tool must never be pointed at anyone, whether it is loaded or not! A powder-actuated tool should never be loaded until it is ready to be used for fastening Powder-actuated tools should not be used in areas where flammable or combustible atmospheres may be present. The combination could cause an explosion. Never drive a fastener into a "spalled" or chipped surface, i.e., over an uneven area where a previous fastening was unsatisfactory. Never shoot into a surface unless you are certain it will contain the fastener |
| Cleaning | Striking against other objects Being struck by other objects Fall to a different level Fall on the same level Slip/Trip Overexertion, strain, sprain Blown, chipped, splashed particles Pollution Extreme temperature or weather Absorption through skin Inhalation | Be aware of surroundings Wear full body harness when working 6’ above deck and secured lanyard Ensure proper seals on liquids being transferred Maintain proper footing Maintain proper body positioning at all times Wear proper protection when handling chemicals Get assistance when needed Wear proper eye protection Wear proper protection for extreme cold/hot temps Wear proper breathing apparatus to avoid inhaling hazard |
| Excavations/Trenching | General Access and Egress | A Dig Permit is required Evaluation of shoring, sloping, or other means to eliminate the potential for cave-ins must be performed prior to the start of work If digs are to be 4 feet or greater then a Confined Space JHA and a Safety Checklist are to be completed and turned in to Construction Safety Engineer Exact location of utilities are to be found/located following LBNL Policies Competent Person to determine the soil type, do inspections daily and prior to start of each work shift to ensure safe work conditions. Any previously dug soil is to be considered Class “C” soil. The atmosphere in excavations/trenches greater than 4 feet in depth shall be tested for Oxygen deficiency or a hazardous atmosphere Stairway, ladder, ramp, or other safe means of egress shall be located in excavations/trenches that are 4 feet or greater in depth so that no more than 25 feet of lateral travel is required Materials and equipment are to be kept at least 2 feet from the edge of the excavations so as to keep anything from falling into hole. Adequate precautions must be taken to ensure that vibrating equipment and vehicular traffic do not cause a cave-in. Always consider ground water seepage as a potential cause of collapse of any trench or excavation. |
| Ladders | Falls | All employees shall be instructed in the safe use and operation of ladders used on this project; All ladders shall conform to OSHA standards; All ladders shall be inspected prior to their use and if found to be defective, shall be removed from service; All step ladders used on this project shall be Type I, Industrial; Employees are not to use the top 2 rungs of a ladder; Metal ladders are expressly prohibited around charged electrical parts; When using a step ladder, employees must make sure the ladder is properly set on firm ground and that the spreader bars are properly locked in place; Step ladders are not to be used as a lean-to ladder; and Extension ladders must extend 3 feet above the landing unless handholds are provided. Area around ladders are to be kept dry, clean of any debris, and access/egress clear |
| Descending | Striking against other objects Being struck by other objects Caught in between objects Fall to a different level Fall on the same level Slip/Trip Overexertion, strain, sprain | Be aware of surroundings Wear full body harness when working 6’ above deck and secured lanyard Maintain proper footing Maintain proper body positioning at all times Use Hand Rails |
| Welding | Striking against other objects Being struck by other objects Caught in between objects Fall to a different level Fall on the same level Slip/Trip Overexertion, strain, sprain Blown, chipped, splashed particles Extreme temperature or weather Arc/X-ray exposure Electric shock Inhalation Fire Prevention Pollution | Be aware of surroundings Wear full body harness when working 6’ above deck and secured lanyard Maintain proper footing Maintain proper body positioning at all times Wear proper eye protection Wear proper protection for extreme cold/hot temps Wear proper eye protection around welding Wear proper breathing apparatus to avoid inhaling hazard Secure work area Fire Extinguishers following LBNL policies Hot Work Permit Required |
| Equipment/machinery operation | Striking against other objects Being struck by other objects Caught in between objects Fall to a different level Fall on the same level Slip/Trip Overexertion, strain, sprain Blown, chipped, splashed particles Pollution Extreme temperature or weather Electric shock Inhalation | Be aware of surroundings Wear full body harness when working 6’ above deck and secured lanyard Maintain proper footing Maintain proper body positioning at all times Wear proper eye protection Wear proper protection for extreme cold/hot temps Wear proper breathing apparatus to avoid inhaling hazard Ensure proper seals on liquids being transferred Wear proper protection when handling chemicals No loose clothing, etc. Training as required (Certifications) Daily Equipment checks |
| Handling liquids/materials | Slip/Trip Overexertion, strain, sprain Blown, chipped, splashed particles Pollution Extreme temperature or weather Inhalation | Be aware of surroundings Maintain proper footing Maintain proper body positioning at all times Wear proper protection when handling chemicals Wear proper eye protection Ensure proper seals on liquids being transferred Wear proper protection for extreme cold/hot temps Wear proper breathing apparatus to avoid inhaling hazards all time |
| Ergonomics | Repetitive Motion Injuries (RMI) Back Injuries | All employees shall be instructed in the safe use and operation of equipment used on this project; The proper tool shall be used for the job at hand; Whenever possible, mechanical lifting equipment shall be used in place of manually lifting and moving of loads; If a tool is damaged, it should be replaced as soon as possible; Employees using repetitive motions doing their work shall take the necessary breaks to avoid injuries to themselves; RMI injuries shall be reported to your supervisor right away; All employees shall use proper back lifting techniques as trained when lifting heavy loads; and PPE shall always fit properly. |

General mitigating requirements are as follows:

- All employees shall be aware of General Safety Rules.

- All employees shall be aware and trained in the Illness & Prevention Program.

- All employees shall be aware and trained in the Chemical Hazards Communication Program.

- All MSDS for proposed and used chemicals shall be on file and approved with the General Contractor prior to the start of work. Provide training as required by the specific MSDS.

- All PPE shall be used in accordance with the applicable MSDS.

- All employees, where required shall be trained and certified when required by OSHA & Cal-OSHA.

- All PPE to be approved by ANSI or applicable approval agency.

- All MSDS sheets shall be submitted to the General Contractor prior to starting work.

- Fall protection measures shall be in place for ladder safety in heights of 6 feet and higher.

- Any injury is to be reported to the Supervisor immediately

______________________________________________________	_____________________

Agreed To –                        							Date

______________________________________________________	_____________________

Approved –                                							Date

______________________________________________________	_____________________

Reviewed / Approved – Lawrence Berkeley National Lab			Date

A signed copy of this JHA must be posted while the applicable subcontractor is working on-site and be available to any LBNL employee upon request.

Copy Distribution:

General Contractor	        Project Superintendent    	   	   Subcontractor

LBNL Safety Officer            LBNL Construction Manager

Construction JHA Safety Sign-in Sheet

Date: __________

Print                                                                      Signature

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________