Streetcar Loop

Portland, Oregon

(November 2007)

The City of Portland, Oregon, in conjunction with the Tri-County Metropolitan Transportation District (TriMet), is proposing to construct a 3.3-mile extension to its existing “Westside” streetcar line.  The project would result in a new streetcar line originating at the existing streetcar station at 10th Street and Lovejoy in the Pearl District northwest of downtown Portland, running east across the Willamette River to the City’s Lloyd District, and then south along Martin Luther King (MLK) Jr. Boulevard and Grand Avenue, terminating near the Oregon Museum of Science and Industry (OMSI).  This “Eastside” alignment includes 18 new stations and significant capital improvements to the Broadway Bridge to accommodate streetcar operations.  The project would require seven new vehicles, all of which are being procured outside of the scope of the proposed Small Start.  Service would operate at 12-minute headways during weekday peak periods in the opening year of 2011; future streetcar operations would result in “through” service (i.e. not requiring a transfer) between the Westside and Eastside alignments.  In addition, later phases of rail project development in the region are proposed to include a new crossing over the Willamette River to the south and west of OMSI, resulting in a direct connection to the southern end of the Westside streetcar alignment to create a continuous central city “streetcar loop.”

| Summary Description |
| --- |
| Proposed Project: | Modern Streetcar |
|  | 3.3 Miles 18 Stations |
| Total Capital Cost ($YOE): | $126.92 Million (Includes $5 million in finance charges) |
| Section 5309 Small Starts Share ($YOE): | $75.00 Million (59.1%) |
| Annual Operating Cost ($YOE): | $3.70 Million |
| Opening Year Ridership Forecast (2011): | 8,700 Average Weekday Boardings |
| FY 2009 Local Financial Commitment Rating: | Medium |
| FY 2009 Project Justification Rating: | Medium-High |
| FY 2009 Overall Project Rating: | Medium-High |

Project Development History and Current Status

The City of Portland formed an Eastside Corridor Steering Committee in 2003 to explore opportunities for extending the existing Westside Portland Streetcar to the Lloyd District and Central Eastside area.  Based upon this work, Metro, the metropolitan planning organization for the Portland region, initiated an alternatives analysis study in July 2005, evaluating the costs and benefits of various streetcar alignments and bus service in the Eastside corridor.  In July 2006, local stakeholders selected a streetcar alignment running north-south along MLK Boulevard and Grand Avenue terminating at OMSI as the initial construction segment.  TriMet submitted a complete request for entry into Small Starts project development for this alignment in March 2007; the request was approved by FTA the following month.  TriMet is expected to complete an Environmental Assessment on the project in December 2007.

The project’s current cost estimate lacks detail and carries low contingencies.  However, the team assembled to implement the project has significant experience in the design and construction of modern streetcar systems.  TriMet has a strong track record for constructing major transit capital investments on time and within budget.

Project Justification Rating: Medium-High

The project is rated Medium-High for project justification based on a Medium-Low rating for cost effectiveness and a High rating for transit-supportive land use.  The rating for the project’s Making the Case document was not factored into the project justification rating for FY 2009.

Making the Case Rating: Low

The Portland Streetcar Loop project would extend the current system to the east side of the Portland Central City area.  The project’s purpose is to address the transportation needs of travelers in the area and achieve additional economic development.  Problems of increased traffic and congestion are cited as well as a need to support local land use and development goals with faster, more reliable transit service.  No evidence is presented in the “case” showing how much congestion will increase versus today, nor is there any discussion of the travel markets affected by the congestion.  Similarly, there is no discussion of the travel markets that would be served by the Streetcar, which would not be expected to serve traditional CBD-oriented markets because of its circuitous routing.  Based upon experience along the “Westside” streetcar alignment, TriMet estimates that the Streetcar Loop will result in an additional 3,400 residential units and 2.4 million square feet of additional development along the project corridor in 2025 than without the streetcar investment.  However, evidence is lacking of the comparability of conditions between the two areas (such as proximity to downtown Portland), and of the contribution of the existing streetcar system - versus other factors, such as the region’s strong land use policies and controls (for which the Streetcar Loop project has received credit under the Transit-Supportive Land Use rating) - to the achievement of economic development objectives.

Cost Effectiveness Rating: Medium-Low

The Medium-Low rating is based on the level of travel-time benefits (1,000 average weekday hours) relative to the project’s annualized costs.  The project’s travel forecast carries some risk, as it may not reliably capture the travel patterns of short-distance urban circulation trips.

| Cost Effectiveness |
| --- |
| Cost per Hour of Transportation System User Benefit | New Start vs. Baseline $29.22 |

Transit-Supportive Land Use Rating: High

The High rating is based upon the average of the ratings assigned to the subfactors below, each of which contribute one-third to the land use rating.  The rating reflects conditions as of April 2007.

Existing Land Use: High

- Portland’s central business district, which includes most of the Streetcar Loop Corridor, has a total employment of about 173,000. Total population in proposed station areas as of 2005 is 29,600 at an average density of 7,600 persons per square mile.  Total station area employment is 84,900.  Total employment served in existing and proposed station areas is just over 200,000.

- Development patterns in the corridor are urban in character, with minimal to moderate amounts of surface parking, buildings fronting the streets, and a number of multi-story buildings.  The northern section of the corridor consists largely of major office, retail, and entertainment uses, while the southern section consists largely of lower-rent office and industrial uses.  Street and pedestrian connectivity are good throughout the corridor.

Transit-Supportive Plans and Policies: High

- Policies and planning requirements at the state and regional levels support transit-oriented development and growth management.  Portland’s Central City Plan (1988) includes urban design goals that aim to create an enjoyable pedestrian environment and place high density development in potential and existing transit corridors.  The plan anticipates transit service along the proposed streetcar alignment by zoning blocks in the Lloyd District as well as along a north-south spine in the Central Eastside District for the highest densities and establishing policies to support mixed-use development. Design review is required for all major developments in a Design Review Overlay Zone which encompasses the proposed streetcar corridor.

- Two Urban Renewal Districts cover the area served by the proposed streetcar extension.  These districts have financed redevelopment projects and infrastructure improvements, with other projects in the planning stages to support the streetcar investment.

- The Central City Plan District restricts the maximum size of retail uses and provides various requirements, such as minimal setbacks and active uses on the ground floor, to promote pedestrian friendliness.  Some provisions apply specifically to streetcar corridors.

- State, regional, and local agency programs and guidelines, such as Metro’s Transit Oriented Development (TOD) and Centers Program, promote pedestrian and transit-friendly development and design.  For decades, the City of Portland’s comprehensive planning and zoning process has anticipated transit service in the Eastside corridor.  A number of regulatory and financial incentives for development exist and have been applied by the city and other agencies.

Performance and Impacts of Policies: Medium-High

- The successful application of land use and TOD policies in the Portland region has been demonstrated through numerous housing developments in light rail station areas, commercial development in downtown and the Lloyd District, and most recently a boom in high-density residential construction in the existing Westside streetcar corridor.

- Redevelopment activity in Eastside areas has not been as successful to date.  However, a major mixed-use catalyst project is underway and other projects are in the planning stages.

- There is a considerable amount of underutilized or vacant property in the corridor that could be available for redevelopment, especially comparing existing Floor Area Ratios (FAR) to allowable FARs of 4:1 or greater.  A local economic impact study projected that the streetcar extension could catalyze 5.3 million square feet of building development by 2025, a 65 percent increase over 2004 development. The market in the Eastside corridor appears to be strengthening, but the timeframe over which development would ultimately be realized is not yet clear.

# Local Financial Commitment Rating: Medium

The project is rated Medium for local financial commitment, based upon TriMet’s acceptable financial condition; a reasonable plan for funding for the non-Small Starts share of capital costs; and evidence that the operations and maintenance cost of the project is less than five percent of the agency’s operating budget.

| Locally Proposed Financial Plan |
| --- |
| Source of Funds | Total Funds ($million) | Percent of Total |
| Federal: Section 5309 Small Starts FHWA Flexible Funds (CMAQ) | $75.00 $3.62 | 59.1% 2.9% |
| Local: Local Improvement District City of Portland Tax Increment Financing City of Portland Development Charges City of Portland General Transportation Revenues | $15.00 $27.18 $6.00 $0.11 | 11.8% 21.4% 4.7% 0.1% |
| Total: | $126.92 | 100.0% |

NOTE:  The financial plan reflected in this table has been developed by the project sponsor and does not reflect a commitment by DOT or FTA.  The sum of figures may differ from total as listed due to rounding.

MAP