| Company Name: | Equipment/Job Identification: Dragline Operator Type of Equipment: Crawler Crane Make: Manitowoc Model: 3000 Year: 1953 Use: Dragline |
| --- | --- |
| Mine Name: |  |
| Date of Analysis: |  |

# Prerequisites:

Basic Crane 40 Hour Course

New Miner Training (if applicable)

Task Training

Annual Refresher (if applicable)

Site Specific Hazard Awareness Training

# Duty 1: Pre-Op

Objective:  The learner will explain the importance of the pre-op in determining work to be accomplished. The learner will explain and interpret information received in the pre-op training to the trainer.  The learner will explain each job step, why it is conducted, any associated risk, and how to implement appropriate controls.  Planning activities include the following duties:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Work area examination |  |  |  |  |
| Perform self assessment |  |  |  |  |
| Check mental condition |  |  |  |  |
| Check physical condition |  |  |  |  |
| Use personal protection equipment |  |  |  |  |
| Approach inspection |  |  |  |  |
| 1. Check crawlers |  |  |  |  |
| 2. Check wire ropes | Maintenance problem; could cause injury |  |  |  |
| Check sheaves | Maintenance problem; could cause injury |  |  |  |
| Check pendant lines and boom | Maintenance problem; could cause injury |  |  |  |
| Check ground conditions |  |  |  | Check for overhead and underground power lines and utilities |
| Check for loose, missing or broken parts |  |  |  |  |
| 7. Check weather conditions |  |  |  |  |
| 8. Check for fresh fluid leaks (coolant, oil, etc) |  |  |  |  |
| 9. Check for signs of unknown activity |  |  |  | Check for human or vehicle tracks – determine if maintenance work had been done or unauthorized activities |
| Check glass |  |  |  |  |
| Daily inspection |  |  |  |  |
| Check crawlers |  |  |  | Cracked or welded pads Check keeper pins which are located at the end of the hinge pin between the pads. Check for kinks or loose travel chains Check the sprockets and rollers for wear, alignment, and missing teeth Check for safe access (clean crawler track if needed) |
| 2. Check car body |  |  |  | Check for cracked or welded parts. Check for fluid leaks Check for and clean off excess dirt and grease |
| 3. Check for cracks |  |  |  |  |
| 4. Open drains for oil sumps to drain water | Maintenance problem; could cause injury |  |  |  |
| 5. Check house rollers |  |  |  | Check for wear, spider cracks, scaling, flat spots, and bearing pieces. Check for the lack of lubrication. |
| 6. Close air tank from the prior shift |  |  |  |  |
| 7. Check if wire rope is spooling straight on drums | Maintenance problem; could cause injury |  |  |  |
| 8. Check condition of wire rope | Maintenance problem; could cause injury |  |  | Refer to rope retirement criteria 30 CRF Subpart R |
| 9. Check fairlead |  |  |  | Check rollers, sheaves, alignment, lubrication fittings, mounting bolts, keepers. |
| 10. Check condition of crane mats (if used) |  |  |  |  |
| Check the condition of the sheet metal |  |  |  | Check entire cab and the condition of door and track assembly Check grab iron |
| Check for obstructions of the tail swing area | Could cause injury or damage |  |  |  |
| Pre Engine Start |  |  |  |  |
| Open the door |  |  |  |  |
| Check fire extinguishers |  |  |  |  |
| Check fluid levels | Maintenance problem; could cause dragline failure |  |  | Diesel fuel, engine oil, coolant, chain cases, sump oil, air compressor oil level, gasoline level, alcohol evaporator |
| Check belts for tension |  |  |  | Engine, air compressor, sump pump (gear lube), kuno filter needs a full turn every day |
| Check chain guard |  |  |  |  |
| Check fan shroud |  |  |  |  |
| Check air compressor belt guard |  |  |  |  |
| Check drum guards |  |  |  | Boom hoist, hoist line, dragline, |
| Check for lock out/tag out as applies |  |  |  |  |
| Check control levers are in neutral position | Inadvertent movement could cause injury or death |  |  | Hoist, Boom, Swing & Master Cutch |
| Check master clutch is disengaged | Inadvertent movement could cause injury or death |  |  |  |
| Adjust throttle |  |  |  | Make sure it is not full throttle. |
| Start Engine |  |  |  |  |
| Turn key and start engine |  |  |  |  |
| Check for leaks |  |  |  |  |
| Permit/allow air pressure to build up to full operating pressure |  |  |  |  |
| Check oil pressure | Could cause damage |  |  |  |
| Check for operators manual and load chart |  |  |  |  |
| Bring engine temperature up to a safe operating temperature |  |  |  |  |
| Engage master clutch |  |  |  | Maintain a low idle prior to slowly engaging. Engage the clutch only after operating temperatures have been reached. |
| Check boom, hoist, and drag brakes and clutches | Maintenance problem; wet or damaged linings could cause injury or equipment failure |  |  | Check boom first Boom up while holding brake on Boom down while applying brake to warm it up Dry brake lining to prevent slippage |
| Lower boom to the ground |  |  |  | Swing to side of bucket placing boom on cribbing to reduce strain on boom pendant lines. |
| Set brakes and place levers in neutral position | Inadvertent movement could cause injury or death |  |  | Never leave the seat with the master clutch engaged!! |
| Disengage master clutch | Inadvertent movement could cause injury or death |  |  |  |
| Inspect boom | Boom failure could cause injury or death |  |  | Bent, broken, or missing lacing, and damaged cords, bolts & pin connections, keepers, attachments, rollers and wire rope guides, sheaves (guards, chips, cracks, wear, damage, lubrication, bearings, alignment, & missing sheave), boom angle indicator (free moving & correct calibration), pendant lines (broken wires, pins and keepers are intact, rust, wear, lubrication, defects) equalizer (pins and keepers are intact & check sheaves), boom hoist wire rope (broken wires & strands, rust, wear, lubrication, defects), boom stops, gantry (pins keepers, sheaves, lubrication, and other damage) |
| Inspect bucket |  |  |  | Teeth, hoist chains above and below the spreader bar, spreader bar, hoist clevis, pins, and keepers, dump (trip) sheave assembly, trunions, drag yokes (frog), drag hitch clevises, all other components |
| Raise the boom |  |  |  |  |
| Set to desired boom angle |  |  |  |  |
| Dry the hoist and drag brakes | Maintenance problem; wet or damaged linings could cause injury or equipment failure |  |  | Run wire rope up and down with the brakes lightly applied to dry the brakes. |
| Raise bucket |  |  |  |  |
| Swing machine side to side to dry the swing clutches |  |  |  |  |
| Pre Shift Meeting |  |  |  |  |
| Listen to supervisor instructions |  |  |  |  |
| Plan daily operations | proper planning improves all categories |  |  | Traffic patterns, haul road maintenance, personal protective equipment, material blending |
| Discuss any change in conditions |  |  |  |  |
| Participate in daily safety meeting |  |  |  |  |

# Duty 2: Set-up to dig

Objective:  Learner will demonstrate proper set-up procedures. The learner will explain the results of committing unsafe acts on the job. The learner will explain and demonstrate the steps to properly set up the dragline for work.  The learner will explain listed job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  Set-up work includes the following duties:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Examine the site |  |  |  | Mats and cribbing needed, travel route, soil conditions, any changes from previous shift, re-check the swing radius |
| Disengage travel dogs | Could cause injury |  |  | Discuss mounting and dismounting safety |
| Mount dragline | Could cause injury |  |  | If located on a hill, do not disengage travel dogs until ready to travel. |
| Engage master clutch |  |  |  | Maintain a low idle prior to slowly engaging. Engage the clutch only after operating temperatures have been reached. |
| Place boom at proper angle for travel | could tip over causing severe damage, injury or death |  |  |  |
| Engage travel clutches |  |  |  | Ensure the drive chains are located away from digging end. |
| Travel onto the mats (if needed) |  |  |  | Center dragline on mats, make sure the idlers are not at the seam of two mats, chock/block the tracks in front of dragline |
| Engage directional travel lock to prevent over travel toward excavation site | Could cause dragline to be pulled into excavation causing severe damage, injury or death |  |  |  |
| Ensure dragline is level | effects all categories |  |  |  |

# Duty 3: Position

Objective:  The Learner will demonstrate how to properly position the dragline. The learner will explain the job steps listed, why they are conducted, any associated risk, and how to implement appropriate controls.  A thorough execution of the job includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Re-examine conditions |  |  |  |  |
| Determine the depth of the cut | Effects production and safety |  |  | Lower bucket to the bottom, raise bucket slightly, gingerly sweep back and forth to determine depth and location of material, test various radii and depths |
| Start working the cut | Effects production and safety |  |  | Dig within the front quadrant. DO NOT UNDERCUT!!! |
| Monitor ground conditions continuously while digging | Effects production and safety |  |  |  |
| Monitor the dragline | Effects production and safety |  |  | Check engine gauges, listen for abnormal sounds, bucket conditions, wire rope condition, boom connections, wire rope alignment, sheaves, fairleads |
| Build and monitor stockpile |  |  |  | Slope for proper drainage, ensure proper placement |
| Prepare for shutdown |  |  |  |  |

# Duty 4:  Shut Down Procedures

Objective: The Learner will demonstrate how to safely shut down the dragline. The learner will demonstrate the proper procedure for shutdown.  The learner will also explain and demonstrate other job steps listed, and explain why they are conducted, any associated risk, and how to implement appropriate controls.  The proper shutdown procedure will include the following job steps and activities:

| Job Steps | Importance Narrative (Consider Safety, Production, and Maintenance) | Importance Narrative 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Hoist bucket out of excavation |  |  |  |  |
| Disengage travel locks |  |  |  |  |
| Check boom angle | Effects production and safety |  |  |  |
| Adjust boom angle for travel | Effects production and safety |  |  |  |
| Swing to the direction of travel |  |  |  |  |
| Move dragline into stable position | Effects production and safety |  |  |  |
| Swing dragline to position safe cab access |  |  |  |  |
| Position bucket on ground or crib blocks |  |  |  |  |
| Engage all brakes | Effects production and safety |  |  |  |
| Disengage master clutch | Inadvertent movement could cause injury or death |  |  | Never leave the seat without disengaging the master clutch |
| Allow engine to cool down at idle speed |  |  |  |  |
| Shut off engine |  |  |  |  |
| Dismount | Could cause injury |  |  | Mount/Dismount Safety |
| Engage travel locks | Inadvertent movement could cause injury or death |  |  |  |
| Drain air tank |  |  |  |  |
| Lubricate to manufacturer’s specifications |  |  |  |  |
| Re-examine site |  |  |  |  |

# Duty 5: Abnormal Conditions

Objective: The Learner will discuss how to identify abnormal conditions. The learner will discuss the proper procedure for correcting abnormal conditions.   Abnormal conditions may include some or all the following:

| Conditions | Importance Narrative (Consider Safety, Production, and Maintenance) | Importance Narrative 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Weather |  |  |  | Be aware of company policy |
| Lightning | Exposure to lightning could cause injury or death |  |  |  |
| Wind |  |  |  |  |
| Precipitation | Could cause brakes or clutches to function improperly; effecting all three categories |  |  |  |
| Caved in bank | Could cause severe damage, injury or death |  |  |  |
| Medical emergencies | Could cause severe damage, injury or death |  |  | Basic first-aid procedures Be aware of company communication system and policy Know where first-aid equipment is located |
| Malfunction of machine | Could cause injury or equipment damage |  |  |  |
| Fire |  |  |  |  |
| Catastrophic machine failure | Could cause severe damage, injury or death |  |  |  |