TO:	Chair, National Fire Equipment Steering Committee (NFES)

RE:	Helicopter Accessory Equipment

DATE: 	February 6th 2007

The Chair of IHOps was recently tasked with providing representation for the aviation community to the NFES Steering Committee.  I attended a meeting of the NFES on November 15th 2006 here in Boise.  Based on existing issues and discussions at that meeting several concerns regarding helicopter accessory equipment need to be addressed.

The USFS and BLM representatives to IHOps recently met with Carl Bambarger, Aviation Program Leader, San Dimas Technology & Development Center (SDTDC).  I will attempt to recap the issues and proposed resolutions that were discussed.

- Helicopter Swivel Retrofit

  - Carl mentioned that we are entering the final year of the contract to retrofit swivels from the inferior spring gated keeper hook to the eyelet-style (failsafe) hook and that there are still swivels in the system that need to be converted.

Recommend: SDTDC send IHOps a memo to forward to the helicopter community discussing the process and prompting field units to get all remaining swivels in need of upgrade sent in for retrofit.

Info Emailed 2-23-2007.

- Leadline Proof Tags are problematic:

  - The new specification (Specification 5100-503 and 505) addresses this issue by specifying the attachment point and tag composition material (stainless or brass) of the tag.  Existing equipment is far from standard, proof tags are sometimes made of aluminum and are attached in a variety of locations by several different means.  Opportunity exists for proof tags to wallow out and separate in-flight creating a flight safety hazard.

  - Upon refurbishment if a proof tag is missing the leadline must be re-sent to a certified rigging company to be proofed to twice the rated working load and retagged regardless of when it was last checked.

  - Why not stamp the rated capacity on the swedge in an effort to eliminate the need for a proof tag?  Why are we continually re-testing this piece of equipment?  Rappel Ropes are stamped on the swedge by the manufacturer.

Recommend: SDTDC re-evaluate the requirement to continually proof the wire rope to see if this is an OSHA requirement or self imposed.  Share results with NFES and IHOps.

Feb 23, 2007 – OSHA requirements being investigated (Ron Tam).

Recommend: SDTDC research the ramifications of stamping metal swedges as it applies to the leadline and rappel rope. Share results with NFES and IHOps.

Feb 23, 07 – Stamping swedges being investigated.

Recommend: NFES direct the Refurbishment Committee to change Storage and Refurbishing Standards Handbook as needed.

TBD depending on above.

- Straight Throated J-hook equipped leadlines are not compatible with existing cache helicopter equipment:

  - On July 26th of 2005 DOI Safety Alert 05-02 identified this issue of the new smaller J-hooks not accepting two rings of a cargo net to attach properly.  No corrective solution has been identified at this time.

  - All leadline J-hooks have a spring loaded metal keeper gate, the same problematic gate that we are attempting to get rid of through retrofit on all swivels.

  - Specification 5100-503 and 505 call for the use of the eyelet-style (failsafe) hook only.  This will address the issue for all new purchases of leadlines.

  - Carl demonstrated a potential solution of installing a shorter spring loaded metal keeper gate on the hook; this would only resolve a portion of the lines due to inconsistent tolerances between manufactures.  The final product of this solution is less than ideal and continues to prolong the continual issue of spring loaded metal keeper gates.

Recommend: NFES issue direction to all caches and field units to go through stocks of leadlines to inventory and set aside the problematic equipment until a solution is determined.

Recommend: SDTDC generate a proposal addressing issues associated with converting the problematic leadline hooks to an eyelet-style hook; cost estimate to replace the hook as well as the effect on the length of a leadline, etc.  Share results with NFES and IHOps.

Feb 23, 2007 – Boise Cache sent approx. 60 units for retrofit.  Will meet with supplier next week to discuss retrofit.

- Four Corner Cargo Nets

  - Specification 5100-502 allows for either “Four-Corner Pickup-Style” or “Drawstring-Style” cargo nets to be constructed under the same specification.

  - In excess of $400K worth of “Four-Corner Pickup-Style” nets were inadvertently purchased.  These nets have been held out of the system at the request of the National HOS of both USFS and BLM.  This cargo net is inferior to the current stock and will create a multitude of issues if issued.

Recommend:  SDTDC separate the cargo nets into two distinct specifications to promote ordering the desired type of cargo net while still allowing for future purchase of the “Four-Corner Pickup-Style” cargo net if needed.

Feb 23, 2007 – Two separate specs are in draft form.  Plan to release by Mid March.

Recommend: SDTDC contract for retrofit of ten “Four-Corner Pickup-Style” cargo nets into “Drawstring-Style” nets to determine cost estimate, impact to overall volume and feasibility of converting. Share results with NFES and IHOps.

Feb 23, 2007 – GSA to send two nets for retrofit.  Vendor states that the size will not decrease.  The retrofit nets will tell the full story.

Recommend: NFES asks National Cache postpone issuance of “Four-Corner Pickup-Style Nets” pending research of retrofit options.

- Helicopter Load Beam Nominal Ring Size issue:

  - Not all of the various sizes of rings associated with cache helicopter accessory equipment are compatible with every make and model of helicopter belly hooks.

  - An alternate style of swivel and leadline could prove cheaper to procure and provide a solution to the Nominal Ring Size issue.

Recommend: SDTDC fabricate ten, double ringed swivels and associated double hooked leadlines.  IHOps will facilitate conducting a beta test with the equipment and report finding back to SDTDC.

Feb 23, 2007 – Two samples for testing at SDTDC have been sent to NIFC for concept demonstration.  Upon return of samples, SDTDC will test samples on belly hook test stand.  NIFC to send additional belly hook data to assure that two ring sizes will meet the interface requirements of all hooks.

- SEI proposed changes to their Pumpkin Tanks:

  - Carl briefed us in regards to SEI’s proposal to reduce the total supplied fill/discharge outlets on their vinyl pumpkin tanks.  Currently the outlets are standard 3” NPT and total number incorporated vary from 2 to 4 based on tank size.  SEI would like to limit all tank outlet to 2 and at the same time reduce the diameter of the outlet from 3 inches to 2 inches.

  - A minimum of 2 outlets should be sufficient.

Recommend: SDTDC consult with water handling specialist at National Cache in regards to proposed change of diameter to volume pump outlet interface with pumpkin tank.

Feb 23, 2007 – SDTDC to discuss at Cache managers meeting during Mar 6-8 meeting.

Recommend: SDTDC send IHOps a memo outlining the agreed to changes to forward to the helicopter community for informational purposes.

Feb 23, 2007 – TBD  depending on above.

Brad Gibbs

Brad Gibbs

Chair, IHOps Steering Committee

(208) 387-5182

brad_gibbs@nifc.blm.gov

CC: Carl Bambarger

CC: Paul Naman

CC: Matt Cnudde