OH-58 A, A+, and C

Helicopters

INSPECTION PLANNING GUIDE

INTERAGENCY COMMITTEE for AVIATION POLICY (ICAP)

_________________________________________________________________________________

# Updated 1 March 2002

Table of Contents

________________________________________________________________________________

Chapter/ Section 										Page

Record of Revisions	.	.	.	.	.	.	.	.	2

List of Effective Pages	.	.	.	.	.	.	.	.	7

Definitions	.	.	.	.	.	.	.	.	.	.	8

Points of Contact	.	.	.	.	.	.	.	.	.	13      |

Chapter 1	Introduction	.	.	.	.	.	.	.	15

1-1. General 	.	.	.	.	.	.	.	15      |

1-2. Warnings, Cautions, and Notes Defined	.	.	16

1-3. Aircraft, Aircraft Engines, and

Appliances Documents/Records Review	.	.	.	.	16

1-4. Format Defined	.	.	.	.	.	.	17

Chapter 2	Inspection Descriptions	.	.	.	.	.	.	18

2-1. Chapter 3 Preventive Maintenance Inspection (P.M.I.)	18      |

2-2. Chapter 4 Intermediate Inspection (25 Hour)	.	18      |

2-3. Chapter 5 Periodic Inspection (300 Hour)	.	.	18      |

2-4. Chapter 6 Special Inspections	.	.	.	.	18      |

2-5. Chapter 7 Conditional Inspections	.	.	.	18      |

Inspection Schedules 		.	.	.	.	.	19      |

Chapter 3	Preventive Maintenance Inspection (P.M.I.).	.	.	20

Chapter 4	Intermediate Inspection (25 Hour)	.	.	.	.	28      |

Chapter 5	Periodic Inspection (300 Hour).	.	.	.	.	31      |

Chapter 6	Special Inspections	.	.	.	.	.	.	35

Special Inspections Index	.	.	.	.	.	35      |

Chapter 7	Conditional Inspections	.	.	.	.	.	.	50

Conditional Inspections Index	.	.	.	.	.	50      |

APPENDIX	Letter from Bell Textron

Ref: Overhaul and Retirement Schedule,

Manuals and Technical Assistance					65      |

Record of Revisions

_________________________________________________________________________________

As originally submitted to the FAA for

acceptance on January 17, 1997.                      Revisions posted as of:|

| Posted: |
| --- |
| Date | By: | Revision Number | Page Number (s) (Page numbers are as they appeared in the January 17, 1997 version.) |
| March 1, 2002 |  | Revision 1 | TOC revised to reflect changes. Page numbers in Revision 1 were changed as needed. |
| March 1, 2002 |  | Revision 1 | Cover page date “January 17, 1997” Changed to “1 March 2002” |
| March 1, 2002 |  | Revision 1 | TOC changed to include “Points of Contact” in Chapter 1 and an “Appendix” |
| March 1, 2002 |  | Revision 1 | Page 4 “List of Effective Pages” Changed to reflect “Revision 1” changes. |
| March 1, 2002 |  | Revision 1 | Page 5 Change to “Civil Aircraft” definition. |
| March 1, 2002 |  | Revision 1 | Page 7 Change to ”Public Aircraft” definition. |
| March 1, 2002 |  | Revision 1 | Page 8 Changed to include “Safety of Flight” definition |
| March 1, 2002 |  | Revision 1 | “Point of Contact” information added. |
| March 1, 2002 |  | Revision 1 | Page 13 Changed last “NOTE” to state “emphasize” instead of “highlight”. |
| March 1, 2002 |  | Revision 1 | Page 11, 10.1, a., changed “Main” to “Tail”. |
| March 1, 2002 |  | Revision 1 | Page 22, Chapter 4, Section III, 3.2, changed to read, “Inspect cross tube attachment points.” |
| March 1, 2002 |  | Revision 1 | Page 26, Chapter 5, Section III, 3.7, b., changed to read “Install cap plug.” |
| March 1, 2002 |  | Revision 1 | Page 26, Chapter 5, Section III, 3.7, c., changed to read, “Lightly coat mast nut threads with corrosion preventive compound (C53), install mast nut, torque to 250 to 275 inch pounds and install lockwire.” |
| March 1, 2002 |  | Revision 1 | Page 33, Chapter 6, “Special Inspections”, now states, “Special Inspection Index” |
| March 1, 2002 |  | Revision 1 | Page 33, Special Inspection, 6-6, b., changed to read, “Start aircraft and run for 15 minutes at full RPM then rapidly reduce throttle to ground idle and observe a momentary split of the NR and N2 needle and then confirm that the needles rejoin.” |
| March 1, 2002 |  | Revision 1 | Page 33, Special Inspections, 6-6, c., changed to read, “Fly helicopter in vicinity of a safe landing area for 15 minutes, and then perform a power recovery autorotation.” |
| March 1, 2002 |  | Revision 1 | Page 33, Special Inspections, 6-9, a., changed to read, “Verify torque on tail rotor gearbox attaching hardware 50-70 inch pounds plus drag torque.” |
| March 1, 2002 |  | Revision 1 | Page 36, Special Inspections, 6-22, “NOTE” has been removed. |
| March 1, 2002 |  | Revision 1 | Page 38, Special Inspections 6-26, “NOTE” has been removed. |
| March 1, 2002 |  | Revision 1 | Page 40, Special Inspections, 6-39, c, 1., “NOTE” has been removed. |
| March 1, 2002 |  | Revision 1 | Page 42, Special Inspections, 6-47 a., changed to read, “Every 14 Days.” |
| March 1, 2002 |  | Revision 1 | Page 42, Special Inspections, 6-47 a., 1., changed to read, “If the idle time of the helicopter has been for a period of 14 days following the last flight, it is required that a ground run of 5 to 10 minutes be performed (attainment of the operating temperature).” |
| March 1, 2002 |  | Revision 1 | Page 42, Special Inspections, 6-47, a., 2., changed to read, “If a ground run is not possible every 14 days the helicopter and especially the engine should be preserved in accordance with the current military document. Engine preservation requirements and instructions are in Allison publication 5W2 or 10W2.” |
| March 1, 2002 |  | Revision 1 | Page 44, Chapter 7 Conditional Inspections, now state “Conditional Inspection Index”. |
| March 1, 2002 |  | Revision 1 | Page 46, Conditional Inspections, 7-1., i., 5., “NOTE” has been removed. |
| March 1, 2002 |  | Revision 1 | Page 49, Conditional Inspections, 7-4., c., “NOTE” (“Wrinkles of this nature .”) has been removed. |
| March 1, 2002 |  | Revision 1 | Page 52, Conditional Inspections, 7-6., e., 6., changed to read, ”Tail rotor driveshafts for concentricity and cracks. Dye penetrate/NDI is required”. |

1.	All personnel to whom this IPG is furnished shall keep it up to date

with the changes and additions furnished to them.

2.	Each IPG shall have the date of the last revision on each page.

## List of Effective Pages

_________________________________________________________________________________

This listing contains all current pages, with effective dates, of the OH-58 A, A+, and C Helicopters INSPECTION PLANNING GUIDE (IPG).  It should be used after posting changes to insure the IPG is complete and up-to-date.

Chapter/Section				Status			Date

Record of Revisions	.	.	Revision 1	.	.	March 1, 2002

List of Definitions	.	.	Revision 1	.	.	March 1, 2002

Points of Contact				Revision 1			March 1, 2002

### Chapter 1	.	.	.	.	Revision 1	.	.	March 1, 2002

### Chapter 2	.	.	.	.	Revision 1	.	.	March 1, 2002

Chapter 3	.	.	.	.	Revision 1	.	.	March 1, 2002

Chapter 4	.	.	.	.	Revision 1	.	.	March 1, 2002

Chapter 5	.	.	.	.	Revision 0	.	.	March 1, 2002

Chapter 6	.	.	.	.	Revision 1	.	.	March 1, 2002

Chapter 7	.	.	.	.	Revision 1	.	.	March 1, 2002

Definitions

_________________________________________________________________________________

AIRCRAFT means a device that is used or intended to be used for flight.

AIRCRAFT ENGINE means an engine that is used or intended to be used for propelling aircraft.  It includes turbo-superchargers, appurtenances, and accessories necessary for its functioning, but does not include propellers.

AIRFRAME means the fuselage, booms, nacelles, cowlings, fairings, airfoil surfaces (including rotors but excluding propellers and rotating airfoils of engines), and landing gear of an aircraft and their accessories and controls.

AIRCRAFT MAINTENANCE means that work which is required to be performed by an appropriately certificated and qualified person(s).

AIRWORTHINESS DIRECTIVE means a maintenance procedure dictated by the Federal Aviation Administration that must be performed on an aircraft in order to remain airworthy.

APPROVED unless used with reference to another person, means approved by the FAA Administrator.

APPLIANCE means any instrument, mechanism, equipment, part, apparatus, appurtenance, or accessory, including communications equipment, that is used or intended to be used in operating or controlling an aircraft in flight, is installed in or attached to the aircraft, and is not part of an airframe, engine, or propeller.

CALIBRATION means making precise measurements and adjustments to equipment or systems in order to obtain optimum performance and to certify that output data falls within prescribed tolerances.

CAUTION means a maintenance or inspection procedure, practice, etc., which, if not strictly observed, could result in damage to or destruction of equipment.

CHECK means an action taken to examine and verify, in accordance with established procedures and requirements, the condition or status of an aircraft, its systems, components, and/or accessories.

CIVIL AIRCRAFT means aircraft other than “public aircraft”.				  |

COMPONENT any self-contained part, combination of parts, subassemblies or units, which perform a distinctive function necessary to the operation of the airframe, powerplant or propeller.

CONDITIONAL INSPECTION means an inspection which is contingent upon specific conditions or incidents that arise, and only because of these conditions or incidents.  Examples of these conditions or incidents are hard landings, overspeed, and sudden stoppage.  An inspection is required in such cases before further flight.

(ENGINE) CYCLE means an engine start and shutdown procedure to be counted as “1”.  For the purposes of this document (2 cycles per flight hour plus 25%) is the method recommended to determine the number of cycles on engines that have not been logging cycles.  After that, 1 cycle per flight hour.		  		  |

DMWR (pronounced dimwar) means Depot Maintenance Work Requirement.  It is a document that details maintenance and inspection criteria for specific components.

FOREIGN OBJECT DAMAGE (FOD) means damage to an aircraft, airframe. or engine caused by a foreign object that is not part of the aircraft, or has broken loose of the aircraft and caused damage.

GROUND RUN (see RUN-UP) means operating the aircraft on the ground, with no intention of taking off, from a normal start thru flight idle, as a minimum.

HARD LANDING means any accident or incident in which ground impact of the helicopter causes severe pitching of main rotor, allowing hard contact of hub with mast, or results in yielding or noticeable cracking of fuselage pylon support structure or landing gear.

HARD-TIME means a primary maintenance process that requires an appliance or part be periodically overhaul in accordance with the Agency’s maintenance manual or that it be removed from service.

HEALTH INDICATOR (ENGINE) TEST (HIT) means a method for engine trend monitoring to evaluate engine health and performance.

INSPECT means a method of qualifying the condition or status of the aircraft, its systems, components, and/or accessories to specific standards and requirements.

INTERMEDIATE INSPECTION means an inspection that is performed each 25 hours.

MAINTENANCE INSPECTIONS include daily/preflight, segment, safety, service, special, and numbered inspections.  These inspections vary in scope and frequency of performance according to types of aircraft.

MODIFICATION WORK ORDER (MWO) means an authorization to perform a modification on an aircraft to correct or enhance an existing condition.  This is a military term and is similar to a commercial model service instruction.

MAJOR ALTERATIONS means an alteration not listed in the aircraft, or aircraft engine/rotor specifications that (1) might appreciably affect weight, balance, structural strength, performance, powerplant operation, flight characteristics, or other qualities affecting airworthiness; or (2) is not done according to accepted practices, or cannot be done by elementary operations (refer to

Part 43).

MAJOR REPAIR means a repair that (1) if improperly done, might appreciably affect weight, balance, structural strength, performance, powerplant operations, flight characteristics, or other qualities of airworthiness; or (2) is not done according to accepted practices, or cannot be done by elementary operations (refer to Part 43).

MAST BUMPING or flapping-stop contact means the condition which occurs when the main yoke contacts the mast and may result in a fractured mast and rotor seperation.  It usually occurs during; slope landings, rotor startup/coastdown, or when the flight envelope is exceeded.

MINIMUM EQUIPMENT LIST (MEL) means a regulatory authorization to continue to operate an aircraft with inoperable instruments or equipment.  The aircraft may be operated under all applicable conditions and limitations contained  in the minimum equipment list.

MINOR ALTERATION means a modification that is an alteration other than a major alteration.

MINOR REPAIR means a repair that is other than a major repair.

NOTE means an inspection or maintenance procedure, condition, etc., which is essential to highlight

ON CONDITION ITEM (OC) means an item of equipment that must be restricted to one on which a determination of continued airworthiness may be made by a visual check, measurement, test, or other means.

OPERATIONAL CHECK means an "in motion" or "power on" test for determining that an item of equipment will operate at a specified performance level.

OVERHAUL means the complete disassembly, cleaning, inspection, necessary replacement or repair of parts, reassembly, adjustment, and testing of an item or equipment in accordance with recommended procedures.

PERIODIC INSPECTION means an inspection that is performed each 300 hours or 12 calendar months whichever comes first.

PREVENTIVE MAINTENANCE means simple or minor preservation operations and the replacement of small standard parts not involving complex assembly operations.  It is corrective action taken before it becomes necessary to make a major repair.

PREVENTIVE MAINTENANCE INSPECTION (P.M.I.) means an inspection which is accomplished each 12 1/2 flight hours or every 14 calendar days, whichever occurs first.

PUBLIC AIRCRAFT means an aircraft used only for the United States Government,   |

an aircraft owned by the Government and operated by any person for purposes     |

related to crew training, equipment development, or demonstration, an aircraft  |

owned and operated by the government of a State, the District of Columbia, or a |

territory or possession of the United States or a political subdivision of one  |

of these governments, an aircraft exclusively leased for at least 90 continuous |

days by the government of a State, the District of Columbia, or a territory or  |

possession of the United States or a political subdivision of one of these      |

governments, an aircraft owned or operated by the armed forces or chartered to  |

provide transportation to the armed forces.  In this definition, the following  |

definitions apply:                                                              |

(1) COMMERCIAL PURPOSES means the transportation of persons or property for     |

compensation or hire, but does not include the operation of an aircraft by the  |

armed forces for reimbursement when that reimbursement is required by any       |

Federal statute, regulation, or directive, in effect on November 1, 1999, or by |

one government on behalf of another government under a cost reimbursement       |

agreement if the government on whose behalf the operation is conducted certifies|

to the Administrator of the Federal Aviation Administration that the operation  |

is necessary to respond to a significant and imminent threat to life or property|

(including natural resources) and that no service by a private operator is      |

reasonably available to meet the threat.							  |

(2) GOVERNMENTAL FUNCTION means an activity undertaken by a government, such as |

national defense, intelligence missions, firefighting, search and rescue, law   |

enforcement (including transport of prisoners, detainees, and illegal aliens),  |

aeronautical research, or biological or geological resource management.        |

(3) QUALIFIED NON-CREWMEMBER means an individual, other than a member of the    |

crew, aboard an aircraft--									  |

(A) operated by the armed forces or an intelligence agency of the United      |

States Government; or

(B) whose presence is required to perform, or is associated with the          |

performance of, a governmental function.                                        |

(4) ARMED FORCES has the meaning given such term by section 101 of title 10.    |

An aircraft does not qualify as a public aircraft when the aircraft is used for |

commercial purposes or to carry an individual other than a crewmember or a      |

qualified non-crewmember. 								        |

AIRCRAFT OWNED OR OPERATED BY THE ARMED FORCES qualifies as a public aircraft   |

if: 													  |

(A) the aircraft is operated in accordance with title 10; 		        |

(B) the aircraft is operated in the performance of a governmental function    |

under title 14, 31, 32, or 50 and the aircraft is not used for commercial       |

purposes; or 											  |

(C) the aircraft is chartered to provide transportation to the armed forces   |

and the Secretary of Defense (or the Secretary of the department in which the   |

Coast Guard is operating) designates the operation of the aircraft as being     |

required in the national interest.								  |

LIMITATION An aircraft that is owned or operated by the National Guard of a     |

State, the District of Columbia, or any territory or possession of the United   |

States, qualifies as a public aircraft only to the extent that it is operated   |

under the direct control of the Department of Defense. 				  |

PYLON WHIRL (see SPIKE KNOCK) means a condition which occurs after blade flapping and mast bumping.  The resultant motion of the pylon is elliptical, and spike knock is apt to occur.

REPAIR means the restoration of an item of equipment to a serviceable condition after fault detection.

RUN UP (see GROUND RUN) means operation of the aircraft from normal start thru flight idle.  Flight of the aircraft may be planned.

SPECIAL INSPECTION means an inspection, in addition to the P.M.I., Intermediate and Periodic Inspections, that are inspections performed on a calendar basis, a cycle basis, a combination of hourly/calendar basis, or following the installation of a major component such as a gearbox installation.

TIME CONTROLLED COMPONENT means a part or component which has an established service life, at which time certain maintenance must be performed or the item disposed of as unserviceable.  The service life may be based on operating hours, cycles, landings, calendar time, or combinations of these.

UNSALVAGEABLE means an aircraft part that should not be returned to aviation use as defined by Federal Aviation Administration (FAA) Advisory Circular

(AC) No. 21-38 “Disposition of Unsalvageable Aircraft Parts and Materials

(7-5-94).“.  Persons disposing of unsalvageable aircraft parts and materials should, when appropriate, mutilate those parts and materials prior to release.  Mutilation should be accomplished in such a manner that the parts become unusable for their original intended use (see AC No. 21-38).

VISUAL INSPECTION means an inspection of an item of equipment for cleanliness, and deterioration of parts or materials by visual means.

WARNING means a maintenance or inspection procedure, practice, etc., which if not correctly followed,could result in personal injury or loss of life.

WIRE STRIKE Protection System (WSPS) means a basic system consisting of an upper cutter assembly, a windshield deflector/cutter assembly, and a lower cutter assembly that provides protection against frontal impacts with horizontally strung mechanical and power transmission wires.

SAFETY OF FLIGHT MESSAGE means an Army issued message that details a method to  |

inspect, maintain, repair, or replace a component of a U.S. Army aircraft, in   |

this case an OH-58 or UH-1 helicopter.  SOF could also apply to flight          |

procedures, operating limits, or operational policy.					  |

SPIKE KNOCK means a condition which occurs when the round pin in the drag-pin fitting contacts the side of the square hole of the pylon stop, which is mounted to the roof.  A loud noise will be heard and will occur during a rocking of the pylon.  Spike Knock usually occurs during; low rotor RPM, extreme asymmetric loading, poor execution of an autorotational landing and low G maneuvers below +.5 G’s.

Points Of Contact

_________________________________________________________________________________

www.gsa.gov/aircraftpolicy		Web Site for the General Services Administration Aircraft Management Policy Division.  The ‘caretaker’ of the Inspection Planning Guides.

Charlie Elkins

(256) 955-0773				ATCOM UH-1 contact.

Susan Lewis

(256) 955-0773				ATCOM OH-58 contact.

Paul Elliott

(602) 231-3077

paul.Elliott@honeywell.com

Russ Smith

(602) 231-3599

russ.smith@honeywell.com

Dan Grady

(602) 231-3348

dan.grady@honeywell.com			Honeywell contacts for T53 engines.  Technical publications.

National Technical Information Service

1 800 553-6847

(703) 605-6000

5285 Port Royal Raod

Springfield, VA  22161			Maintenance manuals for Army helicopters.

Randy Stewart

Department of Energy

Senior Aviation Policy Officer, MA-10

Office of Aviation Management

1000 Independence Ave., SW,

Rm 9H-063

Washington, DC  20585

(202) 586-6171				IPG Work Group

Andrew L. Kelley

Product Support Engineer

Bell Helicopter Textron

PO Box 482

Fort Worth, TX  76101

(817) 280-4074				IPG Work Group

Richard Thomas

Federal Aviation Administration

FTW-Aircraft Evaluation Group (AEG)

3601 MEACHAM BLVD.

Fort Worth, Texas  76193-0270

(817) 222-5272				IPG Work Group

Mike Miles

General Services Administration

1800 F Street, NW  Rm 1221A

Washington, DC  20405

(202) 219-1356				IPG Work Group and

IPG Custodian

Chapter 1

Introduction

_________________________________________________________________________________

1-1.	GENERAL

This document, the OH-58A, A+, and C Helicopters Inspection Planning Guide (IPG), is available to operators of OH-58A, A+, and C Helicopters for the purpose of providing operators with an alternative inspection program.  The IPG has been developed as a reasonable basis for the inspection program development.

The owner/operator conducting public use operations may use this document as an alternative of an inspection program to assure an adequate level of safety.

WARNING

Unless specifically designated herein, standards for

serviceability for the airframe maintenance and inspection contained

in this document are found in the applicable military maintenance document

for these specific make and models of aircraft, OH-58A, A+, C aircraft.

Unless specifically designated herein standards for serviceability

for the engine maintenance and inspection contained in this document are

found in the Allison Operation and Maintenance Manual; Allison publication

5W2 or 10W2 for these specific models of engine, Allison 250-series engines.

This document contains the requirements for the Preventive Maintenance Inspection (P.M.I.), Intermediate Inspection, Periodic Inspection, and Special Inspections that shall be performed on the OH-58A, A+, and C helicopters.

Inspections required herein shall be performed by an appropriately certificated person (under 14 Code of Federal Regulations, Part 65) or a Federal Aviation Administration certified Airframe and Powerplant mechanic.

An owner/operator shall develop a checklist for each inspection outlined in this document.

Maintenance functions and definitions of terms shall be in accordance with applicable military maintenance manual for the OH-58A, A+, and C unless otherwise stipulated in this document.

The IPG is applicable to an OH-58A, A+, and C helicopters operating in a flight profile similar to the U.S. Military.

NOTE

OH-58A, A+, and C helicopters used for repetitive lift operations

(logging,water bucket, long line, etc.), shall require additional

and/or more frequent inspections as deemed necessary based on

operational experience and/or Alert Service Bulletins and/or airworthiness Directives.  OH-58A, A+, and C helicopters modified through incorporation

of Supplemental Type certificates or equipped with special mission kits

shall require additional inspections as deemed necessary.

The IPG is presented for OH-58A, A+, and C model helicopters.  The IPG is also presented for the Allison 250 series engines.  The engine should be maintained and inspected in accordance with the manufacturer’s Operation and Maintenance Manual; Allison publication 5W2 or 10W2 and the appropriate manufacturer’s service bulletins.

NOTE

An engine Health Indicator Test (HIT) is normally a pre-flight

function performed by the pilot and has not been included in the IPG.

However, the operator should establish a method for engine trend monitoring

to evaluate engine health and performance.  A suggested method for engine

trend monitoring is found in the Allison Operations and Maintenance Manual.

1-2.	WARNING, CAUTIONS, AND NOTES DEFINED.

WARNING

An inspection procedure, practice, etc., which if not

correctly followed,could result in personal injury or loss of life.

CAUTION

An inspection procedure, practice, etc., which, if not strictly

observed, could result in damage to or destruction of equipment.

NOTE

An inspection procedure, condition, etc., which is essential to emphasize.

1-3.	AIRCRAFT, AIRCRAFT ENGINES, AND APPLIANCES DOCUMENTS/RECORDS REVIEW:

Review aircraft, aircraft engines, appliances, forms and records for any recorded discrepancies and for any applicable Airworthiness Directives or Department of Defense Safety of Flight Messages.

1-4.	FORMAT DEFINED

The IPG is divided into:	Example:

Chapters,				CHAPTER 7 Special Inspections

Sections,				SECTION V.  LOWER PYLON

Headings,				8-1. HARD LANDING

Paragraphs,				10.	Tail rotor gearbox.

and subparagraphs.			10.1	Remove tail rotor gearbox.  Check

for cracks.  Etc.

a.	Main rotor blades.

1.	Bolt contact etc.

(a)	Remove spline etc.

(1)	Tighten bolt 											etc.

Chapter 2

Inspection Descriptions

_________________________________________________________________________________

NOTE

Prior to placing an aircraft on this program,

a P.M.I., Intermediate, Periodic and any Special

Inspections that may be required, should be accomplished.

2-1.	PREVENTIVE MAINTENANCE INSPECTION (P.M.I.) Chapter 3

A P.M.I. is accomplished each 12 1/2 flight hours or every 14 calendar 	days, whichever occurs first.

2-2.	INTERMEDIATE INSPECTION (25 Hour) Chapter 4

An inspection that is performed each 25 hours.

2-3.	PERIODIC INSPECTION (300 Hour) Chapter 5

An inspection that is performed each 300 hours or 12 calendar months whichever comes first.

2-4.	SPECIAL INSPECTIONS Chapter 6

In addition to the P.M.I., Intermediate and Periodic Inspections, required 	Special Inspections are performed on a calendar basis, a cycle basis, a 	combination of hourly/calendar basis, or following the installation of a 	major component such as a gearbox installation.

Special Inspections performed on the engine are required at periodic 	intervals to maintain proper operation and performance of the engine to 	assure airworthiness.

Refer to applicable Allison publication 5W2 or 10W2, commercial engine 	bulletins, commercial service letters, etc., for specific or supplemental 	information and instructions.

2-5.	CONDITIONAL INSPECTIONS Chapter 7

An inspection which is contingent upon specific conditions or incidents 	that arise and only because of these conditions or incidents.  Examples of 	these conditions or incidents are hard landings, overspeed, and sudden 	stoppage.  An inspection is required in such cases before further 	flight.  Refer to the applicable military aircraft operations manual, 	aircraft technical manual, and DMWRs for limitations and inspection 	criteria.

Inspection Schedules

_____________________________________________

Flight Hours

25		50		75		100	125	150	175	200	225	250	275	300

Inspections

P.M.I.		Every 12 1/2 Flight Hours or 14 Days, whichever comes first.

INTERMEDIATE	 X		 X		 X		  X	 X	 X	 X	 X	 X	 X	 X	 X

PERIODIC					 X

SPECIAL		As required

CONDITIONAL		As required

NOTE

1.	If an aircraft will be out of service more than 30 days, a P.M.I. shall be 	performed prior to returning the aircraft to service.

2.	If an aircraft is out of service more than 14 days, a run-up in accordance 	with appropriate manuals is strongly recommended.

3.	The complete aircraft must be inspected within 12 calendar months, which 	means a P.M.I., Intermediate inspection, and Periodic inspection, and any 	required special inspections must have been performed.  Therefore, if an 	aircraft flies less than 300 hours in 12 calendar months, the next 	Intermediate and a Periodic inspection must be performed.  If an aircraft 	flies greater than 300 hours, the inspection cycle is continued and no 	additional inspections are required.  See inspection schedules chart above.

4.	Engine overhaul and retirement life limited intervals (hours/cycles) - 	refer to the Allison Operations and Maintenance Manual; Allison publication 	5W2 or 10W2.

5.	Airframe retirement life intervals (hours/calendar), refer to appropriate 	military technical manuals.

Chapter 3

Preventive Maintenance Inspection (P.M.I.)

_________________________________________________________________________________

NOTE

Refer to applicable OH-58 lubrication chart and

review aircraft, aircraft engines, appliances, forms and

records for any recorded discrepancies and for any applicable

Airworthiness Directives or Department of Defense Safety of Flight Messages.

SECTION I		NOSE AREA

1.1	Inspect nose section exterior for visible damage.

1.2	Check pitot tube and static ports for obstructions, cleanliness, and pitot 	static drains for damage.

1.3	Inspect landing/search lights, brackets, terminals and wiring for condition 	and security.

1.4	Inspect vent system drain for obstructions, condition.

1.5	Check windshields, windows and chin bubbles for cracks or damage and 	cleanliness.

1.6	Check WSPS windshield deflector, upper and lower cutters for damage and 	security.  Check breakaway tip for looseness.

SECTION II		CABIN AND LANDING GEAR AREA (RIGHT SIDE)

2.1	Check cabin exterior for damage.

2.2	Inspect antennas for condition and security.

2.3	Check crew and cabin doors for positive latching and operation.  Inspect  		door posts for cracks and safeties properly installed on jettison handles.

2.4	Check cabin and nose section interior for cleanliness, proper stowage of 		equipment, loose connections and visible damage.

2.5	Inspect anti-torque pedals for freedom of operation and security.

2.6	Check current compass correction card.

2.7	Inspect instrument panel and instruments for security,condition and range 	markings.

2.8	Inspect Outside Air Temperature (OAT) indicator for condition and security.

2.9	Check fuel valve handle for binding and condition.  Check full range of 	travel, leave in "ON" position.

2.10	Inspect overhead console for condition and security.

2.11	Inspect utility light and heater control for condition, security and 	mounting.

2.12	Check collective and power controls for freedom of operation, boots for 	condition and throttle set screw.

2.13	Inspect cyclic control for freedom of operation, boots and grips for 	condition and security of electrical connectors.

2.14	Inspect shoulder harness, seat belts, seat backs and bottoms for condition, 	security and proper installation.  Inspect and check inertia reels for 	damage, security, and positive locking.  Check seat belt mounting hinges 	and brackets for cracks.  Check retarder springs for proper operation.  	Check armor plates for cracks, delamination and security if installed.

2.15	Check fire extinguisher for designated location, inspection tag and seal.

2.16	Inspect first aid kits, for security and completeness of contents.

2.17	Inspect passenger seat backs, cushions and retainer loops for condition, 	security and proper installation.  Inspect and check sound-proofing for 	condition, security and cleanliness.

2.18	Inspect aft electrical equipment shelf for unauthorized or foreign objects, 	cleanliness and security of components.

SECTION III		ENGINE AREA (RIGHT SIDE)

3.1	Inspect induction fairing for proper seal at firewall and particle 	separator.

3.2	Inspect engine air intake ducts and plenum for obstructions or damage.  	Inspect air induction fairing for seal security, conditions, and bond voids 	along the seals complete length.  Inspect sand and dust separator for 	damage and particle ejection opening for freedom of obstructions.

3.3	Inspect engine cowling and fairing for damage and security of fasteners and 	hinges.

3.4	Check anti-collision light for condition and security.

3.5	Inspect engine mounts and fittings for cracks, damage and security.

3.6	Inspect fuel control linkage for damage and security.

3.7	Check compressor bleed valve for condition and security.

3.8	Inspect engine accessories and connections for damage, corrosion and 	security.

3.9	Inspect exhaust stack and clamps for condition, corrosion and cracks and 	engine combustion chamber housing, turbine support and exhaust ducts for 	cracks, dents, burned or buckled areas.

3.10	Check starter generator and exhaust duct for condition, security and 	obstructions.

3.11	Inspect engine to transmission driveshaft for condition and evidence of 	grease leakage and over-heating.  If engine to transmission driveshaft

P/N 206-040-371-111 is used, inspect for damage and fastener security.

SECTION IV		AFT FUSELAGE AREA (RIGHT SIDE)

4.1	Check fuel filler cap for proper locking, condition of seal and lanyard.

4.2	Inspect rubber pad below fuel receiver for debonding.

4.3	Inspect battery and fuel vents for condition and security, proper 	positioning and obstructions.

4.4	Check air ducts for condition and security.

4.5	Check Ground Power Unit (GPU) access door for condition and security.

SECTION V		AFT FAIRING AND OIL COOLER (RIGHT SIDE)

5.1	Inspect engine oil tank for condition and security and oil level.  Inspect 	oil lines for leaks and damage.

5.2	Inspect oil filler access door for condition, marking and placard, and 	security.

5.3	Inspect engine scavenge oil filter for security, leaks and indication of 	bypass (if installed).

SECTION VI		TAIL BOOM AREA

6.1	Inspect tail boom exterior and driveshaft cover for visible damage and 	condition of fasteners.

6.2	Inspect long tail rotor drive shaft and bearings for evidence of overheat, 	splinded adapters for freedom of movement and slippage marks.

NOTE

Do not wipe grease from seal area

(not required after compliance with MWO 55-1520-228-50-25).

6.3	Inspect segmented driveshaft for condition and security, coupling disc for 	distortion, cracks and security.  Check splined adapter for freedom of 	movement and bearing and driveshaft for evidence of overheating.

NOTE

Do not wipe grease from seal area

(not required after compliance with MWO 55-1520-228-50-25).

6.4	Inspect horizontal stabilizer and navigational lights for condition and 	security.

6.5	Inspect vertical stabilizer, tail skid, tail light and support and antenna 	leads for damage and security.

6.6	Inspect ballast installation for security and condition.

  - Inspect tail rotor controls for damage and security of attachment bolts.

NOTE

Suspected crack will be confirmed by penetrate inspection.

6.8	Inspect tail rotor gearbox for security, oil level and vent for 	obstruction.  Inspect sight glass for damage or stains that might give a 	false indication of oil level.  Inspect tail rotor gearbox casing and 	support rivets for cracks, damage or evidence of ‘working’ rivets.

6.9	Inspect tail rotor hub and blade assembly for security and damage.  Check 	blades for cleanliness.

WARNING

Tail rotor blades P/N 206-010-750 are not authorized for use.

6.10	Inspect all self-locking nuts on the hub and blade assembly for cracks and 	security.

6.11	Following check not required after compliance with MWO 55-1520-228-50-25.  	Inspect tail rotor blades for cracks on both sides in the area 	approximately 7 inches outboard from the butt end and l.5 inches aft of the 	leading edge.

WARNING

If cracks are revealed blade must be removed prior to furtherflight.

NOTE

Tail rotor blades SN TLL-8000 and below require ten power

magnification for this check and careful inspection for corrosion and deterioration of clear coating on the areas left clear for this inspection.

6.12.	Inspect tail rotor blade tip blocks for cracks, debonding and loose, 	missing or corroded rivets.

SECTION VII		AFT FAIRING AND OIL COOLER AREA (LEFT SIDE)

7.1	Inspect engine oil tank for damage, access door for security.

7.2	Inspect oil cooler blower, ducts and driveshaft for damage, cracks and 	foreign material.

7.3	Inspect aft fairing assembly for damage.

SECTION VIII	AVIONICS AND AFT FUSELAGE AREA (LEFT SIDE)

8.1	Inspect avionics compartment for security of items and door for condition 	and operation.

8.2	Inspect antennas for damage, debonding and security.

8.3	Check battery for leakage and security.  Check foam pad for condition and 	security.

8.4	Inspect external power receptacle for condition and security.

SECTION IX		ENGINE AREA (LEFT SIDE)

9.1	Inspect engine cowling and fairing for damage, security and condition of 	fasteners.

9.2	Inspect engine mounts and fittings for cracks and security.

9.3	Check airframe mounted fuel filter for leaks and security.

9.4	Inspect engine accessories and connections for damage and security.

9.5	Check linear actuator, linkage and electrical lead for condition and 	security.

9.6	Inspect exhaust stack and clamps for condition, corrosion and cracks and 	engine combustion chamber housing, turbine support and exhaust ducts for 	cracks, dents, burned or buckled areas.

9.7	Check drain valve for leakage, security and evidence of contact with 	driveshaft.

9.8	Check fuel nozzle and lines for leaks, condition and security.

9.9	Inspect forward tail rotor driveshaft for corrosion, freedom of movement on 	the splined adapters and cleanliness.

9.10	Inspect particle separator for damage.

9.11	Inspect engine air inlet air bellmouth for damage, obstructions and plenum 	area for loose or foreign objects.

SECTION X		TRANSMISSION AND PYLON AREA

10.1	Inspect main rotor hub assembly for leakage, damage, security and proper 	oil level.

10.2	Check pillow blocks for condition and security of mounting hardware and 	slippage marks.

CAUTION

If slippage has occurred, replace hardware.

10.3	Inspect static stops for damage and security.

10.4	Inspect main rotor yoke assembly for cracks and evidence of corrosion 	between the pillow block bores and the lower flange on inboard surfaces.  	Wipe clean the yoke web section and outer surfaces.

NOTE

If inspection by flashlight reveals indication of crack, validate by

fluorescent penetrant.  If crack is confirmed remove hub assembly for evaluation.

10.5	Inspect main rotor blades for cleanliness, damage, condition, corrosion and 	security.  Check for condition of protective coating.

10.6	Inspect visible areas of the mast for damage.

NOTE

Assure swashplate is level for inspection of outer

ring self aligning bearings for main rotor push-pull tubes.

10.7	Inspect swashplate, lever and sleeve, and connecting linkage for security 	and damage.  Check swashplate support base drain holes are open and free of 	foreign matter. Inspect swashplate support for evidence of damage.

10.8	Check cyclic and collective control linkage for security and condition.  	Check security of attachment bolts by attempting to turn nuts with fingers

CAUTION

Do not remove cotter pin.

10.9	Inspect main rotor pitch links for damage and security of attachment, tubes 	for corrosion and cracks.

NOTE

Pay particular attention to swaged ends at the jam nut.

10.10	Inspect hydraulic system components and lines for security, chaffing, 	leaks, damage and reservoir for  oil level.  Check collective actuator 	bellcrank cover for missing rubber flipper or bond failure.  Check for 	proper security of reservoir cap and pin assembly.

10.11	Inspect hydraulic filter element for indication of filter by pass.

10.12	Check power turbine governor (N2) linkage for freedom of operation, 	condition and security.

10.13	Check hydraulic pump, rotor tach generator for condition and security.

10.14	Inspect transmission oil cooler ducting, filter head and filter for 	damage, condition and security

10.15	Inspect pylon isolation mount, cover, drag pin assembly and cabin roof for 	damage and condition.

10.16	Visually inspect clevis area and mount for cracks or other damage.  	Inspect entire area for loose, broken or missing hardware.

10.17	Check area under drag pin for oil or water.  Inspect transmission deck 	area for dents, cracks, holes and overall condition.

10.18	Inspect pylon support links for cracks, condition and security of hardware.

10.19	Inspect main transmission case assembly and all electrical connections for 	damage, condition and security.  Check transmission fluid level and service 	if required.  Inspect sight glass for condition and leakage.

10.20	Inspect particle separator intake and swirl tubes for damage and security.

10.21	Check security of engine cleaning tube and cap assembly.

10.22	Inspect cowling and cabin roof mounted antennas and connections for 	serviceability and security.

SECTION XI		CABIN AND LANDING GEAR AREA (LEFT SIDE)

11.1	Inspect landing gear for condition of skid tubes, cross tubes attachment 	fittings and skid shoes for damage or evidence of hard landing and 	security.

11.2	Check crew and cabin doors for positive latching and operation, vents and 	hinges for operation and security.

11.3	Inspect seats for damage and security.  Inspect cushions for cleanliness 	and proper installation.  Inspect armor plates for cracks, delamination and 	security if installed.

11.4	Check crew and cabin door jettison handles for proper operation and 	safeties.

SECTION XII		LUBRICATION (ALL AREAS)

12.1	Service in accordance with TM 55-1520-228-23, applicable to daily and 25 	hour requirements.

SECTION XIII	ELECTRICAL POWER ON

13.1	Check pitot heater for proper operation.

13.2	Check all panel mounted warning, caution and segmented panel lights 	illuminate properly.

13.3	Check operation of all cockpit and cabin lighting.

WARNING

Assure defog blower motors are free of debris prior to checking operation.

13.4	Operate defogging blower motors for a minimum of 15 seconds for proper 	function check.

13.5	Operate all exterior lights and check for illumination.

Chapter 4

Intermediate Inspection (25 Hour)

_________________________________________________________________________________

SECTION I	GENERAL

NOTE

Refer to applicable OH-58 lubrication chart.

1.1	Perform a P.M.I. inspection.

SECTION II		NOSE AREA

2.1	Drain moisture from pressure and static ports (if required).

2.2	Check attached optional equipment for condition and security.

SECTION III		CABIN, ELECTRICAL EQUIPMENT SHELF AND LANDING GEAR AREA

3.1	Check radio antenna, masts, and insulators for condition and security.

3.2	Inspect cross tube attachment points.						  |

3.3	Check radio switches and knobs for condition and security.

3.4	Check radio headsets, microphones, leads, plugs and jacks for operation and 		general condition and security.

3.5	Inspect visible pitot and static tubes for damage, security and freedom 		from obstruction.

3.6	Inspect visible wiring, insulating tubing, and retaining clamps for general 		condition and security.

3.7	Check ventilating system controls for operation.  Inspect air ducts for 		condition and security and check drains for obstruction.

SECTION IV		TRANSMISSION AND PYLON AREA

4.1	Inspect main rotor hub for condition and security of hardware.  Inspect 		flapping bearings for freedom of operation by tipping hub assembly 				spanwise.  Inspect main rotor retaining nut for security and safety.  			Inspect pillow blocks for mounting condition, security of mounting bolts 		and slippage marks.

4.2	Inspect blade bolts and latch retainer and nut for security.

4.3	Inspect main rotor control tubes and links for condition and security.

4.4	Inspect swashplate and control for condition and security.  Inspect inner 		and outer swashplate arms for cracks.  Check bearings for freedom of 			movement.

4.5	Inspect fuselage upper and intermediate structure and cowling for damage, 		cracks, and condition.

4.6	Inspect hydraulic servo actuator control linkage and bolts for condition 		and security.  Check actuator valve linkage for freedom of movement.

4.7	Inspect hydraulic reservoir for damage, leakage and correct oil level.  		Check reservoir cover for proper locking and security.  Check groove area 		of reservoir cover tab for cracks.

SECTION V		ENGINE AREA

5.1	Inspect engine and engine area for loose or missing nuts and bolts, loose 		or broken wires and connectors.  Check accessories for security or broken, 		missing, or improper safety.

5.2	Inspect engine and accessible area for obvious damage and evidence of fuel 		or oil leakage.

5.3	Check engine mount and support bolts for condition, security, and proper 		safety.

5.4	Check engine firewall and cowling for condition and security.

5.5	Check fuel system components and lines for security and leakage.  Inspect 		filter for security and leakage.

NOTE

If leakage is evidenced refer to Allison publication 5W2 or 10W2.

5.6	Check governor and fuel control linkage for freedom of operation, proper 		rigging, and security.

5.7	Tachometer generator (power turbine):  Inspect mounting flange for cracks.  		Check paint marks for slippage.

5.8	Tachometer generator (gas producer):  Inspect mounting flange for cracks.  		Check paint marks for slippage.

SECTION VI		AFT FUSELAGE AREA AND AVIONICS COMPARTMENT

6.1	Inspect Fuselage for signs of damage, cracks, and general condition.

6.2	Check lower anti-collision light for condition and security.

6.3	Inspect voltage regulator and associated components for condition and 			security.  Inspect wiring for chafing, condition, security, and proper 			connection.  Inspect terminals for security or corrosion.

6.4	Check lead acid battery electrolyte for proper level.  Check vent tube 			for freedom from obstruction.

6.5	Check nickel cadium (nicad) battery in accordance with manufacturer’s 			instructions.

SECTION VII		TAIL BOOM AREA

7.1	Inspect tail rotor flapping bearings for freedom of movement.

7.2	Inspect tail rotor pitch change linkage for wear, security and freedom of 		operation and tail rotor pitch change (PC) links for cracks with ten power 		magnification.

NOTE

Suspected cracks will be confirmed by dye penetrant inspection.

7.3	Inspect tail rotor pitch change bearings and rod end bearings for 					looseness.

SECTION VIII	POWER ON

8.1	Check all switches and circuit breakers for proper operation.

8.2	Check airframe fuel filter bypass warning system for proper operation.

SECTION IX		AVIONICS

9.1	Perform avionics inspections, and check, and/or test avionics equipment as 		required.

SECTION X		POWER OFF

10.1	Check all fixed equipment is refitted and properly secured.

10.2	Check that tools, rags, and foreign objects are removed from aircraft.

10.3	Check all inspection doors and access panels are properly closed or 				installed.

Chapter 5

Periodic Inspection (300 Hour)

_________________________________________________________________________________

SECTION I	GENERAL

NOTE

Refer to applicable OH-58 lubrication chart.

1.1	Perform a P.M.I. and an Intermediate Inspection in addition to the 	following items.

SECTION II		CABIN, ELECTRICAL EQUIPMENT SHELF AND LANDING GEAR AREA

2.1	Remove access panel above electrical shelf and inspect fuel shutoff valve 	and linkage for condition, proper operation, security and evidence of 	leaks.

2.2	Check seat cushions. seat belts, inertia reels, and shoulder harnesses for 	security, cleanliness, and general condition.

2.3	Check door jettison mechanism for proper operation.

2.4	Check cyclic, collective, and directional controls for general installation 	and freedom of movement through full range of operation and correct 	response to control movement.

2.5	Check all control friction adjustments for correct control operation and 	general condition.

2.6	With vertical post cover and pilot and copilot seat panels removed, inspect 	cyclic, collective, anti-torque and throttle control linkage and cable for 	damage, operation, binding and interference.

2.7	Inspect control linkage and bellcranks for cracks, security, and general 	condition.

2.8	Remove access panel from instrument console and inspect instrument 	wiring and plumbing for damage, security, deterioration and proper 	connection.

2.9	Inspect radio cables, plugs, and associated fittings for damage, security. 	and general condition.  Inspect bonding straps for condition and security.

2.10	Check removable radio units for condition and security.

2.11	Check radio equipment for cleanliness from dust and foreign material.

  - Check torque meter for accuracy during run-up.

2.13	Check turbine outlet temperature indicator for accuracy using electronic 	test equipment (Barfield).

SECTION III		TRANSMISSION AND PYLON AREA

3.1	Check swashplate duplex bearing for smoothness by disconnecting idler link 	and rotor pitch links (do not allow rotor blades and grips to rotate on the 	yoke), free lower end of boot, and rotate outer ring in both directions.

3.2	Check swashplate uniball for proper friction, adjust as required.

3.3	Check swashplate support pivot sleeve bearing slot sidewalls and Teflon 	sleeve and bolts for condition and security.

3.4	Inspect hydraulic servo-cylinder supports for cracks.

3.5	Inspect main rotor system flight control bolts.

3.6	Remove particle separator and induction cowling.  Inspect engine inlet for 	foreign object damage.  Inspect separator and cowling for damage.

3.7	Inspect mast assembly as follows:

a.	Remove mast nut and cap plug.  Inspect internal surface (ID) of 			mast for corrosion and condition of protective coating by using a 		bright light.

b.	Install cap plug.									  |

c.	Lightly coat mast nut threads with corrosion preventive compound    |

(C53), install mast nut, torque to 250 to 275 inch pounds and       |

install lockwire.									  |

d.	Check mast nut torque after 25 operating hours as outlined in  			SPECIAL INSPECTION 6-22.

3.8	Inspect longeron and engine pan interface as follows:

a.	Remove access panel from access hole through canted web.

b.	Open engine compartment cowling.

c.	Use bright light and mirror to expose upper and lower edges of the 		joints and fastener between the aluminum longeron and titanium engine 		pan.  The edge of the Proseal 890 fraying surface coating should be 		visible.

CAUTION

No indications of corrosion such as corrosion pits, finish blisters

or surface stains by corrosion material from joint should be detected.

3.9	Inspect airframe fuel filter elements.  Using a 0.020 inch wire, pass the 	wire through the outlet bleed port to check that the bleed port is not 	clogged.  Replace with new fuel filter element.

3.10	Drain hydraulic reservoir and system and inspect inside bottom of reservoir 	for corrosion and pitting.  Re-service hydraulic reservoir.

SECTION IV		ENGINE AREA

4.1	Inspect particle separator and engine inlet bellmouth for damage, 	obstructions and plenum area for loose or foreign objects.  Inspect exhaust 	stack clamp as follows:

CAUTION

Do not bend clamps during removal, inspection or installation.

a.	Remove both right hand and left hand exhaust stack clamp, by			removing nuts on both "T" bolts.

b.	Inspect both sides of each clamp for any evidence of cracking around 		rivets, particularly at the gaps between the V band sections.

NOTE

Cracks will most likely begin at the edge of a rivet and

run radially to the edge or to the next rivet.  Look for cracks

or corrosion tracks which indicate an imminent crack.  Any clamp that

displays evidence of cracking shall be condemned and replaced with a like,

serviceable item.  Clamps that exhibit surface corrosion only, may be reinstalled on exhaust stacks.  Replace corroded clamps as soon as new ones become available.

4.2	With freewheeling unit drained, check magnetic plug for metal particles.

4.3	Refer to Allison publication 5W2 or 10W2 for all inspection requirements 	and recommended maintenance procedures regarding engine operations.

SECTION V		FUSELAGE AREA

5.1	Check fuel cell for leakage and check torque of access opening bar and 	cover bolts

NOTE

If MWO 55-1520-228-30-32 has not been complied with, re-torque

upper clamp on fuel support hose inside fuel cell (refer to applicable TM).

5.2	Check air ducts, heater, and access panel for condition and security.

5.3	Inspect tail rotor control tubes located under engine for security, 	condition, chafing or binding.

5.4	Inspect engine deck longeron for condition.

SECTION VI		TAIL BOOM AREA

6.1	Inspect tail rotor driveshaft bonded fittings for security.

6.2	With tail rotor control tube assembly removed, inspect for wear at five 	areas where tube may contact fairleads.

SECTION VII		ELECTRICAL POWER ON

7.1	Inspect transmission, tail rotor and engine chip detector circuit for 	continuity.  With power on, ground detector plug to airframe and short 	across magnet, light should illuminate.

SECTION VIII	RUN-UP

8.1	Test all electrical systems and lights for proper operation.

8.2	Wash compressor in accordance with Allison publication 5W2 or 10W2.

8.3	Ground run aircraft and check for leaks, vibrations in tail, fuel and oil 	pressures, anti-ice valve operation and engine performance (HIT).

8.4	Check heater for proper operation and fuel odor.

8.5	Check voltage and adjust voltage regulator if required.

8.6	Check idle RPM and governor beep range.

8.7	Check compressor bleed control valve for proper operation.

8.8	Check turn and slip indicator for proper operation.

8.9	Check attitude indicator for proper operation.

8.10	Check engine oil pressure indicator for proper operation.

8.11	Check engine oil temperature indicator for proper operation.

8.12.	Check tachometer indicator, rotor and power turbine, for proper operation.

8.13	Check tachometer indicator, gas producer, for proper operation.

8.14	Check free air temperature indicator for proper operation.

8.15	Check on board clock for proper operation.

8.16	Check operation of any optional equipment.

8.17	Check oil and hydraulic fluid levels after run-up and engine shutdown.

Chapter 6

Special Inspections

_________________________________________________________________________________

In addition to the P.M.I., Intermediate, and Periodic Inspections required Special Inspections are performed on a calendar basis, a cycle basis, a combination of hourly/calendar basis, or following the installation of a major component such as a gearbox installation.

Special Inspections performed on the engine are required at periodic intervals to maintain proper operation and performance of the engine to assure airworthiness.  Refer to applicable Allison publication 5W2 or 10W2, commercial engine bulletins, commercial service letters, etc., for specific or supplemental information and instructions.

Special Inspections Index								Page

6-1.	ANY TIME ENGINE ASSEMBLY IS REPLACED 	.	.	.	.	39

DUE TO METAL CONTAMINATION

6-2.	ANY TIME THE TRANSMISSION IS REMOVED	.	.	.	.	39

6-3.	ANY TIME MAIN ROTOR MAST ASSEMBLY IS

TRANSFERRED TO ANOTHER AIRCRAFT	.	.	.	.	.	39

6-4.	ANY TIME TRANSMISSION IS REMOVED AS A

RESULT OF METAL PARTICLES	.	.	.	.	.	.	39

6-5.	AFTER INSTALLING AN ENGINE OR ENGINE

COMPONENT	.		.	.	.	.	.	.	.	39

6-6.	AFTER INSTALLING A REPAIRED FREEWHEELING UNIT	.	.	.	39

6-7.	AFTER EACH ENGINE CHANGE	.	.	.	.	.	.	40

6-8.	ANYTIME MAIN DRIVESHAFT IS REMOVED	.	.	.	.	.	40

6-9.	AFTER INITIAL RUN-UP FOLLOWING TAIL ROTOR

GEARBOX INSTALLATION	.	.	.	.	.	.	.	40

6-10.	ANYTIME AIR IN THE FUEL LINE IS SUSPECTED	.	.	.	.	40

6-11.	ANY TIME MAIN ROTOR HUB AND BLADE ASSEMBLY

IS TRANSFERRED TO ANOTHER HELICOPTER	.	.	.	.	40

6-12.	AFTER THE HELICOPTER HAS BEEN SUBJECTED TO

SALT WATER OR SALT WATER SPRAY	.	.	.	.	.	40

Special Inspections Index Continued.						Page

6-13.	WHEN OPERATING FROM A BASE WITHIN 10 MILES

OF SALT WATER OR WHEN HELICOPTER IS FLOWN

BELOW 500 FEET OVER SALT WATER	.	.	.	.	.	40

6-14.	AFTER WASHING HELICOPTER	.	.	.	.	.	.	40

6-15.	WHEN MAJOR MODIFICATIONS OR MAJOR AIRFRAME

REPAIRS ARE ACCOMPLISHED, ANY SPECIAL

EQUIPMENT HAS BEEN ADDED TO OR REMOVED FROM

THE BASIC AIRFRAME, OR WHEN WEIGHT AND BALANCE

DATA ARE SUSPECTED TO BE IN ERROR	.	.	.	.	.	41

6-16.	AT EACH ENGINE OIL CHANGE	.	.	.	.	.	.	41

6-17.	AT EACH TIME MAIN ROTOR PITCH LINKS AND THE

IDLER LINK ARE DISCONNECTED	.	.	.	.	.	.	41

6-18.	AFTER EACH ENGINE CHANGE, ELECTRICAL EQUIPMENT

CHANGE, OR MAJOR STRUCTURAL CHANGE LIKELY

TO AFFECT THE COMPASS	.	.	.	.	.	.	.	41

6-19.	AFTER INSTALLATION OF ENGINE MOUNT

TO AIRFRAME BOLTS		.	.	.	.	.	.	.	41

6-20.	AFTER INSTALLATION OF TAIL BOOM  	.	.	.	.	.	41

6-21.	FIVE TO TEN HOURS AFTER INSTALLATION OF

PILLOW BLOCK HARDWARE	.	.	.	.	.	.	.	41

6-22.	25 HOURS AFTER MAIN ROTOR MAST NUT INSTALLATION	.	.	.	42

6-23.	25 HOURS AFTER INSTALLATION OF SWASHPLATE	.	.	.	.	42

6-24.	EVERY 50 HOURS	.	.	.	.	.	.	.	.	42

6-25.	EVERY 100 HOURS	.	.	.	.	.	.	.	.	42

6-26.	AT FIRST 100 HOUR INSPECTION FOLLOWING

MAST NUT INSTALLATION	.	.	.	.	.	.	.	44

6-27.	AT FIRST 100 HOURS AFTER INSTALLATION

OF TAIL BOOM	.	.	.	.	.	.	.	.	44

6-28.	EVERY 100 HOURS OR 120 CALENDAR DAYS

WHICHEVER OCCURS FIRST	.	.	.	.	.	.	.	44

6-29.	100 HOURS AFTER INSTALLATION OF PILLOW

BLOCK RETENTION BOLTS AND NUTS OR

INSTALLATION OF A NEW OR OVERHAULED

MAIN ROTOR HUB ASSEMBLY	.	.	.	.	.	.	.	44

6-30.	100 HOURS AFTER SERVO ACTUATOR INSTALLATION	.	.	.	44

Special Inspections Index Continued.						Page

6-31.	100 HOURS OF OPERATION AFTER THE TAIL ROTOR

GEARBOX HAS BEEN INSTALLED OR HARDWARE ADJUSTED	.	.	.	44

6-32.	EVERY 150 HOURS OR 6 CALENDAR MONTHS WHICHEVER OCCURS FIRST	.	44

6-33.	EVERY 200 HOURS	.	.	.	.	.	.	.	.	45

6-34.	AFTER 200 HOURS OR WHEN RED BUTTON (IMPENDING

BYPASS INDICATOR) IS SHOWING	.	.	.	.	.	.	45

6-35.	EVERY 500 HOURS OR 12 CALENDAR MONTHS.	.	.	.	.	45

6-36.	EVERY 600 HOURS	.	.	.	.	.	.	.	.	45

6-37.	AFTER 600 HOURS AND 900 HOURS OF OPERATION

OF NEW RETENTION STRAP	.	.	.	.	.	.	.	45

6-38.	EVERY 1000 HOURS	.	.	.	.	.	.	.	.	45

6-39.	EVERY 1200 HOURS 	.	.	.	.	.	.	.	.	45

6-40.	EVERY 100 HOURS AFTER THE 1200 HOUR INSPECTION

OF SWASHPLATE DUPLEX BALL BEARING UNTIL THE 2400

HOUR OVERHAUL OF THE SWASHPLATE	.	.	.	.	.	46

6-41.	AFTER 1200 HOURS OPERATION OF NEW OR

OVERHAULED MAIN ROTOR HUB ASSEMBLY 	.	.	.	.	.	46

6-42.	AFTER 1200 HOURS OPERATION OF NEW OR

OVERHAULED MAIN TRANSMISSION 	.	.	.	.	.	.	47

6-43.	AFTER 1200 HOURS OPERATION OF NEW OR

OVERHAULED MAIN TRANSMISSION MAST ASSEMBLY	.	.	.	47

6-44.	AFTER 1500 HOURS OPERATION OF NEW OR

OVERHAULED FREEWHEELING ASSEMBLY	.	.	.	.	.	48

6-45.	EVERY 1500 HOURS	.	.	.	.	.	.	.	.	48

6-46.	EVERY 12 CALENDAR CALENDAR MONTHS	.	.	.	.	.	48

6-47.	AFTER 12 CALENDAR MONTHS: OR WHENEVER HELICOPTER IS

TRANSFERRED, RECEIVED, PLACED IN STORAGE,

OR REMOVED FROM STORAGE	.	.	.	.	.	.	.	48

6-48.	EVERY 24 CALENDAR MONTHS	.	.	.	.	.	.	48

6-49.	AFTER 1550 HOURS OPERATION OF NEW OR OVERHAULED

ENGINE WITH PRODUCT IMPROVED TURBINE FOR T63-A-700

AND AFTER 1775 HOURS OR 3000 CYCLES OPERATION OF

NEW OR OVERHAULED ENGINE WITH PRODUCT IMPROVED

TURBINE FOR T63-A-720	.	.	.	.	.	.	.	49

Special Inspections Index Continued.						Page

6-50.	EVERY 1750 HOURS	.	.	.	.	.	.	.	.	49

6-51.	AFTER 2400 HOURS OF OPERATION OF NEW OR

OVERHAULED MAIN TRANSMISSION	.	.	.	.	.	.	49

6-52	AFTER 2400 HOURS OF OPERATION OF NEW OR

OVERHAULED MAIN TRANSMISSION MAST ASSEMBLY	.	.	.	49

6-53	AFTER 2400 HOURS OF OPERATION OF NEW OR

OVERHAULED TAIL ROTOR GEARBOX ASSEMBLY	.	.	.	.	49

6-54	AFTER 3000 HOURS OF OPERATION OF NEW OR

OVERHAULED FREEWHEELING ASSEMBLY 	.	.	.	.	.	49

Special Inspections

_________________________________________________________________________________

6-1.	ANY TIME ENGINE ASSEMBLY IS REPLACED DUE TO METAL CONTAMINATION

a.	Refer to Allison publication 5W2 or 10W2 for instruction regarding 		the necessary actions required.

b.	Replace engine oil cooler.

6-2.	ANY TIME THE TRANSMISSION IS REMOVED

a.	Remove and inspect the pylon support links and the isolation mount.

6-3.	ANY TIME MAIN ROTOR MAST ASSEMBLY IS TRANSFERRED TO ANOTHER AIRCRAFT

a.	Disassemble and inspect for corrosion and condition of parts.

6-4.	ANY TIME TRANSMISSION IS REMOVED AS A RESULT OF METAL PARTICLES

a.	Disassemble as required and inspect main rotor mast bearing for 			corrosion.

b.	Replace transmission oil cooler and filter.

c.	Inspect external transmission oil lines for contamination.

6-5.	AFTER INSTALLING AN ENGINE OR ENGINE COMPONENT

a.	Refer to Allison publication 5W2 or 10W2 for instruction regarding:

1.	Engine operations and check for leaks.

2.	Performance of engine post installation inspection.

6-6.	AFTER INSTALLING A REPAIRED FREEWHEELING UNIT

a.	Refer to Allison publication 5W2 or 10W2 for instruction regarding 		the necessary actions required.

b.	Start aircraft and run for 15 minutes at full RPM then rapidly reduce throttle to ground idle and observe a momentary split of the NR and | N2 needle and then confirm that the needles rejoin.                 |

c.	Fly helicopter in vicinity of a safe landing area for 15 minutes, and 		then perform a power recovery autorotation.                         |

d.	Remove freewheeling unit magnetic plug and drain oil into a clean 		container.

e.	Check magnetic plug and oil for metal chips.

6-7.	AFTER EACH ENGINE CHANGE

a.	Refer to Allison publication 5W2 or 10W2 for instruction regarding:  		check of turbine outlet temperature system.

6-8.	ANY TIME MAIN DRIVESHAFT IS REMOVED

a.	Inspect for condition.

6-9.	AFTER INITIAL RUN-UP FOLLOWING TAIL ROTOR GEARBOX INSTALLATION

a.	Verify torque on tail rotor gearbox attaching hardware 50-70 inch   | pounds plus drag torque.							  |

6-10.	ANYTIME AIR IN THE FUEL LINE IS SUSPECTED

a.	Disconnect the battery and ground the aircraft.

b.	If the helicopter has full fuel, it may be necessary to remove 			approximately two gallons of fuel in order to perform the inspection.

c.	Remove the cap and adapter.  Ascertain that the upper clamp is 			radial.  Re-tighten the upper clamp on the self sealing hose finger 		tight plus two and one half turns.

d.	When re-installing the receiver assembly or cap and adapter, use a 		new packing and torque bolts (refer to applicable TM).

e.	After the inspection, bleed the engine fuel system in accordance with 		Allison publication 5W2 or 10W2.

6-11.	ANY TIME MAIN ROTOR HUB AND BLADE ASSEMBLY IS TRANSFERRED TO ANOTHER 	HELICOPTER

a.	Verify mast nut torque after first flight and after 25 hours of 			operation (refer to applicable TM).

6-12.	AFTER THE HELICOPTER HAS BEEN SUBJECTED TO SALT WATER OR SALT WATER SPRAY

a.	Wash entire helicopter with fresh water, particularly inside of 			engine compartment doors.  Wash all components which were exposed to 		salt water and make a detailed check of all surfaces for corrosion.  		Apply corrosion preventive compound to exposed non-painted, anodized, 		or cadmium plated assemblies.  Refer to TM 55-1500-204-25/1.

6-13.	WHEN OPERATING FROM A BASE WITHIN 10 MILES OF SALT WATER OR WHEN HELICOPTER 	IS FLOWN BELOW 500 FEET OVER SALT WATER

a.	Rinse engine compressor after the last flight of each day.  Refer to 		Allison publication 5W2 or 10W2.

6-14.	AFTER WASHING HELICOPTER

a.	Inspect pitot-static system for moisture.

b.	Check fuselage and tail boom attachment fittings for accumulation of 		water.

6-15.	WHEN MAJOR MODIFICATIONS OR MAJOR AIRFRAME REPAIRS ARE ACCOMPLISHED, ANY 	SPECIAL EQUIPMENT HAS BEEN ADDED TO OR REMOVED FROM THE BASIC AIRFRAME, OR 	WHEN WEIGHT AND BALANCE DATA ARE SUSPECTED TO BE IN ERROR

a.	Weigh aircraft and perform weight and balance records check.

b.	Re-compute empty weight and center of gravity and revise weight and 		balance record (refer to applicable TM)

6-16.	AT EACH ENGINE OIL CHANGE

a.	Refer to Allison publication 5W2 or 10W2 for instruction regarding 		engine oil change.

b.	Change external oil filter if installed.

6-17.	AT EACH TIME MAIN ROTOR PITCH LINKS AND THE IDLER LINK ARE DISCONNECTED

a.	Inspect swashplate duplex ball bearing by rotating swashplate outer 		ring.

NOTE

Replace bearing if rough.

6-18.	AFTER EACH ENGINE CHANGE, ELECTRICAL EQUIPMENT CHANGE, OR MAJOR STRUCTURAL 	CHANGE LIKELY TO AFFECT THE COMPASS

a.	Check magnetic standby and remote compass indicators for accuracy.

NOTE

Compensate when necessary.  Refer to applicable TM.

6-19.	AFTER INSTALLATION OF ENGINE MOUNT TO AIRFRAME BOLTS

a.	Verify torque on attachment bolts and nut (refer to applicable TM) 		and secure with cotter pin.

6-20.	AFTER INSTALLATION OF TAIL BOOM

a.	Verify torque on tail boom attachment bolts after maintenance test 		flight (refer to applicable TM).

6-21.	FIVE TO TEN HOURS AFTER INSTALLATION OF PILLOW BLOCK HARDWARE.

a.	Inspect pillow block retention bolts and nut for slippage.

b.	Verify torque on nuts (refer to applicable TM).

CAUTION

If slippage has occured, replace the bolt.

6-22.	25 HOURS AFTER MAIN ROTOR MAST NUT INSTALLATION

a.	Re-torque mast nut (refer to applicable TM).

6-23.	25 HOURS AFTER INSTALLATION OF SWASHPLATE

a.	Check tilt friction after first 25 flight hours.

6-24.	EVERY 50 HOURS

a.	Verify torque (refer to the applicable TM) of upper clamp of fuel 		hose inside fuel tank.

NOTE

No longer required after completion of MWO 55-1520-228-30-32.

1.	Disconnect the battery and electrically ground the helicopter.

2.	If helicopter fuel cell is full, remove approximately two 				gallons of fuel.

3.	Remove the cap and adapter.  Inspect upper clamp.  If the clamp 			is not radial, install a radial clamp.  Tighten the upper clamp 			assembly on self-sealing hose finger tight plus two and one 			half turns.

4.	Install cap and adapter with new packing and torque bolts 				(refer to applicable TM).

b.	Clean engine compressor.  Refer to Allison publication 5W2 or 10W2.

6-25.	EVERY 100 HOURS

- Refer to Allison publication 5W2 or 10W2 for all inspection 			requirements and recommended maintenance procedures regarding engine 		operations.

NOTE

The below special inspection is not required on those

servo cylinders having an “A” suffix after the serial number.

b.	Servo actuators serial numbers 8383 through and including serial 			number 9318, inspect for cracking on aft end of piston rod between 		jam nut on rod end and valve housing.

c.	Rotating control inspection.

1.	Inspect main rotor pitch links for damage and security of 				attachment.

2.	Inspect tubes for corrosion and cracks, pay particular 				attention to swaged ends at jam nut.

3.	Inspect pitch horn trunnion bearing for evidence of wear.

d.	Inspect bearing clearance of collar set.

e.	Inspect main rotor yoke as follows:

1.	Yoke for evidence of corrosion.

NOTE

If corrosion is evident, remove with scotch brite

fine abrasive pads.  If corrosion cannot be removed with

pads, or is excessive, dissemble hub and inspect and repair.

2.	Yoke center section inboard and outboard surfaces from pillow 			block bores and tooling holes to lower web section for nicks, 			scratches tool marks, and cracks.

3.	Inspect to insure no sealant voids are evident around shields.

NOTE

Re-coat with bead of sealing compound as required.

Coat the remaining exposed fillet radii and repaired

surfaces with a film of corrosion prevention compound.

f.	Inspect tail boom attachment fittings by:

1.	Opening access panel on the right side of the aft fuselage and 			inspect the four tail boom attachment fittings on fuselage aft 			bulkhead and tail boom forward bulkhead for cracks.

NOTE

Give special attention to the tail boom attach fittings and

bolts and to the fasteners between the fittings and intercostals.

Particular attention must be given to inspection of the upper left fittings.

CAUTION

Any cracks, corrosion, loose or sheared

rivets, is cause for immediate corrective maintenance.

g.	Check engine air intake ducts and plenum for obstructions or damage.  		Check air induction fairing for seal security, conditions, and bond 		voids along the seals complete length.  Check sand and dust separator 		for damage and particle ejection opening for freedom of obstruction.

h.		Check voltage regulator for proper operation.

i.	Inspect tail rotor for proper dynamic balance.

6-26.	AT FIRST 100 HOUR INSPECTION FOLLOWING MAST NUT INSTALLATION

a.	Re-torque mast nut (refer to applicable TM).

6-27.	AT FIRST 100 HOURS AFTER INSTALLATION OF TAIL BOOM

a.	Verify torque of tail boom attachment bolts (refer to applicable TM).

6-28.	EVERY 100 HOURS OR 120 CALENDAR DAYS WHICHEVER OCCURS FIRST.

a.	Perform preventive battery maintenance checks and services on the 		nickel-cadmium battery (refer to battery maintenance and instruction 		manual or TM).  After battery removal, check area around battery for 		cleanliness, corrosion, paint and condition.

b.	Remove transmission oil cooler duct and inspect radiator for foreign 		objects blocking air flow.

6-29.	100 HOURS AFTER INSTALLATION OF PILLOW BLOCK RETENTION BOLTS AND NUTS OR 	INSTALLATION OF A NEW OR OVERHAULED MAIN ROTOR HUB ASSEMBLY.

a.	Verify torque of pillow block retention bolts and nuts (refer to

applicable TM).

NOTE

Paint a slippage mark across bolt heads to pillow block

surfaces and across nuts to yoke surfaces including washers.

6-30.	100 HOURS AFTER SERVO ACTUATOR INSTALLATION

a.	Verify torque of trunnion plate nuts.

b.	Verify torque of bearing plate nuts.

NOTE

Refer to applicable TM for proper torque.

6-31.	100 HOURS OF OPERATION AFTER THE TAIL ROTOR GEARBOX HAS BEEN INSTALLED OR 	HARDWARE ADJUSTED

a.	Verify torque of the tail rotor gearbox retaining hardware (refer to 		applicable TM).

6-32.	EVERY 150 HOURS OR 6 CALENDAR MONTHS WHICHEVER OCCURS FIRST

a.	Remove, disassemble, clean, inspect, reassemble and lubricate engine 		to transmission main input driveshaft assembly.

NOTE

This inspection does not apply to P/N 206-040-3171-111.

6-33.	EVERY 150 HOURS

a.	Inspect tail rotor gearbox chip detector for metal particles and 			contamination.  Change tail rotor gearbox oil.

6-34.	EVERY 300 HOURS OR WHEN RED BUTTON (IMPENDING BYPASS INDICATOR) ON 	TRANSMISSION OIL FILTER IS SHOWING

a.	Replace transmission oil filter and reset impending by-pass 			indicator.

b.	Inspect transmission oil for contamination and metal particles.

NOTE

Cut filter open (do not saw) to inspect pleated element.

c.	Inspect transmission oil sump screen and chip detectors for 			contamination and metal particles.  Change transmission oil.

6-35.	EVERY 500 HOURS OR EVERY 12 CALENDAR MONTHS

Refer to Allison publication 5W2 or 10W2 for all inspection requirements and recommended maintenance procedures regarding engine operations.

6-36.	EVERY 600 HOURS

Refer to Allison publication 5W2 or 10W2 for all inspection requirements and recommended maintenance procedures regarding engine operations.

6-37.	AFTER 600 HOURS AND 900 HOURS OF OPERATION OF NEW RETENTION STRAP

a.	Retention straps inspection (refer to applicable TM).

6-38.	EVERY 1000 HOURS

Refer to Allison publication 5W2 or 10W2 for all inspection requirements and recommended maintenance procedures regarding engine operations.

6-39.	EVERY 1200 HOURS

NOTE

For the following inspection refer to the applicable TM.

a.	Check the tail rotor gearbox attaching hardware for proper torque 		(refer to applicable TM).

b.	Remove transmission isolation mount and inspect absorber plate for 		cracks and wear.  Inspect metal parts for, dents, notches, or other 		damage.  Inspect rubber parts for separation and cracks.

c.	Inspect the main rotor control components listed below for damage, 		wear, and cracks.

1.	Inspect spherical bearings in these parts for damage and 				looseness.

2.	Inspect Teflon lined bearings in these parts for loose fabric, 		damaged Teflon, and for exposed fiberglass base.

3.	Inspect metal bushings in these parts for damage and looseness.

Name					Part Number

Swashplate Idler Lever		206-010-335-1

Idler link				206-010-336-5

Main rotor pitch link		206-010-360-3

assemblies

Collective lever link		206-010-407-1

assembly

Collective lever assembly	206-010-467-1

Collar set				206-011-005-1

6-40.	EVERY 100 HOURS AFTER THE 1200 HOUR INSPECTION OF SWASHPLATE DUPLEX BALL 	BEARING UNTIL THE 2400 HOUR OVERHAUL OF THE SWASHPLATE.

a.	Disconnect main rotor pitch links and the idler link.  Inspect 			swashplate duplex ball bearing for roughness by rotating swashplate 		outer ring.

6-41.	AFTER 1200 HOURS OPERATION OF NEW OR OVERHAULED MAIN ROTOR HUB ASSEMBLY.

a.	Inspect main rotor grips per following:

1.	Remove grips from hub and inspect for wear and corrosion in 			excess of limits.

2.	Clean paint from grips and pitch horns with paint remover, 				MIL-R-46116.

3.	Prepare grips and pitch horns for inspection by procedures 				outlined by fluorescent penetrant manufacturer.

4.	Inspect pitch horns and grips for cracks.

5.	After inspection is complete, assemble main rotor hub.

6.	Paint main rotor hub as follows:

(a)	Touch up all exposed steel surfaces with brush cadmium 				plate LHE Solution, MIL-STD-865.

(b)	Touch up all exposed aluminum surfaces with chemical 					conversion coating (Alodine), MIL-C-81706.

(c)	Paint main rotor hub.

6-42.	AFTER 1200 HOURS OPERATION OF NEW OR OVERHAULED MAIN TRANSMISSION

a.	Inspect transmission as follows:

WARNING

The inspection of this transmission must be

accomplished by an appropriately certificated and qualified person.

1.	Inspect top case for cracks.  Use fluorescent penetrant method.  			It is not necessary to strip paint from the top case.  Do not 			use dye-check method to make this inspection.  Check ring gear 			carefully around area of roots of splines.  If any cracks are 			detected, reject the top case.

2.	Inspect splines in top case for wear.  Place O.1200 inch 				diameter pins in splines and measure distance between pins.  If 			dimension is greater than 11.8840 inches, reject the top case.

3.	Inspect planetary sun gear as follows:

(a)	Visually inspect for general condition.

(b)	Place two 0.1600 inch diameter pins, not longer than 					0.250 inch in splines.  Measure dimension over the pins 				in area of greatest wear.  If dimension over pins is 					2.7290 inches or greater, inspect sun gear and planetary 				gear teeth for evidence of interference.  If gears are 				satisfactory, the sun gear may be reinstalled.

(c)	If dimensions over pins is less than 2.7290 inches, 					reject the sun gear.

4.	Inspect planetary bearings and gear assemblies as follows:

(a)	Visually inspect gears for chipped, broken and worn 					teeth.

(b)	Check bearing surfaces of rollers, inner race and outer 				race for chips, cracks, nicks, brinnelling, spalling and 				corrosion.

6-43.	AFTER 1200 HOURS OPERATION OF NEW OR OVERHAULED MAIN TRANSMISSION MAST 	ASSEMBLY

a.	Inspect as follows:

1.	Mast splines for burrs, nicks, cracks and wear.

2.	Mast inner and outer surfaces for corrosion.  Inspect surface 			protective coatings for condition.

3.	Bearing for pits, erosion, spalling and brinelling.

6-44.	AFTER 1500 HOURS OPERATION OF NEW OR OVERHAULED FREEWHEELING ASSEMBLY.

a.	Inspect shafts, bearing and clutch P/N CL 41742-1 or CL 42250-1 			visually for wear and damage.

b.	Conduct magnetic particle inspection of shafts in accordance with the 		applicable TM.

6-45.	EVERY 1500 HOURS

Refer to Allison publication 5W2 or 10W2 for all inspection requirements and recommended maintenance procedures regarding engine operations.

6-46.	EVERY 12 CALENDAR MONTHS

a.	Inspect portable fire extinguisher in accordance with the 				manufacturer’s instructions and check for hydro static test date and 		life limit.

b.	First Aid kit inspection in accordance with the manufacturer’s 			instructions.

c.	Calibrate (swing) magnetic (standby) compass in accordance with 			applicable TM.

d.	Check current magnetic compass and gyro-compass correction cards for 		availability and legibility.

6-47.	EVERY 12 CALENDAR MONTHS: OR WHENEVER HELICOPTER IS TRANSFERRED, RECEIVED, 	PLACED IN STORAGE, OR REMOVED FROM STORAGE.

a.	Every 14 Days									  |

- If the idle time of the helicopter has been for a period of   |

14 days following the last flight, it is required that a      |

ground run of 5 to 10 minutes be performed (attainment of the |	operating temperature). 						  |

2.	If a ground run is not possible every 14 days the helicopter  | and especially the engine should be preserved in accordance   | with the current military document.  Engine preservation requirements and instructions are in Allison publication 5W2 or 10W2.

6-48.	EVERY 24 CALENDAR MONTHS

a.	Perform test on pitot static system in accordance with applicable Federal Aviation Regulations and TM.

b.	Inspect fuel tank for condition, contamination.

c.	Check fuel quantity indicator for accuracy.

6-49.	AFTER 1550 HOURS OPERATION OF NEW OR OVERHAULED ENGINE WITH PRODUCT 	IMPROVED TURBINE FOR T63-A-700 AND AFTER 1775 HOURS OR 3000 CYCLES 	OPERATION OF NEW OR OVERHAULED ENGINE WITH PRODUCT IMPROVED TURBINE FOR 	T63-720.

a.	Refer to Allison publication 5W2 or 10W2 for engine component P/N 		applicability, retirement life schedule, and special notes regarding 		differing turbine module operating configurations.

6-50.	EVERY 1750 HOURS

Refer to Allison publication 5W2 or 10W2 for all inspection requirements and recommended maintenance procedures regarding engine operations.

6-51.	AFTER 2400 HOURS OF OPERATION OF NEW OR OVERHAULED MAIN TRANSMISSION

a.	Overhaul and inspect main transmission per DMWR 55-1615-157.

6-52.	AFTER 2400 HOURS OF OPERATION OF NEW OR OVERHAULED MAIN TRANSMISSION MAST 	ASSEMBLY

a.	Inspect mast assembly per applicable TM.

6-53.	AFTER 2400 HOURS OF OPERATION OF NEW OR OVERHAULED TAIL ROTOR GEARBOX 	ASSEMBLY

a.	Overhaul and inspect tail rotor gearbox assembly per DMWR 55-1615-159 		or DMWR 55-1615-298.

6-54.	AFTER 3000 HOURS OF OPERATION OF NEW OR OVERHAULED FREEWHEELING ASSEMBLY

a.	Overhaul and inspect freewheeling assembly per DMWR 55-1615-161.

Chapter 7

Conditional Inspections

_________________________________________________________________________________

Inspections which are contingent upon specific conditions or incidents that arise, and only because of these conditions or incidents.  Examples of these conditions or incidents are hard landings, overspeed, and sudden stoppage.  An immediate inspection is required in such cases to ensure safe flight.  Refer to the applicable military aircraft operations manual, aircraft technical manual, and DMWR’s for limitations and inspection criteria.

Conditional Inspections Index (Airframe)						Page

7-1.	AFTER A HARD LANDING	.	.	.	.	.	.	.	51

7-2.	AFTER LOWER WSPS GROUND CONTACT	.	.	.	.	.	54

7-3.	AFTER WIRE STRIKE	.	.	.	.	.	.	.	.	55

7-4.	AFTER PYLON WHIRL	.	.	.	.	.	.	.	.	55

7-5.	AFTER SPIKE KNOCK	.	.	.	.	.	.	.	.	56

7-6.	AFTER SUDDEN STOPPAGE-MAIN ROTOR	.	.	.	.	.	56

7-7.	AFTER SUDDEN STOPPAGE-TAIL ROTOR	.	.	.	.	.	58

7-8.	AFTER MAIN ROTOR OVERSPEED	.	.	.	.	.	.	59

7-9.	AFTER AIRFRAME OVERTORQUE OPERATION	.	.	.	.	.	60

7-10.	ANY TIME FUEL FILTER LIGHT COMES ON	.	.	.	.	.	61

7-11.	ANY TIME TRANSMISSION OR TAIL ROTOR MAGNETIC

CHIP LIGHT COMES ON	.	.	.	.	.	.	.	61

7-12.	LIGHTING STRIKE	.	.	.	.	.	.	.	.	62

Conditional Inspections Index (Engine)

7-13.	SUSPECTED FOREIGN OBJECT DAMAGE	.	.	.	.	.	63

7-14.	AFTER ENGINE OVERTEMPERATURE OPERATION	.	.	.	.	64

7-15.	AFTER ENGINE OVERSPEED OPERATION	.	.	.	.	.	64

7-16.	ANY TIME ENGINE MAGNETIC CHIP LIGHT COMES ON	.	.	.	64

7-17.	IF ENGINE OIL TEMPERATURE EXCEEDS 107 DEGREES

CELSIUS WITH A CHANGE IN NORMAL OIL PRESSURE	.	.	.	64

7-18.	EMERGENCY FUEL USAGE	.	.	.	.	.	.	.	64

Conditional Inspections

_________________________________________________________________________________

7-1.	AFTER A HARD LANDING

Definition:	Hard landing is defined as any accident or incident in which ground impact of the helicopter causes severe pitching of main rotor, allowing hard contact of hub with mast, or results in yielding or noticeable cracking of fuselage pylon support structure or landing gear.  This definition is confined only to those accidents not involving sudden stoppage of main rotor or tail rotor.  When a probable hard landing incident has occurred, proceed as follows:

Refer to Allison publication 5W2 or 10W2 for instruction regarding the necessary actions required for engine inspection.

a.	Check all cowling and doors for proper fit and alignment.  Mis-			aligned cowling may indicate a distorted fuselage, resulting in major 		stresses and damage.  Remove center post cover assembly and inspect 		cap angles for buckling and bending.

b.	Remove all cowling as necessary to perform a complete visual 			inspection.

c.	Inspect landing gear skid tubes and crosstubes for damage and 			deflection.  Inspect crosstube attachment points for damage or 			distortion.

d.	Inspect structure with a ten-power magnifying glass around the 			transmission mounting points.  Particular attention should be given 		to the isolation mount and pylon support mounts.

e.	Inspect upper longerons and adjacent skin near the aft engine 			firewall (Station 167.00) for loose rivets, cracks, distortion and 		structural damage.

f.	Inspect tail skid tube and mounting for damage.  Inspect tail boom 		internally and externally for cracks, distortion, and loose rivets.  		Inspect the tail boom attachment points for elongated bolts and 			damaged structure.  Inspect external skin of tail boom for cracks in 		area of attachment of the horizontal stabilizer.

g.	Inspect flight control system from pilot’s controls to rotor head for 		bent or damaged tubes, bellcranks, and supports, and for damaged 			bearings.  Particular attention should be given to the mast control 		rods and collective sleeve assembly.

h.	Check for leaks in the hydraulic system and interference or binding, 		and for satisfactory operation.

i.	Inspect transmission and mast assembly for the following:

1.	Mast for indentation caused by hard contact with static stops.

2.	Mast outside diameter for out-of-round condition as follows:

NOTE

Cadmium plating on the outside diameter (O.D.) of mast

is 0.0003 to 0.0004 inch.  When measuring mast O.D. at six places

for out-of-round, ensure that 0.0003 to 0.0004 inch surface differential is considered when measuring plated surfaces or where plating may have been removed.

(a)	Using a suitable micrometer, measure the mast O.D., at a 				minimum of six places for out-of-round condition; two 				opposing measurements under the collar set and above the 				swashplate, two opposing measurements midway between the 				collar set and the static stop contact area, two opposing 				measurements approximately two inches below the static 				stop contact area on the mast.

(b)	If any set of opposing measurements vary in excess of 				0.002 inch, the mast is suspected of bending and a run-				out check must be performed.

3.	Structure supporting the transmission mount points for cracks 			or deformation.

4.	Transmission drag pin for security of attachment.  Replace 				adapter mount studs as required.

5.	Transmission-drag pin-transmission mount support on cabin 				roof for deformation and/or loss of attachment bolt torque.  			Supporting structure for damage and loose or sheared rivets.

(a)	The transmission to engine coupling will be removed and a 				detailed inspection performed.

(b)	The transmission assembly will be removed and returned to 				authorized overhaul or repair facility for evaluation.

j.	If no major damage is found in the inspections listed above, start 		engine and check main rotor (while in a flat pitch condition) for any 		evidence of a 1/rev. vibration.

k.	Inspect main rotor blades for contact with tail boom.

NOTE

If damage is found, refer to 7-6 AFTER SUDDEN STOPPAGE - MAIN ROTOR.

l.	Inspect tail rotor blades for damage.

NOTE

If damage is found, refer to 7-7 AFTER SUDDEN STOPPAGE - TAIL ROTOR.

m.	Inspect fuel and oil systems for damage.  Before flight, check fuel 		and oil systems for leaks.  Inspect the crashworthy fuel system for 		the following:

1.	Sump retainer and surrounding airframe for cracks and/or 				distortion.

2.	Sump area for leaks.

3.	Sump drain valve for proper operation.

4.	Fuel boost pump wiring for broken leads.

5.	Retainer at filler cap and adapter for cracks and/or sheared 			rivets.

6.	Relation of fuel cell fitting with airframe fuel opening.

7.	Fuel feed hose for clamping security inside fuel cell.

8.	Cover assembly to ensure no pullout has occurred at screws 				attaching cover assembly to seat back panel.

9.	Fuel feed valve at top right side of fuel tank for cracks.

10.	Boost pump pressure available to engine and that no leakage 			occurs.

11.	Manual shutoff valve for binding.

12.	Fuel quantity indicator for proper operation and probe leads or 			broken wires.

13.	All hoses for chafing and broken or distorted clamps.

n.	Inspect engine mounts and fuselage attachment points for cracks and 		damage.

o.	Check power and accessory gearbox for cracked flanges.

p.	Inspect magnetic chip detectors for metal accumulation.

q.	Check engine mounting pads for cracks.

r.	Check air, oil and fuel hose connections for tightness.

s.	Check all engine accessories for cracked flanges, loose bolts and 		nuts, connections and general condition.

t.	After a hard landing:	If damage or misalignment to fuselage 			structure, skid gear, or tail boom is such that a major repair, 			replacement or alignment is necessary, remove the following 			components and conduct a major overhaul inspection in accordance with 		instructions in the appropriate TM:

1.	Main rotor blades and attachments.

2.	Main rotor hub.

3.	Swashplate and controls.

4.	All control bolts.

5.	Transmission and mast assembly.

6.	Transmission to engine coupling assembly.

7.	Tail rotor shafts and bearings.

8.	Tail rotor gearbox.

9.	Tail rotor hub and blades.

10.	Isolation mount.

11.	Freewheeling assembly.

u.	If misalignment is indicated as a result of excessively hard contact 		of main rotor hub static stop against mast, remove the following 			components and conduct a major overhaul inspection in accordance with 		instructions in the appropriate TM.

1.	Main rotor blades and attachments.

2.	Main rotor hub.

3.	Transmission and mast assembly.

4.	Transmission-to-engine coupling assembly.

5.	Isolation mount.

6.	Freewheeling assembly.

v.	If damage is found in rotating controls, accomplish the following 		steps:

1.	Replace all control rods and bolts.

2.	Remove and overhaul the following components.

(a)	Main rotor hub assembly.

(b)	Swashplate and controls.

7-2.	AFTER LOWER WSPS GROUND CONTACT

NOTE

Loss of breakaway tip or damage not affecting structural integrity

of installation are not causes for grounding of aircraft.  However,

replacement of tip damage repair shall be accomplished as soon as practical.

a.	Inspect lower WSPS for obvious damage.

b.	Inspect attachment area for damage.

c.	Remove panel and inspect structure and directional control tubes and 		bellcranks for damage.

7-3.	AFTER WIRE STRIKE

a.	Windshield deflector-upper and lower WSPS.

1.	Inspect for obvious damage.

2.	Inspect attachment areas for damage.

7-4.	AFTER PYLON WHIRL

Definition:	A combination of very low rotor speeds and high collective blade angles which results in excessive flapping of the main rotor hub, which in turn causes bumping and rotation of the pylon in an elliptical pattern.  Pylon Whirl will usually include spike knocking and swashplate to cowling contact.

NOTE

Oil canning and some wrinkling occurring aft of the

avionics compartment door below WL 61.76 is normal on the helicopter.

a.	Inspect tail boom in the area aft of the tail boom attach point to 		the elevator.  Check for bending, buckling or creasing, especially on 		the top and bottom of the tail boom.

b.	Inspect fiberglass fairing under the tail boom assembly on the aft 		section assembly for cracking.

c.	Inspect aft section assembly of the helicopter forward of the tail 		boom attach point for approximately 36 inches both sides of aircraft.  		Check for skin wrinkling above WL 61.76 which is characterized by 		permanent creasing and abrupt changes in profile.

NOTE

If the fiberglass fairing has been cracked, or if the aft

section assembly skin is wrinkled above WL 61.76, the longerons

and stiffeners must also be inspected for bending, cracking or tearing.

d.	Inspect transmission cowling for swashplate to cowling contact.  			Check for loose jam nuts on swashplate control tubes.

e.	Inspect transmission drag pin assembly and its static stop for 			permanent deformation and security of attachment.

NOTE

If the preceding inspections reveal no damage as a result of

pylon whirl, or suspected pylon whirl, the helicopter may be released

for flight.  Otherwise, a complete hard landing inspection is required.

7-5.	AFTER SPIKE KNOCK

a.	If spike knocking occurred as a result of ground impact, or sudden 		stoppage of the helicopter in sand or mud, the 7-1 AFTER A HARD 			LANDING inspection is required.

b.	If spike knocking occurred during flight, but did not involve rotor 		RPM’s below 330 RPM and high collective blade angles, only the 			transmission adapter mount (drag link) and isolation mount must be 		inspected.  If spike knocking was accompanied by severe vibrations 		(shuddering), the 7-4 AFTER PYLON WHIRL inspection is applicable.

c.	If spike knocking occurred during ground run-up, but was induced by 		lateral movement to the cyclic, rather than full up collective and 		rotor speed below 225 RPM only the transmission adapter mount (drag 		link) and isolation mount must be inspected.

WARNING

If swashplate to cowling or main driveshaft to

isolation mount contact occurs, the following inspections

must be complied with: 7-1 HARD LANDING INSPECTION, 7-4 PYLON WHIRL

INSPECTION to include special inspection of main driveshaft assembly.

The drag pin assembly must be removed from transmission assembly for a

detailed inspection.  The four drag pin assembly mounting studs will be replaced.

d.	If spike knocking occurred during ground run up with full up 			collective and rotor speed below 225 RPM, the 7-4 AFTER PYLON WHIRL 		will be accomplished.

7-6.	AFTER SUDDEN STOPPAGE-MAIN ROTOR

Definition: Sudden stoppage is defined as an abnormal deceleration of the drive system caused by internal seizure of the transmission or by the main rotor or tail rotor blades striking something which causes rapid deceleration.

Refer to Allison publication 5W2 or 10W2 for instruction regarding Engine Sudden Stoppage and the necessary actions required.

a.	If visible damage to either one or both of the blades (other than tip 		cap fairing damage) is evident, remove the following components for 		major overhaul inspections:

1.	Main rotor blades and attachments.

2.	Main rotor hub.

3.	Mast.

4.	Swashplate and controls.

5.	Transmission.

6.	Freewheeling unit.

7.	Main driveshaft.

b.	After Sudden Stoppage with no visible damage.  Inspect the exterior 		of blades for security of all bonds and visible damage.  Remove tip 		cover plate.

NOTE

If tip weight has moved, blade shall be disposed of as unsalvageable.

c.	Engine and transmission mounts at fuselage attachment points for 			cracks.

d.	After sudden stoppage with minor damage to main rotor, inspect the 		following components.  If any damage is found proceed to category of 		major damage.

1.	Main rotor hub pillow block bearings and grip bearings for 				freedom and security.

2.	Flight control system from the rotor to hydraulic boost 				cylinder for bent or damaged tubes.  Bell cranks and supports 			for damaged bearings.

3.	Swashplate idler links and lever for damage.

4.	Swashplate pivot for damage.

5.	Structure at transmission mounting points for cracks (use ten 			power magnifying glass).

6.	Isolation mount and pylon supports for damage, security, and 			distortion.

e.	If main rotor has major damage, inspect the following components:

1.	Flight control system from the rotor to hydraulic boost 				cylinder for bent or damaged tubes.  Bell cranks and supports 			for damaged bearings.

2.	Swashplate idler links and lever for damage.

3.	Swashplate pivot for damage.

4.	Isolation mount and pylon support for damage, security and 				distortion.

5.	Tail rotor driveshaft adapters and disk assemblies for cracks 			using magnetic particle process.

6.	Tail rotor driveshafts for concentricity and cracks.  Dye     | penetrate/NDI is required. 						  |

f.	If more than minor damage is found on any component, remove and 			perform a major overhaul inspection in accordance with instructions 		in the applicable TM.

7-7.	AFTER SUDDEN STOPPAGE-TAIL ROTOR

Refer to Allison publication 5W2 or 10W2 for instruction regarding the necessary actions required.

a.	Remove and replace tail rotor hub and blade assembly.

b.	Inspect the following tail rotor driveshaft system components for 		damage.

1.	Flexible couplings, driveshaft, and adapters for cracks, use 			magnaflux or zyglo method.

2.	All components dimensionally in accordance with applicable TM.

3.	Bonds between tail rotor driveshaft and adapters for failure.

CAUTION

This requirement also applies to tail rotor blades which

may have contacted water during float operation.  Damage to the hub

and blade could be present although it may not be readily detected by

standard visual, dimensional, magnaflux or zyglo methods of inspection.

4.	Driveshaft support hangers for cracks and distortion.

c.	If tail rotor driveshaft is damaged, remove the following components 		and perform a major overhaul in accordance with instructions in the 		overhaul sections of the applicable TM:

1.	Tail rotor gearbox.

2.	Freewheeling unit.

3.	Replace all tail rotor driveshaft hangers.

d.	Inspect tail boom in the area of the tail rotor gearbox mounting 			studs, using a ten-power magnifying glass.

e.	Inspect four tail boom attachment points for cracks, distortion, 			damage and security.  Check torque on nuts of attachment bolts 			(refer to applicable TM).

f.	Inspect tail boom internally for cracks, distortion and loose or 			missing rivets.  Check external skin of tail boom for cracks in area 		of the attachment of the horizontal stabilizer.

g.	Inspect horizontal stabilizer for skin cracks and looseness in 			mounting.

h.	Inspect vertical fin for security and overall condition.  Check the 		tail skid for condition and security.  Check anti-collision light for 		condition and security.

NOTE

Known or suspected contact of tail rotor blades

with loose earth, snow, water, or vegetation does not

require removal and replacement of the tail rotor gearbox unless

inspection as required by this section, d. through h. (above), reveals

an obvious defect, and provided the hub assembly can be dynamically balanced.

CAUTION

Sudden stoppage may result in a tail rotor out of balance condition

which could be detrimental to the structure.   Perform the following:

i.	If sudden stoppage originated at the main rotor, the tail rotor hub 		and blade assembly may remain in service providing no visual external 		damage is noted.

NOTE

Obvious damage noted to the tail rotor hub and blade

assembly is cause for detailed inspection and/or repair.

j.	If sudden stoppage originated at the main transmission, the 			transmission, input driveshaft and freewheeling assembly will be 			removed and subjected to a major overhaul.  If sudden stoppage 			originated at the tail rotor gearbox, the tail rotor gearbox and tail 		rotor driveshafts will be removed and subjected to a major overhaul.  		Tail rotor hub and blade will be inspected for damage.

7-8.	AFTER MAIN ROTOR OVERSPEED

If main rotor overspeeds in excess of 390 RPM, 110%, perform the following inspections:

Refer to Allison publication 5W2 or 10W2 for instruction regarding the necessary actions required.

a.	Main rotor blades.  Inspect for the following:

- Main retention bolt hole for elongation or deformation.

NOTE

Elongation in excess of 0.0015 inches is cause to replace blade.

2.	Main retention bolt bushings for looseness.  Replace blade if 			bushing is loose.

3.	Tip cap screws and matching holes.  Replace blade if screws or 			holes are deformed.

4.	Blade skin for wrinkles or deformation.  Replace blade if skin 			is deformed or wrinkled.

5.	Inertia weight retaining screws for damage or looseness.  				Replace blade if screws or holes are deformed.

6.	Replace grip retention strap assemblies.

7.	Replace inboard strap fittings and pins.

8.	Replace outboard strap latch bolts.

b.	Tail rotor blades.  Inspect for the following:

1.	If one of the blades of a pair has been damaged badly enough 			that metal has been torn or any bond lines have separated, the 			hub and blade assembly should be disposed of as unsalvageable.

2.	If one of the blades contour has been damaged slightly, the hub 			and blade assembly should be disposed of as unsalvageable.

3.	If any movement of the tip end or root end balance weights has 			occurred, the hub and blade assembly should be disposed of as 			unsalvageable.

4.	If the tip block is cracked, the hub and blade assembly should 			be disposed of as unsalvageable.

c.	Inspect tail rotor driveshaft bearing hanger brackets for security of 		attachment and for cracks or bends.

d.	Inspect oil cooler blower fan for visible distortion or cracks of the 		brazed vane joints.

e.	Conduct a major overhaul inspection of main and tail rotor hub 			assemblies.  Refer to DMWR 55-1615-158 for the Main Rotor Hub 			Assembly, and DMWR 55-1615-162 for the Tail Rotor Hub Assembly.

7-9.	AFTER AIRFRAME OVERTORQUE OPERATION

a.	Refer to the appropriate military operating manual for the definition 		of overtorque condition applicable to the make and model.

b.	If engine overtorque occurs, perform a P.M.I.  Conduct an inspection 		of the following components for evidence of damage, deformation, 			yielding, etc:

1.	Main rotor hub.

2.	Main rotor mast.

3.	Transmission top case.

4.	Pylon mount arm attachment fittings, upper and lower.

5.	Cabin roof at pylon mount fittings.

6.	Isolation mount attachment.

7.	Transmission chip detectors.

8.	Main driveshaft couplings for overheating.  If main rotor 				driveshaft 206-040-371 is used, check for damage and fastener 			security.

9.	Tail rotor hub and attachments.

10.	For engine overtorque inspection requirement refer to Allison 			publication 5W2 or 10W2 for instruction regarding the necessary 			actions required.

c.	After 25 flight hours following overtorque, inspect the following:

1.	Main rotor hub.

2.	Main rotor mast.

3.	Transmission top case.

4.	Pylon mount arm attachment fittings, upper and lower.

5.	Cabin roof at pylon mount fittings.

6.	Isolation mount attachment.

7.	Transmission chip detector.

8.	Tail rotor hub, blades, and attachments.

7-10.	ANY TIME FUEL FILTER LIGHT COMES ON

a.	Refer to Allison publication 5W2 or 10W2 for instruction regarding 		the necessary actions required.

b.	Inspect air frame fuel system.

7-11.	ANY TIME TRANSMISSION OR TAIL ROTOR MAGNETIC CHIP LIGHT COMES ON

a.	Remove chip detector leads (one at a time), to determine which 			magnetic plug caused the light.

b.	Remove and inspect the applicable magnetic plug for metal 				accumulation, determine if accumulation is acceptable.

c.	Clean or replace oil and/or filter of component if acceptable.

d.	Remove component for inspection or overhaul if accumulated material 		is considered unacceptable

7-12.	LIGHTNING STRIKE INSPECTION

a.	General requirements when helicopter is struck by lightning:

1.	Inspect fuselage interior and exterior, landing gear, rotor 			system, and static ground wire for burn marks, cracks, pitting, 			or signs of high temperature stress; to determine lightning 			entry and exit points.

2.	Trace path of lightning strike to extent possible using a 				magnetometer.

3.	Check magnetic compass for accuracy (degree of inaccuracy may 			serve as an indicator of severity of strike).

4.	Inspect wiring in tunnel areas and exposed areas for burns.

5.	Inspect antennas for burns and pitting.

6.	Inspect all electrically operated components and lighting 				systems for damage.

7.	Inspect communications and navigation equipment for damage.

8.	If the preceeding steps 1 through 7 (above) reveal major damage 			has occured, proceed as follows:

9.	Bench test all avionics and electrical systems and components.

10.	Perform a continuity check on all wiring cables.

11.	Perform a Voltage Standing Wave Ration (VSWR) check on all 				antennas, antenna cables, and connectors.

12.	Perform specific inspection/replacements as required.

13.	Perform a ground run operational check on the aircraft.  				Functionally check the flight control system, and all avionics, 			electrical, lighting, communication, and navigation systems.

14.	Repair any damage and replace damaged components as required 			using standard maintenance pratices.

b.	Specific requirements whenever lightning strike is evident on main 		rotor system:

1.	Inspect blades for damage such as burns, pitting, skin 				seperation, etc.  If damage is evident, dispose of as 				unsalvageable.

2.	Remove hub assembly and return for overhaul.

3.	Replace all bearings (or next higher assembly if required) in 			the fixed and rotating control system located above the servo-			cylinders.

4.	Remove swashplate assembly, mast assembly and transmission 				assembly, and return for overhaul.

5.	Check driveshafts for residual magnetism.  If magnetized or 			damaged replace driveshafts and remove engine and return for 			overhaul.

c.	Specific requirements when lightning strike is evident on tail rotor 		system:

1.	Inspect blades for damage such as burns, pitting, skin 				seperation, etc.  If damage is evident, dispose of as 				unsalvageable.

2.	Tail rotor hub, dispose of as unsalvageable.

3.	Remove and condem pitch change links, and crosshead bearings.

4.	Inspect crosshead and control rod for any indications of aging.  			Replace if necessary.

5.	Remove 90 degree gearbox and return for overhaul.

6.	Replace any magnetized tail rotor driveshaft hanger bearings.

7.	Check disc assembly, blower assembly, splined adapter, 				freewheeling assembly, main driveshaft and tail rotor 				driveshaft couplings for residual magnetism.  Replace as 				necessary.

8.	Inspect oil cooler and oil cooler filter assembly for damage.  			Replace as necessary.

9.	If previous drive train items show magnetism, remove 					transmission and return for overhaul.

10.	If freewheeling assembly shows magnetism remove engine assembly 			and return for overhaul.

11.	Inspect engine mounts, support installation, pylon, and mount 			installation, isolation pylon for damage.  Replace if 				necessary.

Conditional Inspections (Engine)

All Conditional Inspections (Engine) are to be performed in accordance with the Allison publication 5W2 or 10W2.  Refer to these publications for instruction regarding the necessary actions required.

7-13.	SUSPECTED FOREIGN OBJECT DAMAGE

a.	Refer to Allison publication 5W2 or 10W2 for instruction regarding 		foreign object damage inspection.

7-14.	AFTER ENGINE OVERTEMPERATURE OPERATION

a.	Refer to Allison publication 5W2 or 10W2 for instruction regarding 		overtemperature operation inspection.

7-15.	AFTER ENGINE OVERSPEED OPERATION

a.	Refer to Allison publication 5W2 or 10W2 for instruction regarding 		overspeed limits and maintenance actions.

b.	Inspect transmission for obvious damage.

7-16.	ANY TIME ENGINE MAGNETIC CHIP LIGHT COMES ON

a.	Refer to Allison publication 5W2 or 10W2 for instruction regarding 		the necessary actions required.

7-17.	IF ENGINE OIL TEMPERATURE EXCEEDS 107 DEGREES C WITH A CHANGE IN NORMAL OIL 	PRESSURE

a.	Refer to Allison publication 5W2 or 10W2 for instruction regarding 		the necessary actions required.

7-18.	AFTER EMERGENCY FUEL USAGE

a.	Emergency fuel usage is limited to an accumulation of 6 hours per 		overhaul period.  Refer to Allison publication 5W2 or 10W2 for

instruction regarding the necessary actions required.

APPENDIX

_________________________________________________________________________________

Letter from Bell Textron

Ref:  Overhaul and Retirement Schedule, Manuals, and Technical assistance.

Bell Helicopter						                Post Office Box 482

A Textron Company 				                              Fort Worth, Texas 76101

Dear Bell Helicopter Excess/Surplus Aircraft Operators:

Bell Helicopter is aware of several situations in which many operators need technical assistance in maintaining their OH-58A/C Helicopters.  When the helicopters are surplused by the Defense Logistics Agency (DLA), many operators do not receive the appropriate Technical Manuals to maintain their helicopters.

The military Technical Manuals (TM's) required to maintain the OH-58A/C are:

TM 55-1520-228-23P 	PARTS MANUAL

TM 55-1520-228-10 	OPERATORS MANUAL

TM 55-1520-228-23-1/-2 	MAINTENANCE MANUAL

TM 55-1520-228-CL 	CHECKLIST, OPERATOR

TM 55-1520-228-PMD 	PREVENTIVE MAINTENANCE DAILY

TM 55-1520-228-PM 	PHASE MAINTENANCE

These are not Bell Helicopter manuals, Bell Helicopter doesn't maintain, update or distribute these manuals. These manuals are available for purchase at:

NTIS- National Technical Information Service

Military Publications Department

5285 Port Royal Road

Springfield, V A 22161

PHONE: 	703-605-6000

800-553-6847

FAX: 	703-605-6900

Email ORDERS@NTIS.GOV

In order to assist operators operating in the Public Use, Bell Helicopter has developed and recommends the Overhaul and Retirement Schedule. Unfortunately Bell Helicopter cannot assist operators in Type Certified Restricted Category. These operators are obligated to maintain their aircraft in accordance with the Type Certificate Holder requirements.

The rationale behind Bell Helicopter developing this recommended Overhaul and Retirement Schedule is to remove the Gearboxes out of a "On-Condition": Airworthy Limitation. In compliance with the TM's an operator is required to take an oil analysis every 25 hours and submit for a lab analysis. Bell Helicopter is aware that all operators are not performing this maintenance task and therefore Bell Helicopter has developed a recommend Overhaul/Retirement schedule, it's only provided to assist Public Use operators.

Regards

/Andrew L. Kelley/

Product Support Engineer

4/18/2002

OH-58A/C Retirement/Overhaul Schedule						4/18/2002

OVERHAUL 	RETIREMENT 	ITEM 	PART NUMBER

INTERVAL 	INTERVAL

(HOURS)	(HOURS)

24 Months 	PILOT AND CO-PILOT 	602COO01-8

SEAT COVERS

# MAIN ROTOR

4800 	Grip Assembly	206-010-102-009

4800 	Grip Assembly	206-010-102-013

4800 	Grip Assembly	206-010-102-121

400 	Pin Strap Retainer 	206-010-123-001

1200 	Pin Strap Retainer 	206-010-123-003

400 	Fitting Assembly 	206-010-155-007

1200 	Fitting Assembly	206-010-155-015

1200	Fitting Assembly	206-011-140-001

1200 		Hub Assembly	206-011-100-001

1200 		Hub Assemb!y	206-011-100-005

1200 		Hub Assembly 	206-011-100-023

Hub Assembly 	206-011-100-131

(Note 1)

Hub Assembly 	206-011-100-143

(Note 1)

2400 	Trunnion Assembly 	206-011-113-001

(Note2)

4800 	Trunnion Assembly 	206-011-113-103

1200/24 months 	Strap Assembly	206-011-147-001

1200/24 months 	Strap Assembly. 	206-011-147-005

1200/24 months 	Strap Assembly	206-011-154-101

1200/24 months 	Strap Assembly. 	206-011-154-105

3600 	Blade Assembly 	206-011-250-003

(Note 3)

3600 	Blade Assembly 	206-011-250-113

(Note 3)

3600	Blade Assembly	206-011-250-119

3000 		Mast 	206-040-003-007

(OH-58A)

3000 		Mast 	206-040-003-025

(OH-58C)

# MAIN ROTOR CONTROLS

4800 	Control Tube 	206-001-194-001

4800 	Control Tube 	206-001-194-005

4800 	Collective Idler Link 	206-010-407-001

Assembly

4800 	Swashplate and Support 	206-010-450-005

Assembly

4800 	Swashplate and Support 	206-010-450-007

Assembly

4800 	Swashplate and Support 	206-010-450-009

Assembly

4800 	Support Swashplate 	206-010-452-001

Assembly

4800 	Support Swashplate 	206-010-452-005

Assembly

4800 	Support Swashplate 	206-010-452-109

Assembly

4800 	Sleeve Swashplate 	206-010-454-001

Assembly

1

OH-58A/C Retirement/Overhaul Schedule						            4/18/2002

OVERHAUL 	RETIREMENT 	ITEM 	PART NUMBER

INTERVAL 	INTERVAL

(HOURS)	(HOURS)

# MAIN ROTOR CONTROLS (continued)

4800 	Sleeve Swashplate 	206-010-454-005

Assembly

- Sleeve Swashplate 	206-010-454-109

Assembly

4800 	Collective Lever 	206-010-467-001

Assembly

MAIN ROTOR DRIVE					|

2400	Main Transmission	206-040-003-005	|

206-040-003-023	|

TAIL ROTOR DRIVE SYSTEM

ON CONDITION 	Blower Assembly Oil 	206-061-432-001

Cooler 	(OH-58 A)

ON CONDITION 	Blower Assembly Oil 	206-061-432-039

Cooler 	(OH-58 C)

1200 	Blade Assembly 	206-010-750-005

900 	Blade Assembly (Serial 	206-010-750-005

Numbers TLL8000 and

below only)

1200 	Blade Assembly 	206-010-750-109

2400 	Blade Assembly 	206-016-201-111

2500 	Blade Assembly 	206-016-201-131

(Note 4)

2400 	Trunnion Assembly 	206-011-803-005

Unlimited 	Trunnion Assembly 	206-011-812-005

4800 	Yoke Assembly 	206-011-819-101

2400 		Gearbox Assembly 	206-040-400-007

2400 		Gearbox Assembly 	206-040-400-009

2400 		Gearbox Assembly 	206-040-402-003

3000 	Freewheeling Unit Clutch 	CL42250-1

3000 		Freewheeling Unit 	206-040-230-025

5000 	Main Driveshaft 	206-040-371-111

Assembly 	(SKCP2348-5)

2

Notes:

All retirement components will have a Demil code of "L" and be mutilated.

#1.  The complete -131 and -143 Hub Assembly has no overhaul or retirement interval. It

does contain retirement items listed on this schedule. For record keeping purposes the -131 and -143 hub assembly will be treated as a time change component. Hub Assemblies will be recorded on the aircraft time change DA Form 2408-16, with the lowest retirement life components as the driver for time change requirements.

#2.  Main Rotor Hub Assemblies PIN 206-011-100-131 or earlier may contain the 206-011- 113-001 or -103 Trunnion. The 206-011-100-143 Hub Assembly should only have the -103 Trunnion. Replacement of Main Rotor Trunnion PIN 206-011-113-001 has been controlled at overhaul of the Main Rotor Hub. When operating time of the -001 Trunnion is unknown due to no records, field units may replace the Trunnion on PIN 206-011-100-131 Hubs at 1200 hours since last Main Rotor Hub overhaul. The PIN 206-011-100-023 or earlier Hubs may be operated to next scheduled Main Rotor overhaul. When part number or serial number of the installed Trunnion cannot be determined, the unit may be operated to next required special (magnetic particle) Trunnion inspection.

#3.  Reference BHT Technical Bulletin SU-OH-2. Main Rotor Blade PIN 206-011-250-0031- 113, Increase in Retirement Life. This bulletin is not applicable to Type Certified Helicopters.

#4.  Reference BHT Technical Bulletin SU-OH-01, Alternate Spare Part; Tail Rotor Blade Assembly, PIN 206-016-201-131. This bulletin is not applicable to Type Certified Helicopters.

#5.  Applies to any engine having the Letter B as part of the suffix.

3