Instructions:

1)	Use the calibrated cable to calibrate the time-to-amplitude converter.  You should derive from this exercise a parameter with units [ns/channel].

2)	Determine the channel corresponding to zero time-of-flight, i.e., simultaneity.

3)	What is the theoretical shortest ToF that should be measured from the Am-Be source?  Neutrons from an Am-Be source have an average energy of about 4 MeV with a maximum (end point) of ~10 MeV.

4)	What do you measure for this quantity?

You will need the kinematic expression for elastic scattering of neutrons off hydrogen, i.e.,

sin2 q = Ep1/En

The mass of the neutron is 931.5 MeV.  Use the expression for b given in the other half of the practicum.

5)	What are factors contribute to the uncertainty in measuring the end point of the neutron spectrum?

Test Setup, TAC principle

PMT: photomultiplier

TAC: time to amplitude converter

CFD: constant fraction discriminator

MCA: multi-channel analyzer, a.k.a. pulse height analyzer (PHA)

Detector thresholds, as set with the CFDs: ~250 keV electron equivalent (g)

Neutron threshold energy (proton equivalent): ~1 MeV

Plastic scintillator detectors (2)

Measurement geometry

Lead absorbers (2 mm thick) to stop the 60 keV photos from the Am/Be source are not shown.

Dimensions ±0.5 cm

Time-of-Flight (ToF)

| Neutron ToF | Gamma ToF |
| --- | --- |

Calibration

| The 60Co source (1.2 µCi) emits two photons (1.17 MeV and 1.33 MeV), essentially simultaneously. Place this source at the midpoint between the scintillation detectors to find the ToF zero. |  |
| --- | --- |

Delay the start or the stop signal to the time to amplitude converter (TAC) by a known amount (9.4 ns) to calibrate the time scale of the measurement system (ns/channel).

The Am/Be neutron source (10 mCi) emits both neutrons and gamma-ray photons, including a 4.4 MeV photon.

Reference: Knoll, Radiation Detection and Measurement

ToF Spectra