JRG-68

ITU-R JRG 1A-1C-8B

4th Meeting – Mainz Germany – 13th-15th November 2006

Spectrum emission measurements of various radars

(Germany)

# Introduction

The Joint Rapporteurs Group JRG-1A-1C-8B has to investigate the possibility of introducing a more stringent emission mask for the out-of-band domain of radar emissions.. This document aims to support the work of this group by providing spectrum measurements performed in Germany on a number of magnetron based and one clystron based radar systems.

# Measured radars and their parameters

Measurements were made on the following radars:

- Fixed weather radar in Hamburg on 5919 MHz, using a coaxial magnetron

- Fixed weather radar in Hannover on 5639 MHz, using a coaxial magnetron

- Fixed maritime radar in Bremerhaven on 8959 and 9141 MHz, using a coaxial magnetron

- Fixed aeronautical radar at Deister on 1259 and 1345 MHz, using a clystron

Radars 3 and 4 consist of two transmitters on different frequencies using a common antenna via directional couplers. Since they have two different output devices with different characteristics they are regarded as two radars and numbered radar 3a, 3b, 4a and 4b.

The following is a summary of the radar parameters relevant for this project:

| Parameter | Radar 1 | Radar 2 | Radar 3a | Radar 3b | Radar 4a | Radar 4b |
| --- | --- | --- | --- | --- | --- | --- |
| Reference | M.1638 A | M.1638 A | M. [8B] S1 |  |
| Frequency | 5619 MHz | 5639 MHz | 8959.2 MHz | 9141.2 MHz | 1259 MHz | 1345 MHz |
| Radar Manufacturer | EEC (USA) | Gematronic (GER) | AEG Telefunken (GER) | DASA (GER) |
| Output device | Coaxial Magnetron Varian SFD-373A | Coaxial Magnetron Varian SFD-341A | Coaxial magnetron CPI VMX2037 | Clystron Thompson 2068A |
| Peak Power | 250 kW | 250 kW | 30 kW | 30 kW | 2500 kW | 1585 kW |
| Pulse length | 930 ns | 852 ns | 130.6 ns | 130.2 ns | 2.0 µs | 2.0 µs |
| Rise/fall time | 51 ns | 125 ns | 13.6 ns | 14.4 ns | 150 ns | 150 ns |
| PRF | 500 – 1200 Hz | 500 – 1200 Hz | 2400 Hz | 2400 Hz | 6 x 400 Hz 8 x 500 Hz | 6 x 400 Hz 8 x 500 Hz |

# Measurement setup and procedure

Radar 1 was equipped with a filter to suppress sideband emissions. Measurements were taken after this filter, directly before the rotary joint.

Radar 2 was also equipped with a filter. Measurements were taken both in front of and after this filter. This enables to verify the effect of the filter in the results.

Radar 3 and 4 were measured at the output of directional couplers, before the combiner. Decoupling between both transmitters was about 50 dB for radar 3 and 65 dB for radar 4, so that emissions less than 50 / 65 dB below the spectrum of the transmitter under test could originate from the other transmitter. For radar 4, pulses from both transmitters had an offset of 4.3 µs, so that at no time both transmitters were up simultaneously.

The spectrum was measured with an R&S FSIQ40 spectrum analyzer.

The pulse parameters were measured with a 1 GHz Infinium oscilloscope 54835A in conjunction with a broadband pulse detector.

Interpretation and conclusion

The results show that even spectra from identical types of radars differ considerably. Especially for magnetron based radars it sometimes seems difficult to meet the current 20 dB/decade mask (radars 1 and 2). In most cases, the 40 dB/decade mask from the design objective could not be met. Exception is Radar 3b that seems to meet the design objective. To make a definite statement here, a higher measurement dynamic range would be necessary. When looking at the effect of filters as used for the sidebands of radars 1 and 2, it may be possible to meet this mask if the filters were better optimized for both sidebands.

Although the clystron based radar 4b has a very clean spectrum, it can not meet a -40 dB/decade mask, mainly because of the 40 dB bandwidth being too wide when compared with the current formula.

The chosen radar examples, all with unmodulated pulses, show how critical the -40 dB bandwidth formulas are when applying OoB masks. Whereas the current formula may even be insufficient in case of radar 2, it is much too generous in case of radar 4.

# Annex: Result radar 1

Fig. 1: The sideband emissions depend on the PRF. In the worst case, even the 20 dB/decade mask is exceeded, in all other cases, the 40 dB/decade mask is still exceeded around 5500 MHz (offset around -120 MHz).

Result radar 2 (full span 7 GHz)

Fig. 2: A filter is used to suppress sideband emissions. Without this filter, not even the -60 dB attenuation for high frequency offsets can be met.

Result radar 2 (span 1 GHz)

Fig. 3: The filter cannot suppress the sideband emissions at about 100 MHz offset. Therefore, even with filter, the 20 dB/decade mask can not be met.. The 40 dB/decade mask still seems critical, mainly due to the very tight fit at the -40 dB bandwidth points, even if the filter would be better optimized and/or narrower.

Result radar 3a

Fig. 4: The peak at 9141 MHz is from the second radar working to the same antenna, but the peaks around 8500 MHz (offset -450 MHz) prevent conformance with the design objective. The -40 dB bandwidth formulas are very generous in this case. The actual bandwidth is only about 50% of the calculated.

Result radar 3b

Fig. 5: The peak at 8959 MHz is from the second radar working to the same antenna. Due to the very generous -40 dB bandwidth formulas (measured bandwidth is only about 50% of that), the 40 dB/decade mask from the design objective could be met.

Result radar 4a

Fig. 6: Neither the current nor the mask from the design objective could be met by this radar which obviously has a problem with the transmitter, because even the -40 dB necessary bandwidth is exceeded by nearly 100%.

Results radar 4b

Fig. 7: This radar can easily meet the 20 dB/decade mask, but sideband emissions around 1285 MHz (offset around -80 MHz) make it impossible to meet the design objective. The -40 dB bandwidth is a very critical fit.

# Text boxes

Measurement of pulse parameters. In case the parameters were not constant, like in this example, about 10000 pulses were averaged.