JRG 1A-1C-8B

DRAFTING GROUP 3 – MAGNETRONS

Interim drafting group report on the DG3 task according to JRG-46 Rev2

Introduction

This report contains the findings reached at January 2006 by the working group on the task set by the ITU-R Joint Rapporteurs Group JRG 1A-1C-8B in document JRG-46 Rev2 as

JRG-DG3: Magnetron Emission Masks

Terms-of-Reference

1.	Review the measured magnetron emission spectrum data to determine whether there is sufficient data to reach a conclusion on whether more stringent masks are achievable.  Priority 1.

Priority 1 Milestone: December 15, 2005

Relevant JRG Contributions: JRG-14, 16, 20, 22, 40, 42

Documents JRG-DG3-01 and JRG-DG3-02 contains the basis and the work format followed by the drafting group to formulate the required answer to the set task and thus to formulate the basis of the work done here.

Identification of all magnetron-based radars was the starting point followed by a search and collection for all available spectrum data to the identification list, that was the only possible way to obtain the data due to time constraints, massive cost of measurements and hardware availability.

The collected spectrum data would then be used for making the assessment on the spectrum capabilities based on criteria set in JRG-DG3-02 under agenda item 5.

Magnetron classifications

In order to generate a check list for the spectrum data collection, a classification or identification list for the Radars and their related magnetrons would need to be generated covering as much of the magnetron population available  for current day technology (Ref JRG-DG3-02 Agenda item 1&2).

This can be based on:

- Peak power and pulse width **

- Frequency band **

- Fixed /Mobile Radars

- Application (aeronautical, maritime, weather, space..etc) and class (military /civil) **

- By RR application e.g. radiolocation /radiodetermination

- By technology type; cavity, linear and coaxial **

** Category used by Magnetron manufacturers

A reference to ITU-R recommendations in conjunction with the above table was used to produce a more comprehensive detailed list for magnetron based radars that resulted in the following tables:

| Reference System M.[8B.8 –10]GHz* | Description RD/RL** | Output device | Peak Power (kW) | Minimum Pulse width (µS) | Spectrum data available |
| --- | --- | --- | --- | --- | --- |
| A2 | Airborne search radar (RD) | Tunable magnetron | 220 | 0.5 | No |
| A3 | Ground mapping (RD) | Cavity tuned magnetron | 95 | 0.5 | No |
| A9 | Weather/Search and rescue/mapping (RD) | Magnetron | 25 | 0.2 | No |
| A11 | As A9 | Magnetron | 6 | 4 | No |
| S1 | Search/navigation (RD) | Magnetron | 35 | 0.1 | No |
| S4 | Radionavigation (RD) | Magnetron | 50 | 0.03 | No |
| S6 | Radionavigation (RD) | Magnetron | 25 | 0.08 | Yes |
| S7 | Navigation/Search (RD) | Magnetron | 1.5 | 0.08 | Yes* |
| S8 | Radionavigation (RD) | Magnetron | 5 | 0.05 | Yes |
| S9 | Radionavigation (RD) | Magnetron | 10 | 0.08 | Yes |
| G1 | Airborne Beacon transponder (RD) | Magnetron | 0.3 | 0.3 | No |
| G9 | Meteorological (RL) | Magnetron | 50 | 0.1 | No |
| G10 | As G9 | Magnetron | 250 | 0.5 | No |
| G11 | As G10 | Magnetron | 35 | 1.0 | No |

*	System reference – A(airborne) – S(shipborne) – G (Ground)

**	RD – radiodetermination – RL – radiolocation

Yes* 	Spectrum for 2 kW version

| Reference System M.1638 | Description | Output device | Peak Power (kW) | Minimum Pulse width (µS) | Spectrum data available |
| --- | --- | --- | --- | --- | --- |
| A | Meteorological Ground/ship | Coaxial magnetron | 250 | 2.0 | No |
| B | Meteorological Airborne | Coaxial magnetron | 70 | 6.0 | No |
| D | Aeronautical Airborne (radionavigation) | Magnetron | 0.2 | 1.0 | No |
| F | Meteorological Ground | Tunable magnetron | 250 | 0.8 | No |
| G | Meteorological Ground | Coaxial magnetron | 250 | 3.0 | No |
| H | As G | Coaxial magnetron | 250 | 0.8 | No |
| I | As G | Coaxial magnetron | 250 | 0.8 | No |
| J | As G | Coaxial magnetron | 2.25 | 0.1 | No |
| K | As G | Coaxial magnetron | 250 | 2.5 | No |

| Reference ITU RM.1460 | Description | Output device | Peak Power (kW) | Minimum Pulse width (µS) | Spectrum data available |
| --- | --- | --- | --- | --- | --- |
| IMO/ Fishing | Maritime radionavigation (shipborne) | Magnetron | 75 | 0.05 | No |

| Reference ITU RM.1313 | Description | Output device | Peak Power (kW) | Minimum Pulse width (µS) | Spectrum data available |
| --- | --- | --- | --- | --- | --- |
| Leisure craft | Maritime radionavigation (shipborne) | Magnetron | 10 | 0.08 | Yes |
| River | As above | Magnetron | 5 | 0.05 | Yes* |

Yes*	Spectrum for 4kW version

| Reference ITU RM.1464 | Description | Output device | Peak Power (kW) | Minimum Pulse width (µS) | Spectrum data available |
| --- | --- | --- | --- | --- | --- |
| D | Ground ATC | Magnetron | 450 | 1 | No |
| H | Ground Weather | Coaxial magnetron | 556 | 1 | No |

Note: For all tables, the word No under “Spectrum data available” column indicates that drafting group 3 was not able to source /find or measure spectrum data for that class of radar.

#### Summary of ITU Recommendations for radar systems

| ITU** Recommendation | Frequency range MHz | Radio service allocation* |
| --- | --- | --- |
| 1226 | 50 | Wind profiler radar |
| 1462 | 420 - 450 | RL |
| 1227 | 1000 | Wind profiler radar |
| 1463 | 1215 - 1400 | RD |
| 1464 | 2700 - 2900 | ARN + RL |
| 1460/1313 | 2900 - 3100 | RN + RL + Meteorological |
| 1465 | 3100 - 3700 | RD |
| 1638 | 5250 - 5850 | RL + ARN + Meteorological |
| [8B.8 – 10 GHz]/1313 | 8000 - 10000 | RL + ARN + MRN + RN |
| 1644 | 13750 – 14000 | RL + RN |
| 1730 | 15700 – 17300 | RL |
| 1466 | 31800 - 33400 | RN |
| 1640 | 33400 - 36000 | RD |
| 1452 | 60000-61000 and 76000-77000 | RL(automobiles) |

*	RL – Radiolocation	RD  - Radiodetermination	RN – Radionavigation

ARN – Aeronautical radionavigation

MRN – Maritime radionavigation

**	Radar output devices are not included in Recommendations 1226, 1227, 1452, 1462, 1465, 1466, 1640, and 1644.

In 1463 and 1730 there are no magnetron devices.

Observations

From the tables listed in the previous section of magnetron classifications, one can clearly conclude that the portion of the collected spectrum data is considerably less than the total number of  categories /types identified. A continued effort to collect data has not resulted in any further gain on the position shown despite the wider search /approach to the JRG /ITU-R WP8B communities.

This can be down to many factors most important of which is the time scale for the work in hand versus the size of the data needed, which is easily reflected in the number of categories, listed above.

The other problem encountered is reflected in the summary table of the ITU-R recommendations where output devices are not specified at all, research on some of those radar categories revealed the existence of mixed devices in use including magnetrons. One can easily see that this situation would make the spectrum assessments (when and if located) extremely difficult if not impossible.

Reflecting back to the terms of reference that the drafting group was tasked with, clearly there is a need to obtain spectrum data for most if not all those listed above in order that a proper and correct consideration can be made to the span of fluctuations /variation in spectrum performance.

Collected Spectrum data

All collected spectrum data represented in plots 1-8, have been captured using the direct method as described in ITU-R M1177 and represent current day technology mobile marine radars utilising current day technology magnetron devices. The identification of make and model of those radars is not provided due to the commercial confidentiality.

Plot 1 is for a 25kW X band mobile marine radar, the plot indicates that the resultant spectrum is well within the current roll off of –20dB/dec. The harder roll off limit line is that of –40dB/dec and is extremely close to the resultant (just fails).

Plot 2 is for a different 25kW X band mobile marine radar (different radar manufacturer to that in plot 1), here the plot clearly shows that this radar resultant spectrum fails both the –20db/dec and –40dB/dec roll off.

Naturally the radar designs are different from the microwave (plumbing) aspects and are not of the same size/electronics, however it is important to note that  they also incorporate different magnetrons, in effect the magnetrons are also designed by two different magnetron manufacturers.

Plot 3 &4 are for two different 30kW S band mobile marine radars (two different manufacturers), resultant spectrum on both radars is within the –20db/dec roll off limit line and breaking the –40dB/dec roll off limit line (extremely marginal break on the radar in plot 4).

The two radars are of the same class /size but different design from each other; here we also have two different magnetron makes in use by the two radars.

Plot 5 is for an IMO X band mobile marine radar; the spectrum shown of this radar in the plot is well within the limit lines of both –20dB/dec and –40dB/dec.

Plots 6 & 7 are for 2kW and 4kW X band mobile marine radars, both are capable of meeting the –40dB/dec roll off limit line. Both radars are non-IMO class.

Plot 8 is for an IMO mobile marine X band radar, the resultant spectrum clearly breaks both the 20dB/dec & -40dB/dec limit lines. It is important to note here that this spectrum is typical of those radars found today and represent one of the many sample spectrum data obtained and it is worth noting that it is representative of radars out in the field by many manufacturers (all similar spectrum).

A glance back at the obtained results and analysis above can be summarised as follows:

- Spectrum data obtained for this task are for marine mobile radars only.

- Some existing radars in the data collected are not capable of meeting the –20dB/dec

- The sample of data obtained against given type /power of radar is too narrow except in plot 8.

- Different pulse width /in different radars used as well as different magnetrons for same class radars (at least 3 variables in a single equation type analysis).

- Different antennas in use on systems for like to like comparison in the same class (plots 3 & 4 for e.g.) over and above the other variables that are different between the two radars under comparison.

Multiple variables in every plot “equation” would prevent accurate analysis of the spectrum ability of a given device, as the magnetron device spectrum performance can be seriously affected by the microwave characteristics of the radar system using the device. A good example of that is to consider the “what would happen” scenario if the radar in plot 1 was fitted with the magnetron used in plot 2, these are questions that are key to the assessment and the study, however they require full access to the hardware and provision of the time and cost to make the measurements. If the latter is projected on few of the plots shown above, one could quickly see the size of the task in hand and now taking that further to other categories of radars (or even few of them) in the tables listed earlier in this report would make the overall task of massive magnitude in time, efforts and cost.

A limited sample spectrum of magnetron devices measured in wave guide at perfect load conditions supplied by a two of the major manufacturers in UK and Japan has reflected the same pattern noted above, i.e. some do have a roll off capabilities close to –40dB/dec and some do not (even from the same manufacturer but with different power output device), even when considering a fixed perfect (50 ohms) load conditions, cavity type magnetron would deliver different spectrum performance with changes in power and pulse width values.

SUMMARY

Spectrum data collected represented only the mobile marine radar category from the total list identified in the work of drafting group 3 (reference document JRG-DG3-02 and this report).

Data reflected in the spectrum collected cannot enable a conclusion to be reached on magnetron based radar spectrum agility from roll off capabilities point of view due to the number of variations in the available narrow sample data obtained. That portrayed by the plots has shown variation from not able to meet –20dB/dec up to well within the –40dB/dec limit line.

Only cavity type magnetron data was available. Although the cavity type is widely used in commercial radar application it is most certainly not the dominant one as coaxial magnetron based radar do also represent a respectable portion of the total radar population picture. Linear magnetron devices also do exist as per the magnetron manufacturers current product data (UK and Japan), the latter is admittedly not widely in use by radar system but never the less it is in use today.

Key areas of radar usage like Marine fixed installation Radars (VTS), Air traffic control Radars (ATC), Aeronautical Radars and Metrological/ Weather Radars spectrum data availability are considered vital to aid the correct consideration to be made on the span of fluctuations /variation in spectrum performance of those radars from their magnetron point of view.

Magnetron performance and behaviour in terms of resultant spectrum is strongly dependent on the drive characteristics of the radar modulator as well as the characteristics of the radar microwave system including the antenna.

Recommendations

- The JRG urgently needs to find a mechanism whereby the sample size and categories of magnetron spectra can be increased;

- The next meeting of WP8B should be used to take forward the data collection process by specific requests from the JRG;

- WP8B should be requested to identify the type of transmitter device used in those Recommendations listed in this report;

- There is a need to determine whether there is radar operating in other bands than those listed in this report, in which there are currently radiodetermination allocations.

Plot 1

Plot 2

## Plot 3

## Plot 4

## Plot 5

## Plot 6

Plot 7

## Plot 8