WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A13555 | In-Flight Anomaly Number -- | Contractor Report Number E-144 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title COAX CABLE CONNECTOR DAMAGED |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1 |
| HCRIT -- | Sys_Lvl N | Misc Codes A (1) B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE LRU | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE COAXIAL CABLE ASSY | PART# 80933003704-139 | SER/LOT# 909 | MANUFACTURER MMMSS |
| Test/Operation L - FLD | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EL - SHORT | Cause ESW - EI-SHIP-WORK |
| System ELECTRICAL | Defect DC - BROKEN | Material E - EL C/W | Work Contact J. ADAMS | Fail Date 02/26/1991 |
| Received at MSFC 03/06/1991 | Date Isolated 02/27/1991 | FMEA Reference 80-16-314 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location KSC | Symptom EL - SHORT | Time Cycle -- |
| Effectivity Text PROBLEM CLOSED 04/26/91 |
| Vehicle Effectivity Codes |
| Vehicle 1 ET46 | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date 03/08/1991 | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary PROBABLE CAUSE - HANDLING DAMAGE DURING WORK AT KSC |
| Last MSFC Update 02/13/1995 | CN RSLV SBMT 03/26/1991 | Defer Date -- | Add Date 03/11/1991 | R/C Codes 0 - EXPL -- -- |
| Assignee |
| Design R. MOYE | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR G. LADNER |
| Approval |
| Design R. MOYE | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR G. LADNER |
| PAC Assignee T. HESTER | PAC Review Complete TH | MSFC Closure Date 04/26/1991 | Status C - CLOSED | F/A Completion 03/21/1991 |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID F/A T-117660 |
| Related Document Title FAILURE ANALYSIS REPORT |
| Related Document Type -- | Related Document ID IPR IV6-39V-0177 |
| Related Document Title INTERIM PROBLEM REPORT |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary OPEN |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description A DAMAGED COAXIAL CABLE CONNECTOR ON ET-46, REFERENCE DESIGNATOR 314W16P1, IN THE RANGE SAFETY COMMAND DESTRUCT SYSTEM (RSS) CAUSED AN ELECTRICAL TEST FAILURE AT KSC. THE INTEGRATED RECEIVER - DECODER RF INPUT SIGNAL WAS ATTENUATED DUE TO THE DAMAGE CRITICALITY: THE CABLE IS CRIT. 1: USBI-RA-20 FMEA 80-16-314; "LOSS OF RF SIGNAL" GENERAL: THE RANGE SAFETY SYSTEM (RSS) INTEGRATED RECEIVER-DECODER (IRD) PERFORMANCE ON ET-46 WAS BEING TESTED AT KSC PER OMI S00008-20-005. A -47 DBM RF SIGNAL WAS APPLIED TO THE "N" SERIES CONNECTOR ON THE INTERTANK GROUND TEST PORT. THE RECEIVER PERFORMANCE WAS BEING CHECKED BY MEASURING THE AUTOMATIC GAIN CONTROL (AGC) VOLTAGE. THE MINIMUM EXPECTED VOLTAGE WAS 3.6 VDC. THE ACTUAL VOLTAGE OBTAINED WAS 3.0 VDC THE TEST ANOMALY OCCURRED ON FEBRUARY 13, 1991, AND WAS DOCUMENTED ON INTERIM PROBLEM REPORT IV6-39V-0177. DUE TO SCHEDULE/TIME CONSTRAINTS, THE WORK WAS DELAYED UNTIL THE VEHICLE WAS MOVED TO THE LAUNCH PAD WHEN TROUBLESHOOTING WAS ALLOWED TO CONTINUE, A DAMAGED COAXIAL CABLE CONNECTOR, 314W16P1, WAS DISCOVERED ON THE CABLE BETWEEN THE IRD AND THE HYBRID COUPLER. THE CABLE WAS REPLACED. THE COUPLER WAS ALSO REPLACED AS A PRECAUTION. WHEN THE RSS PERFORMANCE WAS CHECKED ON FEBRUARY 26, 1991, THE IRD PROVIDED THE PROPER AGC VOLTAGE. THIS CONFIRMED THAT THE ORIGINAL ANOMALY WAS THE RESULT OF THE FAILED/DAMAGED CONNECTOR |
| Contractor Investigation/Resolution |
| MSFC Response/Concurrence TASK I. FAILURE INVESTIGATION FAILURE ANALYSIS T-117660 IS IN PROGRESS ON THE DAMAGED RF CONNECTOR ECD: MARCH 8, 1991 COMPLETE: MARCH 21, 1991 CLOSURE STATEMENT FAILURE ANALYSIS T-117660 DETERMINED THAT THE TUBULAR PORTION OF THE CONNECTOR BODY, WHICH FORMS THE INNER WALL OF THE BRAID ATTACHMENT, HAD FRACTURED IN A BENDING MODE. THERE WAS NO DEFECTIVE MATERIAL, DIMENSIONAL DEFECT, OR ASSEMBLY ERROR IN THE CONNECTOR. THE FRACTURE WAS THE DIRECT RESULT OF THE APPLICATION OF AN EXTERNAL FORCE AT, OR NEAR, A RIGHT ANGLE TO THE LONGITUDINAL AXIS OF THE CONNECTOR. THE AMOUNT OF FORCE NECESSARY TO CAUSE THE FAILURE, DETERMINED BY BOTH STRESS ANALYSIS AND TEST, WAS BETWEEN APPROXIMATELY 17 AND 26 POUNDS IT WOULD HAVE BEEN DIFFICULT TO DEVELOP SUCH FORCE UNLESS THE CONNECTOR WAS SECURED TO A MATING CONNECTOR, SUCH AS THAT ON THE HYBRID COUPLER IT IS PROBABLE THAT THE DAMAGE OCCURRED AT KSC AS THE ET ACCEPTANCE TESTING AND SHAKEDOWN INSPECTIONS AT MAF WOULD HAVE DETECTED SUCH DAMAGE HAD IT BEEN PRESENT AT THAT TIME TASK CLOSED TASK II. CORRECTIVE ACTION NO CORRECTIVE ACTION IS REQUIRED. THE MANUFACTURING CONTROLS, TESTS, AND INSPECTIONS NOW IN USE ARE SUFFICIENT TO PROPERLY ASSEMBLE THE CABLES AND TO DETECT DAMAGE WHEN IT OCCURS. THIS IS AN ISOLATED CASE THE ELECTRICAL TEST FAILURE ON ET-46 IS THE ONLY ONE KNOWN TO HAVE OCCURRED ON AN ET AT DUE TO A DAMAGED INTERNAL RSS CABLE ASSEMBLY TASK CLOSED TASK III. CLEARANCE OF EFFECTIVITIES ALL ETS CLEARED. THERE ARE SUFFICIENT FABRICATION CONTROLS AND TESTS OF THE COAXIAL CABLES TO DETECT DAMAGE WHEN IT OCCURS AND ASSURE PROPER ASSEMBLY. THE DAMAGED COMPONENTS ON ET-46 WERE REPLACED. AS IT IS UNKNOWN HOW THE FORCE WHICH DAMAGED THE CABLE WAS APPLIED, THE HYBRID COUPLER WAS ALSO REPLACED. REFERENCE: INTERIM PROBLEM REPORT IV6-39V-0177 AND PROBLEM REPORT ET46-RSS0004 THE NON-CONFORMANCE DOCUMENTS FOR ALL COMPLETED ETS, WHETHER DELIVERED TO THE GOVERNMENT OR NOT, WERE REVIEWED FOR OTHER INSTANCES OF FRACTURED COAXIAL CABLE CONNECTOR PLUGS. ONLY ONE INSTANCE WAS FOUND. CONNECTOR 314W15P1 ON THE HYBRID COUPLER OF ET-47 HAD BEEN DAMAGED AT MAF. THE DAMAGE HAD BEEN DETECTED VISUALLY AND THE CABLE HAD BEEN REPAIRED. THE HYBRID COUPLER HAD NOT BEEN REPLACED. AS A PRECAUTIONARY ACTION, THE HYBRID COUPLER WAS REPLACED. REFERENCE: MARS T-118187 AND PROBLEM REPORT ET47-RSS0001 TASK CLOSED TASK IV. CLOSURE SUMMARY THE 314W16P1 COAXIAL CABLE CONNECTOR PLUG ON ET-46 WAS DAMAGED AS THE RESULT OF THE APPLICATION OF AN EXTERNAL FORCE. ET-46 WAS REPAIRED BY REPLACING THE DAMAGED EQUIPMENT. NO CORRECTIVE WAS REQUIRED. THIS WAS AN ISOLATED CASE. THERE ARE SUFFICIENT CONTROLS AND TESTS TO PROPERLY ASSEMBLE THE HARDWARE AND TO DETECT DAMAGE WHEN IT OCCURS TASK CLOSED THIS PROBLEM REPORT IS DEFERRED FOR THE NEXT SIX MONTHS PER NSTS 07700, VOLUME XI, PARAGRAPH 3.4.1, ITEM C AND NSTS 08126, REV. D, PARAGRAPH 3.3.10.1, ITEM C WHICH STATES, "THE PROBLEM CONDITION DOES NOT EXIST IN THE FLIGHT HARDWARE." ______________GERALD C. LADNER 3/21/91________________ ** DEFERRAL RATIONALE APPROVED BY G. LADNER, ET PROJECT MANAGER ON 3/21/91 ** ** CLOSURE RATIONALE APPROVED BY G. LADNER, ET PROJECT MANAGER ON 4/26/91 ** |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A13555 | IFA# -- | Contractor RPT# E-144 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 80933003704-139 | Asmnt Part Name COAXIAL CABLE ASSY | Asmnt Serial/Lot# 909 |
| HCRIT CD -- | FCRIT CD 1 | CAUSE CD ESW - EI-SHIP-WORK | FAIL MODE EL - SHORT |
| Asmnt FMEA USBI 80-16-314 | Asmnt FM N/A | FMEA CSE N/A | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |