Lunar Laser Ranging Analysis Report

J.G. Williams, D.H. Boggs, J.O. Dickey, and J.T. Ratcliff

##### Jet Propulsion Laboratory, California Institute of Technology, Pasadena, CA 91109, USA

#### Introduction/Background/Data Products Provided:

Analyses of laser ranges to the Moon are used for a variety of investigations:  lunar science, gravitational physics, geodesy, geodynamics and astronomy.  Unique contributions from LLR include: detection of a molten lunar core; measurement of tidal dissipation in the Moon; an accurate test of the principle of equivalence for massive bodies (strong equivalence principle); and detection of lunar free librations.  LLR analyses provide tests of gravitational physics, measurements of the Moon's tidal acceleration and the Earth's rotation and precession, and orders-of-magnitude improvements in the accuracies of the lunar ephemeris and three-dimensional rotation.  Lunar and planetary ephemerides and lunar physical librations are available to the scientific community at http://ssd.jpl.nasa.gov/horizons.html.

Current Activities:

Lunar Laser Ranges are regularly received from the Observatoire de la Côte d'Azur and McDonald Observatory sites. These ranges are processed at regular intervals for Earth rotation information.  UT0 and variation of latitude for the two stations are input to the JPL Earth rotation filter.

The tidal acceleration of the Moon has been computed for several ephemerides based on iterated solutions.  The acceleration in mean longitude due to dissipative effects is -25.7 "/cent2, of which -26.0 "/cent2 is due to tides on Earth and +0.3 "/cent2 is due to tidal and fluid core dissipation in the Moon.  The tidal increase in semimajor axis is 38 mm/yr.

Dissipation in the Moon is discussed in (4).  The solid-body tidal Q is low and a fluid core is detected.  An oblate core-mantle boundary will influence the determination of the Love number k2.  First attempts allowing for CMB oblateness give k2=0.026, with uncertainty 0.003 (6, 7).

Uncertainties continue to tighten for tests of gravitational physics.  The Earth and Moon are accelerated alike in the Sun's gravitational field to 1.5 parts in 1013 (1).  This equivalence principle test is sensitive to differences between Earth and Moon due to both composition and self-energy.  The relativistic geodetic precession of 19 mas/yr is confirmed within 0.35%.  Based on point mass interactions, the uncertainties for Parameterized Post Newtonian beta and gamma are both 0.004 (2).  The equivalence principle test limits the beta uncertainty further to 0.0005 (1).  The gravitational constant G has no detectible rate for dG/dt / G within 1.1x10-12 /yr (2, 8).

Papers

1) J. D. Anderson and J. G. Williams, Long-Range Tests of the Equivalence Principle, Classical and Quantum Gravity, vol. 18, in press, 2001.

2) J. G. Williams, D. H. Boggs, and J. O. Dickey, Lunar Laser Tests of Gravitational Physics, Proceedings of Ninth Marcel Grossmann Meeting (World Scientific Publ.), in press, 2001, there is a short print version and a longer electronic version.

3) P. J. Shelus, J. G. Ries, J. G. Williams, and J. O. Dickey, A Summary of LLR Activities and Science Results, Proceedings of 12th International Workshop on Laser Ranging, Matera, Italy, November 2000, in press, 2001.

4) J. G. Williams, D. H. Boggs, C. F. Yoder, J. T. Ratcliff, and J. O. Dickey, Lunar Rotational Dissipation in Solid Body and Molten Core, submitted to J. Geophys. Res. - Planets, under revision, 2001.

###### Abstracts

5) J. G. Williams,, D. H. Boggs, J. O. Dickey, and W. M. Folkner, Lunar Laser Tests of Gravitational Physics, Marcel Grossmann IX, July 2-8, 2000, Rome, Italy.

6) J. G. Williams, D. H. Boggs, J. T. Ratcliff, C. F. Yoder and J. O. Dickey, The Moon's Molten Core, Tides, and Energy Dissipation, Abstract for Division of Planetary Sciences, October 23-27, 2000, Pasadena, CA, Bull. Amer. Astron. Soc. 32, 1034, 2000.

7) J. G. Williams, D. H. Boggs, J. T. Ratcliff, C. F. Yoder and J. O. Dickey, Influence of a Fluid Lunar Core on the Moon's Orientation, Abstracts of the Lunar and Planetary Science Conference XXXII, abstract #2028, March 12-16, 2001.

8) J. G. Williams, J. D. Anderson, D. H. Boggs, E. L. Lau, and J. O. Dickey, Solar System Tests for Changing Gravity, Amer. Astron. Soc., Pasadena, CA, June 3-7, 2001, Bulletin of the American Astronomical Society, Vol. 33, 836, 2001.

Key Points of Contact:

Name				e-mail					Telephone No.

James G. Williams	James.G.Williams@jpl.nasa.gov		(818) 354-6466

Dale H. Boggs		Dale.H.Boggs@jpl.nasa.gov			(818) 354-1630

Jean O. Dickey	Jean.O.Dickey@jpl.nasa.gov			(818) 354-3235

J. Todd Ratcliff	James.T.Ratcliff@jpl.nasa.gov		(818) 354-0204

All Key Points of Contact can be reached at:

Jet Propulsion Laboratory

Mail Stop 238-332

4800 Oak Grove Drive

Pasadena, CA  91109-8099

FAX:  (818) 393-6890

Future Plans:

Continue investigation of lunar science and gravitational physics utilizing LLR data.  Generate Earth rotation results.  Continue lunar ephemeris and physical libration developments.