PROGRAM TJI95

C

C........+.........+.........+.........+.........+.........+.........+..

C     Multi-platform COSMIC-RAY TRAJECTORY PROGRAM

C     FORTRAN 77     transportable version

C     Read in control card; LAT, LON, RIG, ZENITH, AZIMUTH, DELPC, INDO

C          Then calculate        INDO    trajectories

C               Starting at      PC

C               Incrementing at  DELPC   intervals

C     Includes conversion from Geodetic to Geocentric coordinates

C     Includes re-entrant albedo calculations

C     Uses subroutine SINGLTJE to do trajectory calculations

C     Magnetic field - IGRF 1995 (order 10)                          ###

C........+.........+.........+.........+.........+.........+.........+..

C     Restrictions: Cannot run over N or S pole; will get BETA blowup

C........+.........+.........+.........+.........+.........+.........+..

C     Mod History

CLast Mod 21 Dec 00  Make all intrinsic function double precision for PC

C     Mod 20 Dec 00  Insert 8 character format 1000 with AZ & ZE

C     Mod 17 Feb 99  set limit to 600000

C     Mod 17 Feb 99  if (ymax.lt.6.6) IFATE = 3

C     Mod    Aug 97  Adjust step size to minimize beta problems

C     Mod    Jan 97  High latitude step size adjust, introduce AHLT

C     Mod    Jun 96  EDIF limit set to 1.0e-5

C     Mod    Jun 96  IERRPT formats, Boundary and look ahead

C     Mod    Feb 96  Standard reference TJ1V line check

C     Mod    Dec 94  Print out start and end times of PC run

C     **************************************************************

C          Timing estimates base on COMPAQ Digital FORTRAN

C     Will run on PIII PC at 850 MHZ        55000 steps/sec (Real*8)

C     Will run on PIII PC at 700 MHZ        39000 steps/sec (Real*8)

C     Will run on PIII PC at 550 MHZ        32000 steps/sec (Real*8)

C     Will run on PII  PC at 400 MHZ        23000 steps/sec (Real*8)

C     **************************************************************

C     *  TAPE*       Monitor program operation

C     *  TAPE1       Trajectory control cards

C     *  TAPE7       80  character line (card image)  output

C     *  TAPE8       132 character line printer output

C     *  TAPE16      Diagnostic output for trouble shooting

C     *              Normally turned off (open statement commented out)

C     **************************************************************

C........+.........+.........+.........+.........+.........+.........+..

C     Programmer - Don F. Smart; FORTRAN77

C     Note - The programming adheres to the conventional FORTRAN

C            default standard that variables beginning with

C            'i','j','k','l','m',or 'n' are integer variables

C            Variables beginning with "c" are character variables

C            All other variables are real

C........+........+.........+.........+.........+.........+.........+..

C            Do not mix different type variables in same common block

C            Some computers do not allow this

C........+.........+.........+.........+.........+.........+.........+..

C

IMPLICIT INTEGER (I-N)

IMPLICIT REAL * 8(A-B)

IMPLICIT REAL * 8(D-H)

IMPLICIT REAL * 8(O-Z)

C

C........+.........+.........+.........+.........+.........+.........+..

C

COMMON /WRKVLU/ F(6),Y(6),ERAD,EOMC,VEL,BR,BT,BP,B

COMMON /WRKTSC/ TSY2,TCY2,TSY3,TCY3

COMMON /TRIG/   PI,RAD,PIO2

COMMON /GEOID/  ERADPL, ERECSQ

COMMON /SNGLR/  SALT,DISOUT,GCLATD,GDLATD,GLOND,GDAZD,GDZED,

*                RY1,RY2,RY3,RHT,TSTEP

COMMON /SNGLI/  LIMIT,NTRAJC,IERRPT

C

C........+.........+.........+.........+.........+.........+.........+..

C

OPEN (1, FILE='TAPE1', STATUS='OLD')

OPEN (7, FILE='TAPE7', STATUS='UNKNOWN')

OPEN (8, FILE='TAPE8', STATUS='UNKNOWN')

open (16,FILE='TAPE16',STATUS='UNKNOWN')

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ User defined program control

C........+.........+.........+.........+.........+.........+.........+..

FSTEP = 4.0E08

LIMIT = 600000

C

C........+.........+.........+.........+.........+.........+.........+..

C     /\ FSTEP  is total number of steps before run is terminated

C        LIMIT  is       max number of steps before trajectory declared F

C........+.........+.........+.........+.........+.........+.........+..

C     \/ Define program constants

C........+.........+.........+.........+.........+.........+.........+..

C        DISOUT is       radial distance for trajectory termination

C        ERAD   is       average earth radius

C        NTRAJC is       number of trajectory computed in this run

C        RHT    is       top of atmosphere for re-entrant trajectory

C        TSTEP  is       number of steps executed in this run

C........+.........+.........+.........+.........+.........+.........+..

C

NTRAJC = 0

TSTEP = 0.0

C

DISOUT = 25.0

ERAD   = 6371.2

RHT    = 20.0

VEL    = 2.99792458E5/ERAD

C

C........+.........+.........+.........+.........+.........+.........+..

C      "VEL" is light velocity in earth radii per second

C      Light speed defined as    299792458 m/s

C       Ref: E. R. Cohne AND B. N. Taylor, "The Fundamental Physical

C            Constants, Physics Today P11, August 1987.

C........+.........+.........+.........+.........+.........+.........+..

C     \/ Define essential trigonometric values

C........+.........+.........+.........+.........+.........+.........+..

C

PI   = ACOS(-1.0)

RAD  = 180.0/PI

PIO2 = PI/2.0

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ TAPE1 must contain trajectory control cards

C        Terminate program if no data on TAPE1 file

C        Terminate if EOF encountered

C        Terminate if negative data found on input file

C        Terminate if bad      data found on input file

C........+.........+.........+.........+.........+.........+.........+..

C

100 READ (1,1010,IOSTAT=IOSTAT,ERR=120,END=110) GDLATD,GLOND,PC,

*     GDZED,GDAZD,DELPC,INDO,IERRPT,INDEX

1010 FORMAT (BZ,6F8.2,3I8)

C

110 CONTINUE

IF (IOSTAT.LT.0) THEN

WRITE (*,1020)

GO TO 150

ENDIF

1020 FORMAT (' END OF FILE ON TAPE 1 (DATA INPUT)')

120 IF (IOSTAT.GT.0) THEN

WRITE (*,1030) IOSTAT,GDLATD,GLOND,PC,DELPC,

*                  INDO,IERRPT,INDEX

GO TO 150

ENDIF

1030 FORMAT (' ERROR ON DATA INPUT FILE (TAPE1), IOSTAT =',I5/

*   4F8.3,3I8)

C

IF (PC.LE.0) THEN

WRITE (*,1040)

GO TO 150

ENDIF

1040 FORMAT (' END OF DATA INPUT (NEGATIVE VALUE READ IN)')

C

WRITE (*,1050) GDLATD,GLOND,PC,GDZED,GDAZD,DELPC,INDO,IERRPT,INDEX

1050 FORMAT (' TAPE 1  ',6F7.2,3I6)

C

C.......+.........+.........+.........+.........+.........+.........+..

C     \/ Start at top of atmosphere (20 km above surface of oblate earth)

C        Coding is relic of past when ISALT was read in

C.......+.........+.........+.........+.........+.........+.........+..

C

ISALT = 0

IF (ISALT.LE.0) SALT = 20.0

IF (ISALT.GT.0) SALT = ISALT

C

KNT = 0

IDELPC = DELPC*1000.0+0.0001

INDXPC = PC*1000.0+0.0001

C

C.......+.........+.........+.........+.........+.........+.........+..

C     For trajectories from Earth

C         convert from Geodetic coordinates to Geocentric coordinates

C                Geodetic   coordinates used for input

C                Geocentric coordinates used for output

C        All calculation are done in Geocentric coordinates!

C     \/ Conversion from Geodetic to Geocentric coordinates

C.......+.........+.........+.........+.........+.........+.........+..

C

CALL GDGC (TCD, TSD)

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ Remember positron of initial point on trajectory

C                 in Geocentric coordinates

C        Y(1) is distance in earth radii from geocenter

C             Start with height above geoid and convert to earth radii

C                   The initial values of Y(1), Y(2), and Y(3) are

C                   calculated in subroutine GDGC

C        Coordinate reference system

C            Y(1) = R      = vertical

C            Y(2) = THETA  = south

C            Y(3) = PHI    = east

C........+.........+.........+.........+.........+.........+.........+..

C

RY2 = Y(2)

RY3 = Y(3)

RY1 = Y(1)

C

GDAZ = GDAZD/RAD

GDZE = GDZED/RAD

TSGDZE = SIN(GDZE)

TCGDZE = COS(GDZE)

TSGDAZ = SIN(GDAZ)

TCGDAZ = COS(GDAZ)

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ Get Y1, Y2, Y3 components in Geodetic coordinates

C         Azimuth is measured clockwise from the north

C         in R, THETA, PHI coordinates, in the THETA-PHI plane

C         The angle is 180 - AZD

C........+.........+.........+.........+.........+.........+.........+..

C

Y1GD =  TCGDZE

Y2GD = -TSGDZE*TCGDAZ

Y3GD =  TSGDZE*TSGDAZ

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ The small angle delta at the point in space between the

C        downward Geodetic   direction and the

C        downward Geocentric direction is given by

C        DELTA = Geocentric co-latitude + Geodetic latitude  - 90 (deg)

C

C        We are looking up

C           The rotation from Geodetic vertical to Geocentric Vertical

C               Is always rotation toward the equator

C

C     \/ Convert from Geodetic to Geocentric Components for Y1, Y2,

C........+.........+.........+.........+.........+.........+.........+..

C

Y1GC =  Y1GD*TCD+Y2GD*TSD

Y2GC = -Y1GD*TSD+Y2GD*TCD

Y3GC =  Y3GD

C

C     WRITE (*,1060) GDZED,GDZE,GDAZD,GDAZ,TSGDZE,TCGDZE,TSGDAZ,TCGDAZ

C     WRITE (*,1060) Y1GD,Y2GD,Y3GD,Y1GC,Y2GC,Y3GC

C1060 FORMAT (' 1050',8F15.5)

C

C........+.........+.........+.........+.........+.........+.........+..

C     ***************************************************

C     Main control of trajectory calculations begins here

C     Trajectories are calculated in subroutine SINGLTJ

C     ***************************************************

C

C     PC     =  rigidity IN GV

C     INDXPC =  index of rigidity in MV (integer)

C     IRSLT  =  trajectory result

C               IRSLT     +1     allowed

C               IRSLT      0     failed

C               IRSLT     -1     re-entrant

C........+.........+.........+.........+.........+.........+.........+..

C

DO 130 NDO = 1, INDO

C

IF (IERRPT.GE.1) WRITE (16,1070) GDLATD,GLOND,KNT,INDO,NDO,

*                    IDELPC,INDXPC,DELPC, PC

C

CALL SINGLTJ (PC,IRSLT,INDXPC,Y1GC,Y2GC,Y3GC)

C

KNT = KNT+1

INDXPC = INDXPC-IDELPC

PC = FLOAT(INDXPC)/1000.0

C

C        +.........+.........+.........+.........+.........+.........+..

C        \/ Check termination conditions

C        +.........+.........+.........+.........+.........+.........+..

C

IF (PC    .LE. 0.0)    GO TO 140

IF (TSTEP .GE. FSTEP)  GO TO 150

C

130 CONTINUE

140 CONTINUE

1070 FORMAT (' 1070 ',2F7.2,5I6,2F6.2)

C

C........+.........+.........+.........+.........+.........+.........+..

C        ************************

C        End of main control loop

C        ************************

C     /\ Go read in next control card

C........+.........+.........+.........+.........+.........+.........+..

C

GO TO 100

C

C........+.........+.........+.........+.........+.........+.........+..

C     ******************************

C     End of trajectory calculations

C     ******************************

C........+.........+.........+.........+.........+.........+.........+..

C

150 CONTINUE

C

WRITE (*, 1120) TSTEP,NTRAJC

WRITE (8, 1120) TSTEP,NTRAJC

1120 FORMAT (//' TOTAL NUMBER OF STEPS        ',F15.0///

*          ' TOTAL NUMBER OF TRAJECTORIES',I15///)

Write (*,1130)

1130 format (' End program TJI95I')

C

STOP

C

C........+.........+.........+.........+.........+.........+.........+..

C     Y(1) is R coordinate         Y(2) is THETA coordinate

C     Y(3) is PHI coordinate       Y(4) is V(R)

C     Y(5) is V(THETA)             Y(6) is V(PHI)

C     F(1) is R dot                F(2) is THETA dot

C     F(3) is PHI dot              F(4) is R dot dot

C     F(5) is THETA dot dot        F(6) is PHI dot dot

C     BR   is B(R)                 BT   is B(THETA)

C     BP   is B(PHI)               B    is magnitude of magnetic field

C........+.........+.........+.........+.........+.........+.........+..

C

C     ierrpt vlu  Program Format Variables printed out

C     IERRPT = 1  "MAIN"   1070  Input to SINGLTJ

C     IERRPT = 1  SINGLTJ  2000  Input to SINGLTJ

C     IERRPT = 2  SINGLTJ  2070  PC,BETA,KBF,RCKBETA,NSTEP,TBETA,Y,H

C     IERRPT = 4  SINGLTJ  2090  Y,F,ACCER,H,NSTEP

C     IERRPT = 3  SINGLTJ  2100  H,HCK,Y(1),DELACC,PC,NSTEP

C     IERRPT = 3  SINGLTJ  2110  H,HCK,Y(1),RFA,   PC,NSTEP

C     IERRPT = 3  SINGLTJ  2120  H,HCK,Y(1),NAMX,F(ICK),ICK,FOLD(ICK),

C                                ICK,PC,STEP

C     IERRPT = 4  SINGLTJ  2130  Y(1),DISCK,PVEL,H,HSNEK,HOLD,NSTEP

C     IERRPT = 4  SINGLTJ  2140  Y(1),DISCK,PVEL,H,      HOLD,NSTEP

C

END

SUBROUTINE GDGC (TCD, TSD)

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ Convert from Geodetic to Geocentric coordinates

C        Adopted from NASA ALLMAG

C         GDLATD = Geodetic   latitude (in degrees)

C         GCLATD = Geocentric latitude (in degrees)

C         GDCLT  = Geodetic co-latitude

C         ERPLSQ is earth radius AT poles   squared = 40408585 (km sq)

C         EREQSQ is earth radius AT equator squared = 40680925 (km sq)

C         ERADPR is earth polar      radius = 6356.774733 (km)

C         ERADER is earth equatorial radius = 6378.160001 (km)

C         ERAD   is earth average    radius = 6371.25     (km)

C         ERADFL is flattening factor = 1.0/298.25

C         ERADFL =  (ERADEQ - factor)/ERADEQ

C         ERECSQ is eccentricity squared = 0.00673966

C         ERECSQ =  EREQSQ/ERPLSQ - 1.0

C........+.........+.........+.........+.........+.........+.........+..

C

CLast Mod 15 Jan 97  Common block SNGLR & SNGLI

C     Mod    Feb 96  Standard reference TJ1V line check

C

C........+.........+.........+.........+.........+.........+.........+..

C     Programmer - Don F. Smart; FORTRAN77

C     Note - The programming adheres to the conventional FORTRAN

C            default standard that variables beginning with

C            'i','j','k','l','m',or 'n' are integer variables

C            Variables beginning with "c" are character variables

C            All other variables are real

C........+........+.........+.........+.........+.........+.........+..

C            Do not mix different type variables in same common block

C            Some computers do not allow this

C........+.........+.........+.........+.........+.........+.........+..

C

IMPLICIT INTEGER (I-N)

IMPLICIT REAL * 8(A-B)

IMPLICIT REAL * 8(D-H)

IMPLICIT REAL * 8(O-Z)

C

C........+.........+.........+.........+.........+.........+.........+..

C

COMMON /WRKVLU/ F(6),Y(6),ERAD,EOMC,VEL,BR,BT,BP,B

COMMON /WRKTSC/ TSY2,TCY2,TSY3,TCY3

COMMON /TRIG/   PI,RAD,PIO2

COMMON /GEOID/  ERADPL, ERECSQ

COMMON /SNGLR/  SALT,DISOUT,GCLATD,GDLATD,GLOND,GDAZD,GDZED,

*                RY1,RY2,RY3,RHT,TSTEP

C

C........+.........+.........+.........+.........+.........+.........+..

C

ERPLSQ = 40408585.0

EREQSQ = 40680925.0

ERADPL = SQRT(ERPLSQ)

ERECSQ = EREQSQ/ERPLSQ - 1.0

C

GDCLT = PIO2-GDLATD/RAD

TSGDCLT = SIN(GDCLT)

TCGDCLT = COS(GDCLT)

ONE = EREQSQ*TSGDCLT*TSGDCLT

TWO = ERPLSQ*TCGDCLT*TCGDCLT

THREE = ONE+TWO

RHO = SQRT(THREE)

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ Get geocentric distance from geocenter in kilometers

C........+.........+.........+.........+.........+.........+.........+..

C

DISTKM = SQRT(SALT*(SALT+2.0*RHO)+(EREQSQ*ONE+ERPLSQ*TWO)/THREE)

C

C........+.........+.........+.........+.........+.........+.........+..

C     TCD and TSD are sine and cosine of the angle the Geodetic vertical

C         must be rotated to form the Geocentric vertical

C........+.........+.........+.........+.........+.........+.........+..

C

TCD = (SALT+RHO)/DISTKM

TSD = (EREQSQ-ERPLSQ)/RHO*TCGDCLT*TSGDCLT/DISTKM

TCY2 = TCGDCLT*TCD-TSGDCLT*TSD

TSY2 = TSGDCLT*TCD+TCGDCLT*TSD

C

Y(2) = ACOS(TCY2)

Y(3) = GLOND/RAD

Y(1) = DISTKM/ERAD

C

GCLATD = (PIO2-Y(2))*RAD

C

C     WRITE (*,1200) GDLATD,GDCLT,TSGDCLT,TCGDCLT,ONE,TWO,THREE,RHO

C1200 FORMAT (' 1200',8F15.5)

C     WRITE (*,1200) DISTKM,TCD,TSD,TCY2,TSY2,GCLATD

C

RETURN

END

SUBROUTINE SINGLTJ (PC,IRSLT,INDXPC,Y1GC,Y2GC,Y3GC)

C

C........+.........+.........+.........+.........+.........+.........+..

C     Cosmic-ray trajectory calculations subroutine

C                calculates cosmic ray trajectory at rigidity  PC

C........+.........+.........+.........+.........+.........+.........+..

C        PC     = rigidity in GV

C        IRSLT  = trajectory result

C        INDXPC = index of rigidity in mv (integer)

C                 Y1GC,Y2GC,Y3GC are initial geocentric coorinates

C........+.........+.........+.........+.........+.........+.........+..

C     \/ Step size optimization & look ahead for potential BETA problems

C             monitor accelerating terms and reduce step length

C                     if large increase occurs

C        Restart at smaller step size if BETA error occurs

C........+.........+.........+.........+.........+.........+.........+..

C     Restrictions: Cannot run over N or S pole; will get BETA blowup

C........+.........+.........+.........+.........+.........+.........+..

CLast Mod 17 Feb 99  if (ymax.lt.6.6) IFATE = 3

C     Mod 18 Jan 97  Patch high latitude beta problem

C     Mod    Jan 97  High latitude step size adjust, introduce AHLT

C     Mod    Jun 96  EDIF limit set to 1.0e-5

C     Mod    Jun 96  IERRPT formats, Boundary and look ahead

C     Mod    FEB 96  standard reference TJ1V (line check 17 Feb)

C........+.........+.........+.........+.........+.........+.........+..

C     Programmer - Don F. Smart; FORTRAN77

C     Note - The programming adheres to the conventional FORTRAN

C            default standard that variables beginning with

C            'i','j','k','l','m',or 'n' are integer variables

C            Variables beginning with "c" are character variables

C            All other variables are real

C........+........+.........+.........+.........+.........+.........+..

C            Do not mix different type variables in same common block

C            Some computers do not allow this

C........+.........+.........+.........+.........+.........+.........+..

C

IMPLICIT INTEGER (I-N)

IMPLICIT REAL * 8(A-B)

IMPLICIT REAL * 8(D-H)

IMPLICIT REAL * 8(O-Z)

C

C........+.........+.........+.........+.........+.........+.........+..

C

COMMON /WRKVLU/ F(6),Y(6),ERAD,EOMC,VEL,BR,BT,BP,B

COMMON /WRKTSC/ TSY2,TCY2,TSY3,TCY3

COMMON /TRIG/   PI,RAD,PIO2

COMMON /GEOID/  ERADPL, ERECSQ

COMMON /SNGLR/  SALT,DISOUT,GCLATD,GDLATD,GLOND,GDAZD,GDZED,

*                RY1,RY2,RY3,RHT,TSTEP

COMMON /SNGLI/  LIMIT,NTRAJC,IERRPT

C

C........+.........+.........+.........+.........+.........+.........+..

C

DIMENSION P(6),Q(6),R(6),S(6),YB(6),FOLD(6),YOLD(6)

C

C........+.........+.........+.........+.........+.........+.........+..

C

CHARACTER*1 CF,CR

CHARACTER*6 CNAME

C

DATA CF,CR / 'F','R'/

DATA CNAME / '  I95 '/                                            ###

C

C........+.........+.........+.........+.........+.........+.........+..

C

IF (IERRPT.GT.0) WRITE (16,2000) PC,INDXPC,RY1,RY2,RY3

2000 FORMAT (' SINGLTJ ',F8.3,I8,3F8.4)

C

BETAST = 2.0

LSTEP = 0

KBF = 0

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ Runge-Kutta constants

C........+.........+.........+.........+.........+.........+.........+..

C

RC1O6 = 1.0/6.0

SR2 = SQRT(2.0)

TMS2O2 = (2.0-SR2)/2.0

TPS2O2 = (2.0+SR2)/2.0

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ Initialize Runge-Kutta variables to zero

C........+.........+.........+.........+.........+.........+.........+..

C

100 DO 110 I = 1, 6

YB(I) = 0.0

S(I) = 0.0

R(I) = 0.0

Q(I) = 0.0

P(I) = 0.0

F(I) = 0.0

110 CONTINUE

C

NMAX = 0

NMIN = 0

NSTEP = 0

NSTEPT = 0

C

TAU = 0.0

TU100 = 0.0

YMAX = RY1

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ Define initial point at start of trajectory

C........+.........+.........+.........+.........+.........+.........+..

C

Y(1) = RY1

Y(2) = RY2

Y(3) = RY3

GRNDKM = (ERADPL/SQRT(1.0-ERECSQ*TSY2SQ))

Y10 = (RHT+GRNDKM)/ERAD

R120KM = (ERAD+120.0)/ERAD

C

C........+.........+.........+.........+.........+.........+.........+..

C     Rigidity = momentum/charge

C                use oxygen 16 as reference isotope

C     Constants used from Handbook of Physics (7-170)

C                         1 amu = 0.931141  GeV

C........+.........+.........+.........+.........+.........+.........+..

C

ANUC = 16.0

ZCHARGE = 8.0

C

EMCSQ = 0.931141

TENG = SQRT((PC*ZCHARGE)**2+(ANUC*EMCSQ)**2)

EOMC = -8987.566297*ZCHARGE/TENG

GMA = SQRT(((PC*ZCHARGE)/(EMCSQ*ANUC))**2+1.0)

BETA = SQRT(1.0-1.0/(GMA*GMA))

PVEL = VEL*BETA

HMAX = 1.0/PVEL

disck = disout - 1.1*hmax*pvel

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ Set max step length ("HMAX") to 1 earth radii

C        PVEL  is particle velocity in earth radii per second

C        DISCK is check for approaching termination boundary

C                 (within 1.1 steps)

C........+.........+.........+.........+.........+.........+.........+..

C

EDIF = BETA*1.0E-4

if (edif.lt.1.0-5)  edif = 1.0e-5

if (beta.lt.0.1)    edif = 1.0e-4

C

Y(4) = BETA*Y1GC

Y(5) = BETA*Y2GC

Y(6) = BETA*Y3GC

C

azd = gdazd

zed = gdzed

IAZ = AZD+0.01

IZE = ZED+0.01

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ Set HSTART to about 1 % of the time to complete one gyro-radius

C                            in a 1 Gauss field

C        H = [(2.0*PI*33.333*PC)/(BETA*C)]/0.01

C            if restart after BETA error, set HCK to small value

C        Introduce   AHLT  to control step size at high lat (beta problem)

C                    HCK   - reduce step size when large acceleration

C                    HOLD  - last step size used

C                    HCNG  - only allow 20% max growth in step size

C                    HSNEK - attempt to approach boundary quickly

C        Problem at z=90 at high lat

C                add zen angle in deg to reduce first step

C........+.........+.........+.........+.........+.........+.........+..

C

PTCY2 = ABS(TCY2)

AHLT = (1.0 + PTCY2)**2

HSTART = 6.0E-6*PC/(BETA*AHLT + ZED*PTCY2)

IF (HSTART.LT.1.0E-6) HSTART = 1.0E-6

HOLD = HSTART

HCK  = HSTART

HCNG = HSTART

C

C     WRITE (16, 2010)  HMAX,HOLD,HCK,HCNG,Y(4),Y(5),Y(6),PVEL, NSTEP

C2010 FORMAT (' 2010 ',18X, 4F9.6, 3F9.4, F9.4,9X,15X,I6)

C

C........+.........+.........+.........+.........+.........+.........+..

C     Start Runge-Kutta

C      \/\/\/\/\/\/\/\/

C        \/\/\/\/\/\/

C          \/\/\/\/

C            \/\/

C             \/

C........+.........+.........+.........+.........+.........+.........+..

C     Change in step size criteria, Aug 97

C            remove cos VxB step size, causes problems in tight loops

C            step size is now only a function of B and BETA

C........+.........+.........+.........+.........+.........+.........+..

C

130 IF (HCK.LT.1.0E-6) HCK = 1.0E-6

CALL FGRAD

HB = 1.6E-5*PC/(B*BETA)

H = HB/BETAST

C

IF (KBF.GT.0)  H=H/(FLOAT(KBF*2))

IF (H.GT.HMAX) H = HMAX

IF (H.GT.HCNG) H = HCNG

IF (H.GT.HCK)  H = HCK

C

DO 140 I = 1, 6

S(I) = H*F(I)

P(I) = 0.5*S(I)-Q(I)

YB(I) = Y(I)

Y(I) = Y(I)+P(I)

R(I) = Y(I)-YB(I)

Q(I) = Q(I)+3.0*R(I)-0.5*S(I)

140 CONTINUE

C

CALL FGRAD

C

DO 150 I = 1, 6

S(I) = H*F(I)

P(I) = TMS2O2*(S(I)-Q(I))

YB(I) = Y(I)

Y(I) = Y(I)+P(I)

R(I) = Y(I)-YB(I)

Q(I) = Q(I)+3.0*R(I)-TMS2O2*S(I)

150 CONTINUE

C

CALL FGRAD

C

DO 160 I = 1, 6

S(I) = H*F(I)

P(I) = TPS2O2*(S(I)-Q(I))

YB(I) = Y(I)

Y(I) = Y(I)+P(I)

R(I) = Y(I)-YB(I)

Q(I) = Q(I)+3.0*R(I)-TPS2O2*S(I)

160 CONTINUE

C

CALL FGRAD

C

DO 170 I = 1, 6

S(I) = H*F(I)

P(I) = RC1O6*(S(I)-2.0*Q(I))

YB(I) = Y(I)

Y(I) = Y(I)+P(I)

R(I) = Y(I)-YB(I)

Q(I) = Q(I)+3.0*R(I)-0.5*S(I)

170 CONTINUE

C

C........+.........+.........+.........+.........+.........+.........+..

C             /\

C            /\/\

C          /\/\/\/\

C        /\/\/\/\/\/\

C      /\/\/\/\/\/\/\/\

c      One Runge-Kutta

c      step completed

C........+.........+.........+.........+.........+.........+.........+..

C

NSTEP = NSTEP+1

NSTEPT = NSTEPT + 1

TAU = TAU+H

HOLD = H

HCNG = H*1.2

HCK  = HCNG

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ Emergency diagnostic printout if desired

C........+.........+.........+.........+.........+.........+.........+..

C     WRITE (16, 2030)     H,  Y(1),Y(2),Y(3),   PVEL,B, NSTEP

C     WRITE (16, 2040)  HB,H,HMAX,HOLD,HCK,HCNG,Y(4),Y(5),Y(6),

C    *                  PVEL,B,NSTEP

C2030 FORMAT (' 2030 ',  9X,    F9.6, 36X,    3F9.5,F9.4,F9.5,18X,I6)

C2040 FORMAT (' 2040 ',        6F9.6,         3F9.5,F9.4,F9.5,18X,I6)

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ Check for altitude less than 100 km

C        if less than 120 km, compute exact altitude above oblate earth

C           and sum time trajectory is below 100 km altitude.

C        set re-entrant altitude at  RHT  km above oblate earth

C               computed from international reference ellipsoid

C     ...+.........+.........+.........+.........+.........+.........+..

C

IF (Y(1).LT.R120KM) THEN

TSY2SQ = SIN(Y(2))**2

GRNDKM = (ERADPL/SQRT(1.0-ERECSQ*TSY2SQ))

R100KM = (100.0+GRNDKM)/ERAD

R120KM = (120.0+GRNDKM)/ERAD

IF (Y(1).LT.R100KM) TU100 = TU100+H

PSALT = Y(1)*ERAD-GRNDKM

Y10 = (RHT+GRNDKM)/ERAD

C

IF (NSTEP.GT.5)  THEN

IF (Y(1).LT.Y10.OR.PSALT.LE.0.0) THEN

IF (IERRPT.GT.2)  WRITE (16, 2045) PSALT, Y(1), Y10

IRT = -1

GO TO 260

ENDIF

ENDIF

ENDIF

2045 FORMAT (' 2045 PSALT,Y(1),Y10',F10.6,1PE14.6,E14.6)

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ Begin error checks

C        (1) Check for unacceptable changes in BETA

C........+.........+.........+.........+.........+.........+.........+..

C

RCKBETA = SQRT(Y(4)*Y(4)+Y(5)*Y(5)+Y(6)*Y(6))

TBETA = BETA-RCKBETA

IF (ABS(TBETA).GT.EDIF) THEN

KBF = KBF+1

BETAST = BETAST + AHLT

EDIF = 2.0*EDIF

IF (RCKBETA.GT.(1.0+EDIF)) THEN

BETAST = BETAST+FLOAT(KBF)*(1.0+AHLT)

WRITE (*,2050) KBF,BETA,RCKBETA

WRITE (*,2060) Y,H,PC,NSTEP

WRITE (16,2050) KBF,BETA,RCKBETA

WRITE (16,2060) Y,H,PC,NSTEP

ENDIF

C

WRITE (16,2070)  PC,BETA,KBF,RCKBETA,NSTEP,TBETA,Y,H

WRITE ( *,2070)  PC,BETA,KBF,RCKBETA,NSTEP,TBETA,Y,H

C

C        +.........+.........+.........+.........+.........+.........+..

C        \/ Check for irrecoverable beta error

C           if KBF > 4, set fate to failed and start next rigidity

C        +.........+.........+.........+.........+.........+.........+..

C

IF (KBF.lt.5) THEN

GO TO 100

ELSE

IRT = 0

PATH = -PVEL*TAU

ISALT = SALT+0.0001

WRITE (*,2080)

GO TO 280

ENDIF

ENDIF

C

2050 FORMAT (' 2050 ','KBF=',i5,5x,' error, the velocity of the ',

*   'particle (BETA) has exceeded the velocity of light'/

*   '          BETA at start of trajectory was ',F10.7/

*   '          BETA now equals                 ',F10.7/

*   '          reduce step size and try again    ')

2060 FORMAT (' 2060 ','Y,H,PC,NSTEP=',8F12.6,I10)

2070 FORMAT (' 2070 ','ERROR, Particle BETA changed;',

*        ' PC = ',F10.6,' GV'/

*     6x,' Beta at start was ',F10.7,17X,'KBF=',I6/

*     6x,' Beta new equals   ',F10.7,10X,'step number',I6/

*     6x,' Beta difference   ',F10.7/

*     6x,' step length reduced and trajectory recalculated '/,

*     6x,'Y=',6F12.6,6X,' H=',F15.7)

2080    FORMAT (' 2080 ','Irrecoverable BETA error problem'/6x,

*      ' Set fate to Failed & make path length negative'/6x,

*      ' Terminate this trajectory & continue with program')

C

C     ...+.........+.........+.........+.........+.........+.........+..

C     \/ Continue status checks

C       (2) Compute composite acceleration

C     ...+.........+.........+.........+.........+.........+.........+..

C

ACCER = SQRT(F(4)*F(4)+F(5)*F(5)+F(6)*F(6))

C

IF (IERRPT.GT.3) WRITE (16,2090) Y, F, ACCER, H, NSTEP

2090 FORMAT (' Y,F,A,H ',f7.4,5f7.3,1x,1pe8.1,5e8.1,1x,e8.1, e9.2,I6)

C

C     ...+.........+.........+.........+.........+.........+.........+..

C     \/ Continue status checks, make adjustment latitude dependant

C        (3) Monitor change in composite acceleration

C            If composite acceleration (new-old) change > 5

C            If composite acceleration (new/old) ratio  > 2

C               change step size to a smaller value

C    ....+.........+.........+.........+.........+.........+.........+..

C

IF (NSTEP.GE.2) THEN

IF (ACCER.GT.ACCOLD) THEN

DELACC = ACCER-ACCOLD

IF (DELACC.GT.5.0)  THEN

HCK = HCK/(1.0+AHLT)

IF (IERRPT.GT.2) WRITE (16,2100)

*                          H,HCK,y(1),DELACC,PC,NSTEP

RFA = ACCER/ACCOLD

IF (RFA.GT.2.0) THEN

HCK = HCK/(1.0+AHLT)

IF (IERRPT.GT.2) WRITE (16,2110)

*                             H,HCK,Y(1),RFA,PC,NSTEP

ENDIF

ENDIF

ENDIF

C

2100    FORMAT (' 2100 ','H-REDUCE',2x,'H=',F8.6,2x,'HCK=',F8.6,2x,

*    'Y(1)=',f7.4,2X,'DELACC=',F6.2,4X,'PC=',F8.3,4x,'NSTEP=',I8)

2110    FORMAT (' 2110 ','H-REDUCE',2x,'H=',F8.6,2x,'HCK=',F8.6,2x,

*    'Y(1)=',f7.4,4X,' RFA=',F6.2,4X,'PC=',F8.3,4x,'NSTEP=',I8)

C

C     ...+.........+.........+.........+.........+.........+.........+..

C     \/ Continue status checks, make adjustment latitude dependant

C        (4) Monitor change in acceleration components

C            If change in any acceleration component is more than

C               a factor of 3, reduce step length

C     ...+.........+.........+.........+.........+.........+.........+..

C

DO 200 ICK = 4, 6

AFOLD = ABS(FOLD(ICK))

IF (AFOLD.GT.3.0) THEN

RFCK = ABS(F(ICK)/AFOLD)

IF (RFCK.GT.3.0) THEN

HCK = HCK/(1.0+AHLT)

IF (IERRPT.GT.2)  THEN

WRITE (16,2120)  H,HCK,Y(1),NMAX,ICK,F(ICK),

&                       ICK,FOLD(ICK),PC,NSTEP

ENDIF

ENDIF

ENDIF

200    CONTINUE

ENDIF

C

2120 FORMAT (' 2120 ','H-reduce',2X,'H=',F8.6,2X,'HCK=',F8.6,2X,

*        'Y(1)=',F7.4,2X,'NAMX=',I4,2X,'F(',I1,')=',F6.2,2X,

*        'FOLD(',I1,')=',F6.2,2X,'PC=',F6.3,2X,'NSTEP=',I6)

C

ACCOLD = ACCER

C

C........+.........+.........+.........+.........+.........+.........+..

C     /\ Error checks complete

C

C     \/ Find if a max or a min has occurred

C........+.........+.........+.........+.........+.........+.........+..

C

IF (NSTEP.GT.1) THEN

IF (YOLD(4).LE.0.0.AND.Y(4).GT.0.0) NMIN = NMIN+1

IF (YOLD(4).GE.0.0.AND.Y(4).LT.0.0) NMAX = NMAX+1

ENDIF

C

IF (Y(1).GT.YMAX) YMAX = Y(1)

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ Check for termination conditions

C         Allowed    - radial distance exceeded disout

C         Failed     - number of steps exceeded

C         Re-entrant - trajectory is below "top" of atmosphere

C

C     ...+.........+.........+.........+.........+.........+.........+..

C     \/ (1) Check for step limit exceeded

C     ...+.........+.........+.........+.........+.........+.........+..

C

IF (NSTEP.GE.LIMIT) THEN

IRT = 0

GO TO 260

ENDIF

C

C     ...+.........+.........+.........+.........+.........+.........+..

C     \/  (2) Check if y(1) within 1.1 max step lengths of disout.

C                   if so, reduce step size and

C                          approach boundary at smaller step

C     ...+.........+.........+.........+.........+.........+.........+..

C

IF (Y(1).GT.DISCK) THEN

DISTR = ABS(DISOUT - Y(1))

HSNEK = DISTR/PVEL

HCNG = HCNG/2.0

HCK  = HCK/2.0

IF (HSNEK .LT. HCNG)  HCNG = HSNEK

IF (HSNEK .LT. HCK)   HCK  = HSNEK

DISCK = DISOUT - DISTR/2.0

IF (DISCK.GE.DISOUT)  THEN

DISCK = 24.999

GO TO  210

ENDIF

IF (H.LT.1.0E-5 .OR. HCK.LT.1.0E-5 .OR. HCNG.LT.1.0E-5)  THEN

H    = 1.0E-5

HCK  = 1.0E-5

HCNG = 1.0E-5

ENDIF

C

IF (IERRPT.GT.3) WRITE (16,2130) Y(1),DISCK,PVEL,H,HSNEK,NSTEP

C

210    IF (Y(1).GT.DISOUT) THEN

IF (H.LE.1.0E-5)  THEN

IRT = 1

GO TO 260

ENDIF

TAU = TAU - H

DO 220 I = 1, 6

Y(I) = YOLD(I)

F(I) = FOLD(I)

220       CONTINUE

endif

GO TO 130

ENDIF

2130 FORMAT (' 2130 ',2X,'Y(1),DISCK,PVEL,H,HSNEK',

*        4X,1PE12.6,4X,E12.6,4X,E12.6,4X,2E9.2,22X,I6)

C

C     +.........+.........+.........+.........+.........+.........+..

c     \/ Have penetrated boundary if you are here.

c          if large step size, go back one step and

c             reduce step length (and adjust "TAU")

C     +.........+.........+.........+.........+.........+.........+..

C

230    IF (Y(1).GT.DISOUT) THEN

C

IF (IERRPT.GT.3)  WRITE (16, 2140) y(1),disck,pvel,H,nstep

C

if (h.lt.1.0e-5 .or. hck.lt.1.0e-5 .or. hcng.lt.1.0e-5)  then

IRT = 1

go to 260

else

hck  = hck/2.0

hcng = hcng/2.0

TAU = TAU - H

DO 240 I = 1, 6

Y(I) = YOLD(I)

F(I) = FOLD(I)

240       CONTINUE

GO TO 130

ENDIF

ENDIF

C

2140 FORMAT (' 2140 ',2x,'y(1),disck,pvel,H',

*        4x,1pe12.6,4x,e12.6,4x,e12.6,4x,e9.2,27x,i6)

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ Store values of  Y  and  F  as  FOLD & YOLD

C........+.........+.........+.........+.........+.........+.........+..

C

DO 250 I = 1, 6

YOLD(I) = Y(I)

FOLD(I) = F(I)

250 CONTINUE

C

GO TO 130

C

C........+.........+.........+.........+.........+.........+.........+..

C*********************************************************************

C        **********          **********          **********

C                  **********          **********

C                           **********

C                 TRAJECTORY COMPLETE IF YOU ARE HERE

C........+.........+.........+.........+.........+.........+.........+..

C

260 CONTINUE

C

IF (Y(1).GE.DISOUT)  IRT = 1

PATH  = PVEL*TAU

ISALT = SALT+0.0001

LSTEP = BETAST - 1.9

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ Write out results

C        IRT     +1     ALLOWED          (FATE = 0)

C        IRT      0     FAILED           (FATE = 2)

C        IRT     -1     RE-ENTRANT       (FATE = 1)

C........+.........+.........+.........+.........+.........+.........+..

C

IF (IRT.GT.0) THEN

TCY2 = COS(Y(2))

TSY2 = SIN(Y(2))

YDA5 = Y(5)*TCY2+Y(4)*TSY2

ATRG1 = Y(4)*TCY2-Y(5)*TSY2

ATRG2 = SQRT(Y(6)*Y(6)+YDA5*YDA5)

FASLAT = 0.0

IF (ATRG1.NE.0.0.AND.ATRG2.NE.0.0) FASLAT =

*                                      ATAN2(ATRG1,ATRG2)*RAD

FASLON = Y(3)*RAD

IF (Y(6).NE.0.0.AND.YDA5.NE.0.0) FASLON = (Y(3)+ATAN2(Y(6),

*                                    YDA5))*RAD

IF (FASLON.LT.0.0)    FASLON = FASLON+360.0

IF (FASLON.GT.360.0)  FASLON = FASLON-360.0

C

WRITE (8,2150) GDLATD,GCLATD,GLOND,IZE,IAZ,PC,FASLAT,FASLON,

*                  PATH,NMAX,NSTEP,TU100,YMAX,LSTEP,SALT,CNAME

C

IFATE = 0

WRITE (7,2160) GDLATD,GLOND,PC,ZED,AZD,ISALT,FASLAT,FASLON,

*                  NSTEP,IFATE,CNAME

ENDIF

2150 FORMAT (2F7.2,F9.2,I5,I4,F10.3,2F8.2,F11.5,I4,I7,F9.5,F9.4,

*        I4,F11.1,1X,A6,13X)

2160 FORMAT (F7.2,F8.2,F9.3,2F6.1,I7,F7.2,F8.2,I7,3X,I3,3X,A6)

C

IF (IRT.LT.0) THEN

RENLAT = (PIO2-Y(2))*RAD

RENLON = Y(3)*RAD

C

WRITE (8,2170) GDLATD,GCLATD,GLOND,IZE,IAZ,PC,CR,CR,PATH,NMAX

*      ,NSTEP,TU100,YMAX,LSTEP,SALT,CNAME,RENLAT,RENLON

C

IFATE = 1

WRITE (7,2180) GDLATD,GLOND,PC,ZED,AZD,ISALT,NSTEP,IFATE,CNAME

ENDIF

2170 FORMAT (2F7.2,F9.2,I5,I4,F10.3,5X,A1,2X,5X,A1,2X,F11.5,I4,I7,

*        F9.5,F9.4,I4,F11.1,1X,A6,F6.1,F7.1)

2180 FORMAT (F7.2,F8.2,F9.3,2F6.1,I7,4X,'R',7X,'R',I9,3X,I3,3X,A6)

C

280 IF (IRT.EQ.0) THEN

C

WRITE (8,2190) GDLATD,GCLATD,GLOND,IZE,IAZ,PC,CF,CF,PATH,

*                  NMAX,NSTEP,TU100,YMAX,LSTEP,SALT,CNAME

C

IFATE = 2

IF (YMAX.LT.6.6) IFATE = 3

WRITE (7,2200) GDLATD,GLOND,PC,ZED,AZD,ISALT,NSTEP,IFATE,CNAME

ENDIF

2190 FORMAT (2F7.2,F9.2,I5,I4,F10.3,5X,A1,2X,5X,A1,2X,F11.5,I4,I7,

*        F9.5,F9.5,I4,F11.1,1X,A6,13X)

2200 FORMAT (F7.2,F8.2,F9.3,2F6.1,I7,4X,'F',7X,'F',I9,3X,I3,3X,A6)

C

NTRAJC = NTRAJC+1

TSTEP = TSTEP+FLOAT(NSTEP)

C

C     ...+.........+.........+.........+.........+.........+.........+..

C     \/ Comment out to reduce IO

C     ...+.........+.........+.........+.........+.........+.........+..

C

C     WRITE (*,2210) PC, ZED, AZD, NSTEP, IFATE

C2210 FORMAT (1H+, 22X, 3F7.2,7x,2I6)

C

IRSLT = IRT

RETURN

END

SUBROUTINE FGRAD

C

C........+.........+.........+.........+.........+.........+.........+..

C     Mod    Feb 96  standard reference TJ1V (line check 17 Feb)

C     Mod 27 Jan 1999  Change MAGNEW to NEWMAG95                        ###

C........+.........+.........+.........+.........+.........+.........+..

C     Programmer   -  Don F. Smart; FORTRAN77

C     Note -  The programming adheres to the conventional FORTRAN

C             default standard that variables beginning with

C            'i','j','k','l','m',or 'n' are integer variables

C             Variables beginning with "c" are character variables

C             All other variables are real

C........+.........+.........+.........+.........+.........+.........+..

C        Do not mix different type variables in same common block

C           Some computers do not allow this

C........+.........+.........+.........+.........+.........+.........+..

C

IMPLICIT INTEGER (I-N)

IMPLICIT REAL * 8(A-B)

IMPLICIT REAL * 8(D-H)

IMPLICIT REAL * 8(O-Z)

C

C........+.........+.........+.........+.........+.........+.........+..

C

COMMON /WRKVLU/ F(6),Y(6),ERAD,EOMC,VEL,BR,BT,BP,B

COMMON /WRKTSC/ TSY2,TCY2,TSY3,TCY3

C

C........+.........+.........+.........+.........+.........+.........+..

C

F(1) = VEL*Y(4)

F(2) = VEL*Y(5)/Y(1)

TSY2 = SIN(Y(2))

TCY2 = COS(Y(2))

F(3) = VEL*Y(6)/(Y(1)*TSY2)

SQY6 = Y(6)*Y(6)/Y(1)

Y5OY1 = Y(5)/Y(1)

TAY2 = TSY2/TCY2

CALL MAGNEW95                                                     ###

F(4) = EOMC*(Y(5)*BP-Y(6)*BT)+VEL*(Y(5)*Y5OY1+SQY6)

F(5) = EOMC*(Y(6)*BR-Y(4)*BP)+VEL*(SQY6/TAY2-Y5OY1*Y(4))

F(6) = EOMC*(Y(4)*BT-Y(5)*BR)-VEL*((Y5OY1*Y(6))/TAY2+Y(4)*Y(6)/

*       Y(1))

RETURN

C

C........+.........+.........+.........+.........+.........+.........+..

C     Y(1) is R coordinate         Y(2) is THETA coordinate

C     Y(3) is PHI coordinate       Y(4) is V(R)

C     Y(5) is V(THETA)             Y(6) is V(PHI)

C     F(1) is R dot                F(2) is THETA dot

C     F(3) is PHI dot              F(4) is R dot dot

C     F(5) is THETA dot dot        F(6) is PHI dot dot

C     BR   is B(R)                 BT   is B(THETA)

C     BP   is B(PHI)               B    is magnitude of magnetic field

C........+.........+.........+.........+.........+.........+.........+..

C

END

SUBROUTINE MAGNEW95                                               ###

C

C........+.........+.........+.........+.........+.........+.........+..

C     Compute Magnetic field

C     Derived from NASA (NSSDC) routine NEWMAG version of December 1965

C             modified for 10 order field

C     Coefficients for IGRF 1995 loaded into this subroutine            ###

C     Coefficients obtained from program CNGMAGN

C........+.........+.........+.........+.........+.........+.........+..

CLast Mod 27 Jan 1999  IGRF 95 coefficients                             ###

C     Mod    Feb 1996  standard reference TJ1V (line check 17 Feb)

C     Mod    Nov 1980  for arguments in labeled common

C........+.........+.........+.........+.........+.........+.........+..

C........+.........+.........+.........+.........+.........+.........+..

C     Programmer - Don F. Smart; FORTRAN77

C     Note - The programming adheres to the conventional FORTRAN

C            default standard that variables beginning with

C            'i','j','k','l','m',or 'n' are integer variables

C            Variables beginning with "c" are character variables

C            All other variables are real

C........+........+.........+.........+.........+.........+.........+..

C            Do not mix different type variables in same common block

C            Some computers do not allow this

C........+.........+.........+.........+.........+.........+.........+..

C

IMPLICIT INTEGER (I-N)

IMPLICIT REAL * 8(A-B)

IMPLICIT REAL * 8(D-H)

IMPLICIT REAL * 8(O-Z)

C

C........+.........+.........+.........+.........+.........+.........+..

C

COMMON /WRKVLU/ F(6),Y(6),ERAD,EOMC,VEL,BR,BT,BP,B

COMMON /WRKTSC/ TSY2,TCY2,TSY3,TCY3

C

C........+.........+.........+.........+.........+.........+.........+..

C

DIMENSION     G(11,11),BM(11)

C

C........+.........+.........+.........+.........+.........+.........+..

C

C     \/ Load in data constants if this is the first time called

C        otherwise, skip to evaluation of magnetic field

C          designed to drop high order terms if contribution

C                   would be less then "BERR"

C           also designed so the maximum order of expansion

C               can be specified

C........+.........+.........+.........+.........+.........+.........+..

C

IF (JDATA.EQ.77) GO TO 120

C

C........+.........+.........+.........+.........+.........+.........+..

C     Gauss normalized Schmidt coefficients ordered for fast computation

C

Cards for FORTRAN

C     1995.00     Coef in CNGMAG format                             IGRF95

DATA(G(N, 1),N=1,11)/   0.000000E+00

c,   0.296820E+05,   0.329550E+04,  -0.332250E+04,  -0.411687E+04

c,   0.165375E+04,  -0.952875E+03,  -0.209137E+04,  -0.120656E+04

c,  -0.379844E+03,

c   0.541277E+03/

DATA(G(N, 2),N=1,11)/  -0.531800E+04

c,   0.178900E+04,  -0.532432E+04,   0.694430E+04,  -0.432758E+04

c,  -0.357864E+04,  -0.120980E+04,   0.237646E+04,  -0.268125E+03

c,  -0.114663E+04,

c   0.973144E+03/

DATA(G(N, 3),N=1,11)/   0.408071E+04

c,   0.368061E+03,  -0.145925E+04,  -0.241868E+04,  -0.113872E+04

c,  -0.182140E+04,  -0.971375E+03,  -0.289608E+02,   0.560824E+02

c,  -0.108650E+03,

c  -0.421384E+03/

DATA(G(N, 4),N=1,11)/   0.805270E+03

c,  -0.584820E+03,   0.320971E+03,  -0.607948E+03,   0.880585E+03

c,   0.574158E+03,   0.171361E+04,  -0.593873E+03,   0.372776E+03

c,   0.995794E+03,

c   0.826402E+03/

DATA(G(N, 5),N=1,11)/  -0.144990E+04

c,   0.907844E+03,  -0.204982E+03,   0.222593E+03,  -0.857832E+02

c,   0.370495E+03,  -0.109137E+02,  -0.493957E+02,   0.374307E+03

c,  -0.507382E+03,

c   0.233742E+03/

DATA(G(N, 6),N=1,11)/  -0.447330E+03

c,  -0.120658E+04,   0.715344E+03,   0.141986E+03,  -0.694545E+02

c,   0.182406E+02,  -0.395558E+02,  -0.493957E+02,  -0.593223E+02

c,   0.134764E+03,

c  -0.295662E+03/

DATA(G(N, 7),N=1,11)/   0.302450E+03

c,  -0.115071E+04,  -0.667509E+03,   0.311041E+03,  -0.930726E+01

c,  -0.188074E+02,   0.631392E+02,  -0.242182E+02,  -0.343261E+02

c,   0.347959E+02,

c  -0.123960E+03/

DATA(G(N, 8),N=1,11)/   0.273116E+04

c,   0.724020E+03,  -0.614352E+02,  -0.271676E+03,  -0.987915E+02

c,   0.557020E+02,   0.194178E+01,   0.129452E+01,   0.000000E+00

c,  -0.527347E+02,

c  -0.200432E+02/

DATA(G(N, 9),N=1,11)/  -0.804375E+03

c,   0.112165E+04,  -0.289937E+03,   0.561461E+03,  -0.177967E+03

c,  -0.686523E+02,   0.426161E+02,   0.626707E+01,   0.438695E+01

c,   0.000000E+00,

c  -0.245478E+02/

DATA(G(N,10),N=1,11)/   0.242067E+04

c,  -0.162975E+04,  -0.912811E+03,   0.394630E+03,   0.235837E+03

c,  -0.156581E+03,  -0.527347E+02,   0.206718E+02,  -0.609049E+00

c,   0.365430E+01,

c  -0.796435E+01/

DATA(G(N,11),N=1,11)/  -0.486572E+03

c,  -0.210692E+03,  -0.495841E+03,  -0.701225E+03,   0.295662E+03

c,   0.000000E+00,   0.400864E+02,  -0.245478E+02,   0.265478E+01

c,   0.356177E+01,

c   0.000000E+00/

DATA JMAG/ 0/,MGNMAX/    11/,GSUM/  -0.885846E+05/

DATA BM/   0.100078E+06

c,   0.100078E+06,   0.396633E+05,   0.253449E+05,   0.134069E+05

c,   0.684114E+04,   0.360156E+04,   0.197007E+04,   0.913524E+03

c,   0.489229E+03,

c   0.152640E+03/

C     1995.00     Coef in CNGMAG format                             IGRF95

C

C   ******************************************************************

C   *    The array G contains Gauss normalized Schmidt coefficients

c   *    the array G contains both the G and H coefficients

C   *     G(1,1) = 0.0

C   *Schmidt G(N,M) corresponds to -G(NN+1,MM+1) Gauss normalized coef

C   *Schmidt H(N,M) corresponds to -G( MI ,NN+1) Gauss normalized coef

C   *                            where MI = M

C   ******************************************************************

C

IF (GMSUM.EQ.0) GO TO 110

P22 = 0.

BERR = 0.0001

AR = 0.

DO 100 L = 1, MGNMAX

DO 100 M = 1, MGNMAX

AR = AR+1.

P22 = P22+AR*G(M,L)

100 CONTINUE

GMSUM = (GMSUM-P22)/GMSUM

C

C........+.........+.........+.........+.........+.........+.........+..

C**** \/ Note following print and stop statements

C........+.........+.........+.........+.........+.........+.........+..

C

IF (ABS(GMSUM).GT.1.E-4) THEN

WRITE (*, 2200) GMSUM

WRITE (7, 2200) GMSUM

WRITE (8, 2200) GMSUM

STOP

ENDIF

2200 FORMAT (' DATA WRONG IN MAGNEW',E15.6)

C

110 CONTINUE

C

GMSUM = 0.

JDATA = 77

C

120 CONTINUE

P21 = TCY2

P22 = TSY2

AR = 1.0/Y(1)

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ N= 2

C........+.........+.........+.........+.........+.........+.........+..

C

DP22 = P21

TSY3 = SIN(Y(3))

TCY3 = COS(Y(3))

TSP2 = TSY3

TCP2 = TCY3

DP21 = -P22

AOR = AR*AR*AR

RC2 = G(2,2)*TCP2+G(1,2)*TSP2

BR = -(AOR+AOR)*(G(2,1)*P21+RC2*P22)

BT = AOR*(G(2,1)*DP21+RC2*DP22)

BP = AOR*(G(1,2)*TCP2-G(2,2)*TSP2)*P22

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ N = 3

C........+.........+.........+.........+.........+.........+.........+..

C

IF (MGNMAX.LT.3) GO TO 130

AOR = AOR*AR

ERR = BERR*SQRT((BP/P22)**2+BR**2+BT**2)

IF ((BM(3)*AOR).LT.ERR) GO TO 130

TSP3 = (TSP2+TSP2)*TCP2

TCP3 = (TCP2+TSP2)*(TCP2-TSP2)

P31 = P21*P21-0.333333333

P32 = P21*P22

P33 = P22*P22

DP31 = -P32-P32

DP32 = P21*P21-P33

DP33 = -DP31

RC2 = G(3,2)*TCP2+G(1,3)*TSP2

RC3 = G(3,3)*TCP3+G(2,3)*TSP3

BR = BR-3.0*AOR*(G(3,1)*P31+RC2*P32+RC3*P33)

BT = BT+AOR*(G(3,1)*DP31+RC2*DP32+RC3*DP33)

BP = BP-AOR*((G(3,2)*TSP2-G(1,3)*TCP2)*P32+

*     2.0*(G(3,3)*TSP3-G(2,3)*TCP3)*P33)

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ N = 4

C........+.........+.........+.........+.........+.........+.........+..

C

IF (MGNMAX.LT.4) GO TO 130

AOR = AOR*AR

IF ((BM(4)*AOR).LT.ERR) GO TO 130

TSP4 = TSP2*TCP3+TCP2*TSP3

TCP4 = TCP2*TCP3-TSP2*TSP3

P41  = P21*P31-0.26666666*P21

DP41 = P21*DP31+DP21*P31-0.26666666*DP21

P42  = P21*P32-0.20000000*P22

DP42 = P21*DP32+DP21*P32-0.20000000*DP22

P43  = P21*P33

DP43 = P21*DP33+DP21*P33

P44  = P22*P33

DP44 = 3.0*P43

RC2 = G(4,2)*TCP2+G(1,4)*TSP2

RC3 = G(4,3)*TCP3+G(2,4)*TSP3

RC4 = G(4,4)*TCP4+G(3,4)*TSP4

BR = BR-4.0*AOR*(G(4,1)*P41+RC2*P42+RC3*P43+RC4*P44)

BT = BT+AOR*(G(4,1)*DP41+RC2*DP42+RC3*DP43+RC4*DP44)

BP = BP-AOR*((G(4,2)*TSP2-G(1,4)*TCP2)*P42+

*     2.0*(G(4,3)*TSP3-G(2,4)*TCP3)*P43+

*     3.0*(G(4,4)*TSP4-G(3,4)*TCP4)*P44)

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ N = 5

C........+.........+.........+.........+.........+.........+.........+..

C

IF (MGNMAX.LT.5) GO TO 130

AOR = AOR*AR

IF ((BM(5)*AOR).LT.ERR) GO TO 130

TSP5 = (TSP3+TSP3)*TCP3

TCP5 = (TCP3+TSP3)*(TCP3-TSP3)

P51  = P21*P41-0.25714285*P31

DP51 = P21*DP41+DP21*P41-0.25714285*DP31

P52  = P21*P42-0.22857142*P32

DP52 = P21*DP42+DP21*P42-0.22857142*DP32

P53  = P21*P43-0.14285714*P33

DP53 = P21*DP43+DP21*P43-0.14285714*DP33

P54  = P21*P44

DP54 = P21*DP44+DP21*P44

P55  = P22*P44

DP55 = 4.0*P54

RC2 = G(5,2)*TCP2+G(1,5)*TSP2

RC3 = G(5,3)*TCP3+G(2,5)*TSP3

RC4 = G(5,4)*TCP4+G(3,5)*TSP4

RC5 = G(5,5)*TCP5+G(4,5)*TSP5

BR = BR-5.0*AOR*(G(5,1)*P51+RC2*P52+RC3*P53+RC4*P54+RC5*P55)

BT = BT+AOR*(G(5,1)*DP51+RC2*DP52+RC3*DP53+RC4*DP54+RC5*DP55)

BP = BP-AOR*((G(5,2)*TSP2-G(1,5)*TCP2)*P52+2.0*(G(5,3)*TSP3-

*     G(2,5)*TCP3)*P53+3.0*(G(5,4)*TSP4-

*     G(3,5)*TCP4)*P54+4.0*(G(5,5)*TSP5-

*     G(4,5)*TCP5)*P55)

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ N = 6

C........+.........+.........+.........+.........+.........+.........+..

C

IF (MGNMAX.LT.6) GO TO 130

AOR = AOR*AR

IF ((BM(6)*AOR).LT.ERR) GO TO 130

TSP6 = TSP2*TCP5+TCP2*TSP5

TCP6 = TCP2*TCP5-TSP2*TSP5

P61 =  P21*P51-0.25396825*P41

DP61 = P21*DP51+DP21*P51-0.25396825*DP41

P62 =  P21*P52-0.23809523*P42

DP62 = P21*DP52+DP21*P52-0.23809523*DP42

P63 =  P21*P53-0.19047619*P43

DP63 = P21*DP53+DP21*P53-0.19047619*DP43

P64 =  P21*P54-0.11111111*P44

DP64 = P21*DP54+DP21*P54-0.11111111*DP44

P65 =  P21*P55

DP65 = P21*DP55+DP21*P55

P66 =  P22*P55

DP66 = 5.0*P65

RC2 = G(6,2)*TCP2+G(1,6)*TSP2

RC3 = G(6,3)*TCP3+G(2,6)*TSP3

RC4 = G(6,4)*TCP4+G(3,6)*TSP4

RC5 = G(6,5)*TCP5+G(4,6)*TSP5

RC6 = G(6,6)*TCP6+G(5,6)*TSP6

BR = BR-6.0*AOR*(G(6,1)*P61+RC2*P62+RC3*P63+RC4*P64+RC5*P65

*       +RC6*P66)

BT = BT+AOR*(G(6,1)*DP61+RC2*DP62+RC3*DP63+RC4*DP64+RC5*DP65

*       +RC6*DP66)

BP = BP-AOR*((G(6,2)*TSP2-G(1,6)*TCP2)*P62+2.0*(G(6,3)*TSP3

*       -G(2,6)*TCP3)*P63+3.0*(G(6,4)*TSP4

*       -G(3,6)*TCP4)*P64+4.0*(G(6,5)*TSP5

*       -G(4,6)*TCP5)*P65+5.0*(G(6,6)*TSP6-G(5,6)*TCP6)*P66)

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ N = 7

C........+.........+.........+.........+.........+.........+.........+..

C

IF (MGNMAX.LT.7) GO TO 130

AOR = AOR*AR

IF ((BM(7)*AOR).LT.ERR) GO TO 130

TSP7 = (TSP4+TSP4)*TCP4

TCP7 = (TCP4+TSP4)*(TCP4-TSP4)

P71  = P21*P61-0.25252525*P51

DP71 = P21*DP61+DP21*P61-0.25252525*DP51

P72  = P21*P62-0.24242424*P52

DP72 = P21*DP62+DP21*P62-0.24242424*DP52

P73  = P21*P63-0.21212121*P53

DP73 = P21*DP63+DP21*P63-0.21212121*DP53

P74  = P21*P64-0.16161616*P54

DP74 = P21*DP64+DP21*P64-0.16161616*DP54

P75  = P21*P65-0.09090909*P55

DP75 = P21*DP65+DP21*P65-0.09090909*DP55

P76  = P21*P66

DP76 = P21*DP66+DP21*P66

P77  = P22*P66

DP77 = 6.0*P76

RC2  = G(7,2)*TCP2+G(1,7)*TSP2

RC3 = G(7,3)*TCP3+G(2,7)*TSP3

RC4 = G(7,4)*TCP4+G(3,7)*TSP4

RC5 = G(7,5)*TCP5+G(4,7)*TSP5

RC6 = G(7,6)*TCP6+G(5,7)*TSP6

RC7 = G(7,7)*TCP7+G(6,7)*TSP7

BR = BR-7.0*AOR*(G(7,1)*P71+RC2*P72+RC3*P73+RC4*P74+RC5*P75

*       +RC6*P76+RC7*P77)

BT = BT+AOR*(G(7,1)*DP71+RC2*DP72+RC3*DP73+RC4*DP74+RC5*DP75

*       +RC6*DP76+RC7*DP77)

BP = BP-AOR*((G(7,2)*TSP2-G(1,7)*TCP2)*P72+2.0*(G(7,3)*TSP3

*       -G(2,7)*TCP3)*P73+3.0*(G(7,4)*TSP4

*       -G(3,7)*TCP4)*P74+4.0*(G(7,5)*TSP5

*       -G(4,7)*TCP5)*P75+5.0*(G(7,6)*TSP6

*       -G(5,7)*TCP6)*P76+6.0*(G(7,7)*TSP7-G(6,7)*TCP7)*P77)

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ N = 8

C........+.........+.........+.........+.........+.........+.........+..

C

IF (MGNMAX.LT.8) GO TO 130

AOR = AOR*AR

IF ((BM(8)*AOR).LT.ERR) GO TO 130

TSP8 = TSP2*TCP7+TCP2*TSP7

TCP8 = TCP2*TCP7-TSP2*TSP7

P81  = P21*P71-0.25174825*P61

DP81 = P21*DP71+DP21*P71-0.25174825*DP61

P82  = P21*P72-0.24475524*P62

DP82 = P21*DP72+DP21*P72-0.24475524*DP62

P83  = P21*P73-0.22377622*P63

DP83 = P21*DP73+DP21*P73-0.22377622*DP63

P84  = P21*P74-0.18881118*P64

DP84 = P21*DP74+DP21*P74-0.18881118*DP64

P85  = P21*P75-0.13986013*P65

DP85 = P21*DP75+DP21*P75-0.13986013*DP65

P86  = P21*P76-0.07692307*P66

DP86 = P21*DP76+DP21*P76-0.07692307*DP66

P87  = P21*P77

DP87 = P21*DP77+DP21*P77

P88  = P22*P77

DP88 = 7.0*P87

RC2 = G(8,2)*TCP2+G(1,8)*TSP2

RC3 = G(8,3)*TCP3+G(2,8)*TSP3

RC4 = G(8,4)*TCP4+G(3,8)*TSP4

RC5 = G(8,5)*TCP5+G(4,8)*TSP5

RC6 = G(8,6)*TCP6+G(5,8)*TSP6

RC7 = G(8,7)*TCP7+G(6,8)*TSP7

RC8 = G(8,8)*TCP8+G(7,8)*TSP8

BR = BR-8.0*AOR*(G(8,1)*P81+RC2*P82+RC3*P83+RC4*P84+RC5*P85

*       +RC6*P86+RC7*P87+RC8*P88)

BT = BT+AOR*(G(8,1)*DP81+RC2*DP82+RC3*DP83+RC4*DP84+RC5*DP85

*       +RC6*DP86+RC7*DP87+RC8*DP88)

BP = BP-AOR*((G(8,2)*TSP2-G(1,8)*TCP2)*P82

*       +2.0*(G(8,3)*TSP3-G(2,8)*TCP3)*P83

*       +3.0*(G(8,4)*TSP4-G(3,8)*TCP4)*P84

*       +4.0*(G(8,5)*TSP5-G(4,8)*TCP5)*P85

*       +5.0*(G(8,6)*TSP6-G(5,8)*TCP6)*P86

*       +6.0*(G(8,7)*TSP7-G(6,8)*TCP7)*P87

*       +7.0*(G(8,8)*TSP8-G(7,8)*TCP8)*P88)

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ N = 9

C........+.........+.........+.........+.........+.........+.........+..

C

IF (MGNMAX.LT.9) GO TO 130

AOR = AOR*AR

IF ((BM(9)*AOR).LT.ERR) GO TO 130

TSP9 = (TSP5+TSP5)*TCP5

TCP9 = (TCP5+TSP5)*(TCP5-TSP5)

P91  = P21*P81-0.25128205*P71

DP91 = P21*DP81+DP21*P81-0.25128205*DP71

P92  = P21*P82-0.24615384*P72

DP92 = P21*DP82+DP21*P82-0.24615384*DP72

P93  = P21*P83-0.23076923*P73

DP93 = P21*DP83+DP21*P83-0.23076923*DP73

P94  = P21*P84-0.20512820*P74

DP94 = P21*DP84+DP21*P84-0.20512820*DP74

P95  = P21*P85-0.16923076*P75

DP95 = P21*DP85+DP21*P85-0.16923076*DP75

P96  = P21*P86-0.12307692*P76

DP96 = P21*DP86+DP21*P86-0.12307692*DP76

P97  = P21*P87-0.06666666*P77

DP97 = P21*DP87+DP21*P87-0.06666666*DP77

P98  = P21*P88

DP98 = P21*DP88+DP21*P88

P99  = P22*P88

DP99 = 8.0*P98

RC2 = G(9,2)*TCP2+G(1,9)*TSP2

RC3 = G(9,3)*TCP3+G(2,9)*TSP3

RC4 = G(9,4)*TCP4+G(3,9)*TSP4

RC5 = G(9,5)*TCP5+G(4,9)*TSP5

RC6 = G(9,6)*TCP6+G(5,9)*TSP6

RC7 = G(9,7)*TCP7+G(6,9)*TSP7

RC8 = G(9,8)*TCP8+G(7,9)*TSP8

RC9 = G(9,9)*TCP9+G(8,9)*TSP9

BR = BR-9.0*AOR*(G(9,1)*P91+RC2*P92+RC3*P93+RC4*P94+RC5*P95

*       +RC6*P96+RC7*P97+RC8*P98+RC9*P99)

BT = BT+AOR*(G(9,1)*DP91+RC2*DP92+RC3*DP93+RC4*DP94+RC5*DP95

*       +RC6*DP96+RC7*DP97+RC8*DP98+RC9*DP99)

BP = BP-AOR*((G(9,2)*TSP2-G(1,9)*TCP2)*P92+2.0*(G(9,3)*TSP3

*       -G(2,9)*TCP3)*P93+3.0*(G(9,4)*TSP4

*       -G(3,9)*TCP4)*P94+4.0*(G(9,5)*TSP5

*       -G(4,9)*TCP5)*P95+5.0*(G(9,6)*TSP6

*       -G(5,9)*TCP6)*P96+6.0*(G(9,7)*TSP7

*       -G(6,9)*TCP7)*P97+7.0*(G(9,8)*TSP8

*       -G(7,9)*TCP8)*P98+8.0*(G(9,9)*TSP9-G(8,9)*TCP9)*P99)

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ N = 10

C........+.........+.........+.........+.........+.........+.........+..

C

IF (MGNMAX.LT.10) GO TO 130

AOR = AOR*AR

IF ((BM(10)*AOR).LT.ERR) GO TO 130

TSP10  = TSP2*TCP9+TCP2*TSP9

TCP10  = TCP2*TCP9-TSP2*TSP9

P101   = P21*P91-0.25098039*P81

DP101  = P21*DP91+DP21*P91-0.25098039*DP81

P102   = P21*P92-0.24705882*P82

DP102  = P21*DP92+DP21*P92-0.24705882*DP82

P103   = P21*P93-0.23529411*P83

DP103  = P21*DP93+DP21*P93-0.23529411*DP83

P104   = P21*P94-0.21568627*P84

DP104  = P21*DP94+DP21*P94-0.21568627*DP84

P105   = P21*P95-0.18823529*P85

DP105  = P21*DP95+DP21*P95-0.18823529*DP85

P106   = P21*P96-0.15294117*P86

DP106  = P21*DP96+DP21*P96-0.15294117*DP86

P107   = P21*P97-0.10980392*P87

DP107  = P21*DP97+DP21*P97-0.10980392*DP87

P108   = P21*P98-0.05882352*P88

DP108  = P21*DP98+DP21*P98-0.05882352*DP88

P109   = P21*P99

DP109  = P21*DP99+DP21*P99

P1010  = P22*P99

DP1010 = 9.0*P109

RC2 = G(10,2)*TCP2+G(1,10)*TSP2

RC3 = G(10,3)*TCP3+G(2,10)*TSP3

RC4 = G(10,4)*TCP4+G(3,10)*TSP4

RC5 = G(10,5)*TCP5+G(4,10)*TSP5

RC6 = G(10,6)*TCP6+G(5,10)*TSP6

RC7 = G(10,7)*TCP7+G(6,10)*TSP7

RC8 = G(10,8)*TCP8+G(7,10)*TSP8

RC9 = G(10,9)*TCP9+G(8,10)*TSP9

RC10 = G(10,10)*TCP10+G(9,10)*TSP10

BR = BR-10.0*AOR*(G(10,1)*P101+RC2*P102+RC3*P103+RC4*P104

*       +RC5*P105+RC6*P106+RC7*P107+RC8*P108+RC9*P109+RC10*P1010)

BT = BT+AOR*(G(10,1)*DP101+RC2*DP102+RC3*DP103+RC4*DP104

*       +RC5*DP105+RC6*DP106+RC7*DP107+RC8*DP108+RC9*DP109

*       +RC10*DP1010)

BP = BP-AOR*((G(10,2)*TSP2-G(1,10)*TCP2)*P102+2.0*(G(10,3)*TSP3

*       -G(2,10)*TCP3)*P103+3.0*(G(10,4)*TSP4

*       -G(3,10)*TCP4)*P104+4.0*(G(10,5)*TSP5

*       -G(4,10)*TCP5)*P105+5.0*(G(10,6)*TSP6

*       -G(5,10)*TCP6)*P106+6.0*(G(10,7)*TSP7

*       -G(6,10)*TCP7)*P107+7.0*(G(10,8)*TSP8

*       -G(7,10)*TCP8)*P108+8.0*(G(10,9)*TSP9

*       -G(8,10)*TCP9)*P109+9.0*(G(10,10)*TSP10

*       -G(9,10)*TCP10)*P1010)

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ N = 11

C........+.........+.........+.........+.........+.........+.........+..

C

IF (MGNMAX.LT.11) GO TO 130

AOR = AOR*AR

IF ((BM(11)*AOR).LT.ERR) GO TO 130

TSP11  = (TSP6+TSP6)*TCP6

TCP11  = (TCP6+TSP6)*(TCP6-TSP6)

P111   = P21*P101-0.25077399*P91

DP111  = P21*DP101+DP21*P101-0.25077399*DP91

P112   = P21*P102-0.24767801*P92

DP112  = P21*DP102+DP21*P102-0.24767801*DP92

P113   = P21*P103-0.23839009*P93

DP113  = P21*DP103+DP21*P103-0.23839009*DP93

P114   = P21*P104-0.22291021*P94

DP114  = P21*DP104+DP21*P104-0.22291021*DP94

P115   = P21*P105-0.20123839*P95

DP115  = P21*DP105+DP21*P105-0.20123839*DP95

P116   = P21*P106-0.17337461*P96

DP116  = P21*DP106+DP21*P106-0.17337461*DP96

P117   = P21*P107-0.13931888*P97

DP117  = P21*DP107+DP21*P107-0.13931888*DP97

P118   = P21*P108-0.09907120*P98

DP118  = P21*DP108+DP21*P108-0.09907120*DP98

P119   = P21*P109-0.05263157*P99

DP119  = P21*DP109+DP21*P109-0.05263157*DP99

P1110  = P21*P1010

DP1110 = P21*DP1010+DP21*P1010

P1111  = P22*P1010

DP1111 = 10.0*P1110

RC2  = G(11,2)*TCP2+G(1,11)*TSP2

RC3  = G(11,3)*TCP3+G(2,11)*TSP3

RC4  = G(11,4)*TCP4+G(3,11)*TSP4

RC5  = G(11,5)*TCP5+G(4,11)*TSP5

RC6  = G(11,6)*TCP6+G(5,11)*TSP6

RC7  = G(11,7)*TCP7+G(6,11)*TSP7

RC8  = G(11,8)*TCP8+G(7,11)*TSP8

RC9  = G(11,9)*TCP9+G(8,11)*TSP9

RC10 = G(11,10)*TCP10+G(9,11)*TSP10

RC11 = G(11,11)*TCP11+G(10,11)*TSP11

BR = BR-11.0*AOR*(G(11,1)*P111+RC2*P112+RC3*P113+RC4*P114

*       +RC5*P115+RC6*P116+RC7*P117+RC8*P118+RC9*P119+RC10*P1110

*       +RC11*P1111)

BT = BT+AOR*(G(11,1)*DP111+RC2*DP112+RC3*DP113+RC4*DP114

*       +RC5*DP115+RC6*DP116+RC7*DP117+RC8*DP118+RC9*DP119

*       +RC10*DP1110+RC11*DP1111)

BP = BP-AOR*((G(11,2)*TSP2-G(1,11)*TCP2)*P112+2.0*(G(11,3)*TSP3

*       -G(2,11)*TCP3) *P113 + 3.0 *(G(11,4)*TSP4

*       -G(3,11)*TCP4) *P114 + 4.0 *(G(11,5)*TSP5

*       -G(4,11)*TCP5) *P115 + 5.0 *(G(11,6)*TSP6

*       -G(5,11)*TCP6) *P116 + 6.0 *(G(11,7)*TSP7

*       -G(6,11)*TCP7) *P117 + 7.0 *(G(11,8)*TSP8

*       -G(7,11)*TCP8) *P118 + 8.0 *(G(11,9)*TSP9

*       -G(8,11)*TCP9) *P119 + 9.0 *(G(11,10)*TSP10

*       -G(9,11)*TCP10)*P1110+10.0*(G(11,11)*TSP11

*       -G(10,11)*TCP11)*P1111)

C

C........+.........+.........+.........+.........+.........+.........+..

C     \/ Convert to units of Gauss

C........+.........+.........+.........+.........+.........+.........+..

C

130 BP = BP/P22*1.E-5

BT = BT*1.E-5

BR = BR*1.E-5

B = SQRT(BR*BR+BT*BT+BP*BP)

RETURN

C

C........+.........+.........+.........+.........+.........+.........+..

C     Y(1) is R coordinate         Y(2) is THETA coordinate

C     Y(3) is PHI coordinate       Y(4) is V(R)

C     Y(5) is V(THETA)             Y(6) is V(PHI)

C     F(1) is R dot                F(2) is THETA dot

C     F(3) is PHI dot              F(4) is R dot dot

C     F(5) is THETA dot dot        F(6) is PHI dot dot

C     BR   is B(R)                 BT   is B(THETA)

C     BP   is B(PHI)               B    is magnitude of magnetic field

C........+.........+.........+.........+.........+.........+.........+..

C

END