PROJECT 			LARGE HADRON COLLIDER (LHC)

IR FEEDBOX

TITLE		 	RELIEF VALVE CIRCUIT DESIGN

Revision B Synopsis:

Revision done on November 2, 2005 after finding that the flow capacity of the Circle Seal relief valves, model D500-T1-8M, was overestimated in the original note. The Circle Seal relief capacity is 153 g/sec, not 485 g/sec as originally stated.

Also, we found that the required relief valve flow rate of the DFBX liquid helium vessel used in Section 6 was 807 g/sec, whereas it should have been 644 g/sec to be in agreement with Section 5.

Pressure safety of the DFBX liquid helium vessel is achieved by replacing the original 2-inch-diameter rupture disc with a spring-loaded relief valve, Kunkle model 912BHGM01, that has a capacity of 648 g/sec.

Section 10 was revised to account for the lowered Circle Seal Relief valve flow rate. In the revision we used the actual design fault pressure of 20 bar rather than the 25 bar test pressure used in the original calculation.

In Section 3.2g we recommend that the extreme consequences of a triple fault in the DH line be addressed by installing suitable relief devices in the HTS lead gas recovery lines.

Affected sections are: 2, Figure 3, 3.2a, 3.2b, 3.2c, 3.2f, 3.2g, 3.2h, 3.2i, 6.1, 6.2, 8, 10, 11a, and 11c.

PROJECT 			LARGE HADRON COLLIDER (LHC)

IR FEEDBOX

TITLE		 		RELIEF VALVE CIRCUIT DESIGN

1.  INTRODUCTION

This engineering note summarizes the required parameters and documents the flow analysis for the relief valve circuit design for the DFBX (distribution feedbox) liquid helium vessel and the insulating vacuum vessel.

2.  HARDWARE OVERVIEW

The DFBX series consists of 8 cryogenic feedboxes that will be used at CERN in the LHC. They will serve as the cryogenic, vacuum, and electrical interfaces between the US-supplied inner triplet superconducting quadrupoles and dipoles and the appropriate CERN system. The magnets are cooled with pressurized superfluid helium at a temperature of 1.9K and a pressure of 1 bar. The liquid inventory in the magnets is on the order of 1500 liters.  The DFBX has a vessel containing liquid helium that is used to cool the variety of current leads needed to power the inner triplet magnet system. This vessel will contain 255 liters of saturated liquid helium at 4.3 K and 1.3 bar. A 70K, 18 bar helium gas stream that trace-cools a copper shield provides thermal shielding in the DFBX and associated magnets; there is no liquid nitrogen. The insulating vacuum space of the DFBX is common to the magnet insulating space; a vacuum barrier on the CERN side of the interface separates the DFBX/magnet vacuum space from the vacuum space on the cryogenic distribution system. The external dimensions of the DFBX are shown in Figure 1.

Figure 1.  DFBX External Dimensions

The flow schematics for the DFBX are shown on LBNL drawing 24C3706, and a representative top level mechanical assembly drawing is shown on LBNL drawing 25I352. The relief valves for the superconducting magnets are special cryogenic relief valves, designated as QV92n on the flow schematics. These are on the CERN side of the interface and are connected via DFBX piping lines LDn.

The DFBX liquid helium vessel is physically separated from the magnet system by a 2.5 inch thick lambda plug made of Nema-G10 and Stycast( 2850MT epoxy that is proof tested to 25 bar.  The liquid helium vessel is supplied with liquid from the CERN cryogenic system through line CC’1 which is connected to control valve CV930, having a nominal diameter of 6 DN[1]. The action of CV930 is controlled by the DFBX liquid helium level sensors and the liquid helium vessel pressure sensor. A second cryogenic connection to the DFBX liquid helium vessel is provided by line DH which provides a flow of 20K, 1.3 bar helium gas for cooling the upper portions of the 7500 A HTS current leads. A pressure controlled valve, PV930, closes when the supply pressure exceeds the nominal set point of 1.3 bar. This supply pressure increase could occur in case of magnet quench when the pressure could rise to 20 bar, or in case of pressure testing at 25 bar. Valve PV930 has a nominal diameter of 20 DN[1]. Figure 2 shows the cryogenic pressure piping in the DFBX.

Figure 2. DFBX Pressure Boundary, some chimneys not shown. 1 – DH Line, 2 – LHe vessel fill, 3 – Primary LHe Vessel Relief Valves (second not shown), 4 – DH Line Relief Valves (second not shown), 5 – HTS Lead Cooling Hoses, 6 – Check Valve in Vessel Vent Line, 7 – HTS Lead Gas Outlet, 8 – Secondary LHe Vessel Relief Valve, 9 – Lambda Plug, 10 – Vapor Cooled Lead

The DFBX relief devices are shown schematically in Figure 3.  RV01, RV02, and RV06 are spring-loaded relief valves for the liquid helium vessel, and RV03 and RV04 are spring-loaded relief valves for the HTS lead cooling line. In the following section we show that RV06, a Kunkle Relief valve Model 912BHGN01, with a 35 psig set pressure or equivalent provides protection against over pressure. RV01 and RV02, Circle Seal D500-T1-8M-10%-30 psig, provide supplemental protection against minor upsets.   RV05, the relief valve on the vacuum vessel is the same as that provided on the FNAL inner triplet cryostats, and is shown on FNAL drawing 1620-MB-106391.

Figure 3. DFBX Relief Valve Schematic

3.  DESIGN REQUIREMENTS, ASSUMPTIONS, AND CONCLUSIONS:

3.1  Pressure Relief Requirements:

- The Maximum Allowable Working Pressure (MAWP) of the Liquid Helium Tank and associated components is 3.5 bar absolute (50.8 psia), while in an external vacuum. The test pressure is 4.4 bar absolute, while in an external vacuum [2].

- The relief devices in this document will vent into the LHC tunnel [3].

- To minimize the occurrence of venting gaseous helium into the LHC tunnel, the relief settings must be as close to the MAWP (3.5 bar) as possible.

- The pressure drop across the relief valve and liquid helium vessel vent relief piping must be less than 0.5 bar (7.2 psi).

- No relief device can be set higher than the MAWP.

- The relief capacity must be sufficient to vent the contents of the vessel without exceeding the MAWP by more than 10% under all conditions.

- The relief device on the DFBX vacuum vessel is chosen to be identical to those on the LQX vessels for reasons of commonality and ensuring adequate relief by limiting the pressure rise to 6 psig or less in case of cryogenic pipe leakage.

3.2  Accident Scenarios:

## a)  Fill Valve (CV930) in QRL Remains in Open State

This would cause the helium vessel to overfill and eventually the liquid level would reach a point of increased boiloff causing a pressure rise in the liquid helium vessel.  This would trip any or all of the relief valves that are connected to the helium vessel. In section 6 of the Appendix we calculate the total flow capacity of the relief valves to be 954 g/sec in this case, which far exceeds the ability of the supply line.

## b) Check Valve in the DFBX fails closed

In this case the excess boiloff gas will not be vented into the QRL and the pressure in the liquid helium vessel will build. The pressure rise will cause the fill valve CV930 to be closed to prevent overfilling. Even with the fill valve closed, the pressure would continue to rise and eventually cause the relief valve(s) RV01, RV02, and/or RV06 to trip. The capacity of the relief valves is more than adequate for this scenario.

## c) Loss of Insulating Vacuum

Since the US-supplied superconducting magnet system shares a common vacuum space, a leak anywhere in the string would have the potential to crack the vacuum space and cause a rapid vaporization of the liquid helium in the DFBX. Because the vacuum box has no glass windows or other types of brittle covers, an up-to air event would most likely be caused by someone opening a vacuum valve. This is analyzed in Appendix Section 5 where we perform a simulation of the pressure buildup due to an up-to-air event using the helium properties code HEPAK and determine how much helium mass must be removed from the vessel to maintain the pressure at 3 bar absolute. In section 5 we estimate the required peak mass ejection rate to be 644 g/sec for a 0.6 W/cm2 heat flux[4].

In Appendix Section 6 we calculate the flow capacity of the selected main relief valve to be  648 g/sec at 20 K, which is a reasonable estimate of the temperature of the ejected helium gas.  The vent for the LHe vessel also contains two additional relief valves in parallel, which provide a combined additional discharge capacity of 306 g/sec. We show in Section 8 that the pressure drop in the piping is low enough to prevent the helium vessel from exceeding its pressure rating.

Vacuum degradation due to a helium leak is extremely unlikely, since the pressure containing components that communicate with the insulating vacuum in the DFBX are fabricated entirely of austenitic stainless steel which has excellent toughness at cryogenic temperature.

## d) Leak in Lambda Plug

A leak in the Lambda plug is extremely unlikely because the materials used (NEMA G-10 CR, Stycast 2850MT, and 304L stainless steel) are proven for low temperature service. In addition, the production process is well characterized, and the articles will be thermally cycled, pressure tested, and leak checked before they are installed on the DFBX. The design of the NEMA G-10CR plug ensures that a high pressure on the magnet side will not cause the plug to be ejected into the DFBX and cause a large mass flow into the liquid helium chamber. Any leakage across the lambda plug would be very small in relation to the flow capability of the relief system as described in C above since any potential flow paths would have a cross sectional area of less than 0.02 mm2 [5].

e) High Pressure in Warm Helium Recovery Header

The warm helium header will be pressure tested at CERN to as high as 6 bar; this could pressurize the liquid helium vessel through the DFBX current lead vent lines. We expect the header to be equipped by CERN with a relief device to maintain the pressure below 3 bar.

When the warm header is pressure tested the current lead vent lines must be disconnected.

## f) Failure of PV930 to close as needed

PV930 is a pressure-controlled valve in the CERN valve box that isolates the DH line from a potential 290 psia (20 bar) pressure in Header D.  The high pressure can occur as result of a magnet quench. In Section 10 we calculate the flow rate from PV930 to the DH relief valve to be limited to less than the relief capacity by a .312 inch (7.9 mm) diameter orifice. The pressure drop from the relief valves to the HTS Lead Chamber is calculated to be 0.7 psi (50 mbar).  The resulting vessel pressure is 50 psia (3.5 bar).

## g) Failure of PV930 to close as needed, and a failure of the DH relief to open

This would pressurize the HTS Lead Chambers to an unsafe level and would likely cause severe damage to the DFBX. We recommend that CERN install a 75 g/sec relief valve in each of gas recovery lines to prevent this from happening.

## h) Failure of PV930 to close as needed, and a failure of the check valve to close

This would cause a rapid vaporization of the liquid helium that would have to be vented by the relief valves on the liquid helium vessel.

## i)  Failure of PV930 to close as needed, and a failure of the PEEK seal

The PEEK seal has been found to be leak tight for DH line pressures up to 50 psig (4.4 bara), so we expect no blow-by if the DH relief valves open as expected. If there is an unexpected leak in the PEEK seal, the situation is roughly the same as H above, and the  relief valves will vent the vessel.

### 3.3  Operational Recommendations

- It is recommended that an oxygen deficiency hazard is avoided by installing large diameter ducts above the relief valves to ensure that any helium gas flow is directed up and away from the DFBX.

- It is recommended that the relief valves and rupture disc be checked every 12 months full luminosity operation to verify that they are not leaking  Replace any devices that are found to be leaking.

- It is recommended that the relief valves be readjusted every two years.

- Rupture discs shall be replaced every two years.

Appendix A. CALCULATIONS and HARDWARE DETAILS

1.  NET VOLUME OF THE DFBX VACUUM TANK AND HELIUM VESSEL

- Internal Volume of the DFBX Helium vessel

VHe vessel internal =406 x 55.2 =22.411x 103cu. in. = 367.25 x 103 cc = 367.25 liter

V actual internal = 362 cc = 362 liter  (approx. 5 liter less volume from various items)

VHe vessel external =435 x 57.2 =24.882x 103cu. in.= 407.74 x 103cc = 407.74 liter

- Internal Volume of the DFBX Vacuum tank.

VVac. Tank = (41.90 x 83.30 + 12.50 x 14.50) x 36.20 =1.330 x 105cu. in.

VHe vessel external = 24.882 x 103cu. in.

- Net volume of DFBX vacuum tank (note: ignoring pipe volumes)

Vnet Vac. Tank= 1.330 x 105 - 24.882 x 103 = 1.080 x 105cu in. = 2.2 m3

2. DFBX HELIUM VESSEL LIQUID HELIUM WETTED SURFACE AREA

The liquid helium wetted surface area is 2,895 sq. in. = 18.677 x 103 cm2

3. HEAT FLUX TO THE LHe VESSEL DUE TO A LOSS OF INSULATING VACUUM

We use the heat flux data reported by [4], 0.6 W/cm2 and find the

total heat load using the wetted surface area of the He vessel calculated in 2 above

with 10 layers of super insulation to be:

Q =( 0.6W/cm2)( 18.677  x 103 cm2) = 11.207 KW

4.  LIQUID HELIUM VOLUME

Maximum Volume:

Maximum level = 13.20 inch from the bottom of the He vessel.

Sectional Area A = 282.444 in2 = 1.822 x 103 cm2

with longitudinal length = 55.20 in =140.21cm

Therefore:

Maximum liquid helium volume is

Vmax= (282.45 in2)(55.20 in) = 15.590 x 103 in3

= 255.495 x 103 cm3 = 255 liter

Minimum Volume:

Minimum level = 11.64 inch from the bottom of the He vessel.

Sectional Area A = 246.630 in2 = 1.591 x 103 cm2

with longitudinal length = 55.20 in =140.21cm

Therefore:

Minimum liquid helium volume is

Vmin= (246.63 in2)(55.20 in) = 13.614 x 103 in3

= 223.093 x 103 cm3 = 223 liter

5.  HEAT DEPOSITION INTO THE LIQUID HELIUM IN THE He VESSEL

Density of the liquid helium at 1 atmosphere 4.2oK is ( = 0.125 g/cc

or (0.125 g/cc)(1000cc/l) = 125 g/l

Mass of liquid helium at maximum level is

Wliquid = (255 l)(125 g/l) = 31.875 x 103 g

Total volume of the He vessel = 362 liter

Therefore, the density of Helium (liquid and gas )

( = total mass of He in the vessel/total volume of the He vessel

= 31.875 x 103 g/362 liter = 88.05 g/ liter

= .0881 g/cc

or specific volume = 11.351 cc/g

The allowable design pressure of the Helium vessel is 3.5 bar (50.8 psia) while in an external vacuum and we need to determine the required flow capability of the relief system to exhaust the helium gas without exceeding the MAWP of the vessel by more than 10%.

We solve this transient problem by a manual simulation in 1-sec increments.

Upon break in the vacuum and lost vacuum heat insulation for the helium vessel

heat flux of Q = 11.207 KW comes into the vessel.

Q = 11.207 x 103 W = 11.207 x 103 J/sec

From the HePAK program [6]:

At T = 4.5oK and ( = 0.0881 g/cm3   input,

P = 18.89 pisa, and Ho = 13.15 J/g     output

(H =

Htotal = Ho + (H t

therefore at  t = 1 sec:

Htotal 1sec  = Ho + (H t = 13.15 J/g + (.352 J/g sec)( 1sec) = 13.502 J/g,

Htotal 2sec  = Ho + (H t = 13.15 J/g + (.352 J/g sec)( 2sec) = 13.854 J/g,

Htotal 3sec  = Ho + (H t = 13.15 J/g + (.352 J/g sec)( 3sec) = 14.206 J/g,

and so on until at t = 21 second the relief valve opens up and starts releasing the Helium gas to prevent from pressure build up beyond 45.0 psia.

From this point on the density in the Helium vessel must decrease in order to maintain constant pressure.

From here on the input to the HePAK is P= 45.0 psia and Ht, where Ht, the enthalpy, is increased by .352 J/g every second because of the heat input. We then find the helium density corresponding to the P, H values and determine the helium mass in the vessel. By comparing this to the mass determined in the previous step we calculate the mass that must be removed to keep the pressure constant as the internal enthalpy is increased.

For example:

At t = 22 sec, P = 45.0 psia and

Htotal at 22 sec= Ho + (H t = 13.15 J/g + (.352 J/g sec)( 22sec) = 20.892 J/g

From HEPAK [6] we find that ( =0.08657 g/cc and T =5.541 oK,

Since the total volume of the Helium vessel =  362 liter = 362,000 cc

therefore,

at t = 22 sec,  mat t =22sec = mass flow out = helium mass at step 21 sec - (t(He vessel total volume)

= 31,875 g - (at 22 sec(362,000 cc)

=  31,875 g – (0.08657 g/cc)(362,000 cc) = 536.66 g

(the mass flow rate out the relief valve is 536.66 g/sec)

at t = 23 sec,

P = 45.0 psia, Htotal at 23 sec = 21.246 J/g, and we find ( = 0.08479 g/cc and T  = 5.540 oK,

mat t=23 sec = mass flow out = helium mass at step 22 sec - (t(He vessel total volume)

= (31875 g – 536.66g )- (at 23 sec(362,000 cc)

=  31338.34 g – (0.0.08479 g/cc)(362,000 cc)

= 644.36 g

( the mass flow rate out the relief valve is  644.36 g/sec)

at t = 24 sec.

P = 45.0 psia, Htotal at 24 sec = 21.598 J/g and we find ( =0.08304 g/cc and T =5.567 oK,

mat t=24 sec = mass flow out = helium mass at step 23 - (t(He vessel total volume)

= (30693.98 g – 633.5 g )- (at 23 sec(362,000 cc)

=  30060.48 g – (0.08304 g/cc)(362,000 cc)

= 633.5 g

(the mass flow rate out the relief valve is 633.5 g/sec)

and so on.

For a tabulation of the data for  t =0 ~200 second see Section 12 of the Appendix.

The results of the simulation is shown on the graphs below.

In order to keep the internal pressure of Helium vessel at or below 45.0 psig, it must exhaust within initial 1 second 644.3 g of helium mass from the vessel.  We must choose the relief valve to meet this criteria.

6. HELIUM MASS FLOW RATE THROUGH RELIEF VALVES

6.1 Circle Seal Relief Valves

Normally commercial safety relief valves are rated for air flow, and in this section we convert the air flow ratings to helium flow ratings.

We use the formulation given in Section  UA-20 of theASME Boiler & Pressure Vessel Code, Sec.VIII,  Div 1.

The basic equation is:

W =

where

Wa = rated capacity, converted to lbs of air per hr at 60 deg F, inlet temp.

Whe = flow of helium gas or vapor, lb/hr

C = constant for gas or vapor which is a function of the ratio of specific heat k = Cp/Cv

K =coefficient of discharge ( see UG 131(d) and (e)

A =actual discharge area of the safety valve (sq. in)

P = (set pressure x 1.10) plus atmospheric pressure,  (psia)

M =Molecular weight (of air M = 28.97; of He M = 4)

T = absolute temp. at inlet (deg F + 460 deg) or oR =

We obtained flow data from Circle Seal for their cryogenic safety relief valve model No. D500 8M- where the pressure is 10% above the cracking pressure of P = 3 bar = 43.5 psia = 28.8 psig, the volume flow rate of air is

Wair= 175.90 SCFM (cu ft/min)

The density of air at 60 deg F, 14.7 psia is ( = 0.0765 lb/ft3

since from the graph Wair = 175.90 SCFM (standard cu ft/min), this converts to

Wair 	= (175.90 cu ft/min)( .0765 lb/ft3) (60 min/hr) =  807 lb/hr

= ( 807lb/hr)(454g/lb)(1 hr/3600 sec)

=  101.8 g/sec

using the equation Wair =   and C=356 for air at  60oF and 1 atm,

we can solve for KAP.

807 lb/hr = 356 KAP

KAP =  9.6

From the HEPAK computer program [6] we find for P =46.38 psia and T = 20 K:

( = 0.008 g/cc,

Cp = 5.37 J/g-K, and

Cv = 3.13 J/g-K.

Therefore, for 20 K (36 R) helium, the specific heat ratio, k = , and

the constant C for He gas becomes Che.

The helium flow rate through the relief valve WHe is calculated, using

M = 4,

T =36R

C = 381.5

KAP =  9.6

WHe =

WHe = ( 1.22x 103 lb/hr)(454g/lb)(1 hr/60min) =  9.2 x103 g/min

WHe = 153 g/sec

6.2 Kunkle Valve Model 912BHGM01

This valve has 11/2 inch pipe threads on inlet and outlet, an H orifice (area of 0.864 in2 ), and all metal seals. At a set pressure of 35 psig, the flow capacity is 740 SCFM (air).

Wair  = 740 SCFM x .0765  lb/ft3 x 60 sec/min = 3397 lb/hr

Using:  	Wair = , where C = 356, M = 28.97, and T = 520 R,

We find 	CKAP = Wair = 3397  = 1.44 x 104

KAP = 1.44 x 104/356 = 40.4.

Using this value of  KAP, solve for WHe, where C = 381.5, M = 4, and T = 36 R (20 K).

WHe =   =  lb/hr

= 5137 lb/hr = 5137 x 454 /3600 = 648 g/sec

The Kunkle valve alone satisfies the 644 g/sec flow requirement

Since the mass of liquid helium in the helium vessel is 31.875 x 103 g and if we assume the mass flow rate through all threerelief valves is 954g/sec if we assume the density of the helium stays constant at 0.0881 g/cc then the the chosen relief valve is capable of exhausting all helium gas from the vessel in

7. FLOW RATES FOR DIFFERENT HELIUM DENSITIES

We show the flow capacity of the relief valve as a function of density (or Temperature) in the table below. We assume that the heat flux input maintains the pressure of the vessel at 50.75 psia, during the exhaust.

( (% of orig) 	( (g/cc)	T(oK)	Cp(J/g-K)	Cv	H(J/g)	W(g/sec)	t(sec)

100%	0.0881 	5.691	19.86		2.776	 21.50	1,226	24

50%	0.044	6.409	12.12	3.010	  34.34	1,023	28

25%	0.022	8.874	6.524	3.089	  54.06	   729	44

10%	0.0088	19.20	5.407	3.132	113.00	   465	69

1%	0.0008	190.9	5.193	3.117	1008.0	   146	218

8. PRESSURE DROP IN HELIUM VESSEL RELIEF VALVE PIPING

We will specify the cracking pressure for the DFBX helium vessel relief valve

to be P = 3 bar =43.5 psia = 28.8 psig and assumethe relief valve will build pressure 10% over the cracking pressure. Therefore at the upstream of the relief valve Pupstream=31.68 psig.

Since the allowable pressure of the vessel is PHe vessel =3.5 bar = 50.75 psia

= 36.05 psig, we require the pressure drop through the tube to be (P = 4.37 psig or less.

The pressure drop through relief valve exhaust tube will be calculated by

using Darcy’s equation [7].

(P =

Reference [7] states that if the calculated pressure drop through the tube is greater than 10% of inlet

pressure but less than 40% of inlet pressure then the Darcy’s equation may be used with reasonable accuracy.

The primary  relief line is a  1.870 inch ID x 37.10 in long 304L  Stainless steel tube.

To determine the type of flow through the tube, calculate the Reynold’s number

Re =123.9

where

d = internal diameter of the tube (in) = 1.870 in.

v = mean velocity of flow  (ft/sec)  = 203.4 ft/sec (see calculation below)

( = absolute (dynamic) viscosity (centipoise) = 25.65 x 10-6 poise

=0.0026 centipoise

( = density of helium (lb/cu ft)  = 0.00881 g/cc = .55 lb/cu ft

Calulation of mean velocity of flow  (ft/sec)

Since mass flow rate Whe= 644 g/sec

Density of helium ( = 0.0088 g/cc and tube ID = 1.870 in

Cross sectional area of the tube A = (/4 (1.870)2 =2.75 in2 =17.72 cm2

Re =123.9

Since Re>4000  the flow is  turbulent.

Solving Darcy’s equation

(P =

where:

(P = Pressure drop through tube = psi

( = helium gas density 0.0088g/cc = (0.0088g/cc)(62.428 lb/ft3 / 1g/cc)

= .55 lb/ft3

D = internal diameter = 0.156 ft

f = friction factor = 0.0113 ( from Moody diagram: assume drawn tube[8])

L = length of the tube = 42 in = 3.5 ft

g = gravitational acceleration = 32.2 ft/sec2

V = mean velocity = 135.5 ft/sec

(P =

=

Since the pressure drop through the vent tube is (P = .24 psig, the helium vessel  will be 35.24 psig, which is below the allowable vessel pressure of P = 3.5 bar =50.75 psia.

9. DFBX VACUUM TANK PRESSURE RELIEF VALVE

Normally the DFBX Vacuum tank is under vacuum (10-8torr) but due to leaks in cryogenic piping, DFBX helium vessel, or the magnet cryostats, it is possible to have a pressure build up in the DFBX vacuum tank.

We calculate the capacity of the relief valve to vent 200 K helium gas at a pressure of 17.7 psia.

From HePAK program:

T (K)  	( (g/cc)	P (psia)	Vsonic(m/sec)	Cp(J/g-K)	Cv(J/g-K) 	( (10-6 poise)

200	 	0.0002934		17.7	832.8	5.193	3.116	151.4

We install the Fermi lab custom made relief valve  DWG 1620-MB-106391(see Section 14) on the DFBX vacuum tank.

The nozzle of this relief valve is 2.625 in. diameter. Gas flow through a nozzle is given by [9]

where

Assume the helium gas leaked out from the helium vessel has following properties from HEPAK program

T = 200oK

( =0.0002934 g/cc = (2.934 x 10-4g/cc)(62.428lb/ft3)/(g/cc) =1.832 x 10-2lb/ft3

P =17.7  psia

Cp = 5.193 J/g-K

Cv = 3.116 J/g-K

H = enthalpy = 1073 J/g

V = sonic velocity =832.8 m/sec=(865.1 m/sec)(3.28 ft/m)=2,838 ft/sec

C = nozzle flow coefficient = 0.60

( =dynamic viscosity = 151.4 x 10-6 poise = 1.514 x 20-2 centi-poise

(P = assume pressure drop through nozzle = 3 psig

= 17.7 psia

p2 = Pressure downstream of nozzle = 14.7 psia

= 2.625 in. dia =0.219 ft dia.

= 3.760in. dia =0.313 ft dia

A = Nozzle cross sectional area(sq. ft) = ((/4)(2.625)2/144 =.0376 sq ft.

V = Inner volume of the vacuum tank = 143.461 x 103 in3 = 83.021 ft3

= 2.351 x 103 liter.

therefore

as result:

Under our assumed conditions, the mass flow rate of this relief valve  is w = (q1= 0.520 lb/sec = 236 g/sec. Therefore, the relief valve has the necessary flow capability to exhaust helium gas from a credible size cryogenic leak  into the vacuum space.

Pressure drop through the tubing prior to the relief valve.

There is a tubing section between vacuum tank and the relief valve approx. length of 13 .0 inches with an inside diameter of 3.760 in.  With volume flow rate we calculated above we will calculate pressure drop of the tube using Darcy’s equation.

where:

(P = Pressure drop through tube in psi

( =0.0002934 g/cc = (2.934 x 10-4g/cc)(62.428lb/ft3)/(g/cc) =1.832 x 10-2lb/ft3

d = internal diameter = 3.760 in ID

D = internal diameter = 0.313 ft ID

f = friction factor = 0.011 ( from Moody diagram: assume drawn tube)

L = length of the tube = 13.00 in = 1.083 ft

g = gravitational acceleration = 32.2 ft/sec2

A = ((/4)(3.760)2=11.104 in2 = 0.0771 ft2

V = mean velocity = qA = (28.38 ft3/sec)/(.0771ft2) = 368.09 ft/sec

(P =

(P =

Therefore the DFBX vacuum tank relief capacity is not limited by the vent pipe that penetrates through the thermal shield.

10. DH PRESSURE RELIEF PIPE

We place an orifice with a diameter of 0.312 inch (7.9 mm) diameter in the 0.87 inch ID line from the QRL. The flow through this orifice is given by:[8]

, where

q = flow rate, ft3/sec at flow conditions

Y = expansion factor

C = flow coefficient

A = cross sectional area of orifice, ft2 = 5.3 x10-4

g = acceleration of gravity = 32.2 ft/sec2

(P = Pressure drop in lb/in2

( = weight density, lb/ft3

The expansion factor, shown in Figure 10-1, is a function of the specific heat ratio, the ratio of orifice to pipe diameter, and the ratio of downstream to upstream pressure. The flow factor, shown in Figure 10-2 is a function of diameter ratio and Reynolds number of the flow in the inlet pipe.

Under fault conditions we have a 20 bar (290 psia) upstream pressure and a 3.5 bar (50 psia) downstream pressure.

The relevant helium properties at 20 K are:

| Pressure, psia | Cp, J/g-K | Cv, J/g-K | Vsound, ft/sec | Visc, lbm/ft-sec | Density, Lb/ft3 |
| --- | --- | --- | --- | --- | --- |
| 290 | 6.101 | 3.18 | 968 | .29 x10-5 | 2.94 |
| 170 | 5.81 | 3.16 | 916 | 0.27 x10-5 | 1.75 |
| 50 | 5.39 | 3.13 | 876 | 0.24 x10-5 | 0.52 |

In Figure 10-1 use the properties at the average pressure:

Figure 10-1 does not extend to the specific heat ratio for helium, 1.86, but to be conservative we assume Y = 1.

We need to estimate the Reynolds number, based on the inlet pipe diameter, 0.87 inch, in order to determine the flow coefficient C.

,

where		D = inlet diameter, ft = 7.25 x 10-2

v = mean velocity of flow, ft/sec

( = density, lb/ft3 = 2.94

(e = viscosity, lbm/ft-sec = 0.29 x 10-5

If we limit the fault flow to around 300 g/sec (0.66 lb/sec), the flow rate of therelief valves in the DH line, the mean flow velocity in the inlet pipe is:

v = 54.8 ft/sec,

and we find Re =  4 x 106.

From Figure 10-2, we see that C =0.6 for our conditions. Substituting into:

ft3/sec,

we obtain q =  0.36ft3/sec, which is 0.63lb/sec at the average density, or 286 g/sec. Since the two relief valves in the DH line have a combined flow capacity of 306 g/sec, the proposed orifice provides passive protection against a failure of PV930 to close.

Under normal operating conditions, the upstream pressure is 1.3 bar (18.9 psia) and the downstream pressure is 1.25 bar (18.1 psia).

The relevant helium properties at 20 K are:

| Pressure, psia | Cp, J/g-K | Cv, J/g-K | Vsound, ft/sec | Visc, lbm/ft-sec | Density, Lb/ft3 |
| --- | --- | --- | --- | --- | --- |
| 18.5 | 5.267 | 3.12 | 868 | 0.24 x10-5 | .191 |

From Figure 10-1, we see that it is reasonable to assume Y = 1 since the pressure ratio is nearly zero.

We need to estimate the Reynolds number, based on the inlet pipe diameter, 0.87 inch, in order to determine the flow coefficient C.

,

where		D = inlet diameter, ft = 7.25 x 10-2

v = mean velocity of flow, ft/sec

( = density, lb/ft3 = .191

(e = viscosity, lbm/ft-sec = 0.24 x 10-5

If we desire the flow to be 5 g/sec (.011 lb/sec), the mean flow velocity in the inlet pipe is: v = 18 ft/sec,

and we find the Reynolds number to be 0.8 x 105.

From Figure 10-2, we see that C =0.6 for our conditions. Substituting into:

ft3/sec,

we obtain q = 0.062 ft3/sec, which is 0.012 lb/sec at the average density, or 5 g/sec.

This is consistent with our starting assumption that we require 5 g/sec flow under normal operation.

Figure 10-1. Y values, taken from reference [7].

Figure 10-2.  C values, taken from reference [7].

Estimate the Pressure drop from DH vent pressure relief valves to the orifice (dwg:25I2256).

L = straight tube length from orifice = (6 +12.7)/12 = 1.55 ft

Lequivalent =  straight section of tube length + straight length equivalent of  two Tees

Figure 10-3. Equivalent straight lengths for bends.

We assume the resistance of a Tee joint behaves as a 90 degree miter bend.

At a bend angle of 90 degree, the L/D equivalent length becomes 60.

Since there are two miter bends in this circuit , the equivalent length from them becomes

2(60D) = 2(60)(0.870/12) = 8.70 ft

Lequivalent = 1.55  + 8.70 =  10.25 ft

From Darcy’s equation the pressure drop through the tube is calculated:

where:

( = helium gas density =0.52 lb/ft3

D = internal diameter = 0.0725 ft ID

f = friction factor = 0.011 ( from Moody diagram: assume drawn tube)

L = length of the tube = 10.25ft

g = gravitational acceleration = 32.2 ft/sec2

V = mean velocity = 90 ft/sec

(P =

=

Since the DH relief valve is set to a cracking pressure of 3 bar, if we add in the 10% over pressure and the 0.7 psi drop in the vent line, the liquid helium vessel will be pressurized to 3.46 bar. The pressure drop is quite conservative, since the resistance of the Tee joints is probably less than the value we assumed.

11. RELIEF VALVE DETAILS

a. Circle Seal Pressure Relief Valves, Model D580-T1-8M

This valve is equipped with a deflector cap that serves as a dust shield and also increases the flow capacity (probably because it acts as a divergent nozzle). A further benefit is that it facilitates a manual override of the relief valve. The valve uses a Teflon O-ring in order to be consistent with cryogenic operation. The valve and performance charts  are shown on Figure 11-1.

b.  Relief valve for DFBX vacuum tank

The valve is made by FNAL and is shown on FNAL Drawing 1620-MB-106391, reproduced in Figure 11-2 below. The cracking pressure setting is less than 3 psig. The relief valve has sharp edges at inlet and exit of the nozzle and as a result the flow coefficient behaves like a square edged orifice rather than a normal nozzle flow. In general square edge orifice flow coefficient ranges from .60 to .61.

c. Kunkle Relief Valve, Model 912BHGM01

This valve has a brass/bronze base, body, and bonnet with metal to metal seat and seal and threaded cap. The inlet is 11/2 inch NPT male pipe (38.1 mm) and the outlet has 21/2 inch female threads (63.5 mm). The orifice area is 0.864 in2 (5.574 cm2). At a set pressure of 35 psig, the flow rate is 740 SCFM (air).

Valves of this type have been used reliably in the Magnet Test Facility at Fermilab.

Figure 11-1. Pressure relief valve for the DFBX.

Figure 11-2. Vacuum Vessel relief valve for the DFBX.

12 TABULATED RESULTS FROM LOSS-OF-VACUUM SIMULATION

13.  References

1.  “Technical Specification for a Compound Cryogenic Helium Distribution Line for the Large  Hadron Collider (LHC), LHC Document LHC-QRL-LI-0001 rev 2.0.

- “DFBX Helium Vessel Structural Analysis”, LBL Engineering Note M8036.

- “Pressure Levels and Overpressure Protection of Helium Circuits of the LHC Electrical Feedboxes”, draft dated 2000-03-10.

- W. Lehman and G. Zahn, “Safety Aspects of LHe Cryostats and LHe Transport Containers”, Proc. 7th Int’l Cryogenic Engineering Conf., London, 1978, p 569 – 576.

- “DFBX Lambda Plug Design Note, in preparation.

- HEPAK – A computer program for calculating the thermophysical properties of helium, supplied by Cryodata, Inc., P.O. Box 173, Louisville, CO 80027, USA.

- Crane Company publication, “ Flow in Fluids”, p 1-7.

- Ibid, “Flow Through Nozzles and Orifices”, p.  2-14.

- “Standard Handbook for Mechanical Engineers”, 7th edition, p. 4.62-4.63. Note: later editions of this handbook may contain errors in this formulation.

- 1998 ASME Section VIII Div. 1 Boiler & Pressure Code. Pg 92 UG-125 Pressure Relief Devices paragraph c).