# Breakdown of Required Port Engineering Design Tasks,

# Any Party

## Equatorial Port  Design Tasks

## Upper Port Design Tasks

## Prototype Tasks for ref

## Divertor Design Tasks- skelton

# Working draft, date 2006-01-27

|  |  |  | Interest? Capable? | PPY | Priority | Ass | If not any PortEng party , then Who? | Resources |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| EQ |  | Ref ITER_D_22MGM6 v1.0 (EqPP Review of IT Design) |
| EQ | 1 | EM Forces on Eq Plug | ( | 0.1 | 1 |  | IT/ Rocella, D’Agata | e-m analysis |
| EQ | 2 | EM Stresses in Eq Port Plug | ( | 0.5 | 2 |  | RF/Effremov | e-m analysis, struct anal |
| EQ | 3 | Cantilevered Handling |  | 0.2 | 3 |  | IT/ ATesini Service Contract | Handling Mech Eng |
| EQ | 4 | Cantilevered or Supported In-Situ (Arrangement for Supported) |  | 0.2 | 2 |  |  | CAD . Handling Construction An. Stress Analysis. |
| EQ | 5 | Port Plug Attachment/Seal Geometry | ( Service Contr? | 0.4 | 1 |  | IT/VV KO/Port | CAD, Mfr Proto Test |
| EQ | 6 | BSM Design for Equatorial Port Plugs | ( | 2 | 1 |  | IT/Bl Gp | CAD, Mech Eng, Therm, e-m, Indust, mfg |
| EQ | 7 | BSM Attachment Arrangement |  | 0.2 | 2 |  |  | CAD, Maint, RH, Stress Analysis, Thermal Analysis |
| EQ | 8 | Improved Shielding at Front of Port Plug |  | 0.1 | 2 |  | ENEA (MCNP) UKAEA (Atilla?) | Neutr Anal Concl |
| EQ | 9a | Equatorial Port Plug Variant waveguides | ( |  |  |  | US (RF) |  |
| EQ | 9b | Equatorial Port Plug Variant vacuum extensions, | ( |  |  |  | RF |  |
| EQ | 9c | Equatorial Port Plug Variant access apertures |  | 0.02 | 2 |  |  | Mech Eng CAD (viewing) |
| EQ | 10 | Design of Standard RH Orbital Welded Water Connection |  | 0.6 | 1 |  | (Service Contract?) | Weld Eng, Laser weld,, Hydr Anal, Mfr, Proto test |
| EQ | 10’ | other standard interface features (bolting, lifting, precise position guiding and location) |  | 0.1 | 3 |  |  | Opt,Diagn, Mech Eng |
| EQ | 11 | Thermo-hydraulic Evaluation of Cooling |  | 0.2 | 1 |  |  | Mech Eng Therm, Th-hydr, 2flow, |
| EQ | 12 | Far Forward Diagnostic Module Extension |  | 0.5 | 2 |  | (Service Contract ? | CAD, Attach’t, Weld-,Mech Eng, Stress Analysis e-m, Therm, Th-hydr,Manufg FW, HFC |
| EQ | 13 | Electrically Heated Flange Plate |  | 0.5 | 2 |  |  | Mech Eng, Ind’l,Therm, Experience, |
| EQ | 14 | Handling of Window Plate, Drawers and Tubes etc | (sub-flanges) | 0.1 | 2 |  | US (Full Plate) | Mech Eng Therm, Experience, Ind’l, |
| EQ | 15 | BSM Coolant Feed - Independent of Port Plug Structure |  | 0.1 | 2 |  |  | Mech Eng, Hydr, Weld Eng Handling |
| EQ | 16 | Hydraulic Design Draining and drying analysis |  | 0.3 | 2 |  |  | Mech Eng, Hydr, |
| EQ | 17 | Documentation |  | 0.2 | 1 |  |  | Mech Eng, Experience, Analysis packs |
| EQ | 18 | Neutronic Analysis more diagnostic details; Comp & assess Attila/MCNP |  | ≤0.5 | 3 |  |  | Neutronics CAD MCNP, Atilla |
| EQ | 19 | Procurement Strategy | ( | .1 |  |  | IT/Diag Gp/DI | Procurement Eng Mfr, Legal |

| Where? | No. |  | Interest? Capable? | PPY | Priority | Ass | If not any Port Eng party , then Who? | Resources |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| UP |  | Ref ITER_D_22MGQQ v1.0 (UpPP Review of IT Design) |
| UP | 1 | Port Plug Attachment/Seal Geometry (B11.3) | ( tho poss Service Cont | 0.3 | 1 |  | IT/VV KO/Port | CAD Mfr Proto Test |
| UP | 2 | BSM-Attachment Arrangement |  | 0.2 | 2 |  |  | CAD, Maint, RH, Stress Analysis, Thermal Analysis |
| UP | 3 | BSM Construction | ( | 2 | 2 |  | IT/Bl Gp | CAD. Mech Eng, Therm, e-m, Indust, mfg |
| UP | 4 | Definition Diagnostic BSM Apertures | ( | 0.1 | 1 |  | IT/Dia Eng | CAD Diag Integ |
| UP | 5a | Further design Port Plug Structure ( inverted U cover) - Improved Torsional Stiffness Study of attachment arrangement to front frame, scoping structural analysis of front frame stresses, vibration modes and DAF, |  | 0.2 | 1 |  |  | FE Struct’l, CAD, |
| UP | 5b | diagnostic module attachment and connection |  | 0.1 | 1 |  |  | CAD, |
| UP | 5c | possible convergencs to a common structure with ECH. |  | 0.2 | 1 |  | IT/Diag ECHLUA | CAD FE Struct’l, |
| UP | 5d | Manufacturability. **B11.1 Coolant channels design in upper port-plug structure. (Low, medium) + Structure Coolant Channels |  | 0.1? | 2 |  |  | Mech Eng Ind’l |
| UP | 6 | Cantilevered Handling (Arrangement for Supported) |  | 0.2 | 1 |  | IT/ATesini Service Contract | CAD Handling Mech Eng |
| UP | 7 | EM Forces for variants of Upper Port Plug Variations in BSM Connection Realistic port plug extensions B, dB/dt in port plug | ( | 0.1 | 1 |  | T/ Rocella, D’Agata | e-m analysis |
| UP | 8 | EM Forces on Cantilevered In-Situ Port Plug | ( | 0.1 | 1 |  | T/ Rocella, D’Agata | e-m analysis |
| UP | 9 | Central Tube Handling |  | 0.2 | 2 |  | US (G10) | Mech Eng CAD Handling |

| UP | 10 | Structure Coolant Channels **B11.2 Thermal hydrauric analysis of coolant channels for upper port-plug. (Low, medium) |  | 0.2 | 1 |  |  | Mech Eng Therm, Th-hydr, 2flow, |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| UP | 11 | Neutronic Analysis Up#11 streaming through apertures Streaming through gaps Activation in port cell, nuclear heat on diag comp’ss, minimum bulk shield, |  | ≤0.5 | 2 |  |  | Neutronics CAD MCNP, Atilla |
| UP | 12 | Location (Engagement) of Central Tube |  | 0.1 | 1 |  | US? | CAD, Mech Eng, Strucl Analysis |
| UP | 13* | Far Forward Diagnostic Module Extension |  | 0.2 | 2 |  | (Service Contract ? | CAD, Attach’t, Weld Eng, Stress Analysis e-m,Therm, Th-hydr, Manufg FW, HFC |
| UP | 14* | Hydraulic Design Draining and drying analysis |  | 0.2 | 2 |  |  | Mech Eng, Hydr, |
| UP | 14b** | B11.3 - Thermal hydraulic stress analysis for upper port-plug structure. |  |  |  |  |  | Mech Eng, Hydr, Th-Hydr |
| UP | 15* | Documentation |  | 0.2 | 1 |  |  | Mech Eng, Experience, Analysis packs |
| UP | 16** | D4.2 Identify any issues specific to U6. (Low, short) |  |  |  | KO-1 NFRC |  | Diagn Eng |
| UP | 17** | B14.3 Aspects of vacuum extensions for upper port. (High, medium) |  |  |  |  |  | UHV, Safety, Mech Eng |
| UP | 18** | B17.b Manufacturing and testing aspects of design of flange and channel-section for upper port-plug. including Further design Port Plug Structure ( inverted U cover) (High, short) |  |  |  |  |  | Mech Eng, Manuf’g , In’l |
| UP | 19** | B6.4 Full EM stress analysis in upper port-plug structure. (High, medium) |  |  |  | 3 |  | Mech Eng, FE Stress analy |
| UP | 20 *** | Develop engineering and CAD aspects of Neutron Activation System and Vacuum Extensions for upper port with an extended visit (2m) to ITER IT. (Medium, long) |  |  |  | KO |  | Diag, Diag Integr Diag Eng CAD Mech Eng UHV Safety |
|  | * | Added post DRM |  |  |  |  |  |  |
|  | ** | Added post DRM, outstanding from 2005 |  |  |  |  |  |  |
|  | *** | Non Port eng Design activity |  |  |  |  |  |  |

|  |  |  | Complementary Design Task |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| PROTO | ITER_D_2223EG v1.0 (port engineering prototypes) |  |  |  |  |  |  |
|  | 1 | Lifting/Handling of Port Plug | EQ 3 |  |  |  |  |  |
|  | 2 | Port Plug Flange Attachment | EQ 5 |  |  |  |  |  |
|  | 3 | Port Plug Sealing | EQ 5 |  |  |  |  |  |
|  | 4 | BSM Attachment | EQ 7 |  |  |  |  |  |
|  | 5 | Port Plug Structure | EQ 2 |  |  |  |  |  |
|  | 6 | RH water Welds | EQ 10 |  |  |  |  |  |
|  | 7 | Draining and Filling Tests | EQ 16 |  |  |  |  |  |
|  | 1 | Lifting/Handling of Port Plug | UP 6 |  |  |  |  |  |
|  | 2 | Port Plug Flange Attachment | UP 1 |  |  |  |  |  |
|  | 3 | Port Plug Sealing | UP 1 |  |  |  |  |  |
|  | 4 | BSM Attachment | UP 2 |  |  |  |  |  |
|  | 5 | Port Plug Structure | UP 5 |  |  |  |  |  |
|  | 6 | RH water Welds | PROTO 6 |  |  |  |  |  |
|  | 7 | Draining and Filling Tests | UP 14* |  |  |  |  |  |

No estimates of ppy etc. No details of funding etc- still tbd

## Divertor Design Tasks

These were not identified in Diagnostic Prot Engineering Task Final Report Summary

Items included have an element of generality.

They are listed because they must be processed at some stage.

Whether they are appropriate for distributing to an extension of the port engineering task has still to be discussed within the IT, specially Divertor Group and Diagn Engineering

|  |  |  | Interest? Capable? | PPY | Priority | Ass | If not any PortEng party , then Who? | Resources |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | General Diagnostic Port Engineering Process |
|  |  | Application of the general diagnostic port engineering process, as seen in the task so far, to the divertor level diagnostic support systems. |  |  |  |  |  | Fig. 1 |
| DIV |  | Design Tech Spec for, Diagnostic Divertor Structures Diagnostic Port structures Diagnostic Vac Bdy Structures Cables, |  | 0.4 | 2 |  | IT | Mech Eng |
|  |  | Diagnostic Divertor Components |
| DIV |  | Cassette Target, cables, T/C location ref2 | (? | 0.2 | 1 |  | Within a Diagn Design Task | HFC |
| DIV |  | Cassette Body as sprung component ref3 Cut-outs (LVNC, T.S) replacement stiffness ref4 | (? |  | 1 |  | IT/Dia Eng & Div | Assessment Struct |
| DIV |  | Mirror Mount, cassette body mounted Design ref5 ref6 ref7 Fig. 8 Definition of common system ref9 ref9a Interfaces (RH, ..) Construction Attachment, Connection Cooling ref10 |  | 0.2 | 2 |  | IT/Diag | Mech Eng |
| DIV |  | Electrical forces Thermal studies |  | 0.2 | 2 |  |  | e-m,Th anal |
| DIV |  | streaming through apertures on mirror housing, shutter and built-in heating mechanisms |  | 0.2 | 2 |  |  | Neutr/ thermal |
| DIV |  | Maintenance |  | 0.1 | 3 |  |  | RH |
| DIV |  | Dome Liner ref20 Movements & Vibrations | ( |  | 1 |  | IT/Div | Assessment |
| DIV |  | Dome-Liner side & space usage | ( | 0.1 | 2 |  | IT/DiagEng | Assessment |
| DIV |  | Mirror Mount, Dome Liner mounted ref10 Design Definition of common system Interfaces (RH, ..) Construction Attachment, Connection Cooling sensitivity to movements and vibrations. | (? | 0.3 | 2 |  | IT/DiagEng | Mech Eng Assessment CAD, Vib Analy Sensitivity analysis |
| DIV |  | Electrical forces Thermal studies |  | 0.2 | 2 |  | IT/DiagEng | e-m,Th anal |
| DIV |  | Mirror design for maintenance. attachment |  | 0.1 | 3 |  | IT/DiagEng | Mech/Opt Eng Struct/Therm Analysis |
| DIV |  | Cassette Side Plate Fig. 11 Design Definition of common system Side Plate attach cool viewing | ( |  | 2 |  | IT/DiagEng | Mech Eng, CAD Assessment |
| DIV |  | Thermal Analysis |  | 0.1 | 2 |  |  | Th |
| DIV |  | Back Box Central Cassette Definition of common system (LVNC, Refl, ) ref12, ref12 Interfaces (RH, ..) Construction Attachment Cooling Maintenance |  | 0.3 | 2 |  |  | Mech / Opt Eng e-m, th, struct analysis, RH |
| DIV |  | Connector & Connector Link Fig. 14 Design incl Housing Installation, interfaces Anchor and cooling Handling |  | 0.2 | 2 |  |  | Mech Eng, CAD, Handling |
| DIV |  | Detail design for Prototype |  | 0.3 | 3 |  |  | CAD |
| DIV |  | Cassette Central access Neutron streaming assessment: - comparison of optical relay and fibre approach. |  | 0.1 | 2 |  |  | Neutr |
|  |  | Diagnostic Divertor Port Structures |
| DIV |  | InV Sevices Design N10 Fig. 15 ref16 fixed Cable loom to Bl#18 fixed Cable loom to cassette removable cable loom to racks layout, design |  | 0.4 | 2 |  |  | Mech Eng CAD, Th Anal |
| DIV |  | Diagnostic Sealed Shield Rack ref17 Generic & Variations | ( | 0.1 | 2 |  | IT/Dia | Mech Eng, |
| DIV |  | Need for cooling |  | 0.1 | 1 |  |  | Neutr?/Therm Analysis |
| DIV |  | Design, Chassis, structure, wheels loads Wt, Lubrication Location Engagement |  | 0.2 | 2 |  |  | Mech Eng & Analysis |
| DIV |  | Handling Gripper Articulation Cask Interface |  | 0.2 | 3 |  |  | RHAnalysis |
| DIV |  | Diagnostic Rack Generic & Variations | ( | 0.1 | 2 |  | IT/Dia | Mech Eng, |
| DIV |  | Design, Chassis, structure, wheels loads Wt, Lubrication Location Engagement |  | 0.2 | 2 |  |  | Mech Eng & Analysis |
| DIV |  | Diagnostic Sevices Cooling diagnostics Services Delivery of gas/water Allowable gas leak |  | 0.1 | 2 |  |  | Mech Eng & Analysis |
| DIV |  | Handling Gripper Articulation Cask Interface |  | 0.2 | 3 |  |  | RHAnalysis |
| DIV |  | Insertable Access Tube to Cassette ref18 ref19 Design, structure, Location, Engagement |  | 0.1 | 3 |  |  | Mech Eng, CAD.RH |
| DIV |  | Retractable Tube to Cassette Design, structure, Location, Engagement | ( | 0.1 | 1 | Any |  | Mech Eng, CAD.RH |
| DIV |  | Mech Transmission across Divertor-Rack interface Design, structure, Shutter systems | ( | 0.2 | 2 | Any |  | Mech Eng, CAD. |
| DIV |  | Diagnostic Auto Refurbishment Fibre blowing for fibre replacement. Mirror maintenance. | ( |  | 3 |  | IR Therm | Mech Eng, Interf, Safety, |
| DIV |  | Diagnostic Component Designs Multiple fibre connector at feedthroughs Multiple fibre connector on non-central cassettes. Feedthrough concept. | ( |  | 3 |  | IR Therm | CAD, Opt Eng |
| DIV |  | Port Mounting diag G03-Pressure Gauges [P21-EU] G04 Hydrogen Monitor, RGA [P28-US] Structure | ( | 0.1 | 3 | Any | US | Mech Eng, Instr, CAD |
| DIV |  | Bio-shield plug Construction, handling sequence | ( | 0.1 | 3 | Any | IT | Mech Eng, Instr, CAD |
|  |  | Cassette RH |  |  |  |  |  |  |
| DIV |  | Centr c. Pipe hand /CMM cask.Seq. Central c hand/CMM/cask.Seq CTM umbilical hand CMM cask.Seq. CTM hand/CMM/cask.Seq. Std assette hand/CMM/cask.Seq 2nd cassette hand/CMM/cask.Seq Pipe tool connector & cables in cell Cask connector & cables in cell CTM connectors & cables in cell Cassette refurbishment | ( |  | 3 |  | IT | RH |
|  |  | Diagnostic RH |  |  |  |  |  |  |
| DIV |  | Diag, rack/CMM/cask. Seq. | ( | 0.1 | 2 |  | [IT] | RH |
| DIV |  | Cassette Diagnostics Refurb Diag rack refurbishment | ( | 0.3 | 3 |  | [IT] | RH |
| DIV |  | diagnostic testing Test Assembly for cass, rack & diag Test Equip In Hot Side On Vac Bdy On Cold Side | ( | 0.2 | 1 |  |  | Mecxh Eng, CAD RH |

ITER-FEAT Procurement Package	                   	G 55 SP 22 00-08-05 W 0.1

Diagnostic Procurement Package 5.5.PN.03 Annex 1.2 		Diagnostic Divertor Closure Plates

2.3	Divertor Diagnostic Rack

Diagnostic components, such as waveguides and optical elements that are in the divertor port, are mounted on a supporting structure, referred to as the divertor diagnostic rack. Each is installed in its port, complete with diagnostic equipment, as one assembly (see Figs 1, 2 and 3 in Annex 2 pt 3). They extend from the back side of the divertor cassette to the port flange. The diagnostic components (and blocks of water-cooled shielding) may be at any position on the rack. Specifically in two of these there are sets of microwave waveguides. The requirements of the divertor diagnostic rack with microwave waveguides are used as the basis for this description.

The divertor diagnostic rack is a structure with diagnostic module locations and is similar for all racks. The diagnostic module locations are different for each port. Diagnostic modules, waveguides and shield blocks are attached to the rack at these locations. These elements are not part of the procurement package.

A rack comprises a welded space-frame assembly of base, side frames, bracing, carriage, locking and handling features and diagnostic module locations.

It carries water-cooling pipes from the port flange to the front portion, and to some of the attached diagnostic or shielding modules, where there is sufficient nuclear heating to necessitate cooling during long burn pulses. The cooling channel is in the form of 50mm diameter x 5mm wall stainless steel, seamless, piping welded to the rack components externally. This part only of the structure is subject to the leak tightness and leak testing requirements. All of the assembly is subject to limitations on in-vessel equipment regarding design, material, off-gassing, cleaning etc.

Diagnostic components (waveguides and optical elements) are mounted in the rack by simple bolting to reference locations.

The base, frame and bracing of the rack is stiff enough that it offers a suitable base for the support of optics and can be lifted cantilevered from the RH features on the outboard end. The base is used as the support when the rack is finally in the port or when it is in the maintenance area. When in position, defined by calibrated end stops, the diagnostic block is locked and the height is set. It is strong enough that it can support the components in-situ without deflection of more than 5mm anywhere along its length.

| Divertor Diagnostic Rack | Summary of Materials. Dimensions, Weight, Processes |
| --- | --- |
| Required pressure rating | Only the pipes 0.5 MPa |
| He leak rate | Only the pipes < 1.0x10 -10 Pam3s-1 |
| Structure | 1.0 m high x 0.7 m wide x 5.87 m long, total weight ~8t |
| Load Capacity | 0.75 m high x 0.50 m wide x 5.87 long, total weight ~3t |
| Materials | Stainless Steel 316L(N), seamless tube, 316 L (N)-IG, cold rolled structural sections. |
| Processes | Machining, TIG welding, glass bead blasted, cleaned. Leak testing of the tube. |
| Special materials | Vacuum compatible roller bearings, for base wheels |
| Typical dimensional tolerance of most parts | ± 5 mm achieved by jigging during fabrication |
| Tightest typical dimensional tolerance of some parts | ± 1mm achieved by machining after fabrication |

ITER-FEAT Procurement Package		IDoMS G 55 SP 3 00-07-06 W 0.1

Diagnostic Procurement Package 5.5.PN.05 		Diagnostic Divertor Components

| Deliverables | Qty |
| --- | --- |
| Side Plates | 62 |
| Central Mirror Mount | 11 |

#### 4.1	Instrumented Side Plate Assemblies

The side plate is 20mm thick x ~2.9 m x ~ 2.1m. It is made from one stainless steel forged plate, machined with the profile of the cassette. The left side plates are mirror images of right side plates. Welded to the back side is a 20mm thick x 100mm x 600mm long stiffening web. There are 2 x 12mm positioning dowel holes and  ~9 bolt holes for location and attachment onto the cassette. The plate is bored with 10mm water cooling channels. These are sealed with welded plugs, inter-connected and fed by a standard pair of remotely maintainable water cooling connections. There are 6 x 100mm through-holes to allow access to the divertor high heat flux component attachment pins. The instrumentation on the side plate varies for each plate and will be defined at procurement. Each sensor position requires a machined location or recess, tapped holes for attachment, and a groove for the sensor wiring loom. This extends from the sensor recess to the outboard end of the plate and is typically 10mm deep (into the plate) x ~20mm wide. Near the outboard end the grooves from different sensors merge. The routing of the grooves can be adjusted to best suit other features of the plate.

The diagnostic equipment is provided by ITER to the supplier. Each sensor has a wiring loom and electrical connector, pre-assembled and tested. The supplier is required to assemble these to the side plate, by bolting and locking with small welds.

#### 4.2	Microwave Wave-guide Side Plate Assemblies

The microwave wave-guide side plate assemblies have all of the features described above for the instrumented side plates. (They also support diagnostic sensors and instrumentation). In addition there is a series of grooves, typically 10 per plate, 15mm deep (into the plate) x 20mm wide. The routing of these grooves is fixed and cannot be adjusted to suit other features. At the outboard end of the plate is a block ~800 mm long x 280 mm wide x 750 mm high. This is used to support the wave-guide convertors and connectors. It is also made of stainless steel and is an integral part of the side plate structure and cooling channel arrangement. There are 2 x 12mm positioning dowel holes and  ~9 x 12mm counter-bored holes for location and attachment onto the cassette. The plate is bored with 10mm water cooling channels. These are sealed with welded plugs, inter-connected and fed by a standard pair of remotely maintainable water cooling connections. There are 6 x 100mm through-holes to allow access to the divertor high heat flux component attachment pins.

The diagnostic wave-guides are provided to the supplier by ITER. Each wave-guide is pre-assembled and tested. The supplier is required to install these into the side plate, by bolting and locking with small welds.

#### 4.3	Central Mirror Mount

The central mirror mount is a stainless steel fabrication 170mm square cross section x 965 mm long. The plate is bored with 10mm water cooling channels. These are sealed with welded plugs, inter-connected and fed by a standard pair of remotely maintainable water cooling connections.

The wall of the mount is typically 15mm thick and has bored cooling water channels. There are four penetrations for diagnostic viewing through the wall at various positions. These are typically 10 to 25 mm wide and up to 200 mm long. Internally there are machined reference faces and tapped holes for the mounting of up to four metal mirrors. At the base of the mirror mount is a flange region 250mm square x 50mm deep that is used to locate the mount in a recess in the bottom of the divertor cassette. There are 2 x 12mm positioning dowel holes and  ~12x 12mm counter-bored holes for location and attachment onto the cassette.

ITER will fit the diagnostic mirrors into the central mirror mounts and will fit the mirror mount to the diagnostic cassette.

## Figures

Fig.  1	Variety of Access at Divertor Level

Fig.  2 HHF Units are tolerant of pins, also therefore of thermocouple pockets

Fig.  3 Cassette Body

Fig.  4 Cassette Body Cuts, require Retention/Replacement of Cassette Stiffness

Fig.  5  Diagnostic Cassette Mirror Mount e.g. 1)

Fig.  6  Diagnostic Cassette Mirror Mount e.g. 2)

Fig.  7  Diagnostic Cassette Mirror Mount e.g. 3)

Fig.  8  Diagnostic Interfaces with Cassette, search for Acceptable Solutions – Input to IR Thermography Design

Fig.  9  Diagnostic Interfaces with Cassette, search for Standard Solutions

1 - Carbon Targets assumed

possible change to metallic target will significantly affect reflectivity

and possibly diagnostic approach

a – Viewable Target

b - Highly desirable extension of view required

c - view of typical target required, not edge of casstte or sub-target

2 - Standard Pumping slot has been used for outer and inner target viewing

aperture may close generally

d - viewing slot should keep full poloidal target view

3 - Dome Liner Gaps have been used for diagnostic viewing

e - central support may be introduced

will be cooled, should be able to support & cool mirror box

4 - Liner side have been used for diagnostic support (instrumented cassette)

may be removed (with mod e), substitute support is required

- Narrower liner side has been used as viewing gap

5 - Dome-Liner space sometimes used

avoided in some designs because of uncertainty about dome

used in other designs to get viewing access to b

6 - Under Liner space used - pumping only in one direction

7 - 'Pumping Aperture' not used for pumping on diagnostic cassettes

used for diagnostic access an cassette centre

f - may close for pumping & shielding reasons - maintain diagnostic apertures

8 -  Target- mid cassette

Thermocouples are required, use pin-hole feature

g - sacrificial (if necessary) in front of water channel and

h - permanent behind

9 - Cassette Body as sprung component

some diagnostic apertures required with

i - replacement stiffness

10 - Lock Actuator split into 2 systems, for some

11 - Anchor and cooling for Electrical Connectors

12 - Central Cassette Cut-Away

j - complete - a few central cassettes

k - holes- 1-2 cassettes

13 - Cassette Side Cut-away

2 cassettes

14 - Cassette Body Extension

part of Microwave waveguide system

part of LVNC

15- Side Plate attach cool view

Fig.  10  Design Changes in the Divertor Cassette are still Anticipated

[Design of the Private Region: A.Makhankov. Genoa Oct 26 2005]

Fig.  11  Diagnostic Cassette Side Plates

Fig.  12  Back Box Central Cassette -LVNC

Fig.  13  Back Box Central Cassette –Waveguide

Fig.  14  Connector & Connector Link

Fig.  15  In-Vessel Services Design, Port Cabling

Fig.  16  In-Vessel Services Design, Port Feedthroughs

Fig.  17  Port Diagnostic Racks

Fig.  18  Making Divertor Port Diagnostic Components Retractable or Insertable

Fig.  19  Making Divertor Port Diagnostic Components Retractable or Insertable

Fig.  20	Diagnostic Access to view the Divertor Plasma and Divertor Target Plates will change

# Footnotes

Possibly KO, HHI are responsible for the VV Port Extensions. Tasks will depend on the workscope & budget

Possibly KO

Possibly KO