RESEARCH AIRCRAFT DEPLOYMENT DOCUMENT

Gulfstream G-1 Aircraft

Pacific Northwest National Laboratory

P.O. Box 999, MSIN K9-30

Richland, WA  99352

J. M. Hubbe (509) 372-6134

A.  PROJECT IDENTIFICATION

| 1. Requestor's Name/Telephone number: | 2. Requestor's Address: | 3. Date: |
| --- | --- | --- |
| 4. Title that describes this activity: |
| 5. Abstract of proposed aircraft use: |

| B. RESEARCH SPONSOR |
| --- |
| 1. Name of sponsor: | 2. Contract officer name/address/telephone: | 3. Funding (check one): _____ Approved _____ Pending |
| 4. Title of research project: |
| 5. Principal Investigator(s): |

C.  FLIGHT OPERATIONS

| 1. Proposed deployment period including equipment installation and removal: Dates for equipment installation: From: _________________________ To: _________________________ Dates for field deployment: From: _________________________ To: _________________________ Dates for equipment removal: From: _________________________ To: _________________________ |
| --- |
| 2. Number of flights required: __________ | 3. Estimated duration of each flight: __________ |
| 4. Number of flights per day: __________ Number of consecutive flying days:__________ | 5. Are over water operations required? _____ Yes _____ No |
| 6. Proposed base for equipment installation: _________________ Proposed base for field deployment: ____________________ | 7. Alternate base(s) of operations: ________________________ |
| 8. Average flight radius from base: __________ | 9. Desired flight altitudes: __________ |
| 10. Typical takeoff time (local time): __________ Length of duty day: __________ | 11. Expected number of flight days within proposed deployment period: __________ |
| 12. Sketch or describe desired flight patterns, state priorities, and estimate number of flights for each (use additional sheets if needed): Pattern No. 1: |
| Pattern No. 2: |
| 13. Number of scientific observers (including PNNL science crew) required on each flight: _________ |

D.  SUPPLEMENTAL INFORMATION FOR COMPLIANCE WITH DOE 440.2A

The aircraft is operated by PNNL for the Department of Energy in accordance with DOE Order 440.2A.

1. Names, titles, affiliations, and duties of personnel onboard the aircraft (do not include PNNL pilots or PNNL scientific crew):

2. Analysis of hazards associated with proposed deployment (e.g., unusual maneuvers, meteorological conditions, terrain, heavy air traffic areas, on-board hazardous chemicals and radioactive materials, high voltages, heat, lasers):

3. Actions taken to mitigate associated hazards:

4. Expected flight conditions (e.g., visual flight rules, instrument flight rules, night flight, meteorological conditions):

5. Proposed deviations from Federal Aviation Regulations and justification (e.g., flights below 500 feet):

E.  SCIENTIFIC PAYLOAD

| 1. List of instruments that can be provided by the Research Aircraft Facility (check those required for this deployment). |
| --- |
| Instrument | Weight (lbs) | Size (inches) (19" panel or other) | Power Required (watts, amperes) | Type of power (volts DC, AC) | External Sensor/Probe Requirements | Check to Select |
| Permanent RAF Instruments |
| GPS (TANS & DSM) |  | Fuselage & Data Rack |  | 28VDC 12VDC | Fuselage top antennas | ( |
| Particle size (PCASP-300) | 40 | On Nose Boom | 215 W 180 W | 28 VDC 110 VAC | Nose boom | ( |
| Temperature (Rosemount Pt) |  | In Power Rack | 3 W | 28 VDC | Fuselage | ( |
| Pressure/Altitude (Rosemount absolute) |  | In Power Rack | 3 W | 28 VDC | Fuselage static | ( |
| Vector winds (5-port ΔP gust probe) |  | In Nose Cone | 9 W | 28 VDC | Nose cone | ( |
| Cabin temperatures (4) |  |  |  |  |  | ( |
| User Selectable RAF Instruments |
| Real-time Particles |  |  |  |  |  |  |
| Aerosol Inlet (BMI) | 100 (w/KVM) | 19W x 24D x 3U | 100 W | 110VAC | Window |  |
| Particle size (FSSP-300) | 40 | On Nose Boom | 300 W 100 W | 28 VDC 110 VAC | Nose boom |  |
| Particle image (OAP-2D) | 40 | Replaces either FSSP / PCASP | 300 W 100 W | 28 VDC 110 VAC | Nose boom |  |
| Liquid water content (KLWC-5) | 4 |  | 120 W | 110 VAC | Hatch |  |
| Liquid water content (PVM-100A) | 25 | 19W x 23D x 6H | 200 W 60 W | 28 VDC 110 VAC | Window |  |
| Ultrafine particle concentration (TSI 3025A, >3 nm) | 27 | 9.5W x 15D x 10H tray mounted | 200 W | 110 VAC | Aerosol inlet |  |
| Particle concentration (TSI 3010, >7 nm) | 12 | 8.5W x 7.5D x 7.5H tray mounted | 30 W | 110 VAC | Aerosol inlet |  |
| Aerosol light scattering, bscat (TSI 3563 3λ) | 51 | 43W x 12D x 10H rack-top mounted | 175 W 20 W laptop | 28 VDC 110 VAC | Aerosol inlet |  |
| Aerosol light absorption (Radiance PSAP) | 8 | 19W x 9.5D x 5.25H | 10 W | 110 VAC | Aerosol inlet |  |
| Real-time Gases |  |  |  |  |  |  |
| SO2 (TECO 43S) | 52 | 19W x 23D x 8.75H | 120 W | 110 VAC | Teflon inlet |  |
| O3 (TECO 49) | 52 | 19W x 23D x 8.75H | 180 W | 110 VAC | Teflon inlet |  |
| CO (TECO 48) | 65 | 19W x 23D x 8.75H | 200 W | 110 VAC | Teflon inlet |  |
| Radiometric Instruments |  |  |  |  |  |  |
| UV irradiance (Eppley) | 5 | In Power Rack |  | 28 VDC | Hatch, wing root |  |
| Surface/Sky IR temperature (PRT-5) | 23 | 19W x 16D x 8.75H | 20 W | 110 VAC | Window |  |
| Short-wave irradiance (Eppley pyranometer) | 2 | In Power Rack |  | 28 VDC | Hatch, wing root |  |
| Long-wave irradiance (Eppley pyrgeometer) | 2 | In Power Rack |  | 28 VDC | Hatch |  |
| Spectral radiation (PNNL MFR) | 20 | tray mounted | 120 W | 110 VAC | Hatch, wing root |  |
| Meteorological State |  |  |  |  |  |  |
| Dew-point temperature (GE 1011B) | 5 | In Power Rack | 85 W | 110 VAC | Window |  |
| Absolute Humidity(AIR lyman-alpha) |  | In Power Rack |  | 28 VDC | Fuselage |  |

| 2. List of collaborative instruments previously flown on G-1. Requestor is responsible for arranging for collaboration and updating table. |
| --- |
| Instrument (Mentor) | Weight (lbs) | Size (inches) (19" panel or other) | Power Required (watts, amperes) | Type of power (volts DC, AC) | External Sensor/Probe Requirements | Check to Select |
| Particle size & drop/crystal image, CAPS (Sennum, BNL) | 45 | On Nose Boom | 1680W | 28 VDC | Nose boom |  |
| BNL 3-Channel NO/NO2/NOy instrument (Springston, BNL) | 304 | Double wide rack + 15W x 31D x 11H for pump + O2 cylinder 6D x 24H with regulator | Main: 4.2-5.2 A Pump motor: 5-6 A | 110 VAC Pump 220 VAC | 1/4 ss forward facing. Pump requires exhaust port on aircraft. |  |
| TECO Model 49 O3 Detector (Springston, BNL) | 35 | 19W x 23D + 4 (for connections) x 8.75H rack mountable | 150 W | 110 VAC | 1/4 ss forward facing |  |
| TECO Model 48 CO Detector (Springston, BNL) | 65 | 19W x 23D + 3 (for connections) x 8.75H rack mountable | <1 A (~2 A for short periods) | 110 VAC | 1/4 ss forward facing |  |
| VUV CO Detector (Springston, BNL) | 20 pump extra | 19W x 23D + 3 (for connections) x 8.75H rack mountable | ~0.5 A | 110 VAC | 1/4 ss forward facing |  |
| TECO Model 43S SO2 Detector (Springston, BNL) | 43 pump extra | 19W x 23D + 4 (for connections) x 8.75H rack mountable | 100 W | 110 VAC | 1/4 ss forward facing |  |
| Carbonyl Sampling System (Lee, BNL) | 132 | Single wide rack | 10 A (nameplate) | 110 VAC | 1/4 ss forward facing |  |
| Peroxides (Lloyd via BNL) | 175 | Single wide rack | 500 W | 110 VAC | 1/4 ss forward facing |  |
| PAN-NO2 GC/Luminol (Gaffney/Marley, ANL) | 65 | rack mounted | 200 W | 110 VAC | 1/4 ss forward facing |  |
| ANL canister sampling rack (Doskey, ANL) | 127 | 43W x 17D x 42H | 600 W Pump off during takeoff and landing | 110 VAC | 1/4 ss rear facing |  |
| Proton-Transfer Reaction Mass Spectrometer (Jobson, PNNL) | 240 | 42W x 18D x 42H | 700 W MS 58 W pump 20 W flow control 100 W trap | 110 VAC | 1/4 ss rear facing |  |
| API-365 Mass Spectrometer (Spicer, BCO) | 815 | 60W x 24D x 44H | 1380 W | 220 VAC | 1/4 ss forward facing |  |
| BNL Calibrator with cylinders (Springston, BNL) | 92 | 19W x 24D + 2 (for connections) x 8.5H rack mountable 2 cylinders @ 6.5D x 22H with regulator | ~2 A (estimated) | 110 VAC |  |  |
| Aerosol sizing system (Brechtel via BNL) | ~270 | 19W x 24D x 39H | 3 A ~3.5 A pumps | 110 VAC 220 VAC pumps | Aerosol inlet |  |
| Aerosol Chemical Composition (Lee, BNL) | ~155 | Single wide rack | 6 A | 110 VAC | Aerosol inlet |  |
| Aerodyne Aerosol Mass Spectrometer (Jayne, ARI or Alexander, PNNL) | 410 | 42.5W x 24D x 44H | 880 W 20 W laptop | 220 VAC 110 VAC | Aerosol inlet |  |
| Time Resolved Aerosol Collector (Laskin, PNNL) | 15 | tray mounted | 200 W | 110 VAC | Aerosol inlet |  |
| Drum aerosol sampler (Disselkamp, PNNL) | 30 | tray mounted | 420 W | 110 VAC | Aerosol inlet |  |

| 3. List requirements of requestor-supplied instruments or equipment (attach drawings/photos; add rows as needed). All AC power is 60 Hz 1-phase. |
| --- |
| Instrument (Mentor) | Weight (lbs) | Size (inches) (19" panel or other) | Power Required (watts, amperes) | Type of power (volts DC, AC) | External Sensor/Probe Requirements |
| 4. List details of data recording requirements of requestor-supplied and collaborative instrumentation (add rows as needed) |
| Instrument | Aanalog or Digital | Signal Voltage Range | Resolution | Sample Rate | Remarks |
| 5. Describe special or unusual installation requirements: |
| 6. Describe hazardous materials required for collaborative and requestor-supplied instrumentation (toxic gases or liquids, flammable materials, radioactive sources, other): |
| Instrument Using Material | Material | MSDS Provided | Amount On Board (kg, liters) | On Board Usage |
| 7. Describe hazardous wastes produced or emitted by collaborative and requestor-supplied instruments: |
| Instrument or Process | Material | Amount Generated(kg, liters) | Physical Form (liquid, solid, gas) | Where Generated(ground, plane) | Provision for Management and Disposition |
| 8. Describe emissions of hazardous materials into the air (instrument, material, mass orvolume rate): |
| 9. Describe transportation provisions for moving hazardous materials to/from field site and enroute on aircraft: |

F.  GROUND SUPPORT FACILITIES

| 1. Describe any field site data access/processing requirements (floppy disk, tape, network, software compatibility, etc.): |
| --- |
| 2. Describe ground support needs for collaborative or requestor-supplied instrumentation: : : |
| On flight days: A. Pre-flight needs (prior to takeoff): Access _____ hrs. Power _____ hrs | B. Post-flight needs (after landing): Access _____ hrs Power _____ hrs | On non-flight days: C. Routine maintenance/calibration: Access _____ hrs Power _____ hrs |
| D. Any special support needs: |
| 3. Describe office, technical work area, storage, and logistical requirements (telephones, desks, etc.): |
| 4. Other information or remarks: |

G. OTHER PARTICIPATING AIRBORNE MEASUREMENT SYSTEMS

1. Will other airborne measurement systems (e.g., aircraft, lighter-than-air craft, radiosonde, tetroon, kite, tethersonde, etc.) participate in the proposed measurement program? _____ YES ______ NO If NO continue at Section H.

2. Identify system type(s) and provide name and telephone number for contact person(s):

3. How will the system(s) be used in proposed measurement program? Describe operations relative to the PNNL aircraft.

H.  APPROVALS

|  | Name (print) | Signatures | Date |
| --- | --- | --- | --- |
|  |  | Approve | Disapprove |  |
| 1. Requestor: |  |  |  |  |
| 2. PNNL Lab Safety: | T. Criscuolo |  |  |  |
| 3. PNNL Environmental Compliance Representative: | J. L. Akers |  |  |  |
| 4. PNNL Aviation Safety Point of Contact: | R. V. Hannigan |  |  |  |
| 5. Research Aircraft Facility Coordinator: | J. M. Hubbe |  |  |  |

cc:	PNNL Field Services Representative

PNNL Hazardous Materials Transportation

Comments: