Answers

Testing for Pearling

- Exactly 50 grams.

- Approximately 32 to 35 grams.

- Kernel texture, heat damage and injured-by-heat.

- The length of time for which the pearler has been standardized (a full pearl).

- One-third of the length of time for which the pearling machine has been standardized (a 1/3 pearl).

- The second hand of a watch or clock.

- On the total weight of the kernels after pearling.

- To prevent partially or unpearled kernels from entering the chamber drawer, thus causing an incomplete pearling operation.

- A scale approved by FGIS.

- (  Step 1 - Empty the pearling chamber and hull drawer.

(  Step 2 - Close the pearling chamber slide, and pour the test portion into the chamber.

(  Step 3 - Replace the funnel lid.

(  Step 4 - Start the pearler by turning the timer switch to the number of seconds for

which the pearler is standardized.

(  Step 5 - After the pearler stops, remove the pearled portion.

(  Step 6 - Weigh the pearled portion on a balance scale and record the weight on the

pan ticket.

- Barley and Sunflower seed.

- Heat damage and damaged-by-heat.

- It removes the hull by abrasion for the determination of heat damage and injured-by-heat in barley, and heat damage and damaged-by-heat in sunflower seed.

- 30 grams (( 1.5 grams).

- 14 to 16 grams.

- After the removal of mechanically separated foreign material.

- A full standardized pearl.