Monitoring the Performance of an Alternative Cover

Using Caisson Lysimeters

ABSTRACT

The U.S. Department of Energy (DOE) office in Grand Junction, Colorado, and the 
U.S. Environmental Protection Agency (EPA), Region 8, collaborated on a series of field lysimeter studies to design and monitor the performance of an alternative cover for a uranium mill tailings disposal cell at the Monticello, Utah, Superfund Site. Because groundwater recharge is naturally limited at Monticello in areas with thick loess soils, DOE and EPA chose to design a cover for Monticello using local soils and a native plant community to mimic this natural soil-water balance.

Two large drainage lysimeters fabricated of corrugated steel culvert lined with high-density polyethylene were installed to evaluate the hydrological and ecological performance of an alternative cover design constructed in 2000 on the disposal cell. Unlike conventional, low-permeability designs, this cover relies on (1) the water storage capacity of a 163-cm soil “sponge” layer overlying a sand-and-gravel capillary barrier to retain precipitation while plants are dormant and (2) native vegetation to remove precipitation during the growing season. The sponge layer consists of a clay loam subsoil compacted to 1.65 g/cm2 in one lysimeter and a loam topsoil compacted to 1.45 g/cm2 in the other lysimeter, representing the range of as-built conditions constructed in the nearby disposal cell cover.

About 0.1 mm of drainage occurred in both lysimeters during an average precipitation year and before they were planted, an amount well below the EPA target of <3.0 mm/yr. However, the cover with less compacted loam topsoil sponge had a 40% greater water storage capacity than the cover with overly compacted clay loam subsoil sponge. The difference is attributable in part to higher green leaf area and water extraction by plants in the loam topsoil. The lesson learned is that seemingly subtle differences in soil types, sources, and compaction can result in salient differences in performance. Diverse, seeded communities of predominantly native perennial species were established on both lysimeters during an extended 3-yr drought, highlighting the importance of a sound understanding of the local ecology and of implementing the science and methods of disturbed-land revegetation.

_____

*The Environmental Sciences Laboratory is operated by S.M. Stoller Corporation for the U.S. Department of Energy, Grand Junction, Colorado, under DOE Contract Number DE(AC01(02GJ79491.

INTRODUCTION

The Monticello, Utah, mill, built in 1942 to provide vanadium for World War II, later processed nearly 1.0 million tons of uranium ore and produced more than 2.5 million m3 of tailings before its closure in the early 1960s. The U.S. Department of Energy (DOE) office in Grand Junction, Colorado, Region 8 of the U.S. Environmental Protection Agency (EPA), and the State of Utah Department of Environmental Quality collaborated on the design and construction of a disposal cell to contain tailings and tailings-contaminated materials at Monticello. Remedial actions were regulated under the Comprehensive Environmental Response, Compensation, and Liability Act (CERCLA). The disposal cell design satisfied both (1) minimum technology guidance for hazardous waste disposal facilities [1] under subtitle C of the Resource Conservation and Recovery Act of 1976 (RCRA) and (2) design guidance for radon attenuation and 1,000-yr longevity [2] under the Uranium Mill Tailings Radiation Control Act of 1978 (UMTRCA).

Early cover designs constructed for UMTRCA disposal cells typically consist of compacted soil layers (CSLs), sand drains, and rock riprap intended to function as physical barriers to radon releases, water infiltration, and erosion.[2, 3] Typical RCRA cover designs also include prescribed physical barriers.[1] These conventional engineered covers, which attempt to resist natural processes rather than work with them, will likely require increasing maintenance.[4] After only a few years, CSLs have desiccated and cracked under routine wetting and drying conditions [5], and biological disturbances threaten cover integrity at many sites.[6, 7, 8, 9, 10] The goal at Monticello was to design an engineered cover system that enhances beneficial natural processes to help make long-term containment possible.[11]

At semiarid sites such as Monticello, relatively low precipitation (P), high potential evapotranspiration (PET), and thick unsaturated soils seem to favor long-term hydrologic isolation of buried waste.[12, 13, 14, 15] But simple P/PET relationships inadequately predict recharge in arid regions that can approach 60% of precipitation in coarse-textured soils denuded of vegetation.[16] At arid and semiarid waste disposal sites, recharge can be minimized with thick, fine-textured soil layers that store precipitation in the root zone where evapotranspiration (ET) seasonally removes it.[17, 18, 19, 20, 21] Capillary barriers consisting of coarse-textured sand and gravel placed below this soil “sponge” layer can enhance water storage and limit unsaturated flow.[22, 23] To be accepted by regulators, end users must demonstrate that the water balance of these alternative cover designs is at least equivalent to conventional designs.

Weighing and drainage lysimeters offer the most direct and reliable means for evaluating soil-water balance of alternative cover designs.[24] Lysimeters have been used for many years to evaluate irrigation needs [25] and have been used more recently to test the hydrologic performance of waste landfill cover designs.[26, 27, 28, 29] DOE and EPA conducted a series of field lysimeter experiments at Monticello beginning in 1990 to help design and then monitor the performance of a disposal cell cover that would rely in part on a high soil water-storage capacity and high ET to limit infiltration and leaching of contaminants from tailings.[30]

This paper presents the status of a lysimeter study of an alternative cover design at Monticello, Utah. The purposes of this study are (1) monitor the hydrological and ecological performance of the Monticello design for as-built conditions in the actual cover and (2) evaluate the general application of the design as an alternative to EPA design guidance for arid and semiarid sites.

STUDY AREA: CLIMATE, SOILS, AND VEGETATION

The study area is adjacent to the tailings disposal cell 2 km south of Monticello, Utah. Monticello is semiarid with cold, windy winters and mild summers. The 30-yr average (1961(1990) annual precipitation is 39 cm. The average minimum January temperature is 
-10.5 °C and the average July maximum temperature is 28.9 °C. The year can be characterized as three seasons with respect to soil-water balance: November through March, the season of deep infiltration and moisture accumulation in soils (average precipitation equals 16 cm); April through June, a moisture-depletion period when plants become water stressed (average precipitation equals 6 cm); and July through October, a season of variable shallow moisture accumulation and depletion resulting from monsoonal convection storms (average precipitation equals 17 cm). Annual snowfall averages 160 to 170 cm.

The soils within the footprint of the Monticello disposal cell formed in Pleistocene loess.[31] The taxonomic classification is Monticello very fine sandy loam.[32] The soil texture varies from clay loam to sandy loam. The natural vegetation of the Monticello very fine sandy loam at the disposal cell site consists primarily of Western wheatgrass (Pascopyrum smithii [Rydb.] Á. Löve), Sandberg bluegrass (Poa secunda J. Presl), blue grama (Bouteloua gracilis [Kunth] Lag.), mountain big sagebrush (Artemisia tridentata Nutt. subsp. vaseyana [Rydb.] Beetle), and rubber rabbitbrush (Ericameria nauseosa [Pallas ex Pursh] Nesum & Baird) with a canopy coverage of 50% to 60%.[32]

COVER DESIGN AND LYSIMETER INSTALLATION

Installation of a cover on the Monticello disposal cell similar to the RCRA Subtitle C design [1] began in fall 1998. The disposal cell has a double liner and a leachate collection system with a design permeability of 1 x 10-9 cm/s. EPA accepted a design with a geomembrane and a CSL in the cover to ensure that water flux through the cover will not exceed flux through the liner—at least in the short term. Because of the uncertain durability of the geomembrane and the CSL, the design incorporates an alternative cover system as the primary means for limiting percolation for the long term.

Alternative Cover Design

The Monticello alternative cover design (Figure 1) is fundamentally an ET cover with a capillary barrier.[33] The design relies on the water-storage capacity of a 163-cm fine-textured soil layer (sponge) overlying a 38-cm sand capillary barrier layer to retain precipitation until it is seasonally removed by vegetation (solar pumps). Leakage into the sand should occur only if water accumulation at the sponge/sand layer interface approaches saturation and tensions decrease sufficiently for water to enter the larger pores of the sand layer. Hydraulic performance can be evaluated as the probability that, over time, ET is sufficient to prevent water accumulation in the soil sponge from exceeding the storage capacity.[11]

Figure 1.  Alternative cover design tested in caisson lysimeters 
and constructed on a uranium mill tailings disposal cell at the 
Monticello Superfund Site.

Other components of the Monticello design either facilitated construction or were included to enhance long-term performance. A geotextile fabric maintains the fine-grained soil/coarse sand layer discontinuity during construction and until soil aggregation occurs by natural pedogenic processes.[34] The combination of vegetation and gravel admixture controls erosion. Vegetation and organic litter disperse raindrop energy, shield underlying fine soils, increase infiltration, reduce water flow and surface wind velocity, bind soil particles, and filter sediment from runoff.[35] Gravel mixed into the surface helps control erosion when vegetation is sparse (following construction, fires, drought, etc.), mimicking conditions that lead to the formation of gravel pavements. The gravel admixture can control both wind and water erosion [36, 37] and, functioning as a mulch, can enhance seedling emergence and plant growth.[20]

The Monticello design includes frost protection, deterrents for biointrusion, and other attributes for plant growth. The depth is more than adequate to isolate the underlying RCRA components (CSL and geomembrane) from frost damage.[38] The soil sponge thickness is also the primary biointrusion deterrent. Water retention in the soil sponge creates habitat for relatively shallow-rooted plants, and the thickness of the sponge exceeds the depth of most burrowing vertebrates in the Monticello area. A layer of cobble-size rock 30.5 cm above the capillary barrier is an added deterrent should deeper burrowers, such as prairie dogs, move into the area in response to climate change. Fine-textured sponge soil fills the interstices of the rock layer, preventing it from behaving like a second capillary barrier. The topsoil layer, obtained from the root zone of the borrow area, has physical and hydraulic properties similar to the rest of the soil sponge, but also contains available nutrients, propagules, and microorganisms (e.g., mycorrhizae) needed for the establishment of a sustainable plant community.

Lysimeter Installation and Soil Materials

We installed two large drainage lysimeters to evaluate the range of as-built conditions in the actual Monticello alternative cover. Lysimeter 1 closely matches the materials and compaction as built during the latter stages of construction. Lysimeter 2 mimics less desirable materials and compaction as built during the early stages of construction.

Pleistocene eolian soils from the lysimeter excavation were used for the fine-grained sponge layers in Lysimeter 1. The upper 61 cm was stockpiled topsoil that had been separated from subsoils. Lysimeter 1 sponge soil layers were compacted to about 1.45 g/cm3, closely matching the dry-weight bulk density of native Monticello very fine sandy loam. Fine-grained sponge soils for Lysimeter 2, taken from the disposal cell stockpile, consisted of a mixture of loess soils and underlying pediment paleosols, the material used during early stages of the cover construction. Lysimeter 2 sponge layers were compacted to about 1.65 g/cm3, closely matching the bulk density achieved during the early stages of construction.

A combination of sieve and hydrometer methods [39] was used for soil particle-size analysis (Table I). The U.S. Department of Agriculture (USDA) soil textural classes for Lysimeters 1 and 2 sponge soils are loam and clay loam, respectively. Because sample volumes were inadequate for accurate analysis of gravel splits, representative sampling and analysis of all materials will be conducted at the conclusion of the study.

Table I.  Soil Particle Sizea and Dry-Weight Bulk Densityb for Lysimeters 1 and 2.

| Layer | Classc | CG (%) | FG (%) | VCS (%) | CS (%) | MS (%) | FS (%) | VFS (%) | Si (%) | Cl (%) | B.D.b (g/cm3) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Lysimeter 1 |
| Gravel Admixture | GL | 13 | 2 | ( | ( | 1 | 7 | 23 | 31 | 23 | ( |
| Fine-Grain Topsoil | L | ( | ( | ( | 1 | 1 | 5 | 24 | 45 | 24 | ( |
| Fine-Grain Soil A | L | 3 | 2 | 2 | 2 | 2 | 7 | 23 | 36 | 27 | 1.44 |
| Biointrusion Barrierd | GL | 38 | 11 | 2 | 3 | 4 | 6 | 9 | 15 | 12 | ( |
| Fine-Grain Soil B | L | 3 | 9 | 5 | 5 | 3 | 7 | 15 | 29 | 24 | 1.45 |
| Capillary Barrier | S | ( | 37 | 9 | 15 | 21 | 12 | 3 | 2 | 1 | ( |
| Compacted Soil Layer | L | 4 | 1 | 1 | 1 | 2 | 7 | 18 | 39 | 27 | 1.75 |
| Lysimeter 2 |
| Gravel Admixture | GClL | 13 | 2 | 3 | 4 | 4 | 6 | 15 | 29 | 24 | ( |
| Fine-Grain Soil Ae | ClL | ( | 1 | 1 | 1 | 1 | 8 | 30 | 28 | 30 | 1.64 |
| Biointrusion Barrierd | GL | 49 | 16 | 2 | 1 | 2 | 3 | 5 | 13 | 9 | ( |
| Fine-Grain Soil Be | ClL | ( | 10 | 3 | 4 | 5 | 6 | 15 | 31 | 26 | 1.66 |
| Capillary Barrier | S | ( | 38 | 13 | 9 | 12 | 20 | 3 | 3 | 2 | ( |

aUSDA soil particle-size classes: CG = coarse gravel (10(70 mm); FG = fine gravel (2(10 mm); VCS = very coarse sand (1(2 mm); CS = coarse sand (0.5(1 mm); MS = medium sand (0.25(0.5 mm); FS = fine sand (0.1(0.25 mm); VFS = very 
fine sand (0.05(0.1 mm); Si = silt (0.002(0.05 mm); Cl = clay (<0.002 mm).

bDry-weight bulk density (B.D.) was determined using a nuclear gauge. Sample size n ≥ 3.

cUSDA soil texture classes: L = loam, GL = gravely loam, ClL = clay loam, GClL = gravely clay loam, S = sand. Only fine-grained splits (VCS and finer) were used for soil textural classification.

dGravel percentages in the biointrusion layer are inaccurate because of inadequate sample volumes.

eGravel percentages in the fine-grain layers in Lysimeter 2 will be determined at the conclusion of the study.

Construction of the first of two caisson lysimeters (Lysimeter 1) began in fall 1998. We excavated a pit approximately 8 m in diameter by 3 m in depth, using a track hoe, at an existing lysimeter test facility [30] adjacent to the Monticello tailings disposal cell. Eolian and pediment soils excavated from the pit were segregated in stockpiles. A corrugated steel culvert, 3.05 m in diameter by 2.75 m in depth, forms the walls of Lysimeter 1. Access to instrumentation is through an adjacent caisson, 1.52 m in diameter by 3.66 m in depth. We bolted the steel culverts (lysimeter caisson and instrument access caisson) together, lowered them into the pit using a track hoe bucket, and aligned them vertically. We installed Lysimeter 2 adjacent to Lysimeter 1 in fall 1999 (Figure 2). Lysimeter 2 is 2.44 m deep. Caissons were partially backfilled to create a compacted floor with a 20:1 slope and a drainage port at the low end.

The caisson lysimeters were lined with 40-mil high-density polyethylene (HDPE), filled with water, covered with plastic, and leak tested using a manometer. HDPE tubes, welded to drainage holes cut into the lower end of the HDPE floor liner, were inserted through ports into the access caisson. We constructed cover layers in lysimeters by marking soil lift heights on the interior walls, hauling and dumping stockpiled materials into the lysimeters, spreading and wetting lift materials, and then tamping lifts to achieve soil bulk-density specifications. Bulk density was measured with a nuclear density gauge (Troxler Inc.). Instrumentation was installed as the cover layers were constructed. Twenty-cm wide HDPE flaps were heat-welded to the HDPE walls, at a depth of about 60 cm below the lips of the lysimeters, to divert any preferential flow of water along the sidewall back into the soil mass.

Plant Establishment

Revegetation goals for ET covers include plant communities that (1) are well-adapted to the engineered soil habitat, (2) are capable of high transpiration rates, (3) limit soil erosion, and 
(4) are structurally and functionally resilient.[40] Seeding of monocultures or low-diversity mixtures on engineered covers is common. Instead, revegetation should attempt to emulate the structure, function, diversity, and dynamics of native plant communities in the area. Diverse mixtures of native and naturalized plants will maximize water removal and remain more resilient given variable and unpredictable changes in the environment resulting from pathogen and pest outbreaks, disturbances (overgrazing, fire, etc.), and climatic fluctuations. Local indigenous ecotypes that have been selected over thousands of years are usually best adapted. In contrast, the exotic grass plantings common on engineered covers are genetically and structurally rigid, are more vulnerable to disturbance or eradication by single factors, and will require continual maintenance. Successful establishment of a diverse and resilient plant community requires the enlistment of practitioners knowledgeable in the science and methods of disturbed land revegetation.

Revegetation of the lysimeters matched the specifications and methods used for the adjacent tailings disposal cell.[41] We seeded the lysimeters in September 2000 with a mixture of grasses, forbs, and shrubs in an attempt to mimic the potential natural vegetation for the borrow soils and local climate (Table II). Seed was hand-broadcasted, raked, and tamped into the soil surface, and the surface was mulched with straw. Several species were also transplanted. Plants selected for the lysimeters are perennial, native, cool-season species except as indicated in Table II.

Figure 2.  Plan view (top) and cross section (bottom) of instrumentation in the lysimeter and access caissons. Water Content Reflectometers, thermocouples, and root observations tubes, shown separately for purposes of illustrating layouts and depths, were all installed in both lysimeters.

PERFORMANCE MONITORING METHODS AND RESULTS

Evaluating the performance of alternative covers depends on careful analysis of climate, soil hydrology, and plant ecology. Lysimeters enable us to evaluate performance of the cover as a system—an integrated whole—over diurnal, seasonal, and yearly time scales. Our monitoring instrumentation and methods focused on the components of the soil-water balance (precipitation, changes in water storage, drainage, and evapotranspiration) and on plant community composition and relative abundance. Monitoring began during the 1999 growing season for Lysimeter 1 and a year later for Lysimeter 2. This section presents the meteorological, soil-water balance, and vegetation monitoring methods and results as of October 2003.

Table II.  Species Planted on the Lysimeters.

| Scientific Name | Common Name | PLS/Acrea |
| --- | --- | --- |
| Shrubs |  |  |
| Ericameria nauseosa | Rubber rabbitbrush | 1.5 |
| Purshia tridentata | Antelope bitterbrush | 1.0 |
| Artemisia tridentate var. tridentata | Mountain big sagebrushb | 0.5 |
| Artemisia tridentata var vaseyana | Basin big sagebrush | 0.1 |
| Artemisia tridentate var. wyomingensis | Wyoming big sagebrush | 0.05 |
| Forbs |  |  |
| Linum lewisii | Blue flaxb | 2.0 |
| Astragalus cicer | Cicer milkvetchc | 1.6 |
| Sphaeralcea coccinea | Scarlet globemallowd | 0.5 |
| Sphaeralcea grossulariifolia | Gooseberry globemallowd | 0.5 |
| Erigeron speciosus | Aspen daisy | 0.15 |
| Achillea millefolium var. lanulosa | Common yarrow | 0.12 |
| Aster tanacetifolius | Prairie astere | 0.05 |
| Grasses |  |  |
| Bromus carinatus | Mountain bromeb | 4.0 |
| Elymus lanceolatus | Thickspike wheatgrass | 3.0 |
| Pascapyrum smithii | Western wheatgrassb | 3.0 |
| Stipa comata | Needle and thread grass | 2.0 |
| Stipa hymenoides | Indian ricegrass | 2.0 |
| Bouteloua gracilis | Blue gramad | 1.0 |
| Hilaria jamesii | Galleta grassd | 1.0 |

aPLS/acre = pure live seed per acre.

bPlants seeded and transplanted onto small lysimeters.

cAnnual or biennial.

dWarm season (C4) species.

eNot native.

Soil-Water Balance

The primary objective of the caisson lysimeter study is to evaluate the soil-water balance of the as-built cover. The overall soil-water balance of a cover would include inputs of precipitation (P) and run-on (Ri) and outputs of evapotranspiration (ET), drainage past plant roots in the soil profile (D), and runoff (Ro). Soil-water storage changes (ΔS) can be expressed as

ΔS = P + Ri ( ET ( D ( Ro.		(Eq. 1)

The caisson lysimeter soil surfaces are isolated from Ri and Ro, thus ET can be estimated using a simplified water balance equation

ET = P ( D ( ΔS,		(Eq. 2)

where ET, P, and ΔS are recorded as linear units (mm or cm) of water.

Direct measurement of all water-balance terms was not possible. For the Monticello study, precipitation, drainage, and water storage changes are monitored, and actual ET is estimated by difference. Potential ET can be estimated by calculation of the energy budget (Penman-Montieth equation) using the field parameters of wind speed, relative humidity, solar radiation, and air temperature.

##### Meteorological Conditions. A weather station was installed to monitor meteorological conditions in July 2000. The meteorological station consists of a 3-m-high tripod anchored in concrete with supports for sensors and enclosures. The weather station was configured to provide data for the following parameters:

| Parameter | Sensor |
| --- | --- |
| Wind speed | Cup anemometer |
| Wind direction | Vanes that use precision potentiometer |
| Solar radiation | Thermopile pyranometer |
| Air temperature | Platinum resistance temperature detector |
| Relative humidity | Capacity sensors that use integral signal conditioning |
| Precipitation | Tipping-bucket rain gauge |

The weather station uses a programmable data logger (CR23X, Campbell Scientific, Inc., Logan, Utah) that records sensor measurements and stores data. Sensory measurements are stored hourly and daily. Conditional outputs, such as rainfall intensity, are also processed and stored. The data logger is wired to alternating current and data are downloaded via phone modem.

Total annual precipitation has been less than the 30-yr average (39 cm) since the lysimeters were planted in 2000 (Table III). The 2002 growing season was particularly dry, with winter and spring precipitation about 50% and 15% of normal, respectively. Precipitation was only 57% of normal between November 2000 and June 2002, the critical period for plant establishment.

##### Table III. Annual and Seasonal Precipitation (cm) at Monticello.

| Yeara | Annual | November(Marchb | April(Juneb | July(Octoberb |
| --- | --- | --- | --- | --- |
| Average | 39.0 | 16.0 | 6.0 | 17.0 |
| 2000 |  |  |  | 17.4 |
| 2001 | 25.7 | 10.6 | 5.7 | 9.4 |
| 2002 | 22.9 | 8.0 | 0.9 | 14.0 |
| 2003 |  | 21.0 | 11.0 |  |

aAnnual precipitation calculated for November through October of the current year.

bYearly precipitation characterized as three seasons with respect to soil-water balance: November through March is the season of deep infiltration and moisture accumulation in soils; April through June is a moisture-depletion period when plants become water stressed; and July through October is a season of variable shallow moisture accumulation and depletion resulting from monsoonal convection storms.

##### Soil-Water Storage and Drainage Measurements.  Soil moisture and water storage are monitored with CS-615 water content reflectometers (WCRs) manufactured by Campbell Scientific, Inc. (Logan, Utah). WCRs consist of two, 30-cm-long parallel rods attached to an electronic signal generator. A pulsed wavelength traveling down a coax, or waveguide, is influenced by the type of material surrounding the conductors. If the dielectric constant of the material is high, the signal propagates slower. Because the dielectric constant of water is much higher than most other materials, a signal within a wet medium propagates slower than in the same medium when dry. The reflectometer measures the effective dielectric as a pulse transit time, which in turn is calibrated against water content. Changes in soil moisture are determined by reading the WCR probes hourly.

In each lysimeter, 18 WCRs monitor water content within the cover layers with three replicate measurements at six depths:

| Depth (cm) | Material |
| --- | --- |
| 10 | Gravel admixture layer |
| 45 | Topsoil layer of soil sponge |
| 90 | Fine-grain soil sponge layer |
| 120 | Animal intrusion barrier layer |
| 160 | Soil sponge layer just above capillary interface |
| 200 | Capillary barrier layer, near the bottom |

Additional WCRs monitor water content in Lysimeter 1 with three replicate measurements at a depth of 240 cm in the compacted soil layer (radon barrier) and three replicate measurements at a depth of 290 cm in native soil below the engineered cover.

Because probe-to-probe variability is insignificant [42], we calibrated WCRs after the lysimeters were filled. WCR calibrations were determined for all soil materials using 30-cm-diameter by 80-cm-deep polyvinyl chloride (PVC) calibration cells. Soil materials were compacted in 10-cm lifts to match the dry-weight bulk density attained in the lysimeters. Calibrations for each material were obtained for soil moisture contents ranging between air dry and saturation, from approximately 8% to 40% by volume. Calibrations were repeated for three different WCRs to check probe-to-probe variability. WCRs were inserted vertically near the center of a filled PVC cell until the rods were completely covered with soil, five readings were taken for each soil/moisture combination with the probe embedded in a different location each time, and then five volumetric samples were collected spanning the depth of the WCR rods.

Water-content reflectometers, thermocouples, and root observations tubes were placed in shallow trenches cut into the soil lifts. Root observation tubes consist of 5-cm-diameter by 3-m-long clear Lexan cylinders placed horizontally from sealed ports in the access caisson through the center of the lysimeter caisson. Table IV presents layer materials and depths, WCR and thermocouple placement depths, mean WCR calibration coefficients, and depths of root observation tubes. Drainage, soil water content, and soil temperature data are monitored hourly, stored in the microprocessor on site, and downloaded periodically via phone modem.

Table IV.  Cover Layers, WCR Placement Depths and Calibration, and Root Tube Depths.

| Layer Material | Layer Depth (cm) | WCR Depth (cm) | WCR Calibration Coefficients | Root Tube Depth (cm) |
| --- | --- | --- | --- | --- |
|  |  |  | C0 | C1 | C2 |  |
| Lysimeter 1 |
| Gravel Admix | 0(20 | 10 | -0.1001 | -0.0069 | 0.1958 |  |
| Topsoil | 20(61 | 46 | -0.1001 | -0.0069 | 0.1958 | 30 |
| Sponge Soil | 61(102 | 90 | -0.4544 | 0.6998 | -0.1272 | 76 |
| Biobarrier | 102(133 | 120 | -0.2166 | 0.2362 | 0.0815 |  |
| Sponge Soil | 133(163 | 160 | -0.4544 | 0.6998 | -0.1272 | 147 |
| Sand | 163(201 | 200 | 0.4161 | -1.2964 | 0.9926 | 173 |
| Compacted Soil | 201(274 | 240 | -0.4544 | 0.6998 | -0.1272 |  |
| Native Soil | 274( | 290 | -0.4544 | 0.6998 | -0.1272 |  |
| Lysimeter 2 |
| Gravel Admix | 0(20 | 10 | -0.4544 | 0.6998 | -0.1272 |  |
| Sponge Soil | 20(61 | 45 | -0.4544 | 0.6998 | -0.1272 | 30 |
| Sponge Soil | 61(102 | 90 | -0.4544 | 0.6998 | -0.1272 | 76 |
| Biobarrier | 102(133 | 120 | -0.2166 | 0.2362 | 0.0815 |  |
| Sponge Soil | 133(163 | 160 | -0.4544 | 0.6998 | -0.1272 | 147 |
| Sand | 163(201 | 200 | 0.4161 | -1.2964 | 0.9926 | 173 |

Soil Water Responses. Time series of drainage and water storage changes show conspicuous seasonal variability and an overall drying trend (Figure 3). Drainage did not exceed 0.1 mm/yr, well below the EPA target of <3.0 mm/yr. The only drainage occurred in spring 2000. The lysimeters were not planted until 2000 to allow water storage to build to the maximum limit for each soil type. No measurable drainage occurred during the dry years while vegetation was maturing.

Time series of soil-water storage are displayed as millimeters of water in Figure 3. In both lysimeters, seasonal high and low water storage occurred in mid-to-late spring and mid-to-late fall, respectively, depending on the amount and seasonality of precipitation, the soil type and

Figure 3.  Soil-water storage time series in Lysimeter 1 (less compacted loam 
soil sponge) and Lysimeter 2 (more compacted clay loam soil sponge) between 
July 1999 and August 2003.

compaction, and the maturity of vegetation. The maximum storage in both lysimeters occurred in spring 2000 before plants became established. Because drainage also occurred at that time, water storage may have reached the maximum limit for each soil type: about 440 mm in Lysimeter 1 and 400 mm in Lysimeter 2. The lower maximum storage limit for Lysimeter 2 as compared with Lysimeter 1 may be attributable to a lower porosity in the more compacted clay loam than in the less compacted loam. Once vegetation established during the dry years, the seasonal peak storage did not approach the limit in either lysimeter and no drainage occurred. The peak in spring 2002 was virtually nonexistent because precipitation was virtually nonexistent.

Seasonal low water-storage levels also differed between the two lysimeters. The difference is most likely attributable to plant water extraction (evapotranspiration). During the 2000 growing season, before plants established, the seasonal low remained at about 280 mm; only about a 
5-mm difference was observed between lysimeters. After plants became established, water storage in the less compacted loam (Lysimeter 1) dropped below 200 mm, about 30 mm below water storage in the compacted clay loam (Lysimeter 2). The water storage capacity of a soil layer can be calculated as the difference between the maximum storage limit and the lowest measured water storage level after the plant water potential reaches the wilting point. If this definition is used, the water storage capacity for the less compacted loam soil in Lysimeter 1 (about 250 mm) is more than 40% greater than the more compacted clay loam in Lysimeter 2 (about 175 mm). Soil type and layer construction practices can have significant effects on the performance of alternative covers.

Vegetation Composition and Abundance

The water storage data in Figure 3 show that the hydrologic performance of the Monticello cover relies, in part, on the establishment and resilience of a diverse plant community. Plant canopy structure plays a fundamental role in processes involving the interaction of plant communities and their environment, such as ET [43] and biomass productivity.[44] Plant canopy structure can be thought of as the amount and organization of aboveground plant material. Canopy structure may include the size, shape, orientation, and distribution of various plant parts such as leaves, stems, branches, flowers, and fruits. The amount of leaf and stem material in a canopy can be represented by measurements of leaf area index (LAI) and productivity. LAI, the leaf area per unit of ground area, is one of the more useful measures of plant canopy structure because it is also an index of the relative transpiration potential of the canopy. Productivity is the rate of change in biomass per unit time, such as from one year to the next. Percent cover, a more common measure of plant abundance, is the percentage of a unit area (1 m2, for example) beneath the canopy of a given species.

Methods.  Plant species composition and abundance were measured on the caisson lysimeters near the end of the growing seasons in 2002 and in 2003. Species composition and percent cover were measured over the entire 7.3-m2 lysimeter surface. The lysimeter surface was divided into 50- by 100-cm quadrats delineated with string. A quadrat is an area of ground surface delimited for plant measurement. All plant species in each quadrat were recorded. We used an ocular point-intercept sampling method [45] to measure percent cover in each quadrat.

LAI and productivity of green vegetation (current year’s growth) were sampled in half of the quadrats by harvesting green leaf material and running the leaves through a Licor, Inc. LI-3100 Area Meter (www.licor.com). Green leaf material was harvested by hand or cut with shears, placed in paper bags, and processed soon after returning to the laboratory. Artemisia tridentata green leaves were not removed because defoliation can stress or kill the plant. Accuracy of the LI-3100 Area Meter was assessed with a 10-cm2 calibration disk periodically passed through the meter. Green LAI was computed by dividing the total green leaf area in a quadrat by the quadrat area. Green leaf material was then air dried in paper bags and weighed to estimate productivity. We considered that samples were dry if we measured no change after repeated weighings for 
several days.

Species Composition, Cover, LAI, and Productivity.  Species growing on the lysimeters were grouped based on revegetation acceptance criteria (Table V). Total percent cover for all plants growing in lysimeters, when averaged over years and lysimeters (37.1%, S.E.=0.6%, n = 4), is close to the minimum 40% cover criterion.[41] However, as much as 20.6% cover or 56% relative cover consisted of species either not listed as a permissible species or listed as noxious and non-noxious weeds. Only about 16.5% of the cover consisted of permissible species, well below the requirement. Western wheatgrass (Pascopyrum smithii), the dominant native grass growing on Monticello very fine sandy loam, was also the most abundant species on the lysimeters. Six native species not listed as permissible in the acceptance criteria

Table V.  Plant Species Composition and Percent Cover.

| Scientific Namea | Common Namea | % Cover |
| --- | --- | --- |
| Permissible Speciesb | 16.5 |
| Grasses |  | 15.1 |
| Bromus inermis | Smooth brome | 2.2 |
| Pascopyrum smithii | Western wheatgrass | 10.0 |
| Thinopyrum intermedium | Intermediate wheatgrass | 2.9 |
| Forbs |  | 1.4 |
| Astragalus spp | Milk vetch | 0.4 |
| Sphaeralcea spp | Globemallow | * |
| Shrubs |  | 1.0 |
| Artemisia tridentata | Big sagebrush | 0.7 |
| Ericameria nauseosa | Rubber rabbitbrush | 0.3 |
| Non-Noxious Weed Speciesb | 0.5 |
| Kochia scoparia | Mexican fireweed | * |
| Salsola kali | Russian thistle | 0.5 |
| Not Listed as Permissible or Not Permissibleb | 20.1 |
| Grasses |  | 16.0 |
| Achnatherum hymenoides | Indian ricegrass | 0.3 |
| Agropyron cristatum | Crested wheatgrass | 1.1 |
| Bromus tectorum | Cheatgrass | 0.5 |
| Elymus lanceolatus | Streambank wheatgrass | 0.7 |
| Elymus trachycaulus | Slender wheatgrass | 2.8 |
| Pseudoroegneria spicata | Bluebunch wheatgrass | 3.1 |
| Hesperostipa comata | Needle and thread | 0.3 |
| Unidentifiable perennial grasses | 7.2 |
| Forbs |  | 4.1 |
| Achillea millefolium | Common yarrow | * |
| Amaranthus blitoides | Mat amaranth | * |
| Chenopodium album | Lambsquarters | * |
| Linum perenne | Blue flax | 2.6 |
| Medicago sativa | Alfalfa | 1.5 |
| Taraxacum officinale | Common dandelion | * |
| Ground Surface | 68.3 |
| Soil | 30.8 |
| Rock | 10.4 |
| Litter | 27.1 |

aScientific and common names are consistent with the USDA Plants National
Database (http://plants.usda.gov).

bPlant categories are from revegetation acceptance criteria for the Monticello cover.[41]

###### (Achnatherum hymenoides, Elymus lanceolatus, Elymus trachycaulus, Elymus trachycaulus, Pseudoroegneria spicata, Hesperostipa comata, and Achillea millefolium) should be included 
as acceptable. The total cover of all native and permissible species, at least 23.7%, is better 
than expected considering that it occurred during the driest 3 consecutive years on record 
for Monticello.

Total plant cover remained consistent between lysimeters and years (Figure 4). Green LAI, a better measure of the transpiration potential than percent cover, was significantly greater in 2002 on the less compacted loam (Lysimeter 1) than on the overly compacted clay loam (Lysimeter 2). Greater transpiration loss may partially explain the seasonally lower water storage values and consistently greater water storage capacity of the less compacted loam. As an apparent anomaly, productivity was highest on Lysimeter 2 in 2003, possibly attributable to the combination of a wet late summer, different species composition, and a later sampling date in 2003. Much of the high 2003 biomass on Lysimeter 2 is thick-stemmed alfalfa (Medicago sativa) that re-greened following late summer rains.

Figure 4.  Percent cover, green LAI, and annual dry-weight biomass (productivity) comparing Lysimeters 1 and 2 in 2002 and 2003. Within-parameter bars with the 
same letter are not significantly different (P <0.05).

SUMMARY

Two large drainage lysimeters fabricated of steel caissons lined with HDPE were installed to evaluate the hydrological and ecological performance of an alternative engineered cover constructed in 2000 on a uranium mill tailings disposal cell at the Monticello, Utah, Superfund Site. The hydrological performance of the Monticello design relies on the water storage capacity of a 163-cm soil “sponge” layer overlying a capillary barrier of fine gravel and sand, to retain precipitation while plants are dormant, and on native vegetation to seasonally remove precipitation during the growing season. The sponge layer consists of a clay loam subsoil compacted to 1.65 g/cm2 in one lysimeter and a loam topsoil compacted to 1.45 g/cm2 in the other lysimeter, the range of conditions existing in the nearby disposal cell cover.

About 0.1 mm of drainage occurred in both lysimeters before they were planted during an average precipitation year, an amount well below the EPA target of <3.0 mm/yr. However, the cover with the less compacted loam sponge had a 40% greater water storage capacity than the cover with the overly compacted clay loam sponge. The difference is attributable in part to higher green leaf area and water extraction by plants in the loam topsoil. The lesson learned is that seemingly subtle differences in soil types, sources, and compaction can result in salient differences in performance, especially during wet years. Diverse, seeded communities of predominantly native perennial species were established on both lysimeters during an extended 3-yr drought, highlighting the importance of a sound understanding of the local ecology and of implementing the science and methods of disturbed-land revegetation.

REFERENCES

- U.S. Environmental Protection Agency, “Technical Guidance Document, Final Covers 
on Hazardous Waste Landfills and Surface Impoundments,” EPA/530–SW–89–047, Washington, DC (1989).

- U.S. Department of Energy, “Technical Approach Document,” Revision II, UMTRA(DOE/
AL 050425.0002, Uranium Mill Tailings Remedial Action Program, Albuquerque, 
New Mexico (1989).

- W. J. WAUGH, G. M. SMITH, D. BERGMAN-TABBERT, and D. R. METZLER, “Evolution of Cover Systems for the Uranium Mill Tailings Remedial Action Project, USA,” Mine Water and the Environment, 20:190(197 (2001).

- J. H. CLARKE, M. M. MACDONELL, E. D. SMITH, R. J. DUNN, and W. J. WAUGH.  “Engineered Containment and Control Systems: Nurturing Nature,” Risk Analysis (in press).

- C. H. BENSON, D. E. DANIEL, and G. P. BOUTWELL, “Field Performance of Compacted Clay Liners,” Journal of Geotechnical and Geoenvironmental Engineering, 125:390 (1999).

- U.S. Department of Energy, “Vegetation Growth Patterns on Six Rock-Covered UMTRA Project Disposal Cells,” UMTRA–DOE/AL 400677.0000, Uranium Mill Tailings Remedial Action Project, Albuquerque, New Mexico (1992).

- G. W. SUTER, II, R. J. LUXMOORE, and E. D. SMITH, “Compacted Soil Barriers at 
Abandoned Landfill Sites are Likely to Fail in the Long Term,” Journal of Environmental Quality, pp. 217(226 (1993).

- W. J. WAUGH, “Ecology of Uranium Mill Tailings Covers,” pp. 199(212, In: T. Reynolds and R. Morris (editors), Landfill Capping in the Semi-Arid West: Problems, Perspectives, and Solutions, ESRF–019, Environmental Science and Research Foundation, Idaho Falls, Idaho (1997).

- A. G. BOWERMAN, and E. F. REDENTE, “Biointrusion of Protective Barriers as Hazardous Waste Sites,” Journal of Environmental Quality, 27:625(632 (1998).

- W. J. WAUGH, S. J. MORRISON, G. M. SMITH, M. KAUTSKY, T. R. BARTLETT, 
C. E. CARPENTER, and C. A. JONES, “Plant Encroachment on the Burrell, Pennsylvania, Disposal Cell: Evaluation of Long-Term Performance and Risk,” GJO–99–96–TAR, Environmental Sciences Laboratory, U.S. Department of Energy, Grand Junction, 
Colorado (1999).

- W. J. WAUGH, and G. N. RICHARDSON, “Ecology, Design, and Long-Term Performance of Surface Barriers: Applications at a Uranium Mill Tailings Site,” pp. 36(49, In: Barrier Technologies for Environmental Management, National Research Council, National Academy Press, Washington, DC (1997).

- I. J. WINOGRAD, “Radioactive Waste Storage in Thick Unsaturated Zones,” Science, 212:1457(1464 (1981).

- I. J. WINOGRAD, “Archaeology and Public Perception of a Transscientific Problem( Disposal of Toxic Waste in the Unsaturated Zone,” U.S. Geological Survey Circulation 990, U.S. Geological Survey, Denver, Colorado (1986).

- E. H. ROSEBOOM, “Disposal of High-Level Radioactive Waste Above the Water Table 
in Arid Regions,” U.S. Geological Survey Circulation 903, U.S. Geological Survey, Washington, DC (1983).

- C. C. REITH, and B. M. THOMPSON (eds.), “Deserts as Dumps? The Disposal of Hazardous Materials in Arid Ecosystems,” University of New Mexico Press, Albuquerque, New Mexico (1992).

- G. W. GEE, and S. W. TYLER (eds.), “Symposium: Recharge in Arid and Semiarid Regions,” Soil Science Society of America Journal, 58:5(72 (1994)

- W. J. WAUGH, M. R. ADAMS, and R. C. ROUTSON, “Demonstration of a Design for Shallow-Land Burial of Low-Level Radioactive Waste,” In: Proceedings of the 1983 Meetings of the Soil Science Society of America, Washington, DC, American Society of Agronomy, Madison, Wisconsin (1983).

- J. E. ANDERSON, R. S. NOWAK, T. D. RATZLAFF, and O. D. MARKHAM, “Managing 
Soil Moisture on Waste Burial Sites in Arid Regions,” Journal of Environmental Quality, 
22:62(69 (1993).

- S. O. LINK, W. J. WAUGH, and J. L. DOWNS, “The Role of Plants on Isolation 
Barrier Systems,” In: Proceedings of the 33rd Hanford Symposium on Health and the Environment—In-Situ Remediation: Scientific Basis for Current and Future Technologies, Battelle Press, Columbus, Ohio (1994).

- W. J. WAUGH, M. E. THIEDE, D. J. BATES, L. L. CADWELL, G. W. GEE, and 
C. J. KEMP, “Plant Cover and Water Balance in Gravel Admixtures at an Arid Waste 
Burial Site,” Journal of Environmental Quality, 23:676(685 (1994).

- A. WARD and G. GEE, “Performance Evaluation of a Field-Scale Surface Barrier,” Journal of Environmental Quality 26:694(705 (1997).

- J. STORMONT and C. ANDERSON, “Method to Estimate Water Storage Capacity of Capillary Barriers,” Journal of Geotechnical and Geoenvironmental Engineering 124:297(302 (1998).

- M. V. KHIRE, C. H. BENSON, and P. J. BOSSCHER, “Capillary Barriers: Design 
Variables and Water Balance,” Journal of Geotechnical and Geoenvironmental Engineering 126:695(708 (2000).

- G. W. GEE, and D. HILLEL, “Groundwater Recharge in Arid Regions: Review and Critique of Estimation Methods,” Hydrological Processes, 2:255(266 (1988).

- H. KOHNKE, F. R. DRIEBELBIS, and J. M. DAVIDSON, “A Survey and Discussion of 
Lysimeters and a Bibliography on Their Construction and Use,” Miscellaneous Publication No. 372, U.S. Department of Agriculture, Washington, DC (1940).

- J. W. NYHAN, T. E. HAKONSON, and B. J. DRENNON, “A Water Balance Study of 
Two Landfill Cover Designs for Semiarid Regions,” Journal of Environmental Quality, 19:281(288 (1990).

- M. R. SACHSCHEWSKY, C. J. KEMP, S. O. LINK, and W. J. WAUGH, “Soil Water Balance Changes in Engineered Soil Surfaces,” Journal of Environmental Quality, 24:352(359 (1995).

- A. L. WARD, and G. W. GEE, “Performance Evaluation of a Field-Scale Surface Barrier,” Journal of Environmental Quality, 26:694(705 (1997).

- A. C. Roesler, C. H. Benson, and W. H. Albright, “Field Hydrology and Model 
Predictions for Final Covers in the Alternative Cover Assessment Program – 2002,” 
Geo Engineering Report No. 02(08, Geo Engineering Program, University of Wisconsin-Madison, Madison, Wisconsin (2002).

- W. J. Waugh, “Monticello Field Lysimetry: Design and Monitoring of an Alternative Cover,” Proceedings of the Waste Management 2002 Symposium, University of Arizona, Tucson, Arizona (2002).

- C. B. HUNT, “Cenozoic Geology of the Colorado Plateau,” U.S. Geological Survey Professional Paper 279 (1956).

- U.S. Department of Agriculture, “Soil Survey: San Juan Area, Utah,” Series 1945, No. 3, Soil Conservation Service, Washington, DC.

- U.S. Environmental Protection Agency, “Evapotranspiration Landfill Cover System 
Fact Sheet,” EPA 542–F–03–015, Solid Waste and Emergency Response (5102G), Washington, DC (2003).

- B. N. Bjornstad and S. S. Teel, “Natural Analog Study of Engineered Protective Barriers at the Hanford Site,” PNL–8840, Pacific Northwest National Laboratory, Richland, Washington (1993).

- W. H. WISCHMEIER and D. SMITH, “Predicting Rainfall Erosion Losses—A Guide to Conservation Planning,” Agricultural Handbook No. 537. U.S. Department of Agriculture, Washington, DC (1978).

- M. W. LIGOTKE, “Control of Eolian Soil Erosion From Waste-site Surface Barriers,” 
pp. 545–559 in G.W. Gee and N.R. Wing, (editors), “In-Situ Remediation: Scientific Basis for Current and Future Technologies,” Battelle Press, Richland, Washington (1994).

- J. B. FINELY, M. D. HARVEY, and C. C. WATSON, “Experimental Study: Erosion of Overburden Cap Material Protected by Rock Mulch,” pp. 273–282 In: Proceedings of Seventh Symposium on Management of Uranium Mill Tailings, Low-Level Waste, and Hazardous Waste, Colorado State University, Ft. Collins, Colorado (1985).

- G. M. SMITH and R. E. REGER, “Protective Layer Design in Landfill Covers Based 
on Frost Protection,” Journal of Geotechnical and Geoenvironmental Engineering 128:794(799 (2002).

- G. W. GEE and D. OR, “Particle-Size Analysis,” pp. 255(293 In: J. H. Dane and G. C. Topp (editors), Methods of Soil Analysis, Part 4, Physical Methods, Book Series Number 5, Soil Science Society of America, Madison, Wisconsin (2002).

- W. J. WAUGH, G. VANREYPER, and S. L. VANCE, “Characterization of Vegetation Within the 3-Hectare ACAP Lysimeter at the Monticello, Utah, Superfund Site,” 
GJO–2002–302–TAR, Environmental Sciences Laboratory, U.S. Department of Energy, Grand Junction, Colorado (2002).

- M. KASTENS and J. WAUGH, “Methodology for Determining Revegetation Success at the Monticello Repository,” GJO–2002–325–TAR, U.S. Department of Energy, Grand Junction, Colorado (2002).

- K. C. KIM and C. H. BENSON, “Water Content Reflectometer Calibrations for Final Cover Soils,” Geo Engineering Report No. 02–12, Geo Engineering Program, University of Wisconsin-Madison, Madison, Wisconsin (2002).

- K.G. McNaughton and P. G. Jarvis, “Predicting Effects of Vegetation Changes on Transpiration and Evaporation,” pp. 1(47 in T. T. Kozlowski (editor), Water Deficits and Plant Growth, Vol. VII, Academic Press, New York (1983).

- C. T. deWit, “Photosynthesis of Leaf Canopies,” Agriculture Research Report No. 663, Centre Agr. Publ. Doc., Wageningen, The Netherlands (1965).

- D. A. FLOYD and J. E. ANDERSON, “A New Point Interception Frame for Estimating Cover of Vegetation,” Vegetation 50: 185(186 (1982).

This document was authored by the following individuals on behalf of the Office of Legacy Management:

W.J. Waugh

G.M. Smith

P.S. Mushovic