OMAC HMI OPC Data Mapping	Date: 2005-1-13

Standard title: OMAC HMI OPC Data Mapping Draft

| COPYRIGHT NOTICE: This document is not copyright protected. |
| --- |
| ABSTRACT: This document presents a potential list of OPC (OLE for Process Control) item tags related to CNC data server for OMAC (Open Modular Architecture Control) Human Machine Interface (HMI) and then map these data items to commercial CNC controller implementation. KEYWORDS: CNC, COM, OPC, axis, servo, machine, standard |
| COMMENTS TO READER: Information provided in this document is provided 'as is' without warranty of any kind, either express or implied. The user assumes the entire risk as to the accuracy and the use of this document. |
| Project Leader: Address: Telephone: Telefacsimile: Electronic mail: | Document Editor: John Michaloski Address: NIST Bldg. 220 Rm. B124 Gaithersburg, MD 20832 Telephone: 301-975-3458 Telefacsimile: 301-990-9688 Electronic mail: John.Michaloski@nist.gov |

# Background

One objective of the OMAC HMI Working Group is to define a series of standard specifications meeting the data requirements expected to implement a CNC HMI. This document will look at the standardizing OPC Data Item tags (or names) for use in CNC HMI software and related application programming.

This document draws on the OMAC HMI Working Group document, “OMAC HMI Data Points”, which is a list of “important” CNC HMI-related data points. In this document, each variable from this data list has been mapped to a vendor-specific variable wherever possible. This mapping should help to validate the list of “important” CNC data points by insuring completeness against commercial products. This set of standard OMAC HMI items will given specific OPC Full Specified Item Tags (or names). Vendors would then be able to provide a Microsoft COM server or some other interface to map OMAC HMI to their internal OPC data items. In the figure below, a  scenario could be where a vendor or 3rd party supplies a COM component to map OMAC HMI names  into vendor-specific OPC fully qualified names that could then be used to access the vendors OPC server.

Figure 1 Scenario for OMAC HMI OPC Item Naming

The remainder of the document lists variables by section with little or no background on the purpose of the variable/section.  Most of the variables should be obvious, but if confusing, these variables are described in related OMAC HMI documents.

The are a few issues involved in naming OPC items.

- There are OPC item names that have an equivalent fully qualified name.  Each OPC item name must be unique, otherwise the API to map from OPC item name to fully qualified OPC item will not one-to-one.

- How to handle arrays of items, e.g. axis positions or x,y,z. Most of the commercial products return an array with an implicit understanding of the range of valid values within the array. All provide a mapping from the machine configuration (e.g., xyz or xz to specifie array indices.)  Handling arrays within OPC is done using Safearrays, and the actual mechanism would have to be spelled out as to how the arrays would be passed. Further, using OPC browsing would require knowledge of mappings and bound of the arrays, otherwise you could return 26 values of which only three are valid.

- Conformance classes would be helpful in defining application functionality using the OPC names. For example, simple CNC logging of on/off, faults, etc would entail a list of ten conforming variable names. Maybe a fuller  variable list would be required to do asset management, ROI and utilization and condition based management.

- Blank values may not mean the commercial product does not have a mapping. If a mapping is given, it can be determined directly as a one-to-one mapping or as part of a function call. If the information requires extra calculation or required multiple steps or wasn’t obvious, the value was left blank.

- Values may not accurately reflect the correct mapping, but using the available documentation, appeared to map to the OPC item.

# Variable Mappings

## Axis Properties

Axis provide trajectory motion for a degree-of-freedom  in the CNC coordinate system.

| Axis | MDSI | Siemens | Fanuc (methods) | Okuma |
| --- | --- | --- | --- | --- |
| AxisAbsolutePosition | axLoc[i] | $AA_IM[X] Actual value in machine coordinate system (MCS). /Channel/MachineAxis/actToolBasePos | cnc_absolute | OPC//Position/ActualPostion/ActualPositionAxisXX.Position |
| Axis.DistanceToGo | axDistToGo[i] | $AA_DTEB[X] /Channel/State/acDteb[x] /Channel/GeometricAxis/rogDistToGo | cnc_distance | OPC//Position/TargetPosition/TargetPositionAxisXX.Position |
| Axis.FollowingError | axFErr[i] | /Nck/servoDataFl32[1] | N/A | NA |
| Axis.IncrementSystem | plcJogDist | /Channel/MachineAxis/actIncrVal |  | NA |
| Axis.Index | 0,1,2,3,… | /Channel/MachineAxis/index | N/A | 0,1,2,3,… |
| Axis.Label | defAxisLetters | $MN_AXCONF_MACHAX_ NAME_TAB[n] /Channel/MachineAxis/name | cnc_rdsvmeter() label | OPC//Position/TargetPosition/TargetPositionAxisXX.Name |
| Axis.Load | NA | /Channel/MachineAxis/aaLoad[] | cnc_rdsvmeter | OPC/Position/TargetPosition/TargetPositionAxisXX.Load |
| Axis.Maximum | axLocAbsMax | /Axis/Settings/ MDD_WORKAREA_LIMIT_PLUS |  | OPC//Common/NCStatus/NumberAxes |
| Axis.Minimum | axLocAbsMin | /Axis/Settings/ MDD_WORKAREA_LIMIT_MINUS |  | NA |
| Axis.MotionState (in-pos) |  | $AA_STAT /Channel/MachineAxis/status /Channel/MachineAxis/aaStat |  | NA |
| Axis.SetPoint |  | $P_EP (blending) /Nck/servoDataFl32[6] | cnc_rdcommand() | NA |
| Axis.Type | axDistparseOut | $MA_IS_ROT_AX $MN_DRIVE_TYPE[n](hydraulic) /Channel/MachineAxis/type |  | OPC//Position/TargetPosition/TargetPositionAxisXX.Type |
| Axis.Units | jsInchMode | /Channel/MachineAxis/extUnit | cnc_rdparam_ext () unit | OPC//Common/NCStatus/DistanceUnits |
| Axis.Velocity | axVelocity[i] | $AC_VACTW /Channel/MachineAxis/aaVactM |  | OPC//Common/NCStatus/CommandFeedrate |
| Axis.VelocityMax | jsVelocityLimit axVelMax (rapid) | $MA_MAX_AX_VELO[] |  | NA |
| Axis.WorkpiecePosition |  | $AA_IW[X] /Channel/GeometricAxis/actToolBasPosEN | cnc_absolute | OPC//Offset/ZeroOffsets/ZeroOffset/OffsetAxisXX |

## Feedrate

Feedrate defines the trajectory motion rates based on programmed coordinate system.

| Feedrate | MDSI | Siemens | Fanuc | Okuma |
| --- | --- | --- | --- | --- |
| Feedrate.Actual |  | /Channel/MachineAxis/actFeedRate | cnc_actf() | OPC//Common/NCStatus/ActualFeedrate |
| Feedrate.Commanded | jsVelocityNow | $P_F or $AC_F /Channel/State/cmdFeedRateIpo /Channel/MachineAxis/cmdFeedRate | cnc_rdcommand() | OPC//Common/NCStatus/CommandFeedrate |
| Feedrate.FeedUnits | jsFeedMode[0] | /Channel/State/feedRateIpoUnit /Channel/MachineAxis/axisFeedRateUnit |  | OPC//Common/NCStatus/FeedrateUnits |
| Feedrate.Override | jsPctFeedOvRide[0] | $OVRA /Channel/State/feedRateIpoOvr /Channel/MachineAxis/feedRateOvr | cnc_rdopnlsgnl() feed_ovrd | OPC//Common/NCStatus/FeedrateOverride |
| Feedrate.OverrideMaximum | defPctFeedOvrMax | $MN_OVR_FACTOR_FEEDRATE |  | OPC//Common/NCStatus/MaxFeedrateOverride |

## Spec

Specification includes manufacturer, model, and a simple list of machine capabilities. This information would be useful for several applications: such as loggging, or capability querying.

| Machine | MDSI | Siemens | Fanuc | Okuma |
| --- | --- | --- | --- | --- |
| Spec.BaseUnits | defInchModeDeflt | $MN_SCALING_ SYSTEM_IS_METRIC |  | NA |
| Spec.Configuration |  |  |  | NA |
| Spec.Controller |  | /Nck/Configuration/nckType /Nck/Configuration/nckVersion | cnc_rdsyssoft() | File Access |
| Spec.Manufacturer |  |  |  | NA |
| Spec.MaxFeed |  |  |  | NA |
| Spec.MaxPower |  |  |  | NA |
| Spec.MaxSpeed | spRPMMax | /Axis/Settings/ MDD_SPIND_MAX_VELO_LIMS | cnc_rdspmaxrpm() | NA |
| Spec.MaxTraverse |  |  |  | NA |
| Spec.Model |  |  |  | NA |
| Spec.NumberOfAxes |  | /Nck/Configuration numGlobMachAxes | cnc_sysinfo() max_axis | NA |
| Spec.SerialNumber |  |  |  | NA |
| Spec.WorkingArea |  | /Axis/Settings/MDD_WORKAREA_LIMIT_ {MINUS,PLUS}[0..n] |  | NA |

## Machine

Machine and underlying equipment state and modal types within the CNC. More complete configuration and equipment description would be a continuation of this set of variable definitions.

| Machine | MDSI | Siemens | Fanuc | Okuma |
| --- | --- | --- | --- | --- |
| Machine.AlarmPending | (alarms are stored in a file) | /Channel/State/chanAlarm /Channel/State/acAlarmStat | cnc_alarm() or cnc_statinfo () | DNCT3Lib.clsNCStatus. GetAlarmStatus() |
| Machine.BlockDelete | mBlockDeleteReq | skipLevel[0..9]Active | cnc_rdopnlsgnl() blck_del() | NA |
| Machine.CycleTime | n/a | $AC_CYCLE_TIME /Channel/ChannelDiagnose/cycleTime | cnc_rdtimer | DNCT3Lib. clsMachineReport.Cycle ( Per Part Program) |
| Machine.CuttingTime | n/a | /Channel/ChannelDiagnose/cuttingTime | cnc_rdtimer | DNCT3Lib. clsOperatingReport. Cutting |
| Machine.DryRun | mDryRunEnabled | $P_DRYRUN /Channel/ProgramModification/trialRunActive | cnc_rdopnlsgnl() dry_run | BLANK |
| Machine.Feedhold | mFeedHold | /Channel/ProtocolEvent/eventActive[7] /Channgel/State/stopCond | cnc_rdopnlsgnl () feed_hold | DNCT3Lib.clsNCStatus. GetSlideHoldStatus () |
| Machine. Ready | mSyncDone?? | /Bag/State/readyActive |  | BLANK |
| Machine.Status | genMachState | /Channel/State/machFunc | cnc_statinfo | BLANK |
| Machine.OperationMode (e.g., Auto) | mRunMode | /Bag/State/opMode | cnc_statinfo | DNCT3Lib.clsNCStatus. GetRunStatus () |
| Machine.OperationTime |  | $AC_OPERATING_TIME /Channel/ChannelDiagnose/operatingTime | cnc_rdtimer | DNCT3Lib. clsOperatingReport. Operating |
| Machine.OptionalStop | mOptionalStopOn | /Channel/ProgramModification/ optStopActive | cnc_modal() | BLANK |
| Machine.Program (abs vs incr) | jsIncrMode[0] | /Nck/MachineAxis/actIncrVal | cnc_modal() | BLANK |
| Machine.ProgramStatus | mFeedHold mFailHold genCycleOn | /Channel/State/progStatus | cnc_statinfo | DNCT3Lib..clsNCStatus. GetPStopStatus () GetSlideHoldStatus () |
| Machine.RapidTraverseOverride | mPctRapidOvRide | /Channel/State/rapFeedRateOvr | cnc_rdopnlsgnl() rpd_ovrd | BLANK |
| Machine.ServosOn | dioEnergizedState | /Channel/MachineAxis/ drivePowerOn |  | BLANK |
| Machine.SingleBlock | mSingleBlockOn | /Channel/ProgramModification/ singleBlockActive | cnc_modal() | BLANK |
| Machine.SpeedMode | spPositionOn | /Channel/Spindle/opMode | cnc_rdopnlsgnl() sngl_blck cnc_rdopmode() | BLANK |
| Machine.ToolDiameterCompensation | jsToolRadOffNum | /Channel/State/actToolRadius | cnc_modal() | BLANK |
| Machine.ToolLengthCompensation | jsToolLenOffNum | /Channel/State/actToolLength1,2,3 | cnc_modal() | BLANK |
| Machine.WorkingPlane | jsPlaneSel0[0] + jsPlaneSel1[0] | acMeasActPlane?? | cnc_modal() | BLANK |
| Machine.WorkOffsetMode (fixtureoffset) | jsFixtureNumber | /Channel/State/actFrameIndex | cnc_rdzofs()s | BLANK |

## Part Program

A part program is a file containing a sequence of machining operations to the CNC controller which produce a specific workpiece from a given blank, stock or starting workpiece. There are several ways to piece together a job, consisting of a main program, subroutine programs, fixture files, tooling files, etc.  For logging, you would probably just want the current program name, and the executing block.  Passing of Production Management Data, (versioning and modification dates) would be useful and theoretically could be retrieved in a networked file system, but this is not always the case. Without access to the file system (e.g., local non-shared files), it would be useful to have versioning and date stamps associated as part of the part program status.

| Part Program | MDSI | Siemens | Fanuc | Okuma |
| --- | --- | --- | --- | --- |
| Program.creationDate | n/a | n/a |  | NA |
| Program modificationDate | n/a | n/a |  | NA |
| Program.origin | n/a | n/a |  | NA |
| Program.Name | defProgFileName | /Channel/ProgramModification/ progName |  | BLANK |
| Program.Path | defJobFilePath | /Channel/ProgramModification/ workPName |  | OPC//Common/NCStatus/ProgramPath |
| Program |  | ––––––––––––––––––– |  |  |
| Program.Subprograms |  |  |  | DNCT3Lib.clsNCStatus. GetSubProgramFile |
| Program.Comment |  | /Channel/ProgramModification/ msg |  | BLANK |
| Program.CurrentProgramName | defProgramFileName | /Channel/ProgramInfo/progName |  | OPC//Common/NCStatus/ActiveProgram |
| Program.MainProgram |  | /Channel/ProgramInfo/ workPNameLong |  | DNCT3Lib.clsNCStatus. GetMainProgram |
| Program.Size | Message:TAPEINFO |  |  | BLANK |
| Program.CurrentSequenceNumber |  |  | cnc_rdseqnum() | OPC//Common/NCStatus/CurrentSequenceNumber |
| Block |  | ––––––––––––––––––– |  |  |
| Program.ActiveLineNumber | Message:TAPEINFO | /Channel/ProgramInfo/actLineNumber |  | BLANK |
| Program.ActiveBlockNumber | Message:BLKREL_READ msgBlockRelativeRead | /Channel/ProgramPointer/ blockNoStr |  | OPC//Common/NCStatus/CurrentBlock |
| Program.ActiveCodes | jsModalGString | Channel/SelectedFunctions/ ncFkt |  | OPC//ActiveCodes/ActiveGCdoes/GCodes; OPC//ActiveCodes/ActiveMCodes/MCodes |
| Program.ExecutingBlockSource | Message:BLKREL_READ msgBlockRelativeRead | /Channel/ProgramInfo/singleBlock[1] |  | OPC//Common/NCStatus/ExecuteBlock |

Choice here: read blocks from disk using file offset, or read blocks from CNC controller.

Issues: Can’t you just read creation/modification date/time from file system.

## Spindle

Spindle information included commanded, actual, and override information.

| Spindle | MDSI | Siemens | Fanuc | Okuma |
| --- | --- | --- | --- | --- |
| Mode – See System | ––––––––––––––––––– | ––––––––––––––––––– | ––––––––––––––––––– | ––––––––––––––––––– |
| Spindle.GearStage | mEGearChange | /Channel/Spindle/actGearStage | cnc_rdctrldi // cnc_rdspgear | NA |
| Spindle.GearStageCommanded | n/a | /Channel/Spindle/cmdGearStage |  | NA |
| Spindle.Index | defSpAxisBase | /Channel/Spindle/index | cnc_rdnspdl | BLANK |
| Spindle.Load | n/a | /Channel/Spindle/driveLoad | cnc_rdspmeter cnc_rdspload | OPC//Common/NCStatus/SpindleLoad |
| Spindle.Status CW,CCW, STOPPED | spRPMState + spRPMAtZero | /Channel/Spindle/turnState |  | BLANK |
| Spindle.Name |  | /Channel/Spindle/name | cnc_rdspdlname() | BLANK |
| Spindle.OverrideCommanded | spPctOvRide | /Channel/Spindle/speedOvr | cnc_rdopnlsgnl() spdl_ovrd | OPC//Common/NCStatus/SpindlerateOverride |
| Spindle.Speed | spRPMNow | /Channel/Spindle/actSpeed | cnc_rdspeed cnc_acts2 | OPC//Common/NCStatus/AcutalSpindlerate |
| Spindle.SpeedCommanded | spRPMValue | /Channel/Spindle/cmdSpeed | cnc_rdcommand() | OPC//Common/NCStatus/CommandSpindlerate |
| Spindle.Type |  | /Channel/Spindle/spindleType |  | BLANK |
| Spindle.Units |  | /Nck/MachineAxis/axisFeedRateUnit | cnc_rdspeed [speedelm..unit] | OPC//Common/NCStatus/SpindleUnits |

## Tools

Tools are resources necessary to perform a machining operations such as material removal and probing. These are some of the initial tooling data,from most basic to advanced:

- Tool name, number, id, type

- Tool Geometry –  length and radius offsets and wear offsets

- Tool capability – max speed, feed.

- Tool life monitoring – minutes and cycles

- Tool and tool edge description – flutes, orientation

| Tools | MDSI1 | Siemens | Fanuc | Okuma |
| --- | --- | --- | --- | --- |
| Tool.Name | N/A | /Tool/Data/toolIdent |  | NA |
| Tool.Id |  | /Tool/Catalogue/toolInPlace | cnc_rdtool() mgz_no | BLANK |
| Tool. Number |  | /Tool/ActiveCatalogue/toolNo | cnc_rdtool() ->toolnum | BLANK |
| Tool.Type | N/A | /Tool/Compensation/ cuttEdgeParam[1] |  | BLANK |
| Tool.State |  | /Tool/Data/ toolState | cnc_rdtool() life_stat | BLANK |
| Tool.Length | mToolLenOffTbl[0] | /Tool/Compensation/ cuttEdgeParam[1] | cnc_rdtool() ->h_code | BLANK |
| tool offset location |  |  |  |  |
| Tool.xAxis | File access | /Tool/Compensation/ cuttEdgeParam[21] |  | OPC//Offset/ToolOffset/X_ToolOffset//Offset01 |
| Tool. yAaxis | File access | /Tool/Compensation/ cuttEdgeParam[22] |  | OPC//Offset/ToolOffset/Y_ToolOffset//Offset01 |
| Tool.zAaxis | File access | /Tool/Compensation/ cuttEdgeParam[23] |  | BLANK |
| Tool.Radius | mToolRadOffTbl[0] | /Tool/Compensation/ cuttEdgeParam[6] | cnc_rdtool() ->d_code | BLANK |
| Tool.Tip |  | /Tool/Compensation/ cuttEdgeParam[7] |  | BLANK |
| Tool.IdActive (PROG?) |  | /Channel/State/progTNumber |  | OPC//Common/NCStatus/ActiveTool |
| tool count |  | /Tool/Catalogue/numTools |  | OPC//Common/NCStatus/MaxToolNumber |
| Tool.Geometry |  | /Tool/Compensation/ cuttEdgeParam[3,4,5] | cnc_rdtool() (odbtofs.Geometry.data) | BLANK |
| Tool.Wear | mToolLenWrTbl[0] mToolRadWrTbl[0] | /Tool/Compensation/ cuttEdgeParam[12,13,14,15,16] | cnc_rdtool () W_code | OPC//Offset/ToolWearOffset/X_ToolWearOffset/Offset01 |
| Tool.Flutes | N/A | /Tool/Data/numCuttEdges |  | BLANK |
| Tool.MaxRPM | N/A |  | cnc_rdspmaxrpm | BLANK |
| Tool.MaxFeed | N/A |  | cnc_rdtool() feedrate | BLANK |

1 MDSI tooling information is loaded by file into as a table.

## Alarms

Alarms are defined as events detected by the system and displayed on the operator panel. MDSI logs alarms to a file for viewing. Access to the log file name is available.

| Alarms | MDSI | Siemens | Fanuc | Okuma |
| --- | --- | --- | --- | --- |
| Alarm Message | Logged to display/file. |  |  | OPC//Messages/AlarmMessage/ GetAlarmMessages |
| Alarm.Message | Logged to display/file. | /Nck/SequencedAlarms/ fillText1/2/3/4 | cnc_alarm() | OPC//Messages/AlarmMessage/Description |
| Alarm.ID | Logged to display/file | /Nck/SequencedAlarms/textIndex | cnc_rdalminfo() | OPC//Messages/AlarmMessage/Code |
| Alarm.Timestamp | Logged to display/file | /Nck/SequencedAlarms/ timeBCD | '' | OPC//Messages/AlarmMessage/Time; OPC//Messages/AlarmMessage/Date |
| Alarm.Number | Logged to display/file | /Nck/SequencedAlarms/alarmNo | '' | OPC//Messages/AlarmMessage/Code |
| Alarm Message ( history) |  |  | cnc_rdalmhistry2() | File access |
| AlarmHistory.message |  | /Nck/SequencedAlarms/ textIndex | cnc_rdalmmsg() | File access |
| AlarmHistory.message ID |  |  | '' | File access |
| AlarmHistory.timestamp |  |  | '' | File access |
| Operator Message |  |  | cnc_rdopmsg() |  |
| Operator.Message |  | /Channel/ProgramModification/ msg |  | OPC//Messages/OperatorMessage/Description |
| Operator.MessageID |  |  | '' | OPC//Messages/OperatorMessage/Code |
| Operator.Timestamp |  |  | '' | OPC//Messages/OperatorMessage/Time; OPC//Messages/OperatorMessage/Date |
| Operator.Type |  |  | '' |  |
| Operator Message (history) |  |  | cnc_rdophisno() | File access |
| OperatorHistory.Message |  |  | '' | File access |
| OperatorHistorymessageID |  |  | '' | File access |
| OperatorHistory timestamp |  |  | '' | File access |

# Variable Meanings

The table below contains brief descriptions of each of the variables described in the OPC data item mappings.

| VARIABLE | MEANING |
| --- | --- |
| Alarm.ID | Alarm numeric id. |
| Alarm.Message | Alarm text message. |
| Alarm.Number | Alarm number since reset. |
| Alarm.Timestamp | Alarm timestamp. |
| AlarmHistory.message | Alarm history text message. |
| AlarmHistory.message ID | Alarm history message numeric id. |
| AlarmHistory.timestamp | Alarm history message imestamp. |
| AxisAbsolutePosition | Absolute position of the axis in the base system (with/without compensation or as tool tip position?) |
| AxisDistanceToGo | distance-to-go of the path in absolute distance and travel units |
| AxisFollowingError | Following error. |
| AxisIncrementSystem | Active incremental distance for jogging axis |
| AxisIndex | Absolute index into axes array. (0 or 1 based?) |
| AxisLabel | Axis name, e.g., X, Y, Z, A, B, C, SP,… |
| AxisLoad | Drive load. Units (% or Nm)? |
| AxisMaximum | Axis absolute position limit in positive direction. |
| AxisMinimum | Axis absolute position limit in negative direction. |
| AxisMotionState | Enumeration: off, in–pos, moving |
| AxisSetPoint | Axis Position setpoint |
| AxisType | Linear vs. Rotary |
| AxisUnits | Enumeration describing current physical unit of the axis position. Enums TBD. |
| AxisVelocity | Axis velocity in (machine or base?) coordinate system |
| AxisVelocityMax | Maximum axis velocity. |
| AxisWorkpiecePosition | Axis base position of the active tooltip relative to the workpiece zero point |
| Feedrate.Actual | Actual machine federate (per axis or per tooltip?) |
| Feedrate.Commanded | Commanded feedrate setpoint |
| Feedrate.FeedUnits | Interpolation feedrate, units e.g., mm/min, mm/rev, inch/min, inch/rev |
| Feedrate.Override | Interpolation feedrate, override in percentage |
| Feedrate.OverrideMaximum | Interpolation feedrate, override maximum in percentage |
| Machine.AlarmPending | Flag to indicate alarm(s) are pending |
| Machine.BlockDelete | Block delete level. |
| Machine.CuttingTime | Total operating time of machine excluding rapid traverse as measured in all NC programs since machine was last turned on or reset. |
| Machine.CycleTime | Runtime of selected NC program, units in SI (seconds). |
| Machine.DryRun | Dry run federate active. |
| Machine.Feedhold | Feedhold active. |
| Machine.OperationMode | Active mode: JOG, AUTO, MDI |
| Machine.OperationTime | Total runtime of NC programs in auto mode. |
| Machine.OptionalStop | Optional stop active. |
| Machine.Program | (abs vs incr) |
| Machine.ProgramStatus | Active Program status: running, aborted, stopped, ect. |
| Machine.Ready | Machine on and homed. |
| Machine.ServosOn | Servos powered on. |
| Machine.SingleBlock | Single block active |
| Machine.SpeedMode | Spindle mode. |
| Machine.ToolDiameterCompensation | Tool diameter compensation active. |
| Machine.ToolLengthCompensation | Tool length compensation active. |
| Machine.WorkingPlane | Current working plane: xy, yz, xz. |
| Machine.WorkOffsetMode | Current programmed work offset. |
| Operator.Message | Operator message. |
| Operator.MessageID | Id of operator message. |
| Operator.Timestamp | Timestamp of operator message. |
| Operator.Type | Operator message type. |
| OperatorHistory timestamp | Operator history message timestamp. |
| OperatorHistory.Message | Operator history message. |
| OperatorHistory.MessageID | Operator history message id. |
| Program ModificationDate | Last modification date of part program. |
| Program.ActiveBlockNumber | Active block sequence number in current program. |
| Program.ActiveCodes | Active G codes in current program. (OR m codes?) |
| Program.ActiveLineNumber | Active line number in current program. |
| Program.Comment | Program message to operator. |
| Program.creationDate | Creation date of part program. |
| Program.CurrentProgramName | Current executing part program name. |
| Program.CurrentSequenceNumber | Sequence (block) number executing. |
| Program.ExecutingBlockSource | Source of current executing block. |
| Program.MainProgram | Main workpiece part program. |
| Program.Name | Program name of the currently active program |
| Program.origin | Origin of part program. |
| Program.Path | Directory path of part program. |
| Program.Size | Size of part program in bytes. |
| Program.Subprograms | Workpiece part subprograms required. |
| Machine.RapidTraverseOverride | Rapid traverse override active. |
| Spec.BaseUnits | Base units of machine (m or mm or inch) |
| Spec.Configuration | Axis setup textual description, e.g., xyz |
| Spec.Controller | Brand of controller, model |
| Spec.Manufacturer | CNC machine manufacturer. |
| Spec.MaxFeed | CNC maximum feed rate (speced). |
| Spec.MaxPower | CNC maximum power. |
| Spec.MaxSpeed | CNC maximum spindle RPM. |
| Spec.MaxTraverse | CNC maximum traverse rate |
| Spec.Model | Model number. |
| Spec.NumberOfAxes | Number of axes in machine. |
| Spec.SerialNumber | Serial Number of machine for maintenance. |
| Spec.WorkingArea | Working volume, e.g., xyz ranges. |
| Spindle.GearStage | Actual gear stage of spindle |
| Spindle.GearStageCommanded | Commanded setpoint gear stage of spindle |
| Spindle.Index | Absolute axis index. |
| Spindle.Load | Spindle load. |
| Spindle.Name | Spindle name. |
| Spindle.OverrideCommanded | Spindle speed override in %. |
| Spindle.Speed | Actual spindle speed. |
| Spindle.SpeedCommanded | Commanded spindle speed in RPM |
| Spindle.Status | Status : CW,CCW, STOPPED |
| Spindle.Type | Master or not master. |
| Spindle.Units | Unit of the axis-specific: 0 = mm/min, 1 = inch/min, 2 = degree/min |
| Tool.State | Active, not enabled, broken, etc. |
| Tool.yAaxis | Tool length offset in y axis. |
| Tool.Flutes | Number of flutes. |
| Tool.Geometry | Tool geometry offsets: x,y,z. |
| Tool.Id | Tool id in magazine. |
| Tool.IdActive | Identifier of active tool |
| Tool.Length | Tool length offset. |
| Tool.MaxFeed | Tool’s rated maximum feed rate. |
| Tool.MaxRPM | Tool’s rated maximum speed. |
| Tool.Name | Tool description. |
| Tool.Number | Tool number in catalogue. |
| Tool.Radius | Tool radius offset. |
| Tool.Tip | Tool tip edge information. |
| Tool.Type | Tool type description: e.g., end mill. |
| Tool.Wear | Tool wear offsets: x,y,z. |
| Tool.xAxis | Tool length offset in X axis. |
| Tool.zAaxis | Tool length offset in Z axis. |