NWS FORM E-19 (COVER)

U.S. DEPARTMENT OF COMMERCE

NATIONAL OCEANIC AND ATMOSPHERIC ADMINISTRATION

NATIONAL WEATHER SERVICE

REPORT ON RIVER GAGE STATION

REVISED, PRINTED DATES: 12/20/2006, 12/20/2006

LOCATION: Chase

STREAM: Flint River

BASIN: Flint                            HSA: HUN

REFERENCES:

DATED 2-13-75...REVISED 9-26-85.

USGS DESCRIPITION OF GAGING STATION

ABBREVIATIONS:

BM  - bench mark		EPA   - Environmental Protection Agency

DS  - downstream		IBWC  - International Boundary and Water Comm.

US  - upstream		MSRC  - Mississippi River Commission

HW  - high water		MORC  - Missouri River Commission

LW  - low water		NOAA  - National Oceanic and Atmospheric Admin.

RB  - right bank		NOS   - National Ocean Survey

LB  - left bank		NWS   - National Weather Service

MGL - mean gulf level	TVA   - Tennessee Valley Authority

MLW - mean low water		USACE - U.S. Army Corps of Engineers

MSL - mean sea level		USBR  - U.S. Bureau of Reclamation

MLT - mean low tide		USGS  - U.S. Geological Survey

MT  - mean tide		USWB  - U.S. Weather Bureau

WQ  - water quality		NGVD  - National Geodetic Vertical Datum

RM  - reference mark		NAD   - North American Datum

RP  - reference point

LOCATION IDENTIFICATION: CHSA1

NWS INDEX NUMBER: 03575000

USGS NUMBER: 03575000

MAP OF GAGE LOCATION

LATITUDE: 34 49 22  		SOURCE: USGS

LONGITUDE: 86 28 59

LOCATION: Flint River NEAR Chase, AL                                Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: CHSA1                          HSA: HUN                     NWS FORM E-19 PAGE 1: GAGE MAP

BENCHMARKS

ELEVATION OF GAGE ZERO:  640.370         VERTICAL DATUM: NGVD OF 1929

LEVELING AGENCY AND DATE: Level                  CHECKBAR:    0.000

RATING AGENCY: USGS

BENCHMARK     DESCRIPTION                                                            GAGE ZERO      DATUM

----------------------------------------------------------------------------------    ---------     -------

RM10          (9/2/75) CHISELED SQUARE IN THE UPSTREAM LEFT ABUTMENT.                    36.095     676.465

RM11          (6/3/83) NAIL IN THE POWER POLE ON THE SHOREWARD SIDE OF THE HOUSE.        36.273     676.643

RM12          (6/3/83) CHISELED SQUARE IN THE FLOOR OF THE GAGE HOUSE.                   34.099     674.469

RM6           (10/10/63) TOP OF A BOLT SET VERTICALLY IN THE DOWNSTREAM CORNER OF        19.272     659.642

FIRST FOOTING FROM THE GAGE OF THE WALKWAY. THE BOLT IS MARKED WITH

A CHISELED CROSS.

RM8           (SET BY TVA) CHISELED TRIANGLE ON THE RIGHT UPSTREAM CURB.                 34.640     675.010

RM9           (9/2/75) USGS TABLET SET IN THE DOWNSTREAM LEFT CURB.                      36.132     676.502

RP1           PENCILED ARROW ON THE WIRE-WEIGHT GAGE BRACE.                              35.871     676.241

RP2           BOLT SET IN HANDRAIL OF BRIDGE NEAR WIRE-WEIGHT GAGE AT STATION 151.       35.494     675.864

LOCATION: Flint River NEAR Chase, AL                                Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: CHSA1                          HSA: HUN                     NWS FORM E-19 PAGE 2: BENCHMARKS

GAGES

DCP                                        TELEM

NESS ID:                         TYPE OF TELEMETRY: telemark

OWNER:                                     OWNER: USGS

REPORT TIME:                              PHONE NUMBER: 205-852-3156

INTERVAL:                                  INTERVAL: UNK

CRITERIA: NONE

PAYOR/COST OF LINE: USGS / $

GAGE TYPE   OWNER       MAINTENANCE BEGAN      ENDED      GAGE LOCATION/REMARKS

----------- ----------- ----------- ---------- ---------- -----------------------------------------------

staff       NWS         NWS         05/16/1930 05/15/1934 STAFF GAGE LOCATED AT THE RAILROAD BRIDGE.

float       USGS        USGS        05/15/1934 09/01/1965 GRAPHIC RECORDER IN A STANDARD 5' X 5' CONCRETE									    HOUSE AND WELL ON .3 MILE DOWNSTREAM AT SAME DATUM.

float       USGS        USGS        09/01/1965 01/01/1974 DIGITAL RECORDER AT SAME SITE AND DATUM.

pres trans  USGS        USGS        01/01/1974            DIGITAL RECORDER ACTIVATED BY SERVO-MANOMETER AT					                                  PRESENT SITE.

LOCATION: Flint River NEAR Chase, AL                                Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: CHSA1                          HSA: HUN                     NWS FORM E-19 PAGE 3: GAGES

HISTORY

PUBLICATION/LOCATION OF RECORDS       STARTING DATE    ENDING DATE

-------------------------------       -------------    -----------

USGS                                  10/01/1929

TYPE OF GAGE              OWNER       STARTING DATE    ENDING DATE

------------              -----       -------------    -----------

staff                     NWS         05/16/1930       05/15/1934

float                     USGS        05/15/1934       09/01/1965

float                     USGS        09/01/1965       01/01/1974

pres trans                USGS        01/01/1974

ZERO ELEVATION                        STARTING DATE

--------------                        -------------

640.370                              10/01/1929

LOCATION: Flint River NEAR Chase, AL                                Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: CHSA1                          HSA: HUN                     NWS FORM E-19 PAGE 4: HISTORY

CRESTS

FLOOD STAGE: 16.00    ACTION STAGE: 14.00     BANKFULL STAGE: 16.00

FLOOD FLOW: 0           ACTION FLOW:

DATE OF    TIME   CREST  FLOW   FROM HIGH  BASED ON  CAUSED BY

CREST      LST    (ft)   (CFS)  WATERMARKS OLD DATUM ICE JAM   REMARKS

---------- ------ ------ ------ ---------- --------- --------- -------------------------------------------

09/01/1929 UNDEF   25.00  58500     X

05/10/1933 UNDEF   15.00

03/02/1934 UNDEF   17.30

03/12/1935 UNDEF   14.90

07/04/1936 UNDEF   18.10

01/02/1938 UNDEF   15.50

02/03/1939 UNDEF   17.80

12/28/1942 UNDEF   14.20

03/29/1944 UNDEF   16.80

02/17/1945 UNDEF   15.10

01/08/1946 UNDEF   17.10

02/13/1948 UNDEF   17.80

01/05/1949 UNDEF   23.60

01/06/1950 UNDEF   15.40

02/01/1951 UNDEF   22.00

03/11/1952 UNDEF   12.80

02/21/1953 UNDEF   13.80

03/22/1955 UNDEF   17.80

04/16/1956 UNDEF   14.30

02/01/1957 UNDEF   19.70

12/19/1959 UNDEF   17.20

03/03/1960 UNDEF   13.10

02/22/1961 21:30   14.73  12900

03/08/1961 17:00   16.37  16300

03/21/1961 17:30    9.70   6460

06/07/1961 03:30    8.98   5640

12/12/1961 14:00    9.00   5720

12/18/1961 10:30   14.48  12400

01/06/1962 15:30    8.31   5030

01/23/1962 16:00   10.01   6780

01/28/1962 13:00   12.26   9360

02/23/1962 17:30   14.60  12600

02/25/1962 20:30   11.02   7890

02/28/1962 19:00   15.50  14400

03/31/1962 18:00   10.48   7300

04/11/1962 01:30   11.64   8610

03/06/1963 01:30   17.32  18900

03/12/1963 09:00   27.60  55900

03/15/1964 09:00   21.00  30000

04/27/1964 17:00   15.10  13600

03/30/1965 02:15   13.70  11200

02/13/1966 17:45    9.49   6230

12/18/1967 14:45   21.00  29900

02/02/1969 16:15   14.50  12500

05/18/1969 21:00   15.87  15200

12/30/1969 21:00   18.50  23700

04/02/1970 12:45   16.60  19000

LOCATION: Flint River NEAR Chase, AL                                Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: CHSA1                          HSA: HUN                     NWS FORM E-19 PAGE 5: CRESTS

DATE OF    TIME   CREST  FLOW   FROM HIGH  BASED ON  CAUSED BY

CREST      LST    (ft)   (CFS)  WATERMARKS OLD DATUM ICE JAM   REMARKS

---------- ------ ------ ------ ---------- --------- --------- ----------------------------------------------

02/22/1971 12:15   14.52  14400

01/10/1972 16:30   10.16   6960

03/16/1973 12:30   29.52 104000

05/28/1973 05:30   14.37  14100

12/26/1973 17:30   18.92  24800

01/11/1974 17:00   17.01  20000

03/14/1975 00:30   20.97  29800

03/30/1975 04:00   14.79  13100

10/08/1975 19:00   15.25  14000

10/17/1975 19:45   19.20  24000

03/04/1976 18:00   16.10  17600

03/12/1976 23:15   18.01  22500

04/05/1977 00:30   21.22  33100

10/02/1977 12:30   19.61  27500

11/05/1977 18:45   15.06  15200

02/25/1979 16:30   14.14  12800

03/04/1979 10:45   16.50  18100

03/21/1980 16:00   16.43  18000

03/30/1981 UNDEF    8.01   4460

04/06/1983 12:30   18.10  22400

05/19/1983 19:00   19.35  26400

05/03/1984 18:00   15.48  15500

11/24/1986 10:30   13.63  11900

12/10/1986 05:30   13.40  11500

01/20/1988 07:15   13.41  11600

02/21/1989 19:30   14.24  13000

03/06/1989 04:30   19.22  26000

06/09/1989 15:15   15.54  15700

10/02/1989 06:00   16.33  17700

02/04/1990 10:15   15.51  15600

12/23/1990 06:45   31.04  87300                                FLOOD OF RECORD

02/19/1991 21:00   23.61  44000

03/29/1991 18:30   17.97  22200

06/19/1992 UNDEF   12.30

05/04/1993 UNDEF   17.36  20400

02/11/1994 UNDEF   22.07  36900

03/03/1998 UNDEF   14.20

05/07/2000 01:00   18.94

02/16/2003 18:00   11.81

02/23/2003 00:00   14.03                                       estimated crest based on 6-hourly data

05/07/2003 06:00   18.94                                       estimated based on 6-hourly

02/06/2004 15:00   20.50                                       estimated...due to 6-hour river observation

12/07/2004 11:00   19.40  26608                                Inserted from the FloodTS table via Hydrobase

12/10/2004 04:00   16.50  18158                                Inserted from the FloodTS table via Hydrobase

LOCATION: Flint River NEAR Chase, AL                                Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: CHSA1                          HSA: HUN                   NWS FORM E-19 PAGE 5-2: CRESTS

LOW WATER RECORDS

DATE OF     STAGE    FLOW

LOW WATER   (ft)     (CFS)   REMARKS

----------  -------  ------  ---------------------------------------------

09/03/1954     0.82

LOCATION: Flint River NEAR Chase, AL                                Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: CHSA1                          HSA: HUN                     NWS FORM E-19 PAGE 6: LOW WATER

CONDITIONS AFFECTING FLOW

MILES ABOVE MOUTH: 36.2       DRAINAGE AREA: 342.0      POOL STAGE: 0.0

STREAM BED: BEDROCK

REACH: 400 FT UPSTREAM TO 600 FT DOWNSTREAM.

REGULATION: NONE.

DIVERSION: NONE

WINTER: NO ICE EFFECT EXPECTED.

TOPOGRAPHY: CHANNEL IS STRAIGHT FOR ABOUT 6000 FT DOWNSTREAM.  ONE

CHANNEL AT ALL STAGES. THE BANKS ARE LOW AND NOT WELL

DEFINED.

REMARKS: THE CONFLUENCE OF THE FLINT RIVER (230 SQUARE MILES) AND

BRIER FORK (112 SQUARE MILES) IS 400 FT UPSTREAM FROM THE

ORIFICE.

LOCATION: Flint River NEAR Chase, AL                                Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: CHSA1                          HSA: HUN                     NWS FORM E-19 PAGE 7: CONDITIONS

DAMAGE

STAGE    AREAS AFFECTED

-------  ----------------------------------------------------------------------------------------------------

16.00  FLOOD STAGE. FLOODING IS OCCURRING BOTH UPSTREAM AND DOWNSTREAM OF THE GAGE SITE...BUT NO IMPACTS

ARE FELT AT THE GAGE SITE.

25.00  MODERATE FLOODING.

30.00  MAJOR FLOODING.

31.50  EXTENSIVE FLOODING IS LIKELY IN MADISON COUNTY, TO THE NORTHEAST OF HUNTSVILLE FROM NEAR

MERIDIANVILLE TO BELL FACTORY AND BROWNSBORO.

LOCATION: Flint River NEAR Chase, AL                                Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: CHSA1                          HSA: HUN                     NWS FORM E-19 PAGE 8: DAMAGE

RIVER STAGE DATA

|  46-|

|-----|

|-----|

|-----|

|-----|

|  41-|

|-----|

|-----|

|-----|

|-----|

|  36-|

|-----|

|-----|

|-----|

|-----|

31.50 - EXTENSIVE FLOODING IS LIKELY IN MADISON COUNTY, TO THE NORTHEAST OF HUNTSVILLE FROM     |  31-|   31.04  12/23/1990

NEAR MERIDIANVILLE TO BELL FACTORY AND BROWNSBORO.                                      |-----|

30.00 - MAJOR FLOODING.                                                                         |-----|   29.52  03/16/1973

|-----|

|-----|   27.60  03/12/1963

|  26-|

25.00 - MODERATE FLOODING.                                                                      |-----|   25.00  09/01/1929

|-----|

|-----|   23.61  02/19/1991

|-----|   22.07  02/11/1994

|  21-|   21.22  04/05/1977

|-----|   20.97  03/14/1975

|-----|   19.70  02/01/1957

|-----|   18.94  05/07/2003

|-----|   17.97  03/29/1991

16.00 - FLOOD STAGE. FLOODING IS OCCURRING BOTH UPSTREAM AND DOWNSTREAM OF THE GAGE             |  16-|   16.50  12/10/2004

SITE...BUT NO IMPACTS ARE FELT AT THE GAGE SITE.                                        |-----|

|-----|   14.03  02/23/2003

|-----|   13.63  11/24/1986

|-----|

|  11-|   11.81  02/16/2003

|-----|

|-----|

|-----|

|-----|

|   6-|

|-----|

|-----|

|-----|

|-----|

|   1-|

|-----|

|-----|

|-----|

|-----|

REACH: 400 FT UPSTREAM TO 600 FT DOWNSTREAM.                                           	ELEVATION ZERO:  640.37

LOCATION: Flint River NEAR Chase, AL                                Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: CHSA1                          HSA: HUN                     NWS FORM E-19 PAGE 9: STAFF

CONTACTS

SQ  CONTACT/REMARKS                                    PHONE

--  -------------------------------------------------- ------------------

1  Madison County EMA                                 256-427-5130

Director:  John Rusty Russell

LOCATION: Flint River NEAR Chase, AL                                Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: CHSA1                          HSA: HUN                    NWS FORM E-19 PAGE 10: CONTACTS

Downstream view.


View of gage house.