UH-1 SERIES

INSPECTION PLANNING GUIDE

INTERAGENCY COMMITTEE

for

AVIATION POLICY

This UH-1 Inspection Planning Guide (IPG) supersedes

the UH-1 IPG dated March 26, 1996 and includes

Revision 1 (12 March 1997) and Revision 2 (March 1, 2002)          |

________________________________________________________________________

### 1 March 2002                                   |

TABLE OF CONTENTS		PAGE

Chapter/ Section

RECORD OF REVISIONS					3

CHAPTER 1	INTRODUCTION					6

WARNINGS, CAUTIONS, and NOTES DEFINED	7

FORMAT DEFINED					8

#### POINTS OF CONTACT						8                       |

#### LIST OF DEFINITIONS					10                      |

CHAPTER 2	INSPECTION DESCRIPTIONS				15

INSPECTION SCHEDULE CHART			16

SPECIAL INSPECTIONS LISTING			17

CONDITIONAL INSPECTIONS (AIRFRAME) LISTING	18

CONDITIONAL INSPECTIONS (ENGINE) LISTING	19

INSPECTIONS

CHAPTER 3	PREVENTIVE MAINTENANCE INSPECTION (P.M.I.)	20

CHAPTER 4	DETAIL #1					25

CHAPTER 5	DETAIL #2					28

CHAPTER 6	DETAIL #3					30

CHAPTER 7	SPECIAL INSPECTIONS				34

CHAPTER 8	CONDITIONAL INSPECTIONS (AIRFRAME)		38

CHAPTER 9	CONDITIONAL INSPECTIONS (ENGINE)		54

APPENDIX	Letter from Bell Textron

Ref: Overhaul and Retirement Schedule,

Manuals and Technical Assistance		66                      |

RECORD OF REVISIONS

Originally accepted by the FAA on 26 March 1996.

Revision 1 (12 March 1997):

| POSTED: |  |  |  |  |
| --- | --- | --- | --- | --- |
|  |  | REVISION NUMBER | PAGE NUMBER(S) |  |
| DATE | BY |  |  |  |
|  |  | Rev. 1 (12 March 1997) | Removed page 18, Inserted new page 18. |  |
|  |  | Rev. 1 (12 March 1997) | Removed pages 23 to 26, Inserted new pages 23-26. |  |
|  |  | Rev. 1 (12 March 1997) | Removed page 29, Inserted new page 29. |  |
|  |  | Rev. 2 (1 Mar 2002) | Cover page date “March 12, 1997” Changed to “This UH-1 Inspection Planning Guide (IPG) supersedes the UH-1 IPG dated March 26, 1996, and includes Revision 1 (12 March 1997) and Revision 2 1 March 1, 2002) and “1 March 2002” |  |
|  |  | Rev. 2 (1 Mar 2002) | Page 2 Changed to include “Points of Contact”, “Definitions” and “Appendix” |  |
|  |  | Rev. 2 (1 Mar 2002) | Page 3 Changed to indicated “Revision 2, 1 March 2002” updates. |  |
|  |  | Rev. 2 (1 Mar 2002) | Page 6, General, “WARNING” changed to include “UH-1 D and H” helicopters. |  |

|  |  | Rev. 2 (1 Mar 2002) | Page 6, third sentence from end of page now states, “An owner/operator shall develop a checklist for each inspection outlined in this document. Refer to (current version) TM 55-1520-210-PMD UH-1H/V, and EH-1H/X Aircraft Preventive Maintenance Daily Inspection Checklist when developing checklist.” |  |
| --- | --- | --- | --- | --- |
|  |  | Rev. 2 (1 Mar 2002) | Page 4 Added to 1-1. General in the first paragraph, “This includes a review of the aircraft, aircraft engines, appliances, and the forms and records for any recorded discrepancies and for any applicable Airworthiness Directives, Safety of Flight Messages, ASAMS, TM’s TB’s, etc. that must be complied with.” |  |
|  |  | Rev. 2 (1 Mar 2002) | Page 6, “POINTS OF CONTACT” added. |  |
|  |  | Rev. 2 (1 Mar 2002) | New Page 10 Now includes “Definitions”. |  |
|  |  | Rev. 2 (1 Mar 2002) | Page 8 Now page 16. Chapter 2, Inspection Descriptions, 2-7, “NOTE”, 3., changed to include, “THE “ANNUAL CYCLE” STARTS AGAIN WHEN ALL INSPECTIONS ARE COMPLETED.” |  |
|  |  | Rev. 2 (1 Mar 2002) | Page 12 Now page 20. Chapter 3, Preventive Maintenance Inspection (P.M. I.), Section I, 2., now states, 2., “Review service instructions for maintenance and inspection requirements for installed kits, MWOs and STCs as appropriate.” |  |

|  |  | Rev. 2 (1 Mar 2002 | Page 12 Now page 20. Chapter 3, Preventive Maintenance Inspection (P.M. I.), Section I, 5., now states, 5., “Ensure all applicable Airworthiness Directives (Safety of Flight |  |
| --- | --- | --- | --- | --- |
|  |  | Rev. 2 (1 Mar 2002 | Page 13 Now page 21. Chapter 3, Preventive Maintenance Inspection (P.M. I.), Section III, 19., now states, “Check main rotor for proper lubricant level, inspect for evidence of leakage, and obvious contamination. Not applicable if aircraft is modified with grease hub.” |  |

1.	All personnel to whom this IPG is furnished shall keep it up to date with the changes and additions furnished to them.

2.	Each IPG shall have the date of the last revision on each page.

CHAPTER 1

INTRODUCTION

___________________________________________________________________________________________

1-1.  GENERAL

This document, the UH-1 Series Inspection Planning Guide (IPG) is available to operators of UH-1 series helicopters (except UH-1N models) for the purpose of providing operators with a choice in maintenance programs.  In accordance with the inspection standards set forth in the specific aircraft type certificate, the owner/operator must use the complete inspection program developed by the applicable military service.  This includes a review of the aircraft, aircraft engines,        |

appliances, and the forms and records for any recorded discrepancies and for any    |

applicable Airworthiness Directives, Safety of Flight Messages, ASAMS, TM’s TB’s,   |

etc. that must be complied with. 									|

This document, the IPG, has been developed as an alternative reasonable basis for inspection program development.

The owner/operator conducting public use operations may use this document as a reasonable basis for the development of an inspection program to assure an equivalent level of safety.

WARNING

UNLESS SPECIFICALLY DESIGNATED HEREIN, STANDARDS FOR SERVICEABILITY FOR THE AIRFRAME MAINTENANCE AND INSPECTION CONTAINED IN THIS DOCUMENT ARE FOUND IN THE APPLICABLE MILITARY MAINTENANCE DOCUMENT FOR THESE SPECIFIC MAKE AND MODELS OF AIRCRAFT, I.E. NAVY UH-1E, UH-1L, TH-1L, HH-1K; ARMY UH-1B, UH-1C/M, UH-1D/H; AIR FORCE HH-1H).                        |

UNLESS SPECIFICALLY DESIGNATED HEREIN STANDARDS FOR SERVICEABILITY FOR THE ENGINE MAINTENANCE AND INSPECTION CONTAINED IN THIS DOCUMENT ARE FOUND IN THE APPLICABLE MILITARY MAINTENANCE DOCUMENT OR THE APPLICABLE ALLIED SIGNAL LYCOMING DOCUMENT FOR THESE SPECIFIC MODELS OF ENGINE.( T53L11, T53L13, T53L703)

This document contains the requirements for the Preventive Maintenance Inspection

(P.M.I.), Detail (#1-#2-#3) Inspections, Special Inspections and Conditional

Inspections that shall be performed on the UH-1 series helicopters.

Inspections required herein shall be performed by a properly rated repairman (under

14 Code of Federal Regulations, Part 65) or a Federal Aviation Administration

certified Airframe and Powerplant mechanic.

An owner/operator shall develop a checklist for each inspection outlined in this

document.  Refer to (current version) TM 55-1520-210-PMD UH-1H/V, and EH-1H/X Aircraft   |

Preventive Maintenance Daily Inspection Checklist when developing checklist.             |

Maintenance functions and definitions of terms shall be in accordance with applicable military maintenance manual for the UH-1 Series unless otherwise stipulated in this document.

The IPG is applicable to a standard UH-1 series helicopter operating in a flight profile similar to the US military.

NOTE

UH-1 HELICOPTERS USED FOR REPETITIVE HEAVY LIFT AND OTHER UNIQUE OPERATIONS (LOGGING, WATER BUCKET, LONG LINE, ETC.), SHALL REQUIRE ADDITIONAL AND/OR MORE FREQUENT INSPECTIONS AS DEEMED NECESSARY BASED ON OPERATIONAL EXPERIENCE AND/OR ALERT SERVICE BULLETINS AND/OR AIRWORTHINESS DIRECTIVES.  UH-1 HELICOPTERS MODIFIED THROUGH INCORPORATION OF SUPPLEMENTAL TYPE CERTIFICATES OR EQUIPPED WITH SPECIAL MISSION KITS SHALL REQUIRE ADDITIONAL INSPECTIONS AS DEEMED NECESSARY.

The IPG is primarily presented for UH-1H model helicopters.  Inspection requirements peculiar to 540 main rotor equipped helicopters are denoted “540 M/R”. The IPG is also primarily presented for the T53L11, T53L13 and T53L703 engines.  The engine should be maintained and inspected in accordance with the manufacturer’s maintenance manual and the appropriate manufacturer’s service bulletins.

NOTE

AN ENGINE HEALTH INDICATOR TEST IS NORMALLY A PRE-FLIGHT FUNCTION PERFORMED BY THE PILOT AND HAS NOT BEEN INCLUDED IN THE IPG.  HOWEVER, THE OPERATOR SHOULD ESTABLISH A METHOD FOR ENGINE TREND MONITORING TO EVALUATE ENGINE HEALTH AND PERFORMANCE.  A SUGGESTED METHOD FOR ENGINE TREND MONITORING IS THE HEALTH INDICATOR TEST (HIT) AS DESCRIBED IN APPROPRIATE US ARMY MANUALS.

1-2.	WARNING, CAUTIONS, AND NOTES DEFINED.

WARNING

AN INSPECTION PROCEDURE, PRACTICE, ETC., WHICH IF NOT CORRECTLY FOLLOWED, COULD RESULT IN PERSONAL INJURY OR LOSS OF LIFE.

CAUTION

AN INSPECTION PROCEDURE, PRACTICE, ETC., WHICH, IF NOT STRICTLY

OBSERVED, COULD RESULT IN DAMAGE TO OR DESTRUCTION OF EQUIPMENT.

NOTE

AN INSPECTION PROCEDURE, CONDITION, ETC., WHICH IS ESSENTIAL TO HIGHLIGHT

1-3.	FORMAT DEFINED

The IPG is divided into:

Example:

Chapters,				CHAPTER 7 SPECIAL INSPECTIONS

Sections,				SECTION V.  LOWER PYLON

Headings,				8-1. HARD LANDING

Paragraphs,				10.  Tail rotor gearbox.

and subparagraphs.			     10.1.  Remove tail rotor

gearbox.  Check for cracks.  Etc.

a.  Main rotor blades.

(1)  Bolt contact etc.

(a)  Remove spline etc.

1.  Tighten bolt etc.

1-4.  POINTS OF CONTACT											|

www.gsa.gov/aircraftpolicy		Web Site for the General Services Administration| Aircraft Management Policy Division.  The       |

“caretaker” of the Inspection Planning Guides.  |

Charlie Elkins                                                                      |

(256) 955-0773				ATCOM UH-1 contact.                             |

Susan Lewis													|

(256) 955-0773				ATCOM OH-58 contact.                            |

Paul Elliott                   								      |

(602) 231-3077                                                                      |

paul.Elliott@honeywell.com                                                          |

Russ Smith                                                                          |

(602) 231-3599                                                                      |

russ.smith@honeywell.com                                                            |

Dan Grady		                                                                  |

(602) 231-3348

dan.grady@honeywell.com			Honeywell contacts for T53 engines.  Technical  |

publications.                                   |

National Technical Information Service                                              |

1 800 553-6847                                                                      |

(703) 605-6000                                                                      |

5285 Port Royal Road                                                                |

Springfield, VA  22161			Maintenance manuals for Army helicopters.       |

Randy Stewart                                                                       |

Department of Energy                                                                |

Senior Aviation Policy Officer, MA-10                                               |

Office of Aviation Management                                                       |

1000 Independence Ave., SW,                                                         |

Rm 9H-063                                                                           |

Washington, DC  20585			                                                |

(202) 586-6171				IPG Work Group                                  |

Andrew L. Kelley                                                                    |

Product Support Engineer                                                            |

Bell Helicopter Textron                                                             |

PO Box 482                                                                          |

Fort Worth, TX  76101                                                               |

(817) 280-4074				IPG Work Group                                  |

Richard Thomas                                                                      |

Federal Aviation Administration                                                     |

FTW-Aircraft Evaluation Group (AEG)                                                 |

Fort Worth, Texas  76193-0270                                                       |

(817) 222-5272				IPG Work Group                                  |

Mike Miles                                                                          |

General Services Administration                                                     |

1800 F Street, NW  Rm 1221A                                                         |

Washington, DC  20405                                                               |

(202) 219-1356				IPG Work Group                                  |

Definitions               |

_________________________________________________________________________________

AIRCRAFT means a device that is used or intended to be used for flight.

AIRCRAFT ENGINE means an engine that is used or intended to be used for propelling aircraft.  It includes turbo-superchargers, appurtenances, and accessories necessary for its functioning, but does not include propellers.

AIRFRAME means the fuselage, booms, nacelles, cowlings, fairings, airfoil surfaces (including rotors but excluding propellers and rotating airfoils of engines), and landing gear of an aircraft and their accessories and controls.

AIRCRAFT MAINTENANCE means that work which is required to be performed by an appropriately certificated and qualified person(s).

AIRWORTHINESS DIRECTIVE means a maintenance procedure dictated by the Federal Aviation Administration that must be performed on an aircraft in order to remain airworthy.

APPROVED unless used with reference to another person, means approved by the FAA Administrator.

APPLIANCE means any instrument, mechanism, equipment, part, apparatus, appurtenance, or accessory, including communications equipment, that is used or intended to be used in operating or controlling an aircraft in flight, is installed in or attached to the aircraft, and is not part of an airframe, engine, or propeller.

CALIBRATION means making precise measurements and adjustments to equipment or systems in order to obtain optimum performance and to certify that output data falls within prescribed tolerances.

CAUTION means a maintenance or inspection procedure, practice, etc., which, if not strictly observed, could result in damage to or destruction of equipment.

CHECK means an action taken to examine and verify, in accordance with established procedures and requirements, the condition or status of an aircraft, its systems, components, and/or accessories.

CIVIL AIRCRAFT means an aircraft that may or may not be owned or leased by the United States Government or a State or local government; that holds, or is cabable of holding an airworthiness certificate; and is cabable of transporting passengers or engaging in commercial purposes. (see PUBLIC AIRCRAFT)

COMPONENT any self-contained part, combination of parts, subassemblies or units, which perform a distinctive function necessary to the operation of the airframe, powerplant or propeller.

CONDITIONAL INSPECTION means an inspection which is contingent upon specific conditions or incidents that arise, and only because of these conditions or incidents.  Examples of these conditions or incidents are hard landings, overspeed, and sudden stoppage.  An inspection is required in such cases before further flight.

(ENGINE) CYCLE means an engine start and shutdown procedure to be counted as “1”.  For the purposes of this document and historical purposes (2 cycles per flight hour plus 25%) is the method recommended to determine the number of cycles on engines that have not been logging cycles.  After that, 1 cycle per flight hour.

DMWR (pronounced dimwar) means Depot Maintenance Work Requirement.  It is a document that details maintenance and inspection criteria for specific components.

FOREIGN OBJECT DAMAGE (FOD) means damage to an aircraft, airframe. or engine caused by a foreign object that is not part of the aircraft, or has broken loose of the aircraft and caused damage.

GROUND RUN (see RUN-UP) means operating the aircraft on the ground, with no intention of taking off, from a normal start thru flight idle, as a minimum.

HARD LANDING means any accident or incident in which ground impact of the helicopter causes severe pitching of main rotor, allowing hard contact of hub with mast, or results in yielding or noticeable cracking of fuselage pylon support structure or landing gear.

HARD-TIME means a primary maintenance process that requires an appliance or part be periodically overhaul in accordance with the Agency’s maintenance manual or that it be removed from service.

HEALTH INDICATOR (ENGINE) TEST (HIT) means a method for engine trend monitoring to evaluate engine health and performance.

INSPECT means a method of qualifying the condition or status of the aircraft, its systems, components, and/or accessories to specific standards and requirements.

INTERMEDIATE INSPECTION means an inspection that is performed each 25 hours.

MAINTENANCE INSPECTIONS include daily/preflight, segment, safety, service, special, and numbered inspections.  These inspections vary in scope and frequency of performance according to types of aircraft.

MODIFICATION WORK ORDER (MWO) means an authorization to perform a modification on an aircraft to correct or enhance an existing condition.  This is a military term and is similar to a commercial model service instruction.

MAJOR ALTERATIONS means an alteration not listed in the aircraft, or aircraft engine/rotor specifications that (1) might appreciably affect weight, balance, structural strength, performance, powerplant operation, flight characteristics, or other qualities affecting airworthiness; or (2) is not done according to accepted practices, or cannot be done by elementary operations (refer to

Part 43).

MAJOR REPAIR means a repair that (1) if improperly done, might appreciably affect weight, balance, structural strength, performance, powerplant operations, flight characteristics, or other qualities of airworthiness; or (2) is not done according to accepted practices, or cannot be done by elementary operations (refer to Part 43).

MAST BUMPING or flapping-stop contact means the condition which occurs when the main yoke contacts the mast and may result in a fractured mast and rotor seperation.  It usually occurs during; slope landings, rotor startup/coastdown, or when the flight envelope is exceeded.

MINIMUM EQUIPMENT LIST (MEL) means a regulatory authorization to continue to operate an aircraft with inoperable instruments or equipment.  The aircraft may be operated under all applicable conditions and limitations contained  in the minimum equipment list.

MINOR ALTERATION means a modification that is an alteration other than a major alteration.

MINOR REPAIR means a repair that is other than a major repair.

NOTE means an inspection or maintenance procedure, condition, etc., which is essential to highlight

ON CONDITION ITEM (OC) means an item of equipment that must be restricted to one on which a determination of continued airworthiness may be made by a visual check, measurement, test, or other means.

OPERATIONAL CHECK means an "in motion" or "power on" test for determining that an item of equipment will operate at a specified performance level.

OVERHAUL means the complete disassembly, cleaning, inspection, necessary replacement or repair of parts, reassembly, adjustment, and testing of an item or equipment in accordance with recommended procedures.

PREVENTIVE MAINTENANCE means simple or minor preservation operations and the replacement of small standard parts not involving complex assembly operations.  It is corrective action taken before it becomes necessary to make a major repair.

PREVENTIVE MAINTENANCE INSPECTION (P.M.I.) means an inspection which is accomplished each 12 1/2 flight hours or every 14 calendar days, whichever occurs first.

PUBLIC AIRCRAFT means an aircraft used only for the United States Government, an aircraft owned by the Government and operated by any person for purposes related to crew training, equipment development, or demonstration, an aircraft owned and operated by the government of a State, the District of Columbia, or a territory or possession of the United States or a political subdivision of one of these governments, an aircraft exclusively leased for at least 90 continuous days by the government of a State, the District of Columbia, or a territory or possession of the United States or a political subdivision of one of these governments, an aircraft owned or operated by the armed forces or chartered to provide transportation to the armed forces.  In this definition, the following definitions apply:

(1) COMMERCIAL PURPOSES means the transportation of persons or property for compensation or hire, but does not include the operation of an aircraft by the armed forces for reimbursement when that reimbursement is required by any Federal statute, regulation, or directive, in effect on November 1, 1999, or by one government on behalf of another government under a cost reimbursement agreement if the government on whose behalf the operation is conducted certifies to the Administrator of the Federal Aviation Administration that the operation is necessary to respond to a

significant and imminent threat to life or property (including natural resources) and that no service by a private operator is reasonably available to meet the threat.

(2) GOVERNMENTAL FUNCTION means an activity undertaken by a government, such as national defense, intelligence missions, firefighting, search and rescue, law enforcement (including transport of prisoners, detainees, and illegal aliens), aeronautical research, or biological or geological resource management.

(3) QUALIFIED NON-CREWMEMBER means an individual, other than a member of the crew, aboard an aircraft--

(A) operated by the armed forces or an intelligence agency of the United States Government; or

(B) whose presence is required to perform, or is associated with the performance of, a governmental function.

(4) ARMED FORCES has the meaning given such term by section 101 of title 10.

An aircraft does not qualify as a public aircraft when the aircraft is used for commercial purposes or to carry an individual other than a crewmember or a qualified non-crewmember.

AIRCRAFT OWNED OR OPERATED BY THE ARMED FORCES qualifies as a public aircraft if:

(A) the aircraft is operated in accordance with title 10;

(B) the aircraft is operated in the performance of a governmental function under title 14, 31, 32, or 50 and the aircraft is not used for commercial purposes; or

(C) the aircraft is chartered to provide transportation to the armed forces and the Secretary of Defense (or the Secretary of the department in which the Coast Guard is operating) designates the operation of the aircraft as being required in the national interest.

LIMITATION  An aircraft that is owned or operated by the National Guard of a State, the District of Columbia, or any territory or possession of the United States, qualifies as a public aircraft only to the extent that it is operated under the direct control of the Department of Defense.

REPAIR means the restoration of an item of equipment to a serviceable condition after fault detection.

RUN UP (see GROUND RUN) means operation of the aircraft from normal start thru flight idle.  Flight of the aircraft may be planned.

SPECIAL INSPECTION means an inspection, in addition to the P.M.I., Intermediate and Periodic Inspections, that are inspections performed on a calendar basis, a cycle basis, a combination of hourly/calendar basis, or following the installation of a major component such as a gearbox installation.

TIME CONTROLLED COMPONENT means a part or component which has an established service life, at which time certain maintenance must be performed or the item disposed of as unserviceable.  The service life may be based on operating hours, cycles, landings, calendar time, or combinations of these.

UNSALVAGEABLE means an aircraft part that should not be returned to aviation use as defined by Federal Aviation Administration (FAA) Advisory Circular

(AC) No. 21-38 “Disposition of Unsalvageable Aircraft Parts and Materials

(7-5-94).“.  Persons disposing of unsalvageable aircraft parts and materials should, when appropriate, mutilate those parts and materials prior to release.  Mutilation should be accomplished in such a manner that the parts become unusable for their original intended use (see AC No. 21-38).

VISUAL INSPECTION means an inspection of an item of equipment for cleanliness, and deterioration of parts or materials by visual means.

WARNING means a maintenance or inspection procedure, practice, etc., which if not correctly followed, could result in personal injury or loss of life.

WIRE STRIKE Protection System (WSPS) means a basic system consisting of an upper cutter assembly, a windshield deflector/cutter assembly, and a lower cutter assembly that provides protection against frontal impacts with horizontally strung mechanical and power transmission wires.

SAFETY OF FLIGHT MESSAGE means an Army issued message that details a method to inspect, maintain, repair, or replace a component of a U.S. Army aircraft, usually an OH-58 or UH-1 helicopter.  SOF could also apply to flight procedures, operating limits, or operational policy.

CHAPTER 2

INSPECTION DESCRIPTIONS

__________________________________________________________________________________________

NOTE

PRIOR TO PLACING AN AIRCRAFT ON THIS PROGRAM, A P.M.I., DETAIL’S #1, #2, AND #3, AND ANY OTHER SPECIAL INSPECTIONS THAT MAY BE REQUIRED, OR AN INSPECTION FOR INITIAL CERTIFICATION, SHOULD BE ACCOMPLISHED.

2-1.	P.M.I.

P.M.I. is found in Chapter 3 and is accomplished each 10 flight hours or every

14 calendar days, whichever occurs first.

2-2.	Detail #1

Is found in Chapter 4 and is accomplished each 50 flight hours.

2-3.	Detail #2

Is found in Chapter 5 and is accomplished each 100 flight hours.

2-4.	Detail #3

Is found in Chapter 6 and is accomplished each 150 flight hours.

2-5.	SPECIAL INSPECTIONS

In addition to the P.M.I. and the Detail #1, #2, and #3 Inspections, required

Special Inspections found in Chapter 7 of the IPG are performed on a calendar basis, a combination of hourly/calendar basis, or following the installation of a major

component such as a gearbox installation.

2-6.	CONDITIONAL INSPECTIONS (AIRFRAME)

Conditional Inspections (Airframe) found in Chapter 8 of the IPG are

inspections required as a result of unusual events such as hard landings or

sudden stoppage of rotor.

2-7.	CONDITIONAL INSPECTIONS (ENGINE)

Conditional Inspections (Engine) found in Chapter 9 of the IPG are inspections required as a result of an unusual event such as engine oil filter bypass or engine overtemperature.

NOTE

THERE ARE NO PRESCRIBED INTERVALS FOR CONDITIONAL INSPECTIONS.

INSPECTION SCHEDULE CHART

INSPECTION SCHEDULES

Flight Hours

/  50         100        150          200         250         300

Inspection

P.M.I.			Every 10 Flight Hours or 14 Days, whichever occurs first.

DETAIL #1            X          X          X            X           X           X

DETAIL #2                       X                       X                       X

DETAIL #3                                  X                                    X

NOTE

1.	IF AN AIRCRAFT WILL BE OUT OF SERVICE MORE THAN 30 DAYS, A P.M.I. SHALL BE PERFORMED PRIOR TO RETURNING THE AIRCRAFT TO SERVICE.

2.	IF AN AIRCRAFT IS OUT OF SERVICE MORE THAN 14 DAYS, A RUN-UP IN ACCORDANCE WITH APPROPRIATE MANUALS IS STRONGLY RECOMMENDED.

3.	THE COMPLETE AIRCRAFT MUST BE INSPECTED WITHIN 12 CALENDAR MONTHS, WHICH MEANS ALL THREE DETAILS MUST HAVE BEEN PERFORMED.  IF AN AIRCRAFT FLIES LESS THAN 150 HOURS IN 12 CALENDAR MONTHS, THE REMAINDER OF THE DETAIL INSPECTIONS MUST BE PERFORMED.  IF AN AIRCRAFT FLIES GREATER THAN 150 HOURS, THE INSPECTION CYCLE IS CONTINUED.  THE “ANNUAL  |

CYCLE” STARTS AGAIN WHEN ALL INSPECTIONS ARE COMPLETED.  SEE INSPECTION SCHEDULE CHART  | ABOVE.

4.	ENGINE INSPECTIONS AND RETIREMENT LIFE LIMITED INTERVALS - REFER TO MILITARY MAINTENANCE DOCUMENT OR THE ALLIED SIGNAL LYCOMING MAINTENANCE DOCUMENT.

5.	COMPONENT OVERHAUL AND RETIREMENT LIFE LIMITED INTERVALS - REFER TO APPLICABLE MILITARY MAINTENANCE DOCUMENT OR MANUFACTURERS MAINTENANCE DOCUMENT.

2-8. SPECIAL INSPECTIONS LISTING (CHAPTER 7)

In addition to the P.M.I. and the Detail #1, #2, and #3 Inspections, Special Inspections are performed on a calendar basis, a combination of hourly/calendar basis, or following the installation of a major component such as a gearbox installation.

PAGE

1.	7-1.	AFTER EACH INSTALLATION.			34

2.	7-2.	AFTER FIRST FLIGHT, AFTER EACH INSTALLATION.	34

3.	7-3.	BETWEEN 5 AND 10 HOURS, AFTER EACH INSTALLATION.	34

4.	7-4.	EACH 25 HOURS OF OPERATION.			34

5.	7-5.	EACH 100 HOURS OR 120 DAYS, WHICHEVER OCCURS FIRST.	35

6.	7-6.	100 HOURS AFTER EACH INSTALLATION.		35

7.	7-7.	EACH 300 HOURS OR 6 MONTHS OF BATTERY OPERATION.	35

8.	7-8.	EACH 12 MONTHS MAGNETIC (MAG) COMPASS AND

RADIO MAGNETIC INDICATOR (RMI) CALIBRATION.	35

9.	7-9.	EACH 600 HOURS OR 12 MONTHS OF COMPONENT OPERATION,

WHICHEVER OCCURS FIRST.				35

10.	7-10.	EACH 24 MONTHS OF COMPONENT OPERATION.		36

(Includes Corrosion Inspection)

2-9.	CONDITIONAL INSPECTIONS (AIRFRAME) (CHAPTER 8)

Inspections required as a result of unusual events such as hard landings or sudden stoppage of rotor.

PAGE

1.	8-1.	HARD LANDINGS.					38

2.	8-2.	SUDDEN STOPPAGE - POWER ON OR OFF.		40

3.	8-3.	OVERSPEED.						44

4.	8-4.	OVERTORQUE (AIRFRAME AND ENGINE).		46

5.	8-5.	LIGHTNING STRIKE.					48

6.	8-6.	MAST BUMPING.					50

7.	8-7.	AFTER WIRE STRIKE.				50

8.	8-8.	AFTER LOWER WSPS GROUND CONTACT.		51

9.	8-9.	AFTER AIRCRAFT IS FLOWN INTO AREA WITH

BLOWING SAND AND/OR LOOSE GRASS.		51

10.	8-10.	AFTER WASHING HELICOPTER.			51

11.	8-11.	AFTER HELICOPTER SUBJECTED TO SALT WATER/SPRAY.	52

12.	8-12.	HELICOPTERS OPERATED IN SALT LADEN ENVIRONMENT.	52

13.	8-13.	AFTER HELICOPTER HAS BEEN PARKED/OPERATED

IN RAIN, ICE OR SNOW.				52

14.	8-14.	AFTER OVERFLOW OF BATTERY/SUMP JAR.		52

15.	8-15.	TRANSMISSION OIL OVER-TEMPERATURE.		52

16.	8-16.	COMPLETE LOSS OF TRANSMISSION OIL.		53

2-10.	CONDITIONAL INSPECTIONS (ENGINE) (CHAPTER 9)

A Conditional Inspection (Engine) is performed as a result of an unusual event such as engine oil filter bypass or engine overtemperature.

PAGE

1.	9-1.	FOREIGN OBJECT DAMAGE IS NOTED.		54

2.	9-2.	SUSPECTED COMPRESSOR STALL OR SURGE.		54

3.	9-3.	ENGINE IS DROPPED DURING HANDLING.		57

4.	9-4.	ENGINE SUDDEN STOPPAGE OCCURS.		58

5.	9-5.	ENGINE OVERSPEED.					58

6.	9-6.	ENGINE OIL OVERTEMPERATURE.			60

7.	9-7.	ENGINE SUBJECTED TO EXCESSIVE G-LOADS

(HARD LANDING, SEVERE MANEUVERS).		61

8.	9-8.	ENGINE INLET BLOCKAGE.				62

9.	9-9.	ENGINE OIL CONTAMINATION.			63

10.	9-10.	LOSS OF POWER OR HIGH EXHAUST GAS TEMPERATURE.	65

11.	9-11.	ENGINE OVERTEMPERATURE.				65

NOTE

THERE ARE NO PRESCRIBED INTERVALS FOR THESE INSPECTIONS.

CHAPTER 3

PREVENTIVE MAINTENANCE INSPECTION (P.M.I.)

__________________________________________________________________________________________

SECTION I.  GENERAL (SEE INSPECTION SCHEDULE CHART, PAGE 8)

1.	Inspect aircraft forms and records for recorded discrepancies.

- Ensure all applicable Airworthiness Directives (Safety of Flight, Alert Service    |

Bulletin's, ASAM’s, TM’s, TB, MIM’s , etc) are complied with.                            |

3.	Review records for SPECIAL or CALENDAR inspection items which are due.

4.	Review component listing for overhaul or retirement items which need to be

replaced.

5.	Review service instructions for maintenance and inspection requirements for

installed kits, MWOs and STCs as appropriate.                                            |

6.	Perform a general visual inspection of aircraft for condition and

cleanliness.

7.	Clean the aircraft, particularly the areas being inspected.

SECTION II.  LUBRICATION REQUIREMENTS

8.	Refer to applicable UH-1 lubrication chart.

SECTION III.  FORWARD FUSELAGE AREA

9.	Inspect nose structure and following components for condition and security.

a.	Windshields, nose structure and external equipment.

b.	Battery compartment structure and components and wiring.

c.	Pitot and static ports.

10.	Inspect crew and cargo doors and windows for damage and proper operation.

11.	Check cabin exterior for damage.  Inspect stencils, decals, and or placards

for legibility.

12.	Inspect flight, engine controls and manual cargo release assembly if

installed.

13.	Inspect Instrument panel, consoles and installed equipment.

1

14.	Inspect crew and passenger seats, and seat belts and shoulder harnesses for

damage and security.

15.	Inspect navigation, search and landing lights for condition and check for proper operation.

SECTION IV.  UPPER PYLON

16.	Inspect the upper fuselage structure, antennas, cowling and air intake

screens for debris, damage and security.

17.	Inspect upper and lower main rotor blade surfaces for damage, evidence of

corrosion and cracks.  Particular attention shall be given to the doubler area and

all bond lines.  Hairline cracks in the paint finish should be inspected closely

for possible voids.

18.	Inspect leading edge scarf joints for filler erosion, if splice cover is not

installed.

19.	Check main rotor for proper lubricant level, inspect for evidence of leakage,

and obvious contamination.  Not applicable if aircraft is modified with grease hub.      |

20.	Inspect main rotor grips for evidence of corrosion and visible damage.

Inspect shield area for trapped contamination.

21.	Inspect drag brace attachment lugs for damage, cracks and security.

22.	Inspect main rotor hub static stops for obvious deformation and/or cracks.

23.	Inspect main rotor yoke for general condition and security of pillow block

assembly attachment, paying particular attention to the area surrounding the pillow

block bushing bores.  Visually inspect for sealant integrity around yoke to pillow

block mating surface and around head and nut of yoke to pillow block attachment

bolt.

24.	Inspect pillow block bushing flange and outside area of bushing holes for

evidence of cracks/corrosion.

25.	Inspect main rotor pitch change links, damper tubes and connecting links for

scratches, nicks, dents, security of attachment and obviously worn bearings.

26.	Inspect mast assembly for obvious damage, particularly in the area of main

rotor hub static stop contact area.

27.	Check security of mast nut and mast.

28.	Inspect mast seal for evidence of leakage.

29.	Check stabilizer bar dampers for proper fluid level and security of

attachment.

30.	Inspect scissors and sleeve assembly for worn bearings and foreign object damage.

31.	Inspect swashplate assembly for worn bearings and foreign object damage.

32.	Inspect control lugs (3 ea.) on swashplate inner ring and (2 ea.) on swashplate outer ring for cracks.

33.	Inspect collective levers for security of attachment and foreign object damage.

34.	Inspect the transmission and pylon support structure area for damage, cracks, and leaks.

35.	Inspect main drive shaft and ensure freewheel unit functions properly.

36.	Inspect hydraulic reservoir for proper level, and inspect for abnormal

oil discoloration.

SECTION V.  LOWER PYLON

37.	Inspect transmission oil filter for bypass indication.

38.	Inspect transmission for proper oil level, and inspect for abnormal oil

discoloration.

39.	Inspect transmission mounts and supports for cracks and security.

40.	Inspect the transmission tail rotor output quill for grease leakage and for

over temperature indications.

41.	Inspect hydraulic system components for damage and leaks, and the filter for

bypass indication.

42.	Inspect hydraulic servo cylinder mount nuts for slippage marks.

43.	Inspect hell hole area for leaks, working fasteners, and general security of

components.  Pay particular attention to the servo/linkage area and the lift beam

and support case area.

44.	If external loads are anticipated - Clean and inspect hook assembly for wear

and damage.

45.	Inspect landing gear for damage and security.  Inspect cross tubes for visual

indications of excess spread and saddle areas for slippage, cracks and fretting.

SECTION VI.  ENGINE

NOTE

PERFORM A COMPRESSOR WASH WHEN INSPECTION REVEALS AN ACCUMULATION OF DIRT, WHEN ENGINE PERFORMANCE DECREASES EXCESSIVELY, AND WHENEVER EXHAUST GAS TEMPERATURE INCREASES STEADILY DURING NORMAL OPERATION.

46.	Inspect engine cowlings and fairings for security, damage, and loose or

missing fasteners.

47.	Inspect Foreign Object Damage (FOD) screen and particle separator as follows:

47.1.	Inspect FOD screen for damage which would permit foreign object entry.

If screen is damaged inspect compressor for damage.  Inspect as outlined in

9-1 FOREIGN OBJECT DAMAGE IS NOTED inspection.

47.2.	Inspect FOD screen exterior for presence of foreign material.  If

material such as rags, paper, grass or other vegetation is present enough to

disturb airflow to the inlet perform an inlet blockage inspection in

accordance with 9-8 Engine Inlet Blockage Inspection of the IPG.

48.	If the screen or separator is not installed, inspect the inlet as follows:

48.1.	Inspect inlet for accumulation of dirt conforming to contour of inlet

housing.  Buildup of dirt may conform to the shape of the inlet housing and

be difficult to detect.  ALL foreign matter must be completely removed.  Any

evidence of inlet blockage shall result in the 9-8 Engine Inlet Blockage

Inspection of the IPG being performed.

48.2.	Visually inspect compressor blades, inlet housing air passages and

variable guide vanes as visible from inlet housing.  Inspection shall be for;

foreign object damage, partial or complete inlet blockage, and salt, dirt oil

and varnish deposits.  If required, perform a compressor wash in accordance

with the appropriate maintenance manual.  Foreign object damage shall be

repaired if it exceeds the limits in the appropriate maintenance manual.

49.	Inspect droop cam assembly for signs of binding and cleanliness and linear

actuator for proper operation (except 540 M/R).

50.	Inspect engine mounts and shims for damage and security.

51.	Check that oil tank is filled to the proper level.  If oil filter has a

by-pass button, inspect for extension of that button.  If button is extended,

remove and clean filter elements.  Reset button and after next flight check for

extension of the bypass button.  If button is found extended, perform an engine oil

contamination inspection in accordance with 9-9 Engine Oil Contamination Inspection

of the IPG.

52.	Inspect power turbine blades through exhaust diffuser and inspect exhaust

diffuser for, cracks and burnt areas.

SECTION VII.  TAIL BOOM

53.	Inspect the tail boom attachment bolt areas for cracks and security.  Pay

particular attention to the upper left attachment area on both the fuselage and

tail boom.  (Check attachment hardware slippage marks).

54.	Inspect oil cooler blower assembly for cleanliness, blockage and rough bearings.

55.	Inspect tail rotor servo for security and leakage.

56.	Inspect elevators for damage, cracks and looseness.

57.	Inspect the external portions of vertical splice area, just forward of

intermediate gearbox, for cracks and corrosion.

58.	Inspect the external portions of the vertical fin structure for signs of

fretting, corrosion and cracks.

SECTION VIII.  TAIL ROTOR/DRIVE SYSTEM

59.	Clean and inspect tail rotor control chain and sprocket.  Inspect tail rotor cross head for axial and radial movement.

60.	Inspect intermediate and tail rotor gearbox attachment areas for signs of

fretting and movement.

61.	Check intermediate and tail rotor gearboxes for proper oil level and service

if required.  Inspect for abnormal oil discoloration.

62.	Visually inspect tail rotor drive flex couplings and hanger assemblies for

overheat indications, grease leakage, security and foreign objects.

63.	Visually inspect tail rotor blades for damage, cracks, and skin delamination,

with special attention to the area on both sides between the doublers and six

inches outboard of doublers.

CHAPTER 4

DETAIL #1 - 50 FLIGHT HOURS

__________________________________________________________________________________________

SECTION I.  GENERAL

1.	Perform a P.M.I.  Refer to INSPECTION SCHEDULE CHART, PAGE 8.

SECTION II.  MAIN ROTOR

NOTE

THE UH-1 INSPECTION PLANNING GUIDE (IPG) WAS DEVELOPED TO PROVIDE GUIDANCE IN PLANNING INSPECTION PROGRAMS FOR TEN MODELS OF THE UH-1 SERIES HELICOPTER.  THE PRIMARY DIFFERENCE| BETWEEN THE UH-1 SERIES OF HELICOPTERS ARE THOSE MODELS THAT INCORPORATE THE “540” ROTOR SYSTEM.  COMPONENTS OR PARTS LISTED BY PART NUMBER IN THE UH-1 IPG HAVE SPECIFIC INSPECTION CRITERIA THAT APPLY TO THAT PARTICULAR PART NUMBER.  IN ADDITION, THE LISTING OF A COMPONENT OR PART, BY PART NUMBER IN THE IPG, INDICATES THAT DUE TO THE DESIGN OF THAT PARTICULAR COMPONENT OR PART, SPECIAL ATTENTION IS REQUIRED OF THE REPAIRMAN OR INSPECTOR IN ORDER TO VERIFY CONTINUED AIRWORTHINESS.

OTHER COMPONENTS OR PARTS, NOT LISTED BY PART NUMBER IN THE UH-1 IPG, DO NOT REQUIRE SPECIAL ATTENTION OR INSPECTION OTHER THAN WHAT IS CALLED FOR IN THE UH-1 IPG OR REFERENCED MANUALS.

2.	Inspect stabilizer bar assembly for visual damage in the form of scratches,

nicks, dents, cracks, corrosion, and worn bearings.

2.1.	Inspect stabilizer tubes, 204-011-328-001, -011, for cracks, paying

particular attention to an area covering 360 degrees and 1-1/2 inches

outboard from vertical bolt.

3.	Inspect main rotor drag braces for evidence of corrosion and security of

attachment.  Make a close visual examination of inboard end (grip end) of drag

brace assembly for corrosion and/or cracks.

4.	Check torque on main rotor pillow block bolt nuts 64 to 79 foot-pounds.  Do

not loosen nut.  Apply sealant, as required, to area in accordance with applicable

manual.

SECTION III.  PYLON

5.	Inspect swashplate gimbal ring joint.

NOTE

DO NOT ATTEMPT TO TURN BOLTS.  BOLT MOVEMENT WILL FAIL LOCTITE BOND AND CAUSE BOLT WEAR.

5.1.	Grasp swashplate rotating ring (204-011-403) and attempt to move it in

a horizontal plane on an axis in line with gimbal ring attach points to

support assembly (204-011-404).  Maximum allowable axial looseness across

the gimbal ring bearings and attaching bolts is 0.010 inch.

5.2.	Repeat subparagraph 5.1., on axis 90 degrees to the check in

subparagraph 5.1., attempt to move it in a vertical plane to detect looseness

in line with gimbal ring attach points in inner ring (204-011-402).  Maximum

allowable axial looseness across the gimbal ring bearings and attaching bolts

is 0.010 inch.

5.3.	Inspect swashplate trunnion bearings for wear and security.  For

204-011-451 trunnion:  Disconnect scissors drive links from trunnion and

check swashplate bearing for roughness, binding and vertical play.  Rotate

and lubricate trunnion before reconnecting.

SECTION IV.  TRANSMISSION

6.	Inspect web above input quill for cracks.  Any indication of a crack is

cause for removal of case.

7.	Inspect internal filter and chip detector.  If metallic chips or particles      (

are found, investigate to determine cause.

8.	Inspect oil lines and hoses for pin holes or cracks due to chafing.

9.	Inspect oil line quick disconnect for leaks, wear and proper pin engagement.

10.	Inspect wire bundles and controls for chafing.

11.	Check oil sight gage for discoloration and contamination.

12.	Inspect transmission tail rotor drive quill coupling and main drive shaft

seals and surrounding area for evidence of grease leakage, visual overheat

indicator for discoloration and overheat condition.  A change in color of

indicator indicates a possible overheat and/or component degradation.  Cause of

discoloration shall be determined and corrected prior to flight.

13.	Remove and visually inspect generator drive quill magnetic chip plug for

contaminants.

14.	Visually inspect generator condition, (Spline wear and brush inspection is

performed during the Special Inspection, 7-9.  EACH 600 HOURS OR 12 MONTHS OF

COMPONENT OPERATION, WHICHEVER OCCURS FIRST: of the IPG).

15.	Perform an operational check of transmission chip detector system.

SECTION V.  FUSELAGE (PYLON AREA)

16.	Inspect fuselage pylon structure for cracks, distortion, missing rivets.

Inspect transmission support for cracks, distortion, defective/missing rivets.

Inspect lift beam assembly for cracks.

17.	Inspect friction dampers.  Move pylon fore and aft, using mast as lever.

Check friction dampers for freedom of movement and smooth operation.  Repair or

replace dampers found binding.

18.	Inspect isolation mounts, mount boots, mounting brackets and structure for

cracked or broken parts.

19.	Inspect fifth mount attachment for damage and security.  Inspect mount and

support beam for cracks.

20.	Inspect lift link, lift beam fitting and lower sump case attachment for

security and cracks.

NOTE

REFER TO PAGE 5, NOTE, FOR REPETITIVE LIFTS.

SECTION VI.  HYDRAULIC SYSTEM

21.	Inspect all lines, fittings and hoses for leakage and security, kinks,

general condition, and pitting.  Pay particular attention to the condition of the

hoses.

22.	Inspect hydraulic actuators for leakage and security.  Clean exposed area of

cylinder piston with hydraulic fluid and lint free cloth.

23.	Inspect actuator attachment brackets for security, cracks, and corrosion in

immediate area.

24.	Inspect pump for damage and leakage.

SECTION VII.  TAIL ROTOR/DRIVE SYSTEM

25.	Perform operational check of intermediate and tail rotor gearbox chip

detector system.

26.	Check torque of intermediate gearbox attachment bolts; and check torque of

tail rotor gearbox retaining nuts.  Do not loosen bolts/nuts.

27.	Inspect tail rotor pitch change mechanism as follows:

27.1.	Mount dial indicator on tail rotor gearbox output shaft with dial

indicator lever on outboard edge of crosshead adjacent to pitch link bolt.

27.2.	Apply and hold full left pedal.  Move crosshead in a radial (rocking

motion) and note amount of maximum radial movement.  Maximum movement should

not exceed 0.020 inch.

27.3.	Apply and hold full right pedal.  Perform check as stated in

subparagraph 27.2, above.  Maximum movement should not exceed 0.035 inch.

27.4.	If tolerances stated in subparagraphs 27.2 and 27.3 are exceeded,

inspect inner splines of tail rotor crosshead slider and mating splines on

tail rotor gearbox output shaft.

27.5.	Place control pedals in neutral position.  Move crosshead in axial

direction (in and out), being careful not to cause radial movement.  Maximum

movement should not exceed 0.018 inch.

27.6.	If tolerance in subparagraph 27.5 above, is exceeded, inspect crosshead

bearings, control quill bearings and acme thread of control tube and mating

threads in control nut.

CHAPTER 5

DETAIL #2 - 100 FLIGHT HOURS

__________________________________________________________________________________________

SECTION I.  GENERAL

1.	Perform a P.M.I.  See INSPECTION SCHEDULE CHART, PAGE 8.

SECTION II.  FORWARD FUSELAGE AREA

2.	Inspect landing gear for wear of skids and shoes, security of mountings for

skids and crosstubes.  Inspect skid tubes and crosstubes for cracks, distortion, or

yielding.

3.	Inspect fuselage exterior structure for cracks, dents, corrosion, defective

and missing rivets or screws.

SECTION III.  PILOT AND PASSENGER COMPARTMENTS

4.	Check all safety equipment for inspection due dates and operation.

5.	Inspect all heating and cooling ducts and controls for cracks, security, and

operation.

6.	Inspect cabin structure for cracks, loose rivets and other damage.

7.	Functionally check crew door mechanism and jettison mechanism, and inspect

for wear, corrosion and distortion.  Inspect hinges for cracks.

8.	Inspect seat adjustment mechanism and tracks for wear, positive locking and

lubrication.

9.	Functionally check cargo door window jettison mechanism.

10.	Inspect cargo door latching mechanism and door rollers for wear and damage.

11.	Drain pitot static system, if necessary.

SECTION IV.  LOWER PYLON, ENGINE and AFT/CENTRAL AREA

12.	Inspect lift beam and surrounding area for cracks and working rivets.

NOTE

SEE PAGE 5, NOTE, FOR REPETITIVE LIFTS.

13.	Inspect droop compensator shear pin.

14.	Inspect fuel cell X-connector, surrounding structure, and fuel lines for

condition.

15.	Check engine idle solenoid for operation, freedom of plunger, inspect for

corrosion and security.  Check for proper clearance.

16.	Inspect bleed air discharge line for chafing and blockage.

17.	Inspect voltage regulator for damage and security of mounting and terminals.

18.	Inspect relays and main bus area for security of mounting and connections.

SECTION V.  FLIGHT CONTROLS

19.	Inspect all control rods for clearance, security and general condition.

20.	Inspect tail rotor and synchronized elevator control tubes for wear.

21.	Check all controls for freedom of motion.

22.	Check collective stick for proper minimum friction.  Check shoes and liners

for excessive wear.

23.	Check collective sleeve mast friction collet for proper minimum friction

(540 M/R).

24.	Check swashplate uniball for proper minimum tilt friction (540 M/R).

SECTION VI.  TAIL ROTOR

25.	Dynamically track and balance.

CHAPTER 6

DETAIL #3 - 150 FLIGHT HOURS

__________________________________________________________________________________________

SECTION I. GENERAL

1.	Perform a P.M.I.  SEE INSPECTION SCHEDULE CHART, PAGE 8.

SECTION II.  MAIN ROTOR

2.	Check torque on the 8 bolts attaching stabilizer bar supports to trunnion.

SECTION III.  TAIL ROTOR

3.	Inspect tail rotor hub assembly for worn bearings.

4.	Clean tail rotor blades to maintain improved visibility.

5.	Clean and inspect tail rotor control chain and aft cables for wear,

corrosion, cracks, broken strands and proper tension.

SECTION IV.  TAIL ROTOR DRIVE SECTION

6.	Inspect intermediate and tail rotor gearbox sealants for condition and re-seal

as needed.

7.	Inspect both gearbox vents and filler cap packing for condition.

8.	Check condition of clamps for tail rotor shaft coupling to gearbox couplings.

Inspect clamps for evidence of cracks in or near the bolt hole lugs.

9.	Externally examine shaft hanger bearings and shaft couplings for evidence of

grease leakage, overtemperature condition, and excessive play and/or movement.

SECTION V.  TRANSMISSION                                                             (

10.	Remove and inspect the external oil filter (paper filter) for metal chips or   (

particles, investigate to determine cause if metal chips are found, and replace      (

with new filter element.                                                             (

SECTION VI.  TAIL BOOM

11.	Inspect internal and external structure of tail boom for cracks, distortion,

corrosion and security.

12.	Visually inspect all tail boom attachment fittings for cracks and security

as follows:

NOTE

ANY CRACK, CORROSION, OR BOND SEPARATION IS CAUSE FOR IMMEDIATE GROUNDING OF AN

AIRCRAFT UNTIL THE PROBLEM HAS BEEN ELIMINATED.

12.1.	Using a bright light and mirror, inspect visible portions of

attachment fittings for cracks.  Special attention must be given to upper

left attachment fitting, particularly in area of most forward rivets.

Inspect longeron, left and right sides, from attachment fittings to next aft bulkhead for any evidence of corrosion.

12.2.	Remove access panels on lower skin of tail boom to expose lower

attachment fittings.  Using a bright light and mirror, inspect visible

portions of attachment fittings for any indications of cracking, particularly

in area of most forward rivets.  Inspect longeron left and right sides, from

attachment fittings to the next aft bulkhead, for any evidence of corrosion.

12.3.	Remove access plugs at bore for barrel nuts and visually inspect

tail boom attachment fittings.  Check torque of tail boom attachment bolts.

DO NOT BACK OFF NUTS.  Be sure that no less than one, nor more than three

threads protrude through the barrel nut.

12.4.	Open access door on right side of fuselage and inspect the four tail

boom attachment fittings on fuselage aft bulkhead for cracks giving special

attention to the area around tail boom attachment bolts and most aft

fasteners.  Particular attention must be given to inspection of left hand

fittings.

13.	Inspect vertical fin rib along rivet row at fin station 10.08 for cracks,

(tail rotor 90 degree gearbox casting area accessed through topmost lightning

holes).

14.	Inspect vertical skin splice area at boom station 194.3, just forward of

intermediate gearbox, for cracks and corrosion.

15.	Inspect tail rotor gearbox support casting for cracks and corrosion.

16.	Inspect tail rotor and synchronized elevator push-pull tubes for chafing,

cracks and corrosion.

17.	Inspect tail rotor control cables and pulleys for wear, damage, chafing,

corrosion or fraying.

18.	Inspect elevator and horn assembly for security, condition, and corrosion.

SECTION VII.  ENGINE

NOTE

FOR ENGINES WITH PARTICLE SEPARATOR AND FOD SCREENS INSTALLED, PERFORM PARAGRAPH 18., BELOW.  IF THERE IS NO PARTICLE SEPARATOR OR SCREEN, PERFORM PARAGRAPH 19., BELOW.

19.	Remove particle separator.  Clean and inspect seals and gaskets for tears,

separations of material, cracks in the separator and other damage.

20.	Visually inspect compressor blades and inlet housing air passages and

variable guide vanes as required in the IPG, Chapter 3, P.M.I., Section VI.,

ENGINE, Paragraph 48.

21.	Inspect starter and mounts for security of mounting, burned or arced

connections, and cooling air ducts for obstructions, kinking and security.

(Spline wear and brush inspection is performed during Special Inspection,

22.	Inspect engine mounts for security, and tubes for scratches, dents, cracks,

and worn bearings.

23.	Inspect engine bleed air actuator strainer for condition and cleanliness.

Clean if required.  Inspect bleed band assembly for bends, cracks and security.

24.	Inspect air diffuser for security and damage:

24.1.	Inspect brazed joints including vanes brazements for cracks.  Inspect

brazed joints of air outlet pan (P3) fitting for cracks.  Inspect engine

mounts for security and cracks.  Refer to the manufacturer’s maintenance

manual for repair procedures.

25.	Functionally check anti-ice valve.

26.	Inspect and clean fuel control inlet strainer.

27.	Inspect and clean/replace fuel control servo strainer and replace paper

filter if installed.

28.	Replace main fuel filter element.

29.	Inspect and functionally test chip plug.

30.	Inspect and clean engine oil filter assembly.

31.	Inspect quick disconnects and breakaway fittings for security and wear.

32.	Inspect engine decks for damage and de-bonding.

33.	Inspect deck drain holes and channels for obstruction.

34.	Inspect N1 controls for wear and binding.  Verify fuel control lever contacts

stops with both pilot and co-pilot twist grips.  Check idle detent operation and

condition.

35.	Inspect N2 controls for wear and binding.  Verify pin condition.

Functionally test linear actuator for proper operation.

36.	Functionally test heater actuator valve.

37.	Inspect bleed air lines and fittings for wear and blockage.

38.	Inspect engine wiring harness for chafing, loose or corroded connections.

39.	Inspect ignition exciter and leads for damage, chafing, and security.

40.	Inspect oil lines and hoses for damage, chafing, leakage, and security.

41.	Inspect fuel lines and hoses for leakage, chafing and security.

42.	Inspect combustion chamber housing, support cone, fire shield, and exhaust

diffuser for cracks, hot spots, burned areas, and buckling.

43.	Through the aft end of the combustion housing, inspect for missing and cracked (

power turbine blades or cracks in the exhaust diffuser.

44.	Inspect the remainder of engine for condition.  Inspection shall include but

not be limited to items such as; corrosion of magnesium parts, fasteners not torqued properly, oil or fuel leaks found on accessories or their hoses.  All discrepancies shall be inspected to the limits found in the appropriate maintenance manual.

CHAPTER 7

SPECIAL INSPECTIONS

__________________________________________________________________________________________

In addition to the P.M.I. and the Detail #1, #2, and #3 Inspections, Special Inspections are performed on a calendar basis, a combination of hourly/calendar basis, or following the installation of major components such as the intermediate gearbox.

7-1.	AFTER EACH INSTALLATION

1.	Dynamic balance and track tail rotor hub and blade assembly.

2.	Perform an in flight track and balance of the main rotor assembly, if main rotor hub maintenance has been performed or the main rotor blades have been replaced.

7-2.	AFTER FIRST FLIGHT, AFTER EACH INSTALLATION

1.	Main drive shaft Bell Helicopter Textron (BHT Shaft) - Inspect drive shaft for

excessive grease leakage, security and condition.

2.	Tail Boom - Check torque of attachment bolts.  Do not loosen bolts.

3.	Scissors and sleeve collective mast friction collet (540 M/R) - Check friction

as outlined in applicable manual.

7-3.	BETWEEN 5 AND 10 HOURS, AFTER EACH INSTALLATION

1.	Main rotor hub - Check torque of hub retention nut.  Do not loosen nut.

2.	Tail rotor hub - Check torque of tail rotor retaining nut.  Do not loosen nut.

3.	Tail rotor control chain and/or sprocket.  Check control cable tension and

adjust as required.

4.	Intermediate gearbox - Check torque of gearbox attachment bolts.  Do not loosen bolts.

5.	Tail rotor gearbox - Check torque of gearbox retaining nuts.  Do not loosen nuts.

7-4.	EACH 25 HOURS OF OPERATION

1.	540 M/R main rotor hub - Inspect feathering bearings for squeaking, binding

and ratcheting while feathering grips to each limit of travel, with pitch change

links disconnected (one grip at a time).  Remove sand defector for a more detailed visual inspection of feathering bearings for deteriorated or loose Teflon lining.  Inspect Teflon trunnion bearings for squeaking, binding and ratcheting while flapping hub to each limit of travel.

WARNING:

DO NOT FLAP THE ROTOR HARD AGAINST THE MAST.

7-5.	EACH 100 HOURS OR 120 DAYS, WHICHEVER OCCURS FIRST

1.	Voltage regulator - Check voltage regulator setting.

7-6.	100 HOURS AFTER EACH INSTALLATION

1.	Tail boom - Check torque of attachment bolts.  Do not loosen bolts.

7-7.	300 HOURS OR 6 MONTHS OF BATTERY OPERATION

1.	Remove NICAD battery, check capacity and perform re-conditioning cycle, if necessary, in accordance with the battery manufacturer’s instructions.

7-8.	EACH 12 MONTHS MAGNETIC (MAG) COMPASS AND RADIO MAGNETIC INDICATOR (RMI)

CALIBRATION

1.	Verify calibration of MAG compass and the RMI.

2.	Correct as necessary and update calibration placards.

7-9.	EACH 600 HOURS OR 12 MONTHS OF COMPONENT OPERATION, WHICHEVER OCCURS FIRST:

1.	Battery overtemperature - Perform operational check of battery

temperature system (if installed).  (Refer to the manufacturers instructions).

2.	Emergency Locator Transmitter (ELT) -  Functionally check ELT

(if installed) and replace batteries if expired.

3.	Oil Cooler - Remove oil cooler screens and clean fan blades and assembly.

Check bearings for roughness and binding.  Inspect cooler for obstructions and

leaks.

4.	Main Drive Shaft (KAFLEX) - Remove drive shaft and inspect internal fail-

safe diameters for evidence of contact.  If contact is noticed, drive shaft

must be replaced.  Visually inspect drive shaft for obvious mechanical damage,

flexplate looseness, corrosion, and/or fretting at flex plate bolted joints.

4.1	Main Drive Shaft (BHT) - Remove drive shaft and clean, inspect,

lubricate and reassemble in accordance with applicable TM.

5.	Starter/Main Generator - Remove starter generator and; inspect accessory

gearbox generator drive splines for wear and lubricate, inspect the starter

generator splines for wear and lubricate, and inspect the starter generator brushes

for wear.

6.	Lead Acid Battery - Check for proper fluid level and condition in

accordance with battery instruction manual.

7.	Drain transmission and transmission oil cooler.  Inspect and clean

transmission oil pump screen.  Inspect and functionally check chip plug. Replace

external filter.  Service transmission with oil.

8.	Drain engine oil and engine oil cooler.  Inspect and functionally check

chip plug.  Replace external filter.  Service engine with oil.

9.	Drain intermediate gearbox oil.  Inspect and functionally check chip plug.

Service gearbox with oil.

10.	Drain tailrotor gearbox oil.  Inspect and functionally check chip plug.

Service gearbox with oil.

11.	Replace hydraulic filter element(s).

12.	Remove and inspect all tail rotor flex couplings for cracks and condition of internal splines and couplings. (

7-10.	EACH 24 MONTHS OF COMPONENT OPERATION

1.	Perform functional check of the Pitot Static System.

2.	Main rotor yoke - Remove, dissemble and inspect main rotor hub as follows: Remove bearing races, spacers, and radius rings from yoke spindles.  Inspect yoke spindle for cracks and corrosion pits, paying particular attention to the inboard radius of the spindle.  Inspect yoke center section for cracks, paying particular attention to areas surrounding the pillow block bushing bores.  Any crack is cause for rejection of the yoke.  Clean up any corrosion.  Replace tension torsion straps if calendar life is expired.  Reassemble hub using new pillow block attaching hardware.

3.	Main rotor mast - Inspect inside and outside diameters of mast for corrosion

and mechanical damage.

4.	Airframe - The operator will perform a thorough and searching airframe

inspection to find and preclude airframe deterioration.  This inspection will

provide the operator with a structural evaluation to determine if the airframe has

aged to a point that major refurbishment is necessary.  Using the applicable model

TM for damage and repair limits, accomplish the following:

4.1.	Inspect forward and aft upper and lower cargo door tracks for wear and

cracking.

4.2.	Inspect cargo door rollers and guides for wear.

4.3.	Inspect cabin door post(s) vertical angles for cracks.

4.4.	Inspect following honeycomb panels for delamination, voids, surface

damage (dents, punctures) and corrosion:

a.	Forward fuselage, main beams under cabin floor.

b.	L/H and R/H pylon island panels.

c.	Aft cabin bulkhead panels.

d.	Transmission and engine work/service deck panels.

e.	Roof deck panels.

f.	L/H and R/H aft outboard fuel cell bulkheads.

g.	L/H and R/H lower outboard fuel cell panels.

h.	L/H and R/H aft main beam panels (viewed through fuselage

compartment doors).

i.	Forward main fuel cell panel and aft center fuselage panel

(viewed in hell hole area).

5.	Inspect following areas for cracks, corrosion, and loose or working rivets.

a.	Pylon lift bean webs and lift link fitting.

b.	Pylon structure.

c.	Aft fuselage lower skin.

d.	Aft fuselage tail boom attachment fittings and longerons.

e.	Tail boom and vertical fin interior and exterior skin, fuselage

attachment fittings and longerons.

f.	Intermediate and tail rotor gearbox castings.

6.	Inspect electrical wire bundles in main fuselage and tail boom for oil and

hydraulic fluid soaked insulation, discolored wire indicating overheating,

cracked or broken insulation.

CHAPTER 8

CONDITIONAL INSPECTIONS (AIRFRAME)

__________________________________________________________________________________________

Conditional Inspections found in Chapter 8 are inspections required as a result of unusual events such as a hard landing or sudden stoppage of rotor.

8-1.	HARD LANDING - Hard landing is defined as any accident or incident in which ground impact of the helicopter causes severe pitching of main rotor, allowing hard contact of hub with mast, or results in yielding or cracking the mounting lugs of the transmission support case or noticeable yielding or cracking of fuselage pylon support structure or landing gear.  This definition is confined only to those accidents or incidents not involving sudden stoppage of main rotor or tail rotor.

NOTE

COMPONENTS REMOVED FROM A HELICOPTER FOLLOWING A HARD LANDING SHALL BE EVALUATED AS AN INTERRELATED GROUP.  REMOVAL RECORDS ACCOMPANYING EACH COMPONENT SHALL CROSS REFERENCE PART AND SERIAL NUMBERS OF OTHER DRIVE SYSTEM COMPONENTS REMOVED FOR EVALUATION.

If a hard landing is suspected, the following Paragraphs 1 through 6 below, shall be accomplished.

1.	Inspect main and tail rotor blades for evidence of strike damage.  If

such evidence is found on either rotor, perform  8-2. SUDDEN STOPPAGE - POWER

ON OR OFF INSPECTION, of the IPG.

2.	Visually inspect underside of fuselage and tail boom for evidence of

ground contact.

3.	Perform landing gear deflection check.

3.1.	If crosstubes have yielded, remove landing gear and inspect support and

structure to which they are attached for signs of yielding or other damage.

3.2.	If supports and attaching structure are not damaged, replace damaged

landing gear components.

4.	Inspect mast for deformation due to rotor hub contact.

4.1.	Inspect area around lower supports of pylon dampers for loose rivets or

other damage.

5.	If no damage other than yielded landing gear crosstubes has been found at this point it can reasonably be determined that a true hard landing did not occur.  Complete a P.M.I. and return helicopter to flight status provided no further evidence of damage is found.

6.	If damage is more extensive than landing gear crosstube yielding, a hard landing has occurred, the following Paragraphs 7 through 21 below, shall be accomplished:

7.	Remove and perform an overhaul evaluation inspection of the following

components.

a.	Mast assembly.

NOTE

IF THERE IS ANY DEFORMATION IN AREA CONTACTED BY MAIN ROTOR HUB, OR ANY OTHER OBVIOUS DAMAGE, THE MAST IS NOT AIRWORTHY AND IS UNSERVICEABLE.

b.	Transmission.

c.	Main input drive shaft.  (Grease lubricated type.)

8.	Perform a thorough visual inspection of the following components, which

may be kept in service if no discrepancy or obvious damage is found.  Replace

any damaged component.

a.	Main rotor blades.

b.	Main rotor hub.

c.	Tail rotor blades.

d.	Tail rotor hub.

e.	Anti-torque controls.

f.	Intermediate gearbox.

g.	Tail rotor gearbox.

h.	Tail rotor drive shafts.

i.	Tail rotor drive shaft hangers.

j.	Swashplate and support assembly.

k.	Scissors and sleeve assembly.

l.	Stabilizer bar assembly.

m.	Main rotor controls.

n.	Visually inspect KAFLEX drive shaft for the following

conditions:

(1)	Bolt contact with adjacent plate(s).

(2)	Plate contact with end fitting(s).

(3)	Interconnect contact with end fitting(s).

(4)	Contact of fail-safe surface(s).

NOTE

IF ANY OF THE CONDITIONS DESCRIBED IN SUBPARAGRAPHS n., (1) THROUGH (4) ABOVE ARE FOUND, REPLACE KAFLEX SHAFT.

9.	Check all cowling and doors for proper fit and alignment.  Remove

cowling and inspect all attachment fittings.

NOTE

IF SIGNIFICANT DAMAGE HAS BEEN FOUND IN ANY AREA OF THE AIRFRAME, INSPECTION SHALL BE EXPANDED BEYOND THE ZONE OF DAMAGE.

10.	Using 10-power magnifying glass make a complete inspection of pylon support structure for loose or sheared rivets, cracked brackets, buckled or cracked support angles or webs.  Pay particular attention to pylon mounts attaching points and damper support attaching points.

11.	Remove lift link and make a complete inspection of lift link, lift link

attachment fittings and lift beam for cracks and other evidence of damage.  If

lift link is damaged it is not airworthy and is unserviceable.

12.	Remove both pylon dampers, disassemble and check for internal yielding.

Reassemble and reinstall if no evidence of damage.  If pylon dampers have

yielded they are not airworthy and are unserviceable.

13.	Install serviceable mast, transmission assembly and main drive shaft

assembly.  Re-install removed pylon control components.

14.	Check all engine mount fittings and bolts for damage and looseness.

15.	Inspect engine firewalls for evidence of warping, crushing, or other damage.

16.	Make a complete inspection of area where tail boom is attached to

forward fuselage section.  This includes both sets of attachment fittings and

the longerons, beam caps, skins, webs, bulkhead flanges and other structural

members.  Check torque on attachment bolts to determine if yielding has occurred.

17.	Completely inspect flight control system from pilots controls to rotor

head for bent or damaged tubes, bellcranks, bellcrank supports and for damage to

control system bearings.  Particular attention shall be given to pylon controls,

lower cylinder attachment support fitting and adjacent airframe structure.

18.	Pressurize hydraulic system and check for leaks, interference, binding

and for satisfactory operation.

19.	Inspect fuel, oil and pneumatic system for damage, perform engine ground

run and visually check fuel, oil and pneumatic lines for leaks.

20.	Inspect wire strike protection system (WSPS) as follows:

20.1.	Inspect lower assembly for obvious damage to WSPS and attachment

area for damage.

20.2.	Inspect windshield deflector and upper WSPS assembly for obvious damage

to WSPS and attachment area for damage.

21.	Inspect power plant in accordance with engine manufacturer’s inspection

guide.

NOTE

IF NO SIGNIFICANT DAMAGE HAS BEEN FOUND, NO FURTHER INSPECTION IS NECESSARY.

8-2.	SUDDEN STOPPAGE - POWER ON OR OFF.  Sudden stoppage is defined as any rapid

deceleration of the drive system whether caused by seizure within the helicopter

transmission or by contact of the main or tail rotor blades with the ground, water,

snow, dense vegetation or other object of sufficient inertia to cause rapid

deceleration.  Main or tail rotor blade damage, when caused by striking some object

sufficient to require blade replacement, is considered sudden stoppage.  When

sudden stoppage occurs, inspect helicopter and replace components as follows:

NOTE

COMPONENTS REMOVED FROM A HELICOPTER, FOLLOWING A SUDDEN STOPPAGE, SHALL BE EVALUATED AS AN INTERRELATED GROUP.  REMOVAL RECORDS ACCOMPANYING EACH COMPONENT SHALL CROSS REFERENCE PART AND SERIAL NUMBERS OF OTHER DRIVE SYSTEM COMPONENTS REMOVED FOR EVALUATION.

Perform a sudden stoppage inspection as follows:

NOTE

IF SUDDEN STOPPAGE INSPECTION IS THE RESULT OF A TAIL ROTOR STRIKE, COMPLY WITH

8-2. SUDDEN STOPPAGE - POWER ON OR OFF, PARAGRAPHS 7. through 12., BELOW.

1.	Main rotor blades.

1.1.	Visually inspect both main rotor blades for evidence of damage.  Check closely

for wrinkled skin.

1.2.	If either blade is damaged sufficiently to require blade replacement, return

both blades to an authorized overhaul facility.  Make an entry in component record to

show that reason for removal was Sudden Stoppage.

1.3.	If no evidence of damage is found on either blade, both blades

may be returned to service.

2.	Main rotor hub.

2.1.	If main rotor blades were not damaged, the main rotor hub may be

returned to service.

2.2.	If main rotor blades were damaged sufficiently to require blade

replacement, perform an overhaul evaluation inspection on main rotor hub

assembly.  Make an entry in component records to show that reason for

removal was Sudden Stoppage

2.3.	If any main rotor blade is damaged beyond repair, grip is unserviceable

and not airworthy.  Perform overhaul evaluation inspection on main rotor hub.

Make an entry in component record to show that reason for removal was Sudden

Stoppage.

3.	Pylon control components.

3.1.	If one or more of the following discrepancies in subparagraphs a.

through e. below are found, the swashplate assembly, stabilizer bar

assembly, and scissors and sleeve assembly shall be removed and an

overhaul evaluation shall be performed.

a.	Severe main rotor blade damage.

b.	Pitch horn failure.

c.	Yielded stabilizer bar tube.

d.	Control tube buckled or broken.

e.	Transmission main support case mounting leg broken.

3.2.	Using a ten-power magnifying glass, make a complete inspection of

pylon support structure for loose or sheared rivets, cracked support

angles and webs.  Pay particular attention to pylon mounts attaching

points and damper support attach points.

3.3.	If no condition exists as listed in preceding subparagraph 3.2., above,

perform a close visual inspection and if no evidence of damage is found,

the swashplate assembly, stabilizer assembly, and scissors and sleeve

assembly may be returned to service.

4.	Replace all bolts in rotating controls.  Discard removed bolts.

5.	Remove and inspect main drive shaft visually.  If evidence of yielding or

deformation is noted, scrap the drive shaft assembly.  If no visual evidence of

damage is detected, perform an overhaul evaluation.  Make an entry in

component record to show that the reason for removal is Sudden Stoppage.

OR	Visually inspect KAFLEX drive shaft for the following conditions:

a.	Bolt contact with adjacent plate(s).

b.	Plate contact with end fitting(s).

c.	Interconnect contact with end fitting(s).

d.	Contact of fail-safe surface(s).

NOTE

IF ANY ONE OF THE ABOVE CONDITIONS IN PARAGRAPH 5, a. THROUGH d., ARE FOUND, REPLACE SHAFT.  RETURN SHAFT TO SERVICE IF NO DAMAGE IS FOUND.

6.	Transmission and mast assembly.

6.1.	If mast has evidence of torsional yielding, the mast and

transmission shall be considered unserviceable and scrapped.

6.2.	If mast does not have torsional yielding and transmission has

no obvious damage that would render it unserviceable, then transmission

and mast shall have an overhaul evaluation performed.  Make an entry in

component record to show that the reason for removal was Sudden Stoppage.

7.	Tail rotor drive shaft hangers.

7.1.	If a tail rotor drive shaft section has been damaged by main rotor

strike or other circumstances, the hangers to which the damaged section

was attached shall be considered unserviceable and not airworthy.  If a tail

rotor drive shaft fails as a result of torsional load then all hangers and

sections shall be considered unserviceable and not airworthy.  Make a

complete inspection of area where tail boom is attached to forward fuselage

section.  	This includes all attachment fittings and the longerons, beam caps,

skins, webs, bulkhead flanges and other structural members.  Check torque on

attachment bolts to determine if yielding has occurred.

7.2.	If no damage is found in the preceding subparagraph 7.1, overhaul the

bearings in accordance with the applicable maintenance manual.  Make an entry

in component record to show that the reason for removal was Sudden Stoppage.

8.	Tail rotor drive shaft.

8.1.	Remove all tail rotor drive shaft sections and inspect for the following

conditions listed below.  If one or more conditions listed in subparagraphs

a., 	through e., below, are noted, all drive shaft sections and bearing

hangers shall be considered unserviceable and not airworthy.  Make a complete

inspection of area where tail boom is attached to forward fuselage section.

This includes both sets of attachment fittings and the longerons, beam caps,

skins, webs, bulkhead flanges and other structural members.  Check torque on

attachment bolts to determine if yielding has occurred.

a.	Curvic faces distorted.

b.	Evidence of overload.

c.	Cracks.

d.	Loose or sheared rivets.

e.	Scratches in excess of limits. (Refer to applicable Model TM.)

8.2.	If inspection reveals no condition as listed in subparagraphs 8.1.,a.

through e., above exists, then perform an inspection in accordance with

applicable TM.  Make an entry in component record to show that the reason for

removal was Sudden Stoppage.

9.	Tail rotor hub and blade assembly.

9.1.	If sudden stoppage originated at tail rotor blades, the tail rotor hub

and blade assembly shall be considered unserviceable and not airworthy.

9.2.	If sudden stoppage originated at main rotor or transmission, the tail

rotor hub and blade assembly may remain in service provided there is no

visible external damage.  If visible damage is noted on tail rotor hub and

blade assembly; remove tail rotor hub and blade assembly and perform overhaul

evaluation inspection.  Make an entry in component records to show that the

reason for removal was Sudden Stoppage.  The tail rotor grips and blade

attachment bolts must be considered unserviceable and not airworthy.

9.3.	If sudden stoppage originated at tail rotor drive shaft, intermediate

gearbox or tail rotor gearbox, remove tail rotor hub and blade assembly and

perform overhaul evaluation inspection.  Make an entry in component record to

show that the reason for removal was Sudden Stoppage.

10.	Tail rotor gearbox.

10.1.	Remove tail rotor gearbox.  Check for cracks, sheared or bent attaching

studs and evidence of case distortion.  If any of the listed is noted, then

the gearbox is not airworthy and is unserviceable.

10.2.	If no damage is found in the preceding subparagraph 10.1., above,

overhaul the gearbox in accordance with the applicable overhaul manual.

Make an entry in component record to show that the reason for removal was

Sudden Stoppage.

11.	Intermediate gearbox.

11.1.	Remove intermediate gearbox.  Inspect for cracks, case distortion or

broken lugs.  If any of the above is noted then the gearbox is not airworthy

and is unserviceable.

11.2.	If no damage is found in the preceding subparagraph 11.1., overhaul the

gearbox in accordance with the applicable overhaul manual.  Make an entry

in component record to show that the reason for removal was Sudden Stoppage.

NOTE

IF NO EVIDENCE OF DAMAGE WAS FOUND IN HEADING 8-2., PARAGRAPH 7. THROUGH 11., ABOVE, THEN OMIT HEADING 8-2., PARAGRAPH 12., BELOW.

12.	Transmission sump case.

12.1.	If damage was found on bearing hangers, tail rotor drive shaft,

intermediate gearbox or tail rotor gearbox, then remove tail rotor drive

output quill from transmission sump case assembly.

12.2.	Inspect output quill pinion for unusual load patterns on both

sides of teeth.  If no damage is found; reinstall quill, and transmission can

be returned to service.

12.3.	If tail rotor drive quill reveals discrepancies, remove transmission

and perform an overhaul evaluation.  Make an entry in component record to

show reason for removal was Sudden Stoppage.

8-3.	OVERSPEED - Overspeed is defined as any incident in which 356 main rotor rpm and/or engine overspeed limits in engine manufacturer’s manual are exceeded.  Perform overspeed inspection as follows:

NOTE

COMPONENTS REMOVED FROM HELICOPTER, FOLLOWING AN OVERSPEED, SHALL BE EVALUATED AS AN INTERRELATED GROUP.  REMOVAL RECORDS ACCOMPANYING EACH COMPONENT SHALL CROSS REFERENCE PART AND SERIAL NUMBERS OF OTHER DRIVE SYSTEM COMPONENTS REMOVED FOR EVALUATION.

NOTE

REFER TO ENGINE MANUFACTURER’S INSPECTION GUIDE FOR ENGINE OVERSPEED AND INSPECTION REQUIREMENTS.

1.	Main rotor hub assembly.

1.1.	Remove main rotor hub.  Remove main rotor blades.  Perform an overhaul

evaluation inspection.  Make an entry in component record to show that the

reason for removal was Overspeed.

1.2.	Visually inspect main retention bolts and drag brace for shear offset.

2.	Main rotor blades.

2.1.	Inspect main rotor blade for wrinkles and deformation.

2.2.	Remove each rotor blade tip cap and inspect for evidence of looseness

of inertia weight inside blade spar.  If blades have visible screws through

the leading edge abrasion strip to attach inertia weight inside spar, inspect

for loose screws or distorted holes.  Tighten loose balance weight retention

nuts to torque specified in applicable main rotor blade TM or DMWR.

2.3.	If no discrepancies are found in inspections outlined in subparagraphs

2.1 and 2.2., above, the main rotor can be returned to service.

2.4	If discrepancies are found in subparagraphs 2.1 and/or 2.2 above,

return both blades to an authorized blade repair station.  Make an entry in

component record to show that the reason for removal was Overspeed.  Indicate

RPM and duration if known.

3.	Tail rotor hub and blades.

3.1.	Remove tail rotor hub and blade assembly.

3.2.	Remove tail rotor blades.

3.3.	Replace tail rotor blade retention bolts.

4.	Tail rotor blades.

4.1.	Check for bond separations anywhere on the blade.  If any separation

exists, the blade is unserviceable and not airworthy.

4.2.	If any movement of the tip or root and balance weights has occurred,

the blade is unserviceable and not airworthy.

4.3.	Check the retention bushings for evidence of looseness.  If any bushing

is loose, scrap the blade.

4.4.	If blades pass the above inspection requirements and no other

discrepancies exist, the blade can be returned to service.

5.	Perform a close inspection of the following components.  If no visual damage

is found, the component may be returned to service.

a.	Main transmission.

b.	Intermediate gearbox.

c.	Tail rotor gearbox.

d.	Main rotor mast.

e.	Main input drive shaft.

f.	Tail rotor drive shaft hangers.

g.	Stabilizer bar.

h.	Swashplate.

i.	Scissors and sleeve.

j.	Tail rotor hub.

k.	Tail rotor drive shaft (204-040-620-11).

NOTE

REMOVE AND CONDEMN ONLY THE 204-040-620-3 OR -7 LONG TAIL ROTOR DRIVE SHAFTS.

6.	Install a serviceable main rotor hub and blade assembly.  Install serviceable

tail rotor blades.  Balance and install tail rotor hub and blade assembly.

8-4.	OVERTORQUE (AIRFRAME/ENGINE) - Overtorque is defined as any incident in which torsional loads are introduced into the helicopter dynamic system in excess of

established limits.

NOTE

COMPONENTS REMOVED FROM HELICOPTER, FOLLOWING ANY OVERTORQUE, SHALL BE EVALUATED AS AN INTERRELATED GROUP.  REMOVAL RECORDS ACCOMPANYING EACH COMPONENT SHALL CROSS REFERENCE PART AND SERIAL NUMBERS OF OTHER DRIVE SYSTEM COMPONENT REMOVED FOR EVALUATION AND SHALL REFLECT OVERTORQUE AS REASON FOR REMOVAL.

1.	When overtorque has not exceeded 56 PSI perform thorough visual inspection of the

following components.  If inspection does not reveal any discrepancies or obvious damage to components, they may be retained in service.

a.	Main rotor blades.

b.	Tail rotor blades.

c.	Main rotor hub.

d.	Tail rotor hub.

e.	Intermediate gearbox.

f.	Tail rotor gearbox.

g.	Tail rotor drive shafts.

h.	Tail rotor drive shaft hangers.

i.	Stabilizer bar assembly.

j.	Swashplate.

k.	Scissors and sleeve assembly.

l.	Main drive shaft (BHT) as per TM.

m.	KAFLEX drive shaft, visually inspect for the following conditions:

(1)	Bolt contact with adjacent plate(s).

(2)	Plate contact with end fitting(s).

(3)	Interconnect contact with end fitting(s).

(4)	Contact of fail-safe surface(s).

NOTE

IF DISCREPANCIES ARE FOUND IN 1. m., (1) THROUGH (4) ABOVE, REPLACE SHAFT.

n.	Mast.

o.	Transmission.

2.	When overtorque exceeds 56 PSI but does not exceed 61 PSI:

2.1.	Perform thorough visual inspection of components listed in

Paragraph 1. ,subparagraphs a. through m., above.

2.2.	Inspect main transmission chip detector.

2.3.	Inspect main transmission internal filter and pump inlet screen.

2.4.	If metal particles indicating internal failure are found, remove the

transmission for overhaul evaluation.  Make entry in component record that

reason for removal was overtorque.  Remove all transmission system oil lines

and oil cooler.  Replace external oil filter element.  Flush and reinstall

lines.  Install new oil cooler.  Tag old cooler, “metal particle

contaminated”, and return to overhaul facility.

2.5.	If chip detector, internal filter and pump inlet screen appear normal,

and there is no evidence of internal failure, operate the transmission for

five hours, then check chip detector, internal filter and pump inlet screen.

If chip detector, filter and screen inspection does not reveal particles, the

transmission is satisfactory for service.  If metal particles  are found or

if there is an evidence of internal failure, remove the transmission for

overhaul evaluation.  Clean oil lines, replace oil cooler, replace external

oil filter element and make record entries as prescribed in preceding

subparagraph 2.4.

2.6.	Replace main rotor hub pillow block bolts.

2.7.	Replace main rotor trunnion cap bolts (540 M/R).

2.8.	Remove fifth mount bolts, remove fifth mount.  Perform a thorough

inspection of bolts and fifth mount support.  Check for bent bolts and bent

fifth mount support.  Check for proper bolt hole alignment between

transmission and fifth mount support.  Install fifth mount.

3.	When overtorque has exceeded 61 PSI:

3.1.	Remove and condemn 204-040-620-3 or -7 long tail rotor drive shaft.

3.2.	Return following components to an overhaul facility for overhaul

evaluation:

a.	transmission,

b.	main drive shaft (BHT and KAFLEX),

c.	main rotor hub, and

d.	mast.

3.3.	Perform thorough visual inspection of components listed in Paragraph 1.,

of Heading 8-4., page 39.

3.4.	Remove fifth mount bolts, remove fifth mount.  Perform a thorough

inspection of bolts and fifth mount support.  Check for bent bolts and

bent fifth mount support.  Check for proper bolt hole alignment between

transmission and fifth mount support.  Install fifth mount.

  - Install serviceable components.

T53L13B/703 ENGINES - OVERTORQUE LIMITS

OUTPUT SHAFT TORQUE SHALL NOT EXCEED THE FOLLOWING VALUES:

MILITARY (30 MINUTES) - 64 PSI (114%)

NORMAL   (CONTINUOUS) - 60 PSI (107%)

T53L11 SERIES ENGINES - OVERTORQUE LIMITS

OUTPUT SHAFT TORQUE SHALL NOT EXCEED THE FOLLOWING VALUES:

TAKEOFF  (5 MINUTES)  - 50 PSI (926 foot pounds)

MILITARY (30 MINUTES) - 48 PSI (888 foot pounds)

NORMAL   (CONTINUOUS) - 46 PSI (850 foot pounds)

4.	When an ENGINE has been subjected to an overtorque condition exceeding

the preceding limits, perform the following:

4.1.	Check chip detector for metal chips.

4.2.	Check oil filter for metal chips or other foreign matter.

4.3.	If slight accumulation of foreign matter is observed, clean chip

detector and oil filter; operate engine for 10 minutes; then repeat

subparagraphs 4.1. and 4.2., above.

4.4.	If excessive accumulation of metal or foreign matter is observed,

accomplish the following:

a.	Perform an oil contamination inspection.

(Ref. 72-00-00, ENGINE - TROUBLESHOOTING, Para. 1.C.)

b.	Inspect output reduction carrier and gear assembly.

4.5.	Repeat subparagraph 4.3., above, increasing engine operating time to 30

minutes.

4.6.	Perform flight test and repeat subparagraphs 4.1 and 4.2 above.  If no

excessive accumulation of metal or foreign matter is noted, engine may be

released for normal operation.

8-5.	LIGHTNING STRIKES - When the helicopter is suspected of receiving a lightning strike, the following inspections shall be performed.

NOTE

COMPONENTS REMOVED FROM A HELICOPTER, FOLLOWING A LIGHTNING STRIKE, SHALL BE EVALUATED AS AN INTERRELATED GROUP.  REMOVAL RECORDS ACCOMPANYING EACH COMPONENT SHALL CROSS REFERENCE PART AND SERIAL NUMBERS OF OTHER DRIVE SYSTEM COMPONENTS REMOVED FOR EVALUATION.

1.	Visually inspect all external surfaces of the helicopter with particular attention to main rotor blades and the hub, the transmission and mast assembly, tail rotor blades and hub, tail rotor gearbox, and vertical fin.  Check electrical instruments and systems.  Replace defective and/or damaged parts.

2.	If visual indications of damage are present, proceed as follows:

2.1.	Inspect main rotor blades.  If blades show any sign of burns (burn

marks can be very minute) or de-bond in any bonded areas, scrap blades.

2.2.	Inspect main rotor hub for indication of arcing or burning.  Remove

main rotor hub and return to overhaul facility.  State lightning strike

as reason for removal.

2.3.	Remove transmission and mast assembly and return to overhaul facility.

State lightning strike as the reason for removal.

2.4.	Inspect tail rotor blades and hub, scrap blades if indications of

burns or de-bonding are found.  Remove tail rotor hub and return to

overhaul facility.  State lightning strike as the reason for removal.

2.5.	Remove gearboxes and return to overhaul facility.  State lightning

strike as the reason for removal.

2.6.	Inspect vertical fin for indication of electrical arcing burns around

mounting point of intermediate and tail rotor gearboxes.

3.	If no visual indications or damage is found, remove main rotor hub grips and:

3.1.	Visually inspect bearings for signs of electrical arcing or burning.

3.2.	Check bearing for smooth rotation.

3.3.	If indications of electrical arcing or burning are present or rough

bearings, overhaul main rotor hub.

NOTE

IF NO INDICATIONS ARE FOUND, REASSEMBLE MAIN ROTOR HUB.

3.2.	Remove main rotor mast assembly and visually inspect balls in the upper

mast bearing for signs of electrical arcing or burning.  Rotate bearing

during inspection so that all the surface of each ball may be observed.

Check bearing for smooth rotation.  Visually inspect the lower bearing race

on the mast, and driving spline on the mast for signs of electrical arcing or

burning.

a.	If indications of electrical arcing or burning are present, remove

transmission and mast assembly and return to overhaul facility.  State

lightning strike as reason for removal.

b.	If no indications are found, reassemble transmission and mast

assembly and return to service.  After five hours, remove chip

detectors and oil filter and inspect for chips.  If no indications are

found, return transmission to service.  If indications are found,

remove transmission and mast assembly and return to overhaul facility.

State lightning strike as the reason for removal.

3.3.	Remove output quill assembly from tail rotor gearbox.  Visually inspect

gear teeth for signs of electrical arcing or burning.  Rotate tail rotor mast

to check for smooth rotation of bearings.

a.	If evidence of electrical arcing or burning is found or if bearings

do not rotate smoothly, remove gearbox and return to overhaul

facility.  State lightning strike as the reason for removal.

b.	If no indications of damage are found, and if bearings rotate

smoothly, reassemble tail rotor gearbox and return to limited service

as defined below:

(1)	After five hours, remove chip detector and inspect for chips.

(2)	If no indications are found, return tail rotor gearbox to

service.

(3)	If indications are found, return tail rotor gearbox to

overhaul facility.  State lightning strike as the reason for

removal.

(4)	Remove output quill assembly from intermediate gearbox.

Visually inspect gear teeth for signs of electrical arcing or

burning.  Rotate quills to check for smooth rotation of bearings.

(a)	If evidence of arcing or burning is found or if

bearings do not rotate smoothly, remove intermediate gearbox

and return to overhaul facility.  State lightning strike as

the reason for removal.

(b)	If no indications of damage are found, and if

bearings rotate smoothly, reassemble intermediate gearbox and

return to limited service as defined below:

1.	After five hours, remove chip detector and inspect

for chips.

2.	If no indications are found, return intermediate

gearbox to service.

3.	If indications are found, return intermediate gearbox

to overhaul facility.  State lightning strike as the reason

for removal.

8-6.	MAST BUMPING

1.	Visually inspect the mast area where the static stop would contact the mast.  If no surface deformation of the mast has occurred, the inspection is complete.

2.	If there is visual evidence of surface deformation of the mast due to

static stop contact, perform the following:

2.1.	Evaluate the condition of the mast per the damage limits. (Refer to

applicable TM.)

2.2.	Inspect and replace the following items if damage is found:

a.	Main rotor hub trunnion cap or pillow block attach bolts and drag

brace jam nuts and attach bolts for security.

b.	Flight control system for bent or damaged tubes and rod end

bearings.

c.	Structure at transmission mounting points.

d.	Lift link and structure for damage, security and distortion.

e.	Transmission sump oil filter, external oil filter, and chip

detector for metal particles.

f.	Main drive shaft.

g.	Tail rotor drive shafts and hanger assemblies for obvious damage.

h.	Main transmission output tail rotor drive quill.

i.	Top forward section of fuselage.

8-7.	AFTER WIRE STRIKE

1.	Lower Wire Strike Protection System (WSPS) Assembly.

1.1.	Inspect for obvious damage to WSPS.

1.2.	Inspect attachment area for damage.

2.	Windshield Deflector and Upper WSPS Assembly.

2.1.	Inspect for obvious damage to WSPS.

2.2.	Inspect attachment area for damage.

3.	Windshield Wiper Deflector (WWD).

3.1.	Inspect for obvious damage to WWD.

3.2.	Inspect attachment area for damage.

8-8.	AFTER LOWER WSPS GROUND CONTACT

1.	Inspect for obvious damage.

2.	Inspect attachment area for damage.

3.	Remove panel and inspect structure and directional control tubes and

bellcranks for damage.

4.	Replace breakaway tip assembly.

NOTE

LOSS OF BREAKAWAY TIP OR DAMAGE NOT AFFECTING STRUCTURAL INTEGRITY OF INSTALLATION ARE NOT CAUSES FOR GROUNDING OF AIRCRAFT.  HOWEVER, REPLACEMENT OF TIP AND DAMAGE REPAIR SHALL BE ACCOMPLISHED AS SOON AS PRACTICAL.

8-9.	AFTER AIRCRAFT IS FLOWN INTO AREA WITH BLOWING SAND AND/OR LOOSE GRASS ENVIRONMENT.

NOTE

IF FOD SCREEN AND SAND AND DUST SEPARATOR ARE INSTALLED, REMOVE UPPER HALVES TO ACCOMPLISH THIS INSPECTION.  IF BLOCKAGE IS EVIDENT, THE LOWER HALF OF THE SEPARATOR MUST BE REMOVED TO ENSURE COMPLETE REMOVAL OF GRASS OR FOREIGN MATERIAL.

NOTE

IF THE IMPROVED PARTICLE SEPARATOR (IPS) IS INSTALLED, REMOVE ANY FOREIGN OBJECTS FROM THE SCREEN OR SIDE OF VORTEX TUBE PANELS.  BLOWING SAND CAN PENETRATE THROUGH VORTEX TUBES AND IF ENGINE IS NOT RUNNING, WILL NOT BE SCAVENGED OVERBOARD.  IN THESE CIRCUMSTANCES SAND CAN SETTLE IN BOTTOM PLENUM OF IPS.  THE TOP OF IPS SHOULD BE REMOVED AND ALL SAND REMOVED FROM IPS BOTTOM HALF.

8-10.	AFTER WASHING HELICOPTER.

1.	Remove left and right pylon access doors.  Using a clean cloth, wipe water deposits from pylon structural members.  Reaching aft onto forward engine deck through rear pylon structures, wipe water from engine deck.

2.	Check pitot static system for moisture (drain plug removed).

3.	Purge lubricate tail rotor grip assemblies.

8-11.	AFTER HELICOPTER HAS BEEN SUBJECTED TO SALT WATER OR SALT WATER SPRAY.

1.	Wash entire helicopter with fresh water, particularly inside of engine

compartment doors.  Wash all compartments which were exposed to salt water.

Make a detail check of all surfaces for corrosion.  Apply corrosion preventive

compound to exposed non painted, anodized, or cadmium plated assemblies.

Clean engine compressor in accordance with applicable engine TM.

8-12.	HELICOPTERS OPERATED IN SALT LADEN ENVIRONMENT:

1.	Using a mild soap detergent, wash blades daily.  Rinse with clear water

and dry.  All aircraft down for maintenance or non-flyable storage are not

subject to blade wash inspection.

8-13.	AFTER HELICOPTER HAS BEEN PARKED OR OPERATED IN RAIN, ICE, OR SNOW.

1.	Purge lubricate tail rotor hub and blade grip bearings.

2.	Open engine inlet area and remove upper air filter assembly.  Inspect

and clean particle separator parts.

NOTE

INSPECTION DOES NOT APPLY TO HELICOPTERS WITH SELF-PURGE TYPE SEPARATORS.

NOTE

INSPECTION NOT REQUIRED IF HELICOPTER WAS PARKED WITH PROTECTIVE COVERS INSTALLED.

8-14.	AFTER OVERFLOW OF BATTERY AND/OR BATTERY SUMP JAR (IF SUMP JAR IS INSTALLED).

1.	Inspect sheet metal surfaces and overlaps, both internal and external, for damage.

2.	Inspect rivets, bolts, screws, and other hardware in area, internally and externally for damage.

3.	Inspect hidden areas in vicinity of battery and sump jar for damage.

4.	Inspect all metal parts throughout contaminated area for damage.

8-15.	TRANSMISSION OIL OVER TEMPERATURE.

1.	Troubleshoot transmission system to determine cause.

2.	Replace transmission, mast, oil cooler and external oil filter if cause is due to transmission internal failure.

3.	If cause is due to oil system external to transmission and oil temperature did not exceed 130 degrees C (266 degrees F) for 15 minutes, drain and refill transmission oil system.

4.	If temperature exceeded above limits, replace transmission and mast.  If abnormal contamination is present, also replace oil cooler and external filter.

8-16.	COMPLETE LOSS OF TRANSMISSION OIL.

1.	Troubleshoot transmission oil system to determine cause.

2.	If engine power was applied after complete loss of oil, replace transmission and mast.  If abnormal contamination is present, also replace oil cooler and external oil filter

3.	Inspect quick disconnects for engagement and wear.

CHAPTER 9

CONDITIONAL INSPECTIONS (ENGINE)

__________________________________________________________________________________________

Conditional Inspections (Engine) found in Chapter 9 of the IPG are inspections

required as a result of an unusual event such as engine oil filter bypass or engine over temperature.

NOTE

THERE ARE NO PRESCRIBED INTERVALS FOR CONDITIONAL INSPECTIONS.

9-1.	INSPECT FOR FOREIGN OBJECT DAMAGE (FOD).

1.	Open inlet guide vanes manually and conduct a visual inspection of the inlet housing (inlet guide vane and first stage compressor rotor through the inlet ducts).

2.	If damage exceeds limits or appears to extend beyond the first stage compressor rotor, remove the upper compressor housing half and inspect compressor

blades, vanes, centrifugal impellers, and compressor housings.

(Ref. 72-30-XX, of appropriate maintenance manuals).

If centrifugal compressor impeller is damaged beyond limits, return engine to

Overhaul.

3.	Inspect all visible air diffuser vanes for nicks, dents, and burrs.

Minor nicks, dents and burrs are acceptable provided that mutilation has not occurred as

defined by the appropriate manual.

9-2.	SUSPECTED COMPRESSOR STALL OR SURGE.

Engine compressor stall or surge is characterized by a sharp rumble or a series of

load sharp reports, severe engine vibration and a rapid rise in exhaust gas

temperature (EGT), depending on severity of surge.  When a surge has been reported,

progressively perform 9-2.  SUSPECTED COMPRESSOR STALL OR SURGE.,Paragraphs  1., 2., and 3. below, as indicated by discrepant conditions.

NOTE

STALL INSPECTION IS NOT REQUIRED FOR NOISE CAUSED BY BLEED BAND CYCLING OR SURGE BELOW 85 PERCENT N1 THAT IS NOT ACCOMPANIED BY A RAPID RISE IN EGT.

NOTE

COMPONENTS REMOVED FROM A HELICOPTER, FOLLOWING A COMPRESSOR STALL OR SURGE, SHALL BE EVALUATED AS AN INTERRELATED GROUP.  REMOVAL RECORDS ACCOMPANYING EACH COMPONENT SHALL CROSS REFERENCE PART AND SERIAL NUMBERS OF OTHER DRIVE SYSTEM COMPONENTS REMOVED FOR EVALUATION.

Discuss circumstances of reported compressor stall with pilot.  Determine N1 speed at which reported stall occurred.  Check helicopter and engine log for any pertinent history.

1.	Power plant.

1.1.	Examine inlet screen for blockage.

1.2.	Inspect the engine in accordance with engine manufacturer’s inspection

guide.

1.3.	If compressor is dirty, wash in accordance with approved engine

manufacturer’s method.

2.	Power train.

If compressor stall occurs below 85 percent N1 speed, comply with the following subparagraphs 2.1., through 2.3. below:

2.1.	Remove magnetic chip detectors from transmission, intermediate

gearbox and tail rotor gearbox, and inspect for metal particles.

2.2.	If no evidence of damage is found on tail boom vertical fin and no

indication of metal particles are found on chip detectors; clean chip

detectors and reinstall.  Return helicopter to flight status and repeat

chip detector inspection in 5 to 10 hours.  If positive indication of

damage is found on tail boom pylon or metal chips are found on chip

detectors on initial 5 to 10 hour inspection, comply with subparagraphs 2.4

through 2.7 below.

2.3.	Visually inspect main drive shaft.  Main BHT drive shaft, inspect for

internal and curvic coupling damage.  KAFLEX drive shaft, inspect for the

following conditions:

a.	Plate contact with end fitting(s).

b.	Interconnect contact with end fitting(s).

c.	Contact of fail-safe surface(s).

NOTE

IF ANY ONE OF THE ABOVE CONDITIONS ARE FOUND, REPLACE SHAFT.

RETURN SHAFT TO SERVICE IF NO DAMAGE IS FOUND.

If compressor stall occurs at 85 percent N1 or above, comply with the preceding Paragraph 2., (including subparagraphs 2.1, 2.2 and 2.3) and the following subparagraphs 2.4, through 2.7. and Paragraph 3.

2.4.	Remove and condemn 204-040-620-3 and -7 long tail rotor drive shaft.

2.5.	Remove tail rotor gearbox from helicopter and remove input quill.  With

a 10 power glass, inspect gear teeth on pinion and gear for damage.  If

no evidence of scoring or scuffing is found and there is no other damage that

would render gearbox unserviceable, it may be reassembled and reinstalled for

continued use.  If gear teeth are scored or scuffed or there is other damage

that would render gearbox unserviceable, replace gearbox.

2.6.	Remove input and output drive quill from intermediate gearbox and

inspect gear teeth on pinion and gear for damage with a 10 power glass.

If no evidence of scoring or scuffing is found and there is no

mechanical damage that would render gearbox unserviceable, reassemble

and return to service.  If gear teeth are scuffed or scored or gearbox

has sustained other damage; replace gearbox.

2.7.	Remove the tail rotor drive quill from the transmission and

inspect the gear teeth for damage with a 10 power glass.  If there is no

indication of scoring or scuffing and there is no other damage that

would render the transmission unserviceable, it is suitable for

continued use.  If gear teeth are scored or scuffed or there is other

damage that would render the transmission unserviceable, replace

transmission and comply with subparagraph 2.8., below.

2.8.	If transmission is replaced, the tail rotor hanger bearing assemblies

and tail rotor hub and blade assembly must also be replaced and procedures

outlined in subparagraphs a. through e. below, performed.

NOTE

PERFORM AN OVERHAUL EVALUATION ON TAIL ROTOR HUB AND BLADE.  MAKE AN ENTRY IN COMPONENT RECORD TO SHOW THAT THE REASON FOR REMOVAL WAS COMPRESSOR STALL.

a.	Remove inboard and outboard drag brace bolts.  Check bolts for

deformation, and perform a magnetic particle inspection.  If

satisfactory, return to service.

b.	Visually inspect stabilizer bar outer tubes for bending.

(Allowable deflection is 0.150 inch in each tube.)

c.	Remove main rotor pillow blocks from main rotor yoke and check

for deformation of bushing holes in pillow blocks and yoke.

Replace main rotor trunnion cap bolts (540 M/R).

d.	Perform close visual inspection of all main rotor components.

e.	If any discrepancies are noted as a result of inspection in

subparagraphs a. through d. above, remove and replace main rotor hub

and blade assembly, stabilizer bar assembly, and mast assembly.

Removed assemblies shall have an overhaul evaluation performed.  Make

an entry in component records to show that the reason for removal was

Compressor Stall.

3.	Airframe.

3.1.	Check tail boom vertical fin for evidence of damaged skin panels

and/or structure and rivets for looseness and/or sheared heads.  If

inspection shows no indications of damage, return helicopter to service.

If positive evidence of damage is found, comply with subparagraphs 3.2

through 3.4 below.

3.2.	Remove skin from tail boom vertical fin adjacent to tail rotor

gearbox mounting.  Inspect all support structures in this area and

repair as required.  Install new skin.

3.3.	Make close visual inspection of complete tail boom structure for

distortion, buckles, skin cracks and sheared or loose rivets, paying

particular attention to tail boom attachment points and adjacent fuselage to

tail boom structure and intermediate gearbox support structure.

3.4.	Make close visual inspection of main pylon support and engine

mount attachment structure for distortion buckles, cracks, sheared or

loose rivets, etc.

9-3.	ENGINE IS DROPPED DURING HANDLING.

CAUTION

IF ENGINE IS IN SHIPPING CONTAINER, INSPECT CONTAINER AND CONTAINER ENGINE MOUNTS

FOR DAMAGE.  IF EXTENSIVE DAMAGE TO SHIPPING CONTAINER OR SHIPPING CONTAINER ENGINE

MOUNTING SYSTEM IS FOUND, ENGINES MUST BE RETURNED TO OVERHAUL FOR INSPECTION OF ALL

MAIN BEARINGS

1.	Check accessory drive gearbox for cracked mount flanges or loose bolts.

2.	Check overspeed governor and tachometer drive for cracks, distortion,

and bent shafts.

3.	Check oil filter for loose bolts and damaged filter elements.

4.	Check power-driven rotary (oil) pump for loose bolts and cracked flanges.

5.	Check engine mounting pads for cracks.

6.	Check all hose connections for security.

7.	Check all accessories for loose bolts, nuts, connections, and cracked mount

flanges.

8.	Check inlet, compressor, and combustor housings for cracks or loose bolts.

9.	If no visual damage is apparent, accomplish the following inspections:

9.1.	Perform a complete engine ground operational test (with engine on

aircraft) and include vibration and coastdown checks.

NOTE

THE MINIMUM TEST TIME IS 30 MINUTES.  VIBRATION LEVELS MUST BE WITHIN ESTABLISHED

LIMITS.  IF NO DEFECTS ARE NOTED, ENGINE IS CONSIDERED SERVICEABLE. (REF. 71-00-00,

PARA. 12.E.)

9.2.	Perform inspection of oil filter, screens, and chip detector for chips,

lint, or other foreign material.

NOTE

IN THE EVENT THE SEVERITY OF DROP IS SUCH THAT ITEMS AS CALLED OUT IN HEADING 9-3.

ENGINE IS DROPPED DURING HANDLING., PARAGRAPHS 1. THROUGH 8., ABOVE ARE DISCREPANT,

IT IS RECOMMENDED THAT ENGINE BE RETURNED TO A DESIGNATED OVERHAUL FACILITY FOR

FURTHER CORRECTIVE ACTION.

9-4.	ENGINE SUDDEN STOPPAGE.

CAUTION

THE FOLLOWING ENGINE INSPECTION MUST BE COMPLETED IN THE EVENT OF AIRCRAFT DRIVE

SYSTEM STOPPING, EVEN MOMENTARILY.  SUDDEN STOPPAGE IS INTERPRETED TO INCLUDE THE

SHOCK FELT BY THE DRIVE SYSTEM WHEN THE AIRCRAFT ROTOR BLADES COME IN CONTACT WITH

THE GROUND, WATER, TREES, OR OTHER OBSTACLES THAT WOULD CAUSE DAMAGE REQUIRING

AIRCRAFT ROTOR BLADE CHANGE.

IT IS ADVISED THAT ENGINES SUBJECTED TO SUDDEN STOPPAGE BE RETURNED TO A DESIGNATED OVERHAUL FACILITY FOR THE FOLLOWING INSPECTION, AS FAILURE TO DO SO MAY AFFECT AIRWORTHINESS.  DETAILED DISASSEMBLY, INSPECTION AND ASSEMBLY INSTRUCTIONS ARE PROVIDED IN THE OVERHAUL MANUAL, ALLIED SIGNAL NO. 330.3.

1.	Inspect output reduction carrier and gear assembly (1-030-350-08 or

1-030-350-12) and sun gearshaft (1-030-192-03 or 1-030-192-04).

1.1.	Perform a magnetic particle or fluorescent penetrant inspection on

all parts included in the reduction gearing system.

NOTE

CRACKING MAY OCCUR LONGITUDINALLY ALONG GEAR TEETH.  CRACKS CAN BE CONSIDERED

PARTIAL SEPARATION OF METAL RESULTING FROM UNDUE STRESSES.  CHIPPING AND FLAKING

REPRESENT VARIOUS FORMS OF CRACKING.

1.2.	Perform 8-4 Overtorque (Airframe/Engine) Inspection, of the IPG.

1.3.	If there is no damage found in the preceding inspections, perform

9-9 Engine Oil Contamination Inspection, of the IPG.

1.4.	If damage is found in the preceding inspection, perform overspeed

inspection found in 9-5 Engine Overspeed Inspection, Chapter 9, of the IPG.

2.	If damage is found during 9-5 Engine Overspeed Inspection, perform 9-9 Engine

Oil Contamination Inspection, of the IPG.

9-5.	ENGINE OVERSPEED.

If engine has been subjected to an overspeed condition, proceed as follows:

1.	Remove and check oil filter for metal chips or other foreign matter.

2.	Remove and check chip detector for metal chips.

NOTE

IF CHIPS ARE FOUND IN OIL FILTER OR CHIP DETECTOR, PERFORM AN OIL CONTAMINATION

INSPECTION.  (REF. 72-00-00, ENGINE - TROUBLESHOOTING, PARA. 1.C).

3.	If gas producer (N1) overspeed limits are exceeded, proceed as follows:

3.1.	Perform an INTERNAL (HOT END) INSPECTION.  (REF. 72-00-00, ENGINE -

TROUBLESHOOTING, PARA. 1.D)

3.2.	Check compressor rotor assembly by mechanically rotating and listening

for indications of rubbing.

4.	If output shaft (N2) overspeed limits are exceeded, proceed as follows:

T53L11 OVERSPEED LIMITS

101 PERCENT AT TAKE-OFF POWER.

101 PERCENT AT MAXIMUM CONTINUOUS POWER.

T53L13B OVERSPEED LIMITS

1.	AN N2 OVERSPEED CONDITION EXISTS UNDER THE FOLLOWING CONDITIONS:

WHEN N2 SPEED EXCEEDS 101 PERCENT (21,300 POWER TURBINE RPM, OUTPUT SHAFT

6637 RPM) AT THE TAKEOFF POWER POSITION.

2.	THE FOLLOWING MAXIMUM STEADY-STATE N2 SPEEDS MAY BE ATTAINED, PROVIDING THE

MAXIMUM CORRESPONDING TORQUE PRESSURE IS NOT EXCEEDED WITHOUT CREATING AN OVERSPEED

CONDITION:

STEADY STATE COMBINATIONS

N2 SPEED - MAX					TORQUE PRESSURE - MAX

107%  (7,032 RPM)						10 PSI

106%  (6,966 RPM)					         21 PSI

105%  (6,900 RPM)					         32 PSI

103%  (6,769 RPM)					         42 PSI

102%  (6,703 RPM)					         53 PSI

101%  (6,637 RPM)					         60 PSI

T53L703 OVERSPEED LIMITS

109% (7,163 RPM) AT TAKE-OFF POWER.

4.1.	Visually inspect power turbine rotor assembly for damaged or missing

blades (view through tailpipe).

4.2.	Perform tip clearance inspection on second stage power turbine blades

through exhaust diffuser (0.025 inch minimum.)

NOTE

IF DISCREPANCIES ARE NOTED, PERFORM AN INTERNAL (HOT END INSPECTION). (REF. 72-00-00, ENGINE - TROUBLESHOOTING, PARA. 1.D.)

4.3.	Determine and correct cause of overspeed.

4.4.	Perform engine operation check.  If no discrepancies are noted,

the engine is serviceable.

9-6.	ENGINE OIL OVERTEMPERATURE.

An engine overtemperature condition exists when limits given are exceeded.

1.	Observe the following limits for normal operating conditions:

1.1.	The maximum (red line) OIL-IN temperature is 99 degrees C

(210 degrees F).  When oil temperature exceeds 99 degrees C (210 degrees F)

refer to Paragraphs/subparagraphs below as appropriate.

1.2.	A steady-state engine OIL-IN temperature of 100 degrees C

(212 degrees F) is acceptable provided the oil filter is inspected every

50 hours of engine operation for excessive accumulation of carbon or metal

particles.

Under abnormal (emergency) conditions, such as an oil cooling system malfunction or

failure, the following procedures and engine oil temperature limits will minimize

the risk involved in operating an engine which has exceeded temperature limits.

CAUTION

IT MUST BE CLEARLY UNDERSTOOD THERE IS A POSSIBILITY THAT MECHANICAL COMPONENTS MAY

SUFFER DAMAGE IF ENGINE OPERATING CONDITIONS ARE EXTENDED BEYOND THESE LIMITS.

2.	At oil temperatures from 99 degrees C (210 degrees F) to 130 degrees C

(266 degrees F) for 10 minutes or less, check engine oil screens and main oil

filter.

3.	At temperature from 99 degrees C (210 degrees F) to 130 degrees C

(266 degrees F) for more than 10 minutes, but no more than 30 minutes, proceed

as follows:

3.1.	Change oil, clean all screens and main oil filter.  Ground run

engine for 30 minutes and recheck main oil filter for carbon and metal

particles.  If contamination is found, clean oil screens and oil filter.

Repeat oil change and ground run engine.

4.	At temperatures from 99 degrees C (210 degrees F) to 130 degrees C

(266 degrees F) for greater than  30 minutes, perform following oil overtemperature

inspection, Paragraph 7., below.

5.	When oil temperature reaches 131 degrees C (268 degrees F) and above for any

length of time, perform following oil overtemperature inspection, Paragraph 7.,

below.

6.	When oil temperature reaches 150 degrees C (302 degrees F), the engine must

be returned to Overhaul.

7.	Perform following oil overtemperature inspection as required:

7.1.	Remove combustor turbine assembly.  (Ref. 72-40-00)

7.2.	Disassemble combustor turbine assembly to permit removal of power

turbine rotor and bearing  housing assembly.

7.3.	Disassemble power turbine rotor and bearing housing assembly to permit

removal of No. 3 and 4 position main bearings.  Determine part numbers of

bearings and:

a.	Replace bearing 1-300-176-04, 1-300-584-02, and 1-300-015-02/04.

b.	Inspect other bearings for coke/general condition.  Replace if necessary

c.	Inspect No. 2 main bearing seals for coke/general condition.

Replace if necessary.

7.4.	Disassemble gas producer system components to permit removal of No. 2

position main bearing and No. 2 main bearing seals.  Determine part numbers

of bearings and:

a.	Replace bearing 1-300-584-02, 1-300-176-04.

b.	Inspect other No. 2 bearing part numbers for coke and condition.

Replace if necessary.

c.	Reassemble gas producer system components, power turbine rotor

and bearing housing assembly, and combustor turbine assembly.

Reinstall combustor turbine assembly.

7.5	Remove accessory drive gearbox.

a.	Disassemble gearbox to permit removal of bearings 1-300-002-01/02

and 1-300-0001/02 from pinion gearshaft and bearing assembly, bearings

1-300-0001/02 from thrust bearing liner assembly and bearings

1-300-12-01/02 from starter generator drive gearshaft assembly.

(Ref. 72-60-01)  Determine part number of bearing and:

b.	Replace bearing 1-300-002-01/02, and 1-300-012-01.

c.	Inspect bearing 1-300-012-02 and all remaining installed bearings

for coking and heat discoloration.  Replace if necessary.

d.	Inspect all gears and splined parts for coking and heat

discoloration.  Replace if necessary.

e.	Remove output reduction carrier and gear assembly.

f.	Inspect accessible gears and splined parts for signs of heat

distortion.  Replace any part that is discolored.

9-7.	ENGINE SUBJECTED TO EXCESSIVE G-LOADS (HARD LANDING, SEVERE MANEUVERS).

If it is suspected that excessive G loads have been imposed on engine, conduct the

following inspections immediately after flight during which the excessive loads occurred:

1.	Inspect accessory drive gearbox for cracked mount flanges or loose bolts.

2.	Inspect overspeed governor and tachometer drive for cracks, distortion and

bent shaft.

3.	Inspect oil filter for loose bolts and damaged filter elements.

4.	Inspect oil pump for loose bolts and cracked flanges.

5.	Inspect fuel control assembly for cracked flanges and loose nuts.

6.	Inspect engine and aircraft mounts for cracks, loose bolts, bending, or distortion in any of the following areas:

a.	Engine mounts.

b.	Accessory drive gearbox mount flanges.

c.	Accessory mount flanges.

d.	Inlet, compressor, or combustor housings..

NOTE

IF THE AIRCRAFT-FURNISHED ENGINE MOUNT LEGS EXHIBIT ANY CRACKS, BENDING, OR

DISTORTION, IT IS RECOMMENDED THAT THE ENGINE BE RETURNED TO OVERHAUL AS EXTREMELY

HIGH G-LOADS HAVE BEEN IMPOSED.  IT IS FURTHER RECOMMENDED THAT ALLIED SIGNAL BE

CONTACTED TO PROVIDE ADDITIONAL DIRECTION.

7.	Inspect air, oil, and fuel hose connections for tightness.

8.	Inspect all accessories for loose bolts, nuts, and connections.

  - ENGINE INLET BLOCKAGE.

NOTE

ANY TIME THE AIRCRAFT IS FLOWN IN A LOOSE GRASS/FOLIAGE ENVIRONMENT, OR IF IT IS

SUSPECTED THAT RAGS, PAPER OR OTHER DEBRIS COULD HAVE BEEN INGESTED, THE ENGINE

SHALL BE INSPECTED FOR BLOCKAGE AROUND THE INLET GUIDE VANES.  FAILURE TO PERFORM

THIS INSPECTION COULD RESULT IN LOSS OF POWER.

1.	Inlet blockage inspection.

1.1.	Remove the particle separator (both halves) and aircraft inlet screen

(if installed), and inspect the engine inlet area.

1.2.	Inspect the inlet housing struts and each inlet guide vane for rags,

paper, grass, foliage or other foreign material blockage or partial blockage.

1.3.	Completely remove any foreign material that may be lodged on the inlet

strut or guide vanes.  Special attention should be given to the lower

(4 through 8 o’clock) portion of the vane assembly.

1.4.	If blockage or partial blockage is evident or suspected, remove and

scrap all the first and second stage blades and replace with new blades.

1.5.	If removed, reinstall particle separator and aircraft inlet screen.

1.6.	Perform standard engine vibration check with the engine installed in the

aircraft. (Ref. 71-00-00, Para 12.E.)

9-9.	ENGINE OIL CONTAMINATION.

Whenever an oil contamination inspection has revealed a continuance or an increase

of chips in the oil filter or on the chip detector, but output reduction carrier and

gear assembly has freedom of movement and emits no unusual noises, proceed as

follows:

WARNING

PROLONGED CONTACT WITH LUBRICATING OIL MAY CAUSE A SKIN RASH.  THOSE AREAS OF SKIN

AND CLOTHING THAT MAY COME IN CONTACT WITH LUBRICATING OIL SHOULD BE THOROUGHLY

WASHED IMMEDIATELY.  SATURATED CLOTHING SHOULD BE REMOVED IMMEDIATELY.  AREAS IN

WHICH LUBRICATING OIL IS USED SHOULD BE ADEQUATELY VENTILATED TO KEEP MIST AND FUMES

TO A MINIMUM.

CAUTION

LUBRICATING OIL MAY SOFTEN PAINT UPON CONTACT.  IF LUBRICATING OIL IS SPILLED ON

PAINTED SURFACES, THESE SURFACES SHOULD BE THOROUGHLY WASHED.

1.	Check main oil filter elements for chip accumulation which could have placed

the filter into bypass.  Clean with dry cleaning solvent (Ref. 72-00-00, 62,

Table 203, or appropriate manual) and reinstall.

2.	Remove and inspect No. 2 bearing strainer and No. 3 and 4 bearing strainer

bore for metal chips.  If chips are present, remove and inspect three

reduction gear oil transfer tube strainers (Ref. 72-10-01) and overspeed

governor and tachometer drive oil throttle strainer (Ref. 72-60-02).  Forward

engine to Overhaul if metal chips have clogged more than one-third of flow

area of any one of previously mentioned strainers.  If amount of chips is not

excessive, clean and reinstall strainers and proceed to Paragraph 3. below.

3.	Presence of chips in previously mentioned strainers indicates that bypass of

oil filter has occurred.  Replace oil filter.

4.	Drain all oil from accessory gearbox, aircraft, oil tank, and oil cooler.

5.	Remove metal chips from chip detector.  Clean with dry cleaning solvent (Ref.

72-00-00, 62, Table 203).

6.	Check No. 2 bearing scavenge line for metal contamination.  If chips are

evident, disassemble gas producer as necessary, inspect all oil wetted

components; replace parts as needed.  Flush components with dry cleaning

solvent (Ref. 72-00-00, 62, Table 203) and reinstall.

7.	Check No. 3 and 4 bearings scavenge line for metal contamination.  If chips

are evident, remove combustor turbine assembly, disassemble power turbine and

bearing housing assembly, and inspect bearings and other oil wetted components.

Replace if required (Ref. 72-50-04).  Flush components with dry cleaning solvent

(Ref. 72-00-00, 62, Table 203) and reinstall.

8.	If chips are suspected to come from reduction gearing, remove reduction

gearing, inspect its condition and replace if required.

9.	Remove accessory drive gearbox (Ref. 72-60-01).  Remove and inspect shaft

gear assembly.  Particularly note condition of upper and lower bearings on this

shaft.  Inspect and clean scavenge strainer.  Flush shaft gear assembly and

internal components of gearbox with dry cleaning solvent (Ref. 72-00-00, 62.

Table 203) and reassemble.

10.	Flush aircraft oil system and replace oil cooler on aircraft not equipped

with auxiliary external oil filter.

11.	Service oil system with lubricating oil (Ref. 41 or 42, Table 203)  Operate

engine at 70 to 80 percent N1 for 5 minutes.  Shut down engine and allow to cool.

CAUTION

ANY MALFUNCTION IN OIL PRESSURE IN EXCESS OF PLUS OR MINUS 5 PSI, OR RAPID RISE IN

OIL TEMPERATURE AT ANY PRESET POWER SETTING, IS CAUSE FOR IMMEDIATE ENGINE SHUTDOWN.

12.	Check oil filter elements, chip detector, and strainers.

13.	Inspect chip detector and oil filter strainers for chips.  Amount of chips

noted should be less than original amount.  If so, repeat preceding Paragraphs

10. and 11., increasing engine operating time to 10 minutes.

NOTE

CHIPS IN OIL FILTER MAY ORIGINATE IN OIL SUPPLY TANK; CHIPS ON CHIP DETECTOR

ORIGINATE IN ENGINE.

14.	Repeat inspection, servicing and operating cycle, increasing engine

operating time to 30 minutes.  If no appreciable amount of chips or other

contaminates is noted, engine may be returned to service.  If amount of chips or

other contaminants remains the same or increases, perform oil sample analysis (Ref.

72-00-00, ENGINE - INSPECTION, Para. 1.G.); forward engine to Overhaul.

NOTE

THE FOLLOWING ACTIONS ARE RECOMMENDED TO ENSURE THAT OIL, CHIPS, OR OTHER

CONTAMINANT SAMPLES ARE AVAILABLE TO AID IN THE DIAGNOSIS OF THE PROBLEM.  IF AN

ALLIED SIGNAL REPRESENTATIVE IS CALLED IN, RETAIN THE SAMPLE FOR HIS EVALUATION AND

ACTION.

a.	Exercise care to prevent additional contamination of sample.

b.	Mark oil, chips, or contaminant sample to include operator’s name,

address, location on the engine from which the sample was taken, engine

model and seal number, time since new, time since overhaul, and last

related maintenance action.  Include the oil vendor’s name, batch

number, and date of manufacture on the sample.

c.	If the engine is being returned for repair or overhaul, return marked

sample in engine container.

15.	If the amount of carbon particles found on the engine oil filter elements

covers 15 percent or more of the surface area, proceed as follows:

15.1.	Clean and reinstall oil filter assembly.

15.2.	Drain all oil from accessory drive gearbox, oil tank, and oil cooler.

15.3.	Remove and inspect No. 2 strainer, and No. 3 and 4 bearing strainers.

If carbon particles are present, oil filter has bypassed.  Remove, clean, and

reinstall reduction gear oil transfer tube strainers and overspeed governor

and tachometer drive oil throttle strainer.  Clean and reinstall No. 2 bearing

strainer and No. 3 and 4 bearing strainers.

15.4.	Refill oil tank to capacity with new oil.

15.5.	Start engine and run at 70 to 80 percent N1 for 15 minutes.

15.6.	Shut down engine; then remove, inspect, and clean oil filter and

strainers.  Reinstall oil filter and strainers.

15.7.	If contamination is excessive, repeat procedure until filter is clean

after engine run.

9-10.	LOSS OF POWER OR HIGH EXHAUST GAS TEMPERATURE CONDITION.

Thoroughly investigate the engine inline (engine de-ice) valve for proper functioning prior to proceeding with troubleshooting procedures.  (Refer to applicable engine manual).

9-11.	ENGINE OVERTEMPERATURE.

Perform an engine over-temperature inspection.  (Refer to applicable engine TM.)

NOTE

IF ENGINE CANNOT BE OPERATED WITHOUT EXCEEDING EGT LIMITS AS SPECIFIED IN TM, IT IS AN INDICATION OF ENGINE MALFUNCTION OR INSTRUMENT ERROR.  REFER TO TROUBLESHOOTING TO DETERMINE CAUSE AND CORRECT ACTION, AS OVER-TEMPERATURE INSPECTION MAY NOT BE REQUIRED.

APPENDIX

__________________________________________________________________________________________

Letter from Bell Textron

Ref:  Overhaul and Retirement Schedule, Manuals, and Technical assistance.

Bell Helicopter						            Post Office Box 482

A Textron Company 				                          Fort Worth, Texas 76101

Dear Bell Helicopter Excess/Surplus Aircraft Operators:

Bell Helicopter is aware of several situations in which many operators need technical assistance in maintaining their UH-1 Helicopters. When the helicopters are surplused by the Defense Logistics Agency (DLA), many operators do not receive the appropriate Technical Manuals to maintain their helicopters.

The military Technical Manuals (TM's) required to maintain the UH-1 are:

TM 55-1520-210-23P-1/-2/-3 	PARTS MANUAL

TM 55-1520-210-10 	OPERATORS MANUAL

TM 55-1520-210-23-1/-2/-3 	MAINTENANCE MANUAL

TM 55-1520-210-CL 	CHECKLIST

TM 55-1520-210-PMD 	PREVENTATIVE MAINTENANCE DAILY

TM 55-1520-210-PM 	PHASE MAINTENANCE

TM 55-2840-229-23 T53 	ENGINE MAINTENANCE. MANUAL

These are not Bell Helicopter manuals, Bell Helicopter doesn't maintain, update or distribute these manuals. These manuals are available for purchase at:

NTIS- National Technical Information Service

Military Publications Department

5285 Port Royal Road

Springfield, V A 22161

PHONE: 	703-605-6000

800-553-6847

FAX: 	703-605-6900

Email ORDERS@NTIS.GOV

In order to assist operators operating in the Public Use, Bell Helicopter has developed and recommends the Overhaul and Retirement Schedule. Unfortunately Bell Helicopter cannot assist operators in Type Certified Restricted Category. These operators are obligated to maintain their aircraft in accordance with the Type Certificate Holder requirements.

The rationale behind Bell Helicopter developing this recommended Overhaul and Retirement Schedule is to remove the Gearboxes out of a "On-Condition": Airworthy Limitation. In compliance with the TM's an operator is required to take an oil analysis every 25 hours and submit for a lab analysis. Bell Helicopter is aware that all operators are not performing this maintenance task and therefore Bell Helicopter has developed a recommend Overhaul/Retirement schedule, it's only provided to assist Public Use operators.

Regards

/Andrew L. Kelley/

Product Support Engineer

4/18/2002

UH-1 Retirement/Overhaul Schedule							                         4/18/2002

OVERHAUL 	RETIREMENT 	ITEM 	PART NUMBER

INTERVAL 	INTERVAL

(HOURS)	(HOURS)

Main Rotor

2500 .	Main rotor blade 	204-011-250-5/113

Assembly

10,000 	Composite main rotor    	205-015-150-101

blade

3600	Main Rotor Yoke 	204-011-102-17

1100 		Main Rotor Hub 	204-011-101-3/-5/-9

Assembly.

1200 		Main Rotor Hub 	204-011-101-11

Assembly

1200 		Main Rotor Hub 	204-012-101-139/-141

Assembly

9000 	Main Rotor Grip 	204-011-121-117

Note 1

5000 	Plate Assembly 	204-011-207-105

5000 	Bolt 	Ms21250H06000

2400 	Inboard strap fitting 	204-012-102-1/5

2400 	Outboard Strap Fitting 	204-012-103-1

2400 	Strap Pin 	204-012-104-1, -3, -5

2400 	Retention Strap 	2601399, 204-012-112-5

Retention Strap 	204-012-122-1/5

3600 	Clevis 	204-011-142-3

3600 	Clevis 	204-011-179-1

15000 	Center Frame Assembly 	204-011-307-11

5 Years 	Stabilizer Bar Tube 	201-011-328-1

2400 	Retention Strap 	2606650

2400 	Strap Fitting Inboard 	204-012-102-9

Main

1200/24 months 	Strap Assy Main Rotor 	204-310-101-101

1200/24 months 	Strap Assy Main Rotor 	2601139

5000 	Support Assembly 	204-011-208-101

Transmission

1100		Transmission Assembly 	204-040-016-1/-3

2000 		Transmission Assembly 	204-040-016-5

1500 		Main input quill 	205-040-263-003/-111

Assembly

1500 		Mast assemblv 	204-040-366-009/-015

1500 	Mast Bearing 	AMM9122-44-101

1500 	Bearing 	204-040-136-7/-9

1500 	Bearing 	212-040-136-1

1500 	Mast Assembly 	204-011-450-105

1500 	Mast Assembly 	204-011-450-7

Tail Rotor & Drive

System

1100 	Blade Assembly 	204-011-702-11

1200 	Blade Assembly 	204-011-702-15

1000 	Blade Assembly 	204-011-702-121

Note #2

1

OVERHAUL 	RETIREMENT 	ITEM 	PART NUMBER

INTERVAL 	INTERVAL

(HOURS)	(HOURS)

Tail Rotor & Drive

System (Continued)

300 	Grip Assembly 	204-011-728-1

300 	Grip Assembly 	204-011-728-19

2500 	Grip Assembly 	205-011-711-101

1500 	Yoke Assembly 	204-011-722-5

1500 		Gearbox 42° 	04-040-003-7/-13

-19, -23, -29

3000 	Slider, Tail Rotor 	204-010-720-3

600 .	Bearing Hanger 	204-040-623-5 or

PAM9107NPPA2702

600 		Gearbox 90° 	204-040-012-1

1200 		Gearbox 90° 	204-040-012-7

1200 		Gearbox 90° 	204-040-012-13

Main Rotor Mast

Controls

1100 		Swashplate & Support 	204-011-400-1/-3/-5/-7/-9

Assy

1200 		Swashplate & Support 	204-011-400-11

Assy

ON CONDITION 	Scissors and Sleeve 	212-010-400-129

Assembly 	Note 3

9000 	Outer Ring 	204-011-403-001

Note 3

1000 	Support 	204-011-404-125

Note 3

9000 	Outer Ring 	204-011-403-001

1000 	Support 	204-011-404-125

3300 	Support 	204-011-404-1

3600	Support 	204-011-404-5

500 	Pin 	204-011-446-3

4800 	Collective Lever 	212-010-403-5

1000 	Collective Lever 	204-011-438-1

3600 	Scissors Assembly 	204-011-406-1/-9/-13/-15

1100 		Scissors and Sleeve 	204-011-401-1/-7/-9

Assembly

1200 		Scissors and Sleeve 	204-011-401-011

Assembly

ON CONDITION 	Scissors and Sleeve 	212-010-401-021

Assembly 	Note 4

9000 	Scissors & Hub 	204-011-405-013

Note 4

9000 	Drive Link 	204-011-407-001

Note 4

9000 	Collective Sleeve 	204-011-408-105

Note 4

ON CONDITION 	Scissors lever 	212-010-407-109

assembly

9000 	Scissors Hub 	204-011-405-021

9000 	Drive Link 	204-011-407 -001

9000 	Collective Sleeve 	204-011-408-105

2

Notes:

#1.  Reference BHT Technical Bulletin SU 95-5, Alternate Spare Part: Main Rotor

Grip PIN 204-011-121-117

#2.  Reference BHT Technical Bulletin SU94-2, Alternate Spare Part: Tail Rotor

Blade PIN 204-011-702-121

#3.  Reference BHT Technical Bulletin SU 95-4, Alternate Spare Part, Swashplate and

Support Assembly

#4.  Reference BHT Technical Bulletin SU-94-3, Alternate Spare Part and Scissor and

Sleeve Assembly PIN 204-011-401-021

3