Survey Plans

Submittal Form

## Approvals

## _______________________________________________         ____________

George Ison									Date

Ship Operations Contract Project Officer, Ship

Safety Officer

## _______________________________________________         ____________

Glenn Warren								Date

Environmental Monitoring and Indicators Team Leader

## _______________________________________________         ____________

Paul Horvatin								Date

Monitoring Indicators and Reporting Branch Chief

# IFYLE-2005

# August Transect-Diel Cruise (2)

Dates:		August 27, 2005 – August 31, 2005

Vessel:	Lake Guardian

#### Ports:

Embark:  		Cleveland Port Authority:   1100 EDT August 27

Disembarkment:    	Cleveland Port Authority:   1454 EDT August 31

## Cruise Participants:

PIs (indicate project PI if PI will not be on board)                                             Status      Cabin    Citizen

| (M) Henry Vanderploeg (Chief Scientist) | PI |  | US |
| --- | --- | --- | --- |
| (M) Hal Gunder (with S. Brandt) | Student |  | US |
| (M) Jesse Kipp (for S. Ruberg / H. Vanderploeg) | Student |  | US |
| (F) Sheena Ripple (with H. Carrick) | Student |  | US |
| (M) Hunter Carrick | PI |  | US |
| (M) Dave Fanslow | Support |  | US |

Purpose of Cruise:

To determine the vertical distribution of fish, mesozooplankton, phytoplankton, and microbes in central Lake Erie relative to physical habitat features (e.g., oxygen, temperature).

Objectives:

- Monitor 3 diel stations in central Lake Erie for 24 hours each using fish acoustics, a plankton survey system (PSS), zooplankton net and pump sampling, flow cytometry, and incubation and grazing experiments.

- Monitor 3 east-west transects using the PSS and acoustics with periodic stops to do a CTD.  An additional horizontal transect will be sampled as well.

Environmental questions asked by the project:

-How does low dissolved oxygen influence primary production/respiration, microbes, mesozooplankton, and fish distributions, feeding behavior, condition, and production?

# Survey Plan

## Chemical background information:

Fanslow/Vanderploeg

Sugar formalin (10%)

Sugar formalin (10%) with Rose Bengal

Hunter Carrick

Sodium thiosulfate

Manganese chloride

Sodium hydroxide

Sodium iodide

Sulfuric acid

Potassium iodate

Lugols solution (iodine)

Formaldehyde

Glutaraldehyde

Paraformaldehyde

Sodium cacodylate

Primuline

Trizma hydrochloride

Acridine orange

Sugar formalin (formaldehyde)

DCMU (diuron)

Ampicillin (antibiotic)

#### Core measurements for surveys:

Along east-west transects and diel site transects, while underway:

| Variable | PI | Lake Guardian Staff Help? | Instrument/Technique |
| --- | --- | --- | --- |
| Continuous temp., DO, Par, ZP | Kipp/Vanderploeg (for Vanderploeg) | Yes, with A-frame and to run PSS | To-yo Plankton Survey System (PSS) |
| Fish Biomass | Gunder/Fanslow | Yes, with port-side crane | Towed acoustics fish (1m below surface) |
| DO, Temp, chla… | All | Yes | CTD |

At endpoints and midpoints of diel transects (only diel stations not sampled last week)

| Variable | PI | Lake Guardian Staff Help? | Instrument/Technique |
| --- | --- | --- | --- |
| Depth profiles for temp., DO, transmissometry, fluorometry, etc. | All | Yes, with starboard side winch | CTD25, Seabird fluorometer, Rosette sampler |
| Secchi Depth | All | Yes | Secchi Disk (in shadow) |
| Zooplankton net (whole water column) | Kipp/Vanderploeg(for Vanderploeg) | Yes, with starboard side winch at 1:00 & 13:00 only | 64um net & 153um net vertical haul (n=2 reps of each) |
| Discrete water/zooplankton | Kipp/Vanderploeg(for Vanderploeg) | Yes, with starboard side winch | Diaphragm pump (need compressed air) |
| Benthic macroinverts. | Gunder/Fanslow (for Ludsin/Hook) | Yes, with starboard side winch | Ponar sampler with 250-um elutriator (n=3 reps per stopover site) |
| Phytoplankton cell numbers/biomass, algal pigments, sestonic nutrients, and primary production and respiration rates | Carrick | Yes, with starboard side winch | Rossette sampler (20 liters of water required) & on-board incubation |
| Quantify in situ photosynthesis and respiration (stations 7 (Diel_B), 8, & 13 (Diel_D) | Carrick | Yes, deploying lighted mooring from zodiac and with starboard side winch | Diurnal Light-Dark Bottle Experiments attached to moored light, Rosette Sampler; incubators |
| Microzooplankton Grazing (stations 7-Diel_B & 13-Diel_D) | Carrick | Yes, with starboard side winch | Rosette Sampler, incubators |

## Equipment to be brought and used on deck (investigators):

## (Equipment marked with an * will be provided by the individual PI)

- EBT, SeaBird fluorometer, Rosette sampler with Go Flow bottles EBT, DO, Conductivity, pH, Transmissometer (multiple)

- Air Compressor (multiple)

- Secchi disk (multiple)

- *Diaphragm pump: for pumping water at discrete depths (Vanderploeg/Kipp)

- *Plankton survey system (Kipp)

- *Acoustics system (Gunder/Fanslow)

- *64 and 153 µm zooplankton nets  (Vanderploeg/Kipp)

- *Research grade compound microscope (Leica DMR) (Carrick)

- *Automated Titrator (Brinkman Titrino) (Carrick)

- *Fluorometer (10-Au) (Carrick)

- *Laptop computers (Carrick)

- *Filtering manifolds with pumps (Carrick)

## Mooring Requirements:

Lighted moorings will be placed at diel stations B (near mooring 7) and D (near mooring 13) (and possibly at a 3rd diel station, but only if arrived at before sunrise) in order to do in situ photosynthesis and respiration experiments using light and dark bottles.  A mooring with a chain of bottles will need to be deployed just prior to sunrise and retrieved just prior to sunset at both stations.  These experiments require that the Lake Guardian is on each diel station prior to sunset.  A zodiac will be needed to deploy the moorings.

## Diving Operations:

No diving operations are currently planned for this cruise.

## Special Operating Requirements:

For our east-west transects that span most of the lake (Transects from A to C to D and A to H), we would like to tow instruments (PSS, acoustics) at 5.25 knots (if acoustic gear is not losing pings).  Occasional stops to do a CTD will need to be made along the way (at A, midpoint of A-C, and at station C).

For the diel sampling our experimental sites are actually a 3 nautical mile transects with sampling occurring continuously along each transect, and at both ends (~1000 m outside the transect line).  We will sample each 3 nautical mile transect for 24 hr, with sampling blocks divided into the following intervals (EDT):

0100-0500; 0500-0900; 0900-1300; 1300-1700; 1700-2100; 2100-0100.

We would like to complete six 24-hour experiments at 3 sites in the central basin (Diel stations B, D, and A).  Ideally, ship speed will be 4 knots, when on a transect.

Sampling Protocol for Transect Sampling:

Along each east-west transect run, we would like to do the following:

- At start of transect (during daytime)

  - Do a CTD cast to measure temperature, Par, oxygen, conductivity, etc..

- With ship not moving (or only drifting), deploy PSS (from A-frame on stern to depth of 4 m) and acoustics (side from crane to depth of 1 m) at start of transect line (note, an air compressor hose will be attached to the acoustics towfish to collect water continuously).

- Tow PSS and acoustics along transect (ideally at 5.25 knots) until mid-point or end of transect (as outlined in Table 1 below).

  - Please notify PSS and acoustics operators when 10, 5, 1 and then 0 minutes from midpoint (or end) of transect

  - Continue steaming at 4 knots through the end of the transect until PSS is parked at a depth of 4 m

  - Once up at 4 m, we will notify captain, who then can turn around and/or “park” ship

PSS and acoustics equipment can remain in the water during the entire 24 hr sampling period, but should be pulled up during the steam to the next station.

Sampling Protocol for Diel Experiment:

At each station, we would like to do the following:

- With ship not moving (or only drifting), deploy PSS (from A-frame on stern to depth of 4 m) and acoustics (side from crane to depth of 1 m) at ~1000 m before first station (i.e., outside transect line).

- Tow PSS and acoustics along a 3 nautical mile transect (ideally at ~4 knots, 5 knots max). Transect should take about 45-50 min. at 4 knots.  End at coordinates on the opposite end of transect.

  - Please notify PSS and acoustics operators when 10, 5, 1 and then 0 minutes from end of transect

  - Continue steaming at 4 knots through the end of the transect until PSS is parked at a depth of 4 m

  - Once up at 4 m, we will notify captain, who then can turn around and/or “park” ship ~1000 m from the end of the transect (i.e., park ship outside of transect line)

PSS and acoustics equipment can remain in the water during the entire 24 hr sampling period, but should be pulled up during the steam to the next station.

- Once at a stop and waters are settled, conduct a CTD cast to determine vertical structure.

- Use a rosette sampler to collect water at different depths (2-4 depths) for all PIs

  - Water for grazing experiments, chlorophyll

- Duplicate zooplankton net tows, full water column, only two times during the diel period; at1:00 with 64um net, and at 13:00 with both 64 & 153 um nets.

- Pump for zooplankton at no more than 4 depths (to be determined from CTD cast).

- Collect benthic macroinvertebrates with ponars (n=3 reps/diel site

  - Benthos should be collected at both endpoints and the midpoint of each diel transect (n=9 samples/diel transect)

  - Benthic collections only need to be made during 1 cycle of the 24-hr period (n=9 total samples)

- Just prior to sunrise a lighted mooring will need to be deployed for light-dark bottle experiments

- Sit and wait until next cycle to start, per times above.

- Repeat the cycle until 6 cycles have been conducted at the site (24 hr).

- During each cycle in the daytime, we need an extra 30 minutes with acoustics over the side (at surface, but not towed) to calibrate the instrument.  This can only occur in calm conditions.

- Move to next station and repeat.

Attached at the end, are Hunter Carrick’s explicit requests:

In theory, time will permit all stations to be sampled by the early afternoon of August 31.  Below is the prioritizations of stations to be sampled (i.e., 1st stations are more important than last stations).

- Transect B

- Transect D

- Transect H or A (or another with a thick, hypoxic hypolimnion)

- East-west transect from A to C to D

- Transect from A to H.

See Table 2 for sampling station coordinates and Table 3 and Figure 1 for the project cruise track.

# Lab Space Requests (if known):

Vanderploeg/Kipp: 			Back Lab for PSS computer and joy stick (port side)

freezer space

Filtering space for chlorophyll samples

Lab space for water filtration

Deck space for diaphragm pump (starboard side)

Gunder/Fanslow			Back Lab area for acoustics computer (port side)

Deck space for towfish

Carrick:				Bench space in primary productivity (biology) lab for microscope

Deck space for decktop incubator

# Hunter Carrick’s email correspondence (verbatim):

# Hi Stu:

Good talking with you this afternoon.  My chem and equipment list is enclosed. My primary research interests are listed below including a brief overview of required sampling and facilities.  I would request to work in the primary production lab and have some space where i might do microscope work.  I will need one bunk (for myself) and deck space (see below) for one decktop incubator.

1.  Ambient water column conditions (Stations 5, 7, 8, and 13)
I will need to take CTD casts at each station to assess ambient conditions
Whole water samples (20-liters) will be collected from epi, meta, and hypolimnia.
I will subsample collected water to estimates: phytoplankton cell numbers/biomass, algal pigments, sestonic nutrients, and primary production and respiration rates.
The production/resp experiments will conducted by incubating bottles (light and dark 300ml BOD bottles) in a deck top incubator (I will provide).  The incubator was placed on the aft deck behind the pilot house (power and deck water needed).

2.  Diurnal Light-Dark Bottle Experiments (stations 7 and 13)
I will perform bottle experiments to estimate the rates (simultaneous) of primary prod and resp. in the water column.
Whole water samples (15-liters) will be collected from epi, meta, and hypolimnia just prior to dusk.
Water from each depth will be placed into twelve 300ml BOD bottles (36 bottles total).  
One set will be place on a moored light that will be deployed back in the lake at sunrise.  
The other set (18 bottles) will be incubated in the Percival incubator (PPr Lab).  This will require that one of the two Percival incubators will run at hypolimnetic light and temperature conditions (ca 10 oC and <5 ue/m2/s).
The moored light will be retrieved at sunset that day.

3. Zooplankton grazing experiments (stations 7 and 13)
I will perform bottle experiments (8 1-liter bottles) to estimate zoop grazing on phytoplankton that need to be incubated at surface irradiance in the Percival incubators (PPr Lab).
This will require collecting appr. 10-liters of water from the epilimnion and two zooplankton tows (10m to surface with 153um Wis net).

4.  Microzooplankton grazing experiments (stations 7 and 13)
I will perform bottle experiments (12 1-liter bottles) to estimate microzoop grazing on picoplankton that need to be incubated at surface irradiance in the Percival incubators (PPr Lab).
This will require collecting appr. 10-liters of water from the epilimnion

Should you have any questions, feel free to contact me (cell 814-883-1238 or numbers below).
Thanks, Hunter

# Master Sample Sites and Location:

Master list of stations.

|  |  | Decimal Degrees | Degree-Minutes |
| --- | --- | --- | --- |
| Description | Acronym | Lat | Lon | Lat | Lon |
|  | Cleveland | 41.500 | 81.700 | 41.300 | 81.420 |
| Mooring 8 | Buoy8 | 41.833 | 82.200 | 41.500 | 82.120 |
| Diel_A | Diel_AE | 41.990 | 82.058 | 41.594 | 82.035 |
|  | Diel_AM | 41.990 | 82.092 | 41.594 | 82.055 |
|  | Diel_AW | 41.990 | 82.126 | 41.594 | 82.076 |
| Diel_B | Diel_BE | 41.966 | 81.650 | 41.580 | 81.390 |
|  | Diel_BM | 41.966 | 81.688 | 41.580 | 81.413 |
|  | Diel_BW | 41.966 | 81.718 | 41.580 | 81.431 |
| Diel_D | Diel_DE | 42.200 | 80.810 | 42.120 | 80.486 |
|  | Diel_DM | 42.200 | 80.844 | 42.120 | 80.506 |
|  | Diel_DW | 42.200 | 80.878 | 42.120 | 80.527 |
| Diel H | Diel_HW | 41.8520 | -82.3950 | 41.51 | 82.23.7 |
|  | Diel_HM | 41.8520 | -82.3600 | 41.51 | 82.21.6 |
|  | Diel_HE | 41.8520 | -82.3250 | 41.51 | 82.19.5 |
| Diel C | Diel_CW | 42.1750 | -81.2667 | 42.10.5 | 81.16 |

# Projected Cruise Plan

Sampling coordinates and estimated sampling times for Aug 27-31, 2005 Lake Guardian diel cruise.  I assumed that sampling occurred at 4 knots while on a diel stations, at 5.25 knots when doing long PSS/acoustics transects between stations, and at 8 knots during transit between stations (no sampling).

| # | Station name | Latitude | Longitude | Date | ETA | Station Time (hr) | Tasks | Transit time (hr)* | Transit distance | speed knots |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | Cleveland | 41.500 | -81.700 | 27-Aug | 11:00 | 0 | Depart Cleveland |  | 0 |  |
| 1 | AE | 41.9900 | -82.0583 | 27-Aug | 14:50 | 0.5 | CTD/PSS/acoustics | 3.34 | 33.4 | 10 |
| 2 | A-C mid | 42.0797 | -81.6990 | 27-Aug | 18:32 | 0.5 | CTD/PSS/acoustics | 3.20 | 16.8 | 5.25 |
| 3 | CW | 42.1750 | -81.3342 | 27-Aug | 22:17 | 0.5 | CTD/PSS/acoustics | 3.26 | 17.1 | 5.25 |
| 4 | DW | 42.2000 | -80.8775 | 28-Aug | 2:21 | 0 | PSS/acoustics | 4.05 | 20.3 | 5 |
| 5 | DE | 42.2000 | -80.8100 | 28-Aug | 5:01 | 1.93 | CTD/rosette ZP pump/net Secchi | 0.75 | 3.0 | 4 |
| 6 | DE | 42.2000 | -80.8100 | 28-Aug | 5:01 | 0 | PSS/acoustics | 0.00 | 0.0 | 4 |
| 7 | DW | 42.2000 | -80.8775 | 28-Aug | 9:01 | 3.25 | CTD/rosette ZP pump/net Secchi | 0.75 | 3.0 | 4 |
| 8 | DW | 42.2000 | -80.8775 | 28-Aug | 9:01 | 0 | PSS/acoustics | 0.00 | 0.0 | 4 |
| 9 | DE | 42.2000 | -80.8100 | 28-Aug | 13:01 | 3.25 | CTD/rosette ZP pump/net Secchi | 0.75 | 3.0 | 4 |
| 10 | DE | 42.2000 | -80.8100 | 28-Aug | 13:01 | 0 | PSS/acoustics | 0.00 | 0.0 | 4 |
| 11 | DW | 42.2000 | -80.8775 | 28-Aug | 17:00 | 3.25 | CTD/rosette ZP pump/net Secchi | 0.75 | 3.0 | 4 |
| 12 | DW | 42.2000 | -80.8775 | 28-Aug | 17:00 | 0 |  | 0.00 | 0.0 | 4 |
| 13 | DE | 42.2000 | -80.8100 | 28-Aug | 21:00 | 3.25 | CTD/rosette 1m pump (Tracy) | 0.75 | 3.0 | 4 |
| 14 | DE | 42.2000 | -80.8100 | 28-Aug | 21:00 | 0 | PSS/acoustics | 0.00 | 0.0 | 8 |
| 15 | DW | 42.2000 | -80.8775 | 29-Aug | 0:15 | 2.5 | CTD/rosette ZP pump/net Secchi | 0.75 | 3.0 | 4 |
| 16 | BE | 41.9658 | -81.6500 | 29-Aug | 5:01 | 1.07 | PSS/acoustics | 3.70 | 37.0 | 10 |
| 17 | BW | 41.9658 | -81.7175 | 29-Aug | 9:01 | 3.25 | CTD/rosette ZP pump/net Secchi | 0.75 | 3.0 | 4 |
| 18 | BW | 41.9658 | -81.7175 | 29-Aug | 9:01 | 0 | PSS/acoustics | 0.00 | 0.0 | 4 |
| 19 | BE | 41.9658 | -81.6500 | 29-Aug | 13:01 | 3.25 | CTD/rosette ZP pump/net Secchi | 0.75 | 3.0 | 4 |
| 20 | BE | 41.9658 | -81.6500 | 29-Aug | 13:01 | 0 | PSS/acoustics | 0.00 | 0.0 | 4 |
| 21 | BW | 41.9658 | -81.7175 | 29-Aug | 17:00 | 3.25 | CTD/rosette ZP pump/net Secchi | 0.75 | 3.0 | 4 |
| 22 | BW | 41.9658 | -81.7175 | 29-Aug | 17:00 | 0 | PSS/acoustics | 0.00 | 0.0 | 4 |
| 23 | BE | 41.9658 | -81.6500 | 29-Aug | 21:00 | 3.25 | CTD/rosette ZP pump/net Secchi | 0.75 | 3.0 | 4 |
| 24 | BE | 41.9658 | -81.6500 | 29-Aug | 21:00 | 0 | PSS/acoustics | 0.00 | 0.0 | 4 |
| 25 | BW | 41.9658 | -81.7175 | 30-Aug | 1:00 | 3.25 | CTD/rosette 1m pump (Tracy) | 0.75 | 3.0 | 4 |
| 26 | BW | 41.9658 | -81.7175 | 30-Aug | 1:00 | 0 | PSS/acoustics | 0.00 | 0.0 | 4 |
| 27 | BE | 41.9658 | -81.6500 | 30-Aug | 5:00 | 3.25 | CTD/rosette ZP pump/net Secchi | 0.75 | 3.0 | 4 |
| 28 | AE | 41.9900 | -82.0583 | 30-Aug | 9:32 | 0 | PSS/acoustics | 4.53 | 18.1 | 4 |
| 29 | AW | 41.9900 | -82.1257 | 30-Aug | 13:01 | 2.75 | CTD/rosette ZP pump/net Secchi | 0.74 | 3.0 | 4 |
| 30 | AW | 41.9900 | -82.1257 | 30-Aug | 13:01 | 0 | PSS/acoustics | 0.00 | 0.0 | 10 |
| 31 | AE | 41.9900 | -82.0583 | 30-Aug | 17:01 | 3.25 | CTD/rosette ZP pump/net Secchi | 0.74 | 3.0 | 4 |
| 32 | AE | 41.9900 | -82.0583 | 30-Aug | 17:01 | 0 | PSS/acoustics | 0.00 | 0.0 | 4 |
| 33 | AW | 41.9900 | -82.1257 | 30-Aug | 21:01 | 3.25 | CTD/rosette ZP pump/net Secchi | 0.74 | 3.0 | 4 |
| 34 | AW | 41.9900 | -82.1257 | 30-Aug | 21:01 | 0 | PSS/acoustics | 0.00 | 0.0 | 4 |
| 35 | AE | 41.9900 | -82.0583 | 31-Aug | 1:00 | 3.25 | CTD/rosette ZP pump/net Secchi | 0.74 | 3.0 | 4 |
| 36 | AE | 41.9900 | -82.0583 | 31-Aug | 1:00 | 0 | PSS/acoustics | 0.00 | 0.0 | 4 |
| 37 | AW | 41.9900 | -82.1257 | 31-Aug | 5:00 | 3.25 | CTD/rosette ZP pump/net Secchi | 0.74 | 3.0 | 4 |
| 38 | AE | 41.9900 | -82.0583 | 31-Aug | 5:22 | 0 | PSS/acoustics | 0.37 | 3.0 | 8 |
| 39 | AW | 41.9900 | -82.1257 | 31-Aug | 8:37 | 2.5 | CTD/rosette ZP pump/net Secchi | 0.74 | 3.0 | 4 |
| 40 | HE | 41.852 | -82.3250 | 31-Aug | 11:25 | 0.5 | CTD/PSS/acoustics | 2.30 | 12.1 | 5.25 |
| 41 | Cleveland | 41.500 | -81.700 | 31-Aug | 14:54 | 0 | End cruise | 3.48 | 34.8 | 10 |

# Numbers denote the projected cruise track that corresponds to the table below it.

# Text boxes

1  Cruise to Diel Station A (do CTD once there)

2  Tow PSS/acoustics to midpoint of A and C (do CTD once there)

3  Tow PSS acoustics to Diel Station C (do CTD once there)

4  Tow PSS acoustics to Diel Station D

5  Diel at station D (must arrive before sunrise)

6  Cruise to Diel Station B (must arrive before sunrise)

7  Diel at station B

8  Cruise to Diel Station A (or another suitable station with a thick, hypoxic hypolimnion)

9  Diel at Station A (or another chosen station)

10 Tow PSS/Acoustics to diel station HW (do CTD once there)

11  Cruise to Cleveland