# Executive Summary

Grid West Transmission Customers will submit balanced energy schedules.  Due to resistance on transmission lines, energy will be lost as power flows from source to sink.  Transmission Customers are responsible for these losses.  They must make arrangements for them during the Day-Ahead scheduling process.

Highlights of the proposed methodology include:

- Pre-existing transmission service rights are honored

- Grid West’s loss methodology will apply only to Injection Withdrawal Right (IWR) schedules;

- Ex-ante loss factors will be used;

- Transmission customers provide concurrent losses in day-ahead scheduling process; and

- A simplified loss methodology will be used for Grid West startup.

# Background

Currently, many pre-existing transmission rights include loss provisions.  As a part of Grid West operations, these loss provisions will be honored.  However, not all customers have pre-existing rights.  In addition, customers with pre-existing rights may wish to translate them into IWRs in order to participate in Grid West the Grid West Reconfiguration Service (RCS).  For these customers, a new loss methodology is required.

The challenges in developing a new loss methodology are:

- Transmission losses are not linear.

- They are a result of the combined activities on transmission lines.

As a result, it is difficult to attribute losses to specific transactions.  Thus, losses are often treated as an allocation issue.  Losses are allocated to Transmission Customers based on a specific usage measure.  Marginal loss factor are commonly used. However, the use of marginal loss factors results in an over collection of system losses.  Therefore, a scaling factor is applied to the marginal loss factors to prevent over-collection.

The proposed loss methodology is based on the use of scaled marginal loss factors.

# Purpose

This white paper discusses the proposed Grid West loss methodology.  It attempts to satisfy the objectives established by the Regional Representative’s Group (RRG):

- Minimize cost shifts,

- Maintain loss provisions of pre-existing transmission service rights and obligations,

  - Create a good match between loss collection mechanisms and actual loss effects on the transmission system to improve economic efficiency

  - Use ex ante loss factors to provide certainty to transmission customers in advance.

  - Eliminate loss related pancaking (i.e. payment of multiple rates for one transaction) for transactions within the GWT system.

  - Be easy to implement and consistent with the scheduling model.

In practice, not all objectives can be achieved simultaneously because of inherent conflicts. This paper proposes a simplified approach as a starting point. Future improvement can be considered and phased in.

# Losses for Pre-existing Rights

Based on the Regional Proposal, the loss requirements for transmission customers with pre-existing transmission service rights agreement will not change.  However, a new loss methodology will be used for customers with IWRs.    In order to reconcile this difference in methodologies, existing transmission owners (TO) will make up the difference in their loss provisions.

This practice is no different from what the existing transmission owners perform today. There are no new risks imposed to the existing transmission owners.

# Day-Ahead Scheduling

Losses are provided in the day-ahead scheduling process. There are three steps in the proposed loss process as depicted in Figure 5.0.

- Transmission customers with pre-existing rights submit their schedules and loss schedules to their TO. The loss provision is governed by their pre-existing contracts.

- Transmission owners submit combined transmission and loss schedules to Grid West.  At the mean time, transmission customers with IWR rights submit their schedules and loss schedules to Grid West.

- Grid West calculates and creates the interchange schedules between TOs to rebalance the losses collected from IWR and TO customers.

Fig. 5.0 Grid West’s Loss Process

IWR transmission customer’s loss obligations can be in one of two ways:

- Direct: Transmission customers submit a separate loss schedule for the losses attributed to their aggregate schedules

- Indirect: Third-party loss providers submit loss schedules on behalf of the Transmission Customer for the losses attributed to their aggregated schedules.

Currently, some customers have the ability to return losses in kind up to 168 hours after the scheduling period.  Since, Grid West does not own resources to supply or accept the mismatch of actual losses and losses obligations, Transmission customers will not have the ability to return losses in kind to Grid  West after the fact.  If the transmission customers and their existing transmission owners can reach a bilateral agreement, however, the return option between them can be maintained or implemented.  Transmission customers or their existing transmission owners can schedule the transactions of loss returns as a bilateral transaction.

Transmission losses will not apply to the Reconfiguration Service (RCS) process.

# Loss Methodology Description

The loss methodology describes the following:

- Ex-ante loss factor computation

- Loss obligation determination

- Allocation of losses to Control Areas

The attributes of the proposed methodology are further discussed in Appendix A.

Grid West will use ex-ante loss factors to calculate loss obligations.  Ex-ante loss factors will provide Transmission Customers with certainty in the economics of energy transactions.  In order to calculate these loss factors, Grid West will use a power flow model based on various operating scenarios (e.g. Peak , Off-Peak, seasons, etc.).  Based on these detailed loss factors, Grid West will develop a set of aggregated loss factors that have some degree of time and location variation.

Transmission losses are allocated to both load and resources consistent with the loss causation principle.  Grid West will calculate a loss obligation for each submitted schedule. The loss obligations for a transmission customer are accumulated for the scheduled transactions. A transmission customer or its loss provider should submit a separate loss schedule to Grid West as part of the day-ahead scheduling submission process.

Grid West manages transmission losses on a regional level in the Day-Ahead.  Transmission Customers are not required to provide losses at a specific bus, or within a specific control area.  As such, control areas that must account for this loss surplus or loss shortfall.  In order to avoid cost shifting between control areas in Real-Time, Grid West must re-allocate the collected transmission losses in the day-ahead to Grid West control areas.  This reallocation is accomplished through the use of Interchange Schedules.

After receiving the loss schedules from transmission customers, Grid West will create interchange schedules to rebalance losses from one control area to other within GWT. The end results of loss reallocation schedules are that all control areas with the GWT will receive their share of expected losses as computed by the power flow model. This step is necessary to avoid cost shifts between the control areas within the GWT.

An example is given in Appendix B to illustrate how this loss reallocation schedule is to be achieved.

# Roles and Responsibilities

## Grid West’s Responsibilities

Grid west will:

- Calculate and publish a applicable loss factor with sufficient lead time before delivery day;

- Evaluate loss obligations for all submitted day-ahead schedules;

- Ensure the proper amounts of losses are scheduled on the day-ahead;

- Create interchange loss schedules; and

- Settle the loss for transmission customers who submit schedules directly to Grid West.

## Transmission Customers Responsibilities

Transmission customers will:

- Meet their loss obligation by submitting loss schedules either directly or by third party loss provider.

## Loss Providers’ Responsibilities

Loss providers will:

- Schedule the loss obligations for the transmission customers that they represent, and

- Represent multiple transmission customers if they choose.

## Existing Transmission Owners’ Responsibilities

Existing transmission owners will:

- Act as the default loss providers for transmission customers that have pre-existing transmission service rights agreement.

# Market Benchmarks

One fundamental difference exists between Grid West and other RTOs; the day-ahead regional services and real-time markets take place with different geographical boundaries.  As a result, concurrent loss scheduling is required and additional steps are taken to avoid the costs shifts between transmission customers.  Except for this difference, many similarities can be observed from all existing business practices by the existing RTOs and ISOs in North America. A comparison of the proposed loss methodology with other RTO/ISO loss model is given in Table 8.0 below.

Table 8.0: A Comparison of Loss Methodology with Other RTOs

| Loss Methodology Attributes | CAISO Current | ERCOT | LMP market (NYISO/MISO CAISO future) | GW proposal |
| --- | --- | --- | --- | --- |
| Ex ante vs. ex post | Ex ante and ex post (hour-ahead) true up | Ex ante | Ex post for financial settlement. The quantity may be ex ante. | Ex ante |
| Pre-existing transmission service rights agreement | Each TO will be responsible for recovering any losses mismatch |  | In MISO, Transmission customers settles directly with MISO and Marginal Losses rebates to existing contract | Each TO will be responsible for recovering any losses mismatch |
| Who pays? Supply or demand | Supply | Demand | Both | Both |
| Return option | N | N | Some | N |
| Locational signal | Partial | Partial | Yes | Yes |
| Loss factor calculation | Scaled marginal | Scaled marginal | Marginal | Scaled marginal |
| Loss factor granularity | Hourly | Seasonal peak and off-peak as base and extrapolation to 15 minutes interval. | Hourly | Seasonal peak and off-peak |
| Over collection | N | N | Y | N |

# Technology Solutions

The implementation of loss methodology is an integral part of Grid West operations. There are no specific technology components for the loss implementation since the loss methodology is embedded in the scheduling and settlement systems. The major elements of the impact to the overall technology solution are:

- Power system modeling software

- Scheduling system

- Settlement system

- OASIS posting

# Organization Requirements

Table 10.0 presents the resource requirements for the operation and support of the loss methodology and associated business processes.

Table 10.0: Staff Requirements

| Division | Department | Role | Responsibility |
| --- | --- | --- | --- |
| Market Operations | Forward Markets | Manager | Manage the development of loss factors |
| Market Operations | Forward Markets | Analyst | Basecase development Develop loss factors Oasis interfaces Loss provider registration Loss obligation calculation and validations Loss reallocation scheduling |
| Information Technology |  | Analyst | Application Support |

# Cost Drivers

The primary cost drivers for loss methodology implementation relates to the complexity of the solution. For example, the costs will be reduced if Grid West:

  - Use the simplified methods with coarse time and locational loss factors.

On the other hand, the costs will increase if Grid West:

  - Develops power models and compute loss factors for all the delivery periods;

  - Includes losses in RDS and RCS process;

  - Includes a loss true-up process;

  - Assumes the responsibility of the mismatch of pre-existing contractual losses and loss obligations defined in this proposal.

# Design Issues for Further Discussion

- Unintended consequence of “Cherry-picking” by pre-existing transmission service rights holders.  An existing transmission contract holder can easily assess the benefits of holding the contract or releasing the contracts to standard IWR rights. If the option is available for the contract holders, all other terms being equal, the contract holder will selectively switch the contracts to standard IWR rights, leaving a possible shortfall in the transmission provider’s loss balance account.

- “No charge” transmission reservation. In the current practice of many Northwestern utilities, transactions for loss return enjoy the benefit of not needing reserve transmission rights and not being charged.  It is not clear whether such a benefit should be maintained for the loss provision by the transmission customers, or by the loss providers.

- Treatment of curtailments.  If there are infeasibilities in the day-ahead scheduling process, Grid West may have to curtail proposed transactions. The curtailments may impact the loss obligations of the transmission customers. At this time, it is unclear whether such an iterative process should be developed.

- The boundary mismatch of CCA and Grid West. The existence of this mismatch will likely require different sets of loss factors for different purposes. Grid West will need to explore if additional simplifications can be made using the same set of loss factor.

- Use of area loss factors. Caution must be exercised in defining areas since the use of very large area will lead to significant cost shifting. The proposed methodology assess loss obligation of transactions based on the loss factor at both IP and WP. When the IP and WP of a transaction are within the same area, there will no loss obligations for the transaction.

- Distribution losses.

# Appendix A:  Properties of the Proposed Loss Methodology

The following sections describe some of the attributes of the proposed loss methodology.  A summary of two alternate methodologies is also presented for comparison.

## Additive Property

The additive property of a loss methodology (also having been called transitiveness) measures if two equal and opposite transactions will cancel out one another’s flows and the associated loss obligations. The proposed loss factor in the previous section is additive since it has same treatment of supplies and demand in computing the loss obligations at a location.

Selecting an additive methodology is preferable since it conforms to the objective to reflect the actual costs of transactions. For example, if there are two transactions with same quantities from A to B and from B to C, a loss methodology with additive property will result in the same amount of loss obligations as a transaction from A to C while a non additive loss methodology will generally not.

The additive property is generally preserved for the Locational Marginal Pricing (LMP) type loss methodology that has been adopted in several RTO/ISOs.

## No Pancaked Loss Charges

Pancaked rates in transmission and losses have been generally regarded as detrimental to the economical efficiency.  Rate pancaking refers to the payment of multiple transmission rates for one transaction (e.g. a transaction scheduled across multiple transmission systems with a cost to use each one).  Some contend that distance of a transaction is often assumed to be a direct measure of the associated losses, thus a transaction across different areas increases transmission losses. This is incorrect in many cases. For example, a long distance transaction in a lightly loaded transmission area will cause fewer losses than a short distance transaction in a heavily loaded area.  Losses do not necessarily increase with the distance and number of transactions that cross the control area boundaries. As another example, assuming that there are two identical and connected transmission systems, each with balanced supplies and demand. The flows at their tie lines will be zero. The transmission losses of the two systems remain the same, whether one assumes that there no transactions are taking place between the two systems, or one assumes that all demands in one system will transact with supplies of other system.

The proposed loss methodology fulfills the objective of eliminating loss pancaking for transactions within the GWT (CCA). For transactions involving external control areas, transmission customers are responsible for their external losses. The seams issues related to losses, as described in Appendix A, remain to be resolved.

## Locational Loss Signals

Although the proposed loss methodology is not distance sensitive, it is location dependent. The loss obligations of a transaction depend on the loss factors at its IP and WP, thus leading to locational effect of loss obligations.

## Attributes Summary of the Proposed Loss Methodology

The following table shows how the proposed loss methodology addresses the objectives

Table A1: Attributes of the Proposed Loss Methodology

| Objectives | Proposed methodology | Comments |
| --- | --- | --- |
| Pre-existing rights honored | Yes. But the pre-existing rights are honored by the TOs. | Otherwise, costs shifts are unavoidable. |
| Actual losses reflected (minimize cost shifts) | Strong cost causation to transactions. | It is difficult to have a qualitative measure for this objective, but the additive property and strong locational and timing signals in the proposed methodology will result in more accurate loss recovery. A mechanism is in place to avoid cost shifting between Control Areas and their customers, as well as the cost shifts in real-time operations (see example section). |
| Pancaking eliminated | Yes | Within GWT. |
| Losses certainty | Yes | No true-up is proposed. |
| Additive (Transitive) property | Yes | Reflect actual costs more accurately |
| Easy implementation | Yes | See implementation details that are presented as part of the proposed methodology. |
| Consistency with market operations | Yes | See implementation details that are presented as part of the proposed methodology. |

# Appendix B:  Examples of Loss Reallocation for Day-Ahead Scheduling

Assuming that transmission customers in the day-ahead scheduling process have delivered the loss obligations to Grid West, we illustrate the loss reallocation scheduling method to balance the loss obligations among different control areas in the GWT.

In this example, we further assume there are only three control areas (A, CCA and B) whose configuration is given in Figure B1.

Figure B1: Example Configuration of Control Areas

As shown in Table B1, the losses computed by the power flow model are 300, 200 and 100 MWhs for control areas CCA, B and C, respectively. These calculated losses are the target values for each control area to receive.

In the day-ahead scheduling process, however, the three control areas receive different amount of losses as delivered by the transmission customers.  For this example, CCA received 305 MWhs. Since its target loss is only 300 MWhs, 5 MWhs will be reallocated to other control areas.

Table B1: Example of Loss Reallocation Data

| Control Area | Losses computed by Power Flow | Scheduled loss delivery within each control area |
| --- | --- | --- |
| CCA | 300 | 305 |
| B | 200 | 175 |
| C | 100 | 120 |

Table B2 shows one possibility of the reallocated loss schedule arrangement. Namely, Control Area C delivers the excess 20 MWhs losses to CCA, who in turn delivers 25 MWhs to Control Area B. The loss delivered for each control area will then reach to the target value after loss Reallocation Schedules are accounted for. The new balance condition for control areas are listed in Table B3.

Table B2: Example of Loss Reallocation Schedules

| Interchange schedule | Losses Reallocation Schedule | POD | POR |
| --- | --- | --- | --- |
| CCA to B | 30 | CCA | B |
| C to CCA | 20 | C | CCA |

Table B3: Example of Loss Balance after Loss Reallocation Schedule

| Control Area | Losses computed by Power Flow | Scheduled loss delivery within each control area | Net Loss Reallocation | Final Delivered Losses |
| --- | --- | --- | --- | --- |
| CCA | 300 | 305 | -5 | 300 |
| B | 200 | 175 | 25 | 200 |
| C | 100 | 120 | -20 | 100 |

Each control area will include the reallocated loss schedules in the Net Interchange Scheduling calculation. The end result is that each control area will reach the loss target (assuming power flow models are accurate and no other deviations in the system are present), avoiding any cost shifting between Control Areas and their customers. This will also further minimize the cost shifts in real-time operations.

# Footnotes

CAISO will implement LMP based loss methodology soon.

# Text boxes

C

B

CCA