U.S. DEPARTMENT OF AGRICULTURE
NATURAL RESOURCES CONSERVATION SERVICE
IDAHO

operation and maintenance REQUIREMENTS
subsurface drainage
code 606

Landowner/Operator

Job Location

County					 SWCD				 Farm/Tract No.

Referral No.			Prepared By					 Date

# Operation and Maintenance Items

A properly operated and maintained subsurface drainage system is an asset to the farm.  This drainage system was designed and installed to remove excess subsurface water with a system of buried conduits.  The estimated life span of this installation is at least 10 years.  The life of this system can be assured and usually increased by developing and carrying out a good operation and maintenance program.

This practice will require performance of  periodic maintenance and also require operational items to maintain satisfactory performance.  A good operation and maintenance program includes:

- Maintain the design depth of cover.  All settlement or cracks in the soil should be investigated to determine the cause and immediately repaired.

- Avoid travel by heavy equipment over drainlines when the soil is saturated except at designed crossings.  Avoid travel over pipelines by tillage equipment when the soil is saturated. Limit traffic to sections that were designed for traffic loads.

- Avoid any subsoiling operation that may disturb the drain or its filter and/or envelope materials.

- Remove all foreign debris that hinders system operation.

- Immediately remove any obstructions or blockage of, trash racks, drain inlets or drain outlets.

- Maintain all outlets, rodent guards, inlets and access man-holes in good operating condition.

- Eradicate or otherwise remove all rodents and/or burrowing animals that have or can potentially damage any part of the system.  Immediately repair any damage caused by their activity.

- Immediately repair any vandalism, vehicular or livestock damage to any outlets and appurtenances.

Special operation and maintenance requirements