# A&E expectations Summary

## Scope of work

### Scope of Work

Conceptual scope of work. (Approved by SAIC)

Survey of site utilities, conditions, obstructions, etc.

## 15% Design

### Plans and drawings

Conceptual building plans and/or diagrammatic layouts with options.

### support documentation

Conceptual HVAC, plumbing and electrical equipment requirements and recommendations.

Equipment to be furnished and installed under project

Government furnished.

Program furnished.

Equipment furnished by others.

C.   Site Survey Report

### costs and schedules

Conceptual budget and schedule.

## 35% Design

### Scope of work

Preliminary scope of work. (Approved by SAIC)

### Plans and drawings

Floor plans with preliminary interior and exterior elevations and sections.

Appropriate legends, symbol lists, etc for different disciplines.

Location of existing and new equipment (HVAC, plumbing, electrical, etc).

Preliminary plan for main duct, piping, electrical feeders, etc.

Preliminary HVAC, plumbing, electrical, etc. schedules.

Preliminary Test and Balance reports of existing conditions.

### Specifications

Preliminary table of contents of specification sections to be used.

### support documentation

Preliminary material list with cut sheets, installation instructions and equipment specifications.

Environment impact study.

All Primary code criteria developed and addressed.

### costs and schedules

Preliminary Budget and schedule.

Long lead items identified and specified for order.

## 65% Design

### Scope of work

Revised scope of work. (Approved by SAIC)

### Plans and drawings

Detailed floor plans with door, window, hardware, etc. schedules.

HVAC, plumbing, electrical drawings showing all equipment, services, sizes, quantities, airflow, etc.

Complete HVAC, plumbing, electrical schedules.

### Specifications

Complete Specification.

### support documentation

All design-based calculations are available for review.

Updated material lists with cut sheets, installation instructions and equipment specifications.

### costs and schedules

Budget and schedule addressing commissioning and validation.

## Bid Package (95% Design)

### Scope of work

Final scope of work. (Approved by SAIC)

### Plans and drawings

Final detailed floor plans with door, window, and hardware, etc. schedules.

Final HVAC, plumbing, electrical drawings showing all equipment, services, sizes, quantities, airflow, etc.

Final HVAC, plumbing, electrical schedules.

### Specifications

Final Specifications.

### support documentation

Final design calculations.

Final material lists with cut sheets, installation instructions and equipment specifications.

### costs and schedules

Final budget and schedule commitment to commissioning and validation.

### Bid process

Provide (quantity) of drawings and specifications marked for Bid.

Provide responses and technical support to bidders questions

Provide design clarifications and issue corrections in the form of revised drawings and specifications.

Perform BID assistance, review and analysis.

## Construction and Project management

### general

Provide (quantity) of drawings and specification marked “FOR CONSTRUCTION” complete with all revisions and corrections.

Remove all “Bubbles”, on the drawings, issued for changes during the Bid Process.

Remove all “Highlights”, in the specification, issued for changes during the Bid Phase.

Review subcontractors REDLINE field drawing for completeness and accuracy.

### meeting Attendance

Attend and participate in pre-construction meeting

Attend and participate in bi-weekly project meetings. (As Required)

Assist SAIC in reviewing all contractor schedules.

Assist SAIC in identifying coordination issues.

Assist SAIC in identifying utility outages.

Assist SAIC in coordination of major equipment

### RFI’s, submittals and technical assistance

Provide technical support to RFI’s as necessary during the construction process.

Provide or provide for any inspection, certification or validations as necessary.

Review and approve submittals and shop drawings.

Review potential change orders with subcontractors

Assist SAIC in review of change orders for accuracy, validity and cost.

Provide support for proper operation of systems during the commissioning test phases.

Identify routing and locations of various utilities for connections, etc.

Check equipment, materials and supplies to be utilized for compliance by the subcontractor with the approved plans, specifications and shop drawings.

Review daily reports and project documentation.

Review potential changes and potential design solutions.

Assist SAIC with periodic evaluations of the subcontractors for workmanship, materials, code compliance and quality concerns.

Assist SAIC with the development of the project punch list and verifying completeness of work.

## Project closeout

### general

Project inspection with SAIC.

Verify all systems operating properly

All punch list item resolved.

Review the operation and maintenance manual submission for completeness and adherence to requirements.

Provide all STOP (system turnover packages) documentation.

Attend and participate in SAIC’s “Lessons Learned”.

### DELIVERABLES to SAIC

Provide complete set of Record Drawings on Mylar

Provide drawings and specifications on disk.

As per GS-01

Provide submittal and shop drawing logs.

Provide contractor evaluations and assessments.

# NCI A&E Scope of Work (Phase 1)

## General

### Development Scope of Work

Design objectives, limitations and criteria

Develop initial approximate gross facility areas and space requirements

Determine applicable codes and standards

Determine space relations

Determine site requirements

Determine need for:

Soil Erosion Control Plan

Storm Water Management Plan

Determine fire protection requirements

Determine need for utility conditions

Chilled water

Test and Balance

Electric

Determine operating procedures - Materials Handling

Determine security criteria

Develop a list of equipment to be installed.

Government furnished.

Program furnished.

Equipment furnished by others.

Determine work flow relationship

Determination of existing hazardous materials and abatement

Determine project schedule

Develop a ROM Estimate (+/- 20%)

Determine cGMP requirements

Supply and address SEPP design checklist

### other

Value Engineering Recommendations.

Growth potential

Alternative Designs

Alternative mechanical, electrical, etc. systems

Deviations from the NCI Guide Lines.

## site surveys

### Existing Facilities considerations

Verify basis of design

Identify deficiencies of existing facility

Perform space utilization of existing facility

Take photographs

Take field measurements

Review of existing design data

Analyze existing structural capabilities

Analyze existing mechanical capabilities

Present conditions

Preliminary Test and Balance reports of existing conditions.  Include adjacent areas, which may be affected by construction.

Analyze existing electrical capabilities

Review existing drawings for critical inaccuracies

### Site considerations

Site survey

Encroachments

Boundaries

Contours and Grades

Lines of streets, alleys, and pavements

Adjoining property and structures

Adjacent drainage

Existing building information

Trees

Utility locations above and below grade

### existing Site Utility Considerations

Electrical service and distribution

Water supply and distribution

Site drainage

Wind analysis

Sanitary sewer collection and disposal

Storm water collection and disposal

Central-plant mechanical systems

Chilled Water

Steam

Fire systems and water flow test

Emergency systems

Security

Site illumination

Communications system

Determination of requirements for connections to utilities

## Scope of work Review

### Review

Submit all drawing, plans, documents, etc. for review

Attend review meetings as necessary to answer questions

# NCI A&E 15% Design (Phase 2)

## plans and drawings

### Conceptual Architectural Plans

Conceptual building plans and/or diagrammatic layouts

Show options, Flexibility and expandability

Show requestors work flow

Human

Vehicular

Material flow patterns

General space allocations

Special facilities and equipment

Fire evacuation and other life safety requirements

Adjacency

Buildings

Major utilities

Special Architectural requirements

Block layouts of mechanical spaces

Block layouts of electrical spaces

Block layouts of communications spaces

Room data sheets

### conceptual HVAC plan

Present Conditions

Block load calculations to identify utility requirements

Chilled Water

Steam

Design conditions

Outside air temperature and relative humidity

Inside air temperature and relative humidity.

Air changes

Room pressurization flow direction

Analysis of conceptual HVAC systems

Energy source

Energy conservation

Heating and ventilating

Air conditioning

Special HVAC requirements

### conceptual Fire Protection plan

Present conditions

Requirements for fire protection

Block layouts for fire protection system

Evacuation plans

### Conceptual Plumbing Plan

Locate Existing connections for all required services.

Special Plumbing Requirements

### conceptual Electrical Plan

Locate existing connections and load capacity

Power

Communications

Fire alarm system

Security System

Special Electric Requirements

Requirements for lighting

Requirements for electrical system

Requirements for communications systems

Determine the need for Lightning protection.

### conceptual Direct Digital Control System

Locate existing DDC system

Determine expandability

Locate existing Scientific Alarm System

Determine expandability

## reports

### Site survey report

### Conceptual cost estimate

## 15% design Review

### Review

Submit all drawing, plans, documents, calculations, etc. for review

Attend review meetings as necessary to answer questions

Respond in writing to all comments from Scope of work development phase.

# NCI A&E 35% Design (Phase 2)

## Site/Landscape

All Site plans and drawings shall:

Be a minimum of 35% complete

Be coordinated with similar activities in other disciplines

Address all remarks from 15% design phase

### Site/Landscape Plans - existing

Existing Site Plan

Major landscaping

Major trees and vegetation

Outcroppings

Bodies of water

Fences and barriers

Site features and conditions

Existing contours

Flood zones or hazards

Property lines

Layout leases or easements

Identifiable site constraints

Utility lines

Security features.

Manholes, drains, utility access

Historic or archaeological impact

Paved surfaces

Major streets

Vehicular routes

Curbs

Walks

Pedestrian access routes

Bicycle paths and parking

Parking with handicapped locations

Service areas

Other paved areas

Structures

Existing buildings with roof plans

Adjacent buildings with roof plans

Outbuilding or sheds

Canopies.

Other elements

Nuisance land uses

Special equipment (MRI, laser, etc.)

Convenience nodes (mass transit, drop-off area)

Facilities that may have interruption of any utility

### Site/Landscape Plans - Preliminary

Preliminary Site Plan

Existing site information

Erosion control and storm water management plan

Building footprint

Spot elevations

Key design elements

Major landscaping

Utility lines

Concept plan for drainage and grading.

Erosion control measures.

Storm water management.

Vehicular access routes

Pedestrian access routes

Parking

Handicapped

Motorcycle

Bicycle

Striping

Overall dimensions

Walks

Overall dimensions

Curbs

Curb cuts

Dimensions

Service areas

Preliminary contours

Construction marshaling information

Staging areas

Location for excavated material.

Construction office trailer locations

Utility hook-ups, construction trailer

Indications of phasing

Limits of work

Indication of future surrounding improvements

Alternate schemes (indicate no.)

## Architectural/structural

All Architectural/Structural plans and drawings shall:

Be a minimum of 35% complete

Be coordinated with similar activities in other disciplines

Address all remarks from 15% design phase

### structural Plans

Foundation design.

Systems outlines

Structural floor plans each level

Fixed column reference lines

Show reference lines on all drawings, mechanical, Electrical, etc.

Basic structural system and dimensions

Bearing walls

Major bracing locations

Indicate typical bay

Preliminary sizing of major components

Columns

Indicate major bracing locations

Locate typical bay

Indicate structural framing systems

Roof

Loading

Size structural members

Development of alternatives

Foundation design criteria

Comparative cost analysis of at least two structural systems

Critical coordination clearances

### Architectural Plans

Demolition plan

Preliminary demolition and removal

Preliminary design plan

Code analysis

Floor plan of each level

Identification of existing and new construction

Double line plans with precise wall thicknesses

All programmed rooms

Departmental assignments

Room names

Area names

Signal rooms.

Shafts

Circulation corridors

Stairs

Ladders

Automatic conveyances

Capacity information (no. of beds, seating, etc.)

Floor elevations

Light-wells

Mechanical areas

Equipment rooms

Electrical rooms

Telephone closets

Structural grid

Floor elevations

Significant mechanical equipment

Significant electrical equipment

Overall dimensions

Plan and layout of typical or repetitive spaces

Mechanical rooms

Multilevel spaces

Partition locations

Planning grid

Preliminary equipment and description

Public areas

Relative wall thicknesses

Security features

Service areas

Skylights

Elevators

Number

Type

Size

Vertical transportation

Fire protection and egress plan

List features required by BOCA

List features required by NFPA standard 101

Fire protection

3ire walls

Fire areas

Smoke walls

Smoke zones

Fire protection analysis

Travel distances

Areas of refuge

Preliminary lab module plan

Basic layout

Relation to structure.

### Architectural Roof plan

Major roof elements

Skylights

Hatches

Major mechanical equipment

Major electrical equipment

Elevator machine rooms

### Architectural Interiors

Interior space allocation and utilization plan

Preliminary furniture and equipment

Indicate major materials and systems

Outline of finishes

### Architectural Interior Elevations

Building interior elevations

Typical spaces

Major spaces

Areas of special interest

Areas of special complexity

### Architectural Exterior

Building exterior elevations

Indicate surface materials for all areas

Finish grades

Major floor elevations above and below grade

Significant site features (plantings, water, hills, berms, etc.)

Exposed mechanical and electrical equipment

Sketch elevations or perspectives of buildings

Description of various design features

### Architectural Sections

Building section

Relative thickness of floors

Relative thickness of walls

Major floor elevations

Finish grades

Major room names

Important site easements

Significant mechanical and electrical equipment

Relationship to site contours

Above ceiling zoning analysis

## Mechanical – HVAC

All Mechanical HVAC plans and drawings shall:

Be a minimum of 35% complete

Be coordinated with similar activities in other disciplines

Address all remarks from 15% design phase

### HVAC plans

Locate existing mechanical HVAC equipment

Completed demolition plans

Mechanical plan drawings

Layout of major components in equipment rooms

Approximate equipment sizes and capacities

Required space for equipment

Required chases and clearances

Acoustical and vibration control

Visual impacts

Single line presentation of ductwork systems

Single line HVAC piping mains

Energy conservation measures

Shafts

Preliminary air balance

Laboratory planning modules

Lay out major components

Coordinate locations of mechanical rooms with arch plans

Coordinate locations of vertical shafts with arch plans

Identify connections to major utilities

Steam

Chilled water

Indicate existing intakes and exhausts relationships to

Loading docks

Kitchen

Emergency generator

Other

## Plumbing

All Plumbing plans and drawings shall:

Be a minimum of 35% complete

Be coordinated with similar activities in other disciplines

Address all remarks from 15% design phase

### Plumbing plans

Locate existing Plumbing equipment

Completed demolition plans

Lay out major components

Distribution layouts

Utilities

Piped gas systems

Hot water

Water softening

Plumbing piping mains

Drainage piping mains

Shafts

Plumbing specialties

Pipe materials

Verify locations of vertical shafts with arch plans

Identify connections to major utilities

Steam

Chilled water

Water

Special water

Sewer

Specialty gases (systems or tanks)

Vacuum

Compressed air

## Fire protection

All Fire Protection plans and drawings shall:

Be a minimum of 35% complete

Be coordinated with similar activities in other disciplines

Address all remarks from 15% design phase

### Fire Protection plans

Plan drawings

Existing systems

New fire protection mains

Preliminary equipment layouts

Required space for equipment

Schematic plans with overall fire protection concepts

Show lay out of major components

Locate existing fire protection equipment or systems

## Direct digital control (DDC) system

All DDC plans and drawings shall:

Be a minimum of 35% complete

Be coordinated with similar activities in other disciplines

Address all remarks from 15% design phase

### DDC plans

Plan drawings

HVAC control

Existing systems

Preliminary plans and equipment layouts

Safeties

Freeze Stats (supply air fans)

Fire-mans shutdown switch

Required space for equipment

Scientific Alarming

Existing systems

Preliminary plans and equipment layouts

Required space for equipment

Cardkey alarming

## Electrical

All Electrical plans and drawings shall:

Be a minimum of 35% complete

Be coordinated with similar activities in other disciplines

Address all remarks from 15% design phase

### electrical Plans

Layout of major components of existing system

Power

Lighting

Communications

LAN

Phone

Intercom

Safety

Fire Alarm System

Cardkey Access system

Other

Layout of major components for Preliminary systems

Power

Lighting

Communications

LAN

Phone

Intercom

Safety

Fire Alarm System

Cardkey access system

Other

Single line indication of major feeder routes

Indicate general space requirements

Verify locations of electrical rooms with arch plans

Verify locations of vertical shafts with arch plans

## Specifications

Specifications

Table of contents showing applicable sections to be used for project

## Support documentation

### general

All support documentation shall be:

Be a minimum of 35% complete

Be coordinated with similar activities in other disciplines

Address all remarks from 15% design phase

Catalog of Significant materials, for each section shall include:

Equipment

Material List

Cut sheets

All primary code criteria developed, addressed and documented.

### Site

Existing utilities capacities for:

Electrical

Storm water

Sewer

Steam

Chilled Water

City Water

Etc.

Environmental impact study

### structural

Basis for design report

Existing conditions

Structural systems

Underlying soil bearing capacities

Wind-loading (as required by scope of work)

Vibration requirements and analysis (as required by scope of work)

Summary of structural systems requirements

Fire-resistive construction requirements

Development of conceptual design solutions

### hvac

Basis for design report

Present conditions

Preliminary Test and Balance reports of existing conditions, including adjacent areas, which may be affected by construction.

Energy recovery analysis (as required by scope of work)

Connected load requirements

Wind analysis and exhaust plume study (as required by scope of work)

Life cycle cost analysis (as required by scope of work)

### plumbing

Basis for design report

Present conditions

Requirements for plumbing services

Special requirements

Radioactive waste

Waste recovery

Contaminated Waste

Overall plumbing system concepts.

Analysis of conceptual design solutions

Alternative materials, systems, and equipment.

### Fire Protection

Basis for design report

Alternative materials, systems, and equipment

Calculation of the existing water supply

Hydrostatic flow test

Preliminary sprinkler water supply calculations

Special fire suppression systems

Descriptions

Locations

Justification for use

Integrated fire alarm and security system

Alternative materials, systems, and equipment

Fire protection narrative.

Strategy for meeting life safety codes

List any upgrade requirements to achieve fire protection policy

### electrical

Existing conditions and systems

Description of primary service available

Overall electrical system concept

Analysis of conceptual design solutions

Systems outline Preliminary

Life safety equipment load

Description of emergency power system

Energy budget

Preliminary annual usage (as required by scope of work)

Maximum design loads

Test for compliance with all applicable energy codes

## Reports

### Energy reports

Building envelope analysis

Recommendations for overall building envelope

Review of thermal vapor flow and moisture

Recommendation for vapor barriers

Recommendation for vapor isolation

Energy study

Alternate methods of energy conservation

Associated advantages

Associated disadvantages

Payback calculations

Utility company rebates

Alternate methods of energy recovery

Associated advantages

Associated disadvantages

Payback calculations

Utility company rebates

### Estimated Costs

Cost analysis

Itemized breakdown

Mechanical

Electrical

Architectural

Structural

Equipment

Fire protection

DDC system

Preliminary cost based on general square foot cost

Preliminary cost comparison for each alternative

### Schedules reports

Project schedule diagram with phases of development

Long lead items

Identify long lead items and develop purchase description

Construction schedule in bar chart form

Long lead items

Identify items and delivery dates

Schedulin3g instructions

Phasing instructions

Optimum construction efficiency

### Design Calculations reports

Structural

Preliminary structural calculations

HVAC

Calculations for support of hydronic and hydraulic piping

Indoor design conditions U-value calculations

Outdoor design conditions U-value calculations

Theoretical water vapor migration

Dewpoint and condensation potential

Ductwork sizing in plenums and shafts

Cooling loads

Heating loads

Ventilation loads

Humidification

Plumbing.

Plumbing calculations

Pump sizing

Tank sizing

Fire protection

Sprinkler calculations

Fire alarm requirements

Electrical

Calculations of existing Power, size and available capacity

Primary voltage

Primary voltage transformation

Secondary distribution

Illumination

Emergency and UPS systems

Special grounding

Existing Communications

Shielding

Internal communication systems

Telephone system

Data and LAN systems

Television system

Existing Safety

Fire detection systems

Security systems

Equipment and alarm systems

Existing Other

Special electric systems

## 35% design Review

### Review

Submit all drawing, plans, documents, etc. for review

Attend review meetings as necessary to answer questions

Respond in writing to all comments from 15% Design development phase.

Provide Phasing and commissioning requirements.

### Presentation

Rendered perspective

# NCI A&E Check List 65% Design (Phase 2)

## Site/Landscape

All Site plans and drawings shall:

Be a minimum of 65% complete

Be coordinated with similar activities in other disciplines

Address all remarks from Design Development 35% phase

### site Plans

Complete Site Plan

Existing site information

Dimension major site features

Building footprint

Grade elevations at each building corner

Grade elevations at entrances, and critical areas

First floor elevations

Overall dimensions

Key design elements

Major landscaping

Utility lines

Complete plan for drainage and grading.

Vehicular access routes

Profile and alignment of all new roads

Pedestrian access routes

Parking

All striping

All unique spaces

Dimensions

Walks

Dimensions

Paving joints

Curbs

Dimensions

Service areas

Dimensions

Complete erosion control and storm water management plan

Submit to State Agencies as necessary.

Complete contours

Grading at all altered areas.

Construction marshaling information

Locate and outline staging area.

Locate temporary utility hookup.

Locate Field office (Trailer).

Indications of phasing

Limits of work

Indication of future surrounding improvements

Location of Signage

Location(s) of construction sign

Security measures

Planting and Landscape plan

Location of all trees, shrubs, and lawns

Planting list

Utility plot plan

Existing utilities and their connections.

Sewer

Contaminated waste

Chilled water

Condenser water

Steam

Condensate

Domestic water

Gas

Compressed air

Electric

Communications

Other

## Architectural/structural

All Architectural/Structural plans and drawings shall:

Be a minimum of 65% completed

Be coordinate with similar activities in other disciplines

Address all remarks from Design Development 35% phase

Entire project site on one sheet for reference

Reference and coordination symbols

Enlarged plan bubbles

Section indications

Exterior elevation keys

Interior elevation keys

Wall type indications

All dimensions

Overall

Column grid

Locating dimensions

Partitions

Openings

Equipment

### Architectural Plans

Demolition plan

Floor plans of each level

All room names

Room numbers

Accurate door size, and swings

Safety and protective elements

Fire extinguishers

Fire hoses

Lead linings

Radio frequency shielding

Fixed equipment

Portable equipment

Plumbing fixtures placed and identified

Sinks

Showers

Tubs

Toilets

Toilet stalls

Eyewash

Safety showers

Any item requiring plumbing.

Construction dimension

### Structural Plans

Structural floor plans for each level and roof

Final column reference lines

Structural system dimensions

Size bearing walls

Major bracing locations

Bracing type

Dimensions

Indication of typical bay

Sizing of major components

Column sizes

All framing members sized

Girders

Beams

Joists

Open web joists

Concrete joists

Waffle slab

Space frames

Lintels

Type, extent, and direction of framing

Reference structural items to schedule

Slabs

Structural foundation plans

Size of caissons

Size of footings

Size of foundation walls

Size of grade beams

Structural notes

Column schedules

Correlation with architectural and mechanical features

Critical coordination clearances

### Architectural Roof plan

Materials

Elevations

Slopes

Drains

Other penetrations

### Architectural Reflected ceiling plans

Suspended ceiling grids

Lighting fixtures

Diffusers

Registers

Sprinkler heads

Ceiling-mounted equipment

Exit signs

Ceiling modifications for oversized equipment

Wall-mounted items

Shelving and special features

Bulk heads

Beams and other limiting factors

Ceiling Elevations

### Architectural Enlarged plans

Special spaces

Stairs

### Architectural Interior Elevations

Coordination utility cross-section

Corridors

Mechanical rooms

Utility placements

Utility discipline zones

Coordination with existing structural

Coordination with new structural

### Architectural Interiors

Interior space allocation and utilization plan

Establish the final scope relative to interior construction

Special interior design features

Furnishings

Equipment selections

Materials

Finishes

Colors

Equipment Schedules

Dimensions

NIH number

Quantity

Remarks

Floor mount

Other

Current location

Proposed location

Utilities required

Power requirements

Scientific alarm

Alarm set-points

Emergency generator

### Architectural Exterior Elevations

Building exterior elevations

Indicate all surface materials for all areas

Openings (doors and windows)

Roof pitches

### Architectural Sections and details

Building sections

Set floor to floor dimensions

Establish floor elevations

Set interstitial space dimensions

Construction details

Typical wall sections

At window

At solid wall

At parapets and roofs

At finished grades and footings

Roof, wall and floor penetrations

Construction sections

Typical stairways

Typical elevator shaft and machine room

Utility coordination cross sections

### Structural Sections and details

Details

Reinforcing.

Size

Spacing

Elevation of reinforcing

Type

Depths

Foundation details

Dimensioned foundation details

Typical framing details

Sub-drainage

Water proofing

Damp-proofing

Large openings

Nonstandard beam to column framing

Concrete stairs

Exterior wall construction

Anchors and ties

Elevator shaft details

Vibration isolation details

Large mechanical equipment and anchorage

Typical framing details

Standard structural steel connections

Sump pump systems

Reference to appropriate schedules

## Mechanical – HVAC

All HVAC plans and drawings shall:

Be a minimum of 65% complete

Be coordinated with similar activities in other disciplines

Address all remarks from Design Development 35% phase.

### HVAC plans

Complete design

Mechanical plan drawings

Legend

Plan showing Ducts

Indicate size of all ductwork

Main and branch lines

Indicate insulation/moisture prevention

Fire dampers

Smoke dampers

Balancing dampers

Location of all equipment

Indicate smoke detectors

Within ducts

In air-handling units

Special or complex ductwork

Required space for equipment

Required chases and clearances

Acoustical and vibration control

Wind analysis and laboratory exhaust plume

Walk-in coolers, freezers, cold rooms

Refrigeration systems

Schematic piping

Wiring diagrams

Automatic controls

### hvac Sections

Drawing sections

Through equipment rooms

Typical ductwork

### hvac Details

Details of unique conditions

Details of system connections

Details of system configurations

Exhaust stack detail

Humidifier detail

Coil piping detail

Air handling unit elevation detail

Steam condensate piping

### hvac Schedules

Equipment schedules

Air conditioning

Ventilation units

Refrigeration elements

Cooling towers

Fans

Pumps

Heat recovery system

Humidification

De humidification

Reheat system

Exhaust blowers

VAV terminal

Terminal units

Air balance and Room pressurization

Other

## Mechanical – plumbing

All Plumbing plans and drawings shall:

Be a minimum of 65% complete

Be coordinated with similar activities in other disciplines

Address all remarks from Design Development 35% phase.

### Plumbing plans

Plumbing system plan drawings

Create legends

Show location and size of equipment

Pumps

Tanks

Other

Locate piping

Indicate size of pipes

Plumbing Fixtures

Indicate insulation/moisture prevention

Indicate piping system

Steam

Water

Special water (De-ionized)

Sewer

Specialty gases (systems or tanks)

Chilled water

Condenser water

Hot water

Waste

Vent

Process air (oil free)

Compressed air

Vacuum outlets

Other

Riser diagrams

### plumbing Details

Detailing

Unique conditions

Vibration isolation engineering

One line flow and control diagrams

Chilled water

Condenser water

Hot water

Steam piping (including low quantities)

Air conditioning steam.

Specialty systems

Schedules

## Mechanical – fire protection

All Fire Protection plans and drawings shall:

Be a minimum of 65% complete

Be coordinated with similar activities in other disciplines

Address all remarks from Design Development 35% phase.

### Fire Protection

Plan drawings

Create legends

Indicate existing systems

Show location and size of equipment

Locate piping

Indicate size of pipes

Equipment layouts

Ceiling plan drawings

Sprinkler locations

## Direct digital control (DDC) system

All DDC plans and drawings shall:

Be a minimum of 65% complete

Be coordinated with similar activities in other disciplines

Address all remarks from Design Development 35% phase.

### DDC plans

Plan drawings

HVAC control

New and/or existing systems

Complete plans and equipment layouts

Required space for equipment

Scientific Alarming

New and/or existing systems

Complete plans and equipment layouts

Required space for equipment

Cardkey alarming

### DDC Details

Complete control diagrams with legend

Air Conditioning systems

Exhaust systems

Refrigeration systems

Heating systems

DDC Specifications shall include a complete Sequence of Operations for the HVAC systems

Complete Scientific Alarm system diagrams

Device identification (NIH number)

Cold-box panic alarms

Hi and Low alarm set-points

Utility alarming

Hi, med and low pressure steam

Air compressors and vacuum system

Etc.

Fire-men shutdown switch HVAC equipment.

## Electrical

All Electrical plans and drawings shall:

Be a minimum of 65% complete

Be coordinated with similar activities in other disciplines

Address all remarks from Design Development 35% phase

Complete design.

### electrical Plans

Plan drawings indicating location of

Transformer vaults

Overhead and underground

Power lines

Utility and communication lines

Pad-mount transformer location

Auxiliary power system connection

Engine generator sets

Unit substations

Other major equipment

Floor plans

Room numbers

Room titles

Area functions

Lighting fixtures

Outlets for power

Layouts for special systems

Panel-board locations

Scaled ceiling plans for each space

Location of lighting fixtures

Type of lighting fixtures

Light fixture schedules

Identify special features

Telephone connections

Data connections

LAN locations

Under-floor raceways

Occupancy sensors

Power outlets

Exit lights

Fire alarm/Life safety systems

Signal system devices

Cardkey Security system

In and out card readers

Door alarms

Door strikes

Raceway layout

Finalized layouts of components where space is critical

Laboratory planning module

Electrical site plan details

Service entrance locations

Initial distribution diagram for power

Communications Systems

Signal systems

Details for site electrical work and special systems

Plot plan with primary feeder location showing access to the project

### Electrical schedules

Panel-board schedule

Power circuits

Lighting circuits

### electrical Diagrams

One-line diagrams of electrical system

High-voltage circuitry or transformation required

Emergency power

Fire alarm

Layout of major components in all electrical equipment rooms

Complete sizing of major components

Emergency/UPS.

High-voltage systems

Primary transformers

Emergency generator

Riser diagrams for

Electrical distribution

Auxiliary power distribution

Fire alarm

Card-key Security

All low-voltage systems

## Specifications

Specifications

Complete table of contents

Complete project “marked up” specifications sections

## support documentation

### General

All reports and other documentation will

Be a minimum of 65% complete

Be coordinated with similar activities in each discipline

Address all remarks from the Design Development 35% phase

Catalog of Significant materials, for each section shall include:

Equipment

Material List

Cut sheets

All primary code criteria developed, addressed and documented.

### site

Site construction document design report

Establishment of final scope

Relationships

Form

Size

Appearance

Analysis/description of Complete design solutions

Coordination with USAG

Verify location, sizing and timing of all the required interfaces

Provide schedule confirmation of any utility work

Storm-water management report

Erosion/sediment control report

Review planting plan against master plan

Concept plan for drainage and grading

Demolition requirements

### Architectural

Architectural report

Upgrade basis of design

Area analysis

### Structural

Basis for design report

Coordination with piping systems that require support

Laboratory vibration analysis

Final structural design criteria

Comparative cost analysis of at least two structural systems

Critical coordination clearances

Structural report

Final structural system

Design codes

Identification of design stresses

Allowable foundation bearing capacity

Compaction requirements

Completed computations

Boring logs

Girder diagrams

Live loads

Uniform loads

Concentrated loads

Reactions

Girder material

Stresses

Special condition

Shoring/underpinning of adjacent structures

Schedules

Slabs

Beams

Columns

### hvac

Design report

Sizing calculations for ducts and piping

HVAC load calculations

Calculations for fan pressures and pump heads

Fan and Pump curves

Calculations for required sound attenuation of major fans.

### plumbing

Design report

Equipment selections based on manufacturer's catalog data

Sizing calculations

Piping mains and principal branches

Condensate tank

Feed-water heater capacities

Feed-water storage capacity

Other

Capacity, discharge pressure, and Net Positive Suction Pressure (NPSH)

Condensate transfer pumps

Pressure reducing valves

Safety valves

Oil tanks and pumps

Gas systems

Blow-down systems

Other

Coordination with structural for support of piping

### fire protection

Fire Protection Design Report

Sizes and capacities of major components

### electrical

Electrical design report

Electrical analysis

Lighting calculations

Load calculations

Description of short circuit method

Voltage drop calculations

Establishment of the final scope

Overall building connected load requirements

Agreement from USAG on design development drawings

## Reports

### Energy reports

Review energy study

### estimated Cost

Revised Cost analysis

Itemized breakdown

Mechanical

Electrical

Architectural

Structural

Equipment

Fire protection

DDC system

Other

Revised cost based on general square foot cost

Equipment

Use of owner-furnished material/equipment

Special manufacturing requirements

Delivery requirements

Storage requirements

Manufacturer’s plans and details for installation

### Schedule reports

Revise Project schedule diagram with phases of development

Update long lead items

Delivery dates and status

Revise Construction schedule in bar chart form

Bar chart

Long lead items delivery times

Scheduling

Phasing

Optimum construction efficiency

Occupancy schedule

## Review

### Review

Submit all drawings, plans, documents, etc. for review

Copy of submittal letter to MDE for Erosion Control and/or Storm Water Management plans.

Attend review meetings as necessary to answer questions.

Respond in writing to all comments from Design Development 35% Phase

Return copies of 35% comments, plans, mark-ups, etc.

Provide phasing and commissioning requirements.

### Presentation

Revised renderings

# NCI A&E Bid Package – 95% Design (Phase 2)

## Site/Landscape

All Site documentation will

Be 100% complete, Final Design

Be coordinated with similar activities in other disciplines

Address all remarks from Design Development 65% phase

### site Plans

Vicinity Plan

Existing Site Plan

Site Plan

Existing site information

Dimension major site features

Building footprint

Key design elements

Major landscaping

Utility lines

Final plan for drainage and grading.

Vehicular access routes

Pedestrian access routes

Parking

Walks

Curbs

Service areas

Staking plan

Final contours

Construction marshaling information

Indications of phasing

Limits of work

Indication of future surrounding improvements

Locate signage

Security measures

Planting and Landscape plan

Location of all trees, shrubs, and lawns

Complete planting list

Planting details

Utility plot plan.

Existing utilities and their connections

Final trunk sewers

Water distribution loop

Gas distribution mains

Location arrangement of water treatment equipment

## Architectural/structural

All Architectural/Structural documentation will

Be 100% complete, Final Design

Be coordinated with similar activities in other disciplines

Address all remarks from Design Development 65% phase

### Architectural Plans

Demolition plan

Floor plans of each level

Indication of art work

Signage location

All walls dimensioned

All doors and windows located and sized

Roof plan

Exterior Elevations

Reflected ceiling plans

Floor covering plan

Material type

Graphics

Patterns

Enlarged plans

Fire protection egress plan

Lab modules

Schedules

Door

Window

Finish

Building Sections

Construction Details

### Structural Plans

Structural floor plans for each level and roof

Column reference lines

Final dimensions

All bracing

Sizing of all components

Special provisions for installation or removal of equipment

Structural foundation plans

Locate grades

Locate clean out manholes

Locate trenches

Locate area wells

Locate and dimension all elevator pits

Locate elevation of bottom of footing

Indicate concrete member

Dimensions

Size

Spacing

Reinforcing

Locate finished and unfinished spaces

Pipe sleeves through footings

Pipe sleeves through below grade walls

Caissons

Bottom elevation

Bell size

Elevations

Top of slab elevations.

Top of steel elevations

### Architectural Interiors

Interior space allocation and utilization plan

Interior elevations

Signage location

Signage location

Construction details

Any unique condition not previously covered

Installation plans

Furniture

Equipment.

List of new and reused items

Number

Cross referenced to details

Cross referenced to specifications

### Structural Details

Sections and details

Critical coordination clearances

Details

Clarification of lengths or arrangement of reinforcement

Any condition not previously addressed

Schedules

Schedule for reinforcing bar

Column schedule

Structural notes

Correlation with architectural and mechanical features

## Mechanical

All Mechanical documentation will

Be 100% complete, Final Design

Be coordinated with similar activities in other disciplines

Address all remarks from Design Development 65% phase

### Mechanical Plans

Complete Construction Documents for HVAC, Plumbing, Fire Protection and the Direct Digital Control System

Symbols legend sheet

Plans

Elevations

Sections

Notes

Details

Riser diagrams.

Schedules

Control diagrams

Completed calculations

Sanitary

Invert elevations for sewage system

Legends

Notes

Details

Site plan

Sized equipment

Profiles greater than 60 m

Original grade

Finished grade

Manholes

Inlets

Pipe size

Road and walk crossings

Elevations of other pertinent utilities

## Electrical

All Electrical documentation will

Be 100% complete, Final Design

Be coordinated with similar activities in other disciplines

Address all remarks from Design Development 65% phase

### electrical Drawings

Floor plans

Ceiling plans

Plot plan

Electrical distribution plan

Riser diagrams

One line diagrams with size and fault currents

For all switchgear

For all switchboards

For all panel boards

Feeder sizes

Transformer sizes

## Specifications

Final Specifications

Final table of contents

Final project specifications sections

## support documentation

### General

All reports and other documentation will

Be 100% complete, Final Report

Be coordinated with similar activities in each discipline

Address all remarks from 65% phase

Final Catalog of Significant materials, for each section shall include:

Equipment

Material List

Cut sheets

### site

Final schedules

### Architectural

Final schedules

### Structural

Final schedules

Final design calculations

### mechanical

Final schedules

Final design calculations

Final Fan and Pump curves

### electrical

Final schedules

Final design calculations

### estimated Cost

Final Cost analysis

Itemized breakdown

Mechanical

Electrical

Architectural

Structural

Equipment

Fire protection

DDC system

Other

Final cost based on general square foot cost

Equipment

Use of owner-furnished material/equipment

Special manufacturing requirements

Delivery requirements

Storage requirements

Manufacturer’s plans and details for installation

### Schedule reports

Revise Construction schedule in bar chart form

Bar chart

Long lead items delivery times

Scheduling

Phasing

Optimum construction efficiency

Long lead items

Update Delivery dates and status

Occupancy schedule

## Submittal Requirements

### submissions

Submit all drawings, plans, documents, etc.

Attend review meetings as necessary to answer questions.

Respond in writing to all comments from Design Development 65% Phase

Phasing or commissioning requirements

Provide to SAIC (quantity) copies of drawings and specification marked “FOR BID PURPOSES ONLY”.

Drawings and reproducibles shall be complete with all necessary seals by Registered Architect, Landscape Architect and Professional Engineers responsible for the design

### Presentation

Finished rendering

## Bid process

Assist SAIC as necessary in preparation of:

Invitation for bids

Issue responses to SAIC and bidders questions.

Provide design clarifications

Issue corrections in the form of revised drawings and/or specifications

All changes to drawings shall be “Bubbled”.

All changes to specifications shall be “Highlighted”.

Strike out deleted text

Bold new text

# NCI A&E Construction and Project Management (Phase 3)

## general

Provide (quantity) of drawings and specification marked “FOR CONSTRUCTION” complete with all revisions and corrections.

Remove all “Bubbles”, on the drawings, issued for changes during the Bid Process.

Remove all “Highlights”, “Strike outs” and “Bold” in the specification, issued for changes during the Bid Phase.

Review subcontractors RED-LINE field drawing for completeness and accuracy.

## meeting Attendance

Attend and participate in pre-construction meeting, site tours and kickoff meetings.

Attend and participate in bi-weekly project progress meetings.

Assist SAIC in reviewing all contractor schedules.

Assist SAIC in identifying coordination issues.

Assist SAIC in identifying utility outages.

Assist SAIC in coordination of major equipment

Propose a 2-week progress look-ahead to include coordination issues.

## RFI’s, submittals and technical assistance

Review and approve submittals and shop drawings.

Provide technical support to RFI’s as necessary during the construction process.

Identify routing and locations of various utilities for connections, etc.

Provide or provide for any inspection, certification or validations as necessary.

Check equipment, materials and supplies to be utilized for compliance by the subcontractor with the approved plans, specifications and shop drawings.

Review daily reports and project documentation.

Review potential changes and prepare for potential design solutions.

Review potential change orders with subcontractors

Assist SAIC in review of change orders for accuracy, validity and cost.

Assist SAIC with periodic evaluations of the subcontractors for workmanship, materials, code compliance and quality concerns.

Provide support for proper operation of systems during the commissioning test phases.

Assist SAIC with the development of the project punch list and verifying completeness of work.

# NCI A&E Project Closeout (Phase 4)

## general

Project inspection with SAIC.

Verify all systems operating properly

All punch list item resolved.

Review the operation and maintenance manual submission for completeness and adherence to requirements.

Provide all STOP (system turnover packages) documentation.

Attend and participate in SAIC’s “Lessons Learned”.

### DELIVERABLES to SAIC

Provide complete set of Record Drawings on Mylar.

Provide drawings and specifications on disk.

As per GS-01

Provide RFI and shop drawing logs.