NATURAL RESOURCES CONSERVATION SERVICE

Idaho

CONSTRUCTION SPECIFICATIONS

FOR

GRASSED WATERWAY

______________________________________

(Owner/Operator)

______________________________________

(Project/Title)

GENERAL

Installation shall be in accordance with an approved design and plan.  Details of construction shown on the drawings but not included herein are considered as a part of this specification.

Construction operations shall be carried out in a manner to ensure that erosion and air and water pollution are minimized.  Construction activities shall be in accordance with applicable OSHA regulations.

Plan to construct waterways during years when the majority of fields in the watershed above the waterway are in high residue producing crops such as hay, small grains or cover crops.  Also, plan farming and tillage practices on fields adjacent to waterway that will reduce runoff into the waterway during the vegetative establishment period.

SITE PREPARATION

Trees, brush, stumps, and other obstructions, unless otherwise shown on the drawings, shall be removed and be disposed of so they will not interfere with construction or proper functioning of the waterway or outlet.

EARTHWORK

Waterways and outlets shall be constructed or shaped to equal or slightly exceed the dimensions as shown on the plans or staked in the field.  All earth removed and not needed in construction of the waterway shall be spread or disposed of so it will not interfere with surface water from flowing into the waterway.  The filling of gullies and washes shall be in layers of 4 to 6 inches and compacted to prevent unequal settlement.  Over excavate and cover subsoil

areas exposed during shaping with a 4-inch layer of compacted topsoil.

After shaping, smooth the waterway to allow seedbed preparation without further grading.

When conditions do not permit plant establishment adequate to control erosion prior to the onset of winter, furrows may be plowed on both sides of the waterway to keep runoff from entering the waterway during the first winter.  Side furrows will be filled in once the waterway vegetation is established.

VEGETATIVE SPECIFICATIONS

Seedbed Preparation.  Prepare a clean, firm seedbed.  Final seedbed will be firm enough so a person's heel will sink from 1/2 to 3/4 inch when walking over the waterway.

Time of Seeding.  Plant grasses any time moisture is adequate for plant establishment.  Plant legumes during frost-free periods shown in ADDITIONAL SPECIFICATIONS, and when moisture is adequate for plant establishment.

Seeding mixture.  Use an adapted species or mixture from Table I unless otherwise shown in ADDITIONAL SPECIFICATIONS.  A cover crop may be used when needed to help control erosion.  Cover crops will be planted at a rate of less than eight (8) plants per square foot.

Method of planting.  Drill seed 1/4 to 1/2 inch deep.  The drill spacing will not exceed eight (8) inches.  Seed will be drilled in two passes, the first up and down the waterway, the second in a zigzag or serpentine pattern back and forth across the waterway.  Nurse crops will be drilled in a separate seeding operation.

Fertilizer.  Where annual precipitation exceeds 14 inches, fertilize with 20 pounds Nitrogen and 20 pounds Phosphorus per acre at planting.

Mulching.  Unless otherwise specified mulching shall be applied as follows:

Material       Minimum Amount to Apply

Straw	                   3 tons/ac

Hay	                   3 tons/ac

Sawdust                 7 tons/ac

NETTING

After completion of the seeding, erosion control netting shall be installed along the waterway centerline, unless otherwise specified on the drawings or ADDITIONAL SPECIFICATIONS.  The minimum width for the installed netting shall be as shown on the drawings.  The netting may be any commercially available product unless otherwise specified.  The netting shall be anchored on the sides, at splices, and at other locations as per manufacturer recommendations with pins or staples.

MAINTENANCE

After establishment, fertilize and mow as needed to maintain a thick sod.  Perform tillage operation adjacent to the waterway in a manner that will not build dikes or berms or ditches along the edges of the waterway.

ADDITIONAL SPECIFICATIONS