| Name(s) of “Sample” Risk Team Members: R. Backofen, J. Geata,K. Backofen, T. Walsh, N. McIntosh, F. Horn, N. Bernholc | Point Value → Parameter ↓ | 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- | --- | --- |
| Name(s) of Specific Application Risk Team Members: |  |  |  |  |  |  |
| Job Title: Tabletop Paper Folder Operation Job Number or Job Identifier: PG_JRA_TFOLD | Frequency (B) | <once/year | <once/month | <once/week | <once/shift | >once/shift |
| Job Description: Operation of Baum Tabletop folder | Severity (C) | First Aid Only | Medical Treatment | Lost Time | Partial Disability | Death or Permanent Disability |
| Training Procedures List (Optional): Applicable Standard Operating Procedures: | Likelihood (D) | Very Unlikely | Unlikely | Possible | Probable | Multiple |
| Approved by: R.. Backofen Date: 3/21/06 Rev. #: 1 (signature on file in building 197B room 1-101) |  |  |  |  |  |  |
| Stressors (if applicable, please list all) | Reason for Revision (if applicable): | Comments: |

|  |  |  | Before Additional Controls |  | After Additional Controls |  |
| --- | --- | --- | --- | --- | --- | --- |
| Activity | Hazard | Control(s) | Stressor | # of People A | Frequency B | Severity C | Likelihood D | Risk* AxBxCxD | Control(s) Added to Reduce Risk | Stressors | # of People A | Frequency B | Severity C | Likelihood D | Risk* AxBxCxD | % Risk Reduction |
| Loading of stock to be folded into machine | Paper cuts/bruises from paper handling/dropped load | Safety shoes, machine guarding | N | 1 | 3 | 1 | 2 | 6 |  |  |  |  |  |  |  |  |
| Setup of folder Setup of folder (cont.) | Cut, bruise from dropped gate | Proper lifting techniques, safety shoes | N | 1 | 3 | 1 | 1 | 3 | IH ergonomic assessment and operator training | N | 1 | 3 | 1 | 1 | 3 |  |
|  | Cut, bruise, pinch from inadvertent startup of equipment | Machine guarding of power switch | N | 1 | 3 | 1 | 1 | 3 |  |  |  |  |  |  |  |  |
| Operation of folder | Loose clothing, jewelry, hair, caught in moving equipment | Proper clothing, hair clips, machine guarding, area restrictions | N | 1 | 3 | 2 | 2 | 12 |  |  |  |  |  |  |  |  |
|  | Hearing loss from excessive noise | Hearing protection requirement and posting, Noise and Hearing Conservation program, | N | 1 | 3 | 4 | 1 | 12 |  |  |  |  |  |  |  |  |
|  | Struck by item propelled after falling into moving machinery | “No tools” policy, machine guarding | N | 1 | 3 | 4 | 1 | 12 |  |  |  |  |  |  |  |  |
| Unloading folded sheets from machine | Overexertion, strain, dropped load, tripping | Safety shoes, area check prior to operation | N | 1 | 3 | 1 | 1 | 3 |  |  |  |  |  |  |  |  |
| Clearing jammed sheets from folder | Pinch hazard, dropped gate |  | N | 1 | 3 | 1 | 2 | 6 | De-energize equipment prior to attempting to clear jam | N | 1 | 3 | 1 | 1 | 3 | 50% |

| *Risk: | 0 to 20 | 21 to 40 | 41-60 | 61 to 80 | 81 or greater |
| --- | --- | --- | --- | --- | --- |
|  | Negligible | Acceptable | Moderate | Substantial | Intolerable |