SECTION 07611

METAL SHINGLES

PART 1  GENERAL

1.01	SECTION INCLUDES

A.	Preformed metal roofing and flashings.

B.	Miscellaneous trim, flashings, closures, drip flashings and accessories.

C.	Fastening devices.

1.02	RELATED SECTIONS

A.	Section 06100 - Rough Carpentry and sheathing.

B.	Section 07620 - Sheet Metal Flashing and Trim.

1.03	REFERENCES

A.	U. S. General Services Administration, Historic Preservation Technical Procedures, 07313-01 Repairing A Metal Shingle Roof.

B.	ASTM D 226 - Standard Specification for Asphalt-Saturated Organic Felt Used in Roofing and Waterproofing; 1997a.

C.	ASTM D 1970 - Standard Specification for Self-Adhering Polymer Modified Bituminous Sheet Materials Used as Steep Roofing Underlayment for Ice Dam Protection; 2000.

D.	ASTM D 4586 - Standard Specification for Asphalt Roof Cement, Asbestos-Free; 2000.

E.	ASTM A 653/A 653M - Standard Specification for Steel Sheet, Zinc-Coated (Galvanized) or Zinc-Iron Alloy-Coated (Galvannealed) by the Hot-Dip Process; 2000.

F.	Spec Data Sheet - Galvalume Sheet Metal by Bethlehem Corp.

G.	SMACNA (ASMM) - Architectural Sheet Metal Manual; Sheet Metal and Air Conditioning Contractors' National Association; 1993, Fifth Edition.

1.04	ASSEMBLY DESCRIPTION

A.	The roofing assembly includes preformed sheet metal shingles, related accessories, valleys,     hips, ridges, eaves, corners, rakes, build-in rain gutter system and miscellaneous flashing/ attaching devices.

1.05	SUBMITTALS

A.	Submittals must comply with the requirements set forth in Section 01330 - Submittals.

B.	Samples: Submit a sample of each type of roofing shingle showing the shape and finish to match the original tile.

C.	Samples: Submit samples of manufacturer’s standard colors for selection of appropriate color by Contracting Officer.

1.06	QUALITY ASSURANCE

A.	Perform work in accordance with SMACNA Architectural Sheet Metal Manual requirements and standard details, except as otherwise noted.

B.	Installer Qualifications:  Company specializing in performing sheet metal roof installations with minimum five (5) years of experience.

1.07	DELIVERY, STORAGE, AND PROTECTION

A.	Stack material to prevent twisting, bending, or abrasion, and to provide ventilation.

B.	Store shingles in a clean, dry location. Elevate one end to allow moisture to run off.

C.	Shingles with a strippable film must not be stored in the open, exposed to the sun.

D.	Prevent contact with materials which may cause discoloration or staining.

PART 2  PRODUCTS

  - MANUFACTURERS

- W. F. Norman Corp. P.O Box 323, 214 N. Cedar st., Nevada, MO 64772, 800-641-4038 www.wfnorman.com, or approved equal. Note: Metal shingles provide by National Park Service.

2.02	SHEET MATERIALS

A.	New Shingles: Provided by National Park Service

B.	Metal Ridge Cap: Berridge prefinished metal ridge cap, 12 inches wide.

C.	Felt Underlayment: Asphalt-saturated organic roofing felt, unperforated, complying with ASTM D 226, Type II ("No.30").

D.	Adhesive Waterproof Membrane:  Rubberized asphalt sheet bonded to sheet polyethylene, complying with ASTM D 1970, 40 mil total thickness, with strippable treated release paper.

E.	Unfinished metal shall be Grade C Galvalume  ASTM 792-86 AZ-55.

F.	Finish shall be full strength Kynar 500 Fluoropolymer coating, applied by the manufacturer on a continuous coil coating line, with a top side film thickness of 0.70 - 0.90 mil over 0.25 - 0.35 mil prime coat, to provide a total dry film thickness of 0.95 - 1.25 mil. Bottom side shall be coated with primer with a dry film thickness of 0.25 mil. Finish shall conform to all tests for adhesion, flexibility, and longevity as specified by Kynar 500 finish supplier.

G.	Strippable film shall be applied to the top side of the painted coil to protect the finish during fabrication, shipping and field handling. This strippable film must be removed before installation.

2.03	ACCESSORIES

A.	Fasteners:  Galvanized steel, with washers where required.

B.	Nails:  Standard round wire shingle type, of hot-dipped zinc coated steel or copper, of sufficient length to penetrate through roof sheathing or 3/4 inch into roof sheathing or decking. Nails must be compatible with flashing and roofing tiles. Use stainless steel nails over ACQ treated wood materials.

2.04	FABRICATION

A.	Form sections true to shape, accurate in size, square, and free from distortion or defects.

B.	All exposed adjacent flashing shall be of the same material and finish as the roof shingles.

C.	Hem exposed edges on underside 1/2 inch; miter and seam corners.

D.	Shingles to be of overlapping, interlocking design, fastened to solid substrate with hidden roofing nails.

PART 3  EXECUTION

3.01	EXAMINATION

A.	Inspect roof deck to verify deck is clean and smooth, free of depressions, waves, or projections, properly sloped to drains.

B.	Verify deck sheathing is dry.  Verify joints in wood deck are solidly supported and fastened.

D.	Verify roofing termination and base flashings are in place, sealed, and secure.

3.02	PREPARATION

B.	Back paint concealed metal surfaces and surfaces in contact with dissimilar metals with protective backing paint to a minimum dry film thickness of 15 mil.

C.	Place eave edge metal flashings tight with fascia boards.  Weather lap joints 2 inches and seal with plastic cement.  Secure flange with nails spaced 8 inches o/c.

D.	Treat all cut edges of shingles with paint to match shingle finish.

3.03	INSTALLATION – ADHESIVE WATERPROOF MEMBRANE

A.	Install adhesive waterproof membrane on solid sheathing over entire roof .

3.04 UNDERLAYMENT

A.	Install #30 unperforated asphalt saturated roofing felt underlayment over entire roof.

B.	Install horizontally over adhesive waterproof membrane with 6” minimum overlap and 28” endlaps.

C.	Ensure all nail heads are flush with substrate. Nails shall be galvanized roofing nails with coated felt caps.

3.05	INSTALLATION - ROOFING

A.	Carefully remove existing asphalt and or metal roofing.

B.	Comply with shingle manufacturer’s installation instructions and SMACNA standards in order to achieve a watertight installation.

C.	Apply adhesive waterproof membrane and underlayment over entire roof area as noted above.

D.	Install continuous ridge cap in strict accordance with manufacturer’s instructions and in a manner compatible with metal shingles, underlayment and flashing.

E.	Metal Ridge Cap: Install new metal ridge cap as recommended by the metal ridge cap manufacturers. Set ridge cap in a continuous bead of sealant on each side of the ridge.

F.	Install shingles to ensure that horizontal lines are true and level and vertical lines are plumb.

G.	Remove protective strippable film prior to installation of roof shingles.

H.	Attach shingles using manufacturer’s standard clips and fasteners, spaced in accordance with approved shop drawings.

I.	Do not allow shingles or trim to come into contact with dissimilar materials.

J.	Do not allow traffic on completed roof.

K.	Protect installed shingles and trim from damage caused by adjacent construction until completion of installation.

L.	Remove and replace any shingles or components which are damaged beyond successful repair.

3.06  CLEANING

A.	Clean any grease, finger marks or stains from the shingles per manufacturer’s recommendations.

B.	Remove all scrap and construction debris from the site.

END OF SECTION