File Specification for GEOS-5 MERRA Reanalysis Gridded Output

Global Modeling and Assimilation Office

Goddard Space Flight Center, Greenbelt, Maryland

http://gmao.gsfc.nasa.gov

Release Date: tbd

Version 1.0

Latest Revisions: 12/7/2007 1:03:00 PM

Document maintained by Rob Lucchesi (GMAO, SAIC)

Permission to quote from this document should be obtained from the GMAO.

Michele Rienecker

Global Modeling and Assimilation Office

Earth Sciences Division

NASA Goddard Space Flight Center

Greenbelt, Maryland 20771

This page intentionally left blank.

File Specification for GEOS-5 MERRA Reanalysis Gridded Output

Document No. GMAO-100XvX.0

September 21, 2006

Approved by:

__________________________________ __________________________________

Michele Rienecker Date Gi-Kong Kim Date

Head CCB Chair

Global Modeling and Assimilation Office Global Modeling and Assimilation Office

Code 610.1, NASA GSFC Code 610.2, NASA GSFC

REVISION HISTORY

| Version Number | Revision Date | Extent of Changes | Approval Authority |
| --- | --- | --- | --- |
| 1.0 | 03/24/2006 | Baseline |  |
| 2.0 | 04/19/2007 | First version posted for comment on MERRA web site. |  |
| 2.1 | Xx/xx/2007 |  |  |

1. Introduction 	3

2. Format and File Organization 	4

2.1 Dimensions 	5

2.2 Variables 	6

2.3 Global Attributes 	7

ArchivedMetadata.0 character The ECS archive metadata. 	8

3. Instantaneous vs Time-averaged Products 	8

4. Grid Structure 	8

4.1 Horizontal Structure 	8

4.2 Vertical Structure 	9

5. File Naming Conventions 	11

5.1 File Names	11

5.2 Earth Science Data Types (ESDT) Name 	14

6. Summary of MERRA file collections	15

7. Metadata 	17

7.1 EOSDIS Metadata 	17

7.2 CF Metadata 	17

8. Sample Software 	18

8.1 HDF-EOS Example 	18

8.2 HDF (non EOS) Example	20

Appendix A: The IAU procedure 	24

Appendix B: Observational Inputs to MERRA	25

Appendix C: Collection Metadata 	29

Appendix D: Vertical Structure 	32

Appendix E: GEOS-5 data collections 	33

E.1 Time-independent Variables 	33

const_2d_asm_Nx 	33

E.2 Analysis Files 	34

inst6_3d_ana_Nv 	34

inst6_3d_ana_Np	35

E.3 History Files 	36

inst3_3d_asm_Cp 	36

tavg3_3d_cld_Cp	37

tavg3_3d_mst_Cp 	38

tavg3_3d_rad_Cp 	39

tavg3_3d_trb_Cp 	40

tavg3_3d_tdt_Cp	41

tavg3_3d_udt_Cp 	42

tavg3_3d_qdt_Cp 	43

tavg3_3d_odt_Cp 	44

tavg1_2d_slv_Nx 	45

tavg1_2d_flx_Nx 	47

tavg1_2d_rad_Nx 	49

tavg1_2d_lnd_Nx 	51

tavg1_2d_int_Nx 	53

E.4 Chemistry Forcing Files 	55

const_2d_chm_Fx 	55

tavg3_3d_chm_Fv	56

tavg3_3d_chm_Fe	57

tavg3_2d_chm_Fx	58

tavg3_3d_chm_Nv 	59

tavg3_3d_chm_Ne 	60

inst_3d_chm_Ne 	61

Appendix F: Detailed Description of Output Variables 	62

F.1 Three-dimensional Fields 	62

F.2 Two-dimensional Fields 	66

Appendix G: Surface Representation	70

References 	72

Web Resources	73

# 1. Introduction

The Modern Era Retrospective-analysis for Research and Applications (MERRA) is a NASA reanalysis for the satellite era using a major new version of the Goddard Earth Observing System Data Assimilation System Version 5 (GEOS-5). MERRA focuses on historical analyses of the hydrological cycle on a broad range of weather and climate time scales and places the NASA EOS suite of observations in a climate context. It is one of NASA’s deliverables for the Climate Change Science Program (CCSP). MERRA covers the period 1979-2007, with plans to extend the analysis forward in time as resources allow.

MERRA uses the GEOS-5 Data Assimilation System (GEOS-5 DAS), which represents a radical evolution of the system, with the adoption of a joint analysis with the National Centers for Environmental Prediction (NCEP) and of a new set of physics packages for the atmospheric general circulation model (AGCM).  The first choice allows the Global Modeling and Assimilation Office (GMAO) to take advantage of the developments, especially that of radiance assimilation, at NCEP and the Joint Center for Satellite Data Assimilation (JCSDA), and facilitates our own contributions to the operational system.  The second choice allows us to tune the system for both weather and climate applications and to enhance the usefulness of satellite observations.

The new GEOS-5 AGCM uses the finite-volume dynamics (Lin, 2004) integrated with various physics packages under the Earth System Modeling Framework (ESMF) (e.g., Collins et al., 2005) including the Catchment Land Surface Model (CLSM) (e.g., Koster et al., 2000).  The GSI analysis is a new three-dimensional variational (3DVar) analysis applied in grid-point space to facilitate the implementation of anisotropic, inhomogeneous covariances (e.g., Wu et al., 2002;  Derber et al., 2003). In contrast, in the Spectral Statistical Interpolation (SSI) analysis,  used for the NCEP/NCAR Reanalyses, the background error covariances were defined spectrally and were nearly homogeneous around a latitude band. The GSI implementation incorporates a set of recursive filters that produce approximately Gaussian smoothing kernels and isotropic correlation functions.  By superposition of Gaussian kernels with different length scales it is possible to generate non-Gaussian shapes, and generally to implement a large class of flow-dependent inhomogeneous background error covariance models (Purser et al., 2003a, b).

The GEOS-5 DAS is a marked change from the GEOS-4 DAS which was based on the Physical-space Statistical Analysis System (PSAS) coupled to the GEOS-4 model. The GEOS-4 system is documented in Bloom et al. (2005).   Like GEOS-5, GEOS-4 used the finite-volume dynamical core, but integrated in version 3 of the Community Climate Model (CCM3) and version two of the Community Land Model (CLM2).  PSAS assimilated retrievals of satellite data, not radiances, and the analysis was a height-wind analysis.  Like GEOS-5, the background error covariance functions were in grid-point space, but were horizontally-isotropic, compactly-supported spline functions.  The GEOS-4 system assimilated roughly 105 observations per analysis time whereas the GEOS-5 system assimilates over an order of magnitude more – roughly 2  106 observations are actively assimilated each analysis, including about 7.5  105 AIRS radiance data.  The input stream is roughly twice this volume, but because of the large volume, the data are thinned commensurate with the analysis grid to reduce the computational burden.  Data are also rejected from the analysis through quality control procedures designed to detect, for example, the presence of cloud.

To minimize the spurious periodic perturbations of the analysis, MERRA uses the Incremental Analysis Update (IAU) technique developed by Bloom et al. (1996). More details of this procedure are given in Appendix A.

The version of the DAS used for MERRA is GEOS-5.1.1.

Observations used for MERRA are summarized in Appendix B. The data streams assimilated by the GEOS-5 DAS for MERRA are shown in Table B.1; their availability and the source of the data assimilated for MERRA are shown in Table B.2.

The analysis is performed at a horizontal resolution of 2/3 degrees longitude by ½ degree latitude and at 72 levels, extending to 0.01 hPa. Some products, such as the instantaneous analysis fields, are available on the native three-dimensional grid. Hourly two-dimensional diagnostic fields are also available at the native horizontal resolution. Other products are available on a coarser horizontal grid with resolution of 1.25 1.25 degrees or 1  1.25 degrees, the latter for use by the chemistry transport community. These may be on the model’s native vertical grid or at 42 pressure surfaces extending to 0.1 hPa. Surface data, near surface meteorology, selected upper-air levels, and vertically integrated fluxes and budgets are produced at one-hour intervals, which will help the development of offline land and ocean models and data assimilation systems by resolving the diurnal cycle. Monthly mean versions of most of these products will also be available.

This document describes the gridded output files produced by the MERRA reanalysis. These are considerably different from the operational GEOS-5 DAS output. The MERRA data will be available online through the Goddard Earth Sciences (GES) Data and Information Services Center DISC).  The disk cache and interface tools in this Modeling DISC (MDISC) system leverage new DISC capabilities in serving active data archives. More information can be found at http://mdisc.sci.gsfc.nasa.gov. Detailed documentation of the data access procedures can be found at http://gmao.gsfc.nasa.gov.

# 2. Format and File Organization

GEOS-5 files are in HDF-EOS format, which is an extension of the Hierarchical Data Format Version 4 (HDF-4), developed at the National Center for Supercomputing Applications http://www.hdfgroup.org/. HDF-EOS provides additional capabilities over HDF-4, but does not prevent the use of the files as standard HDF-4 files.

Each GEOS-5 file will contain a single HDF-EOS grid, which in turn contains a number of geophysical quantities that we will refer to as “fields” or “variables.” Some files will contain 2-D variables on a longitude-latitude grid, and some files will contain 3-D variables, or a mixture of 2-D and 3-D variables on the same longitude-latitude grid, but with a vertical dimension applicable to all the 3D variables.

The variables are created using the GDdeffield function from the HDF-EOS GD (GriD) API, which stores them as HDF Scientific Data Set (SDS) arrays, so that they can be read with standard HDF routines. In addition to the geophysical variables, the files will have SDS arrays that define dimension scales (or coordinate variables). There will be two distinct scales for each dimension, which will ensure that a wide variety of graphical display tools can interpret the data. In particular, there are dimension scales that adhere to the CF conventions, as well as ones that adhere to the COARDS conventions.

Due to the size of the MERRA archive, all data will be compressed with a GRIB-like method that is invisible to the user. This method does degrade the precision of the data, but every effort has been made to ensure that differences between the product and the original, uncompressed data are not scientifically meaningful. Once the precision has been degraded, the files are written using the standard gzip deflation available in HDF-4.

EOS Core System (ECS) metadata and other information will be stored as global attributes.

## 2.1 Dimensions

GMAO HDF-EOS files will contain two sets of dimension scale (coordinate) information. One set of dimensions is defined using the SDsetdimscale function of the standard HDF SD interface. This set of scales will have an attribute named “units,” set to an appropriate string defined by the CF and COARDS conventions that can be used by applications to identify the dimension. The other set of dimension scales is created using the GDdeffield/GDwritefield functions.

Table 2.1-1. Dimension Variables Contained in GMAO HDF-EOS Files

| Name | Description | Type | units attribute |
| --- | --- | --- | --- |
| XDim:EOSGRID | Longitude | float32 | degrees_east |
| YDim:EOSGRID | Latitude | float32 | degrees_north |
| Height:EOSGRID (3D only) | pressure or layer index | float32 | hPa or layer |
| TIME:EOSGRID | minutes since first time in file | float32 | minutes |
| XDim | Longitude, in degrees east | float64 | N/A |
| YDim | Latitude, in degrees north | float64 | N/A |
| Height (3D only) | pressure or level indices | float64 | N/A |
| Time | seconds since 00:00Z on 1 January 1993 | float64 | N/A |

The 32-bit dimension variables have a "units" attribute that makes them COARDS-compliant, while the 64-bit dimension variables satisfy ECS requirements.

## 2.2 Variables

Variables are stored as SDS arrays, even though they are defined with the HDF-EOS GDdeffield function. As a result, one can use the SD interface of the HDF library to read any variable from the file. The only thing one must know is the sds variable name or short name of the variable and the number of dimensions (the rank). You can quickly list the variables in the file by using common utilities such as ncdump or hdp. Both utilities are distributed from NCSA with the HDF library. In Section 8 we will present sample code for reading one or more data fields from this file. The short names for all variables in all GMAO data products are listed in Appendix E.  A glossary with a brief description of each variable is given in Appendix F.

Each variable will have several useful metadata attributes. Many of these attributes are required by the CF and COARDS conventions, while others are specific for GMAO products. The following table lists required attributes. Other attributes may be included for internal GMAO use and can be ignored.

Table 2.2-1 Metadata attributes associated with each SDS.

| Name | Type | Description |
| --- | --- | --- |
| _FillValue | float32 | Floating-point value used to identify missing data. Will normally be set to 1e15. Required by CF. |
| missing_value | float32 | Same as _FillValue. Required for COARDS backwards compatibility. |
| valid_range | float32, array(2) | This attribute defines the valid range of the variable. The first element is the smallest valid value and the second element is the largest valid value. Required by CF. missing_value |
| long_name | String | Ad hoc description of the variable. Required by COARDS. |
| standard_name | String | Standard description of the variable as defined in CF conventions. (See References). |
| units | String | The units of the variable. Must be a string that can be recognized by UNIDATA's Udunits package. |
| scale_factor | float32 | If variable is packed as 16-bit integers, this is the scale_factor for expanding to floating-point. Currently we do not plan to pack data, thus value will be 1.0 units |
| add_offset | float32 | If variable is packed as 16-bit integers, this is the offset for expanding to floating-point. Currently, we do no plan to pack data, thus value will be 0.0. |

## 2.3 Global Attributes

In addition to SDS arrays containing variables and dimension scales, global metadata is also stored in GMAO HDF-EOS files. Some metadata are required by the CF/COARDS conventions, some are present to meet ECS requirements, and others as a convenience to users of GMAO products. A summary of global attributes present in all MERRA files is shown in Table 2.3-1.

Table 2.3-1 Global metadata attributes associated with each SDS.

| Name | Type | Description |
| --- | --- | --- |
| Conventions | character | Identification of the file convention used, currently “CF-1.0” |
| title | character | Experiment identification: “MERRA” |
| history | character | CVS tag of this release. CVS tags are used internally by the GMAO to designate versions of the system. |
| institution | character | “NASA Global Modeling and Assimilation Office” |
| source | character | CFIO Version (CFIO is the GMAO’s IO layer) |
| references | character | GMAO website address |
| comment | character | As required |
| HDFEOSVersion | character | Version of the HDF-EOS library used to create this file. |
| StructMetadata.0 | character | This is the GridStructure metadata that is created by the HDF-EOS library. |
| CoreMetadata.0 | character | The ECS inventory metadata. |
| ArchivedMetadata.0 | character | The ECS archive metadata |

# 3. Instantaneous vs Time-averaged Products

Each file collection listed in Section 6 contains either instantaneous or time-averaged products, but not both.

All instantaneous collections contain fields at synoptic times (00 GMT, 06 GMT, 12 GMT, and 18 GMT). In addition, three-hourly instantaneous collections also include snapshots at mid-synoptic times (03 GMT, 09 GMT, 15 GMT, and 21 GMT).

Time-averaged collections may contain either hourly, three-hourly, monthly, or seasonal means, but not mixtures of these. Each time-averaged collection consists of a continuous sequence of data averaged over the indicated interval and time stamped with the central time of the interval. For hourly data, for example, these times are 00:30 GMT, 01:30 GMT, 02:30 GMT, etc.. Only products consisting exclusively of two-dimensional (horizontal) fields are produced hourly. Three-hourly time-averaged files contain averages over time intervals centered and time stamped at 01:30 GMT, 04:30 GMT, 07:30 GMT, and so on. Monthly files represent averages for the calendar months, accounting for leap years. For monthly means, each file contains a single month.

Each hourly, three-hourly, or six-hourly collection, whether instantaneous or time-averaged, consist of a set of daily files, with the date as part of the filename. For collections of monthly or seasonal means each month or season is in a separate file, and file names are also include a date in the file name.

# 4. Grid Structure

## 4.1 Horizontal Structure

Fields will be produced on three different horizontal grids: the a native grid of the Finite-Volume dynamical core, with a resolution of 2/3 longitude by 1/2 degree latitude, a coarse version of the FV grid, with a resolution of 1.25 longitude by 1 degree latitude,  and a uniform coarse grid, with a resolution of 1.25 by 1.25 degrees.

GEOS-5 native resolution gridded output is on a global horizontal grid, consisting of IMn=540 points in the longitudinal direction and JMn=361 points in the latitudinal direction. The horizontal native grid origin, associated with variables indexed (i=1, j=1) represents a grid point located at (180W, 90S). Latitude and longitude of grid points as a function of their indices (i, j) can be determined by:

Where =2/3 o and  = 1/2o. For example, (i = 271, j = 181) corresponds to a grid point at ().

FV reduced resolution gridded output is used only for the specialized chemistry forcing files (see Appendix E). It is on a global horizontal grid, consisting of IMf=288 points in the longitudinal direction and JMf=181 points in the latitudinal direction. The horizontal native grid origin, associated with variables indexed (i=1,j=1) represents a grid point located at (180W, 90S). Latitude and longitude of grid points as a function of their indices (i, j) can be determined by:

where  = 1.25 and  = 1o.

MERRA reduced resolution gridded output is on a global horizontal grid consisting of IMc=288 points in the longitudinal direction and JMc=144 points in the latitudinal direction. The horizontal coarse grid origin, associated with variables indexed (i=1, j=1), represents a grid point  at (179.375W, 80.375S), so that the Dateline and the South Pole are “edges” of the first grid box. Latitude and longitude as a function of their indices (i, j) for the coarse grid can be determined by:

where = =1.25o.

## 4.2 Vertical Structure

Gridded products will use four different vertical configurations: Horizontal-only (can be vertical averages, single level, or surface values), pressure-level, model-level, or model-edge. Horizontal-only data for a given variable appear as 3-dimensional fields (x, y, time), where multiple times can span multiple files, while pressure-level, model-level, or model-edge data appear as 4-dimensional fields (x, y, z, time). Pressure-level data will be output on the LMp=42 pressure levels shown in Appendix D . The GEOS-5 model layers used for MERRA output are on a terrain-following hybrid sigma-p coordinate. Model-level data will be output on the LM=72 layers shown in Appendix D. The model-edge products contain fields with LMe = LM + 1 levels representing the layer edges. Model-level files will contain the LM-layer 3D variable (DELPijl), the pressure thickness for each layer, as well as the surface pressure (PSij). The pressure at the model top is a fixed constant, PTOP=0.01 hPa. Pressures at model edges should be computed by summing the DELP starting at PTOP. A representative pressure for the layer can then be obtained from these.  In the GEOS-4 eta files, one could compute the pressure on the edges by using the “ak” and “bk” values and the surface pressure. In GEOS-5, the full 3-dimensional pressure variables are explicitly provided through (DELPijl), PTOP, and (PSij). For the MERRA products documented here, all model-level fields are on a hybrid-sigma coordinate, and their vertical location could be obtained from the “ak-bk” relationship as well. But this may change in future GMAO systems. We thus recommend that users rely on the reported 3D pressure distribution, and not use ones computed from the “ak” and “bk”.

Figure 1 is a schematic (not to scale) of the GEOS-5 vertical coordinate system. Note that the indexing in the vertical is top to bottom, i.e., layer 1 is the top layer of the atmosphere, while layer LM is adjacent to the earth’s surface. The same is true for edge variables, with level 1 being the top of the model’s atmosphere (PTOP), and level LM+1 being the surface.

# 5. File Naming Conventions

Each GEOS-5 product file will have a complete file name identified in the EOSDIS metadata as "LocalGranuleID". EOSDIS also requires eight-character abbreviated naming indices for each Earth Science Data Type (ESDT). In MERRA each file collection has a unique ESDT index. The ESDT index convention is described in section 5.2.

## 5.1 File Names

The standard full name for the assimilated GEOS-5 MERRA products will consist of five dot-delimited nodes:

runid.runtype.config.collection.timestamp

The node fields, which vary from file to file, are defined as follows:

runid

All MERRA runs will be identified by MERRASVv , where the numeric qualifiers S and Vv denote the production Stream and the Version numbers.

MERRA will be run in three production Streams, each covering approximately a third of the MERRA period, plus overlaps and spin-up periods. If the stream number is not applicable (the case for ancillary products, such as forecasts), S is set to 0, otherwise it is 1, 2, or 3.

The Version numbers are non-zero when there is more than one version of the dataset. It is usually zero, denoting the original processing.  MERRA will be conducted with a frozen assimilation system, so there should be no updates or patches to the GEOS-5 software. Version changes indicate either that a problem was encountered after product release and a reprocessing was necessary (v), or a period was reprocessed with a modified version of the system for scientific studies (V). For any such reprocessing, we will increment the version number appropriately and this will be documented in the metadata parameter “history.” Information on version differences will also be available at the MERRA web site (http://gmao.gsfc.nasa.gov/research/merra/).

runtype:

The main GEOS-5 MERRA products will be from standard production (prod) runs. Products from other runs or run segments may be made available for specialized analyses.

prod   - Standard product

ovlp  - Overlap product

spnp - Spin-up product

swep – Sweeper/Scout product

rosb  - Reduced observing system product

cers  - CERES observing system product

config:

The GEOS-5 analysis and forecast system can run in different configurations.

assim – Assimilation. Uses a combination of atmospheric data analysis and model forecasting to generate a time-series of global atmospheric quantities.

simul – Simulation. Uses a free-running atmospheric model with some prescribed external forcing, such as sea-surface temperatures.

frcst – Forecasts. Uses a free-running atmospheric model initialized from an analyzed state.

The main configuration used to support MERRA will be assimilation (assim). A long, AMIP-style simulation will also be performed and it will be labeled simul.

collection:

All MERRA data are organized into file collections that contain fields with common characteristics. These collections are used to make the data more accessible for specific purposes. Fields may appear in more than one collection. Collection names are of the form freq_dims_group_HV, where the four attributes are:

freq: time-independent (cnst), instantaneous (instF), or time-average (tavgF), where F indicates the frequency or averaging interval and can be any of the following:

1 = Hourly

3 = 3-Hourly

6 = 6-Hourly

D = Daily

M = Monthly (tavg only)

U = Monthly-Diurnal (tavg only)

S = Seasonal (tavg only)

A = Annual (tavg only)

0 = Not Applicable

dims: 2d for collections with only 2-dimensional fields or 3d for collections with a mix of 2- and 3-dimensional fields.

group:  A three-letter mnemonic for the type of fields in the collection. It is a lowercase version of the group designation used in the ESDT name, as listed in the next section.

HV: Horizontal and Vertical grid.

H can be:

N: Native (2/3 x ½) horizontal resolution

C: Reduced (1.25 x 1.25) horizontal resolution

F: Reduced FV (1.25 x 1) horizontal resolution

V can be:

x: horizontal-only data (surface, single level, etc.) ; dims must be 2D

p: pressure-level data (see Appendix D for levels) ; dims must be 3D

v: model layer centers (see Appendix D ) dims must be 3D

e: model layer edges (see Appendix D ) dims must be 3D

timestamp:

This node defines the date and time associated with the data in the file. It has the form yyyymmdd for either instantaneous or time-averaged daily files, yyyymm for monthly-mean files, or yyyysss for seasonal-mean files.

yyyy - year string (e.g. , "2002")

mm - month string (e.g.., "09" for September)

dd - day of the month string (optional)

sss - season (e.g., DJF) (optional)

EXAMPLE:

MERRA300.prod.assim.tavg3_3d_tdt_Cp.20020915.hdf

This is an example of a MERRA filename from the production segment of the original version of the third (most recent) assimilation stream. The data are time-averaged, three-dimensional, temperature tendency products, at reduced horizontal resolution, interpolated to pressure levels. The file contains all data for 15 September 2002.

## 5.2 Earth Science Data Types (ESDT) Name

To accommodate EOSDIS toolkit requirements, all MERRA files are associated with an eight-character ESDT. The ESDT is a short (and rather cryptic) handle for users to access sets of files. In MERRA the ESDT will be used to identify collections and will consist of a compressed version of the collection name of the form:

CTFHVGGG

where

C: Configuration

A = Assimilation

F = Forecast

S = Simulation

T: Time Description:

I = Instantaneous

T = Time-averaged

C = Time-independent

F: Frequency

1 = Hourly

3 = 3-Hourly

6 = 6-Hourly

D = Daily

M = Monthly

S = Seasonal

A = Annual

0 = Not Applicable

H: Horizontal Resolution

N = Native.

F  = Reduced resolution version of model grid

C = Reduced resolution

V: Vertical Location

X = Two-dimensional

P = Pressure

V = model layer center

E = model layer edge

GGG: Group

ANA 	= direct analysis products

ASM 	= assimilated state variables (from the IAU corrector, see Appendix A)

TDT 	= tendencies of temperature

UDT 	= tendencies of eastward and northward wind components

QDT 	= tendencies of specific humidity

ODT 	= tendencies of ozone

LND 	= land surface variables

FLX 	= surface turbulent fluxes and related quantities

OCN 	= ocean surface variables

MST 	= moist processes

CLD 	= clouds

RAD 	= radiation

TRB 	= turbulence

SLV 	= single level

INT 	= vertical integrals

CHM 	= chemistry forcing

# 6. Summary of MERRA file collections

The GEOS-5 MERRA product is organized into the 24 collections listed in Tables 6.1 and 6.2. These are described in detail in Appendix E. The 17 collection in Table 6-1 are the “standard” product intended for most diagnostic work. The seven “chemistry” collections in table 6-2 are more specialized products, intended for forcing off-line chemistry transport models (CTMs). The last three of these, in particular, are for CTMs using the GEOS-5 transport cores.

Collection names follow the conventions described in Section 5. Sizes are given in Gbytes/day and Tbytes for the entire collection. Numbers in parentheses are estimates for the corresponding compressed file.

Table 6-1 List of standard collections

| Name | Description | Size Gbytes/day // Tbytes |
| --- | --- | --- |
| const_2d_asm_Nx | Constant fields |  |
| inst6_3d_ana_Nv | Analyzed fields on model layers | 1.347 (0.455) // 14.8 (5.0) |
| inst6_3d_ana_Np | Analyzed fields at pressure levels | 0.792 (0.290) // 8.71 (3.2) |
| inst3_3d_asm_Cp | Basic assimilated fields from IAU corrector | 0.616 (x.xxx) |
| tavg3_3d_cld_Cp | Upper-air cloud related diagnostics | 0.512 (x.xxx) |
| tavg3_3d_mst_Cp | Upper-air diagnostics from moist processes | 0.900 (x.xxx) |
| tavg3_3d_trb_Cp | Upper-air diagnostics from turbulence | 0.501 (x.xxx) |
| tavg3_3d_rad_Cp | Upper-air diagnostics from radiation | 0.228 (x.xxx) |
| tavg3_3d_tdt_Cp | Upper-air temperature tendencies by process | 0.445 (x.xxx) |
| tavg3_3d_udt_Cp | Upper-air wind tendencies by process | 0.557 (x.xxx) |
| tavg3_3d_qdt_Cp | Upper-air humidity tendencies by process | 0.613 (x.xxx) |
| tavg3_3d_odt_Cp | Upper-air ozone tendencies by process | 0.279 (x.xxx) |
| tavg1_2d_slv_Nx | Single-level atmospheric state variables | 0.546 (0.248) // 6.0 (2.73) |
| tavg1_2d_flx_Nx | Surface turbulent fluxes and related quantities | 0.505 (x.xxx) |
| tavg1_2d_rad_Nx | Surface and TOA radiative fluxes | 0.561 (x.xxx) |
| tavg1_2d_lnd_Nx | Land related surface quantities | x.xxx (x.xxx) |
| tavg1_2d_int_Nx | Vertical integrals | x.xxx (x.xxx) |
| TOTAL |  | x.xxx (x.xxx) |

Table 6-2 List of chemistry collections

| Name | Description | Size (Gbytes) |
| --- | --- | --- |
| const_2d_chm_Fx | 2-D invariants on chemistry grid | x.xxx (x.xxx) |
| tavg3_3d_chm_Fv | Chemistry related 3-D at model layer centers | x.xxx (x.xxx) |
| tavg3_3d_chm_Fe | Chemistry related 3-D at model layer edges | x.xxx (x.xxx) |
| tavg3_2d_chm_Fx | Chemistry related 2-DSingle-level | x.xxx (x.xxx) |
| tavg3_3d_chm_Nv | Accumulated transport fields at layers | x.xxx (x.xxx) |
| tavg3_3d_chm_Ne | Accumulated transport fields at edges | x.xxx (x.xxx) |
| inst3_3d_chm_Ne | Instantaneous fields for off-line transport | x.xxx (x.xxx) |
| TOTAL CHEM |  | x.xxx (x.xxx) |

# 7. Metadata

GEOS-5 gridded output files will include or be linked to two types of metadata. When using the HDF-EOS library and tools, the EOSDIS metadata will be used. Other utilities such as GrADS will use the CF metadata.

## 7.1 EOSDIS Metadata

The EOSDIS toolkit will only use the EOSDIS metadata. EOSDIS identifies two major types of metadata:, collection and granule.

Collection metadata are stored in a separate index file. This file describes an ESDT and is like a card in a library catalog. Each GMAO data product will have an ESDT description in the EOS Core System that contains its unique collection attributes. Appendix C describes the ESDT collection metadata.

Granule metadata is the "table of contents" information stored on the data file itself. The EOSDIS granule metadata include:

- File name (local granule ID)

- Grid structure

- Number of time stamps stored in the file

- Number of vertical levels for each variable in this file

- Names of variables in this file

- Variable format (32-bit floating point, 16-bit integer, etc.)

- Variable storage dimensions

time, latitude and longitude for 2-d fields

time, latitude, longitude and vertical levels 3-d fields

- "Missing" value for each variable

## 7.2 CF Metadata

When GrADS or FERRET are used to view GEOS-5 gridded data sets, the application will use the CF metadata imbedded in the data products. These metadata will comply with the CF conventions and include the following information:

- Space-time grid information (dimension variables)

- Variable names and descriptions

- Variable units

- "Missing" value for each variable

# 8. Sample Software

The following example illustrates the use of the standard HDF library or the ECS HDF-EOS library to read GEOS-5 products. The program shown below will accept as command line arguments a file name and a field name. It will open the file, read the requested field at the first time, compute an average for this field, and print the result to standard output. There are two versions of this program. The first version uses the HDF-EOS library to read the file. The second version uses the standard HDF library to read the file. Electronic copies of these programs can be obtained from the Operations section of the GMAO web page.

## 8.1 HDF-EOS Example

/****************************************************************************/

/*  This program demonstrates how to read a field from a GMAO HDF-EOS	*/

/*  product using the HDF-EOS library. It will take a file name and 	*/

/*  field name on the command line, read the first time of the given 	*/

/*  field, calculate an average of that time and print the average.	*/

/* 	*/

/*  usage: avg <file name> <field name> 	*/

/*  	*/

/*  Rob Lucchesi 	*/

/*  rlucchesi@GMAO.gsfc.nasa.gov 	*/

/****************************************************************************/

#include "hdf.h"

#include "mfhdf.h"

#include <stdio.h>

main(int argc,char *argv[]) {

int32 sd_id, sds_id, status;

int32 sds_index;

int32 start[4], edges[4], stride[4];

char *fname, *vname;

float32 *data_array;

float32 avg, sum;

int32 i;

int32 file_id, gd_id;

int32 xdim, ydim, zdim, len;

if (argc != 3) {

printf("Usage: avg <filename> <field> \n");

exit (-1);

}

fname = argv[1];

vname = argv[2];

/* Open the file (read-only) */

if ( (file_id = GDopen (fname, DFACC_RDONLY))< 0) {

printf ("Could not open %s\n",fname);

exit(-1);

}

/*  Attach to the EOS grid contained within the file.                                            */

/*  The GMAO uses the generic name "EOSGRID" for the grid in all products. */

if ( (gd_id = GDattach (file_id,"EOSGRID"))< 0) {

printf ("Could not open %s\n",fname);

exit(-1);

}

status = GDget(file_id,xdim,ydim,zdim),

/*  Set positioning arrays to read the entire field at the first time. */

start[0] = 0;

start[1] = 0;

start[2] = 0;

start[3] = 0;

stride[0] = 1;

stride[1] = 1;

stride[2] = 1;

stride[3] = 1;

edges[0] = 1;

edges[1] = zdim;

edges[2] = ydim;

edges[3] = xdim;

len =  xdim*ydim*zdim;

data_array = (float32 *)malloc(len);

/*  Read the data into data_array */

status = GDreadfield (gd_id, vname, start, stride, edges, data_array);

printf ("Read status=%d\n",status);

/*  Calculate and print the average */

sum=0.0;

for (i=0; i<len; i++)  sum += data_array[i];

avg = sum/(float32)len;

printf ("Average of %s in 3 dimensions is=%f\n",vname,avg);

/* Close file. */

status = GDdetach (gd_id);

status = GDclose (file_id);

}

## 8.2 HDF (non EOS) Example

/****************************************************************************/

/* This program demonstrates how to read a field from a GMAO HDF-EOS 	*/

/* product using the HDF library (HDF-EOS not required). It will take 	*/

/* a file name and field name on the command line, read the first time 	*/

/* of the given field, calculate an average of that time and print the average. 	*/

/* 	*/

/* usage: avg <file name> <field name> 	*/

/* 	*/

/* Rob Lucchesi 	*/

/* rlucchesi@GMAO.gsfc.nasa.gov 	*/

/*  	*/

/****************************************************************************/

#include "hdf.h"

#include "mfhdf.h"

#include <stdio.h>

main(int argc,char *argv[]) {

int32 sd_id, sds_id, status;

int32 sds_index;

int32 start[4], edges[4], stride[4];

char *fname, *vname;

float32 *data_array;

float32 avg, sum;

int32 i, xdim, ydim , zdim, len;

if (argc != 3) {

printf("Usage: avg <filename> <field> \n");

exit (-1);

}

fname = argv[1];

vname = argv[2];

/* Open the file (read-only) */

if ( (sd_id = SDstart (fname, DFACC_RDONLY))< 0) {

printf ("Could not open %s\n",fname);

exit(-1);

}

/* Find the index and ID of the SDS for the given variable name and get its dimensions. */

if ( (sds_index = SDnametoindex (sd_id, vname)) < 0) {

printf ("Could not find %s\n",vname);

exit(-1);

}

sds_id = SDselect (sd_id,sds_index);

status = GDget(file_id,xdim,ydim,zdim),

/* Set positioning arrays to read the entire field at the first time. */

start[0] = 0;

start[1] = 0;

start[2] = 0;

start[3] = 0;

stride[0] = 1;

stride[1] = 1;

stride[2] = 1;

stride[3] = 1;

edges[0] = 1;

edges[1] = zdim;

edges[2] = ydim;

edges[3] = xdim;

len =  xdim*ydim*zdim;

data_array = (float32 *)malloc(len);

/* Read the data into data_array */

status = SDreaddata (sds_id, start, stride, edges, (VOIDP) data_array);

printf ("read status=%d\n",status);

/* Calculate and print the average */

sum=0.0;

for (i=0; i<len; i++)  sum += data_array[i];

avg = sum/(float32)len;

printf ("Average of %s in 3 dimensions is=%f\n",vname,avg);

/* Close file. */

status = SDendaccess (sds_id);

# status = SDend (sd_id);

}

# Appendix A: The IAU procedure

The implementation of the Incremental Analysis Update (IAU, Bloom et al., 1996) used for MERRA is summarized in Figure A.1.  Every six hours, at the synoptic times, an analysis is performed using backgrounds at that time, three hours earlier, and three hours later, which incorporates observations during the six-hour period spanned by the three backgrounds. The results of this analysis are the products included in the two analysis collections. The analysis increments (i.e., the difference between the analysis and the corresponding synoptic background) are then divided by a time scale (in MERRA we used 6 hours) to produce an “analysis tendency.”  The model is then “backed-up”, restarting it from its state three hours before the analysis time, and run for six hours, adding in the time-invariant “analysis tendency” in addition to its normal physics tendencies. At that point a restart is created that will be used next time the model is backed-up, and the first background for the next analysis cycle is saved. We refer to this first 6-hour run as the “corrector” segment of the IAU. The run is then continued without an analysis tendency for another six hours, saving the other two backgrounds needed by the next analysis---one at the next synoptic time and another at the end of the six hours. We refer to this 6-hour run as the “predictor” segment of the IAU. The entire cycle is then repeated for subsequent synoptic times. Note that during each of the four daily analysis cycles the model is run for 12 hours---a 6-hour “corrector” followed by a 6-hour “predictor.”

Figure A.1

Except for the analyses themselves, all products from MERRA are produced by the model during the corrector run segment. The sequence of corrector segments (follow the green line in the figure) is a continuous model run, with the extra forcing term from the analysis tendencies. The analysis tendencies do change abruptly every six hours, but state variables are continuous (within the model’s time step) solutions of the equations of motion, albeit with the extra forcing term.

# Appendix B: Observational Inputs to MERRA

Table B.1 Input conventional observations.

| Radiosondes | u, v, T, q, Ps |
| --- | --- |
| PIBAL winds | u, v |
| Wind profiles | u, v |
| Conventional, ASDAR, and MDCARS aircraft reports | u, v, T |
| NEXRAD radar winds | u, v |
| Dropsondes | u, v, T, Ps |
| PAOB | Ps |
| GMS, METEOSAT, cloud drift IR and visible winds | u, v |
| MODIS clear sky and water vapor winds | u, v |
| GOES cloud drift IR winds | u, v |
| GOES water vapor cloud top winds | u, v |
| Surface land observations | Ps |
| Surface ship and buoy observations | u, v, T, q, Ps |
| SSM/I | Rain rate, wind speed |
| TMI | Rain rate |
| QuikSCAT | Wind speed and direction |

Table B.2 Input Satellite Data

| TOVS 1b Radiances | AMSU-A: N15, N16, N18 AMSU-B: N15, N16, N17 MHS: N18 HIRS2: TIROS-N, N6, N7, N8, N9, N10, N11, N12, N14 HIRS3: N16, N17 HIRS4: N18 MSU: TIROS-N, N6, N7, N8, N9, N10, N11, N12, N14 SSU: TIROS-N, N6, N7, N8, N9, N10, N11, N14 |
| --- | --- |
| EOS/Aqua Level 1b Radiances | AIRS (150 channels), AMSU-A |
| SSM/I radiances | DSMP-13, DSMP-14, DSMP-15 (7 channels) |
| GOES sounder TB | GOES-08, GOES-10, GOES-12 Channels 1-18 |
| SBUV2 ozone (Version 8 retrievals) | Nimbus 7, NOAA 9, 11, 14, 16, 17 |

Table 1.2 Conventional data availability and source.

| DATA SOURCE/TYPE | PERIOD | DATA SUPPLIER |
| --- | --- | --- |
| Radiosondes | 1970 - present | NOAA/NCEP |
| PIBAL winds | 1970 - present | NOAA/NCEP |
| Wind profiles | 1992/5/14 - present | UCAR CDAS |
| Conventional, ASDAR, and MDCARS aircraft reports | 1970 - present | NOAA/NCEP |
| Dropsondes | 1970 - present | NOAA/NCEP |
| PAOB | 1978 - present | NCEP CDAS |
| GMS, METEOSAT, cloud drift IR and visible winds | 1977 – present | NOAA/NCEP |
| GOES cloud drift winds | 1997 – present | NOAA/NCEP |
| EOS/Terra/MODIS winds | 2002/7/01 - present | NOAA/NCEP |
| EOS/Aqua/MODIS winds | 2003/9/01 - present | NOAA/NCEP |
| Surface land observations | 1970 - present | NOAA/NCEP |
| Surface ship and buoy observations | 1977 - present | NOAA/NCEP |
| SSM/I rain rate | 1987/7 - present | NASA/GSFC/DAAC |
| SSM/I V6 wind speed | 1987/7 - present | RSS |
| TMI rain rate | 1997/12 - present | NASA/GSFC/DAAC |
| QuikSCAT surface winds | 1999/7 - present | JPL |
| ERS-1 surface winds | 1991/8/5 – 1996/5/21 | CERSAT |
| ERS-2 surface winds | 1996/3/19 – 2001/1/17 | CERSAT |

Table B.4 Satellite data availability and source

| DATA SOURCE/TYPE | PERIOD | DATA SUPPLIER |
| --- | --- | --- |
| TOVS/tn (TIROS N) | 1978/10/30 – 1980/06/01 | NCAR |
| TOVS/na (NOAA 6) | 1979/07/02 – 1983/04/17 | NCAR |
| TOVS/nc (NOAA 7) | 1981/07/11 - 1986/06/01 | NCAR |
| TOVS/ne (NOAA 8) | 1983/04/26 - 1985/01/01 | NCAR |
| TOVS/nf (NOAA 9) | 1985/01/01 - 1988/11/01 | NOAA/NESDIS & NCAR |
| TOVS/ng (NOAA 10) | 1986/11/25 - 1991/09/17 | NOAA/NESDIS & NCAR |
| TOVS/nh (NOAA 11) | 1988/09/02 - 1994/12/31 | NOAA/NESDIS & NCAR |
| TOVS/nd (NOAA 12) | 1991/08/18 - 1997/07/14 | NOAA/NESDIS & NCAR |
| TOVS/nj (NOAA 14) | 1995/01/19 - present | NOAA/NESDIS |
| TOVS/nk (NOAA 15) | 1998/07/01 - present | NOAA/NESDIS |
| TOVS/nl (NOAA 16) | 2001/03/02 - present | NOAA/NESDIS |
| TOVS/nm (NOAA 17) | 2003/03/01 - present | NOAA/NESDIS |
| TOVS/nn (NOAA 18) | 2005/10/05 – present | NOAA/NESDIS |
| EOS/Aqua | 2002/10 - present | NOAA/NESDIS |
| SSM/I V6 (F08) | 1987/7 - 1991/12 | RSS |
| SSM/I V6 (F10) | 1990/12 – 1997/11 | RSS |
| SSM/I V6 (F11) | 1991/12 – 2000/5 | RSS |
| SSM/I V6 (F13) | 1995/5 - present | RSS |
| SSM/I V6 (F14) | 1997/5 - present | RSS |
| SSM/I V6 (F15) | 1999/12 – 2006/8 | RSS |
| GOES sounder TB | 2001/01 - present | NOAA/NCEP |
| SBUV2 ozone (Version 8 retrievals) | 1978/10 - present | NASA/GSFC/Code 613.3 |

# Appendix C: Collection Metadata

GEOS-5 collection metadata will contain the following. To view the ESDTs associated with GMAO products, which include collection metadata, see the GMAO Operations web page: http://gmao.gsfc.nasa.gov/operations.

ECS Collection

Revision Date

Suggested Usage

Single Type Collection

Collection State

Maintenance and Update Frequency

Spatial

Spatial Coverage Type

Bounding Rectangle

West Bounding Coordinate

North Bounding Coordinate

East Bounding Coordinate

South Bounding Coordinate

Altitude System Definition (for 3d files only)

Altitude Datum Name

Altitude Distance Units

Altitude Encoding Method

Altitude Resolution Class

Altitude Resolution

Depth System Definition (land surface files only)

Depth Datum Name

Depth Distance Units

Depth Encoding Method

Depth Resolution Class

Depth Resolution

Geographic Coordinate System

Latitude Resolution

Longitude Resolution

Geographic Coordinate Units

Temporal

Time Type

Date Type

Temporal Range Type

Precision of Seconds

Ends at Present Flag

Range Date Time

Range Beginning Date

Range Beginning Time

Range Ending Date

Range Ending Time

Contact Person

Role

Hours of Service

Contact Job Position

Contact First Name

Contact Middle Name

Contact Last Name

Contact Person Address

Street address

City

State/Province

Postal Code

Country

Telephone

Telephone Container

Telephone Number

Telephone Number Type

Email

Electronic Mail Address

Contact Organization

Role

Hours of Service

Contact Instruction

Contact Organization Name

Contact Organization Address

Street Address

City

State/Province

Postal Code

Country

Organization Telephone Number

Telephone Number

Telephone Number Type

Organizational Email

Electronic Mail Address

Discipline Topic Parameters

ECS Discipline Keyword

ECS Topic Keyword

ECS Term Keyword

ECS Variable Keyword

ECS Parameter Keyword

Temporal Keyword Class

Temporal Keyword

Spatial Keyword Class

Spatial Keyword

Processing Level

Processing Level Description

Processing Level ID

Analysis Source

Analysis Short Name

Analysis Long Name

Analysis Technique

Analysis Type

CSDT Description

Primary CSDT

Additional Attributes

Additional Attribute Data Type

Additional Attribute Description

Additional Attribute Name

Physical Parameter Details

Parameter Units of Measure

Parameter Range

Parameter Value Accuracy

Parameter Value Accuracy Explanation

Parameter Measurement Resolution

Storage Medium Class (filled in by DAAC)

# Appendix D: Vertical Structure

Pressure-level data will be output on the following 42 pressure levels:

Products on the native vertical grid will be output on the following levels. Pressures are nominal for a 1000 hPa surface pressure and refer to the top edge of the layer. Note that the bottom layer has a nominal thickness of 15 hPa.

| Lev | P(hPa) | Lev | P(hPa) | Lev | P(hPa) | Lev | P(hPa) | Lev | P(hPa) | Lev | P(hPa) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0.0100 | 13 | 0.6168 | 25 | 9.2929 | 37 | 78.5123 | 49 | 450.000 | 61 | 820.000 |
| 2 | 0.0200 | 14 | 0.7951 | 26 | 11.2769 | 38 | 92.3657 | 50 | 487.500 | 62 | 835.000 |
| 3 | 0.0327 | 15 | 1.0194 | 27 | 13.6434 | 39 | 108.663 | 51 | 525.000 | 63 | 850.000 |
| 4 | 0.0476 | 16 | 1.3005 | 28 | 16.4571 | 40 | 127.837 | 52 | 562.500 | 64 | 865.000 |
| 5 | 0.0660 | 17 | 1.6508 | 29 | 19.7916 | 41 | 150.393 | 53 | 600.000 | 65 | 880.000 |
| 6 | 0.0893 | 18 | 2.0850 | 30 | 23.7304 | 42 | 176.930 | 54 | 637.500 | 66 | 895.000 |
| 7 | 0.1197 | 19 | 2.6202 | 31 | 28.3678 | 43 | 208.152 | 55 | 675.000 | 67 | 910.000 |
| 8 | 0.1595 | 20 | 3.2764 | 32 | 33.8100 | 44 | 244.875 | 56 | 700.000 | 68 | 925.000 |
| 9 | 0.2113 | 21 | 4.0766 | 33 | 40.1754 | 45 | 288.083 | 57 | 725.000 | 69 | 940.000 |
| 10 | 0.2785 | 22 | 5.0468 | 34 | 47.6439 | 46 | 337.500 | 58 | 750.000 | 70 | 955.000 |
| 11 | 0.3650 | 23 | 6.2168 | 35 | 56.3879 | 47 | 375.000 | 59 | 775.000 | 71 | 970.000 |
| 12 | 0.4758 | 24 | 7.6198 | 36 | 66.6034 | 48 | 412.500 | 60 | 800.000 | 72 | 985.000 |

# Appendix E: GEOS-5 data collections

This section lists the variables in eachh the data collection. More details on the variable definitions may be found in Appendix F. Most variables tabled in this section are hyperlinked to their definitions in Appendix F. In the tables, variable names refer to HDF names, which are uppercase. Sizes refer to the daily files.

## E.1 Time-independent Variables

These are prescribed 2-dimensional fields that do not vary during the reanalysis. They are available as: MERRA000.prod.assim.const_2d_asm_Nx.00000000.hdf at the full resolution.

### const_2d_asm_Nx

ECS short name: 		AC0NXASM

ECS long name: 		MERRA DAS 2d constants,

Characteristics: 		Constant at native resolution

Dimensions: 		longitude: 540, latitude: 361

## E.2 Analysis Collections

These are the fields resulting from the GSI analyses performed at the four synoptic times (states labeled ANALYSIS in Figure A.1). They are produced on the native horizontal grid and on both model levels and pressure levels in the vertical. The data on model levels are the values actually analyzed.

### inst6_3d_ana_Nv

ECS short name: 	AI6NVANA

ECS long name: 	MERRA DAS 3d analyzed state,

Characteristics: 	Instantaneous, on model levels, at native resolution

Dimensions: 	longitude: 540, latitude: 361, levels:  72  (see Appendix D)

Times: 		00, 06, 12, 18 GMT

| Variable Name | Dims | Description | Units |
| --- | --- | --- | --- |
| PS | 2D | Surface pressure | Pa |
| DELP | 3D | Layer pressure thickness | Pa |
| T | 3D | Air temperature | K |
| U | 3D | Eastward wind component | m s-1 |
| V | 3D | Northward wind component | m s-1 |
| QV | 3D | Specific humidity | kg kg-1 |
| O3 | 3D | Ozone mixing ratio | kg kg-1 |

### inst6_3d_ana_Np

ECS short name: 	AI6NPANA

ECS long name: 	MERRA DAS 3d analyzed state on pressure,

Characteristics: 	Instantaneous, on pressure levels, at native resolution

Dimensions: 	longitude: 540, latitude: 361, pressure levels: 42  (see Appendix D)

Times: 		00, 06, 12, 18 GMT ; monthly and seasonal also available.

| Variable Name | Dims | Description | Units |
| --- | --- | --- | --- |
| SLP | 2D | Sea-level pressure | Pa |
| PS | 3D | Surface pressure | Pa |
| H | 3D | Geopotential height | m |
| T | 3D | Air temperature | K |
| U | 3D | Eastward wind component | m s-1 |
| V | 3D | Northward wind component | m s-1 |
| QV | 3D | Specific humidity | kg kg-1 |
| O3 | 3D | Ozone mixing ratio | kg kg-1 |

## E.3 History Collections

These histories are produced from the GCM during the “corrector” segment of the IAU cycle. All collections in this group are at reduced horizontal resolution and 3-D fields are on pressure levels.

### inst3_3d_asm_Cp

ECS short name:	AI3CPASM

ECS long name:	MERRA IAU 3d assimilated state on pressure,

Characteristics: 	Instantaneous, on pressure levels, at reduced resolution

Dimensions: 	longitude: 288, latitude: 144, pressure levels: 42 (see Appendix D)

Times : 		00, 03, 06, 09, 12, 15, 18, 21 GMT

| Variable Name | Dims | Description | Units |
| --- | --- | --- | --- |
| SLP | 2D | Sea-level pressure | Pa |
| PS | 2D | Surface pressure | Pa |
| PHIS | 2D | Surface Geopotential | m2 s-2 |
| H | 3D | Geopotential height | m |
| O3 | 3D | Ozone mixing ratio | kg kg-1 |
| QV | 3D | Specific humidity | kg kg-1 |
| QL | 3D | Cloud liquid water mixing ratio | kg kg-1 |
| QI | 3D | Cloud ice mixing ratio | kg kg-1 |
| RH | 3D | Relative humidity | fraction |
| T | 3D | Air temperature | K |
| U | 3D | Eastward wind component | m s-1 |
| V | 3D | Northward wind component | m s-1 |
| EPV | 3D | Ertel potential vorticity | K m2 kg-1s-1 |
| OMEGA | 3D | Vertical pressure velocity | Pa sec-1 |

### tavg3_3d_cld_Cp

ECS short name: 	AT3CPCLD

ECS long name: 	MERRA IAU 3d cloud diagnostics,

Characteristics: 	Time averaged, on pressure levels, at  reduced resolution

Dimensions: 	longitude: 288, latitude: 144, levels: 42  (see Appendix D)

Times : 		1:30, 4:30, 7:30, 10:30, 13:30, 16:30, 19:30, 22:30 GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| RH | Relative humidity | fraction |
| QLLS | Cloud liquid water mixing ratio – large-scale | kg kg-1 |
| QILS | Cloud ice mixing ratio – large-scale | kg kg-1 |
| QLAN | Cloud liquid water mixing ratio – anvils | kg kg-1 |
| QIAN | Cloud ice mixing ratio – anvils | kg kg-1 |
| QCCU | Cloud condensate mixing ratio – convective updraft | kg kg-1 |
| CFLS | 3-D Cloud fraction – large scale | fraction |
| CFAN | 3-D Cloud fraction – anvils | fraction |
| CFCU | 3-D Cloud fraction – convective | fraction |

### tavg3_3d_mst_Cp

ECS short name: AT3CVMST

ECS long name: 	MERRA IAU 3d moist processes diagnostic,

Characteristics: 	Time averaged, on pressure levels, at reduced resolution

Dimensions: 	longitude: 288, latitude: 144, levels: 42 (see Appendix D)

Times : 		1:30, 4:30, 7:30, 10:30, 13:30, 16:30, 19:30, 22:30 GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| CMFMC | Upward moist convective mass flux | kg m-2 s-1 |
| DQRCU | Precipitation production rate – convective | kg kg-1 s-1 |
| DQRLSAN | Precipitation production rate - large-scale+anvil | kg kg-1 s-1 |
| PFLCU | Downward flux of liquid precipitation – convective | kg m-2 s-1 |
| PFICU | Downward flux of ice precipitation – convective | kg m-2 s-1 |
| PFLLSAN | Downward flux of liquid precip - large-scale+anvil | kg m-2 s-1 |
| PFILSAN | Downward flux of ice precip - large-scale+anvil | kg m-2 s-1 |
| REEVAPCN | Evaporation of precipitating convective condensate | kg kg-1 s-1 |
| REEVAPLSAN | Evaporation of precipitating LS &anvil condensate | kg kg-1 s-1 |

### tavg3_3d_rad_Cp

ECS short name: 	AT3CPRAD

ECS long name: 	MERRA IAU 3d radiation diagnostics,

Characteristics: 	Time averaged, on pressure levels, at reduced resolution

Dimensions: 	longitude: 288, latitude: 144, levels: 42  (see Appendix D)

Times : 		1:30, 4:30, 7:30, 10:30, 13:30, 16:30, 19:30, 22:30 GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| CLOUD | 3-D Cloud fraction | fraction |
| DTDTLWR | T tendency from terrestrial radiation | K s-1 |
| DTDTLWRCLR | T tendency from terrestrial radiation (clear sky) | K s-1 |
| DTDTSWR | T tendency from solar radiation | K s-1 |
| DTDTSWRCLR | T tendtendency from solar radiation (clear sky) | K s-1 |

### tavg3_3d_trb_Cp

ECS short name: 	AT3CPTRB

ECS long name: 	MERRA IAU 3d turbulence diagnostics,

Characteristics: 	Time averaged, on pressure levels, at reduced resolution

Dimensions: 	longitude: 288, latitude: 144, levels: 42  (see Appendix D)

Times : 		1:30, 4:30, 7:30, 10:30, 13:30, 16:30, 19:30, 22:30 GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| KM | Momentum diffusivity | m2 s-1 |
| KMLS | Momentum diffusivity from Louis | m2 s-1 |
| KMLK | Momentum diffusivity from Lock | m2 s-1 |
| KH | Heat (scalar) diffusivity | m2 s-1 |
| KHLS | Heat (scalar) diffusivity from Louis | m2 s-1 |
| KHLK | Heat (scalar) diffusivity from Lock | m2 s-1 |
| KHRAD | Heat (scalar) diffusivity Lock radiative contribution | m2 s-1 |
| KHSFC | Heat (scalar) diffusivity Lock surface contribution | m2 s-1 |
| RI | Richardson Number | Nondimensional |

### tavg3_3d_tdt_Cp

ECS short name: 	AT3CPTDT

ECS long name: 	MERRA IAU 3d temperature tendencies,

Characteristics: 	Time averaged, on pressure levels, at reduced resolution

Dimensions: 	longitude: 288, latitude: 144, levels: 42 (see Appendix D)

Times : 		1:30, 4:30, 7:30, 10:30, 13:30, 16:30, 19:30, 22:30 GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| DTDTRAD | Temperature tendency from radiation | K s-1 |
| DTDTMST | Temperature tendency from moist physics | K s-1 |
| DTDTTRB | Temperature tendency from turbulence | K s-1 |
| DTDTFRI | Temperature tendency from frictional heating | K s-1 |
| DTDTGWD | Temperature tendency from gravity wave drag | K s-1 |
| DTDTTOT | Temperature tendency from physics | K s-1 |
| DTDTDYN | Temperature tendency from dynamics | K s-1 |
| DTDTANA | Temperature tendency from analysis | K s-1 |

### tavg3_3d_udt_Cp

ECS short name: 	AT3CPUDT

ECS long name: 	MERRA IAU 3d eastward wind tendencies,

Characteristics: 	Time averaged, on pressure levels, at reduced resolution

Dimensions: 	longitude: 288, latitude: 144, levels: 42 (see Appendix D)

Times : 		1:30, 4:30, 7:30, 10:30, 13:30, 16:30, 19:30, 22:30 GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| DUDTMST | U-wind tendency from moist physics | m s-2 |
| DUDTTRB | U-wind tendency from turbulence | m s-2 |
| DUDTGWD | U-wind tend from gravity wave drag | m s-2 |
| DUDTDYN | U-wind tendency from dynamics | m s-2 |
| DUDTANA | U-wind tendency from analysis | m s-2 |
| DVDTMST | V-wind tendency from moist physics | m s-2 |
| DVDTTRB | V-wind tendency from turbulence | m s-2 |
| DVDTGWD | V-wind tend from gravity wave drag | m s-2 |
| DVDTDYN | V-wind tendency from dynamics | m s-2 |
| DVDTANA | V-wind tendency from analysis | m s-2 |

### tavg3_3d_qdt_Cp

ECS short name: 	AT3CPQDT

ECS long name: 	MERRA IAU 3d moisture tendencies,

Characteristics: 	Time averaged, on pressure levels, at reduced resolution

Dimensions: 	longitude: 288, latitude: 144, pressure levels: 42 (see Appendix D)

Times : 		1:30, 4:30, 7:30, 10:30, 13:30, 16:30, 19:30, 22:30 GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| DQVDTMST | Water vapor tendency from moist physics | kg kg-1 s-1 |
| DQVDTTRB | Water vapor tendency from turbulence | kg kg-1 s-1 |
| DQVDTCHM | Water vapor tendency from chemistry | kg kg-1 s-1 |
| DQVDTDYN | Water vapor tendency from dynamics | kg kg-1 s-1 |
| DQVDTANA | Water vapor tendency from analysis | kg kg-1 s-1 |
| DQIDTMST | Ice tendency from moist physics | kg kg-1 s-1 |
| DQIDTTRB | Ice tendency from turbulence | kg kg-1 s-1 |
| DQIDTDYN | Ice tendency from dynamics | kg kg-1 s-1 |
| DQLDTMST | Liquid water tendency from moist physics | kg kg-1 s-1 |
| DQLDTTRB | Liquid tendency from turbulence | kg kg-1 s-1 |
| DQLDTDYN | Liquid tendency from dynamics | kg kg-1 s-1 |

### tavg3_3d_odt_Cp

ECS short name: 	AT3CPODT

ECS long name: 	MERRA IAU 3d ozone tendencies,

Characteristics: 	Time averaged, on pressure levels, at reduced resolution

Dimensions: 	longitude: 288, latitude: 144, levels: 42 (see Appendix D)

Times : 		1:30, 4:30, 7:30, 10:30, 13:30, 16:30, 19:30, 22:30 GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| DOXDTMST | Ozone tendency from moist physics | kg kg-1 s-1 |
| DOXDTTRB | Ozone tendency from turbulence | kg kg-1 s-1 |
| DOXDTCHM | Ozone tendency from chemistry | kg kg-1 s-1 |
| DOXDTDYN | Ozone tendency from dynamics | kg kg-1 s-1 |
| DOXDTANA | Ozone tendency from analysis | kg kg-1 s-1 |

### tavg1_2d_slv_Nx

ECS short name: 	AT1NXSLV

ECS long name: 	MERRA IAU 2d atmospheric single-level diagnostics

Characteristics: 	Time averaged, single-level, at native resolution

Dimensions: 	longitude: 540, latitude: 361

Times : 		0:30, 1:30, 2:30, 3:30, 4:30, … GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| SLP | Sea level pressure | Pa |
| PS | Time averaged surface pressure | Pa |
| U850 | Eastward wind at 850 hPa | m s-1 |
| U500 | Eastward wind at 500 hPa | m s-1 |
| U250 | Eastward wind at 250 hPa | m s-1 |
| V850 | Northward wind at 850 hPa | m s-1 |
| V500 | Northward wind at 500 hPa | m s-1 |
| V250 | Northward wind at 250 hPa | m s-1 |
| T850 | Temperature at 850 hPa | K |
| T500 | Temperature at 500 hPa | K |
| T250 | Temperature at 250 hPa | K |
| Q850 | Specific humidity at 850 hPa | kg kg-1 |
| Q500 | Specific humidity at 500 hPa | kg kg-1 |
| Q250 | Specific humidity at 250 hPa | kg kg-1 |
| H850 | Height at 850 hPa | m |
| H500 | Height at 500 hPa | m |
| H250 | Height at 250 hPa | m |
| OMEGA500 | Vertical pressure velocity at 500 hPa | Pa s-1 |
| U10M | Eastward wind at 10 m above displacement height | m s-1 |
| U2M | Eastward wind at 2 m above the displacement height | m s-1 |
| U50M | Eastward wind at 50 m above surface | m s-1 |
| V10M | Northward wind at 10 m above the displacement height | m s-1 |
| V2M | Northward wind at 2 m above the displacement height | m s-1 |
| V50M | Northward wind at 50 m above surface | m s-1 |
| T10M | Temperature at 10 m above the displacement height | K |
| T2M | Temperature at 2 m above the displacement height | K |
| QV10M | Specific humidity at 10 m above the displacement height | kg kg-1 |
| QV2M | Specific humidity at 2 m above the displacement height | kg kg-1 |
| TS | Surface skin temperature | K |
| DISPH | Displacement height | m |
| TROPPV | PV based tropopause pressure | Pa |
| TROPPT | T based tropopause pressure | Pa |
| TROPPB | Blended tropopause pressure | Pa |
| TROPT | Tropopause temperature | K |
| TROPQ | Tropopause specific humidity | kg kg-1 |
| CLDPRS | Cloud-top pressure | Pa |
| CLDTMP | Cloud-top temperature | K |

### tavg1_2d_flx_Nx

ECS short name: AT1NXFLX

ECS long name: 	MERRA IAU 2d surface turbulent flux diagnostics

Characteristics: 	Time averaged, single level, at native resolution

Dimensions: 	longitude: 540, latitude: 361

Times : 		0:30, 1:30, 2:30, 3:30, 4:30, … GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| EFLUX | Latent heat flux (positive upward) | W m-2 |
| EVAP | Surface evaporation | kg m-2 s-1 |
| HFLUX | Sensible heat flux (positive upward) | W m-2 |
| TAUX | Eastward surface wind stress | N m-2 |
| TAUY | Northward surface wind stress | N m-2 |
| TAUGWX | Eastward gravity wave surface stress | N m-2 |
| TAUGWY | Northward gravity wave surface stress | N m-2 |
| PBLH | Planetary boundary layer height | m |
| DISPH | Displacement height | m |
| BSTAR | Surface buoyancy scale | m s-1 |
| USTAR | Surface velocity scale | m s-1 |
| TSTAR | Surface temperature scale | K |
| QSTAR | Surface humidity scale | kg kg-1 |
| RI | Surface Richardson number | nondimensional |
| Z0H | Roughness length, sensible heat | m |
| Z0M | Roughness length, momentum | m |
| HLML | Height of center of lowest model layer | m |
| TLML | Temperature of lowest model layer | K |
| QLML | Specific humidity of lowest model layer | kg kg-1 |
| ULML | Eastward wind of lowest model layer | m s-1 |
| VLML | Northward wind of lowest model layer | m s-1 |
| RHOA | Surface air density | kg m-3 |
| SPEED | Effective surface wind speed | m s-1 |
| CDH | Surface exchange coefficient for heat | kg m-2 s-1 |
| CDQ | Surface exchange coefficient for moisture | kg m-2 s-1 |
| CDM | Surface exchange coefficient for momentum | kg m-2 s-1 |
| CN | Surface neutral drag coefficient | nondimensional |
| TSH | Effective turbulence skin temperature | K |
| QSH | Effective turbulence skin humidity | kg kg-1 |
| PRECANV | Surface precipitation flux from anvils | kg m-2 s-1 |
| PRECCON | Surface precipitation flux from convection | kg m-2 s-1 |
| PRECLSC | Surface precipitation flux from large-scale | kg m-2 s-1 |
| PRECSNO | Surface snowfall flux | kg m-2 s-1 |
| PRECTOT | Total surface precipitation flux | kg m-2 s-1 |
| PGENTOT | Total generation of precipitation | kg m-2 s-1 |

### tavg1_2d_rad_Nx

ECS short name: AT1NXRAD

ECS long name: 	MERRA IAU 2d surface and TOA radiation fluxes

Characteristics: 	Time averaged, single level, at native resolution

Dimensions : 	longitude : 540, latitude : 361

Times : 		0 :30, 1 :30, 2 :30, 3 :30, 4 :30, … GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| EMIS | Surface emissivity | fraction |
| TS | Surface skin temperature | K |
| ALBEDO | Surface albedo | fraction |
| ALBNIRDF | Diffuse beam NIR surface albedo | fraction |
| ALBNIRDR | Direct beam NIR surface albedo | fraction |
| ALBVISDF | Diffuse beam VIS-UV surface albedo | fraction |
| ALBVISDR | Direct beam VIS-UV surface albedo | fraction |
| LWGEM | Emitted longwave at the surface | W m-2 |
| LWGAB | Absorbed longwave at the surface | W m-2 |
| LWGABCLR | Absorbed longwave at the surface with no clouds | W m-2 |
| LWGABCLRCLN | Absorbed longwave at the surface with no clouds or aerosol | W m-2 |
| LWGNT | Net downward longwave flux at the surface | W m-2 |
| LWGNTCLR | Net downward longwave flux at the surface for cloud-free sky | W m-2 |
| LWGNTCLRCLN | Net downward longwave flux at the surface for clear sky | W m-2 |
| LWTUP | Upward longwave flux at top of atmosphere (TOA) | W m-2 |
| LWTUPCLR | Upward longwave flux at TOA assuming clear sky | W m-2 |
| LWTUPCLRCLN | Upward longwave flux at TOA assuming clear clean sky | W m-2 |
| SWTDN | TOA incident shortwave flux | W m-2 |
| SWGDN | Surface incident shortwave flux | W m-2 |
| SWGDNCLR | Surface incident shortwave flux assuming clear sky | W m-2 |
| SWGNT | Surface net downward shortwave flux | W m-2 |
| SWGNTCLR | Surface net downward shortwave flux assuming clear sky | W m-2 |
| SWGNTCLN | Surface net downward shortwave flux assuming clean sky | W m-2 |
| SWGNTCLRCLN | Surface net downward shortwave flux assuming clear clean sky | W m-2 |
| SWTNT | TOA outgoing shortwave flux | W m-2 |
| SWTNTCLR | TOA outgoing shortwave flux assuming clear sky | W m-2 |
| SWTNTCLN | TOA outgoing shortwave flux assuming clean sky | W m-2 |
| SWTNTCLRCLN | TOA outgoing shortwave flux assuming clear clean sky | W m-2 |
| TAUHGH | Optical thickness of high clouds | dimensionless |
| TAULOW | Optical thickness of low clouds | dimensionless |
| TAUMID | Optical thickness of mid-level clouds | dimensionless |
| TAUTOT | Optical thickness of all clouds | dimensionless |
| CLDHGH | High-level (above 400 hPa) cloud fraction | fraction |
| CLDLOW | Low-level (1000-700 hPa) cloud fraction | fraction |
| CLDMID | Mid-level (700-400 hPa) cloud fraction | fraction |
| CLDTOT | Total cloud fraction | fraction |

### tavg1_2d_lnd_Nx

ECS short name: AT1NXLND

ECS long name: 	MERRA IAU 2d land surface diagnostics

Characteristics: 	Time averaged, single level, at native resolution

Dimensions: 	longitude: 540, latitude: 361

Times : 		0:30, 1:30, 2:30, 3:30, 4:30, … GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| GRN | Vegetation greenness fraction | Fraction |
| LAI | Leaf area index | m2 m-2 |
| GWETROOT | Root zone soil wetness | fraction |
| GWETTOP | Top soil layer wetness | fraction |
| TPSNOW | Top snow layer temperature | K |
| TUNST | Surface temperature of unsaturated zone | K |
| TSAT | Surface temperature of saturated zone | K |
| TWLT | Surface temperature of wilted zone | K |
| PRECSNO | Surface snowfall | kg m-2 s-1 |
| PRECTOT | Total surface precipitation | kg m-2 s-1 |
| SNOMAS | Snow mass | kg m-2 |
| SNODP | Snow depth | m |
| EVPSOIL | Bare soil eEvaporation | W m-2 |
| EVPTRNS | Transpiration | W m-2 |
| EVPINTR | Interception loss | W m-2 |
| EVPSBLN | Sublimation | W m-2 |
| RUNOFF | Overland runoff | kg m-2 s-1 |
| BASEFLOW | Baseflow | kg m-2 s-1 |
| SMLAND | Snowmelt | kg m-2 s-1 |
| FRUNST | Fractional unsaturated area | fraction |
| FRSAT | Fractional saturated area | fraction |
| FRSNO | Fractional snow-covered area | fraction |
| FRWLT | Fractional wilting area | fraction |
| PARDF | Surface downward PAR diffuse flux | W m-2 |
| PARDR | Surface downward PAR beam flux | W m-2 |
| SHLAND | Sensible heat flux from land | W m-2 |
| LHLAND | Latent heat flux from land | W m-2 |
| EVLAND | Evaporation from land | kg m-2 s-1 |
| LWLAND | Net downward longwave flux over land | W m-2 |
| SWLAND | Net downward shortwave flux over land | W m-2 |
| GHLAND | Downward heat flux at base of top soil layer | W m-2 |
| TWLAND | Total water store in land reservoirs | kg m-2 |
| TELAND | Energy store in all land reservoirs | J m-2 |
| WCHANGE | Total land water change per unit time | kg m-2 s-1 |
| ECHANGE | Total land energy change per unit time | W m-2 |
| SPLAND | Spurious land energy source | W m-2 |

### tavg1_2d_int_Nx

ECS short name: AT1NXINT

ECS long name: 	MERRA IAU 2d Vertical integrals

Characteristics: 	Time averaged, single level, at native resolution

Dimensions : 	longitude : 540, latitude : 361

Times : 		0 :30, 1 :30, 2 :30, 3 :30, 4 :30, … GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| TO3 | Total column ozone | Dobson |
| TTO3 | Tropospheric total column ozone | Dobson |
| DMDTANA | Vertically integrated atmospheric mass tendency for analysis | kg m-2 s-1 |
| DMDTDYN | Vertically integrated atmospheric mass tendency for dynamics | kg m-2 s-1 |
| DQVDTDYN | Vertically integrated water tendency for dynamics | kg m-2 s-1 |
| DQVDTMST | Vertically integrated water tendency for moist | kg m-2 s-1 |
| DQVDTTRB | Vertically integrated water tendency for turbulence | kg m-2 s-1 |
| DQVDTCHM | Vertically integrated water tendency for chemistry | kg m-2 s-1 |
| DQVDTANA | Vertically integrated water tendency for analysis | kg m-2 s-1 |
| DQLDTDYN | Vertically integrated liquid water tendency for dynamics | kg m-2 s-1 |
| DQLDTMST | Vertically integrated liquid water tendency for moist | kg m-2 s-1 |
| DQIDTDYN | Vertically integrated ice water tendency for dynamics | kg m-2 s-1 |
| DQIDTMST | Vertically integrated ice water tendency for moist | kg m-2 s-1 |
| DOXDTDYN | Vertically integrated total ozone tendency for dynamics | kg m-2 s-1 |
| DOXDTCHM | Vertically integrated total ozone tendency for dynamics | kg m-2 s-1 |
| DOXDTANA | Vertically integrated total ozone tendency for analysis | kg m-2 s-1 |
| DKEDTDYN | Vertically integrated kinetic energy tendency for dynamics | W m-2 |
| DPEDTDYN | Vertically integrated cpT tendency for dynamics | W m-2 |
| DTEDTDYN | Ps phis tendency for dynamics | W m-2 |
| DKEDTPHY | Vertically integrated kinetic energy tendency for physics | W m-2 |
| DPEDTPHY | Vertically integrated cpT tendency for physics | W m-2 |
| DTEDTPHY | Ps phis tendency for physics | W m-2 |
| DKEDTANA | Vertically integrated kinetic energy tendency for analysis | W m-2 |
| DPEDTANA | Vertically integrated cpT tendency for analysis | W m-2 |
| DTEDTANA | Ps phis tendency for analysis | W m-2 |
| UFLXCPT | Vertically integrated eastward flux of dry enthalpy | J m-1 s-1 |
| VFLXCPT | Vertically integrated northward flux of dry enthalpy | J m-1 s-1 |
| UFLXPHI | Vertically integrated eastward flux of geopotential | J m-1 s-1 |
| VFLXPHI | Vertically integrated northward flux of geopotential | J m-1 s-1 |
| UFLXKE | Vertically integrated eastward flux of kinetic energy | J m-1 s-1 |
| VFLXKE | Vertically integrated northward flux of kinetic energy | J m-1 s-1 |
| UFLXQV | Vertically integrated eastward flux of specific humidity | kg m-1 s-1 |
| VFLXQV | Vertically integrated northward flux of specific humidity | kg m-1 s-1 |
| UFLXQL | Vertically integrated eastward flux of liquid condensate | kg m-1 s-1 |
| VFLXQL | Vertically integrated northward flux of liquid condensate | kg m-1 s-1 |
| UFLXQI | Vertically integrated eastward flux of ice condensate | kg m-1 s-1 |
| VFLXQI | Vertically integrated northward flux of ice condensate | kg m-1 s-1 |
| CONVCPT | Vertically integrated convergence of dry enthalpy | W m-2 |
| CONVPHI | Vertically integrated convergence of geopotential | W m-2 |
| CONVKE | Vertically integrated convergence of kinetic energy | W m-2 |
| KEGEN | Vertically integrated generation of kinetic energy | W m-2 |
| KEGWD |  |  |
| KERAY |  |  |
| KEBKG |  |  |
| KEORO |  |  |
| KETRB |  |  |
| KESRF |  |  |
| KEINT |  |  |
| KETOP |  |  |
| KEMST |  |  |

### inst1_2d_int_Nx

ECS short name:  AI1NXINT

ECS long name: 	MERRA IAU 2d Vertical integrals

Characteristics: 	Instantaneous, single level, at native resolution

Dimensions: 	longitude: 540, latitude: 361

Times : 		0, 1, 2, 3, 4, …,23 GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| TQV | Total water vapor | kg m-2 |
| TQI | Total cloud ice water | kg m-2 |
| TQL | Total cloud liquid water | kg m-2 |
| TOX | Total column odd oxygen | kg m-2 |
| MASS | Atmospheric mass | kg m-2 |
| KE | Kinetic Energy | J m-2 |
| CPT | Dry enthalpy | J m-2 |

## E.4 Chemistry Forcing Files

These histories are intended for forcing off-line chemistry/aerosol models with the results of the reanalysis. Like other histories, they are produced from the GCM during the “corrector” segment of the IAU cycle. As explained in Appendix A, such results represent a continuous evolution of the model’s state, without the shocks of data insertion and initialization. By doing it in this way, we can provide consistent data at intervals finer than the six-hour analysis interval.  In order to provide the most accurate forcing for off-line calculations, these forcings are produced at 3-hourly intervals and on the native vertical grid using a reduced horizontal resolution version of the model’s horizontal grid. This horizontal grid was chosen for backward compatibility with earlier products.  In addition, the last three streams in this section consist of those fields needed to reproduce as closely as possible the model’s large-scale transport calculation. These are on the 3-dimansional C-grid used by the model and can reproduce, within time truncation, the model’s continuity equation. These native streams are fairly specialized and are intended primarily for users of Goddard’s Chemistry Transport Model or its Finite-Volume advection module.

### const_2d_chm_Fx

ECS short name: 		AC0FXCNS

ECS long name: 		MERRA CHM 2d constants,

Characteristics: 		Constant at reduced FV resolution

Dimensions: 		longitude: 288, latitude: 181

| Variable Name | Description | Units |
| --- | --- | --- |
| PHIS | Surface geopotential | m2 s-2 |
| SGH | Standard deviation of topography for gravity wave drag | m |
| FRLAKE | Fraction of lake type in grid box | fraction |
| FRLAND | Fraction of land type in grid box | fraction |
| FRLANDICE | Fraction of land ice type in grid box | fraction |
| FROCEAN | Fraction of ocean in grid box | fraction |

### tavg3_3d_chm_Fv

ECS short name: AT3FVCHM

ECS long name: 	MERRA IAU 3d Chem On Layers

Characteristics: 	Time averaged, 3D model levels, at reduced FV resolution

Dimensions: 	longitude: 288, latitude: 181, levels: 72 (see Appendix D)

Times : 		1:30, 4:30, 7:30, 10:30, 13:30, 16:30, 19:30, 22:30 GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| DELP | Layer pressure thickness | Pa |
| T | Air temperature | K |
| QV | Specific humidity | kg kg-1 |
| QL | Cloud liquid water mixing ratio | kg kg-1 |
| QI | Cloud ice mixing ratio | kg kg-1 |
| U | Eastward component of wind | m s-1 |
| V | Northward component of wind | M s-1 |
| CFLS | Large-scale cloud fraction | fraction |
| CFAN | Anvil cloud fraction | fraction |
| CFCU | Convective cloud fraction | fraction |
| DQRCON | Precipitation production rate – convective | kg kg-1 s-1 |
| DQRLSC | Precipitation production rate - large-scale | kg kg-1 s-1 |
| DQRANV | Precipitation production rate - anvils | kg kg-1 s-1 |
| DTRAIN | Detrainment cloud mass flux | kg m-2 s-1 |
| TAUCLI | Layer ice cloud optical thickness | nondimensional |
| TAUCLW | Layer liquid cloud optical thickness | nondimensional |

### tavg3_3d_chm_Fe

ECS short name: AT3FECHM

ECS long name: 	MERRA IAU 3d Chem On Layer Edges

Characteristics: 	Time averaged, 3D model levels, at reduced FV  resolution

Dimensions: 	longitude: 288, latitude: 181, levels: 73  (see Appendix D)

Times : 		1:30, 4:30, 7:30, 10:30, 13:30, 16:30, 19:30, 22:30 GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| MFZ | Upward resolved mass flux | kg m-2 s-1 |
| CMFMC | Upward moist convective mass flux | kg m-2 s-1 |
| PFLLSAN | Liquid large-scale plus anvil precipitation | kg m-2 s-1 |
| PFILSAN | Ice large-scale plus anvil precipitation | kg m-2 s-1 |
| PFLCU | Liquid convective precipitation | kg m-2 s-1 |
| PFICU | Ice convective precipitation | kg m-2 s-1 |
| KH | Total scalar diffusivity | m2 s-1 |

### tavg3_2d_chm_Fx

ECS short name: AT3FXCHM

ECS long name: 	MERRA IAU 2d Chem

Characteristics: 	Time averaged, single-level, at reduced  FV resolution

Dimensions: 	longitude: 288, latitude: 181  (see Appendix D)

Times : 		1:30, 4:30, 7:30, 10:30, 13:30, 16:30, 19:30, 22:30 GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| PRECANV | Surface precipitation flux from anvils | kg m-2 s-1 |
| PRECCON | Surface precipitation flux from convection | kg m-2 s-1 |
| PRECLSC | Surface precipitation flux from large-scale | kg m-2 s-1 |
| FRCLS | Fractional area of large-scale precipitation | Fraction |
| FRCAN | Fractional area of anvil precipitation | Fraction |
| FRCCN | Fractional area of convective precipitation | Fraction |
| PRECSNO | Surface snowfall flux | kg m-2 s-1 |
| TS | Surface skin temperature | K |
| QV2M | Specific humidity 2 m above displacement height | kg kg-1 |
| T2M | Temperature 2 m above displacement height | K |
| U10M | Eastward wind 10 m above displacement height | m s-1 |
| V10M | Northward wind 10 m above the displacement height | m s-1 |
| PARDF | Surface downward PAR diffuse flux | W m-2 |
| PARDR | Surface downward PAR beam flux | W m-2 |
| NIRDF | Surface downward NIR diffuse flux | W m-2 |
| NIRDR | Surface downward NIR beam flux | W m-2 |
| LWGNET | Surfece net downward longwave flux | W m-2 |
| SWGNET | Net surface downward shortwave flux | W m-2 |
| LWGDWN | Surface downward longwave flux | W m-2 |
| SWGDWN | Surface downward shortwave flux | W m-2 |
| EVAP | Surface evaporation | kg m-2 s-1 |
| HFLUX | Sensible heat flux (positive upward) | W m-2 |
| GWETROOT | Root zone soil wetness | fraction |
| GWETTOP | Top soil layer wetness | fraction |
| CLDHGH | High-level (above 400 hPa) cloud fraction | fration |
| CLDLOW | Low-level (1000-700 hPa) cloud fraction | fraction |
| CLDMID | Mid-level (700-400 hPa) cloud fraction | fraction |
| CLDTOT | Total cloud fraction | fraction |
| PBLH | Planetary boundary layer height above surface | m |
| PBLTOP | Pressure at PBL top | Pa |
| PS | Surface pressure | Pa |

### tavg3_3d_chm_Nv

ECS short name: AT3NVCHM

ECS long name: 	MERRA IAU 3d Chem On Layers

Characteristics: 	Time averaged, 3D model levels, at native resolution

Dimensions: 	longitude: 540, latitude: 361, model levels: 72 (see Appendix D)

Times : 		1:30, 4:30, 7:30, 10:30, 13:30, 16:30, 19:30, 22:30 GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| MFXC | Eastward mass flux on C-Grid | Pa m s-1 |
| MFYC | Northward mass flux on C-Grid | Pa m s-1 |
| UC | Eastward component of wind on C-Grid | m s-1 |
| VC | Northward component of wind on C-Grid | m s-1 |
| DTRAIN | Detrainment cloud mass flux | kg m-2 s-1 |

### tavg3_3d_chm_Ne

ECS short name: AT3NECHM

ECS long name: 	MERRA IAU 3d Chem On Layer Edges

Characteristics: 	Time averaged, 3D model levels, at native resolution

Dimensions: 	longitude: 540, latitude: 361, model levels: 73 (see Appendix D)

Times : 		1:30, 4:30, 7:30, 10:30, 13:30, 16:30, 19:30, 22:30 GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| MFZ | Upward mass flux on C-Grid | kg m-2 s-1 |
| CMFMC | Upward moist convective mass flux | kg m-2 s-1 |
| KH | Total scalar diffusivity | m2 s-1 |

### inst3_3d_chm_Ne

ECS short name: AT3NECHM

ECS long name: 	MERRA IAU 3d Chem On Layer Edges

Characteristics: 	Instantaneous, 3D model levels, at native resolution

Dimensions: 	longitude: 540, latitude: 361, model levels: 73 (see Appendix D)

Times : 		 0, 3, 6, 9, 12, 15, 18, 21 -GMT

| Variable Name | Description | Units |
| --- | --- | --- |
| PLE | Edge pressures | Pa |

# Appendix F: Detailed Description of Output Variables

## F.1 Three-dimensional Fields

CFLS,CFAN,CFCU: The horizontal fractional cloud cover of each cloud type for each layer. In the vertical, clouds are assumed to fill the layer. The sum of these fractions may exceed one. See CLOUD for the single fraction used in the radiation calculations.

CLOUD: The horizontal fractional cloud cover for each layer. In the vertical, clouds are assumed to fill the layer. This fraction is the combination of the model’s predicted large-scale and convective fractions that is used for radiative purposes. See CLDTOT for a description of how these fractions are overlapped in the radiation calculations.

CMFMC: The total vertical convective mass flux through levels between model layers (edges), in kg m-2 s-1. This is produced by the convection parameterization (RAS) and it includes the mass flux due to all cloud types crossing the level. Constituent transport due to these fluxes can be computed off-line as described in DTRAIN

DELP: Pressure thickness of model layers, in Pa. See PLE. The layer mass is DELP / 9.81 kg m-2.

DDPDTANA: Tendency of the layer’s pressure thickness due to analysis, in Pa s-1.  The GSI analyzes the surface pressure and this is the vertical distribution of that mass increment.

DQRCON, DQRLSC, DQRANV: The layer production rate of precipitating condensate from convective, large-scale, and anvil clouds, per unit horizontal area, in kg m-2 s-1. They include both liquid and frozen precipitating condensate, but not the production of cloud condensates.

DQVDTMST, DQLDTMST, DQIDTMST: Tendency of vapor, liquid and ice water due to moist processes, in kg kg-1 s-1. This includes the effects of the convection parameterization (RAS) and all other effects from the cloud microphysics and large scale and anvil precipitation schemes.

DQVDTDYN: Tendency of water vapor due to resolved dynamics, in kg kg-1 s-1.

DQVDTTRB: Tendency of water vapor due to turbulence, including surface evaporation,
in kg kg-1 s-1.

DTDTANA: The analysis tendency introduced during the corrector segment of the IAU cycle, in K s-1.

DTDTDYN: Temperature tendency due to dynamics, including the spurrious frictional dissipation of kinetic energy by numerical processes, in K s-1.

DTDTFRI: Temperature tendency due to the frictional dissipation of kinetic energy by turbulence, including surface friction, in K s-1. It does not include dissipation from gravity wave drag or the implicit dissipation in the model’s dynamics.

DTDTGWD: Temperature tendency due to the frictional dissipation of kinetic energy by gravity wave drag, in K s-1.

DTDTLWR, DTDTLWRCLR: Temperature tendency due to terrestrial (longwave) radiation for all-sky and clear-sky conditions, in K s-1.

DTDTMST: Temperature tendency due to moist processes, in K s-1.

DTDTSWR, DTDTSWRCLR: Temperature tendency due to solar (shortwave) radiation for all-sky and clear-sky conditions, in K s-1.

DTDTTOT: The total diabatic temperature tendency for the model layers, in K s-1 . It is the same as the sum DTDTFRI+DTDTGWD+DTDTLWR+DTDTSWR+DTDTMST+DTDTTRB, and in the long-term mean should balance DTDTDYN.

DTDTTRB: Temperature tendency due to turbulence, including surface sensible heat flux, but not including the heating due to frictional dissipation (see DTDTFRI), in K s-1. Above the surface it includes the diffusive effects due to the Louis and Lock turbulence schemes (see KH).

DTRAIN:   The total detrained convective mass flux into each model layer, in kg m-2 s-1. This is produced by the convection parameterization (RAS).  The total entrainment mass, E,  due to all clouds crossing a layer can be computed from , where .

DUDTDYN, DVDTDYN: Eastward (zonal) and northward (meridional) wind tendency due to dynamics, in m s-2.

DUDTGWD, DVDTGWD: Eastward (zonal) and northward (meridional) wind tendencies due to gravity wave drag, in m s-2.

DUDTMST, DVDTMST: Eastward (zonal) and northward (meridional) wind tendencies due to moist processes, in m s-2. Currently this represents the “cumulus friction” effect of mixing momentum in a conservative way, using the convective mass fluxes from RAS.

DUDTTRB, DVDTTRB: Eastward (zonal) and northward (meridional) wind tendencies due to turbulent processes, in m s-2. This includes surface friction. Above the surface, it includes the diffusive effects due to the Louis and Lock turbulence schemes (see KM).

H: Geopotential height, in m. It is simply the height, , interpolated linearly in from the model’s edge levels to the desired pressure level. The model’s edge heights are computed using the hydrostatic equation:  PHIS +  cP, where is the difference in at the lower and upper edges of layer , and  is the virtual potential temperature in the layer.

KH, KM : Turbulent diffusivity for heat and other scalars and for momentum, in m2 s -1. This is defined at the layer edges, beginning at the top, where it is zero. At the surface (LM+1) it is set …..….. It includes the diffusive effects due to the Louis and Lock turbulence schemes.

MFX, MFY, MFZ: The eastward and northward pressure weighted velocity components, in Pa m2 s-1, and the vertical component of the large-scale mass flux at the layer edges, in kg m-2 s-1.   MF[X,Y] =  , where  are the velocity components as defined by the dynamical core on the Arakawa C grid and  are the meridional and zonal grid spacings, in meters.. These cannot be computed from UC and VC and the pressures because the time average of the product is done over every step taken by the core, so that the following continuity equation is exactly satisfied.

.

OMEGA: The kinematic vertical pressure velocity estimated by the Finite-Volume dynamics. It is defined for the layers, not the edges. For layer l, it is discretized vertically as , where the pressure is defined at the layer edges and the overbar indicates the average of the layer’s upper and lower edges.

PL: The layer pressure defined as the average of the upper and lower edge pressures, PLE, in Pa (see DELP).

PLE: The time-averaged pressure at the upper edge of a layer. PLE = PS + DELP l. This is the preferred way of obtaining edge pressures in lcv-coordinates, rather than relying on the model’s hybrid-sigma coordinate system (i.e., the AKs Aks and BKsBks), which may change in future releases.

PFLCU, PFICU, PFLLSAN, PFILSAN: Downward flux of precipitating liquid and ice condensate from convective and combined anvil and large-scale clouds, in kg m-2 sec-1.

PV: The Ertel’s potential vorticity, approximated as , in m2 kg-1 sec-1. Here, is the vertical component of relative vorticity,, is the Coriolis parameter, and   is the virtual potential temperature., Note the definition in terms of entropy instead of potential temperature and the neglect of the part associated with the horizontal components of vorticity.

QL, QI: The liquid and ice cloud condensate mixing ratios. These are grid-averaged, not in-cloud, values. They include condensate produced by both large-scale condensation and that detrained from convective clouds. They do not include the condensate within convective updrafts.

QLLS, QILS, QLAN, QIAN, QCCU: The liquid and ice cloud condensate mixing ratios. These are grid-averaged, not in-cloud, values. These are the separate contributions from ice and liquid, anvil and large-scale clouds predicted by the model. QCCU is a diagnostic estimate of the total condensate in convective updrafts; it does not enter any model calculations, but may be useful in comparing with satellite data.

REEVAP: Total re-evaporation of all precipitating condensates, in kg m-2 sec-1.

TAUCLI, TAUCLW: Each layer’s total cloud optical thickness in the visible (0.40 to 0.69 micron band), for ice clouds and liquid water clouds, respectively.

TAUIR: Total (liquid + ice) in-cloud optical thickness in the infrared (540-980 cm-1 band).

## F.2 Two-dimensional Fields

ALBEDO: The time-averaged surface albedo defined as the ratio of the time-averaged incident and reflected fluxes and should satisfy ALBEDO = SWGDWN/(SWGDWN-SWGNET). At night points, this is set to _FillValue.

ALBVISDF, ALBVISDR, ALBNIRDF, ALBNIRDR: The direct (beam) and diffuse albedos for the “visible” (the GCM uses the same albedos for the UV and the PAR spectral regions––0.175 to 0.69 microns) and the “near-infrared” (0.69 to 3.85 microns). These are simply time-averaged surface properties, but are defined only where there was daylight at the point during the averaging interval. They do not correspond to the ratios of time-averaged incident and reflected fluxes.

BSTAR: The bouyancy scale of the surface layer in m s-2. It is defined as , where   is the near-surface air density (RHOA) and   the near-surface air temperature,  is the friction velocity (USTAR), and  is the surface flux of virtual dry static energy in W m-2,   = (HFLUX + EFLUX).

CLDHGH, CLDMID, CLDLOW, CLDTOT: High, middle, low, and total cloudiness. The high, middle, low level values correspond to the three superlayers used in the GEOS-5 solar and terrestrial radiation parameterizations. Clouds within these superlayers are assumed to be maximally overlapped. High clouds are those occuringoccurring above roughly 400 hPa and low clouds are those occuringoccurring below 700 hPa, although the groupings are done ion the model’s terrain following coordinate and so the bounding pressures will differ significantly from these values over high topography. The model assumes that the overlapped between the superlayers is random, and the total cloudiness uses this assumption. The total cloudiness is computed each time the radiation is called, and so its time mean cannot be exactly constructed from the time-mean cloudiness in the three super layers.

CLDPRS, CLDTMP: The cloud-top temperature and pressure of the first cloud “seen” from above at 540-980 cm-1 in the infrared. Clouds are visible if in-cloud (not layer) optical thickness in this band exceeds 0.14, independent of their fractional areal coverage.

DISPH: Surface displacementy height in meters. See the description of the neutral drag coefficient.

DTG: Change in surface temperature during the averaging interval in deg K. This refers to the area-mean surface temperature under each atmospheric column, and so, it may contain contributions from land-, water-, and ice-covered parts of the grid box.

EFLUX: The upward turbulent flux of latent heat flux at the surface, in W m-2. This includes the latent heat relative to liquid of all turbulent moisture fluxes through the surface (see EVAP).

EMIS: The surface emissivity. This is areally averaged over all surface tiles and is constant in time.

EVAP: Evaporation in kg m-2 s-1., a Actually the total turbulent flux of water vapor at the surface, including fluxes from transpiration, sublimation, and surface condensation. The turbulent flux of could cloud condensate (fog) is assumed to be zero. .

FRLAKE, FRLAND, FRLANDICE, FROCEAN: GEOS-5 uses these four primary surface types and these are their fractions under each atmospheric column.

GRN: The “greenness” or fraction of transpiring leaves averaged over the land areas of a grid box. If there are several vegetation tiles within the land part of a grid box, the average is LAI weighted. GRN is set to _FillValue where FRLAND = 0.

GWETROOT, GWETTOP: The degree of saturation or “wetness” in the root-zone (top meter of soil) and top soil layer (top 2 cm). These are defined as the ratio of the volumetric soil moisture to the porosity. These quantities are set to _FillValue where FRLAND = 0. Elsewhere they are time-mean and area-mean values of the ratio over the land part of the grid box.

HFLUX: The upward turbulent sensible heat flux at the surface, in W m-2.

LAI: The areal average of the leaf-area index over all land parts of a grid box. LAI is set to _FillValue where FRLAND = 0.

LWGDWN, LWGDWNCLR: The all-sky and cloud-free fluxes of downwelling terrestrial (longwave) radiation at the surface in W m-2.

LWGNET: The net downward flux of terrestrial (longwave) radiation at the surface in W m-2. This is identical to LWGDWN- LWGUP.

LWGUP: The all-sky upwelling terrestrial (longwave) radiation at the surface, in W m-2. This includes both the surface emmission and the reflection..

LWI: A Land-Water-Ice mask provided for backward compatibility with the GEOS-4 product. It is 1 over continental areas, 0 over open ocean, and 2 over sea-ice covered ocean. Since in GEOS-5 a grid box can be a combination of these, continental areas are arbitrarily defined as those where FRLAND+FRLANDICE>=0.5. The remaining grid boxes are designated as sea-ice if the ice cover exceeds 50%; otherwise they are open (ice-free) ocean.

LWTUP, LWTUPCLR: Outgoing longwave (terrestrial) radiation at the top of the model’s atmosphere (currently 0.01 hPa) for all-sky and clear-sky conditions, in W m-2.

PARDF, PARDR, NIRDR, NIRDF: Incident flux of of diffuse and direct PAR and NIR at the surface, in W m-2. PAR is defined as the solar radiation between 0.4 and 0.69 microns. NIR is the solar near- infrared, defined as the solar radiation between 0.69 and 3.85 microns. These are scaled so that the total solar flux is accounted for in a band from 0.175 to 3.85 microns.

PBLH: Height above the surface of the planetary boundary layer in meters. This is obtained diagnostically at every time step from the heat diffusivity in the model layers. It is defined as the height of the lowest layer in which the diffusivity falls below 2 m2 s-1. Where no layer is above this value, the boundary layer height is set to the height of the surface layer.

PHIS: The surface geopotential, , in m-2 s-2. Here is the height of the surface above sea level, and  m s-2.

PRECANV, PRECLSC, PRECCON: the large-scale precipitation from anvils, the non-anvil large-scale precipitation, and the convective precipitation, in kg m-2 s-1. These include both rainfall and snowfall.

PRECTOT: The total precipitation (PRECANV+PRECLSC+PRECCON) in kg m-2 s-1.

PRECSNO: The “snowfall” includes all frozen precipitation, in kg m-2 s-1.

PS: The surface pressure in Pa. The height at this pressure can be obtained from the surface geopotential PHIS. The total atmospheric mass is PS kg m-2.

QV10M, QV2M: The specific humidity at 10 m and 2m above the displacement height (DISPH) in the surface layer, in kg kg-1.

REEVAP: Total re-evaporation of precipitating condensate, in kg m-2 s-1. Includes evaporation and sublimation and is the total contribution from all three cloud types.

RH: The relative humidity. This is approximated by q/qs where q is the specific humidity and qs is its saturated value. The saturated value is computed over liquid for temperatures above 273.16K and over ice for temperatures below 253.16K. At intermediate temperatures the values over liquid and ice are averaged with weights that vary linearly with temperature.

RHOA: Surface air density in the lowest model layer, in kg m-3. This is the density used in bulk formulasformulae.

SGH: The isotropic standard deviation of topography used for the subgrid-scale gravity wave drag parameterization, in m. Currently the effect of orographic gravity waves is independent of the angle between the flow and the orographic ridges, so only this isotropic component is relevant.

SLP: The surface pressure reduced to sea level, in Pa. Over topography the reduction is done by assuming a lapse rate of 6.5 K km-1 from a free atmospheric temperature, which is currently taken as the lowest model layer above 150 hPa above the surface.

SNOMAS: The mass of snow per unit of ice-free land area (FRLAND), in kg m-2. In grid boxes with no land it is set to _FillValue. Over other land areas it represents an average over the non-glaciated part.

SNODP: The geometric snow depth in meters. This accounts for packing and aging of the snow.

SWGDN, SWGDNCLR, SWTDN: Incident solar radiation (0.175 to 3.85 microns) at the surface for all-sky and clear-sky conditions and the top of the atmosphere, in W m-2. Since we do a single atmospheric radiative transfer calculation in a grid box, we assume the incident radiation is the same for all surface tiles within the box. MERRA uses a solar constant of 1365 W m-2.

SWGNT, SWGNTCLR, SWGNTCLN, SWGNTCLRCLN, SWTNT, SWTNTCLR, SWTNTCLN, SWTNTCLRCLN: Net downward flux of solar radiation at the surface and the top of the model’s atmosphere (0.01 hPa) averaged over all land tiles for all-sky, clear-sky, clean-sky, and clear-clean-sky conditions, in W m-2.  The term “clean-sky” refers to fluxes computed with the aerosol loading set to zero.

TAUGWX, TAUGWY: The eastward (zonal) and northward (meridional) components of the atmospheric stress on the surface due to atmospheric gravity wave drag, in N m-2.

TAUHGH, TAUMID, TAULOW, TAUTOT: Total cloud optical thickness in the 0.40 to 0.69 micron band for the high, middle, and low cloud regions (see CLDHGH) and for the entire column.

TAUX, TAUY: The eastward (zonal) and northward (meridional) components of the atmospheric frictional stress on the surface, in N m-2.

TO3 : The vertically integrated ozone, in Dobson units.

TPW, TQV: The vertically integrated water vapor in the column, in kg m-2.. These are synonyms.

TQL, TQI: The vertically integrated liquid and ice water in the column, in kg m-2.

TROPP: The tropopause pressure in Pa. The tropopause pressure is defined as the pressure where the function  reaches its first minimum above the surface. Here  and  is in hPa. If no minimum is found between 550 hPa and 40 hPa, TROPP is set to _FillValue.

TROPQ: The tropopause specific humidity in kg kg-1. The tropopause is defined as in TROPP.

TROPT: The tropopause temperature in K. The tropopause is defined as in TROPP.

TSRAD: The area weighted skin temperature of all surface tiles in a grid box, in K. This is the skin temperature used for radiation.

TTO3: The vertically integrated ozone in the troposphere, in Dobson units. The troposphere is defined as all levels below TROPP. TTO3 and TROPP are computed at every time step and averaged separately.

U50M, U10M, U2M, V50M, V10M, V2M: The eastward and northward wind component at 50m, 10 m, and 2m in the surface layer, in m s-1. The 2m and 10m values are defined above displacement height (DISPH), the 50m values are above the surface.

USTAR: The surface friction velocity, , in m s-1. This mean quantity is formed by doing the the areal average over the surface tiles in a grid box instantaneously to  , and the time averaging on  itself. It is thus not exactly what would be obtained from TAUX, TAUY, and RHOA.

Z0H: The surface roughness for heat, in m.

Z0M: The dynamic surface roughness, in m.

# Appendix G: Surface Representation

In GEOS-5 the surface below each atmospheric column consists of a set of tiles that represent various surface types. Tiles can be of four different types: Ocean, Land, Ice, Lake, as illustrated in the figure. In each grid box a single Ice tile represents those areas covered by permanent ice. Similarly a single Lake tile represents continental areas covered permanently by water. Other continental areas (non Lake or Ice) can be further subdivided into tiles that represent parts of the grid box in different hydrological catchments, defined according to the Pfaffsteter (19xx) system. Each of these is, in turn, divided into subtiles (not shown in figure) that represent the wilted, unsaturated, saturated, and snow-covered fractions of the tile. These fractions vary with time and are predicted by the model based on the hydrological state of the catchment and its fine-scale topographic statistics. Details of the land model, including the partitioning into subtiles, can be found in Koster et al. (2001).  The Ocean tile can be divided into two subtiles that represent the ice-covered and ice-free parts of the ocean part of the atmospheric grid box. The fractional cover of these subtiles also varies with time. In MERRA, the fractional cover of sea ice and the ocean surface temperature are specified from the climatology of Reynolds and Smith (19xx).

# Appendix H: Budgets

As described in Appendix A, the concatenation of the IAU corrector segments of each analysis cycle is equivalent to a single, continuous run of the AGCM with an additional term–the analysis tendency–on the right hand side of all equations that predict analyzed quantities. Budgets in MERRA are thus identical to those in the free-running AGCM, with the addition of the effects of analysis tendencies, which are constant during the six-hour duration of each corrector segment.

In the MERRA output we produce a full accounting for seven atmospheric quantities: kinetic energy, the enthalpy of moist air, the mass of the atmosphere, the mass of water in vapor, liquid, and ice forms, and the total mass of odd oxygen.. We also keep exact budgets for XX land surface quantities:……

An exact accounting for each of the seven atmospheric quantities is kept in two file collections: inst1_2d_int_Nx  and tavg1_2d_int_Nx. Both collections consist of 2-dimensional data on the model’s native horizontal grid, and both contain only vertical integrals. The first contains instantaneous vertical integrals of the seven quantities at the beginning of each hour (i.e., 00:00Z, 01:00Z, etc). The second collection contains various hourly-mean, vertically-integrated contributions to the tendencies of each of the seven quantities. This Appendix explains how these contributions can be combined to produce the local change in the quantity implied by values in the inst1_2d_int_Nx collection, how the contributions were computed, and what assumptions enter this accounting.

In the following, we will denote the vertical mass-weighted integrals of quantities by an overbar:

,

where  is the surface pressure, and  is the pressure at the top of the model’s atmosphere (1 Pa).

Atmospheric Mass The spatial distribution of the total atmospheric mass, , is stored in the variable MASS in the inst1_2d_int_Nx collection. In the tavg1_2d_int_Nx collection, the total tendency is separated into contributions from dynamics (DMDTDYN), and analysis (DMDTANA). The finite-volume dynamics used in GEOS-5 conserves mass to within round-off at 64-bit precision, so the global mean of DMDTDYN is effectively zero. The physics used in the GEOS-5 AGCM does not include changes in column mass due to changes in water content; there is, therefore, no physics contribution. Although the atmospheric physics does not include atmospheric water in its mass budget, realistic changes in atmospheric mass can still occur since the surface pressure is analyzed and surface pressure observations include the effect.. Mass changes due to water content thus appear as analysis increments rather than physics increments. It is not clear how much improvement in the mass budget, as measured, say, by the degree of invariance of dry mass, would be achieved if the atmospheric model had a more complete treatment. [WE CAN INCLUDE A FOUR PANEL FIGURE HERE FOR ONE YEAR FROM THE MOST RECENT SCOUT RUN SHOWING THE HOURLY MASS IN ONE PANEL AND THE TENDENCY THE TWO CONTRIBUTIONS AND THEIR SUM IN THE ANOTHER PANEL. TWO OTHER PANELS COULD BE THE SAME THING FOR THE MEAN DIURNAL CYCLE.]

Kinetic Energy The instantaneous total kinetic energy for each grid column,  , is stored in the variable KE in the inst1_2d_int_Nx collection. In the tavg1_2d_int_Nx collection, the total tendency is first separated into contributions from dynamics (DKEDTDYN), physics (DKEDTPHY), and analysis (DKEDTANA) increments of winds and atmospheric masses.

(1)

The sum of the three contributions obtained from the tavg1_2d_int_Nx collection exactly matches the difference of values in the inst1_2d_int_Nx, since the contributions are computed by differencing  before and after each process is included. For example,

.

The dynamical contribution can be further divided by considering the vertically integrated kinetic energy equation written in flux form. Ignoring contributions from the analysis and from explicit frictional processes that are included in the physics, this is:

(2)

The first two terms on the right hand side of (1) are the divergence of the vertically integrated kinetic energy and geopotential fluxes. The third term, which appears with opposite sign in the thermodynamic equation, is the conversion between kinetic and total potential energy. The fifth term is the change in gravitational potential energy associated with raising the mass in the column from sea-level to the local height of the surface topography. The sixth term is the change in gravitational potential energy of the mass above the model top (1 Pa or about 0.1 kg m-2) at the height of the top rises and falls. The last term groups all spurious contributions from the discretization of the equation.

The numerics of finite volume dynamical core used in GEOS-5 do not naturally conserve total energy (Lin 200x). This is so for several reasons:

First the advection of the flow field produces numerical dissipation and so does not conserve kinetic energy. Some numerical dissipation is present in all discrete formulations of the dynamics useful for long-term integrations. Even conservative formulations, such as spectral schemes or centered finite-difference schemes like those based on the Arakawa Jacobians, need to be supplemented by explicit dissipation from horizontal diffusion or filters applied to the flow.  In the finite volume dynamical core, the dissipation is not added explicitly and so is harder to track.

A second spurious tendency of total energy comes from the form of the pressure gradient force and the discretization of the thermodynamic equation.. In the continuous equations, the vertical integral of the rate of work done by the pressure gradient force is represented by second through fifth terms in the above equation with the  term being identical to the corresponding term in the thermodynamic equation. This also is not true in the discrete core.

A third spurious contribution comes from time-truncation errors. This arises because the state variables that are directly updated are the horizontal components of the wind, the surface pressure, and the virtual potential temperature, while the kinetic and total potential energy before and after the time step are non-linear combinations of these.

All of these spurious contributions are present even when the core is in its vertically Lagrangian mode, where all layers are bounded by material surfaces. Periodically the core returns to hybrid sigma-pressure coordinates by doing a vertical coordinate transformation or “vertical remapping”. Since this step does not involve any new physics, only a change in vertical coordinate, it should produce no energy transformations. The vertical remapping is indeed done to conserve the sum of internal, gravitational potential, and kinetic energies, but not the three individually.

To enforce total energy conservation, the core needs to compensate for all of these spurious sources. It does this by simply computing the global-mean change in total energy across the entire code and arbitrarily adding it back as a heating in the thermodynamic equation; it makes no adjustment to the kinetic energy.

Terms on the right hand side of (2) are stored in the tavg1_2d_int_Nx and satisfy

,

where the first two contributions are the convergence of kinetic energy and geopotential fluxes, the third is the generation of kinetic energy,, the fourth is the sum of the two boundary terms, and the fifth is the total spurious contribution computed as a residual. The two convergences are computed diagnostically using the core’s own advection scheme. The conversion term is computed using a finite difference form of:

,

which corresponds closely to the form that appears in the core’s potential-temperature-based thermodynamic equation. [HERE WE CAN PUT I A COUPLE OF FIGURES SHOWING THE BREAKDOWN OF THE KE BUDGET THUS FAR,; BOTH LINE PLOTS AND HORIZONTAL PLOTS.]

[IF WE SUCCEED IN A BETTER ATTRIBUTION OF THE RESIDUAL OF THE DYNAMICS CONTRIBUTION TO THE KE BUDGET, THAT DISCUSSION GOES HERE.]

The vertically integrated physics contribution to the kinetic energy tendency consists of frictional effects due to subgrid-scale motions. It can be separated into contributions due to turbulence, including all boundary layer friction, to vertical mixing of momentum by the convective parameterization, and to the friction associated with gravity wave drag. Since the GEOS-5 physics does not time split the effects of these three processes, there is some time truncation in the separation, and this is stored as a residual.

,

# References

Bloom, S., L. Takacs, A. DaSilva, and D. Ledvina, 1996: Data assimilation using incremental analysis updates. Mon. Wea. Rev., 124, 1256-1271.

Bloom, S., A. da Silva, D. Dee, M. Bosilovich, J.-D. Chern, S. Pawson, S. Schubert, M. Sienkiewicz, I. Stajner, W.-W. Tan, M.-L. Wu, 2005: Documentation and Validation of the Goddard Earth Observing System (GEOS) Data Assimilation System - Version 4. Technical Report Series on Global Modeling and Data Assimilation 104606, v26.

Collins, N., G. Theurich, C. DeLuca, M. Suarez, A. Trayanov, V. Balaji, P. Li, W. Yang, C. Hill, and A. da Silva, 2005: Design and implementation of components in the Earth System Modeling Framework. Int. J. High Perf. Comput. Appl., 19, 341-350, DOI: 10.1177/1094342005056120.

Derber, J. C., R. J. Purser, W.-S. Wu, R. Treadon, M. Pondeca, D. Parrish, and D. Kleist, 2003: Flow-dependent Jb in a global grid-point 3D-Var. Proc. ECMWF annual seminar on recent developments in data assimilation for atmosphere and ocean. Reading, UK, 8-12 Sept. 2003.

deWitt, Shaun, 1996: Writing HDF-EOS Grid Products for Optimum Subsetting Services. ECS Technical Paper 170-TP-007-001.

Dopplick, T., 1997: The Role of Metadata in EOSDIS. EOSDIS Technical  Paper 160-TP-013-001.

Gross, C., 1997: B.0 Earth Science Data Model for the ECS Project. EOSDIS Technical Paper 420-TP-015-001.

Koster, R. D., M. J. Suárez, A. Ducharne, M. Stieglitz, and P. Kumar, 2000: A catchment-based approach to modeling land surface processes in a GCM, Part 1, Model Structure.  J. Geophys. Res., 105, 24809-24822.

NOAA, 1995: Conventions for the Standardization of NetCDF Files (COARDS).  http://ferret.wrc.noaa.gov/noaa_coop/coop_cdf_profile.html

Pfaffsteter

Purser, R. J., W.-S. Wu, D. F. Parrish, and N. M. Roberts, 2003a: Numerical aspects of the application of recursive filters to variational statistical analysis. Part I: Spatially homogeneous and isotropic Gaussian covariances. Mon. Wea. Rev., 131, 1524-1535.\

Purser, R. J., W.-S. Wu, D. F. Parrish, and N. M. Roberts, 2003b: Numerical aspects of the application of recursive filters to variational statistical analysis. Part II: Spatially inhomogeneous and anisotropic general covariances. Mon. Wea. Rev., 131, pp. 1536-1548.

Reynolds and Smith or Hadley??

Wu, W.-S., R.J. Purser and D.F. Parrish, 2002:  Three-dimensional variational analysis with spatially inhomogeneous covariances.  Mon. Wea. Rev., 130, 2905-2916.

# Web Resources

GMAO web site: http://gmao.gsfc.nasa.gov/

GMAO Operations page: http://gmao.gsfc.nasa.gov/operations/

CF Standard Description: http://www.cgd.ucar.edu/cms/eaton/cf-metadata/CF-current.html

CF Standard Names: http://www.cgd.ucar.edu/cms/eaton/cf-metadata/standard_name.xml

NCSA, 1999: The NCSA HDF Home Page. http://hdf.ncsa.uiuc.edu/

NASA, 1999: HDF-EOS Standards. http://hdfeos.gsfc.nasa.gov/

# Comments

Is this correct?

NOTE that text needs to be inserted.  This is missing also in our official GEOS-5 spec for intrument teams.

# Text boxes

| Level | P(hPa) | Level | P(hPa) | Level | P(hPa) | Level | P(hPa) | Level | P(hPa) | Level | P(hPa) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1000 | 8 | 825 | 15 | 600 | 22 | 250 | 29 | 30 | 36 | 2 |
| 2 | 975 | 9 | 800 | 16 | 550 | 23 | 200 | 30 | 20 | 37 | 1 |
| 3 | 950 | 10 | 775 | 17 | 500 | 24 | 150 | 31 | 10 | 38 | 0.7 |
| 4 | 925 | 11 | 750 | 18 | 450 | 25 | 100 | 32 | 7 | 39 | 0.5 |
| 5 | 900 | 12 | 725 | 19 | 400 | 26 | 70 | 33 | 5 | 40 | 0.4 |
| 6 | 875 | 13 | 700 | 20 | 350 | 27 | 50 | 34 | 4 | 41 | 0.3 |
| 7 | 850 | 14 | 650 | 21 | 300 | 28 | 40 | 35 | 3 | 42 | 0.1 |

| Variable Name | Description | Units |
| --- | --- | --- |
| PHIS | Surface geopotential | m2 s-2 |
| SGH | Standard deviation of topography for gravity wave drag | m |
| FRLAKE | Fraction of lake type in grid box | fraction |
| FRLAND | Fraction of land type in grid box | fraction |
| FRLANDICE | Fraction of land ice type in grid box | fraction |
| FROCEAN | Fraction of ocean in grid box | fraction |