4.0 AFFECTED ENVIRONMENT

## INTRODUCTION

Agency Procedures (22 CFR 216) state that the section of the EA addressed to the (potentially) Affected Environment “shall succinctly describe the environment of the area(s) to be affected or created by the alternatives under consideration. The descriptions shall be no longer than necessary to understand the effects of the alternatives.  Data and analysis in the Environmental Assessment shall be commensurate with the significance of the impact with less important material summarized, consolidated or simply referenced.”

In order to describe the existing conditions in the areas potentially affected, the following introductory material presents:

- Definition of the Project Area;

- Identification of the relevant environmental criteria for EA purposes;

The remainder of the Section presents the details of the potentially affected environment under four headings structured according to the relevant environmental criteria as will be detailed below.

## Definition of the Project Area. The potentially Affected Environment for a given project (generally referred to as the Project Area) is defined by the nature of the proposed action and the sensitivity and circumstances of the environment in which it will occur. Both the nature of the project and the sensitivity of the environment must be considered.  An environmentally benign project in one location might be detrimental in another.

The potential for both direct and indirect impacts must be considered in the definition of the Project Area. Potential direct impacts of a road project such as the proposed rehabilitation of the Kabul-Kandahar Road will be largely confined to the Project’s construction limits and immediately adjacent environs. The conceptual limits of the Project Area must be expanded, however, to include the potential impacts of network improvements and other indirect and cumulative impacts in accordance with the circumstances of the particular environmental characteristic under discussion. A change in drainage patterns, for example, could have an impact on the conditions within the rehabilitation area and the watercourses directly affected, but may also impact hydrological conditions down stream to a degree that can only be determined by circumstances. The increased runoff due to highway development and the additional development that it attracts (referred to as an “induced impact”) often warrants investigations in a considerably larger area than the construction limits and the immediately adjacent area. In the case of the Kabul-Kandahar Road Rehabilitation Project indirect and cumulative impacts, particularly socio-economic impacts, are likely to occur in all provinces through which road passes. Many of these impacts will be beneficial. Improvements to the roadway networks generally will, for example, present a potential for significant economic and social impacts along all network connections.

Accordingly, the Project Area for the purpose of the EA is defined as the area immediately adjacent to the 482-kilometer Kabul-Kandahar Road. The scope of the examination has been expanded to ensure that environmental impacts such as the example of potential down-stream hydrological impacts are taken into account.

Identification of the Relevant Environmental Criteria. The scope and significance of environmental issues for the Kabul-Kandahar Road Rehabilitation Project were addressed by a Scoping Process leading to the preparation of a Scoping Statement submitted to and approved by USAID in November 2002.  Steps in the Scoping Process included review of the definition of environmental issues as established by the applicable regulations and other considerations. The review provided the framework for the identification and presentation of the relevant environmental criteria as follows.

Paragraph 216.1 (c) (10) of the Agency Environmental Procedures states that the “term environment, as used in these procedures with respect to effects occurring outside the United States, means the natural and physical environment”. Accordingly, the initial sections of the description of the potentially affected environment presents:

- Physical Resources (Item 4.1). Physical resources are generally defined to include topographic, soil, geological and related attributes.  Sub-headings in this section are:

- Topography (Item 4.1.1)

- Soils (Item 4.1.2)

- Seismic & Geological Conditions (Item 4.1.3)

- Hydrology (Item 4.1.4)

- Climate and Air Quality (Item 4.1.5)

- Mines and Unexploded Ordnance (Item 4.1.6).

- Natural/Biological Resources (Item 4.2). Natural/biological aspects of the potentially affected environment are discussed under the sub-headings of:

- Flora (Plant Species) (Item 4.2.2)

- Fauna (Wildlife) (Item 4.2.1)  and

- Protected Areas (Item 4.2.3).

In addition to these requirements, Paragraph 216.6 of the Procedures states that “… Environmental Assessment(s) should include discussions of ….. possible conflicts between the proposed action and land use plans policies and controls for the areas concerned; energy requirements and conservation potential of variouColeman SiteƒÔ
Ô

Ä

| ÄÁà ì |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Ì$FÁFIGURE 3ƒ
OKAHUMPKA WEST SITE
Ó	nø+	ÓÑ ô`Ü-D4p±à„( ÑÁ`	Ì$/ÁLOUIS BERGER & ASSOCIATES, INC.ƒÔ
f.Ô

Ñ R¬Ü-D4p±à…³ ÑÐ

XXXX

ÐÐ

8

8

ÐÚyHà.„XdddyÚÚyHà.€%XdddyÚÑ R¬Ü-D4p±à…³ ÑSITE BOUNDARIES:Á`Ì$FÁFIGURE 4ƒ
OKAHUMPKA WEST
Ó	nø+	ÓÑ ô`Ü-D4p±à„( ÑÚyHà.„XdddyÚÚyHà.€%XdddyÚÁ`	Ì$/ÁLOUIS BERGER & ASSOCIATES, INC.ƒÔ
f.Ô

Ñ R¬Ü-D4p±à…³ ÑÐ

XXXX

ÐÐ

8

8

| ÐÚyHà.„XdddyÚÚyHà.€%XdddyÚÑ R¬Ü-D4p±à…³ ÑSITE VIEW:Á` |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

# Endnotes

National Atlas of the Democratic Republic of Afghanistan, Organization for Surveying and Cartography and GEOKART Poland, 1995.

National Atlas of the Democratic Republic of Afghanistan, Organization for Surveying and Cartography and GEOKART Poland, 1995, page VII.

National Atlas of the Democratic Republic of Afghanistan, Organization for Surveying and Cartography and GEOKART Poland, 1995, page 20.

Asian Development Bank, Afghanistan Country Strategy Paper.

Afghanistan Civil Infrastructure Assessment, Final Report to USAID/Afghanistan, 20 August 2002, page 274.

National Atlas of the Democratic Republic of Afghanistan, Organization for Surveying and Cartography and GEOKART Poland, 1995, pages 9-11.

Original estimate supplied by the Afghanistan Civil Infrastructure Assessment, Final Report to USAID/Afghanistan, 20 August 2002. Revised estimate by Jim Myers, Kabul 16 November 2002.

Lonely Planet

REFS Contract, page C-8.

National Atlas of the Democratic Republic of Afghanistan, Organization for Surveying and Cartography and GEOKART Poland, 1995, page VII.

Lonely Planet

Asian Development Bank, Afghanistan Country Strategy Paper.

National Atlas of the Democratic Republic of Afghanistan, Organization for Surveying and Cartography and GEOKART Poland, 1995, page 12.

National Atlas of the Democratic Republic of Afghanistan, Organization for Surveying and Cartography and GEOKART Poland, 1995, page VII.

World Bank, Technical Annex for a Proposed Grant… to Afghanistan for an Emergency Infrastructure Reconstruction Project, May 2002, Annex V, Attachment 1, page 46 with additional information supplied by Koen Tooner, UN Environmental Project (Telephone: 070n 276-431), Kabul, interviewed 18 November 2002.

CIA Profile

World Bank, Technical Annex for a Proposed Grant… to Afghanistan for an Emergency Infrastructure Reconstruction Project, May 2002, paragraph 8, page 2.

CIA Profile

World Bank, Technical Annex for a Proposed Grant… to Afghanistan for an Emergency Infrastructure Reconstruction Project, May 2002, paragraph 8, page 2.

EIA.DOE.Gov Web Site

World Bank, Technical Annex for a Proposed Grant… to Afghanistan for an Emergency Infrastructure Reconstruction Project, May 2002, paragraph 9, page 2.

EIA.DOE.Gov Web Site

World Bank, Technical Annex for a Proposed Grant… to Afghanistan for an Emergency Infrastructure Reconstruction Project, May 2002, paragraph 19, page 4.

CIA Profile

World Bank, Technical Annex for a Proposed Grant… to Afghanistan for an Emergency Infrastructure Reconstruction Project, May 2002, paragraph 9, page 2.

National Atlas of the Democratic Republic of Afghanistan, Organization for Surveying and Cartography and GEOKART Poland, 1995, page 15.

World Bank, Technical Annex for a Proposed Grant… to Afghanistan for an Emergency Infrastructure Reconstruction Project, May 2002, paragraph 7, page 2.

World Bank, Technical Annex for a Proposed Grant… to Afghanistan for an Emergency Infrastructure Reconstruction Project, May 2002, paragraph 7, page 2.

World Bank, Technical Annex for a Proposed Grant… to Afghanistan for an Emergency Infrastructure Reconstruction Project, May 2002, paragraph 16, page 4.

CIA Profile

World Bank, Technical Annex for a Proposed Grant… to Afghanistan for an Emergency Infrastructure Reconstruction Project, May 2002, paragraph 7, page 2.

REFS Contract, Section C, Item B, page C-2.

World Bank, Technical Annex for a Proposed Grant… to Afghanistan for an Emergency Infrastructure Reconstruction Project, May 2002, paragraph 79, page 15.

World Bank, Technical Annex for a Proposed Grant… to Afghanistan for an Emergency Infrastructure Reconstruction Project, May 2002, paragraph 7, page 2.

World Bank, Technical Annex for a Proposed Grant… to Afghanistan for an Emergency Infrastructure Reconstruction Project, May 2002, paragraph 7, page 2.