DRAFT

Didecyl Dimethyl Ammonium Chloride (DDAC)

Occupational and Residential Exposure Assessment

(DP Barcode 323309)

Office of Pesticide Programs

Antimicrobials Division

U.S. Environmental Protection Agency

1801 South Bell St.

Arlington, VA 22202

Date: April 18, 2006

TABLE OF CONTENTS

EXECUTIVE SUMMARY	3

1.0	 INTRODUCTION	9

1.1	Purpose	9

1.2	Criteria for Conducting Exposure Assessments	9

1.3	Chemical Identification	11

1.4	Physical/Chemical Properties	12

2.0	 USE INFORMATION	12

2.1	 Formulation Types and Percent Active Ingredient	12

2.2	 Summary of Use Pattern and Formulations	12

3.0	SUMMARY OF TOXICITY DATA	13

3.1	Acute Toxicity	13

3.2	Summary of Toxicity Endpoints	13

3.3	FQPA Considerations	15

4.0	RESIDENTIAL EXPOSURE ASSESSMENT	15

4.1	Summary of Registered Uses	15

4.2	Residential Exposure	15

4.2.1	Residential Handler Exposures	17

4.2.2	Residential Post-application Exposures	20

4.2.3	Data Limitations/Uncertainties	36

5.0	RESIDENTIAL AGGREGATE RISK ASSESSMENT AND CHARACTERIZATION	37

6.0	OCCUPATIONAL EXPOSURE ASSESSMENT	37

6.1 	Occupational Handler Exposures	40

6.2  	Occupational Post-application Exposures	45

6.3 	Wood Preservation	47

6.3.1 	Non-Pressure Treatment Scenarios (Handler and Post-application)	48

6.3.2	Pressure Treatment Scenarios (Handler and Post-Application)	52

6.4	Data Limitations/Uncertainties	55

7.0	REFERENCES	57

APPENDIX A: Master DDAC Label	59

APPENDIX B: Summary of CMA and PHED Data	72

APPENDIX C: Input/Output from Residential MCCEM Modeling	75

APPENDIX D: Input/Output from Occupational MCCEM Modeling	87

APPENDIX E:  Calculation of DDAC Unit Exposure Values	96

# EXECUTIVE SUMMARY

This document is the Occupational and Residential Exposure Chapter of the Reregistration Eligibility Decision (RED) document for the Group I Quat Cluster. It addresses the potential risks to humans that result from the use of chemicals in this group in occupational and residential settings.  Group I Quat Cluster is a group of structurally similar quaternary ammonium compounds (“quats”) that are characterized by having a positively charged nitrogen covalently bonded to two alkyl group substituents (at least one C8 or longer) and two methyl substituents.  In finished form, these quats are salts with the positively charged nitrogen (cation) balanced by a negatively charged molecule (anion).  The anion for the quats in this cluster is chloride or bromide. In this document, the Group I Quat Cluster will be referred to as DDAC (didecyl dimethyl ammonium chloride).

DDAC is the active ingredient in numerous types of products.  The products are mainly disinfectants and deodorants that are used in agricultural, food handling, commercial/ institutional/industrial, residential and public access, and medical settings (Use Site Categories I, II, III, IV, and V respectively). Examples of registered uses for DDAC in these settings include application to indoor and outdoor hard surfaces (e.g., walls, floors, tables, toilets, and fixtures), eating utensils, laundry, carpets, agricultural tools and vehicles, egg shells, shoes, milking equipment and udders, humidifiers, medical instruments, human remains, ultrasonic tanks, reverse osmosis units, and water storage tanks. There are also DDAC-containing products that are used in residential and commercial swimming pools (Use Site Category XI), in aquatic areas (Use Site Category XII) such as decorative ponds and decorative fountains, and in industrial process and water systems (Use Site Category VIII) such as re-circulating cooling water systems, drilling muds and packer fluids, oil well injection and wastewater systems. Additionally, DDAC-containing products are used for wood preservation (Use Site Category X) through non-pressure and pressure-treatment methods.  There are registered uses for fogging in occupational settings.  Products containing DDAC are formulated as liquid ready-to-use, soluble concentrate, pressurized liquid, and water soluble packaging. The percentage of DDAC in the various end-use products ranges from 0.08% to 80% as reported in the Master Label spreadsheet (Appendix A).  Residential products such as EPA Reg. No. 10324-69 range up to 50% DDAC for swimming pools and spas.

The durations and routes of exposure evaluated in this assessment include short-term (ST), intermediate-term (IT), and in some instances long-term (LT) inhalation exposures, ST dermal exposures, and ST oral exposures.  The ST inhalation endpoint and the ST oral endpoint is based on a NOAEL of 10 mg/kg/day from a prenatal developmental toxicity study in rats.  The LOAEL (20 mg/kg/day) was based largely on increased incidence of skeletal variations in females.  The developmental study does not indicate increased susceptibility from in utero and postnatal exposure to DDAC.  The IT/LT inhalation endpoint is also based on a 10 mg/kg/day but from a chronic toxicity study in dogs. No short-term dermal endpoint for systemic effects was selected for DDAC, since no systemic effects were identified. However, a short-term dermal irritation endpoint was identified.  The short-term dermal endpoint for the technical grade active ingredient (TGAI) containing 80% ai diluted to 0.1% DDAC as a test material (2 mg/kg/day which is equivalent to 8 μg/cm2) was determined from a LOAEL of 6 mg/kg/day based on increased clinical and gross findings (erythema, edema, exfoliation, excoriation, and ulceration). A 21-day dermal toxicity study was also conducted using a 0.13% ai formulation. No short-term dermal endpoint was identified for this formulation because no irritation or systemic effects were identified up to and including the limit dose of 1,000 mg/kg/day.  Intermediate- or long-term dermal irritation endpoints were not identified for DDAC.  Because the effect to the skin is a localized skin irritation, a skin concentration (μg/cm2) of exposure, rather then a dose (mg/kg/day) was used to assess the dermal risk concerns.  No body weight is needed for the dermal irritation endpoint, since no systemic dose is calculated.  Since the toxicological endpoint for inhalation is female-specific, a body weight of 60 kilograms is used in the assessment.  This represents the body weight of an adult female. They Agency’s level of concern (LOC) for occupational and residential DDAC dermal, inhalation and oral exposures is 100 (i.e., a margin of exposure (MOE) less than 100 exceeds the level of concern). The level of concern is based on 10x for interspecies extrapolation and 10x for intraspecies extrapolation.

The dermal and inhalation margins of exposure were not combined for the DDAC risk assessment because the toxicity endpoints for the dermal and inhalation routes of exposure are based on different toxicological effects. No cancer endpoint was identified; therefore, cancer risks are not assessed.

This occupational and residential assessment was based on examination of product labels describing uses for the product.  There are many end-use products that contain DDAC; therefore, only labels on the Master Label developed by AD and the registrants were reviewed. It has been determined that exposure to handlers can occur in a variety of occupational and residential environments.  Additionally, post-application exposures are likely to occur in these settings.  The representative scenarios selected by the Antimicrobials Division (AD) for assessment were evaluated using maximum application rates as stated on the product labels.  The representative scenarios are believed to represent high-end uses resulting in dermal, inhalation, and incidental oral exposures.

To assess most handler risks, AD used surrogate unit exposure data from the Chemical Manufacturers Association (CMA) antimicrobial exposure study and the Pesticide Handlers Exposure Database (PHED).  Postapplication/bystander exposures were assessed using EPA’s Health Effects Division’s (HED) Standard Operating Procedures (SOPs) for Residential Exposure Assessment, MCCEM (Multi- Chamber Concentration and Exposure Model), and Swim Model. Additionally, handler and post-application exposures resulting from wood preservation activities were assessed using surrogate data from the studies Measurement and Assessment of Dermal and Inhalation Exposures to Didecyl Dimethyl Ammonium Chloride (DDAC) Used in the Protection of Cut Lumber (Phase III) (Bestari et al., 1999, MRID 455243-04) and “Assessment of Potential Inhalation and Dermal Exposure Associated with Pressure Treatment of Wood with Arsenical Wood Products” (ACC, 2002a).

Residential Handler Risk Summary

Dermal

For the residential handler dermal exposure and risk assessment, dermal risks were calculated by comparing residues on the surface of the skin to the short-term dermal irritation endpoints.  Dermal residential handler exposures were not assessed for products containing less than 1% DDAC. Residues on the surface of the skin (dermal irritation exposure) were determined using hand unit exposures from CMA and/or PHED adjusted for the surface area of the hand (mg/lb ai/cm2), application rates, and use amounts. The dermal MOEs were below the target MOE of 100 for all scenarios except the humidifier and swimming pool applications.

Inhalation

For the residential handler inhalation assessment, the inhalation risks were calculated by comparing the daily doses to the short-term inhalation endpoint.  The inhalation MOEs were above the target MOE of 100 for all scenarios.

Residential Post-Application/Bystander Risk Summary

Dermal

The residential post-application dermal risks were assessed by comparing the surface residue on the skin (dermal skin irritation exposure) to the short-term dermal endpoint. It was assumed that during the exposure period the skin repeatedly contacts the treated surface until a steady-state concentration of residues is achieved on the skin.  For residential scenarios, the post-application dermal MOEs were above the target MOE of 100 for the laundered clothing (assuming 1% residue transfer) but below the target MOE for the following:

- Wearing clothes treated with a fabric spray: ST dermal MOE =  less than or equal to 1 using both a 100% clothing to skin transfer factor and a 5% clothing to skin transfer factor.

- Dermal contact on floors (MOE = 33) and carpets (MOE = 45).

- There are no wipe data available to assess the children’s dermal contact to treated decks and/or play sets.  Based on hand measurements of workers at the treatment plants, dermal risks may be of concern and therefore a wipe study is warranted.

Inhalation

For the residential post-application inhalation exposure and risk assessment, the MOEs were below the target MOE of 100 for the following scenario:

- Humidifier: ST/IT 8-hr Inhalation MOE = 27 for adults and 8 for children; ST/IT 24-hr Inhalation MOE = 11 for adults and 5 for children

Incidental Oral

For the residential post-application incidental oral assessment, the MOEs were above the target MOE of 100 for all scenarios except the following:

- Mouthing on clothes treated with a fabric spray: ST oral MOE = 12

Occupational Handler Risk Summary

Dermal

DDAC dermal irritation exposures and risks were not estimated for occupational handler exposures.  Instead, dermal irritation exposures and risks will be mitigated using default personal protective equipment requirements based on the toxicity of the end-use product.  To minimize dermal  exposures, the minimum PPE required for mixers, loaders, and others exposed to end-use products containing concentrations of DDAC that result in classification of category I, II, or III for skin  irritation potential will be long-sleeve shirt, long pants, shoes, socks, chemical-resistant gloves, and chemical-resistant apron.  Once diluted, if the concentration of DDAC in the diluted solution would result in classification of toxicity category IV for skin irritation potential, then the chemical-resistant gloves and chemical-resistant apron can be eliminated for applicators and others exposed to the dilute. Note that chemical-resistant eyewear will be required if the end-use product is classified as category I or II for eye irritation potential.

Inhalation

For the occupational handler inhalation exposure and risk assessment, the MOEs were above the target MOE of 100 for all scenarios.

A confirmatory inhalation toxicity study may be warranted because inhalation MOEs were below 1,000 for the following scenarios:

- Small process water systems, liquid pour: ST/IT Inhalation MOE = 130

- Agricultural fogging, mixing and loading: ST/IT Inhalation MOE = 110

- Medical premises, mopping: ST/IT Inhalation MOE = 280

- Wood Preservation (non-pressure treatment), blender/sprayer: ST/IT/LT Inhalation MOE = 280

Occupational Post-Application/Bystander Risk Summary

Dermal

Dermal irritation exposures are assumed to be negligible for all post-application occupational scenarios, except those associated with wood preservation. As with occupational handlers, dermal irritation exposures and risks from post-application activities in a wood preservation treatment facility will be mitigated using default personal protective equipment requirements based on the toxicity of the end-use product.  For construction workers handling treated wood the MOEs are potentially of concern.  A wipe study on treated wood will be needed to refine these potential exposures.

Inhalation

For the occupational inhalation post-application exposure and risk assessment, the MOEs were above the target MOE of 100 for all scenarios except for the following scenarios listed below.

- Fogging in a food processing plant:  The 8-hr MOE from 2 to 10 hours (2 hour re-entry interval) = 8.

A confirmatory inhalation toxicity study may be warranted because the inhalation MOE was below 1,000 (additional 10x uncertainty factor is considered because of the lack of an inhalation route-specific toxicological endpoint) for the following scenarios:

- Fogging in a hatchery:	 The 8-hr MOE from 0 to 8 hours (entering immediately after fogging) = 120.

- Non-pressure treatment wood preservation, clean-up worker: ST/IT/LT Inhalation MOE = 990

Data Limitations and Uncertainties:

There are a number of uncertainties associated with this assessment and these have been reiterated from Sections 4.2.3 (residential) and 6.4 (occupational) respectively.

The data limitations and uncertainties associated with the residential handler and post-application exposure assessments include the following:

- Surrogate dermal and inhalation unit exposure values were taken from the proprietary Chemical Manufacturers Association (CMA) antimicrobial exposure study (USEPA, 1999: DP Barcode D247642) or from the Pesticide Handler Exposure Database (USEPA, 1998) (See Appendix B for summaries of these data sources). Most of the CMA data are of poor quality therefore, AD requests that confirmatory monitoring data be generated to support the values used in these assessments.

- The quantities handled/treated were estimated based on information from various sources, including HED’s Standard Operating Procedures (SOPs) for Residential Exposure Assessments (USEPA 2000 and 2001).  In certain cases, no standard values were available for some scenarios.  Assumptions for these scenarios were based on AD estimates and could be further refined from input from registrants.

- Some labels for products which can be used by homeowners in residential settings, as well as by workers in occupational settings, indicate that low pressure sprayers can be used for application of the disinfectant to hard, non-porous surfaces such as floors and walls. A low pressure spray scenario was not assessed for the residential scenario because it is not a typical cleaning method for homeowners.

- In this assessment, incidental ingestion and dermal exposures to treated wood were estimated using DDAC data from an occupational exposure study.  The degree of uncertainty (under- or overestimation) associated with using the DDAC hand residue data for dermal and oral exposure from contacting treated lumber are unknown.  The amount of residue measured on the test subjects hands is variable and are influenced by the duration of exposure, how often wood is contacted, and the degree of contact (i.e., do the hand residues from the DDAC study mimic a child’s play activity on decks and playsets?).  A wipe study on treated wood is needed to refine these estimates.

- Available data to assess the levels of DDAC in soil contaminated with DDAC-treated wood do not exist at this time.  In addition, leaching data were also not available.  Because of this data gap, EPA was not able to accurately predict dermal and incidental ingestion residential post-application exposures to soil contaminated with DDAC-treated wood.

The data limitations and uncertainties associated with the occupational handler and post-application exposure assessments include:

- Surrogate dermal and inhalation unit exposure values were taken from the proprietary Chemical Manufacturers Association (CMA) antimicrobial exposure study (USEPA, 1999: DP Barcode D247642) or from the Pesticide Handler Exposure Database (USEPA, 1998) (See Appendix B for summaries of these data sources).   Since the CMA data are of poor quality, the Agency requests that confirmatory data be submitted to support the occupational scenarios assessed in this document.

- Unit exposures are not available for some of the specific scenarios that are prescribed for DDAC, including open loading into oil-well/field environments

  - The CMA data used for oil-well uses are based on open pouring of a material preservative.  Although these data are only represented by 2 replicates each, the exposure values are similar to open loading of pesticides in PHED. Furthermore, there are no representative unit exposure data for chemical metering into secondary recovery oil operations.  Since the volume of water being treated in secondary recovery operations is so large, the available CMA data can not be reliably extrapolated because they are based on activities that handle much lower volumes and possibly different techniques.  Therefore, it was assumed that if the open pour handling activities for the other oil well operations resulted in MOEs that are not of concern, then the MOEs for the closed system chemical metering into secondary recovery operations would also be not of concern.  AD requests that confirmatory data be conducted to show that this is accurate.

- For the wood preservative pressure treatment scenarios, CCA exposure data were used for lack of DDAC-specific exposure data. Limitations and uncertainties associated with the use of these data include:

  - The assumption was made that exposure patterns for workers at treatment facilities using CCA would be similar to exposure patterns for workers at treatment facilities using DDAC, and therefore the exposures could be used as surrogate data for workers that treat wood with DDAC.

  - For environmental modeling, it was assumed that the leaching process from the DDAC treated wood would be similar to that of CCA.  However, due to the lack of real data for DDAC -treated wood, it is not possible to verify this assumption.

- The quantities handled/treated were estimated based on information from various sources, including HED’s Standard Operating Procedures (SOPs) for Residential Exposure Assessments (USEPA 2000 and 2001) and personal communication with experts.  In particular, the use information for oil-well uses and cooling water tower uses are based on personal communication with biocide manufacturers for these types of uses.  The individuals contacted have experience in these operations and their estimates are believed to be the best available without undertaking a statistical survey of the uses.  In certain cases, no standard values were available for some scenarios.  Assumptions for these scenarios were based on AD estimates and could be further refined from input from registrants.

- The percent active ingredient in solution for the pressure treatment of lumber needs to be refined by the registrant.  The labels only provided a retention rate.  For this assessment, the application rate on the master label was used, which is the same as the application rate for non-pressure treatment of lumber.

# 1.0	 INTRODUCTION

## 1.1	Purpose

In this document, the Antimicrobials Division (AD) presents the results of its review of the potential human health effects of occupational and residential exposure to DDAC. This information is for use in EPA's development of the DDAC Reregistration Eligibility Decision (RED) document.

## 1.2	Criteria for Conducting Exposure Assessments

An occupational and/or residential exposure assessment is required for an active ingredient if (1) certain toxicological criteria are triggered and (2) there is potential exposure to handlers (mixers, loaders, applicators, etc.) during use or to persons entering treated sites after application is complete.  For DDAC, both criteria are met. Toxicological endpoints were selected for short- and intermediate-term dermal, inhalation, and incidental oral exposures to DDAC.  There is a significant potential for exposure in a variety of occupational and residential settings.  Therefore, risk assessments are required for occupational and residential handlers as well as for occupational and residential postapplication exposures that can occur as a result of DDAC use.

In this document, handler scenarios were assessed by using unit exposure data to estimate occupational and residential handlers’ exposures. Unit exposures are estimates of the amount of exposure to an active ingredient a handler receives while performing various handler tasks and are expressed in terms of micrograms or milligrams (1 mg = 1,000 µg) of active ingredient per pounds of active ingredient handled.  A series of unit exposures have been developed that are unique for each scenario typically considered in assessments (i.e., there are different unit exposures for different types of application equipment, job functions, and levels of protection).  The unit exposure concept has been established in the scientific literature and also through various exposure monitoring guidelines published by the USEPA and international organizations such as Health Canada and OECD (Organization for Economic Cooperation and Development).

Using surrogate unit exposure data, maximum application rates from labels, and EPA estimates of daily amount handled, exposures and risks to handlers were assessed.  The exposure/risks were calculated using the following equations:

Daily Exposure: Daily dermal and inhalation handler exposures are estimated for each applicable handler task with the application rate, quantity treated/handled in a day, and the applicable inhalation unit exposure using the following formula:

Daily Inhalation Exposure:	E = UE x AR x AT					(Eq. 1a)

Where:

E	=	Amount (mg ai/day) inhaled that is available for inhalation absorption;

UE	=	Hand unit exposure value (mg ai/lb ai) derived from August 1998 PHED data or from 1992 CMA data;

AR	=	Maximum application rate based on a logical unit treatment, such as acres (A), square feet (sq. ft.), gallons (gal), or cubic feet (cu. ft). Maximum values are generally used (lb ai/A, lb ai/sq ft, lb ai/gal, lb ai/cu ft); and

AT 	=	Normalized application area based on a logical unit treatment such as acres (A/day), square feet  (sq ft/day), gallons (gal/day), or cubic feet (cu. ft./day).

Daily Dermal Skin Irritation Exposure:	E = UEhand/SAhand x AR x AT		(Eq. 1b)

Where:

E	=	Amount (mg ai/cm2) deposited on the surface of the skin;

UEhand	=	Unit exposure value (mg ai/lb ai) derived from August 1998 PHED data or from 1992 CMA data;

SAhand	=	Surface area of two hands (820 cm2);

AR	=	Maximum application rate based on a logical unit treatment, such as acres (A), square feet (sq. ft.), gallons (gal), or cubic feet (cu. ft). Maximum values are generally used (lb ai/A, lb ai/sq ft, lb ai/gal, lb ai/cu ft); and

AT 	=	Normalized application area based on a logical unit treatment such as acres (A/day), square feet  (sq ft/day), gallons (gal/day), or cubic feet (cu. ft./day).

Daily Dose: The inhalation dose is calculated by normalizing the daily exposure by body weight and adjusting, if necessary, with an appropriate absorption factor.  An absorption factor of 100% was used for inhalation exposures.  A daily dose is not calculated for dermal exposures, because the dermal endpoint selected is based on irritation effects, not systemic effects. Daily dose was calculated using the following formula:

Daily Dose:	ADD = E x ABS							(Eq. 2)

BW

Where:

ADD 		= 	Average daily dose or the absorbed dose received from exposure to a chemical in a given scenario (mg active ingredient/kg body weight/day);

E 		=	Amount (mg ai/day) inhaled that is available for inhalation absorption;

ABS 		= 	A measure of the amount of chemical that crosses a biological boundary such as lungs (% of the total available absorbed); and

BW		= 	Body weight determined to represent the population of interest in a risk assessment (kg).

Margins of Exposure:  Non-cancer inhalation risks for each applicable handler scenario are calculated using a Margin of Exposure (MOE).  This is the ratio of the daily inhalation dose or dermal exposure to the toxicological endpoint of concern.

Margins of Exposure (inhalation):	MOE = NOAEL or LOAEL			(Eq. 3a)

ADD

Where:

MOE 			= 	Margin of exposure, value used to represent risk or how close a chemical exposure is to being a concern (unitless);

NOAEL or LOAEL	= 	Systemic toxicity level where no observed adverse effects (NOAEL) or where the lowest observed adverse effects (LOAEL) occurred in the study (mg ai/kg body weight/day); and

ADD 			= 	Average daily inhalation dose in a given scenario (mg ai/kg body weight/day).

Margins of Exposure (dermal):	MOE = NOAEL or LOAEL			(Eq. 3b)

E

Where:

MOE 			= 	Margin of exposure, value used to represent risk or how close a chemical exposure is to being a concern (unitless);

NOAEL or LOAEL	= 	Irritation toxicity level where no observed adverse effects (NOAEL) or where the lowest observed adverse effects (LOAEL) occurred in the study ((g/cm2); and

E 			= 	Dermal skin irritation exposure in a given scenario ((g/cm2).

In addition to the target MOEs presented in Table 3.2 that were used for the analysis, a series of assumptions and exposure factors served as the basis for completing the handler risk assessment. Each general assumption and factor for both residential and occupational assessments is detailed below.  Assumptions specific to the use site category are listed in each separate section of this document.  The general assumptions and factors include:

- DDAC products are widely used and have a large number of use patterns that are difficult to completely capture in this document.  As such, AD has patterned this risk assessment on a series of likely representative scenarios for each use site that are believed by AD to represent the vast majority of DDAC uses.

- Based on the adverse effects for the endpoints, the average body weight of a female adult handler (60 kg) was used for the inhalation risk assessment.

- Exposure factors used to calculate daily exposures to handlers were based on applicable data, if available.  When appropriate data were lacking, values from a scenario deemed similar were used.

- The maximum application rates allowed by labels were assumed.

## 1.3	Chemical Identification

The Group I Quat Cluster (DDAC) is a group of structurally similar quaternary ammonium compounds (“quats”) that are characterized by having a positively charged nitrogen covalently bonded to two alkyl group substituents (at least one C8 or longer) and two methyl substituents.  In finished form, these quats are salts with  the positively charged nitrogen (cation) balanced by a negatively charged molecule (anion).  The anion for the quats in this cluster is chloride or bromide.

Currently, there are 4 active ingredients identified by the Agency that are registered and included in Case Number 350.  Table 1.1 below provides the common chemical name, active ingredient code, CAS number, and chemical structure.

| Table 1.1. Active Ingredients in the Group I Quat Cluster Identified by the AIJV |
| --- |
| Prod Code | CAS RN | Name | Structure | Chain Lengths |
| 69149 | 7173-51-5 | Didecyl Dimethyl Ammonium Chloride (DDAC) |  | R = C10 |
| 69166 | 5538-94-3 | Dioctyl Dimethyl Ammonium Chloride |  | R = C8 |
| 69165 | 32426-11-2 | Octyl Decyl Dimethyl Ammonium Chloride |  | R1 = C8 (variable %) R2 = C10 (variable %) |
| 69146 | 84540-07-8 | Alkyl Dimethyl Ethyl Ammonium Bromide |  | R = C12 (5%) C14 (90%) C16 (5%) |

## 1.4	Physical/Chemical Properties

Table 1.2 shows physical/chemical characteristics that have been reported for DDAC.

| Table 1.2. Physical/Chemical Properties of DDAC |
| --- |
| Parameter | DDAC |
| Molecular Weight | 362.08 |
| Density | 0.9216 g/cm3 at 25 C |
| Boiling Point | NA |
| Water Solubility | Completely soluble |
| Vapor Pressure | 2.33E-11 mmHg |

# 2.0	 USE INFORMATION

## 2.1	 Formulation Types and Percent Active Ingredient

The products containing DDAC as the active ingredient (a.i) are formulated as liquid ready-to-use, soluble concentrate, pressurized liquid, and water soluble packaging. Concentrations of DDAC in these products range from 0.08% to 80% as reported on the Master Label spreadsheet (Appendix A).

## 2.2	 Summary of Use Pattern and Formulations

The Agency determines potential exposures to handlers of the product by identifying exposure scenarios from the various application methods that are plausible, given the label uses. These scenarios are identified in Appendix A. Based on a review of product labels, DDAC is the active ingredient in products used in the following use site categories: I (Agricultural premises and equipment), II (Food handling/storage establishments premises and equipment), III (Commercial, institutional and industrial premises and equipment), IV (Residential and public access premises), V (Medical premises and equipment), VIII (Industrial processes and water systems), X (Wood preservatives), XI (Swimming pools), and XII (Aquatic Areas).

From the scenarios in Appendix A, AD selected representative exposure scenarios to assess the labeled uses of DDAC in this document.  These scenarios were selected to be representative of the vast majority of uses and are believed to provide high-end degrees of dermal, inhalation, or incidental ingestion exposure.  The representative scenarios assessed in this document are shown in Table 4.1 (residential) and Table 6.1 (occupational).

# 3.0	SUMMARY OF TOXICITY DATA

## 3.1	Acute Toxicity

The acute toxicity data for DDAC are summarized below in Table 3.1 (USEPA, 2006).

| Table 2. Acute Toxicity Profile for DDAC |
| --- |
| Guideline Number | Study Type/ Test substance (% a.i.) | MRID Number/ Citation | Results | Toxicity Category |
| 870.1100 (§81-1) | Acute oral, rat (Purity 65%) | MRID 41394404 | LD50 =262 mg/kg (combined) | II |
| 870.1100 (§81-1) | Acute oral, rat (Purity 80%) | MRID 42296101 | LD50 =238 mg/kg (combined) | II |
| 870.1200 (§81-2) | Acute dermal, rabbit (Purity 65%) | MRID 42053801 | LD50 =2930 mg/kg (combined) | III |
| 870.1300 (§81-3) | Acute inhalation, rat (Purity not reported) | MRID 00145074 TRID 455201010 | LC50 = 0.07 mg/L (combined) | I |
| 870.2400 (§81-4) | Primary eye irritation, rabbit (Purity 80% a.i.) | MRID 42161602 | Corrosive. | I |
| 870.2500 (§81-5) | Primary dermal irritation, rabbit (Purity 80%) | MRID 42161601 | Corrosive. | I |
| 870.2600 (§81-6) | Dermal sensitization, guinea pigs (Purity 80%) | MRID 46367601 | Not a sensitizer. | NA |

## 3.2	Summary of Toxicity Endpoints

Table 3.2 summarizes the toxicological endpoints for DDAC (USEPA, 2006).  The specific MRID numbers for toxicity studies are referenced in USEPA 2006 and not repeated in this document.

| Table 3.2 Summary of Toxicological Endpoints for DDAC |
| --- |
| Exposure Scenario | Dose Used in Risk Assessment (mg/kg/day) | Target MOE/UF, Special FQPA SF for Risk Assessment | Study and Toxicological Effects |
| Acute Dietary (Females 13-50) | NOAEL(developmental) = 10 mg/kg/day | FQPA SF = 1 UF = 100 (10x inter-species extrapolation, 10x intra-species variation) | Prenatal Developmental Toxicity - Rat MRID 41886701 LOAEL = 20 mg/kg/day based on increased incidence of skeletal variations. |
|  | Acute RfD = 0.1 mg/kg/day (for Females age 13-50) |
| Acute Dietary (general population) | An acute dietary endpoint was not identified in the data base. This risk assessment is not required |
| Chronic Dietary (general population) | NOAEL = 10 mg/kg/day | FQPA SF = 1 UF = 100 (10x inter-species extrapolation, 10x intra-species variation | Chronic Toxicity Study - Dog MRID 41970401 LOAEL = 20 mg/kg/day based on increased incidence of clinical signs in males and females and decreased total cholesterol levels in females. |
|  | Chronic RfD = 0.1 mg/kg/day Dermal, Short-Term (technical a.i.) NOAEL = 2 UF = 100Based on increased dermal clinical and gross findings Rat 90-day Dermal Study MRID 413059-01 |
| Non-Dietary Exposures |
| Incidental Oral Short-Term | NOAEL (developmental) = 10 mg/kg/day | Target MOE = 100 (10x inter-species extrapolation, 10x intra-species variation) FQPA SF = 1 | Prenatal Developmental Toxicity - Rat MRID 41886701 LOAEL = 20 mg/kg/day based on increased incidence of skeletal variations. |
| Incidental Oral Intermediate-Term | NOAEL = 10 mg/kg/day | Target MOE = 100 (10x inter-species extrapolation, 10x intra-species variation) FQPA SF = 1 | Chronic Toxicity Study - Dog MRID 41970401 LOAEL = 20 mg/kg/day based on increased incidence of clinical signs in males and females and decreased total cholesterol levels in females. |
| Dermal, Short-term (formulated product, 0.13% a.i.) | No endpoint identified. No dermal or systemic effects identified in the 21-day dermal toxicity study (MRID 45656601) up to and including the limit dose of 1000 mg/kg/day |
| Dermal, Short-term (TGAI 80% diluted to 0.1% ai) | NOAEL(dermal) = 2 mg ai/kg/day (4 µg ai/cm2)a | Target MOE = 100 (10x inter-species extrapolation, 10x intra-species variation) | 90-day Dermal Toxicity - Rat MRID 41305901 LOAEL = 6 mg ai/kg/day based on increased clinical and gross findings (erythema, edema, exfoliation, excoriation, and ulceration) |
| Dermal, Intermediate- and Long-term (formulated product) | No appropriate endpoint identified. |
| Inhalation, Short-Term | NOAEL b = 10 mg/kg/day | Target MOE = 100 (10x inter-species extrapolation, 10x intra-species variation) FQPA SF = 1 | Prenatal Developmental Toxicity - Rat MRID 41886701 LOAEL = 20 mg/kg/day based on increased incidence of skeletal variations. |
| Inhalation, Intermediate- and Long-Term | NOAEL b = 10 mg/kg/day | Target MOE = 100 (10x inter-species extrapolation, 10x intra-species variation) FQPA SF = 1 | Chronic Toxicity Study - Dog MRID 41970401 LOAEL = 20 mg/kg/day based on increased incidence of clinical signs in males and females and decreased total cholesterol levels in females. |

UF = uncertainty factor, FQPA SF = special FQPA safety factor, NOAEL = no observed adverse effect level, LOAEL = lowest observed adverse effect level, PAD = population adjusted dose (a = acute, c = chronic), RfD = reference dose, MOE = margin of exposure, LOC = Level of concern, NA = Not Applicable.

a  Short-term dermal endpoint = (2 mg/kg rat x 0.2 kg rat x 1000 ug/mg) / 50 cm2  area of rat dosed = 8 µg/cm2.

b an additional uncertainty factor of 10x is used for route extrapolation from an oral endpoint to determine if a confirmatory study is warranted.

## 3.3	FQPA Considerations

The Agency (USEPA, 2006) decided that the FQPA safety factor be removed for DDAC, based upon the existence of a complete developmental and reproductive toxicity database and the lack of evidence for increased susceptibility in these data.

# 4.0	RESIDENTIAL EXPOSURE ASSESSMENT

## 4.1	Summary of Registered Uses

Products containing DDAC can be used as general cleaners, disinfectants, and deodorizers. These products are primarily for use on indoor surfaces such as hard floors, carpets, walls, bathroom fixtures, trash cans, toilet bowls, and household contents.  Additionally, other uses in the home include liquid laundry deodorizers that are added to the final rinse of the wash cycle, algaecide/bacteriocides that are added to portable humidifiers and swimming pools, and deodorizers that are sprayed on fabric.  Residents may also be exposed to items that have been treated with DDAC in occupational settings, such as dimensional lumber for decks and play sets. Appendix A presents a summary of all exposure scenarios that may occur in residential settings based on examination of product labels.  Table 4.1 identifies the representative exposure scenarios assessed in this document.

## 4.2	Residential Exposure

The exposure scenarios assessed in this document for the representative uses selected by AD are shown in Table 4.1. The table also shows the maximum application rate associated with the representative use and the EPA Registration number for the corresponding product label.  It should be noted that for the calculation of application rates in which the density of the product is noted as 8.34 lb/gal, the product is assumed to have the density of water because no product-specific density is available. Handler exposures were assessed for the application of DDAC to indoor hard surfaces, carpets, humidifiers, and swimming pools.  Post-application exposures were assessed for dermal and/or oral contact with treated surfaces including hard floors, carpets, textiles, lumber, and pool water. Post-application/bystander inhalation exposures were assessed for the humidifier use.  DDAC has a low vapor pressure, and therefore, inhalation exposure is to the aerosol generation.

| Table 4.1. Representative Uses Associated with Residential Exposure |
| --- |
| Representative Use | Application Method | Exposure Scenario | Registration # | Application Rate |
| Indoor Hard Surfaces | Mopping Wiping Trigger pump spray | ST Handler: adult dermala and inhalation ST Post-app: child incidental ingestion and dermal | >10% ai 10324-134 1 to 10% ai 10324-80 <1% ai NAb | >10% ai 0.0200 lb a.i./gal (2 oz product/gal water x 15.36% a.i. x 8.34 lb/gal x 1 gal/128 oz) 1 to 10% ai 0.0043 lb ai/gal (3.3% ai x 8.34 lb/gal x 2 oz/gal x 1 gal/128 oz) |
| Carpets | Low pressure spray | ST Handler: adult dermala and inhalation ST Post-app: child incidental ingestion and dermal | >10% ai 10324-108 1 to 10% ai 10324-81 <1% ai NAb | >10% ai 0.0085 lb ai/gal 13.02% ai x 8.34 lb/gal x 1 oz/gal x 1 gal /128 oz) 1 to 10% ai 0.0088 lb ai/gal (4.5% ai x 8.34 lb/gal x 3 oz/gal x 1 gal/128 oz) |
| Swimming pool | Liquid pour | ST Handler: adult dermala and inhalation ST Post-app: ingestion (child and adult) | >10% ai 10324-69 1 to 10% ai 1839-133 <1% ai No products | HANDLERS >10% ai Heavy algae: 0.000017 lb ai/gal (3 ppm) (50.0% x 5.25 oz/10,000 gal x 8.34 lb/gal x 1 gal/128 oz) 1 to 10% ai Winterizing: 0.0000167 lb ai/gal (10.0% x 128 oz/50,000 gal x 8.34 lb/gal x 1 gal/128 oz) POST-APPLICATION Heavy algae: 0.0000488 lb ai/gal (6 ppm) (50.0% x 15 oz/10,000 gal x 8.34 lb/gal x 1 gal/128 oz) |
| Contacting Preserved Wood | NAc | ST Post-app: child incidental ingestion and dermal | 6836-212 | NA |
| Wearing clothing and diapers treated during final rinse cycle of wash | NAd | ST Post-app: adult dermal; child incidental ingestion and dermal | 1677-109 | 0.000733 lb ai/lbs dry fabric (50.0% x 2.25 oz/100 lbs dry fabric x 8.34 lb/gal x 1 gal/128 oz) |
| Wearing clothing treated with fabric spray | NAe | ST Post-app: adult dermal; child incidental ingestion and dermal | 3573-69 | 0.011 lb ai/gal (0.13% ai x 8.34 lb/gal) |
| Humidifier | Liquid pour | ST Handler: adult dermala and inhalation ST Post-app: child and adult inhalation | 10324-80 | 0.0043 lb ai/gal (3.3% ai x 8.34 lb/gal x 2 oz/gal x 1 gal/128 oz) |

a	The dermal risks are based on the short-term dermal endpoint (i.e., rat study) regardless of the percent active ingredient in the product.

b	Application rates for products with <1% ai are not needed because dermal irritation exposures are not assessed for products with <1% ai and the inhalation exposures are assessed with the maximum application for all products.

c	The handlers scenarios were not assessed because the products can only be used by occupational handlers.

d	Handler exposures for application to laundry are represented by the application to humidifiers.

e	Handler exposures were not assessed because products contain <1% ai.

### 4.2.1	Residential Handler Exposures

The residential handler scenarios described in Table 4.1 were assessed to determine dermal and inhalation exposures.  The scenarios were assessed using PHED and CMA data and the equations in Section 1.2, “Criteria for Conducting Risk Assessment.”  A summary of the PHED and CMA data sets are presented in Appendix B.

Unit Exposure Values: Unit exposure values were taken from the PHED data presented in HED’s Residential SOPs (USEPA, 1997) and from the CMA data from the EPA memorandum Evaluation of Chemical Manufacturers Association Antimicrobial Exposure Assessment Study (USEPA, 1999).

- For the mopping scenario, the CMA dermal (hand) and inhalation unit exposure values for ungloved mopping were used (52 mg/lb a.i. and 2.38 mg/lb a.i., respectively).  After normalization for the surface area of the hand (820 cm2), the dermal unit exposure value is 0.063 mg/lb a.i/cm2. These values are based on data collected from six replicates mopping floors and receiving exposure via contact with the mop or with the bucket.

- For the wiping scenario, the CMA dermal (hand) and inhalation unit exposure values for ungloved wiping were used (1,100 mg/lb a.i. and 67.3 mg/lb a.i., respectively). After normalization for the surface area of the hand (820 cm2), the dermal unit exposure value is 1.34 mg/lb a.i/cm2. These values are based on data collected from six replicates (dental technicians) who used a finger pump sprayer to apply the product and then wiped the surfaces with a paper towel.

- For trigger pump scenarios, the PHED dermal (hand) and inhalation unit exposure values are 106 mg/lb a.i. and 2.4 mg/lb a.i., respectively.  After normalization for the surface area of the hand (820 cm2), the dermal unit exposure value is 0.129 mg/lb a.i/cm2. The values are based on homeowners applying an insecticide packaged in an aerosol can to baseboards in kitchens and are representative of a handler wearing short pants and a short sleeve shirt, with no gloves.

- For low pressure handwand, the CMA dermal (hand) and inhalation unit exposure values for ungloved use of a low pressure spray are 132 and 0.681 mg/lb a.i., respectively.  After normalization for the surface area of the hand (820 cm2), the dermal unit exposure value is 0.161 mg/lb a.i/cm2. The values are based on data collected from eight replicates who hand sprayed carpet using 200 psi, then used a push broom rake to raise the carpet nap.

- For liquid pour in swimming pool and humidifier scenarios, the cooling tower CMA data for liquid pour was used for dermal exposures.  This set of data was used because no other CMA data sets represent ungloved replicates pouring liquid.  The dermal hand unit exposure value is 0.196 mg/lb a.i. After normalization for the surface area of the hand (820 cm2), the dermal unit exposure value is 0.000239 mg/lb a.i/cm2. For inhalation exposures, the CMA preservative data were used for swimming pool exposures.  The inhalation unit exposure is 0.00346 mg/lb a.i. and is based on 2 replicates. Although this unit exposure is based on minimal replicates, the exposure value is similar to the one found in PHED for a similar scenarios.  For the humidifier tank scenario, CMA data for liquid pour of disinfectants were used. The inhalation unit exposure value is 1.89 mg/lb a.i. The value is based on data collected from two gloved replicates involving pouring a disinfectant product from a jug into sterilization trays designed for dental instruments, adding water and instruments to the tray, removing the instruments, and discarding the old solution.

Quantity handled/treated: The quantities handled/treated were estimated based on information from various sources, including the Antimicrobial Division’s estimates.

- For mopping scenarios, it is assumed that 1 gallon of diluted solution is used.

- For wiping and trigger pump spray scenarios, it is assumed that 0.5 liter (0.13 gal) of diluted solution is used.

- For low pressure hand wand, it was assumed that 2 gallons are used in all indoor applications.

- For liquid pour in swimming pool scenario, it was assumed that a residential pool contains 20,000 gallons of water.

- For liquid pour in humidifier scenario, it was assumed that a humidifier with a 11 gallon tank would be treated, based on Holmes Model# HM4600-U-11. This humidifier releases 11 gallons/1,700 ft2/24 hours (http://www.holmesproducts.com/estore/product.aspx?CatalogId=3&CategoryId=1120&ProductId=582).

Duration of Exposure: The duration of exposure for most homeowner exposures is believed to be best represented by the short-term duration (1 to 30 days).  The reason that short term duration was chosen to be assessed is because the different handler and post-application scenarios are assumed to be episodic, not daily.  In addition, homeowners are assumed to use different products with varying activities, not exclusively DDAC treated products.

Results

The resulting short-term exposures and MOEs for the representative residential handler scenarios are presented in Tables 4.2 (inhalation) and 4.3 (dermal). The calculated inhalation MOEs are above the target MOE of 100 for all scenarios. The calculated dermal MOEs are above the target MOE of 100 for all scenarios.  A confirmatory inhalation toxicity study may be warranted because inhalation MOE was below 1,000 for the wiping scenario (MOE = 820). The dermal MOEs were below the target MOE of 100 for all scenarios except for the humidifier and swimming pool applications.

| Table 4.2 Short-Term Residential Handler Inhalation Exposures and MOEs |
| --- |
| Exposure Scenario Application Method | Application Method | Application Ratea (lb ai/gallon) | Quantity Handled/ Treated per dayb (gallons) | Unit Exposure (mg/lb a.i.) | Absorbed Daily Dose (mg/kg/day) c | MOE d (Target MOE = 100) |
| Application to indoor hard surfaces | Mopping | 0.020 | 1 | 2.38 | 0.00079 | 13,000 |
|  | Wiping | 0.020 | 0.13 | 67.3 | 0.0029 | 3,400 |
|  | Trigger Spray | 0.020 | 0.13 | 2.4 | 0.00010 | 96,000 |
| Application to Carpets | Low Pressure Spray | 0.0088 | 2 | 0.681 | 0.012 | 50,000 |
| Application to Swimming Pools | Liquid Pour | 0.000017 | 20,000 | 0.00346 | 0.00002 | 510,000 |
| Application to Humidifers | Liquid Pour | 0.0043 | 11 | 1.89 | 0.0015 | 6,700 |

a	Application rates are the maximum application rates determined from EPA registered labels for DDAC.

b	Amount handled per day values are estimates or label instructions.

c	Absorbed Daily dose (mg/kg/day) = [unit exposure (mg/lb a.i.) x application rate (lb ai/gal) x quantity treated (gal/day) x absorption factor (1.0 for  inhalation)]/ Body weight (60 kg for inhalation).

d	MOE = NOAEL / Absorbed Daily Dose.  [Where short-term NOAEL = 10 mg/kg/day for inhalation]. Target MOE = 100.

| Table 4.3 Short-Term Residential Handler Dermal Risks |
| --- |
| Exposure Scenario | Application Method | Application Ratea (lb ai/gal) | Quantity Handled/ Treated per dayb (gallon) | Hand Unit Exposure Adjusted for Surface Area (mg/lb ai/cm2)c | Dermal Skin Irritation Exposure d ((g/cm2) | MOE e (Target MOE = 100) |
| Products with < 1% DDAC |
| No dermal endpoint identified for products with <1% DDAC |
| Products with 1 to 10% DDAC (NOAEL = 8 µg/cm2) |
| Application to indoor hard surfaces | Mopping | 0.0043 | 1 | 0.063 | 0.273 | 29 |
|  | Wiping | 0.0043 | 0.13 | 1.341 | 0.750 | 11 |
|  | Trigger Spray | 0.0043 | 0.13 | 0.129 | 0.072 | 110 |
| Application to Carpets | Low Pressure Spray | 0.0088 | 2 | 0.161 | 2.832 | 3 |
| Humidifier | Liquid Pour | 0.0043 | 11 | 0.000239 | 0.011 | 710 |
| Application to swimming pools | Liquid Pour | 0.000017 | 20,000 | 0.000239 | 0.080 | 98 |
| Products with >10% DDAC (NOAEL = 8 µg/cm2) |
| Application to indoor hard surfaces | Mopping | 0.020 | 1 | 0.063 | 1.27 | 6 |
|  | Wiping | 0.020 | 0.13 | 1.341 | 3.49 | 2 |
|  | Trigger Spray | 0.020 | 0.13 | 0.129 | 0.34 | 24 |
| Application to Carpets | Low Pressure Spray | 0.0085 | 2 | 0.161 | 2.731 | 3 |
| Application to swimming pools | Liquid Pour | 0.000017 | 20,000 | 0.000239 | 0.08 | 98 |

a	Application rates are the maximum application rates determined from EPA registered labels for DDAC.

b	Amount handled per day values are estimates or label instructions.

c	Unit Exposure (mg/lb ai/cm2) = Hand unit exposure from PHED or CMA (mg/lb ai) / surface area of hand (820 cm2).

d	Dermal Skin Irritation Exposure ((g/lb ai/cm2) = Unit Exposure (mg/lb ai/cm2) x Application Rate (lb ai/gal) x Quantity Treated (gal/day) x 1,000 (g/mg

e 	MOE = NOAEL ((g/cm2)/ Dermal Skin Irritation Exposure ((g/cm2).  [Where short-term dermal NOAEL = 8 µg/cm2]. Target MOE = 100.

### 4.2.2	Residential Post-application Exposures

For the purposes of this screening level assessment, post-application scenarios have been developed that encompass multiple products, but still represent a high end exposure scenario for all products represented. As shown in Table 4.1, representative post-application scenarios assessed include crawling on treated hard surfaces, carpets, and treated lumber such as decks/play sets (dermal and incidental oral exposure to children), wearing treated clothing from wash treatment and from spray treatment (dermal exposure to adults and children and incidental oral exposure to children), using portable humidifiers (adult and child inhalation exposure), and swimming in treated pools (adult and child incidental ingestion).

Since no toxicological endpoint of concern was identified for dermal systemic adverse effects, post-application dermal risks were assessed using the toxicological endpoint of concern for dermal irritation.  The residential post-application dermal risks were assessed by comparing the surface residue on the skin (dermal skin irritation exposure) to the short-term dermal irritation endpoint. It was assumed that during the exposure period, the skin repeatedly contacts the treated surface until a steady-state concentration of residues is achieved on the skin.

#### 4.2.2.1 Hard Surface Floor and Carpets

Dermal Exposure to Children from Treated Hard Floors and Carpets

Exposure Calculations

There is the potential for dermal exposure to toddlers crawling on hard floors and carpets after mopping or cleaning with DDAC. Risks were calculated for children contacting treated floors in residential homes. To determine toddler exposure to floor residues, the following equation was used:

E = AR x DTF x DRF x CF1 X CF2						(Eq. 4)

Where:

E	=	Dermal skin irritation exposure (μg/cm2);

AR	=	Application rate (lb/ft2);

DTF	=	Dermal transfer factor (fraction, unitless);

DRF	=	Disinfectant fraction remaining on floor (unitless);

CF1	=	Conversion factor (4.54x108 μg/lb);

CF2	=	Conversion factor (0.00108 ft2/cm2);

Assumptions

Due to limited data, a number of conservative assumptions have been made:

- No transferable residue data were available that could be used to estimate the transfer of DDAC from the floor to skin.  Therefore, it is assumed that 10% of the deposition rate is available for dermal transfer from hard floors and 5% of the deposition rate is available for dermal transfer from carpets (USEPA, 2000 and 2001).

- No data could be found regarding the quantity of solution residue left on the floor after treatment.  As a conservative measure, it has been assumed that 25% of the cleaning solution remains on the floor after the final cleaning/mopping.

- For mopping on hard floors, the labels did not provide information on the volume of disinfectant to be used for cleaning floors.  It was assumed that the diluted treatment solution was applied at a rate of 1 gallon per 1,000 sq. ft. The maximum application rate on the product labels for application to hard surfaces is 0.020 lb ai/gal (see Table 4.1) for a residential setting. Therefore, the application rate used in the post-application hard floor scenarios was 0.000020 lb ai/ft2.  For carpets, the labels stated that 1 gallon of diluted treatment solution should be applied at a rate of 1 gallon per 300 to 500 sq. ft for rotary floor machines.  Using a rate of 1 gallon solution per 300 sq. ft. and a maximum application rate of 0.0088 lb ai/gal (see Table 4.1), the application rate used in the post-application carpet scenarios was 0.0000293 lb ai/ft2.

- It was assumed that the exposed toddler plays regularly on the treated floor.  In a residential home, short-term exposure duration is most likely since homeowners are expected to clean the floor only intermittently.

Results

The calculation of the short-term dermal doses and MOEs are shown in Table 4.4.  The dermal MOEs are below the target MOE of 100 (MOE = 33 for hard surfaces and 45 for carpets).

| Table 4.4. Short-term Dermal Risks Associated with Post-application Exposure from a Treated Hard Surface Floor and Carpet |
| --- |
| Exposure Scenario | Application Rate (lb ai/sq ft) | Product remaining after applying | Percent Transfer Residue | Dermal skin irritation exposure a (µg/cm2) | MOE |
| Hard surface | 0.000020 | 25% | 10% | 0.245 | 33 |
| Carpet | 0.0000293 | 25% | 5% | 0.180 | 45 |

a 	Dermal skin irritation exposure (µg/cm2) = (Application rate, lb/ft2) x (conversion factor, 4.54 E8 µg/lb) x (conversion factor, 0.00108 ft2 /cm2) x (product remaining after mopping, 25%) x (dermal transfer factor, 10% for hard surface and 5% for carpets)

b. 	MOE  = NOAEL (µg/cm2) / Surface Residue on skin (µg/cm2).  Short-term dermal NOAEL is 8 µg/cm2.  Target MOE = 100.

Child Incidental Ingestion Exposure to Treated Hard Floors and Carpets

Exposure Calculations

In addition to dermal exposure, toddlers crawling on treated hard floors will also be exposed to DDAC via incidental oral exposure through hand-to-mouth activity.  To calculate incidental ingestion exposure to these chemicals due to hand-to-mouth transfer, the scenarios established in the Standard Operating Procedures (SOPs) for Residential Exposure Assessments (USEPA 2000 and 2001) were used.  These scenarios use assumptions are similar to those used in calculating exposures due to dermal contact of DDAC from toddlers crawling on treated floors.  Risks were calculated for children contacting treated floors in residential homes and in commercial day care centers.  Typically the day care center scenario is assessed as the intermediate-term duration because the frequency of cleaning is assumed to be greater than that of the residential setting.  However, for DDAC, the short- and intermediate-term incidental oral endpoints are identical.  The following equations were used to determine risks from hand-to-mouth transfer of pesticide residues to toddlers:

PDRnorm= SR x DTF x SA x FQ x ET x SE x CF1					(Eq. 5)

BW

Where:

PDRnorm	=	Potential dose rate (mg/kg/day);

SR		=	Indoor Surface Residue (µg/cm2);

DTF		=	Dermal transfer factor (unitless fraction);

SA		=	Surface area of the hands that contact both the treated area, and the individuals mouth (cm2/event);

FQ		=	Frequency of hand-to-mouth events (events/hr);

SE		=	Saliva extraction efficiency (unitless fraction);

ET		=	Exposure time (hrs/day);

CF1		=	Unit conversion factor (0.001 mg/(g); and

BW		=	Body weight (kg)

SR=AR x DRF x CF2 x CF3

Where:

SR		=		Surface residue on floor (µg/cm2);

AR		=		Application rate (lb ai/ft2);

DRF		=		Disinfectant fraction remaining on floor (25%);

CF2		=		Unit conversion factor (4.54x108 µg/lb); and

CF3		=		Unit conversion factor (0.00108 ft2/cm2)

Assumptions

Due to limited data, a number of conservative assumptions have been made:

- Toddlers (3 years old) were used to represent the 1 to 6 year old age group and are assumed to weigh 15 kg, the median for male and female toddlers (USEPA 2000 and 2001).

- Based on the SOP, it is assumed that the surface area used for each hand-to-mouth event is 20 cm2, and that there are 20 events per hour for short-term exposures (90th percentile (USEPA 2000 and 2001)).

- For hard floors, the exposure time is 4 hours/day, based on the time spent in the kitchen and bathroom for adults. For carpets, the exposure time is 8 hours/day based on the total amount of time spent indoors for young children and subtracting the amount of time spent sleeping, eating, and bathing (USEPA 2000 and 2001).

- The saliva extraction efficiency is 50% (USEPA 2000 and 2001)

- No data could be found regarding the quantity of solution residue left on the floor after treatment.  As a conservative measure, it has been assumed that 25% of the cleaning solution remains after the final mopping or cleaning.

- No transferable residue data were available that could be used to estimate the transfer of DDAC from the floor to skin.  Therefore, it was assumed that 10% of the deposition rate is available for dermal transfer from hard floors and 5% of the deposition rate is available for dermal transfer from carpets (USEPA 2000 and 2001).

Results

The calculation of the short-term oral doses and MOEs are shown in Table 4.5.  The oral MOEs are above the target MOE of 100 (MOE = 760 for hard floors and 520 for carpets).  Note: The short-term duration is protective of the intermediate-term exposures at a day care facility because the toxicity data are identical.

| Table 4.5. Short-term Incidental Oral Risks Associated with Post-application Exposure from a Treated Hard Surface Floor and Carpet |
| --- |
| Exposure Scenario | Appl. Rate (lb ai/ sq ft) | Percent transferable residue | Product remaining after applying | Surface area mouthed (cm2/ event) | Exposure Frequency (events/hr) | Saliva Extraction Factor | Exposure Time (hrs/day) | Surface Residue on floora (µg/cm2) | Potential Dose Rateb (mg/kg /day) | Incidental Oral MOEc |
| Hard Surface | 0.000020 | 10% | 25% | 20 | 20 | 50% | 4 | 2.45 | 0.013 | 760 |
| Carpet | 0.0000293 | 5% | 25% | 20 | 20 | 50% | 8 | 3.60 | 0.019 | 520 |

a 	Surface residue on floor (µg/cm2) = (application rate, lb ai/ft2) x (Disinfectant fraction remaining on floor, 25%) x (conversion factor to convert lb to µg, 4.54E+08 µg/lb) x (conversion factor to convert ft2 to cm2, 1.08E-03 ft2/cm2)

b 	Potential Dose Rate (mg/kg/day) = [(Surface residue on floor, µg/cm2) x (transferable residue, 0.10 for hard floors and 0.05 for carpets) x (exposure time, 4 hrs/day for hard floors and 8hrs/day for carpets) x (surface area of hands, 20 cm2/event) x (exposure frequency, 20 events/hr) x (product remaining after applying, 25%) x (extraction by saliva, 50 %) x (conversion factor to convert (g to mg, 0.001 mg/µg)]/(body weight, 15 kg)

c 	MOE = NOAEL (mg/kg/day) / potential dose rate (mg/kg/day) [Where oral NOAEL = 10 mg/kg/day for short-term].  Target MOE = 100.

#### 4.2.2.2	Textiles

Dermal Exposure to Laundered Clothing-Adult and Child

Exposure Calculations

Some DDAC fabric softener/sanitizing products are added to the final rinse cycle water to provide self-sanitizing and bacteriostatic activity against odor-causing organisms.  To determine dermal skin irritation exposure to treated clothing, the guidance provided in Human and Environmental Risk Assessment (HERA) Guidance Document (2003, 2005) was used.  The following equation, modified from the basic equation provided in HERA (2003), is used to calculate dermal exposure:

Dermal Skin Irritation Exposure (μg/cm2) = AR x F x FD x F1 x F2 x CF1		(Eq. 6)

Where:

AR	=	Application rate in mg a.i./mg weight of fabric;

F	=	Weight fraction of the chemical left on the clothing after the final spin;

FD	=	Fabric density (mg/cm2);

F1	=	Weight fraction transferred from clothing to skin;

F2	=	Weight fraction remaining on skin; and

CF1	=	Conversion factor, 1,000 μg/mg.

Assumptions

- The application rate is 0.000733 mg a.i/mg weight of fabric, based on product label # 1677-109.

- In HERA (2003), it was determined that 2.5% of the chemical in the laundry detergent remains after the final rinse cycle.  It is assumed that a washing machine containing laundry, detergent, and water would go through an agitation period, then spin dry, then refill with fresh water for rinsing, agitate, and then spin dry again.  Assuming that the fraction of chemical removed during each spin dry cycle is the same, then:

Mf / Mi = Xspin2 = 0.025	(Eq. 7)

Where:

Mf	=	Mass of chemical remaining on clothing after the final rinse,

Mi	=	Mass of chemical originally added to laundry machine, and

Xspin	=	Fraction of chemical remaining after each spin cycle.

The quantity Xspin is squared because the laundry and the detergent undergo two spin cycles. For assessment of fabric softener/sanitizer, the fraction of chemical remaining will be equivalent to Xspin, since the fabric softener/sanitizer, which is applied during the rinse cycle, will only undergo one spin cycle.  Taking the square root of both sides of Equation 7 gives an Xspin value of 0.158, or 15.8%.

- The fabric density is 10 mg/cm2, which is the value provided in HERA (2003) for mixed cotton and synthetics.

- No leaching data were available that could be used to estimate a flux rate of the chemical from clothing.  Exposures were calculated using a conservative transfer factor of 100%, which assumes that all residues are transferable from clothing surfaces to the skin, and using HERA’s value of 1% transfer (HERA, 2003).

- No dissipation data were available; therefore, the amount of DDAC remaining on the skin is assumed to be 100 percent.

Results

The resulting short-term dermal exposures and MOEs are presented in Table 4.6.  The dermal MOE was above the target MOE of 100 assuming the 1% transfer, and therefore, not of concern.  A confirmatory study to determine the percent transfer is warranted as the MOE estimated assuming 100% transfer is of concern.

| Table 4.6. Short- and Intermediate-term Dermal Post-application Exposure and MOE for Contacting Laundered Clothing – Adult and Child |
| --- |
| Parameter | Value | Rational |
| Application rate | 0.000733 mg a.i/mg weight of fabric | See Table 4.1 |
| Weight fraction of residue remaining after final spin | 15.8% | Eq. 7 |
| Fabric density | 10 mg/cm2 | Mixed cotton and synthetics (HERA 2003) |
| Residue transfer factor from clothing to skin | 1% and 100% | HERA 2003 and EPA assumption |
| Weight fraction remaining on skin | 100% | HERA, 2003 |
| Dermal Exposurea | 1% = 0.0116 μg/cm2 100% = 1.16 μg/cm2 | Eq. 6 |
| Dermal NOAEL | 4 μg/cm2 | Dermal endpoint selected |
| Dermal Short-term MOEb | 1% = 690 100% = 7 | Eq. 3b (Target MOE = 100) |

a	Dermal Exposure (μg/cm2) =(Application rate, 0.000733 mg a.i/mg weight of fabric) x  (residue left after spin cycle, 15.8%) x (fabric density, 10 mg/cm2) x (weight fraction transferred from clothing to skin) x (weight fraction remaining on skin) x  (conversion factor, 1000 μg/mg)

b 	MOE = NOAEL (μg/cm2) / dermal exposure (μg/cm2) [Where short-term dermal NOAEL = 8 μg/cm2].  Target MOE = 100.

Incidental Oral Exposure to Laundered Clothing-Adult and Child

Exposure Calculations

Oral exposure associated with toddlers mouthing clothing was assessed using an equation similar to that used for assessing dermal exposure to laundered clothing:

Oral Exposure (mg/kg/day) = AR x F x FD x Smouthed x SE				(Eq. 8)

BW

Where:

AR	=	Application rate in mg a.i./mg weight of fabric;

F	=	Weight fraction of the chemical left on the clothing after the final spin;

FD	=	Fabric density (mg/cm2);

Smouthed	=	Surface area of fabric that is mouthed (cm2);

SE	=	Saliva extraction factor; and

BW	=	Body weight (kg).

Assumptions

- The surface area of fabric mouthed is 100 cm2 (HERA, 2003).

- The saliva extraction factor is 50% (USEPA 2000 and 2001).

- Assumptions regarding fabric density and weight fraction of chemical left after final spin are identical to those used for the assessment of dermal exposure to laundered clothing.

Results

The resulting short-term oral exposure and MOE are presented in Table 4.7.  The oral MOE was above the target MOE of 100.

| Table 4.7. Short-term Incidental Oral Postapplication Exposure and MOE for Contacting Laundered Clothing – Child |
| --- |
| Parameter | Value | Rational |
| Application rate | 0.000733 mg a.i/mg weight of fabric | See Table 4.1 |
| Weight fraction of residue remaining after final spin | 15.8% | HERA 2005 |
| Fabric density | 10 mg/cm2 | Mixed cotton and synthetics (HERA 2003) |
| Surface area of clothing available for mouthing | 100 cm2 | HERA 2003 |
| Saliva Extraction Factor | 50% | USEPA 2000 and 2001 |
| Body weight | 15 kg | EPA 1997, median body weight |
| Oral Exposurea | 0.00386 mg/kg/day | Eq. 8 |
| Oral NOAEL | 10 mg/kg/day | Oral endpoint selected |
| Short-, intermediate-term MOEb | 2,600 | Eq. 3 |

a	Oral Exposure  (mg/kg/day) = (Application rate, 0.000733 mg a.i/mg weight of fabric) x (residue left after spin cycle, 15.8%) x (fabric density, 10 mg/cm2) x (surface area mouthed, 100 cm2) x (Saliva extraction factor, 50%) / (body weight, kg)

b 	MOE = NOAEL (mg/kg/day) / potential daily dose (mg/kg/day) [Where short-term oral NOAEL = 10 mg/kg/day].  Target MOE = 100.

#### Dermal Exposure to Clothing Treated with Fabric Spray

Exposure Calculations

There is the potential for dermal exposure to children wearing clothing treated with a trigger-pump spray product containing antimicrobials.  The product label (3573-69) indicates to spray fabric until damp and to allow surface to dry before use. The dermal skin irritation exposure is calculated using following equation and assumptions:

E = C x TR										(Eq. 9)

Where:

E	= 	Dermal Skin irritation Exposure ((g/cm2); and

C 	= 	Concentration on clothing ((g ai/cm2).

TR	=	Transferable residue from clothing to skin (%);

C = A x WF x CF

Where:

C	=	Concentration on clothing ((g ai/cm2);

A 	= 	Water absorption rate of Whatman absorbent materials (198 mg/cm2);

WF 	=	Weight fraction of product (% ai); and

CF	=	Conversion factor (1,000 (g/mg).

Assumptions

- Whatman, Inc. sells “absorbent sinks”, reels of absorbent materials for use in laboratories (Whatman, 2005).  One of their products, CF7, is composed of 100% cotton and is 1.9 mm-thick.  This product has a stated water absorption rate of 198 mg/cm2.  Since 1.9 mm seems a reasonable thickness for clothing, and it is assumed that the spray product is used until the clothing is thoroughly wet (conservative assumption), an application rate of 198 mg product/cm2 is assumed unless product specific data are submitted.

- If data are not available from which a transfer factor could be estimated, potential doses are calculated using a conservative transfer factor of 100%, which assumes that all residues are transferable from clothing surfaces.  Potential doses can also be calculated using a less conservative transfer factor of 5%, which is based on the amount of residue assumed to be transferable from carpeted surfaces (USEPA, 2001) but confirmatory data will be requested to support this assumption.

Results

The resulting short-term oral exposure and MOE are presented in Table 4.8.  The dermal MOEs were below the target MOE of 100 for both the 100% and 5% transfer factors (MOEs are less than or equal to 1).

| Table 4.8. Short-term Dermal Risks Associated with Post-application Exposure from a Clothing Treated with a Fabric Spray |
| --- |
| Weight fraction of product (%ai) | Water absorption rate of Whatman absorbent materials (mg/cm2); | Concentration of Clothing (µg/cm2) | Percent Transfer Residue | Dermal skin irritation exposure a (µg/cm2) | MOE (Target MOE = 100) |
| 0.0013 | 198 | 257 | 100% | 257 | <1 |
| 0.0013 | 198 | 257 | 5% | 12.9 | 1 |

a	Concentration on clothing (µg/cm2) = % active ingredient / 100 * Product absorption rate (198 mg/cm2)* conversion factor (1,000 µg/mg)

b	Dermal Skin Irritation Exposure (µg/cm2) = (concentration on clothing, µg/cm2) * (percent transferable residue from textile).

c 	MOE = NOAEL (µg/cm2) / Dermal Skin Irritation Exposure (µg/cm2)  [Where short-term dermal NOAEL = 8 µg/cm2.  Target MOEs = 100.

Incidental Oral Exposure to Children Mouthing Clothing Treated with Fabric Spray

Exposure Calculations

There is the potential for incidental oral exposure to children from mouthing textiles treated with a trigger-pump spray product containing DDAC.

Potential doses are calculated as follows:

PDD = C x SA x SE									(Eq. 10)

BW

where:

PDD	= 	potential daily dose (mg/kg/day)

C 	= 	concentration on clothing (mg/cm2)

SE	=	saliva extraction efficiency (%)

SA 	= 	Surface area mouthed (cm2/day)

BW 	= 	body weight (kg)

Assumptions

- The concentration of the chemical on clothing was determined using same methodology as discussed in the previous section, post-application dermal exposure to textiles.

- The surface area of textiles mouthed by children is 100 cm2 (HERA 2003).

- The saliva extraction efficiency is 50% (USEPA 2000 and 2001).

- Toddlers (3 years old) are used to represent the 1 to 6 year old age group.  For three-year olds, the median body weight is 15 kg (USEPA 1997).

Results

Table 4.9 shows the calculation of the oral dose and oral MOE for children mouthing treated textiles. The MOE value is below the target MOE of 100 (MOE = 12).

| Table 4.9. Short-term Post-application Incidental Oral Exposures and MOEs for Children Contacting Clothing Treated with a Fabric Spray |
| --- |
| % a.i. | Product absorption rate (mg/cm2) | Concentration on clothinga (mg/cm2) | Area mouthed (cm2/day) | Saliva Extraction Factor | Potential daily dose (mg/kg/day) | Incidental Oral MOEc |
| 0.13 | 198 | 0.257 | 100 | 50% | 0.857 | 12 |

a	Concentration on clothing (mg ai/cm2) = % active ingredient/100 * Product absorption rate (198 mg/cm2)

b	Potential Daily Dose (mg/kg/day) = (Concentration on clothing, mg/cm2) * (area mouthed, cm2/day) * (saliva extraction factor, unitless fraction) / (body weight, kg).

c 	MOE = NOAEL (mg/kg/day) / absorbed potential daily dose [Where short-term oral NOAEL = 10 mg/kg/day].  Target MOE = 100.

#### 4.2.2.3		Treated Lumber

Scenarios

The Agency is concerned that there are potential residential post-application exposure to children and adults exposed to DDAC treated wood.  The potential outdoor residential post-application exposure pathways considered are outlined below:

Children

•	Dermal contact with DDAC-treated wood products (e.g., residential playground equipment, utility poles, posts, decks, shingles, fencing, lumber, piers, etc.);

•	Incidental ingestion due to hand-to-mouth contact with DDAC-treated wood products;

•	Incidental ingestion of soil contaminated with DDAC;

•	Dermal contact with soil contaminated with DDAC (e.g., soil contaminated by treated decks and playground equipment); and

Adults

•	Dermal contact with wood from construction of decks and playground equipment;

•	Incidental ingestion with wood from construction of decks and playground equipment.

Currently, there are no study data that can be used to estimate either exposure to adults during construction of wood decks or to children exposed to treated wood.  Incidental ingestion exposure for adults is expected to be negligible and dermal contact for adults is expected to be lower than children for crawling on wood decks.  Because children exhibit a more intense play contact on surfaces and have a higher surface area to body weight ratio, they would generally be considered to represent the maximum exposed individual.

Available data to assess the levels of DDAC in soil contaminated with DDAC-treated wood do not exist at this time.  In addition, leaching data were also not available.  Because of this data gap, EPA was not able to estimate dermal and incidental ingestion residential post-application exposures to soil contaminated with DDAC-treated wood.

In this assessment, incidental ingestion and dermal exposures to children from contact with treated wood were estimated using DDAC exposure data from an occupational exposure study, “Measurement and Assessment of Dermal and Inhalation Exposures to Didecyl Dimethyl Ammonium Chloride (DDAC) Used in the Protection of Cut Lumber (Phase III)” (Bestari et al., 1999, MRID 455243-04).  The data were used for the following pathways: outdoor residential dermal contact with DDAC-treated wood products (e.g., residential playground equipment, utility poles, posts, decks, shingles, fencing, lumber, piers, etc.); and outdoor residential incidental ingestion due to hand-to-mouth contact with pressure-treated wood products.  The DDAC study measured dermal and inhalation exposures for various worker functions/positions for individuals handling DDAC-containing wood preservatives for non-pressure treatment application methods and for individuals that could then come into contact with the preserved wood.

Outdoor Residential Dermal Contact with DDAC-treated Wood Products

Potential risks resulting from children’s dermal contact with DDAC-treated wood are assessed using maximum and average worker residue data for hands available in the DDAC study. The data in Table 4.10 were used to approximate the residues transferred from treated wood to skin.  No other data are available (e.g., no wipe data).  The data from the following job descriptions in the DDAC study were chosen because of the possibility of the contact with dry treated wood.  The average and maximum concentrations of these data (1.4  and 3.0 (g/cm2) were assumed to be the dermal skin irritation exposure.  The results indicate that the dermal MOEs are below the target MOE.  However, these estimates are only reported as a range finder to determine if a wipe study is warranted.   Based on the results the wipe study is warranted.

- End Stacker - Operates an automated stacking system at the end of the conveyor.  Lumber stacked into loads.

- Stickman - Places sticks between stacks of wood manually.  At some mills, this is done automatically by end stacker operator.

- Tallyman - Staples information sheet on to wood.  May come in contact with treated lumber. (Note: there were two reps available for tallyman)

| Table 4.10. Hand Residue Data for DDAC for Handling of Dry Wood |
| --- |
| Job Description | Total Hand Residue Data (μg/cm2) |
| End Stacker | 1.2 |
| Stickman | 0.6 |
| Tallyman | 0.8 |
| Tallyman | 3.0 |
| Average | 1.4 |
| Dermal Skin Irritation Exposurea (μg/cm2) | 1.4 and 3.0 |
| MOEb (Target MOE =100) | 6 average and 3 maximum |

a	Dermal Skin Irritation Exposurea (μg/cm2)= 1.4  and 3.0μg/cm2 average and maximum hand residues, respectively

b	MOE  = NOAEL (μg/cm2) / dermal skin irritation exposure (μg/cm2).  Dermal NOAEL is 8 μg/cm2.  Target MOE = 100.

Outdoor Residential Hand-to-Mouth Contact with DDAC--treated Wood Products

Potential risks from a child’s hand-to-mouth activities are also assessed using worker residue data for hands that are available in the DDAC study. The most appropriate hand values to estimate potential residues of a child playing on treated decks/playground structures are for the “dry” strata test subjects (as defined above).  These test subjects handled the dry treated wood from the non pressure treatments.  Of the 20 test subjects measured for handling “dry” wood in the DDAC study, 19 had detectable hand values (one value non-detect) ranging from 0.04 to 3.0 µg/cm2 (DDAC study page 104).  The highest value (most conservative) (3.0 µg/cm2) represents the “Tallyman” that wore no gloves (DDAC study page 189).

The daily hand-to-mouth dose (mg/kg/day) is estimated using the following equation:

Oral Dose t= Handt x Hand SA x SEF x  Frequency x CF1  x  ET 		(Eq. 11)

BW

Where:

Handt 		=	DDAC highest hand residue detected (i.e.,“Tallyman” working

with dry wood (μg/cm2)),

Hand SA	=	hand surface area (cm2/event),

SEF		=     	saliva extraction factor (unitless),

Frequency 	= 	frequency of exposure event (events/hr),

ET		=	exposure time (hr/day),

CF1		=	conversion factor (0.001 mg/µg), and

BW		=	body weight (kg).

In addition to the hand residue value from the DDAC study, the following inputs are used in the hand-to-mouth estimate:

- The palmar surface area of 3 fingers of a toddler, 20 cm2, is used to estimate hand-mouthing as opposed to whole hand mouthing (USEPA 2001).

- The rate of hand-to-mouth activity for outdoor playing is 7 events per hour based on Freeman et. al (2001) at the 95th percentile.

- The exposure time (ET) is 2 hours and is consistent with the Agency’s CCA assessment for time playing outdoors.  Although the 2 hour duration represents “outdoor” time, it is used as a conservative estimate for playing on decks and playsets.

- The saliva extraction factor (SEF) is 0.5 and is based on the assumption of 50 percent removal efficiency of residues from hands by human saliva (USEPA 2001).

- The mean body weight of a child at age 3 is 15 kg.

The results of the hand-to-mouth estimates are presented in Table 4.11.  The estimated short-term MOE for the hand-to-mouth exposure is above the target MOE of 100 (MOE = 360) and is not of concern.  Because the dermal and oral endpoints represent different toxicological effects, an aggregate of the dermal (discussed above) and oral MOEs are not appropriate.

| Table 4.11: Residential Post-application Incidental Oral Exposures with DDAC-treated Wood Product |
| --- |
| Hand concentration from DDAC Study (µg/cm2) | Finger surface area (cm2) | Exposure Frequency for outdoor playing (events/hr) | Saliva Extraction Factor | Exposure Time (hrs/day) | Average Daily Oral Dose a (mg/kg/day) | Incidental Oral MOEb (Target MOE = 100) |
| 3.0 | 20 | 7 | 0.5 | 2 | 0.028 | 360 |

a	Average Daily Oral Dose (mg/kg/day) = [handt (3 μg/cm2 ) x Hand SA (20 cm2) x SEF (0.5) x Frequency (7 events/hr) x Exposure Time (2 hrs/day) x 0.001 mg/μg] / BW (15 kg)

b	MOE  = NOAEL (mg/kg/day) / daily dose (mg/kg/day).  For oral, NOAEL is 10 mg/kg/day.  Target MOE = 100.

#### 4.2.2.4	Swimming Pools

There are post-application exposures associated with use of DDAC products in swimming pools and spas.  For swimming pools, only incidental oral exposures are assessed in this document.  Dermal and inhalation exposures are expected to be negligible due to the low concentration of DDAC in pool water and the low vapor pressure of DDAC.  Because the amount of exposure will most likely be greater for swimming pools than for spas, swimming pool scenarios were evaluated to represent the high-end exposures associated with use of DDAC in pools and spas.

The SWIMODEL 3.0 was developed by EPA as a screening tool to conduct exposure assessments of pesticides found in swimming pools and spas (Versar, 2003). The SWIMODEL uses well-accepted screening exposure assessment equations to calculate the total worst-case exposure for swimmers expressed as a mass-based intake value (mg/event). The model focuses on potential chemical intakes only and does not take into account metabolism or excretion of the chemical of concern.  Detailed information and the downloadable executable file are available at http://www.epa.gov/oppad001/swimodel.htm.  For this assessment, the actual model was not used, however, the same equations as provided in the SWIMODEL User's Manual (version 3.0) were used in a spreadsheet format to estimate post application incidental oral and inhalation exposures for use of DDAC in swimming pools.

It should be noted that this exposure assessment identifies short-term (1-30 days) and intermediate-term (1-6 months) noncancer exposure doses based on the reported toxicology endpoints for DDAC.  Because of the shorter exposure durations of these toxicological endpoints, conservative event-based exposure assumptions are used to calculate upper bound daily dose estimates.  The noncancer doses are not amortized over a lifetime.

Post-application Incidental Ingestion Exposure through Swimming Pool Use

The following equation was used to calculate incidental ingestion doses:

PDR = Cw x IR x ET 							(Eq. 12)

BW

Where:

PDR	= 	Potential dose rate (mg/kg/day);

Cw	=	Chemical concentration in pool water (mg/L);

IR	=	Ingestion rate of pool water (L/hr);

ET	=	Exposure time (hrs/day); and

BW	=	Body weight (kg).

Assumptions

- For short-term exposures, it was assumed that the concentration in water after shock treatment is 6.00 ppm (6.0 mg DDAC/L).  This concentration is based on the application of 7.5 oz to the pool skimmers/lines per day (regardless of the pool volume) for two consecutive days to treat heavy algae contamination as per label 10324-69.  Thus the pool concentration would be 15 oz (for two days of treatment) per pool.  EPA uses a 20,000 gallon pool volume for the assessment.  It is likely that the DDAC concentration in water would decrease after the 24 to 48 hour waiting period specified in the label but AD does not have data to indicate the dissipation of DDAC in pool water.

- The ingestion rate is based on the value used in EPA’s Residential SOPs (USEPA 2000) and an EPA pilot study as discussed in ACC’s swimmer survey (ACC, 2002b).

- Exposure time for non-competitive swimmers is based on the summary statistics from the National Human Activity Pattern Survey (NHAPS) (USEPA, 1996) whereas competitive swimmer exposure time data are based on the Agency’s review of the American Chemistry Council (ACC) study (ACC, 2002b).

- The assumed body weight is 60 kg for adults, 48 kg for children (age 11-14 years), and 30 kg for children (age 7-10 years).

| Table 4.12. Parameters for Swimming Ingestion Exposure and Dose Estimate |
| --- |
| Population | Adult | Child 7-10 yrs | Child 11-14 yrs |
| Type of Swimmer | Competitive | Non- Competitive | Competitive | Non- Competitive | Competitive | Non- Competitive |
| Cw (mg/L) – Short term exposure | 6.0 | 6.0 | 6.0 | 6.0 | 6.0 | 6.0 |
| IR (L/hr) | 0.0125 | 0.0125 | 0.05 | 0.05 | 0.025 | 0.05 |
| ET(hr/day) | 3 | 2a | 1 | 3a | 2 | 2.6a |
| BW(kg) | 60 | 60 | 30 | 30 | 48 | 48 |

a	90th percentile values

Short-term MOE values were calculated for ingestion of swimming pool water and are presented in Table 4.13.  The calculations for short-term incidental ingestion of DDAC indicate no risk concern for the non-competitive or competitive swimming pool scenarios (i.e., MOE>100).

| Table 4.13. Short-Term Ingestion Dose and MOE for Residential Swimming Post-Application |
| --- |
| Use Type | Scenario Description | Ingestion Dose (mg/kg/day) | Ingestion MOE a |
| Swimming Pool | Adult, Competitive | 0.0038 | 2,700 |
|  | Adult, Non-Competitive | 0.0025 | 4,000 |
|  | Child (7-10 yrs), Competitive | 0.0100 | 1,000 |
|  | Child (7-10 yrs), Non-Competitive | 0.030 | 330 |
|  | Child (11-14 yrs), Competitive | 0.0063 | 1,600 |
|  | Child (11-14 yrs), Non-Competitive | 0.0163 | 620 |

aMOE = NOAEL (mg/kg/day)/ Ingestion Dose (mg/kg/day).  Short-term Oral NOAEL = 10 mg/kg/day. Target MOE = 100

#### 4.2.2.5	Humidifiers

Inhalation Exposures for Portable Humidifiers - Adult and Child

Inhalation exposures to DDAC used in portable humidifiers may also occur.  To determine potential inhalation risk, the Multi-Chamber Concentration and Exposure Model (MCCEM v1.2) was used to provide a screening-level estimate of potential inhalation risk to adults and children.  MCCEM estimates average and peak indoor air concentrations of chemicals released from products or materials in houses, apartments, townhouses, or other residences.  It estimates inhalation exposures to chemicals, calculated as single day doses, chronic average daily doses, or lifetime average daily doses.  All dose estimates calculated by MCEMM are potential doses; they do not account for actual absorption into the body.

Assumptions

- The entire house is being humidified; therefore, a single chamber model was run.

- A person is exposed to the release for either 8-hours a day or 24-hours a day.

- The inhalation rates for the 8-hour exposure period are based on the sedentary activities (0.5 m3/hr for adults and 0.4 m3/hr for children).  The inhalation rates for the 24-hour exposure period are based on the chronic inhalation rates (13.3 m3/day for adults and 8.3 m3/day for children) (USEPA 1997).

- For the 8-hr exposure duration assessment, the MOE was calculated using concentrations from 0 to 8 hours after the humidifier was turned on. For the 24-hr exposure assessment, it was assumed that the humidifier had already been running for the previous day; therefore, the concentrations from 24 to 48 hours after the fogger was turned on were used.

- Release of the product occurs at a steady state throughout the day (constant emission rate from one source).

- The label indicated that 2 oz of product should be used per gallon. The label did not provide information on the quantity of solution that is released per hour.  A release rate of 11 gallons/1,700 ft2/24 hours was used in this assessment based on the Holmes Model# HM4600U. (http://www.holmesproducts.com/estore/product.aspx?CatalogId=3&CategoryId=1120&ProductId=582). It was assumed that 11 gallons of the dilute solution would be released into the generic MCCEM house (approximately 1,800 ft2 assuming 8 ft ceilings) over a 24-hour period. Based on an application rate of 0.0043 lb ai/gal, approximately 0.895 g ai/hr would be emitted into the house.

- It was assumed that 100% of the product is inhalable.

Results

The resulting short- and intermediate-term inhalation exposure and MOE for the representative post-application inhalation scenarios are presented in Table 4.14 and 4.15.  The 8-hr and the 24-hr MOEs for children and adults are below the target MOE of 100.

| Table 4.14. Short- and Intermediate-term Post-application Exposures and MOEs for Adults and Children in Houses Being Humidified (8-hr Exposure Duration) |
| --- |
| Parameter | Value | Rationale |
|  | Adult | Child |  |
| Housea | Generic House (1-chamber) | A portable humidifier that humidifies the entire house |
| Activity Schedule | Average concentration starting at 0 hour through 8 hours | EPA Assumption |
| Air Exchange Rate | 0.18/hr | MCCEM default |
| Application Rate | 0.0043 lb ai/gal | Chemical specific product label |
| Quantity Dilute Used | 11 gallons/24 hours | Holmes Model# HM4600-U |
| Emission Ratea | 0.895 gram ai/hr | Application rate (lb ai/gal) * Use amount (gal/hr) * CF (g/lb) |
| Body Weighta | 60 kg | 15 kg | Average body weights for adults and young children |
| Inhalation Ratea | 12 m3/day (0.5 m3/hr) | 9.6 m3/day (0.4 m3/hr) | Sedentary rate for adults and young children (USEPA, 1997) |
| MCCEM Outputs |
| Average Concentration over 8-hrs (mg/m3) | 5.59 | 5.59 | Average of MCCEM-calculated air concentrations from 0 to 8 hrs |
| Dose (mg/kg/day) | 0.373 | 1.19 | Average Conc. * 8 hrs * Inhal. Rate / BW |
| Inhalation short- and intermediate-term MOEb | 27 | 8 | NOAEL (10 mg/kg/day) / Dose |

a		Used as MCCEM input.  Default values from MCCEM were used for all inputs not listed in the table above.

b 	MOE = NOAEL (mg/kg/day) / daily dose (mg/kg/day) [Where short-, intermediate-term inhalation NOAEL = 10 mg/kg/day].  Target MOE = 100.

| Table 4.15. Short- and Intermediate-term Post-application Exposures and MOEs for Adults and Children in Houses Being Humidified (24-hr Exposure Duration) |
| --- |
| Parameter | Value | Rationale |
|  | Adult | Child |  |
| Housea | Generic House (1-chamber) | A portable humidifier that humidifies the entire house |
| Activity Schedule | Average concentration starting at 24 hour through 48 hours | EPA Assumption |
| Air Exchange Rate | 0.18/hr | MCCEM default |
| Application Rate | 0.0043 lb ai/gal | Chemical specific product label |
| Quantity Dilute Used | 11 gallons/24 hours | Holmes Portable Humidifier Model# HM1285 |
| Emission Ratea | 0.895 gram ai/hr | Application rate (lb ai/gal) * Use amount (gal/hr) * CF (g/lb) |
| Body Weighta | 60 kg | 15 kg | Average body weights for adults and young children |
| Inhalation Ratea | 13.3 m3/day | 8.3 m3/day | Chronic rate for adults and young children (USEPA, 1997) |
| MCCEM Outputs |
| Average Concentration over 24 hrs (mg/m3) | 12.2 | 12.2 | Average of MCCEM-calculated air concentrations from 24 to 48 hrs |
| Dose (mg/kg/day) | 0.90 | 2.24 | Average Conc. * 24 hrs * Inhal. Rate / BW |
| Inhalation short-, intermediate-term MOEb | 11 | 5 | NOAEL (10 mg/kg/day) / Dose |

a		Used as MCCEM input.  Default values from MCCEM were used for all inputs not listed in the table above.

b 	MOE = NOAEL (mg/kg/day) / potential daily dose (mg/kg/day) [Where short-, intermediate-term inhalation NOAEL = 10 mg/kg/day].  Target MOE = 100.

### 4.2.3	Data Limitations/Uncertainties

There are several data limitations and uncertainties associated with the residential handler and post-application exposure assessments.  These include the following:

- Surrogate dermal and inhalation unit exposure values were taken from the proprietary Chemical Manufacturers Association (CMA) antimicrobial exposure study (USEPA, 1999: DP Barcode D247642) or from the Pesticide Handler Exposure Database (USEPA, 1998) (See Appendix B for summaries of these data sources). Most of the CMA data are of poor quality, therefore, AD requests that confirmatory monitoring data be generated to support the values used in these assessments.

- The quantities handled/treated were estimated based on information from various sources, including HED’s Standard Operating Procedures (SOPs) for Residential Exposure Assessments (USEPA 2000 and 2001).  In certain cases, no standard values were available for some scenarios.  Assumptions for these scenarios were based on AD estimates and could be further refined from input from registrants.

- Some labels for products which can be used by homeowners in residential settings, as well as by workers in occupational settings, indicate that low pressure sprayers can be used for application of the disinfectant to hard, non-porous surfaces such as floors and walls. A residential low pressure spray scenario was not assessed for the residential scenario because it is not a typical cleaning method for homeowners.

- At this time, the Agency does not have exposure data to assess oral exposures to children and adults from using treated mouthpieces and reeds; therefore, the Agency is requesting residue data from treated mouthpieces and reeds.

- In this assessment, incidental ingestion and dermal exposures to treated wood were estimated using DDAC data from the occupational exposure study.  The degree of uncertainty (under- or overestimation) associated with using the DDAC hand residue data for dermal and oral exposure from contacting treated lumber are unknown.  The amount of residue measured on the test subjects hands is variable and are influenced by the duration of exposure, how often wood is contacted, and the degree of contact (i.e., do the hand residues from the DDAC study mimic a child’s play activity on decks and playsets?).

- Available data to assess the levels of DDAC in soil contaminated with DDAC-treated wood do not exist at this time.  In addition, leaching data were also not available. Because of this data gap, EPA was not able to estimate dermal and incidental ingestion residential post-application exposures to soil contaminated with DDAC-treated wood.

# 5.0	RESIDENTIAL AGGREGATE RISK ASSESSMENT AND CHARACTERIZATION – To be determined in the risk assessment.

# 6.0	OCCUPATIONAL EXPOSURE ASSESSMENT

The exposure scenarios assessed in this document for the representative uses selected by AD are shown in Table 6.1. The table also shows the maximum application rate associated with the representative use and the appropriate EPA Registration number for the product label.  It should be noted that for the calculation of application rates in which 8.34 lb a.i./gal is noted, the product is assumed to have the density of water because no product-specific density is available.  Appendix A presents a summary of all exposure scenarios that may occur in occupational settings based on examination of product labels.

Potential occupational handler exposure can occur in various use sites, which include: agricultural premises, industrial processes and water systems, food handling premises, commercial/institutional/industrial premises, medical premises, swimming pools, and aquatic areas.  Additionally, occupational exposure can occur during the preservation of wood. For the preservation of wood, the procedure for treatment can occur in different ways, such that multiple worker functions were analyzed. Due to the complexity of the wood preservative analysis, the results for handler and post-application exposures are presented separately in Section 6.3.

| Table 6.1. Representative Exposure Scenarios Associated with Occupational Exposures to DDAC |
| --- |
| Representative Use | Method of Application | Exposure Scenario | Registration # | Application Rate |
| Agricultural Premises (Use Category I) |
| General Disinfectant for Hard Surfaces, Equipment, Vehicles | Low pressure handwand High Pressure Spray Wiping surface Trigger pump spray Mopping | ST/IT Handler: Inhalation | 10324-81 | 0.0094 lb ai/gal (4.5% a.i. x 3.2 fl. oz/gal water x 1 gal/128 fl. oz x 8.34 lb/gal Florist use) Deodorize garbage cans 4.25 oz/gal or 0.013 lb ai/gal Typical rate 0.78 oz/gal or 0.0023 lb ai/gal |
| Fogger | Liquid pour | ST/IT Handler (mix/load only): Inhalation ST Post-application: inhalation | 10324-81 | 0.22 lb ai/gal (4.5% a.i. x 74.8 fl. oz/gal water x 1 gal/128 fl. oz x 8.34 lb/gal) |
| Food Handling (Use Category II) |
| Indoor Hard Surfaces (including dishes, utensils, equipment) | Low pressure handwand Mop Wipe Trigger pump sprayer | ST/IT Handler: inhalation | 10324-134 | 0.0200 lb a.i./gal (2 oz product/gal water x 15.36% a.i. x 8.34 lb/gal x 1 gal/128 oz) |
|  | Flood Immersion Circulation (Liquid pour) | ST/IT Handler: inhalation | 1839-173 | 0.00196 lb ai/gal (4.5% a.i. x 0.78 oz product/ gal water x 8.34 lb/gal x 1gal/128oz) |
| Fogger | Liquid pour | ST Post-application: Inhalation | 10324-80 | 0.0065 lb ai/gal (3.3% ai x 8.34 lb ai/gal x 3 oz/gal x 1 gal/128 oz) |
| Commercial/Industrial/Institutional Premises (Use Category III) |
| Indoor Hard Surfaces | Low pressure handwand Mop Wipe Trigger pump sprayer | ST/IT Handler: inhalation | 10324-134 | 0.0200 lb a.i./gal (2 oz product/gal water x 15.36% a.i. x 8.34 lb/gal x 1 gal/128 oz) |
|  | Liquid pour | ST/IT Handler: inhalation | 10324-80 | 0.0043 lb a.i./gal (2 oz /gal water x 3.3% a.i. x 8.34 lb/gal x 1 gal/128 oz) |
| Carpets | Truck mounted extraction machines (Liquid pour) | ST/IT Handler: Inhalation | 1839-67 | 0.102 lb ai/gal (13.02% a.i. x12 oz product/gal water x 8.34 lb/gal x 1gal/128oz) |
| Medical Premises (Use Category V) |
| Indoor Hard Surfaces | Mop | ST/IT Handler: inhalation | 10324-134 | 0.0200 lb a.i./gal (2 oz product/gal water x 15.36% a.i. x 8.34 lb/gal x 1 gal/128 oz) |
| Industrial processes and water systems (Use Category VIII) |
| Oil field operations - drilling mud and packing fluidsa | Liquid Pour | ST/IT Handler: Inhalation | 1839-179 | 1.50 lb ai/gal product (18% a.i. x 8.34 lb/gal product) |
| Small process water systems (i.e., evaporative condensers, water scrubbing, wastewater treatment, pasteurizers, auxiliary service water, recirculating cooling water) | Liquid Pour | ST/IT Handler: Inhalation | 1839-129 | 4.17 lb ai/gal product (50% ai x 8.34 lb ai/gal) |
|  | Metered pump | ST/IT Handler: Inhalation | 10707-46 | Maximum 0.0015 lb ai/gal or 1,000 ppm (18%ai x 8.34 lb ai/gal x 1,000 gal/1,000,000 gal) Maintenance 0.00015 lb ai/gal or 100 ppm (18%ai x 8.34 lb ai/gal x 100 gal/1,000,000 gal) |
| Wood Preservation (Use Category X) |
| Non-pressure treatment of wood and wood products in wood treatment facilities | Handler Worker Functions Diptank Operators Blender/spray operators Chemical operators Post-Application Worker Functions Graders Trim saw operators Clean-up crews Construction Workers | ST/IT/LT Handler: inhalation ST/IT/LT Post-application: dermal and inhalation | 6836-212 | Diptank operators and blender/spray operators: 3% ai solution All other worker functions: 80% ai in product |
| Pressure treatment of wood and wood products in wood treatment facilities | Handler Worker Functions Treatment assistant Treatment operator Post-Application Worker Functions Tram setter, stacker operator, loader operator, supervisor, test borer, and tallyman | ST/IT/LT Handler: inhalation ST/IT/LT Post-application: dermal inhalation | 6836-212 | 3% aib |
| Swimming Pools (Use Category XI)c |
| Swimming pools/Spas | Liquid pour | ST/IT Handler: inhalation | 10324-69 1839-133 | Maintenance (IT/LT): 0.00000417 lb ai/gal (10.0% x 1 quart/50,000 gal x 8.34 lb/gal x 1 gal/4 quarts) Heavy algae (ST): 0.000017 lb ai/gal (50.0% x 5.25 oz/10,000 gal x 8.34 lb/gal x 1 gal/128 oz) |

a	For the secondary recovery application, the biocide is meter pumped into the produced water before it is re-injected into the formation or well.  Since the biocide is added via metering pump (continuous or batch) in the secondary recovery systems, the drilling rig worker handling the biocide via open pouring is expected to have a higher exposure than the secondary recovery worker.  Additionally, the current CMA data are not representative of handling the large volume assumed in this scenario.

b	The application rate for pressure treated wood preservation is based on the master label.  The actual label only provides a retention rate.

c	The swimming pool scenario also represents the decorative pond/fountain scenario in the aquatic area use site category because the application rates are very similar.

## 6.1 	Occupational Handler Exposures

The occupational handler scenarios included in Table 6.1 were assessed to determine inhalation exposures.  The general assumptions and equations that were used to calculate occupational handler inhalation risks are provided in Section 1.2, Criteria for Conducting the Risk Assessment. The majority of the scenarios were assessed using CMA data and Equations 1-3.  However, for the occupational scenarios in which CMA data were insufficient, other data and methods were applied.

DDAC dermal irritation exposures and risks were not estimated for occupational handler exposures.  Instead, dermal irritation exposures and risks will be mitigated using default personal protective equipment requirements based on the toxicity of the end-use product.  To minimize dermal  exposures, the minimum PPE required for mixers, loaders, and others exposed to end-use products containing concentrations of DDAC that result in classification of category I, II, or III for skin irritation potential will be long-sleeve shirt, long pants, shoes, socks, chemical-resistant gloves, and chemical-resistant apron.  Once diluted, if the concentration of DDAC in the diluted solution would result in classification of toxicity category IV for skin irritation potential, then the chemical-resistant gloves and chemical-resistant apron can be eliminated for applicators and others exposed to the dilute. Note that chemical-resistant eyewear will be required if the end-use product is classified as category I or II for eye irritation potential.

Unit Exposure Values (UE):  Inhalation unit exposure values were taken from the proprietary Chemical Manufacturers Association (CMA) antimicrobial exposure study (USEPA 1999: DP Barcode D247642) or from the Pesticide Handler Exposure Database (USEPA 1998).

- For the liquid pour scenarios, the unit exposure depends on the material being treated. The following CMA unit exposures were available and used for the assessment of the risk associated with the treatment of the specified materials.

  - Swimming pools, carpets, and oilfield operations (drilling muds and packer fluids): CMA preservative data (gloved).  The inhalation unit exposure is 0.00346 mg/lb a.i. and is based on 2 replicates. Although this unit exposure is based on minimal replicates, the exposure value is similar to the one found in PHED for a similar scenarios.

  - Indoor hard surfaces (immersion, flooding, circulation and liquid pour) in Use Site Categories II and III: The inhalation unit exposure value for disinfectant liquid pour (1.89 mg/lb a.i.) was used.

  - Small process water systems: CMA cooling tower data (gloved). The inhalation unit exposure is 0.450 mg/lb a.i. and is based on 5 replicates.

- For the mopping scenarios, the CMA inhalation unit exposure value for ungloved mopping was used (2.38 mg/lb a.i.).  This value is based on data collected from six replicates in which the applicator mopped the floor and received exposure via contact with the mop or with the bucket.

- For the wiping scenarios, the CMA inhalation unit exposure value for ungloved wiping was used (67.3 mg/lb a.i.).  This value is based on data collected from six replicates (dental technicians) who used a finger pump sprayer to apply the product and then wiped the surfaces with a paper towel

- For the low pressure handwand scenario, the CMA inhalation unit exposure value for low pressure spray was used (0.681 mg/lb a.i.).  This value is based on data collected from eight replicates in which the applicator hand sprayed carpet using 200 psi, then used a push broom rake to raise the carpet nap

- For the trigger pump spray scenarios, the PHED inhalation unit exposure value for aerosol applications (PHED scenario 10) was used. The inhalation unit exposure is 1.3 mg/lb a.i.

- For the liquid/metering pump scenarios, the unit exposure depends on the material being treated. The following CMA unit exposures were available and used for the assessment of the risk associated with the treatment of the specified materials.

  - Small process water systems: CMA cooling tower data. The inhalation unit exposure is 0.00432 mg/lb a.i. and is based on 4 replicates.

- For the high-pressure/high volume spray and medium pressure spray scenarios, the PHED inhalation unit exposure value for liquid/open pour/high pressure spray (PHED scenario 35) was used (0.12 mg/lb a.i.).

- For airless sprayer scenarios, the occupational PHED inhalation unit exposure value for airless sprayer application (PHED scenario 23) was used. The inhalation exposure value is 0.83 mg/lb a.i.

- For the fogging, ULV/mist sprayer and automated system scenarios, it was assumed that most of the exposure to the handler will be due to preparing the fogger, and that the handler leaves the room immediately after fogging commences.  Therefore, the available CMA disinfectant liquid pour inhalation unit exposure value was used.  The inhalation unit exposure value is 1.89 mg/lb a.i., respectively. This value is based on data collected from two gloved replicates involving pouring a disinfectant product from a jug into sterilization trays designed for dental instruments, adding water and instruments to the tray, removing the instruments, and discarding the old solution.

- For the brush/roller scenario, the occupational PHED inhalation unit exposure value for paintbrush applications was used (single layer of clothing). The inhalation exposure value is 0.28 mg/lb a.i.

Quantity handled/treated: The quantity handled/treated values were estimated based on information from various sources.  The following assumptions were made:

- For the liquid pour scenarios, the quantity of the chemical that is handled depends on the material that is being treated.  The following values were used for the different materials:

  - Swimming pools: 200,000 gallons.

  - Indoor hard surfaces (immersion, flooding, circulation, and liquid pour): 2 gallons.

  - Carpets:  32 gallons, based on label 1839-81 (solution is metered at 4 gallons per hour, assuming an 8-hour shift).

  - Oil field operations (drilling muds and packer fluids): The following use information was used to estimate the amount of ai handled per day during oil-well activities.  Biocide is typically added directly to drilling rig mud tanks via open pouring. Over a 3 to 6 week period, while a 13,000 ft well is being drilled, 1 to 2 drums (1 drum = 42 gallons) of biocide may be used if microbiological problems are encountered.  Therefore, the short-term exposure assessment used 5.6 gallons for the amount of biocide handled per day by the drilling rig worker [i.e., (2 drums x 42 gal/drum) / (5 days/week x 3 weeks) = 5.6 gal/day].  The intermediate-term exposure assessment used 2.8 gallons for the amount of biocide handled per day by the drilling rig worker [i.e., (2 drums x 42 gal/drum) / (5 days/week x 6 weeks) = 2.8 gal/day]. Although crew changes may occur in drilling rig operations, typically a designated customer representative is responsible for the biocide feeding.  Therefore, one person would be involved with the biocide application activities on a daily basis.

  - Small process water systems:  Workers in small systems could manually pour up to 5 to 10 gallons of biocide into the system, but larger systems would utilize chemical pumps in order to save time and labor expense.  However, for DDAC the application rate is low (16 oz product/1000 gallons of water), and therefore, the maximum amount used for closed systems is assumed for open pour.  Therefore, AD assumed that workers handle 2.5 gallons of biocide per day when making open pour applications.

- For the liquid/metering pump scenarios the quantity that is handled depends on the material that is being treated.  The following values were used for the different materials:

  - Small process water systems: AD has assumed that 20,000 gallons of water are treated daily when chemical pump applications are made.

- For the mopping scenarios, it was assumed that two gallons of solution are used in the agricultural, food handling, and commercial/institutional/industrial settings and 45 gallons are used in the medical setting.  The medical setting use amount is based on a janitor cleans approximately 28 hospital rooms a day and changing the cleaning water every three rooms (Helwig 2003).

- For the wiping and trigger pump spray scenarios, it was assumed that 1 liter or 0.26 gallons were used.

- For the fogging scenario in the agricultural use site category, it was assumed that 150,000 ft3 is treated, based on the estimated dimensions of a poultry barn (300 ft x 50 ft x 10 ft). As the label directions only state to fog for one minute on maximum output per 4,000 ft3 and does not provide the amount of treatment solution to use per cubic foot, AD assumed that the maximum fogger output is 0.42 gallons/min (25 gal/hr).  This value is the maximum output for the Mistermax fogger which is used to dispense fungicides, insecticides, germicides and disinfectants as wettable powders, emulsifiable concentrates, flowables or liquids in a variety of applications such as greenhouses, warehouses, food processing plants, and swine/poultry houses (http://bugsource.com/mistermax.html).

- For the low-pressure handwand scenario, it was assumed that 40 gallons of solution are used in agricultural scenarios (USEPA 2001) and 2 gallons are used in all other applications.

- For the high-pressure spray scenario, it was assumed that 40 gallons of solution are used.

Duration of Exposure: The MOEs were calculated for the short- and intermediate-term durations for occupational handlers using the appropriate endpoints in Table 3.2.

Exposure Calculations and Results

The resulting inhalation exposures and MOEs for the representative occupational handler scenarios are presented in Table 6.2. The calculated MOEs were above the target MOE of 100 for all scenarios.

A confirmatory inhalation toxicity study may be warranted because inhalation MOEs were below 1,000 for the following scenarios:

- Small process water systems, liquid pour: ST/IT Inhalation MOE = 130

- Agricultural fogging, mixing and loading: ST/IT Inhalation MOE = 110

- Medical premises, mopping: ST/IT Inhalation MOE = 280

- Wood Preservation (non-pressure treatment), blender/sprayer: ST/IT/LT Inhalation MOE = 280

| Table 6.2 Short- , Intermediate- and Long-Term Inhalation Risks Associated with Occupational Handlers |
| --- |
| Exposure Scenario | Method of Application | Inhalation Unit Exposure (mg/lb a.i.) | Application Rate | Quantity Handled/ Treated per day | Inhalation Daily Dose (mg/kg/day)a | Inhalation MOEb, c (Target MOE = 100) |
| Agricultural Premises and Equipment (Use Site Category I) |
| Application to hard surfaces, equipment, and vehicles | Mop | 2.38 | 0.0094 lb ai/gal | 2 gallons | 0.0075 | 13,000 |
|  | High pressure/high volume spray | 0.12 | 0.0094 lb ai/gal | 40 gallons | 0.00075 | 13,000 |
|  | Low pressure handwand | 0.681 | 0.0094 lb ai/gal | 40 gallons | 0.0043 | 2,300 |
|  | Trigger pump sprayer | 1.3 | 0.0094 lb ai/gal | 0.26 gallons | 0.000052 | 190,000 |
|  | Wipe | 67.3 | 0.0094 lb ai/gal | 0.26 gallons | 0.0027 | 3,600 |
| Fogging (mix/load only) | Liquid pour | 1.89 | 1.88E-05 lb/ft3 | 150,000 ft3 | 0.089 | 110 |
| Food Handling/Storage Establishments Premises And Equipment (Use Site Category II) |
| Application to indoor hard surfaces | Low pressure handwand | 0.681 | 0.0200 lb ai/gal | 2 gallons | 0.00045 | 22,000 |
|  | Mop | 2.38 | 0.0200 lb ai/gal | 2 gallons | 0.0016 | 6,300 |
|  | Wipe | 67.3 | 0.0200 lb ai/gal | 0.26 gallons | 0.0058 | 1,700 |
|  | Trigger pump sprayer | 1.3 | 0.0200 lb ai/gal | 0.26 gallons | 0.00011 | 89,000 |
|  | Immersion, Flooding, Circulation | 1.89 | 0.00196 lb ai/gal | 2 gallons | 0.00012 | 81,000 |
| Commercial, Institutional and Industrial Premises and Equipment (Use Site Category III ) |
| Application to indoor hard surfaces | Low pressure handwand | 0.681 | 0.0200 lb ai/gal | 2 gallons | 0.00045 | 22,000 |
|  | Mop | 2.38 | 0.0200 lb ai/gal | 2 gallons | 0.0016 | 6,300 |
|  | Wipe | 67.3 | 0.0200 lb ai/gal | 0.26 gallons | 0.0058 | 1,700 |
|  | Trigger pump sprayer | 1.3 | 0.0200 lb ai/gal | 0.26 gallons | 0.00011 | 89,000 |
|  | Liquid pour | 1.89 | 0.0043 lb ai/gal | 2 gallons | 0.00027 | 37,000 |
| Application to carpets | Liquid pour | 0.00346 | 0.102 lb ai/gal | 32 gallons | 0.00019 | 53,000 |
| Medical Premises and Equipment (Use Site Category V) |
| Application to hard surfaces | Mop | 2.38 | 0.0200 lb ai/gal | 45 gallons | 0.036 | 280 |
| Industrial Processes and Water Systems (Use Site Category VIII) |
| Small process water systems: Recirculating cooling tower | Liquid pour | 0.45 | 4.17 lb ai/gal product | 2.5 gallons | 0.078 | 130 |
|  | Metering pump | 0.00432 | Initial Dose (ST): 1.50E-03lb ai/gal water | 20,000 gallons | 0.0022 | ST = 4,600 |
|  |  |  | Maintenance Dose (IT): 1.50E-04lb ai/gal water | 20,000 gallons | 0.00022 | IT =46,000 |
| Oil field operations - drilling mud and packing fluids | Liquid pour | 0.00346 | 1.50 lb ai/gal product | 5.6 gallons | 0.00048 | ST = 21,000 |
|  |  |  |  | 2.8 gallons | 0.00024 | IT = 41,000 |
| Swimming Pools (Use Site Category X)d |
| Application to swimming pools | Liquid pour | 0.00346 | Heavy algae Dose (ST): 0.000017 lb ai/gal | 200,000 gallons | 0.00020 | ST= 15,000 |
|  |  |  | Maintenance Dose (IT/LT): 0.00000417 lb ai/gal | 200,000 gallons | 0.000048 | IT=210,000 |

ST = short-term,  IT = intermediate-term, LT = long-term, N/A= No data available

a	Daily dose (mg/kg/day) = [unit exposure (mg/lb a.i.) x absorption factor (1.0 for inhalation) x application rate x quantity treated / Body weight (60 kg for inhalation).

b	MOE = NOAEL  (mg/kg/day) / Absorbed Daily Dose [Where NOAEL = 10 mg/kg/day for all inhalation exposure durations].  Target MOE = 100.

c	The MOEs refer to short-term and intermediate-term duration unless indicated otherwise.

d.	The swimming pool scenario also represents the decorative pond/fountain scenario in the aquatic area use site category because the application rates are very similar.

## 6.2  	Occupational Post-application Exposures

Except for the post-application scenarios assessed for fogging and wood preservatives in Section 6.3, occupational post-application exposures are assumed to be negligible.

Fogging (Food Processing Plant and Hatchery)

Post-application inhalation exposures only were assessed for entry into a building (hatchery and food processing plant) after a fogging application, because dermal post application is presumed to be negligible.  The inhalation exposure assessment was conducted using the Multi-Chamber Concentration and Exposure Model (MCCEM v1.2).   MCCEM estimates average and peak indoor air concentrations of chemicals released from products or materials in houses, apartments, townhouses, or other residences. Although the data libraries contained in MCCEM are limited to residential settings, the model can be used to assess other indoor environments.  MCCEM has the capability to estimate inhalation exposures to chemicals, calculated as single day doses, chronic average daily doses, or lifetime average daily doses. (All dose estimates are potential doses; they do not account for actual absorption into the body.)

The product, EPA Reg # 10324-80 (3.3% ai) with a maximum application rate of 0.0065 lb ai/gal, was assessed for fogging use in a food processing plant. The label states to fog one quart of the diluted product per 1,000 cubic feet. All labels which can be used for fogging in food processing areas indicate that all personnel must vacate the room during fogging and for a minimum of 2 hours after fogging. Therefore, exposure was calculated for a person entering the food processing plant 2 hours after all the applied fogger has been deployed.

The product, EPA Reg # 10324-108 (13.02% ai) with a maximum application rate of 0.181 lb ai/gal, was assessed for fogging use in hatcheries and incubators. After fogging, the label states that the building should be well ventilated and not to enter until 2 hours after fogging, unless wearing a self-contained respirator and long pants/long sleeves.  The remaining labels for fogging use in hatchery rooms and incubator indicate re-entry intervals of 0 to 2 hours. Therefore, exposure was calculated for a person entering the building immediately after all the applied fogger has been deployed and 2 hours after all the applied fogger has been deployed

Assumptions used to calculate inputs for MCCEM and the calculated exposure values are presented in Table 6.3 for food processing plants and in Table 6.4 for hatcheries.  The following assumptions were made:

- The area being fogged is a one-chamber barn with dimensions of 300 ft x 50 ft x10 ft (AD standard assumption).

- For the food processing plant, the air exchange rate is 0.18 per hour (MCCEM default based on a residential home).  For a hatchery, the air exchange rate is 4 per hour based on the rate for a poultry barn (Jacobson, 2005).

- Fogging occurs instantaneously, so that the entire mass of product is mixed homogeneously with the indoor air as soon as fogging commences.

- It is assumed that all of the aerosols are inhalable and/or respirable.

| Table 6.3. Short and Intermediate Term Inhalation Risks Associated with Post-application Exposure to DDAC After Fogging a Food Processing Plant |
| --- |
| Parametera | Value | Rationale |
| Dimensions | 300x50x10 ft, 15,000 ft2 floor area, 150,000 ft3 (4,248 m3) volume | EPA Assumption |
| Air Changes per Hour (ACH)* | 0.18/hr | EPA Assumption |
| Activity Pattern* | 8-hr average concentration starting at expiration of 2-hr REI | Based on product(s re-entry interval (10324-80) |
| Concentration of Fogging Liquid | 0.0065 lb ai/gal | Product Label (See Table 6.1) |
| Use rate | 1 quart/1,000 ft3 | Product label |
| Amount applied to room | 0.0258 g ai/m3 | (Use rate) x (Concentration) |
| Body Weight | 60 kg | EPA Assumption |
| Inhalation Rate | 1.0 m3/hr | NAFTA Light Activity for Adults (USEPA, 1997) |
| MCCEM Output |
| Average Concentration over 8-hrs (mg/m3) | 2-hr re-entry: 9.74 | Average of MCCEM-calculated air concentrations from Hour 2 to Hour 10 for 2-hr REI |
| 8-hr Dose (mg/kg/day) | 2-hr re-entry: 1.30 | Average Conc. * 8 hrs * Inhal. Rate / BW |
| 8-hr short-term MOE | 2-hr re-entry: 7 | NOAEL (10 mg/kg/day) / Dose |

*Used as MCCEM input.  Default values from MCCEM were used for all inputs not listed in the table above

| Table 6.4. Short and Intermediate Term Inhalation Risks Associated with Post-application Exposure to DDAC After Fogging a Hatchery |
| --- |
| Parameter | Value | Rationale |
| Barn Dimensions* | 300x50x10 ft, 15,000 ft2 floor area, 150,000 ft3 (4,248 m3) volume | EPA Assumption |
| Air Changes per Hour (ACH)* | 4/hr | Jacobson, 2005 |
| Activity Pattern* | 8-hr average concentration starting at expiration of 0-hr re-entry interval and 2-hr re-entry interval | Based on product(s re-entry interval |
| Application Rate of Fogging Liquid | 0.181 lb ai/gal. (Note: Max rate 0.22 lb ai/gal) | Product Label (See Table 6.1) |
| Use rate | 0.42 gal/4,000 ft3 | Product label states to fog 1 min/4,000 ft3. Output of 0.42 gal/min from http://bugsource.com/mistermax.html |
| Mass applied to barn | 0.301 g ai/m3 | (application rate) x (use rate) |
| Body Weight | 60 kg | EPA Assumption |
| Inhalation Rate | 1.0 m3/hr | NAFTA Light Activity for Adults (USEPA, 1997) |
| MCCEM Output |
| Average Concentration over 8-hrs (mg/m3) | 0-hr Re-entry: 0.62 2-hr Re-entry: 0.0114 | Average of MCCEM-calculated air concentrations from Hour 0 to Hour 8 for 0-hr re-entry and Hour 2 to Hour 10 for 2-hr re-entry |
| 8-hr Dose (mg/kg/day) | 0-hr Re-entry: 0.083 2-hr Re-entry: 0.0015 | Average Conc. * 8 hrs * Inhal. Rate / BW |
| 8-hr short-term MOE | 0-hr Re-entry: 120 2-hr Re-entry: 6,600 | NOAEL (10 mg/kg/day) / Dose |

A detailed report is presented in Appendix D, including hourly air concentrations.  Based on MCCEM output, 8-hr MOE values were calculated.  The MOE for fogging in the food processing plant (2-hr re-entry interval) was below the target MOE of 100 (MOE = 8).  For fogging in hatcheries, the 8-hr MOE immediately following release and after a 2 hr re-entry were above the target MOE of 100 (MOE = 120 and 6,600, respectively). Because the 8-hr MOE for entering a hatchery immediately after fogging is below 1,000, the Agency may request a confirmatory inhalation toxicity study.   The risks of concern for the food processing plant are attributed to the low air changes per hour assumed (i.e., 0.18 ACH) in the assessment.  For the poultry barn, ventilation rate was obtained from Jacobson (2005).  The assessment for food processing plants could be refined if a more accurate ventilation rate could be obtained.

## 6.3 	Wood Preservation

DDAC is used in products that are intended to preserve wood through both non-pressure treatment methods and pressure treatment methods.  The exposure scenarios assessed in this document for the representative wood preservation uses selected by AD are shown in Table 6.1. Section 6.3.1 presents the exposure analysis for the handler and post-application scenarios for non-pressure treatment scenarios and Section 6.3.2 presents the exposure analysis for the handler and post-application scenarios for pressure treatment scenarios.

Dermal irritation exposures from post-application activities in the wood preservation treatment facility will be mitigated using default personal protective equipment requirements based on the toxicity of the end-use product.  Therefore, only inhalation exposures and risks are presented.

### 6.3.1 	Non-Pressure Treatment Scenarios (Handler and Post-application)

#### The proprietary study, “Measurement and Assessment of Dermal and Inhalation Exposures to Didecyl Dimethyl Ammonium Chloride (DDAC) Used in the Protection of Cut Lumber (Phase III)” (Bestari et al., 1999, MRID 455243-04) identified various worker functions/positions for individuals that handle DDAC-containing wood preservatives for non-pressure treatment application methods and for individuals that could then come into contact with the preserved wood. The worker functions/positions identified in the DDAC study are presented below.

Handler:

- Blender/spray operators are workers that add the wood preservative into a blender/sprayer system for composite wood via closed-liquid pumping.

- Diptank Operators can be in reference to wood being lowered into the treating solution through an automated process (i.e., elevator diptank, forklift diptank).  This scenario can also occur in a smaller scale treatment facility in which the worker can manually dip the wood into the treatment solution.

- Chemical operators for a spray box system consist of chemical operators, chemical assistants, chemical supervisors, and chemical captains.  These individuals maintain a chemical supply balance along with flushing and cleaning spray nozzles.

Post-application:

- Graders, positioned right after the spray box, grade dry lumber by hand (i.e. detect faults).  In the DDAC study, graders graded wet lumber; therefore, the exposures to graders using DDAC are worst-case scenarios.

- Millwrights repair all conveyer chains and general up-keep of the mill.

- Clean-up crews perform general cleaning duties at the mill.

- Trim saw operators operate the hula trim saw and consist of operators and strappers. In the DDAC study, hula trim saw operators handled dry lumber.

- Construction workers install treated plywood, oriented strand board, medium density fiberboard, and others.

The blender/spray operator position was assessed using CMA unit exposure data and the remaining handler and post-application positions were assessed using data from the DDAC study (Bestari et al., 1999).

Blender/Spray Operators

The inhalation exposures and risks to the composite wood blender/spray operators were assessed using Equations 1 through 3 in Section 1.2. The surrogate unit exposures were taken from the CMA study (USEPA, 1999b).  Specifically, the liquid pump preservative unit exposures were used in this assessment.  The inhalation unit exposure is 0.000403 mg/lb ai. These values are based on two replicates.  The quantity of the wood being treated was derived from other wood preservative estimates (USEPA, 2004) for the amount of wood slurry treated because no chemical specific data were available for DDAC.  It was assumed that batches of wood slurry are treated in 10,000 gallon tanks, and that eight batches of wood slurry are treated per day (one per hour for an 8-hr work shift).  Additionally, it was assumed that each batch requires 3,000 gallons of preservatives and the remainder volume of the tank consists of wood slurry (7,000 gallons of wood slurry per batch). Since wood chips have a density of approximately 380 kg/m3 (SIMetric, 2005), the total amount of wood slurry treated per day would be 178,000 lbs (8 batches/day x 7,000 gallons/batch x 0.003785 m3/gallon x 380 kg/m3 x 2.2 lb/kg).  The assumptions used for batch sizes and the quantity of preservative needed are consistent with an assessment performed previously by the EPA (USEPA 2003). The DDAC assessment was conducted using an application rate of 3% ai solution.

Table 6.5 provides the inhalation doses and MOEs for the workers adding the preservative to the wood slurry.  The inhalation MOE is above the target MOE of 100 for short-, intermediate-, and long-term inhalation exposures (MOE = 280). However, the MOE is below 1,000; therefore, the Agency may request a confirmatory inhalation toxicity study.

| Table 6.5. Short-, Intermediate-, and Long-Term Inhalation Exposures and MOEs for Blender/Spray Operator |
| --- |
| Exposure Scenario | Inhalation Unit Exposurea (mg/lb ai) | Application Rate (% ai in solution/ day) | Wood Slurry Treatedb (lb/day) | Daily Dosec (mg/kg/day) | ST/IT/LT MOEd (Target MOE = 100) |
| Occupational Handler |
| Blender/spray operator | 0.000403 | 3 | 178,000 | 0.036 | 280 |

ST =	Short-term duration; IT =	Intermediate-term duration; and LT = long-term.

- Inhalation unit exposure: Baseline.

b.	Wood slurry treated = (8 batches/day x 7,000 gallons/batch x 0.003785 m3/gallon x 380 kg/m3 x 2.2 lb/kg)

c.	Daily Dose = unit exposure (mg/lb ai) x App Rate (% ai/day) x Quantity treated (lb/day) x absorption factor (100% for inhalation) / BW (60 kg)

d.	MOE = NOAEL (mg/kg/day)/ Daily dose [Where ST/IT/LT NOAEL = 10 mg/kg/day for inhalation. Target MOE = 100.

Chemical Operators, Graders, Millwrights, Clean-up Crews, and Trim Saw Operators

The inhalation exposures to chemical operators, graders, millwrights, trim saw operators, and clean-up crews were assessed using the exposure data from the DDAC study (Bestari et al., 1999). The DDAC study examined individuals( exposure to DDAC while working with antisapstains and performing routine tasks at 11 sawmills/planar mills in Canada.  Inhalation exposure monitoring data were gathered for each job function of interest using dosimeters and personal sampling tubes.  Dosimeters and personal air sampling tubes were analyzed for DDAC.  Exposure data for individuals performing the same job functions were averaged together to determine job specific averages.  Monitoring was conducted using 2 trim saw workers, 13 grader workers, 11 chemical operators, 3 millwrights, and 6 clean-up staff.

The individual inhalation exposures from the DDAC study are presented in Table E-1 in Appendix E.  The study was conducted using a product containing 80% DDAC; therefore, the exposures do not need to be modified to account for any differences in percent active ingredient. The lb ai handled by each person or the % ai in the treatment solution were not provided for these worker functions in the DDAC study.

The following equation was used to calculate daily dose for DDAC:

Daily Dose = DDAC UE x AB							(Eq. 13)

BW

Where:

DDAC UE	=	DDAC inhalation unit exposure (mg/day);

AB		=	Absorption factor (100% inhalation); and

BW		=	Body weight (60 kg).

In using this methodology, the following assumptions were made:

- DDAC and DDAC end-use products will be used in similar quantities.

- The procedures for applying both chemicals are similar.

- The limits of detections (LOD) for inhalation residues from chemical operators, graders, mill wrights, and clean-up staff replicates were not provided in the DDAC report.  For lack of better data, it was assumed that the inhalation LODs for these worker positions are equal to the LOD of the diptank operator replicates (5.6 μg).  For all measurements below the air concentration associated with this detection limit, half the detection limit was used.

- Air concentrations were reported in the DDAC study. To convert air concentrations (μg/m3) into terms of inhalation unit exposure (mg/day), the air concentrations were multiplied by an inhalation rate of 1.0 m3/hr for light activity (USEPA,1997), a sample duration of 8 hrs/day, and a conversion factor of 1 mg/1000 µg.  Table D-1 in Appendix D presents the inhalation exposures.

Table 6.6 provides the short-, intermediate-, and long-term inhalation doses and MOEs for chemical operators, graders, millwrights, clean-up crews, and trim saw operators.  The inhalation MOEs are above the target MOE of 100 for all worker functions. Any dermal irritation exposures from post-application activities will be mitigated using default personal protective equipment requirements based on the toxicity of the end-use product.

It should be noted that although the target inhalation MOE is 100, the MOE for the clean-crew workers is below 1,000; therefore, the Agency may request a confirmatory inhalation toxicity study.

- Wood Preservation (non-pressure treatment), clean-up crew: ST/IT/LT Inhalation MOE = 990

| Table 6.6. Short-, Intermediate, and Long-Term Inhalation Exposures and MOEs for Wood Preservative Chemical Operators, Graders, Trim Saw Operators, and Clean-Up Crews (Handler and Post-application Activities) |
| --- |
| Exposure Scenarioa (number of volunteers) | Inhalation UEb (mg/day) | Conversion Ratioc | Daily Dosed (mg/kg/day) | MOEe (Target MOE = 100) |
| Occupational Handlers |
| Chemical Operator (n=11) | 0.0281 | NA | 0.000468 | 21,000 |
| Occupational Post-Application |
| Grader (n=13) | 0.0295 | NA | 0.000491 | 20,000 |
| Trim Saw (n=2) | 0.061 | NA | 0.00101 | 9,900 |
| Millwright (n=3) | 0.057 | NA | 0.00095 | 11,000 |
| Clean-Up (n=6) | 0.60 | NA | 0.0101 | 990 |

ST = 	Short-term duration, IT = Intermediate-term duration, LT = Long-term duration

a.	The exposure scenario represents a worker wearing short-sleeved shirts, cotton work trousers, and cotton glove dosimeter gloves under chemical resistant gloves. Volunteers were grouped according to tasks they conducted at the mill.

b.	Inhalation unit exposures are from Bestari et. al. (1999).  Refer to Table E-1 in Appendix E for the calculation of the inhalation exposures. Inhalation exposure (mg/day) was calculated using the following equation: Air concentration (μg/m3) x Inhalation rate (1.0 m3/hr) x Sample duration (8 hr/day) x Unit conversion (1 mg/1000 μg).  The inhalation rate is from USEPA, 1997.

c.	A conversion ratio is not needed because the maximum % active ingredient in the product is the same as the % active ingredient in the DDAC study.

d.	Daily dose (mg/kg/day) = exposure (mg/day) x  absorption factor (100% for inhalation)/body weight (60 kg).

e.			MOE = NOAEL (mg/kg/day)/ Daily dose [Where inhalation NOAEL = 10 mg/kg/day]. Target MOE = 100.

Diptank Operators

Exposures to diptank operators were also assessed using the data from the DDAC study (Bestari et al., 1999). The diptank scenario assessment was conducted differently than for the other job functions because the concentration of DDAC in the diptank solution was provided.  The exposure data for diptank operators were converted into (unit exposures( in terms of mg a.i. for each 1% of concentration of the product. The calculation of the inhalation unit exposure (0.046 mg/1% solution, respectively) is presented in Table E-2 in Appendix E.  The air concentrations presented in the DDAC study were converted to unit exposures using an inhalation rate of 1.0 m3/hr (light activity) (USEPA, 1997) and a sample duration of 8 hrs/day.

The following equations are used to estimate inhalation handler exposure:

Daily Dose = DDAC UE x AI x AB 							(Eq. 14)

BW

Where:

DDAC UE	=	DDAC inhalation unit exposure (mg/ 1% in solution);

AI		=	Percent active ingredient (3% ai in solution/day);

AB		=	Absorption factor (100% for inhalation); and

BW		=	Body weight (60 kg).

Table 6.7 provides the short-, intermediate- and long-term inhalation dose and MOEs for diptank operators. The inhalation MOE is above the target MOE of 100 and, therefore, is not of concern.

| Table 6.7. Short-, Intermediate-, and Long-Term Inhalation Exposures and MOEs for Diptank Operator (Handler Activity) |
| --- |
| Exposure Scenarioa (number of replicates) | Inhalation Unit Exposureb (mg DDAC/1% solution) | App Rate (% a.i. in solution/ day) | Daily Dosec (mg/kg/day) | MOEd |
| Occupational Handler |
| Dipping, with gloves (n=7) | 0.046 | 3 | 0.0023 | 4,300 |

a 	The exposure scenario represents a worker not wearing a respirator.

b	Inhalation unit exposures are from DDAC study (MRID 455243-04). Refer to Table E-2 in Appendix E for inhalation unit exposure calculations. Inhalation exposure (mg) was calculated using the following equation: Air concentration (mg/m3) x Inhalation rate (1.0 m3/hr) x Sample Duration (8 hr).  The inhalation rate is from USEPA, 1997.

c	Daily dose (mg/kg/day) = unit exposure (mg/1% ai solution) x percent active ingredient in solution  (3% ai) x absorption factor (100% for inhalation) / body weight (60 kg).

d			MOE = NOAEL (mg/kg/day) / Daily dose [Where inhalation NOAEL = 10 mg/kg/day. Target MOE = 100.

Construction workers

Potential risks resulting from construction worker dermal contact with DDAC-treated wood are assessed in the same manner as potential risks resulting from children’s dermal contact with DDAC-treated playsets and decks (Section 4.2.2.3). The risks were calculated using average worker residue data for hands available in the DDAC exposure study. Hand residue data from the end stacker, stickman, and tallyman workers were used because of the possibility of the contact with dry treated wood. The maximum and average values of these data (3.0 and1.4 (g/cm2, respectively) were assumed to be the dermal skin irritation exposure. As shown in Table 4.10, the dermal MOE are less than or equal to 1 for maximum and average hand residues.  A wood wipe study is needed to refine these risk estimates.

### 6.3.2	Pressure Treatment Scenarios (Handler and Post-Application)

DDAC may be used to treat wood and wood products using pressurized application methods such as double vacuum. According to the product labels, the maximum retention rate is 0.6 lb/ft3. An application rate was not provided on the product labels; therefore, an application rate of 3% ai solution was used in this assessment, based on the master label. DDAC-specific exposure data are not available for assessment of pressure treatment exposure.  Therefore, the assessment relies on surrogate chromated copper arsenate (CCA) data (ACC, 2002b) and was based on the approach used in a previous exposure assessment (USEPA 2003).

Surrogate Unit Exposure Data

Inhalation exposures for pressure treatment uses are derived from information in the exposure study by the American Chemistry Council (2002) entitled “Assessment of Potential Inhalation and Dermal Exposure Associated with Pressure Treatment of Wood with Arsenical Wood Products” (ACC, 2002b).  In this study, a treatment solution of CCA was approximately 0.5 percent.  The CCA study is the best pressure treatment data available for a water based solution to estimate exposure to DDAC.

The CCA study measured both handlers and post-application activities.  Although there is overlap in job functions, the handlers are defined as being either treating operators (TOs) or treating assistants (TAs).  The TOs were monitored at three sites (A, B, and C) using 5 replicates at each site.  The TAs were monitored at two sites (Sites A and C) using 5 replicates at each site.  The post-application activities included: tram setter (TS) at Site A (n=5); stacker operator (SO) at Site A (n=4); loader operator (LO) at Sites A, B, C (n=15); supervisor (S) at Site B (n=5); test borer (TB) at Site C (n=5); and the tallyman (TM) at Site C (n=5).  According to the CCA study, workers wore cotton long-sleeved shirts and cotton trousers (or one-piece cotton coveralls) over the whole-body dosimeters (“plus additional shirts or jackets per typical practice at Site B”) and chemical-resistant or work gloves, when appropriate.  Therefore, the CCA study provides exposure data associated with maximum PPE (excluding respirators).  In using the CCA study for this DDAC assessment, the TO and TA handlers are assessed separately. The post-application job functions, however, have been combined into one data set to represent post-application activities because for most activities the sample size is small (5 ≤ n ≤ 15).

The measured CCA inhalation exposure values were normalized by the treatment solution concentration used at each of the 3 facilities (i.e., unit exposure reported as µg arsenic/ppm treatment solution).  The normalization by treatment solution concentration was performed to extrapolate the measured exposures in the CCA study (monitored at ~0.5% ai solution) to the maximum DDAC treatment solution concentration (1% ai solution).  Table 6.8 presents the inhalation unit exposure values normalized to the treatment solution concentration in ppm for (1) all sites, (2) treatment operator (TA handler), (3) treatment assistant (TA handler), and (4) all post-application job functions (TS, SO, LO, S, TB, TM).

Exposure Calculations

The following equation was used to estimate inhalation handler exposure:

Daily Dose = UE x AI x AB 							(Eq. 15)

BW

Where:

UE	=	Unit exposure (mg As/ppm);

AI	=	Percent active ingredient (3% ai in solution);

AB	=	Absorption factor (100% inhalation); and

BW	=	Body weight (60 kg).

Results

The estimated inhalation exposures and risks for DDAC are presented in Table 6.9.  The calculated inhalation MOEs are above the target MOE of 100 for all scenarios. All inhalation MOEs also exceed 1,000, therefore, a confirmatory inhalation toxicity study is not warranted based on the results of these exposure scenarios.

| Table 6.8. Inhalation Exposure Values from a CCA Pressure Treatment Study (Exposure Data used as Surrogate Unit Exposures for DDAC Assessment) |
| --- |
| Site | Treatment Solution | Statistic | Air Concentrationb (μg As/m3/ppm) | Inhalation Unit Exposurec (μg As/ppm) |
|  | % | ppma |  |  |  |
| All sites - All Data (n = 64) | 0.438 to 0.595 | 4,380 to 5,950 | Average ± std | 0.00013 ± 0.00023 | 0.00104 |
|  |  |  | Median | 0.00013 | 0.00104 |
|  |  |  | 90th percentile | 0.00077 | 0.00617 |
|  |  |  | Maximum | 0.0011 | 0.00882 |
| All sites - Handler Treatment Operator (n = 15) | 0.438 to 0.595 | 4,380 to 5,950 | Average ± std | 0.00032 ± 0.00038 | 0.00257 |
|  |  |  | Median | 0.00013 | 0.00104 |
|  |  |  | 90th percentile | 0.00092 | 0.00737 |
|  |  |  | Maximum | 0.0011 | 0.00882 |
| All sites - Handler Treatment Assistant (n = 10) | 0.438 to 0.595 | 4,380 to 5,950 | Average ± std | 0.0001 ± 0.00004 | 0.000802 |
|  |  |  | Median | 0.00013 | 0.00104 |
|  |  |  | 90th percentile | 0.00013 | 0.00104 |
|  |  |  | Maximum | 0.00014 | 0.00112 |
| All sites – Post-application: All job functions (TS, SO, LO, S, TB, TM) (n = 39) | -- | -- | Average ± std | 0.00020 ± 0.00025 | 0.00160 |
|  |  |  | Median | 0.00013 | 0.00104 |
|  |  |  | 90th percentile | 0.00050 | 0.00401 |
|  |  |  | Maximum | 0.0011 | 0.00882 |

a.	ppm = (% treatment solution) * (10,000).

b.	Air concentration was calculated as μg collected per sample per ppm / (480 min per day x 2 L/min).

c.	Inhalation unit exposure = air concentration (μg As/m3/ppm) x breathing rate for light activities (0.0167 m3/min) x sample duration (480 min).

| Table 6.9. Short-, Intermediate-, and Long-Term Inhalation Exposures and MOEs for Pressure Treatment Handler and Post-application Scenarios |
| --- |
| Exposure Scenario | Inhalation Unit Exposurea (μg As/ppm) | Application Rate (% ai solution) | Absorbed Daily Dosesb (mg/kg/day) | Inhalation MOEsc (Target MOE = 100) |
| Occupational Handler |
| Treatment Operator (TO) | 0.00257 | 3 | 0.0013 | 7,800 |
| Treatment Assistant (TA) | 0.000802 | 3 | 0.00040 | 25,000 |
| Occupational Post-application |
| All (Tram setter, stacker operator, loader operator, supervisor, test borer, and tallyman) | 0.00160 | 3 | 0.00080 | 13,000 |

a. 	Unit exposure values taken from CCA study and are shown in Table 6.11.

b. 	Absorbed Daily Dose (mg/kg/day) = Unit Exposure (μg As/ppm) x [% DDAC in solution (3) x 10,000 (parts per million conversion)] x (0.001 mg/μg) x absorption factor (100% for inhalation) / Body weight (60 kg).

c.			MOE = NOAEL (mg/kg/day) / Daily dose [Where inhalation NOAEL = 10 mg/kg/day for all durations. Target MOE = 100.

## 6.4	Data Limitations/Uncertainties

There are several data limitations and uncertainties associated with the occupational handler and post-application exposure assessments.  These include:

- Surrogate dermal and inhalation unit exposure values were taken from the proprietary Chemical Manufacturers Association (CMA) antimicrobial exposure study (USEPA, 1999: DP Barcode D247642) or from the Pesticide Handler Exposure Database (USEPA, 1998) (See Appendix B for summaries of these data sources).   Since the CMA data are of poor quality, the Agency requests that confirmatory data be submitted to support the occupational scenarios assessed in this document.

- Unit exposures are not available for some of the specific scenarios that are prescribed for DDAC including open loading into oil-well/field environments

  - The CMA data used for oil-well uses are based on open pouring of a material preservative.  Although these data are only represented by 2 replicates each, the exposure values are similar to open loading of pesticides in PHED. Furthermore, there are no representative unit exposure data for chemical metering into secondary recovery oil operations.  Since the volume of water being treated in secondary recovery operations is so large, the available CMA data can not be reliably extrapolated because they are based on activities that handle much lower volumes and possibly different techniques.  Therefore, it was assumed that if the open pour handling activities for the other oil well operations resulted in MOEs that are not of concern, then the MOEs for the closed system chemical metering into secondary recovery operations would also be not of concern.  AD requests that confirmatory data be conducted to show that this is accurate.

- For the wood preservative pressure treatment scenarios, CCA exposure data were used for lack of DDAC-specific exposure data.  Limitations and uncertainties associated with the use of these data include:

  - The assumption was made that exposure patterns for workers at treatment facilities using CCA and DDAC would be similar to exposure patterns for workers at treatment facilities using DDAC, and therefore the exposures could be used as surrogate data for workers that treat wood with DDAC.

  - For environmental modeling, it was assumed that the leaching process from the DDAC treated wood would be similar to that of CCA and DDAC.  However, due to the lack of real data for DDAC -treated wood, it is not possible to verify this assumption.

- The quantities handled/treated were estimated based on information from various sources, including HED’s Standard Operating Procedures (SOPs) for Residential Exposure Assessments (USEPA 2000 and 2001), and personal communication with experts.  In particular, the use information for oil-well uses and cooling water tower uses are based on personal communication with biocide manufacturers for these types of uses.  The individuals contacted have experience in these operations and their estimates are believed to be the best available without undertaking a statistical survey of the uses.  In certain cases, no standard values were available for some scenarios.  Assumptions for these scenarios were based on AD estimates and could be further refined from input from registrants.

- The percent active ingredient in solution for the pressure treatment of lumber needs to be refined by the registrant.  The labels only provided a retention rate.  For this assessment, the application rate on the master label was used, which is the same as the application rate for non-pressure treatment of lumber.

# 7.0	REFERENCES

American Chemistry Council (ACC). 2002a.  Assessment of Potential Inhalation and Dermal Exposure Associated With Pressure Treatment of Wood with Arsenical Wood Products.  MRID 4550211-01.

American Chemistry Council (ACC). 2002b.  An Analysis of the Training Patterns and Practices of Competitive Swimmers.  Prepared by Richard Reiss.  Sciences International, Inc. Alexandria, Virginia.  December 9, 2002.

Bestari KT, Macey K, Soloman KR, Tower N. 1999.  Measurement and Assessment of Dermal and Inhalation Exposures to Didecyl Dimethyl Ammonium Chloride (DDAC) Used in the Protection of Cut Lumber (Phase III). MRID 455243-04.

CEC, 2001.  Residential Manual for Compliance with California’s 2001 Energy Efficiency Standards.  http://www.energy.ca.gov/title24/residential_manual/index.html, viewed January 2005.

DOE.  1997.  Energy Information Administration: Profile of Commercial Buildings in 1995.  http://www.eia.doe.gov/emeu/cbecs/char95/profile.html

Freeman, N , Jimenez M, Reed KJ,Gurunathan S, Edwards RD, Roy A, Adgate JL, Pellizzari ED, Quackenboss J, Sexton K, Lioy PJ, 2001.  Quantitative analysis of chilren’s microactivity patterns:  The Minnesota Children’s Pesticide Exposure Study.  Journal of Exposure Analysis and Environmental Epidemiology.  11(6): 501-509.

Helwig, D. (2003) Personal Communication between D. Helwig (Johnson Diversy, Inc) and K. Riley (Versar, Inc.), November 11, 2003.

HERA, 2003.  Human and Environmental Risk Assessment, Guidance Document Methodology, April 22, 2002 (http://www.heraproject.com/files/Guidancedocument.pdf).

HERA, 2005.  Human and Environmental Risk Assessment, Guidance Document Methodology, February 2005 (http://www.heraproject.com).

MCCEM V 1.2  The Multi-Chamber Concentration and Exposure Model (MCCEM) Model Version 1.2. Prepared for the US EPA Office of Pollution Prevention and Toxics. Prepared by Versar, Inc. and Wilkes Technologies, LLC.

Jacobson, Larry. 2005.  Professor and Extension Engineer at University of Minnesota.

SIMetric. 2005.  http://www.simetric.co.uk/si_materials.htm  Last viewed November 9, 2005.

USEPA.  Undated.  RISK.  Version 1.9.27.  Developed by Dr. Les Sparks of USEPA/NRMRL/ APPCD.

USEPA. 1996.  Office of Research and Development, Descriptive Statistics Tables from a Detailed Analysis of the National Human Activity Pattern (NHAPS) Data; EPA/600/R-96/148, July 1996.   Data Collection Period October 1992 - September 1994 .

USEPA.  1997.  Exposure Factors Handbook. Volume I-II.  Office of Research and Development.  Washington, D.C.  EPA/600/P-95/002Fa. August 1997.

USEPA. 1998. PHED Surrogate Exposure Guide. Estimates of Worker Exposure from the Pesticide Handler Exposure Database Version 1.1.   Washington, DC:  U.S. Environmental Protection Agency.

USEPA. 1999.  Evaluation of Chemical Manufacturers Association Antimicrobial Exposure Assessment Study (Amended on 8 December 1992).  Memorandum from Siroos Mostaghimi, PH.D., USEPA to Julie Fairfax, USEPA. Dated November, 4 1999.  DP Barcode D247642.

USEPA.  2000.  Residential SOPs.  EPA Office of Pesticide Programs(Human Health Effects Division. Dated April 5, 2000.

USEPA.  2001.  HED Science Advisory Council for Exposure. Policy Update, November 12.  Recommended Revisions to the Standard Operating Procedures (SOPs) for Residential Exposure Assessment, February 22, 2001.

USEPA. 2003.  Assessment of the Proposed Bardac Wood Preservative Pressure Treatment Use.  Memorandum from Tim Leighton and Siroos Mostaghimi.  February 11, 2003.

USEPA. 2004.  Occupational and Residential Exposure Assessment for Carboquat WP-50.  Memorandum from Siroos Mostaghimi, USEPA to Welma Noble, USEPA.   Dated November 4, 2004. DP Barcodes D303714 and D303938.

USEPA. 2006.  Didecyl dimethyl benzyl ammonium chloride (DDAC) – Report of the Antimicrobials Division Toxicity Endpoint Committee (ADTC) and the Hazard Identification Assessment Review Committee (HIARC).  January 9, 2006.

# APPENDIX A: Master DDAC Label

| EPA Reg Number used for Max. Appl. Rate | Use Site | Treatment Site/Surfaces | Method of Application | Notes | Freq of Application |
| --- | --- | --- | --- | --- | --- |
| Industrial processes and water systems |
| 1839-129 | Industrial Recirc Water Systems | Cooling Towers (including evaporative condensers, dairy sweetwater systems, cooling canals, pasteurizers, tunnel coolers and warmers) | Pour/metered | 1839-129 (50% ai) | Weekly |
| 10707-46 | cooling water, disposal water, oil field operations |  | slug treatment |  |  |
| 1839-151 | Oil Field water flood or salt water disposal | oil field water disposal systems | pour/metered | 1839-151 | As needed |
| 1839-179 | Oil Field | injection and wastewater | continuous injection | Blend with ADBAC | As needed |
| 1839-179 | Oil Field | injection and wastewater | batch treatment | Blend with ADBAC | As needed |
| 1839-179 | Oil Field | packer fluids |  | Blend with ADBAC | As needed |
| 1839-179 | Oil Field | drilling muds |  | Blend with ADBAC | As needed |
| Swimming Pools |
| 10324-69 | Swimming Pool |  | pour |  | Once weekly |
| 1839-133 | Outside Spas/Whirlpools/Hot Tub Bath |  | pour |  | Weekly |
| Aquatic Areas |
| 499-482 | greenhouse/nurseries, golf courses, recreational parks, amusement parks, universities, cemeteries | decorative fountains, decorative pools, ponds, water displays, standing waters | dribble, spray ring | Blend with ADBAC | As needed |
| 499-482 | greenhouse/nurseries | irrigation system, watering lines, drip lines, emitters, watering nozzles, and hoses | immersing or running thru system | Blend with ADBAC | As needed |
| Wood Treatment |  |  |  |  |  |
| 6836-212 | Pressure Treatment |  |  | 3% ai soln | As needed |
| 6836-212 | Double vacuum |  |  | 3% ai soln | As needed |
| 6836-212 | Dip/Spray surface treatment |  |  | 3% ai soln | As needed |
| Agricultural Premises and Equipment |
| 10324-80 | hatcheries, swine/poultry/turkey farms, egg receiving area, egg holding area, setter room, tray dumping area, chick holding room, poultry buildings, dressing plants, farrowing barns and areas, blocks, creep areas, chick holding area, hatchery room, chick processing area, and chick loading area | toilets, urinals, portable toilets, floors, walls, ceilings, feed racks, mangers, troughs, automatic feeders/fountains/waterers, other feeding and watering appliances, halters, ropes and other types of equipment used in handling and restraining animals, as well as forks, shovels, and scrapers used for removing litter and manure, blocks, chutes, incubators, hatchers, glazed porcelain, glazed ceramic tile, glass | mop, wipe, spray, immersion |  | As needed |
| 10324-81 | hatchery rooms |  | fogging | Blend with ADBAC | As needed |
| 10324-81 | incubators and hatchers |  | fogging | Blend with ADBAC | Every 12 hrs |
| 10324-108 | Mushroom Farm | breezeways and track alleys before spawning, inside and outside walls of mushroom houses, lofts, floors, storage sheds and casing rings | mop, wipe | Blend with ADBAC | As needed |
| 1839-167 | Mushroom Farm | breezeways and track alleys before spawning, inside and outside walls of mushroom houses, lofts, floors, storage sheds and casing rings | cloth, mop, sponge, spray, immersion | Blend with ADBAC | As needed |
| 1839-167 | Mushroom Farm | waterproof footwear | immersion (shoe bath) | Blend with ADBAC | As needed |
| 1839-167 | Citrus Farm | trucks, vehicles, equipment, trailers, field harvesting equipment, cargo area, wheels, tires, under carriage, hood, roof, fenders | spray, dip, brush | Citrus canker, Blend with ADBAC | As needed |
| 10324-117 | Animal housing facilities | boots and shoes | immersion | Blend with ADBAC | As needed |
| 1839-167 | Florists/flower shops, greenhouses, shippers, packing areas | flower buckets, coolers, floors and walls of coolers, design and packing benches, garbage pails | Mop/wipe, cloth, brush, sponge, sprayer | Blend with ADBAC | As needed |
| 241-74 | Greenhouses | ornamental plants - plant regulator | spray, drench |  |  |
| 499-482 | greenhouse/ nursuries | work tables, benches, pots, flats,knives, pruning tools, floors, plant containers, carts, transplant trays, hanging baskets, tray/ pot holders, water collectors, walkways, windows | immersion, spray, brush | Blend with ADBAC | As needed |
| 48815-1 | farms | fish aquariums, tanks, fish handling equipment, nets, seines, traps, filter boxes, pumps, air diffusers, shipping boxes, feeding equipment, floors, countertops, raceways, garbage pails, other hard nonporous surfaces, holding tanks, lavatories. | immersion, brush, mop or cloth |  | As needed |
| Residential and Public Access Premises |
| 10324-134 | Homes | floors, walls, windows, toilets, bathtubs, shower stalls, shower door/curtain, sinks, mirrors, restroom fixtures, cabinets, tables, chairs, desks, bed frames, doorknobs, garbage cans/pails, outdoor furniture, telephones, glazed porcelain, glazed ceramic tile, glass, Countertops (kitchen/food prep); Internal (external) surfaces of appliances (refrigerator, microwave, freezer); stovetop; table surfaces; sinks, shelves, racks | mop, wipe, (cloth), spray | Disinfect Heavy Duty Cleaning | As needed |
| 1839-175 | Home | floors, walls, metal surfaces, stainless steel, glazed porcelain, glazed ceramic tile, shower stalls, bathtubs, cabinets, plastic surfaces | RTU wipe/spray | Blend with ADBAC | As needed |
| 10324-108 | homes | Carpets | Rotary Floor Machine | Blend with ADBAC | 300-500 sq ft/gal |
| 3573-69 | home | Furniture upholstery, window treatments, clothing, plush toys, shoes/sneakers, children mattresses, pet bed, sports bag/equipment, carpet | Spray (fabric sanitizer) |  | As Needed |
| 3573-69 | homes, mobile home, car, campgrounds, trailer, camper, boat | floors, walls, toilets, urinals, bathrooms, bathtubs, sinks, countertops, shower doors/curtains, toilet seats, shower stalls, tables, chairs, shelves, telephones, cabinets, desks, bed springs, door knobs, linen carts, hampers, exercise equipment,cat litter boxes, bidets, diaper changing tables, toys, high chairs, fountains, synthetic marbel, vinyl, linoleum , sealed granite, glazed porcelain, microwave oven exteriors, marlite, plastic, outdoor furniture, laundry hampers, | spray (disinfect) | potable rinse for chidren toys and food contact |  |
| 10324-117 | Homes | cooking utensils; coolers/ice chest; cups; cutlery; dishes; eating utensils; glassware | Immersion | Blend with ADBAC | As needed |
| 1836-167 | campgrounds, playgrounds, Public facilites, mobile homes, cars, campers, trailers, trucks | floors, walls, toilets, urinals, bathrooms, bathtubs, sinks, countertops, shower doors/curtains, toilet seats, shower stalls, tables, chairs, shelves, telephones, cabinets, desks, bed springs, door knobs, linen carts, hampers, exercise equipment, automobile/truck interiors, garbage cans/pails, fixtures, metal, stainless steel. glazed porcelain, glazed ceramic tile, plastic, granite, marble, chrome, vinyl, glass, enameled surfaces, painted wood work, Formica, vinyl and plastic upholstery, chrome plated fixtures | cloth, mop, sponge, spray | Blend with ADBAC | As needed |
| 10324-117 | homes | water softners and reverse osmosis units | pour |  | As needed |
| 6718-24 | homes | bedframes, tables, sinks, walls, countertops, chairs, other hard nonporous surfaces | cloth, mop, spray |  | As needed |
| 1839-178 | homes | counters, stovetops, sinks, outside microwaves, refrigerator exteriors, walls, appliances, finished wood, cabinets, floors, exterior toilet bowl surfaces, trash cans, tubs, shower walls, bathrooms, door knobs, closets, phones, car interiors, computers, hand rails, switch plates, door frames, urinals, desks, cribs, changing tables, patio furniture, dining room surfaces | RTU wipe/spray | Blend with ADBAC | As needed |
| 48815-1 | homes | fish aquariums, tanks, fish handling equipment, nets, seines, traps, filter boxes, pumps, air diffusers, shipping boxes, feeding equipment, floors, countertops, raceways, garbage pails, other hard nonporous surfaces, holding tanks, lavatories. | immersion, brush, mop or cloth |  | As needed |
| 10324-80 | homes | air ducts | spray, brush,mop, wipe, ULV or mist generating, automated spray | odor causing bacteria, fungi | 6 months |
| Medical Premises and Equipment |
| 1839-167 | Hospitals, Health Care facilities, Medical/Dental offices, Nursing homes, operating rooms, patient care facilities, clinics, isolation wards, medical research facilities, autopsy rooms, ICU areas, recovery anesthesia, emergency rooms, X-ray cat labs, newborn nurseries, orthopedics, respiratory therapy, acute care institutions, alternate care institutions, healthcare institutions, Funeral Homes, mortuaries | floors, walls, toilets, urinals, lavatories, bathrooms, bathing areas, bathtubs, sinks, sink tops, shower stalls, shower doors/curtains, mirrors, ultrasonic bath, whirlpools, foot baths, countertops, cabinets, tables, chairs, desks, hospital beds, bed springs, bed frames, traction devices, MRI, CAT, examining tables, scales, paddles, wheelchairs, lifts, door knobs, wheel chairs, telephones, garbage pails/cans, fixtures, metal, stainless steel. glazed porcelain, glazed ceramic tile, plastic, granite, marble, chrome, vinyl, glass, enameled surfaces, painted wood work, | Wipe, mop, (cloth), swab, brush, spray | Blend with ADBAC | As needed |
| 10324-81 | Nurseries | Floors, walls, countertops (non-kitchen), sinks (bathroom), toilets, external surfaces of appliances | mop, wipe (cloth) | Blend with ADBAC | As needed |
| 1839-175 | Medical Institutions, Hospitals, and Nursing Homes | floors, walls, metal surfaces, stainless steel, glazed porcelain, glazed ceramic tile, shower stalls, bathtubs, cabinets, plastic surfaces | RTU wipe/spray | Blend with ADBAC | As needed |
| 10324-134 | hospitals, medical/dental offices, nursing homes | floors, walls, windows, toilets, bathtubs, shower stalls, shower door/curtain, sinks, mirrors, restroom fixtures, cabinets, tables, chairs, desks, bed frames, doorknobs, garbage cans/pails, telephones, glass, glazed porcelain, glazed ceramic tile, table surfaces; sinks, shelves, racks | mop, wipe, (cloth), spray | Disinfect Heavy Duty Cleaning | As needed |
| 1839-167 | nursing homes and hospitals | floors, walls, windows, toilets, bathtubs, shower stalls, shower door/curtain, sinks, mirrors, restroom fixtures, cabinets, tables, chairs, desks, bed frames, doorknobs, garbage cans/pails, telephones, glass, glazed porcelain, glazed ceramic tile, enameled surfaces, countertops (kitchen/food prep); Internal external surfaces of appliances (refrigerator, microwave, freezer); stovetop, shelves, racks | portable extraction units, truck mounted extraction machines, rotary floor machines, metered, spray | Blend with ADBAC | As needed |
| 6718-24 | hospitals, nursing homes | bedframes, tables, sinks, walls, countertops, chairs, other hard nonporous surfaces | cloth, mop, spray |  | As needed |
| 1839-178 | hospitals, day-care facilities, sick rooms | counters, stovetops, sinks, outside microwaves, refrigerator exteriors, walls, appliances, finished wood, cabinets, floors, exterior toilet bowl surfaces, trash cans, tubs, shower walls, bathrooms, door knobs, closets, phones, car interiors, computers, hand rails, switch plates, door frames, urinals, desks, cribs, changing tables | RTU wipe | Blend with ADBAC | As needed |
| 1839-173 | Morgues and Funeral homes | human remains | sponge, wash cloth, soft brush | Blend with ADBAC | As needed |
| 10324-80 | hospitals, nursing homes | air ducts | spray, brush,mop, wipe, ULV or mist generating, automated spray | odor causing bacteria, fungi | 6 months |
| Commercial, Institutional, and Industrial premises and equipment |
| 10324-134 | Athletic/recreational facilities, exercise facilities, schools, colleges, dressing rooms, transportation terminals, institutions | floors, walls, windows, toilets, bathtubs, shower stalls, shower door/curtain, sinks, mirrors, restroom fixtures, cabinets, tables, chairs, desks, bed frames, doorknobs, garbage cans/pails, outdoor furniture, telephones, glass, glazed porcelain, glazed ceramic tile, chrome plated intakes, enameled surfaces, countertops (kitchen/food prep); Internal (external) surfaces of appliances (refrigerator, microwave, freezer); stovetop; table surfaces; sinks, shelves, racks | mop, wipe, (cloth), spray | Disinfect Heavy Duty Cleaning | As needed |
| 1839-167 | Athletic/recreational facilities, exercise facilites, locker rooms, dressing rooms, schools, colleges, transportation terminals, | floors, walls, toilets, urinals, bathrooms, bathtubs, sinks, countertops, shower doors/curtains, toilet seats, shower stalls, tables, chairs, shelves, telephones, cabinets, desks, bed springs, door knobs, garbage cans/pails, fixtures, metal, stainless steel. glazed porcelain, glazed ceramic tile, plastic, granite, marble, chrome, vinyl, glass, enameled surfaces, painted wood work, | cloth, mop, sponge, spray | Blend with ADBAC | As needed |
| 1839-167 | motels, hotels, schools | carpets | portable extraction units, truck mounted extraction machines, rotary floor machines, metered, spray | Cleaning Claim Blend with ADBAC | As needed |
| 1839-175 | Hotels and schools | floors, walls, metal surfaces, stainless steel, glazed porcelain, glazed ceramic tile, shower stalls, bathtubs, cabinets, plastic surfaces | RTU wipe/spray | Blend with ADBAC | As needed |
| 6836-78 | Barber and Beauty Salons | Barber/ Beauty Instruments and Tools | immersion | Blend with ADBAC | As needed |
| 1839-178 | Barber and Beauty Salons, Health clubs, hotels, motels, emergency vehicles, transportation terminals, correctional facilities, factories, | counters, sinks, walls, finished wood, cabinets, floors, exterior toilet bowl surfaces, trash cans, tubs, shower walls, bathrooms, door knobs, closets, phones, car interiors, computers, hand rails, switch plates, door frames, urinals, desks, | RTU wipe | Blend with ADBAC | As needed |
| 1839-167 | commercial florists | flower buckets, coolers, floors and walls of coolers, design and packing benches, garbage pails | cloth, mop, sponge, spray | Blend with ADBAC | As needed |
| 3573-69 | Hotels, dorms, convenience stores, recreational centers, offices, motels, | floors, walls, toilets, urinals, bathrooms, bathtubs, sinks, countertops, shower doors/curtains, toilet seats, shower stalls, tables, chairs, shelves, telephones, cabinets, desks, bed springs, door knobs, linen carts, hampers, exercise equipment, bidets, fountains, synthetic marble, vinyl, linoleum , sealed granite, glazed porcelain, microwave oven exteriors, marlite, plastic, outdoor furniture, laundry hampers, | spray (disinfect) | potable rinse for chidren's toys and food contact surfaces |  |
| 1677-109 | Commercial and institutional laundry mats | clothing | pour at final rinse or sour to washweel | per 100lbs fabric dry wt | 2wk protect 3wk protect 30dy protect |
| 6718-24 | industry and schools | bedframes, tables, sinks, walls, countertops, chairs, other hard nonporous surfaces | cloth, mop, spray |  | As needed |
| 48815-1 | Schools, Institutional, and Industrial | fish aquariums, tanks, fish handling equipment, nets, seines, traps, filter boxes, pumps, air diffusers, shipping boxes, feeding equipment, floors, countertops, raceways, garbage pails, other hard nonporous surfaces, holding tanks, lavatories. | immersion, brush, mop or cloth |  | As needed |
| 10324-80 | Institutional, Industrial premise, school, restaurant | air ducts | spray, brush,mop, wipe, ULV or mist generating, automated spray | odor causing bacteria, fungi | 6 months |
| Food Handling/Storage Establishments premises and equipment |
| 1839-152 | Restaurants, food service establishments, food processing plants/facilities, beverage processing plants, Bars, Cafeterias, Convenience stores, supermarkets, Dairies, Egg Processing plants, Federally inspected meat and poultry plants , Food Handling areas, Food preparation areas, Food storage areas, Institutional kitchens, USDA inspected food processing facilities, breweries, fast food operations | floors, walls, countertops, appliances (microwaves, refrigerators, stove tops, freezers, coolers), chairs, tables, shelves, picnic tables, outdoor furniture, racks, carts, telephones, door knobs, storage areas, potato storage areas, food storage areas, garbage storage areas, cutting boards, tanks, exhaust fans, refrigerator bins, refrigerated storage/display equipment, coils and drain pans of air conditioning/refrigeration equipment, heat pumps, storage tanks, coolers, ice chests, garbage cans/pails | cloth, mop, spray, flood, immersion, |  | As needed |
| 1839-175 | Restaurants | floors, walls, tables, shelves, garbage disposal areas, metal surfaces, stainless steel, glazed porcelain, glazed ceramic tile, shower stalls, bathtubs, cabinets, plastic surfaces | RTU spray/wipe | Blend with ADBAC | As needed |
| 10324-81 | Dairies and Food Processing Facilities | floors, walls, metal surfaces, stainless steel, glazed porcelain, glazed ceramic tile, shower stalls, bathtubs, cabinets, plastic surfaces | fogging | Blend with ADBAC | As needed |
| 10324-134 | bottling and beverage plants, breweries, tobacco, egg processing plants, meat/poultry processing plants, rendering plants, fishery/milk/citrus/wine/ice cream/ potato processing plants, restaurants | floors, walls, tables, shelves, garbage cans, garbage disposal areas, glazed porcelain, glazed ceramic tile, glass | mop, wipe, (cloth), spray |  | As needed |
| 1839-178 | Restaurants | counters, stovetops, sinks, outside microwaves, refrigerators exteriors, walls, appliances, finished wood, cabinets, floors, exterior toilet bowl surfaces, trash cans, tubs, shower walls, bathrooms, door knobs, closets, phones, computers, hand rails, switch plates, door frames, urinals, desks, dining room surfaces | RTU wipe | Blend with ADBAC | As needed |
| 10324-117 | bottling and beverage plants, breweries, tobacco, egg processing plants, meat/poultry processing plants, rendering plants, fishery/milk/citrus/wine/ice cream/ potato processing plants, restaurants | ice machines, water coolers, counters, tables, food processing equipment, food utensils, dairy equipment, dishes, silverware, eating utensils, glasses, sinks, counters, refrigerated/storage display equipment | spray, wipe, sponge, immersion |  | As needed |
| 10324-117 | bottling and beverage plants, breweries, tobacco, egg processing plants, meat/poultry processing plants, rendering plants, fishery/milk/citrus/wine/ice cream/ potato processing plants, | water softners and reverse osmosis units | pour |  | As needed |
| 10324-117 | bottling and beverage plants, breweries, tobacco, egg processing plants, meat/poultry processing plants, rendering plants, fishery/milk/citrus/wine/ice cream/ potato processing plants, | boots and shoes | immersion | Blend with ADBAC | As needed |
| 1839-173 | dairies, beverage, and food processing plants | floors, walls, countertops, appliances (microwaves, refrigerators, stove tops, freezers, coolers), chairs, tables, shelves, racks, carts, telephones, door knobs, storage areas, potato storage areas, food storage areas, garbage storage areas, cutting boards, tanks, exhaust fans, refrigerator bins, refrigerated storage/display equipment, storage tanks, coolers, ice chests, garbage cans/pails | fogging | Blend with ADBAC | As needed |
| 10324-80 | food processing plants, food service areas, institutional kitchens, industrial/hospital caferias, school lunchrooms, dairies, and packing plants | air ducts | spray, brush,mop, wipe, ULV or mist generating, automated spray | odor causing bacteria, fungi | 6 months |
| Clean/Deodorization |
| 1839-167 | Water/Smoke restoration (institutional, industrial, hospital) | carpets, carpet cushion, sub floors, drywall, trim, farm lumber, tackless strip and paneling | Pour, brush, spray | Blend with ADBAC | As needed |
| 1839-167 | Sewer backup/river flood cleanup, (clean water source) | carpets, carpet cushion, sub floors, drywall, trim, farm lumber, tackless strip and paneling | spray | Blend with ADBAC | As needed |
| 1839-167 | garbage storage areas, pet areas, garbage bins & cans |  |  | Blend with ADBAC | As needed |
| 71814-1 | hospitals | Medical waste | pour | blend w/ ADBAC | Poured into machine |

# APPENDIX B: Summary of CMA and PHED Data

Chemical Manufacturers Association (CMA) Data:

In response to an EPA Data Call-In Notice, a study was undertaken by the Institute of Agricultural Medicine and Occupational Health of The University of Iowa under contract to the Chemical Manufacturers Association.  In order to meet the requirements of Subdivision U of the Pesticide Assessment Guidelines (superseded by  Series 875.1000-875.1600 of the Pesticide Assessment Guidelines), handler exposure data are required from the chemical manufacturer specifically registering the antimicrobial pesticide.   The applicator exposure study must comply with the assessment guidelines for (Applicator Exposure Monitoring( in Subdivision U and the (Occupational and Residential Exposure Test Guidelines( in Series 875.  For this purpose, CMA submitted a study on 28 February, 1990, entitled "Antimicrobial Exposure Assessment Study (amended on December 8, 1992)" which was conducted by William Popendorf, et al.  It was evaluated and accepted by Occupational and Residential Exposure Branch (OREB) of Health Effect Division (HED), Office of Pesticides Program (OPP) of EPA in 1990.  The purpose of this CMA study was to characterize exposure to antimicrobial chemicals in order to support pesticide reregistrations (CMA, 1992).  The unit exposures presented in the most recent EPA evaluation of the CMA database (USEPA, 1999b) were used in this assessment.

The Agency determined that the CMA study had fulfilled the basic requirements of Subdivision U - Applicator Exposure Monitoring.  The advantages of CMA data over other (surrogate data sets( is that the chemicals and the job functions of mixer/loader/applicator were defined based on common application methods used for antimicrobial pesticides.  A few of the deficiencies in the CMA data are noted below:

- The inhalation concentrations were typically below the detection limits, so the unit exposures for the inhalation exposure route could not be accurately calculated.

- QA/QC problems including lack of either/or field fortification, laboratory recoveries, and storage stability information.

- Data have an insufficient amount of replicates.

The Pesticide Handlers Exposure Database (PHED):

The Pesticide Handlers Exposure Database (PHED) has been developed by a Task Force consisting of representatives from Health Canada, the U.S. Environmental Protection Agency (EPA), and the American Crop Protection Association (ACPA).  PHED provides generic pesticide worker (i.e., mixer/loader and applicator) exposure estimates.  The dermal and inhalation exposure estimates generated by PHED are based on actual field monitoring data, which are reported generically (i.e., chemical specific names not reported) in PHED.  It has been the Agency(s policy to use (surrogate( or (generic( exposure data for pesticide applicators in certain circumstances because it is believed that the physical parameters (e.g., packaging type) or application technique (e.g., aerosol can), not the chemical properties of the pesticide, attribute to exposure levels. [Note: Vapor pressures for the chemicals in PHED are in the range of E-5 to E-7 mm Hg.]  Chemical specific properties are accounted for by correcting the exposure data for study specific field and laboratory recovery values as specified by the PHED grading criteria.

PHED handler exposure data are generally provided on a normalized basis for use in exposure assessments.  The most common method for normalizing exposure is by pounds of active ingredient (ai) handled per replicate (i.e., exposure in mg per replicate is divided by the amount of ai handled in that particular replicate).  These unit exposures are expressed as mg/lb ai handled.  This normalization method presumes that dermal and inhalation exposures are linear based on the amount of active ingredient handled.

# APPENDIX C: Input/Output from Residential MCCEM Modeling

Humidifier

MCCEM SUMMARY REPORT

TITLE:    Humidifier - 8hrs - Adult

RUN         Day  Hour  Min      Length   Days  Hours  Min     Reporting

TIME  Start: 0    0     0       of Run:   2     0      0      Interval: 60 minutes

HOUSE   Type: Generic house      State: NA                  Code: GN001

Season: SUMMER             Zones: 2      Infiltration Rate: 0.18 ACH

EMISSIONS   Source   Zone   Type              Details

¯¯¯¯¯¯   ¯¯¯¯   ¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯   ¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯

1       1     Constant          Emission Rate = 0.895  g/hr

2

3

4

SINKS  Sink  Zone  Model          Details

¯¯¯¯  ¯¯¯¯  ¯¯¯¯¯¯¯¯¯¯¯¯¯  ¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯

1

2

3

4

5

6

ACTIVITIES    Primary Activity Pattern is used on days: 1,2,3,4,5,6,7

OVERRIDE ACTIVITIES:  YES

DOSE

Events/yr:    Yrs of Use:    Weight(kg): 60   Length of Life(yrs):

MONTE CARLO: NO          Number of Trials:  1          Seed No:    Random

OPTIONS  Single Chamber:  YES          Saturation Concentration (mg/m³):  NONE      Output Concentration Units: mg/m³

Initial Concentrations          Units:  mg/m³

Zone 1:  0      Zone 2: 0      Zone 3: 0      Zone 4: 0      Outdoors: 0

____________________________________________________________________________

RESULTS

¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯

LADD:  0.011809  mg/(kg day)

LADC:  0.059043  mg/m³

ADD:   0.011809  mg/(kg day)

ADC:  0.059043  mg/m³

Single Event Dose:  258.79  mg

Peak Concentration:  12.191  mg/m³

APDR:  2.4298  mg/(kg day)

Time when APDR occurred:  1.9587  days

Average Inhalation Rate:  12  m³/day

____________________________________________________________________________

MCCEM SUMMARY REPORT

TITLE:    Humidifier - 8hrs - Child

RUN         Day  Hour  Min      Length   Days  Hours  Min     Reporting

TIME  Start: 0    0     0       of Run:   2     0      0      Interval: 60 minutes

HOUSE   Type: Generic house      State: NA                  Code: GN001

Season: SUMMER             Zones: 2      Infiltration Rate: 0.18 ACH

EMISSIONS   Source   Zone   Type              Details

¯¯¯¯¯¯   ¯¯¯¯   ¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯   ¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯

1       1     Constant          Emission Rate = 0.895  g/hr

2

3

4

SINKS  Sink  Zone  Model          Details

¯¯¯¯  ¯¯¯¯  ¯¯¯¯¯¯¯¯¯¯¯¯¯  ¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯

1

2

3

4

5

6

ACTIVITIES    Primary Activity Pattern is used on days: 1,2,3,4,5,6,7

OVERRIDE ACTIVITIES:  YES

DOSE

Events/yr:    Yrs of Use:    Weight(kg): 15   Length of Life(yrs):

MONTE CARLO: NO          Number of Trials:  1          Seed No:    Random

OPTIONS  Single Chamber:  YES          Saturation Concentration (mg/m³):  NONE      Output Concentration Units: mg/m³

Initial Concentrations          Units:  mg/m³

Zone 1:  0      Zone 2: 0      Zone 3: 0      Zone 4: 0      Outdoors: 0

____________________________________________________________________________

RESULTS

¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯

LADD:  0.037787  mg/(kg day)

LADC:  0.059043  mg/m³

ADD:   0.037787  mg/(kg day)

ADC:  0.059043  mg/m³

Single Event Dose:  207.03  mg

Peak Concentration:  12.191  mg/m³

APDR:  7.7754  mg/(kg day)

Time when APDR occurred:  1.9587  days

Average Inhalation Rate:  9.6  m³/day

____________________________________________________________________________

| Humidifier - 8hrs |
| --- |
| Time (days) | Time (hrs) | Conc Outdoors (mg/m³) | Conc Zone 1 (mg/m³) | Conc@Person(mg/m³) |
| 0 | 0 | 0 | 0 | 0 |
| 0.0416667 | 1 | 7.59E-59 | 2.00763 | 2.00763 |
| 0.0833334 | 2 | 2.87E-58 | 3.68471 | 3.68471 |
| 0.125 | 3 | 6.10E-58 | 5.08566 | 5.08566 |
| 0.166667 | 4 | 1.03E-57 | 6.25594 | 6.25594 |
| 0.208334 | 5 | 1.52E-57 | 7.23354 | 7.23354 |
| 0.25 | 6 | 2.09E-57 | 8.05018 | 8.05018 |
| 0.291667 | 7 | 2.70E-57 | 8.73237 | 8.73237 |
| 0.333334 | 8 | 3.36E-57 | 9.30223 | 9.30223 |
| 0.375 | 9 | 4.07E-57 | 9.77826 | 9.77826 |
| 0.416667 | 10 | 4.80E-57 | 10.1759 | 10.1759 |
| 0.458334 | 11 | 5.56E-57 | 10.5081 | 10.5081 |
| 0.5 | 12 | 6.34E-57 | 10.7856 | 10.7856 |
| 0.541667 | 13 | 7.14E-57 | 11.0174 | 11.0174 |
| 0.583334 | 14 | 7.96E-57 | 11.211 | 11.211 |
| 0.625 | 15 | 8.78E-57 | 11.3728 | 11.3728 |
| 0.666667 | 16 | 9.62E-57 | 11.5079 | 11.5079 |
| 0.708334 | 17 | 1.05E-56 | 11.6208 | 11.6208 |
| 0.750001 | 18 | 1.13E-56 | 11.7151 | 11.7151 |
| 0.791667 | 19 | 1.22E-56 | 11.7938 | 11.7938 |
| 0.833334 | 20 | 1.31E-56 | 11.8596 | 11.8596 |
| 0.875001 | 21 | 1.39E-56 | 11.9146 | 11.9146 |
| 0.916667 | 22 | 1.48E-56 | 11.9605 | 11.9605 |
| 0.958334 | 23 | 1.57E-56 | 11.9989 | 11.9989 |
| 1 | 24 | 1.66E-56 | 12.0309 | 12.0309 |
| 1.04167 | 25 | 1.75E-56 | 12.0577 | 12.0577 |
| 1.08333 | 26 | 1.83E-56 | 12.08 | 12.08 |
| 1.125 | 27 | 1.92E-56 | 12.0987 | 12.0987 |
| 1.16667 | 28 | 2.01E-56 | 12.1143 | 12.1143 |
| 1.20833 | 29 | 2.10E-56 | 12.1273 | 12.1273 |
| 1.25 | 30 | 2.19E-56 | 12.1382 | 12.1382 |
| 1.29167 | 31 | 2.28E-56 | 12.1473 | 12.1473 |
| 1.33333 | 32 | 2.37E-56 | 12.1549 | 12.1549 |
| 1.375 | 33 | 2.46E-56 | 12.1613 | 12.1613 |
| 1.41667 | 34 | 2.55E-56 | 12.1666 | 12.1666 |
| 1.45833 | 35 | 2.64E-56 | 12.171 | 12.171 |
| 1.5 | 36 | 2.73E-56 | 12.1747 | 12.1747 |
| 1.54167 | 37 | 2.81E-56 | 12.1778 | 12.1778 |
| 1.58333 | 38 | 2.90E-56 | 12.1804 | 12.1804 |
| 1.625 | 39 | 2.99E-56 | 12.1825 | 12.1825 |
| 1.66667 | 40 | 3.08E-56 | 12.1843 | 12.1843 |
| 1.70833 | 41 | 3.17E-56 | 12.1858 | 12.1858 |
| 1.75 | 42 | 3.26E-56 | 12.1871 | 12.1871 |
| 1.79167 | 43 | 3.35E-56 | 12.1881 | 12.1881 |
| 1.83333 | 44 | 3.44E-56 | 12.189 | 12.189 |
| 1.875 | 45 | 3.53E-56 | 12.1897 | 12.1897 |
| 1.91667 | 46 | 3.62E-56 | 12.1904 | 12.1904 |
| 1.95833 | 47 | 3.71E-56 | 12.1909 | 12.1909 |
| 2 | 48 | 3.80E-56 | 12.1883 | 12.1883 |
| Adults |
| 8 hr exposure duration concentration (0 to 8 hr) | 5.59 |
| Time (hr) | 8 |
| Body Weight (kg) | 60 |
| Inhalation (m3/hr) | 0.50 |
| Dose (mg/kg/day) | 0.373 |
| NOAEL (mg/kg/day) | 10 |
| MOE | 27 |
| Children |
| 8 hr exposure duration concentration (0 to 8 hr) | 5.59 |
| Time (hr) | 8 |
| Body Weight (kg) | 15 |
| Inhalation (m3/hr) | 0.40 |
| Dose (mg/kg/day) | 1.19 |
| NOAEL (mg/kg/day) | 10 |
| MOE | 8.4 |

MCCEM SUMMARY REPORT

TITLE:    Humidifier - 24hrs - Adult

RUN         Day  Hour  Min      Length   Days  Hours  Min     Reporting

TIME  Start: 0    0     0       of Run:   2     0      0      Interval: 60 minutes

HOUSE   Type: Generic house      State: NA                  Code: GN001

Season: SUMMER             Zones: 2      Infiltration Rate: 0.18 ACH

EMISSIONS   Source   Zone   Type              Details

¯¯¯¯¯¯   ¯¯¯¯   ¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯   ¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯

1       1     Constant          Emission Rate = 0.895  g/hr

2

3

4

SINKS  Sink  Zone  Model          Details

¯¯¯¯  ¯¯¯¯  ¯¯¯¯¯¯¯¯¯¯¯¯¯  ¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯

1

2

3

4

5

6

ACTIVITIES    Primary Activity Pattern is used on days: 1,2,3,4,5,6,7

OVERRIDE ACTIVITIES:  YES

DOSE

Events/yr:    Yrs of Use:    Weight(kg): 60   Length of Life(yrs):

MONTE CARLO: NO          Number of Trials:  1          Seed No:    Random

OPTIONS  Single Chamber:  YES          Saturation Concentration (mg/m³):  NONE      Output Concentration Units: mg/m³

Initial Concentrations          Units:  mg/m³

Zone 1:  0      Zone 2: 0      Zone 3: 0      Zone 4: 0      Outdoors: 0

____________________________________________________________________________

RESULTS

¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯

LADD:  0.013088  mg/(kg day)

LADC:  0.059043  mg/m³

ADD:   0.013088  mg/(kg day)

ADC:  0.059043  mg/m³

Single Event Dose:  286.82  mg

Peak Concentration:  12.191  mg/m³

APDR:  2.6931  mg/(kg day)

Time when APDR occurred:  1.9587  days

Average Inhalation Rate:  13.3  m³/day

____________________________________________________________________________

MCCEM SUMMARY REPORT

TITLE:    Humidifier - 24hrs - Child

RUN         Day  Hour  Min      Length   Days  Hours  Min     Reporting

TIME  Start: 0    0     0       of Run:   2     0      0      Interval: 60 minutes

HOUSE   Type: Generic house      State: NA                  Code: GN001

Season: SUMMER             Zones: 2      Infiltration Rate: 0.18 ACH

EMISSIONS   Source   Zone   Type              Details

¯¯¯¯¯¯   ¯¯¯¯   ¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯   ¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯

1       1     Constant          Emission Rate = 0.895  g/hr

2

3

4

SINKS  Sink  Zone  Model          Details

¯¯¯¯  ¯¯¯¯  ¯¯¯¯¯¯¯¯¯¯¯¯¯  ¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯

1

2

3

4

5

6

ACTIVITIES    Primary Activity Pattern is used on days: 1,2,3,4,5,6,7

OVERRIDE ACTIVITIES:  YES

DOSE

Events/yr:    Yrs of Use:    Weight(kg): 15   Length of Life(yrs):

MONTE CARLO: NO          Number of Trials:  1          Seed No:    Random

OPTIONS  Single Chamber:  YES          Saturation Concentration (mg/m³):  NONE      Output Concentration Units: mg/m³

Initial Concentrations          Units:  mg/m³

Zone 1:  0      Zone 2: 0      Zone 3: 0      Zone 4: 0      Outdoors: 0

____________________________________________________________________________

RESULTS

¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯

LADD:  0.03267  mg/(kg day)

LADC:  0.059043  mg/m³

ADD:   0.03267  mg/(kg day)

ADC:  0.059043  mg/m³

Single Event Dose:  178.99  mg

Peak Concentration:  12.191  mg/m³

APDR:  6.7225  mg/(kg day)

Time when APDR occurred:  1.9587  days

Average Inhalation Rate:  8.3  m³/day

____________________________________________________________________________

| Humidifier - 24hrs |
| --- |
| Time (days) | Time (hrs) | Conc Outdoors (mg/m³) | Conc Zone 1 (mg/m³) | Conc@Person(mg/m³) |
| 0 | 0 | 0 | 0 | 0 |
| 0.041667 | 1 | 7.59E-59 | 2.00763 | 2.00763 |
| 0.083333 | 2 | 2.87E-58 | 3.68471 | 3.68471 |
| 0.125 | 3 | 6.10E-58 | 5.08566 | 5.08566 |
| 0.166667 | 4 | 1.03E-57 | 6.25594 | 6.25594 |
| 0.208334 | 5 | 1.52E-57 | 7.23354 | 7.23354 |
| 0.25 | 6 | 2.09E-57 | 8.05018 | 8.05018 |
| 0.291667 | 7 | 2.70E-57 | 8.73237 | 8.73237 |
| 0.333334 | 8 | 3.36E-57 | 9.30223 | 9.30223 |
| 0.375 | 9 | 4.07E-57 | 9.77826 | 9.77826 |
| 0.416667 | 10 | 4.80E-57 | 10.1759 | 10.1759 |
| 0.458334 | 11 | 5.56E-57 | 10.5081 | 10.5081 |
| 0.5 | 12 | 6.34E-57 | 10.7856 | 10.7856 |
| 0.541667 | 13 | 7.14E-57 | 11.0174 | 11.0174 |
| 0.583334 | 14 | 7.96E-57 | 11.211 | 11.211 |
| 0.625 | 15 | 8.78E-57 | 11.3728 | 11.3728 |
| 0.666667 | 16 | 9.62E-57 | 11.5079 | 11.5079 |
| 0.708334 | 17 | 1.05E-56 | 11.6208 | 11.6208 |
| 0.750001 | 18 | 1.13E-56 | 11.7151 | 11.7151 |
| 0.791667 | 19 | 1.22E-56 | 11.7938 | 11.7938 |
| 0.833334 | 20 | 1.31E-56 | 11.8596 | 11.8596 |
| 0.875001 | 21 | 1.39E-56 | 11.9146 | 11.9146 |
| 0.916667 | 22 | 1.48E-56 | 11.9605 | 11.9605 |
| 0.958334 | 23 | 1.57E-56 | 11.9989 | 11.9989 |
| 1 | 24 | 1.66E-56 | 12.0309 | 12.0309 |
| 1.04167 | 25 | 1.75E-56 | 12.0577 | 12.0577 |
| 1.08333 | 26 | 1.83E-56 | 12.08 | 12.08 |
| 1.125 | 27 | 1.92E-56 | 12.0987 | 12.0987 |
| 1.16667 | 28 | 2.01E-56 | 12.1143 | 12.1143 |
| 1.20833 | 29 | 2.10E-56 | 12.1273 | 12.1273 |
| 1.25 | 30 | 2.19E-56 | 12.1382 | 12.1382 |
| 1.29167 | 31 | 2.28E-56 | 12.1473 | 12.1473 |
| 1.33333 | 32 | 2.37E-56 | 12.1549 | 12.1549 |
| 1.375 | 33 | 2.46E-56 | 12.1613 | 12.1613 |
| 1.41667 | 34 | 2.55E-56 | 12.1666 | 12.1666 |
| 1.45833 | 35 | 2.64E-56 | 12.171 | 12.171 |
| 1.5 | 36 | 2.73E-56 | 12.1747 | 12.1747 |
| 1.54167 | 37 | 2.81E-56 | 12.1778 | 12.1778 |
| 1.58333 | 38 | 2.90E-56 | 12.1804 | 12.1804 |
| 1.625 | 39 | 2.99E-56 | 12.1825 | 12.1825 |
| 1.66667 | 40 | 3.08E-56 | 12.1843 | 12.1843 |
| 1.70833 | 41 | 3.17E-56 | 12.1858 | 12.1858 |
| 1.75 | 42 | 3.26E-56 | 12.1871 | 12.1871 |
| 1.79167 | 43 | 3.35E-56 | 12.1881 | 12.1881 |
| 1.83333 | 44 | 3.44E-56 | 12.189 | 12.189 |
| 1.875 | 45 | 3.53E-56 | 12.1897 | 12.1897 |
| 1.91667 | 46 | 3.62E-56 | 12.1904 | 12.1904 |
| 1.95833 | 47 | 3.71E-56 | 12.1909 | 12.1909 |
| 2 | 48 | 3.80E-56 | 12.1883 | 12.1883 |
| Adult |
| 24 hr exposure duration concentration (24 to 48 hr) | 12.2 |
| Time (hr) | 8 |
| Body Weight (kg) | 60 |
| Inhalation (m3/hr) | 0.55 |
| Dose (mg/kg/day) | 0.90 |
| NOAEL (mg/kg/day) | 10 |
| MOE | 11.1 |
| Child |
| 24 hr exposure duration concentration (24 to 48 hr) | 12.2 |
| Time (hr) | 8 |
| Body Weight (kg) | 15 |
| Inhalation (m3/hr) | 0.36 |
| Dose (mg/kg/day) | 2.32 |
| NOAEL (mg/kg/day) | 10 |
| MOE | 4.3 |

# APPENDIX D: Input/Output from Occupational MCCEM Modeling

Food Processing Plant and Hatchery

MCCEM SUMMARY REPORT

TITLE:    Food Processing

RUN         Day  Hour  Min      Length   Days  Hours  Min     Reporting

TIME  Start: 0    0     0       of Run:   2     0      0      Interval: 60 minutes

HOUSE   Type: Hypothetical house    State: NA                  Code: HY06

Season: NA                 Zones: 1      Infiltration Rate: 0.18 ACH

EMISSIONS   Source   Zone   Type              Details

¯¯¯¯¯¯   ¯¯¯¯   ¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯   ¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯

1

2

3

4

SINKS  Sink  Zone  Model          Details

¯¯¯¯  ¯¯¯¯  ¯¯¯¯¯¯¯¯¯¯¯¯¯  ¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯

1

2

3

4

5

6

ACTIVITIES    Primary Activity Pattern is used on days: 1,2,3,4,5,6,7

OVERRIDE ACTIVITIES:  YES

DOSE

Events/yr:    Yrs of Use:    Weight(kg): 60   Length of Life(yrs):

MONTE CARLO: NO          Number of Trials:  1          Seed No:    Random

OPTIONS  Single Chamber:  YES          Saturation Concentration (mg/m³):  NONE      Output Concentration Units: mg/m³

Initial Concentrations          Units:  g/m³

Zone 1:  0.0258      Zone 2: 0      Zone 3: 0      Zone 4: 0      Outdoors: 0

____________________________________________________________________________

RESULTS

¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯

LADD:  0.0065343  mg/(kg day)

LADC:  0.016336  mg/m³

ADD:   0.0065344  mg/(kg day)

ADC:  0.016336  mg/m³

Single Event Dose:  143.2  mg

Peak Concentration:  25.761  mg/m³

APDR:  2.3554  mg/(kg day)

Time when APDR occurred:  1.0003  days

Average Inhalation Rate:  24  m³/day

____________________________________________________________________________

| Food Processing |
| --- |
| Time (days) | Time (hrs) | Conc Outdoors (mg/m³) | Conc Zone 1 (mg/m³) | Conc@Person(mg/m³) |
| 0 | 0 | 0 | 25.8 | 0 |
| 0.0416667 | 1 | 6.38E-55 | 21.55 | 21.55 |
| 0.0833334 | 2 | 1.17E-54 | 18 | 18 |
| 0.125 | 3 | 1.61E-54 | 15.0349 | 15.0349 |
| 0.166667 | 4 | 1.99E-54 | 12.5582 | 12.5582 |
| 0.208334 | 5 | 2.30E-54 | 10.4895 | 10.4895 |
| 0.25 | 6 | 2.56E-54 | 8.76156 | 8.76156 |
| 0.291667 | 7 | 2.77E-54 | 7.31827 | 7.31827 |
| 0.333334 | 8 | 2.95E-54 | 6.11273 | 6.11273 |
| 0.375 | 9 | 3.10E-54 | 5.10578 | 5.10578 |
| 0.416667 | 10 | 3.23E-54 | 4.26471 | 4.26471 |
| 0.458334 | 11 | 3.34E-54 | 3.56218 | 3.56218 |
| 0.5 | 12 | 3.42E-54 | 2.97538 | 2.97538 |
| 0.541667 | 13 | 3.50E-54 | 2.48525 | 2.48525 |
| 0.583334 | 14 | 3.56E-54 | 2.07585 | 2.07585 |
| 0.625 | 15 | 3.61E-54 | 1.7339 | 1.7339 |
| 0.666667 | 16 | 3.65E-54 | 1.44827 | 1.44827 |
| 0.708334 | 17 | 3.69E-54 | 1.2097 | 1.2097 |
| 0.750001 | 18 | 3.72E-54 | 1.01043 | 1.01043 |
| 0.791667 | 19 | 3.74E-54 | 0.843979 | 0.843979 |
| 0.833334 | 20 | 3.76E-54 | 0.70495 | 0.70495 |
| 0.875001 | 21 | 3.78E-54 | 0.588824 | 0.588824 |
| 0.916667 | 22 | 3.80E-54 | 0.491827 | 0.491827 |
| 0.958334 | 23 | 3.81E-54 | 0.410808 | 0.410808 |
| 1 | 24 | 3.82E-54 | 0.343136 | 0.343136 |
| 1.04167 | 25 | 3.83E-54 | 0.286611 | 0.286611 |
| 1.08333 | 26 | 3.83E-54 | 0.239398 | 0.239398 |
| 1.125 | 27 | 3.84E-54 | 0.199962 | 0.199962 |
| 1.16667 | 28 | 3.84E-54 | 0.167022 | 0.167022 |
| 1.20833 | 29 | 3.85E-54 | 0.139509 | 0.139509 |
| 1.25 | 30 | 3.85E-54 | 0.116527 | 0.116527 |
| 1.29167 | 31 | 3.86E-54 | 0.0973318 | 0.0973318 |
| 1.33333 | 32 | 3.86E-54 | 0.0812983 | 0.0812983 |
| 1.375 | 33 | 3.86E-54 | 0.067906 | 0.067906 |
| 1.41667 | 34 | 3.86E-54 | 0.0567199 | 0.0567199 |
| 1.45833 | 35 | 3.86E-54 | 0.0473764 | 0.0473764 |
| 1.5 | 36 | 3.86E-54 | 0.0395721 | 0.0395721 |
| 1.54167 | 37 | 3.87E-54 | 0.0330534 | 0.0330534 |
| 1.58333 | 38 | 3.87E-54 | 0.0276085 | 0.0276085 |
| 1.625 | 39 | 3.87E-54 | 0.0230606 | 0.0230606 |
| 1.66667 | 40 | 3.87E-54 | 0.0192618 | 0.0192618 |
| 1.70833 | 41 | 3.87E-54 | 0.0160888 | 0.0160888 |
| 1.75 | 42 | 3.87E-54 | 0.0134385 | 0.0134385 |
| 1.79167 | 43 | 3.87E-54 | 0.0112248 | 0.0112248 |
| 1.83333 | 44 | 3.87E-54 | 0.0093757 | 0.0093757 |
| 1.875 | 45 | 3.87E-54 | 0.0078313 | 0.0078313 |
| 1.91667 | 46 | 3.87E-54 | 0.0065412 | 0.0065412 |
| 1.95833 | 47 | 3.87E-54 | 0.0054637 | 0.0054637 |
| 2 | 48 | 3.87E-54 | 0.0045637 | 0.0045637 |
| 2-hr Reentry Interval |
| 8 hr exposure duration concentration (2 to 10 hr) | 9.74 |
| Time (hr) | 8 |
| Body Weight (kg) | 60 |
| Inhalation (m3/hr) | 1.25 |
| Dose (mg/kg/day) | 1.62 |
| NOAEL (mg/kg/day) | 10 |
| MOE | 6.2 |

MCCEM SUMMARY REPORT

TITLE:    Hatchery

RUN         Day  Hour  Min      Length   Days  Hours  Min     Reporting

TIME  Start: 0    0     0       of Run:   2     0      0      Interval: 60 minutes

HOUSE   Type: Hypothetical house    State: NA                  Code: HY07

Season: NA                 Zones: 1      Infiltration Rate: 4 ACH

EMISSIONS   Source   Zone   Type              Details

¯¯¯¯¯¯   ¯¯¯¯   ¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯   ¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯

1

2

3

4

SINKS  Sink  Zone  Model          Details

¯¯¯¯  ¯¯¯¯  ¯¯¯¯¯¯¯¯¯¯¯¯¯  ¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯

1

2

3

4

5

6

ACTIVITIES    Primary Activity Pattern is used on days: 1,2,3,4,5,6,7

OVERRIDE ACTIVITIES:  YES

DOSE

Events/yr:    Yrs of Use:    Weight(kg): 60   Length of Life(yrs):

MONTE CARLO: NO          Number of Trials:  1          Seed No:    Random

OPTIONS  Single Chamber:  YES          Saturation Concentration (mg/m³):  NONE      Output Concentration Units: mg/m³

Initial Concentrations          Units:  g/m³

Zone 1:  0.301      Zone 2: 0      Zone 3: 0      Zone 4: 0      Outdoors: 0

___________________________________________________________________________

RESULTS  ¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯

LADD:  0.0033768  mg/(kg day)

LADC:  0.008442  mg/m³

ADD:   0.0033768  mg/(kg day)

ADC:  0.008442  mg/m³

Single Event Dose:  74.003  mg

Peak Concentration:  291.13  mg/m³

APDR:  1.2334  mg/(kg day)

Time when APDR occurred:  0.41701  days

Average Inhalation Rate:  24  m³/day

___________________________________________________________________________

| Hatchery |
| --- |
| Time (days) | Time (hrs) | Conc Outdoors (mg/m³) | Conc Zone 1 (mg/m³) | Conc@Person(mg/m³) |
| 0 | 0 | 0 | 301 | 0 |
| 0.041667 | 1 | 4.43E-53 | 5.51299 | 5.51299 |
| 0.083333 | 2 | 4.51E-53 | 0.100974 | 0.100974 |
| 0.125 | 3 | 4.51E-53 | 0.001849 | 0.001849 |
| 0.166667 | 4 | 4.52E-53 | 3.39E-05 | 3.39E-05 |
| 0.208334 | 5 | 4.52E-53 | 6.20E-07 | 6.20E-07 |
| 0.25 | 6 | 4.52E-53 | 1.14E-08 | 1.14E-08 |
| 0.291667 | 7 | 4.52E-53 | 2.08E-10 | 2.08E-10 |
| 0.333334 | 8 | 4.52E-53 | 3.81E-12 | 3.81E-12 |
| 0.375 | 9 | 4.52E-53 | 6.98E-14 | 6.98E-14 |
| 0.416667 | 10 | 4.52E-53 | 1.28E-15 | 1.28E-15 |
| 0.458334 | 11 | 4.52E-53 | 2.34E-17 | 2.34E-17 |
| 0.5 | 12 | 4.52E-53 | 4.29E-19 | 4.29E-19 |
| 0.541667 | 13 | 4.52E-53 | 7.86E-21 | 7.86E-21 |
| 0.583334 | 14 | 4.52E-53 | 1.44E-22 | 1.44E-22 |
| 0.625 | 15 | 4.52E-53 | 2.64E-24 | 2.64E-24 |
| 0.666667 | 16 | 4.52E-53 | 4.83E-26 | 4.83E-26 |
| 0.708334 | 17 | 4.52E-53 | 8.84E-28 | 8.84E-28 |
| 0.750001 | 18 | 4.52E-53 | 1.62E-29 | 1.62E-29 |
| 0.791667 | 19 | 4.52E-53 | 2.97E-31 | 2.97E-31 |
| 0.833334 | 20 | 4.52E-53 | 5.43E-33 | 5.43E-33 |
| 0.875001 | 21 | 4.52E-53 | 9.95E-35 | 9.95E-35 |
| 0.916667 | 22 | 4.52E-53 | 1.82E-36 | 1.82E-36 |
| 0.958334 | 23 | 4.52E-53 | 3.34E-38 | 3.34E-38 |
| 1 | 24 | 4.52E-53 | 6.11E-40 | 6.11E-40 |
| 1.04167 | 25 | 4.52E-53 | 1.12E-41 | 1.12E-41 |
| 1.08333 | 26 | 4.52E-53 | 2.05E-43 | 2.05E-43 |
| 1.125 | 27 | 4.52E-53 | 3.76E-45 | 3.76E-45 |
| 1.16667 | 28 | 4.52E-53 | 6.88E-47 | 6.88E-47 |
| 1.20833 | 29 | 4.52E-53 | 1.26E-48 | 1.26E-48 |
| 1.25 | 30 | 4.52E-53 | 2.31E-50 | 2.31E-50 |
| 1.29167 | 31 | 4.52E-53 | 4.68E-52 | 4.68E-52 |
| 1.33333 | 32 | 4.52E-53 | 5.29E-53 | 5.29E-53 |
| 1.375 | 33 | 4.52E-53 | 4.53E-53 | 4.53E-53 |
| 1.41667 | 34 | 4.52E-53 | 4.52E-53 | 4.52E-53 |
| 1.45833 | 35 | 4.52E-53 | 4.52E-53 | 4.52E-53 |
| 1.5 | 36 | 4.52E-53 | 4.52E-53 | 4.52E-53 |
| 1.54167 | 37 | 4.52E-53 | 4.52E-53 | 4.52E-53 |
| 1.58333 | 38 | 4.52E-53 | 4.52E-53 | 4.52E-53 |
| 1.625 | 39 | 4.52E-53 | 4.52E-53 | 4.52E-53 |
| 1.66667 | 40 | 4.52E-53 | 4.52E-53 | 4.52E-53 |
| 1.70833 | 41 | 4.52E-53 | 4.52E-53 | 4.52E-53 |
| 1.75 | 42 | 4.52E-53 | 4.52E-53 | 4.52E-53 |
| 1.79167 | 43 | 4.52E-53 | 4.52E-53 | 4.52E-53 |
| 1.83333 | 44 | 4.52E-53 | 4.52E-53 | 4.52E-53 |
| 1.875 | 45 | 4.52E-53 | 4.52E-53 | 4.52E-53 |
| 1.91667 | 46 | 4.52E-53 | 4.52E-53 | 4.52E-53 |
| 1.95833 | 47 | 4.52E-53 | 4.52E-53 | 4.52E-53 |
| 2 | 48 | 4.52E-53 | 4.52E-53 | 4.52E-53 |
| 0 hr Re-entry Interval |
| 8 hr exposure duration concentration (0 to 8 hr) | 0.62 |
| Time (hr) | 8 |
| Body Weight (kg) | 60 |
| Inhalation (m3/hr) | 1.00 |
| Dose (mg/kg/day) | 0.083 |
| NOAEL (mg/kg/day) | 10 |
| MOE | 120 |
| 2-hr Reentry Interval |
| 8 hr exposure duration concentration (2 to 10 hr) | 0.0114 |
| Time (hr) | 8 |
| Body Weight (kg) | 60 |
| Inhalation (m3/hr) | 1.00 |
| Dose (mg/kg/day) | 0.0015 |
| NOAEL (mg/kg/day) | 10 |
| MOE | 6,562 |

# APPENDIX E:  Calculation of DDAC Unit Exposure Values

| Table E-1: DDAC Dermal and Inhalation Exposure Values for Chemical Operators, Graders, Millwrights, Clean-up Crews, and Trim Saw Operatorsa |
| --- |
| Replicate Number | Chemical Operator | Grader | Trim Saw Operator | Millwright | Cleanup Crew |
|  | Dermal | Inhalation | Dermal | Inhalation | Dermal | Inhalation | Dermal | Inhalation | Dermal | Inhalation |
|  | Potential exposure (mg) | Air Concentrationb,c ((g/m3) | Potential exposured (mg) | Potential exposure (mg) | Air Concentrationb,c ((g/m3) | Potential exposured (mg) | Potential exposure (mg) | Air Concentrationb,c ((g/m3) | Potential exposured (mg) | Potential exposure (mg) | Air Concentrationb,c ((g/m3) | Potential exposured (mg) | Potential exposure (mg) | Air Concentrationb,c ((g/m3) | Potential exposured (mg) |
| 1 | 3.5 | 10.1 | 0.0808 | 3.05 | 2.90 | 0.0232 | 0.78 | 2.83 | 0.0227 | 1.31 | 2.92 | 0.0233 | 68.3 | 2.99145 | 0.0239 |
| 2 | 6.11 | 2.80 | 0.0224 | 7.47 | 2.93 | 0.0234 | 1.98 | 12.3 | 0.0984 | 29.08 | 2.83 | 0.0226 | 0.720 | 2.78840 | 0.0223 |
| 3 | 6.07 | 2.79 | 0.0223 | 1.09 | 2.91 | 0.0233 |  |  |  | 8.03 | 15.6 | 0.1248 | 166 | 30.3 | 0.2424 |
| 4 | 46.37 | 2.82 | 0.0226 | 10.51 | 3.00 | 0.0240 |  |  |  |  |  |  | 95.2 | 412 | 3.2960 |
| 5 | 0.94 | 2.93 | 0.0235 | 0.61 | 2.82 | 0.0226 |  |  |  |  |  |  | 1.20 | 2.83585 | 0.0227 |
| 6 | 22.15 | 2.83 | 0.0227 | 0.98 | 2.85 | 0.0228 |  |  |  |  |  |  | 0.260 | 2.80989 | 0.0225 |
| 7 | 21.45 | 2.77 | 0.0222 | 2.63 | 2.91 | 0.0233 |  |  |  |  |  |  |  |  |  |
| 8 | 0.22 | 2.73 | 0.0218 | 5.23 | 2.85 | 0.0228 |  |  |  |  |  |  |  |  |  |
| 9 | 0.44 | 2.77 | 0.0222 | 0.19 | 13.20 | 0.1056 |  |  |  |  |  |  |  |  |  |
| 10 | 0.33 | 3.14 | 0.0251 | 1.47 | 2.89 | 0.0231 |  |  |  |  |  |  |  |  |  |
| 11 | 0.29 | 2.88 | 0.0230 | 2.38 | 2.85 | 0.0228 |  |  |  |  |  |  |  |  |  |
| 12 |  |  |  | 4.09 | 2.81 | 0.0225 |  |  |  |  |  |  |  |  |  |
| 13 |  |  |  | 1.03 | 2.94 | 0.0235 |  |  |  |  |  |  |  |  |  |
| Arithmetic Mean | 9.81 | 3.51 | 0.0281 | 3.13 | 3.68 | 0.0295 | 1.38 | 7.57 | 0.061 | 12.8 | 7.12 | 0.057 | 55.3 | 75.6 | 0.60 |
| Minimum | 0.22 | 2.73 | 0.0218 | 0.19 | 2.81 | 0.0225 | 0.78 | 2.83 | 0.0227 | 1.31 | 2.83 | 0.0226 | 0.260 | 2.79 | 0.0223 |
| Maximum | 46.4 | 10.1 | 0.081 | 10.51 | 13.2 | 0.106 | 1.98 | 12.3 | 0.098 | 29.1 | 15.6 | 0.125 | 166 | 412 | 3.30 |

a.	“Measurement and Assessment of Dermal and Inhalation Exposures to Didecyl Dimethyl Ammonium Chloride (DDAC) Used in the Protection of Cut Lumber (Phase III)” is the study that values were obtained from for this table (Bestari et al., 1999, MRID 455243-04).

b.	The inhalation LOD was not provided for chemical operators, graders, trim saw operators, millwrights, or the clean-up crew.  Therefore, the LOD provided for the diptank operator (5.6 (g) was used for these positions.  Residues less than the LOD were adjusted to 1/2 LOD.

c.	The inhalation limit of detection was converted to (g/m3 using the following equation: air concentration ((g/m3) = 5.6 (g/ [average flow rate (L/min) * sampling duration (480 min) * 1000 L/m3.  Data was obtained from Bestari et al (1999).

d.	DDAC air concentrations were converted to inhalation exposure using the following equation: Air concentration ((g/m3) x inhalation rate (1.0 m3/hr) x Conversion factor (1 mg/1000 (g) x sample duration (8 hours/day

| Table E-2: Normalization of DDAC Dermal and Inhalation Exposure Values for Diptank Operatorsa |
| --- |
| Worker ID | Mill number | Sample Time (min) | DDAC Conc. in Diptank (%) | Gloves | Dermal Body Exposureb (mg) | Hand Exposureb (mg) | Total Dermal Exposure (mg) | Normalized Total Dermal Unit Exposurec (mg/ 1 % solution) | Air Conc.d (mg/m3) | Inhalation Exposuree (mg) | Normalized Inhalation Unit Exposurec (mg /1% solution) |
| M7P1A | 7 | 480 | 0.64 | Rubber | 0.5 | 3.44 | 3.94 | 6.16 | 0.003 | 0.024 | 0.0375 |
| M7P1B | 7 | 480 | 0.64 | Rubber | 0.32 | 2.02 | 2.34 | 3.66 | 0.003 | 0.024 | 0.0375 |
| M8P4A | 8 | 408 | 0.42 | Rubber | 0.04f | 1.34 | 1.38 | 3.29 | 0.003 | 0.024 | 0.057 |
| M8P4B | 8 | 480 | 0.42 | Rubber | 0.04f | 0.5 | 0.54 | 1.29 | 0.003 | 0.024 | 0.057 |
| M8P7 | 8 | 480 | 0.42 | Cotton | 0.03 | 0.04 | 0.07 | 0.17 | 0.003 | 0.024 | 0.057 |
| M11P9A | 11 | 395 | 0.63 | Leather | 0.15 | 3.33 | 3.48 | 5.52 | 0.003 | 0.024 | 0.0381 |
| M11P9B | 11 | 480 | 0.63 | Leather | 0.1 | 0.45 | 0.55 | 0.87 | 0.003 | 0.024 | 0.0381 |
| Arithmetic Mean | 0.17 | 1.59 | 1.76 | 2.99 | 0.0030 | 0.0240 | 0.046 |
| Standard Deviation | 0.18 | 1.39 | 1.53 | 2.32 | 0.0000 | 0.0000 | 0.0103 |
| Median | 0.10 | 1.34 | 1.38 | 3.29 | 0.0030 | 0.0240 | 0.0381 |
| Geometric Mean | 0.10 | 0.83 | 0.99 | 1.86 | 0.0030 | 0.0240 | 0.045 |
| 90%tile | 0.39 | 3.37 | 3.66 | 5.78 | 0.0030 | 0.0240 | 0.057 |
| Maximum | 0.50 | 3.44 | 3.94 | 6.16 | 0.0030 | 0.0240 | 0.057 |

a.	“Measurement and Assessment of Dermal and Inhalation Exposures to Didecyl Dimethyl Ammonium Chloride (DDAC) Used in the Protection of Cut Lumber (Phase III)” is the study that values were obtained from for this table (Bestari et al., 1999, MRID 455243-04).

b.	DDAC concentration that was detected in the monitoring study (MRID #455243-04).

c.	Normalization of DDAC data for percent ai treatment.  Normalized Unit Exposure (mg/1% ai solution) = Exposure (mg DDAC) / concentration in diptank solution (% DDAC)

d.	All inhalation residues were <LOD (5.6 g or 0.0056 mg/m3). 1/2 LOD was used in all calculations (0.003 mg/m3). Air Concentration (mg/m3) = 5.6 g / (~2 L/min flow rate x ~480 min) x 1000 L/m3 conversion x 0.001 g/mg = 0.003 mg/m3

e.	Inhalation exposure (mg) = air concentration (mg/m3) x inhalation rate (1.0 m3/hr) x sample duration (8 hours/day).

f.	Residues were <LOD for dermal samples M8P4A, M8P4B.  Sample size of ~11,231 cm2 x <0.007 ug/cm2 = LOD of 0.079 mg.  1/2 LOD reported (i.e., 0.04 mg)